Dr. ABE Blank

Operation Manual for EM Machine

Sep 2007

# Content

Content	2

Chapter 1: Welcome to Dr. ABE	11

Chapter 2: What’s New	12

Chapter 3: Getting Started	15

3.1 System Requirements	15

3.2 Launch Dr.ABE	15

3.3 Quick Start Guide	15

3.3.1 Dr.ABE Main Window	16

3.3.2 Basic Dr.ABE Settings	16

3.3.3 Basic Operation	16

Chapter 4: Machine Parameter	21

4.1 Machine Parameter Toolbar	21

4.2 Machine Parameter Tree View	22

4.3 Machine Information	22

4.3.1 Machine Information Panel	23

4.3.2 Time Study	25

4.4 NC Device Information	26

4.5 Peripherals	28

4.5.1 Clamp Information	29

4.5.2 Holder Information	31

4.5.3 MJC	32

4.5.4 IJP	34

4.5.5 Loading/Unloading Device	36

4.5.6 Work Chute Information	37

4.5.7 Take Out Information	39

4.5.8 Tapping Information	41

Chapter 5: Material Parameter	43

5.1 Material Manager Toolbar	44

5.1.1 Create a Material Type	45

5.1.2 Edit a Material Type	46

5.1.3 Delete a Sheet Information	48

5.1.4 Download Material Type from AP100	49

5.1.5 Option	50

5.1.6 Backup and Restore Material	51

5.1.6.1 How to Backup Material	52

5.1.6.2 How to Restore Material	53

5.2 Material Type Information	55

5.3 Sheet Information	56

5.3.1 Standard, Remnant, Skeleton and Sketch Materials	57

5.3.2 How to Create a Remnant Sheet	58

5.3.3 How to Create a Skeleton Sheet	60

5.4 Tube Material Information	62

Chapter 6: System Setting	64

6.1 View	64

6.1.1 Main Window	65

6.1.2 CAD Data Drawing	69

6.1.3 Drawing	70

6.1.3.1 View Y Size	72

6.1.3.2 Difference between Quality and Speed	73

6.1.3.3 Display Different Colors for the Elements on the Part	74

6.1.3.4 Expand All is Done after Automatic	78

6.1.4 Information Area	80

6.1.5 Zoom	81

6.1.6 Utilization Setting	83

6.2 System	85

6.2.1 System Setting	86

6.2.1.1 Initial Part Number	88

6.2.1.2 System Determining Sheet by Material Name	88

6.2.1.3 Use Wizard for Sheet Size/Name	89

6.2.2 System Information	91

6.2.3 License Registration	91

6.2.4 System Backup and Restore	94

6.2.4.1 How to Backup the Parameters	95

6.2.4.2 How to Restore the Parameters	96

6.2.5 Preference Frame Current Folder	98

6.2.6 Parameter Processing	98

6.2.6.1 Decrease Sheet Quantity When Save NC	100

6.2.6.2 Select Skeleton/Remnant to Save when Saving NC	101

6.2.7 Access Information Manager	102

6.3 Option	103

6.3.1 Option window	107

6.3.2 Setting of Outputting Result File window	108

Chapter 7: CAD Data Load	115

7.1 How to Load CAD Data	115

7.2 Methods for Specifying the Part Quantity	116

7.3 How to Establish a Connection with a Server	117

Chapter 8: Nesting Plan	118

8.1 Parts Properties Summary	119

8.2 Menus	121

8.2.1 File Menu	121

8.2.2 Edit Menu	122

8.2.3 View Menu	122

8.2.4 Insert Menu	123

8.2.5 Tool Menu	124

8.2.6 Help Menu	130

8.3 Toolbars	130

8.4 My Nesting Plan	132

8.5 Parts List	136

8.5.1 Shortcut Menu	138

8.5.2 Light Attribute Editor	139

8.5.2.1 To Assign attribute data to a pattern	141

8.6 Parts Properties	145

8.6.1 Part Name and Comment	147

8.6.2 Select Data	147

8.6.3 Quantity	148

8.6.4 Dates	149

8.6.5 Material	151

8.6.6 Process	152

8.6.7 Nesting	152

8.6.7.1 Defining the Part Priority	154

8.6.7.2 Defining the Group ID for Parts	155

8.6.7.3 Rotation with Different Condition	155

8.6.7.4 Different Result of the Common Line Cutting	156

8.6.8 Change Check Boxes	158

8.7 Parts Properties Advanced	159

8.7.1 Material	160

8.7.2 Special Information	161

8.7.3 Size Definition	161

8.7.4 Code Definition	162

8.7.5 Nesting	162

8.7.5.1 Standard Nesting	163

8.7.5.2 Sketch Nesting	163

8.7.5.3 Grid Nesting	165

8.7.6 Process and User Define	166

8.7.7 Taking Out Station	166

8.7.8 Taking Out Part Grid as One Part	167

Chapter 9: Preference File Window	169

9.1 Preference Window Overview	169

9.1.1 Splitter Bars	170

9.1.2 Tree View Pane	170

9.1.2.1 Hierarchical Structure	171

9.1.2.2 Shortcut Menu	171

9.1.3 Preference File Pane	175

9.1.3.1 Creating a New File	176

9.1.3.2 Preference File Shortcut Menu	176

9.1.4 Display Area Pane	177

9.2 Preference Window Menu	178

9.2.1 File	178

9.2.2 Edit	179

9.2.3 Tools	179

9.2.4 Window	180

9.2.5 Help	181

9.3 Preference Window Toolbar	181

Chapter 10: Nesting Preference	184

10.1 Nesting Logic 1	185

10.1.1 Nesting Type	186

10.1.2 Pattern Setting	188

10.1.2.1 Nesting Parts by the Production Schedule	189

10.1.3 Start Point/Direction	191

10.1.3.1 How to Define the Start Point/Direction	192

10.1.3.2 Example of Shift After Nesting	194

10.2 Nesting Logic 2	196

10.2.1 Grid Pattern	196

10.2.2 Nest Around Clamps	197

10.2.3 Part Rotation	198

10.2.4 Utilization	198

10.2.4.1 Pair Example	200

10.2.4.2 Part in Part Example	200

10.3 Part-Spacing and Nesting Border	201

10.3.1 Advance	202

10.4 Initial Clamp Position	203

10.4.1 Number of Clamp	204

10.4.2 Absolute	204

10.4.3 Advance	205

10.5 Material Selection	208

10.5.1 Automatic Material Selection	209

10.5.1.1 Material Selection Priority	210

10.5.1.2 Selection Priority	212

10.5.1.3 Use Sketch Material for Non-Sketch Parts	212

10.5.1.4 Don’t nest parts inside skeleton area	213

10.5.2 Reusable Sheet	213

10.5.3 Joint Setting Window	215

10.5.4 How to Create Skeleton Sheet	216

10.5.5 How to Create a Remnant Sheet	218

10.6 Share to Size	221

10.6.1 Sketch Material Tolerance	222

10.6.2 Sketch Type	225

10.6.3 Joint	228

Chapter 11: Tool Assignment	230

11.1 Calculation	231

11.1.1 Main	233

11.1.1.1 Process multiple Line Segments as One Segment	236

11.1.1.2 Search for Stock Tools	237

11.1.1.3 Change the Tool Angle to Process	240

11.1.1.4 Change the Die Clearance of the Fixed Station	242

11.1.1.5 Non AI Station is used with higher Priority	244

11.1.2 Tool Lap Value	246

11.1.3 Assignment	249

11.1.3.1 Slit Tool Assignment	252

11.1.3.2 Perimeter Tool Assignment	253

11.1.3.3 Tool Assignment for the Vertical or Horizontal Notch	257

11.1.3.4 Tool Assignment for Slanted Notch	259

11.1.4 Joint	260

11.1.4.1 Use Special Tool to Create Joints	262

11.1.5 Contouring Assignment	265

11.1.6 Slit & V Notch	269

11.1.6.1 Process the Slit	273

11.1.7 De-burring	274

11.1.8 Slot2&3	278

11.2 Tooling Pattern	281

11.2.1 Simple Tool Assignment Setting for the Specified Template	283

11.2.2 Fit Tool Style Panel	285

11.2.2.1 Hole Pattern List	287

11.2.2.2 Pattern Information and Assignment Pattern List	288

11.2.2.3 Template Detail Settings	289

11.2.3 Match To Line	292

11.2.3.1 Assign SP Tool to Process Line Segment	294

11.3 Edit of Template	296

11.3.1 Template Pane	298

11.3.1.1 Template Menu	298

11.3.1.2 Template Toolbar	299

11.3.1.3 Template Icon	313

11.3.1.4 Template Parameter	316

11.3.1.5 Shape Edit area	317

11.3.1.6 Generate data	317

11.3.1.7 Edit of Path	318

11.3.1.8 Edit of Elements	319

11.3.1.9 Edit Additional Elements Information	320

11.3.2 Pattern Pane	323

11.3.2.1 Tool Assignment Pane	330

11.3.2.2 Basic Shape	331

11.3.2.3 Shape Data	331

Chapter 12: Sequence	335

12.1 Sequence	336

12.1.1 Part as Process Unit	337

12.1.1.1 Sheet and Each Part	338

12.1.1.2 Machine Stop for Prototype	339

12.1.1.3 Process Order	342

12.1.2 For Reducing Bits of Vinyl	342

12.1.3 AI Tool Angle Sort	343

12.1.4 Tool Sorting	344

12.1.5 Process Unit Sorting	346

12.2 Clamp Setting	347

12.2.1 Clamp Removal (Clamp # 3)	348

12.2.2 Clamp Position Change	349

12.3 Clamp Avoidance	350

12.3.1 Avoid DZ	351

12.3.2 Clamp Position Change	352

12.4 Repositioning	355

12.4.1 Repositioning Type	356

12.4.1.1 Minimum	357

12.4.1.2 No Divide of Parts	359

12.4.2 Process Majority of Parts	361

12.4.3 Process Direction	363

12.4.4 Return to First Position	366

12.5 Part-Grid	366

12.5.1 Part-Grid Conditions	367

12.5.2 Output Outside of UV	370

Chapter 13: NC Generate	372

13.1 Material	373

13.2 Loading / Unloading Device	373

13.3 Loading / Unloading Thickness M-Code	374

13.4 Loading / Unloading End Position M-Code	376

13.5 Output work size comment at the end of G92 command line	378

13.6 Use Line Number	379

13.7 Use Setup Sheet	379

13.8 Setup Sheet	380

13.9 Output G93	381

13.10 Percent After G50	382

13.11 Clear Macros	383

Chapter 14: Process After	385

14.1 Process After Cutting Table	385

14.1.1 X/Y/R/CPX/Area/Length/Width Explanation	387

14.2 Joint	388

14.2.1 Fixed Position	389

14.2.2 Auto Position	390

14.2.3 Basic Joint Setting	392

14.2.3.1 Min Distance between Corner	392

14.2.3.2 Min Distance between Wire	393

14.2.3.3 Min Joint Qty	395

14.2.3.4 Max Distance between Corner Joint	395

14.2.4 Joint Type Table	395

14.2.5 Detailed Joint Setting	396

14.2.5.1 Common Settings	397

14.2.5.2 Corner Joint Settings	398

14.2.5.3 Wire Joint Setting	399

14.2.5.4 Chute Setting	400

14.2.6 Joint Setting Condition	401

Chapter 15: Peripherals	403

15.1 MJC	403

15.1.1 MJC Setting	404

15.2 Taking Out	405

15.2.1 Taking Out Conditions	406

15.2.2 Stack Distance	407

15.2.3 Taking Out	409

15.3 MJC/IJP Sequence	411

15.4 IJP	413

15.4.1 IJP Setting	414

15.4.2 IJP Position	416

15.4.3 IJP Strings	417

15.5 Part Removal Sequence	418

15.6 Schedule	420

Chapter 16: Group	422

16.1 Grouping Priority	422

16.2 Prototype Condition	425

16.3 TK Process Type	429

16.4 Filler Parts	430

Chapter 17 Clearance	435

17.1 Clearance Setting	435

Chapter 18: Turret Layout	438

18.1 Import AP100 Turret Layout	441

18.2 TurretLayout Window	444

18.3 Turret Section	445

18.3.1 Turret Section Toolbar	446

18.3.2 Range and Shape buttons	446

18.3.3 View Buttons	447

18.3.4 T No.	447

18.3.5 Search Stations	448

18.3.6 Turret Picture	449

18.3.6.1 Assign tools in the Turret Load Setting mode	449

18.3.6.2 Assign tools in the Effective Station Setting mode	452

18.3.7 Turret Station List	456

Chapter 19: Dead Zone	459

19.1 Dead Zone of the Station	460

Chapter 20: Schedule	464

20.1 Sheet Name	465

20.1.1 Sheet Name Items	465

20.1.2 Nesting Name	466

20.1.3 Date	469

20.1.4 Sequence Number	470

20.1.5 For Combination Process, Change Sheet Name Based on the Machine	471

20.1.6 Sheet Name	472

20.2 Schedule Name	473

20.2.1 Schedule Name Items	474

20.2.2 Number	474

20.2.3 Date	476

20.2.4 Schedule Name	478

20.3 Scheduling Priority	482

20.3.1 Priority	483

20.3.2 Get Information from NC Data	485

Chapter 21: Tool Inventory	485

21.1 SubInventory Window	487

21.1.1 SubInventory Window Toolbar	487

21.1.2 Range and Shape buttons	488

21.1.3 Import Buttons	488

20.1.3.1 Import AP100 tools into Dr ABE tool inventory	489

20.1.3.2 Import Ap100 SP/FM tools into Dr. ABE tool inventory	491

20.1.3.3 Import DXF/DWG SP/FM Shapes	493

21.1.4 View Buttons	495

21.1.5 Advanced Filter Window	496

21.1.6 Machine Type	497

21.2 Tool Inventory Table	497

21.3 Tool Inventory Table Shortcut Menu	501

21.3.1 Edit Group	501

21.3.2 Auto Sort	505

21.4 Tool Window	508

21.4.1 Basic Tool Information	508

21.4.1.1 Share the tool conditions among machines	510

21.4.2 Attribute 1	513

21.4.2.1 Specify the Sheet Saver for the nesting tools to avoid reposition	516

21.4.3 Attribute 2	518

21.4.3.1 The Customize Window	519

21.4.4 Codes	522

21.4.4.1 M Codes	524

21.4.5 PDC Operation	527

Chapter 22: Remnant/Skeleton Name	528

22.1 Remnant Name	529

22.1.1 Remnant Name Items	529

22.1.2 Special Name	530

22.1.3 Date Format	530

22.1.4 Sequence Number	531

22.1.5 Remnant Name	531

22.2 Skeleton Name	534

22.2.1 Skeleton Name Items	534

22.2.2 Special Name	535

22.2.3 Date Format	535

22.2.4 Sequence Number	536

22.2.5 Skeleton Name	536

Chapter 23: Turret Type	539

23.1 Turret Type Window Items	539

23.2 Create or Remove a Turret Type	542

23.3 Adding or Deleting a Station	543

23.4 Append or Remove a Dead Zone	545

Chapter 24: Turret Type (PDC)	546

24.1 Turret Type (PDC) Window Items	546

24.2 Create or Remove a PDC Turret Type	548

24.3 Adding or Deleting a PDC Station	550

24.4 Append or Remove a Dead Zone	551

Chapter 25: Result View	553

25.1 Nesting Result List	556

25.1.1 The No. Column Heading Shortcut Menu	558

25.1.1.1 Save NC Data	559

25.1.1.2 Save SY4	561

25.1.1.3 Save Schedule/Output Report	562

25.1.1.4 Output Report	569

25.1.1.5 Delete Sheet	571

25.1.1.6 Display Material Info	572

25.1.1.7 Display Plan Info	572

25.1.1.8 Row Height	574

25.1.1.9 Save Part	574

25.1.1.10 Save SY5 as File	575

25.1.2 The Column Heading Shortcut Menu	576

25.1.3 The Warning Information Window	578

25.1.4 The Time Study Information Window	578

25.2 Part Layout Shortcut Options	579

25.2.1 Save MJC Data	596

25.2.2 Do Stack	598

25.2.3 Begin TK Edit	600

25.2.3.1 Edit of Pickup/IJP Information window	602

25.3 Information Panel	604

25.3.1 The Parts Information Panel	604

25.3.2 The Error List Panel	606

25.3.3 The NC Panel	607

Chapter 26 Manual Edit Mode	610

26.1 Manual Edit Mode Shortcut Menu	611

26.2 Manual Edit Mode Parameter Panel	612

26.3 Move	613

26.4 Remove	619

26.5 Sequence Edit	625

26.5.1 Specify the range	626

26.5.2 Mouse Command	629

26.5.3 List Command	631

26.6 Part Grid	632

26.7 Change Material	636

26.7.1 Change material by auto-calculation	637

26.7.2 Input size to change material	638

26.7.3 Select sheet code to change material	640

26.8 Remnant Edit	641

26.9 Confirm Schedule Tool	647

26.9.1 Toolbar	647

26.9.1.1 Range toolbar	647

26.9.1.2 Shape toolbar	647

26.9.1.3 Search toolbar	647

26.9.1.4 View menu	649

26.9.2 Schedule list	649

26.9.3 Turret and tool information table	650

26.9.4 Turret Image pane	652

26.9.5 Display Station option	653

26.10 Confirm/Display Setting	653

26.11 Add Parts	660

26.11.1 Add parts by opening a file	660

26.11.2 Add parts from SDD database	662

26.12 Reposition Command	667

26.12.1 Basic Reposition Operation	668

26.12.1.1 Confirm Reposition	668

26.12.1.2 Manual Reposition	672

26.12.2 Divide Reposition	673

26.12.3 Group Reposition	676

26.13 Add New Sheet	677

26.14 Option	679

Chapter 27: Manual Tool Assignment	684

27.1 Part Edit Mode Shortcut Menu	686

27.2 Part Edit Mode Parameter Panel	687

27.3 Confirm/Display Setting	688

27.4 Save Template	690

27.5 Delete Trace	695

27.6 Joint Edit	698

27.7 End Value	705

27.8 Change the Tool Assignment	708

27.9 Assign Tool Lines	715

27.10 Layout Between Single Hit	723

27.11 Merge	725

27.12 Stretch	727

27.12.1 Adjust the process path on the lines	729

27.12.2 Adjust the process path on the arcs	730

27.13 Shift	732

27.13.1 Move the process path on the lines	733

27.13.2 Move the process path on the arcs	734

27.14 Direct Assignment	736

27.14.1 Assignment between 2 points	737

27.14.2 Diagonal Assignment	739

27.14.3 Parameter Assignment	740

27.14.4 Hole Assignment	744

27.15 Move/Copy Tool	745

27.16 Apply Assignment to the Same Inner	759

27.17 Fix Process Order	763

27.18 Change the Nibble Pitch	767

27.19 Show Tool	769

27.20 Option	769

Chapter 28: Auto Correction Condition Setup	774

28.1 Merge	775

28.2 Fill Gaps	777

28.3 Remove Guidelines	781

28.4 Break	783

28.5 Get Outer Loop	785

28.6 Extra Entities Removal	787

28.7 Remove Slot	792

28.8 Small Entities Removal	796

28.9 Standard Hole Detection	799

28.10 Remove Holes Enclosing Pattern	801

28.11 Corner Slot	803

28.12 Parts Separation	805

28.13 Decimal Approximation	808

28.14 Arc Straightening	810

28.15 Slant Line Removal	813

28.16 Minute Gap Removal	815

28.17 Polylines To Arc	817

28.18 Special Hole Detection	820

28.19 Spline to Lines/Arcs	821

28.20 Delete Point	823

28.21 Ignore Conditions for Large Data	824

Index	826

# Chapter 1: Welcome to Dr. ABE

Welcome to Dr. ABE. Dr. ABE is a sophisticated application used for sheet metal fabrication. The software allows you to reduce the costs associated with part production and helps to improve your productivity. Dr. ABE is designed to create the most efficient nesting jobs according to the settings that you specify. You can also edit and verify the nesting results until you are satisfied with the nesting plan.

Dr. ABE has the following features:

- User-friendly operation. Nearly all operations, from tool assignment to NC code generation are automated.

- Strong nesting functions and high material utilization, logical and appropriate tool assignments, optimized sequencing, etc.

- Flexible compatibility. The software is compatible with most CAD data formats (*.dwg, *.iga, *.dxf, etc.). Dr. ABE also supports the AP100 database system (MiniSDD, SDDJ).

For more information, please refer to the corresponding chapters.

# Chapter 2: What’s New

Thank you for your purchase of Dr. ABE. This manual outlines the new features or enhancements in the latest version of the software.

New Features

Multiple Language Support

This version supports eight languages, such as Japanese, Chinese, Korean, English and four European languages.

CSV Format Support

This version supports the output of the nesting plan and nesting result in the CSV files.

Copy Machine

In the Machine Set window, you can select one machine and click Copy button to create an identical machine with a different name.

Backup and Restore Machine Parameters

In the Machine Set window, you can select to backup or restore corresponding preference settings for the corresponding machines.

Output G92 to show the process range rectangle size

The system will output the process range size at the end of G92 command line.

Output G93 to display the coordinate in the AP100 report

In this version, you can output the AP100 report and display the G93 coordinates.

Output G93 for A Single Part

This version supports the output of G93 even though only one part is processed.

Print Result View

In the result view, you can select Print Result View from the shortcut menu to print the result view.

Save SY4 file

After auto execution, you can save nesting result (nesting plan/common info/condition/machine info/material) except preference information in SDD/MiniSDD database and save as file.

Save SY5 file

After auto execution, you can save the tool assignment information of the part as a *.sy5 file.

Row Height

You can adjust cell height for better view in result view by typing a value in Row Height: text box.

Break macro when reposition

The system will break the macro patterns (Part Grid) into single parts to process during the reposition.

Sorting Base Option

You can select to sequence the parts based on the distance or the direction.  Also you can select

One Side Direction in Sequence panel of Laser Sequence preference, and the system will sequence the parts in one direction.

ALA Single Common Line Shift

When a slant common line is processed, the system will extend the tool assignment path to process the common line.

Manual Edit

In previous version, you have to right click to select an option from the shortcut menu, each time you want to process one operation about part or material manually. Now just right click the part layout area to enter the Part Edit mode or Sheet Edit mode. New Manual Edit toolbar consists of part edit toolbar and sheet edit toolbar.

In Part Edit mode, you can perform operations about part, assign tool-lines, change tool assignment, change nibbling pitch, fix process order, assign the same inner, assign tool directly, as well as merge, stretch, shift tool path.

In Sheet Edit mode, you can execute sequence edit, remnant edit, material change, part grid, clamp reposition, schedule tool confirmation, scrap cutting.

Material Manager Multiple Selection

You can select more than one machine and modify sheet information for all the machines you have selected.

Slice Sheet

This function is used to take out a heavy skeleton.

Machine Stop for Prototype

This function is used to determine whether system outputs machine stop for prototype or not.

Deburring Tool Assignments

The new version provides functions of assigning deburring tools automatically.

Slot2&3 Tool Assignments

The new version provides functions of assigning slot2&3 tools automatically.

Adding Tool to Turret/PDC/HMX

The Turret Layout Setting button allows you to add more than one tool at a time to Turret/PDC/HMX.

Reposition Editing Confirm Mode

This function allows you to edit reposition manually. You can insert a track to one reposition freely. You can also divide specified trace into two different repositions.

Template

In Edit of Template, improved interface provides you the easier way to edit the template. It is more conveniently to use the new operation flow to add and edit a template.

Ignore Hole in TK Edit

This feature provides the auto detect function with ignoring holes based on the size you have specified.

TK Process Type

In order to avoid collision and optimize the process, the new feature provides special assignment and process sequence for TK parts.

P

Enhancement

UV Macro

If the NC contents in one UV macro exceed the machine limits, the system will output the NC codes in more than one UV macros.

Cross cursor

The object that the cross cursor catches is not only the pattern, but also including the edge point, middle point, and the center point of tools.

When the cross cursor appears, we can use the [Home] key to check edge point, the [/] key to check middle point, and the [*] to check center point.

When you enable the cross cursor function, the focus is in the dialog box for inputting value; even the mouse moves from the dialog box, the focus stay in the same place.

Consistent Zoom In Operation

The mouse operation in the result view and edit mode are the same if you select Zoom in option.

Don’t nest parts inside skeleton area

This function in Material Selection panel of Nesting Preference instructs you not to nest smaller parts in the skeleton area near where irregular part has been nested.

Output Report

In the result view, you can select Output Reports from shortcut menu and print the relevant reports.

Part Removal Sequence

In Peripheral Preference, the Take Out Sequence panel changes into the Part Removal Sequence panel. These options in the new screen allow you to change the speed of the axis movement in order to avoid destroying the last part.

Process Unit Sorting

This option in the Sequence Preference allows you to select a process unit sorting between Tool Order Logic and Last Tool Logic. You can use the Last Tool Logic to sort sequence for processing safety, while the Tool Order Logic provides more regular sort method.

Addition Parameter to Clearance

New parameters, Clearance Selection and Process Speed, are added into Clearance Preference in order to control clearance exchange order and process speed.

Tool Include

A new check box, Tool Include, is added into the Utilization Setting window of System Setting to consider tool when calculating the sheet utilization.

Mix Tool Sorting

This check box in the Sequence Preference allows you to assign tools to part on the shortest process path. In that case, the process time can be reduced.

Output Outside of UV

New version allows you to select whether the specified M code is included in the UV macro commands or not.

Auto Calculate the Min or Max Value for Nibbling Pitch

This option in Tool Assign Preference allows you to get a nibbling pitch range by calculating automatically based on your settings.

Width of Micro Joints and Wire Joints for Special Tool

These options in Tool Assign Preference allow you to specify the width of macro joints and wire joints for SP tool.

# Chapter 3: Getting Started

This chapter describes the system requirements, how to launch the system, the main window, the basic settings and the basic workflow.

| See: | System Requirements |
| --- | --- |
|  | Launch Dr.ABE |
|  | Quick Start Guide |

## 3.1 System Requirements

| Hardware | Description |
| --- | --- |
| CPU | Intel Pentium III, AMD Athlon or higher CPU. |
| Memory | 512 MB RAM minimums, 1024 MB recommended. |
| Hard Disk | 300 megabytes of free hard disk space minimum. |
| CD-ROM | A CD-ROM is required for local installation. |
| Graphic Card | A video card capable of supporting a minimum resolution of 1024 x 768. |
| Software | Description |
| Operating system | Windows 2000 or Windows XP. |
| Network | Required for a network installation. |

| See: | Launch Dr.ABE |
| --- | --- |
|  | Quick Start Guide |

## 3.2 Launch Dr.ABE

To launch Dr. ABE, select Start to Programs to Amada to Dr. ABE.

| See: | System Requirement |
| --- | --- |
|  | Quick Start Guide |

## 3.3 Quick Start Guide

This section summarizes the procedure for loading parts, adjusting the nesting schedule, creating nesting layouts and generating NC code. You can review these outlines of the software features for training purposes.

| See: | Dr. ABE Main Window |
| --- | --- |
|  | Basic Dr. ABE Settings |
|  | Basic Operation |

| See: | System Requirements |
| --- | --- |
|  | Launch Dr. ABE |

### 3.3.1 Dr.ABE Main Window

The main window of Dr. ABE is comprised of the following:

| See: | Basic Dr. ABE Settings |
| --- | --- |
|  | Basic Operation |

### 3.3.2 Basic Dr.ABE Settings

When you first launch Dr. ABE, you should perform the following steps:

| 1. | Define the machine parameter. See: Machine Parameter |
| --- | --- |
| 2. | Define the material parameter. See: Material Parameter |
| 3. | Set the system setting. See: System Setting |

| See: | Dr. ABE Main Window |
| --- | --- |
|  | Basic Operation |

### 3.3.3 Basic Operation

| 1. | Once you have installed the program, you can navigate and select the command in the menu (Start to Programs to Amada to Dr. ABE), or double-click the Dr. ABE shortcut icon on the desktop to launch the program. |
| --- | --- |
| 2. | Click the Select Data button to display the Avon Data Selection Dialog window: |
| 3. | Select the part(s) and click Open. |
| 4. | Define the part quantity in the main window and put them into the Nesting Schedule. |
| 5. | Click the Nesting Schedule button to specify the part properties. |
| 6. | Click one Preference button in the main window to display the Preference window. Specify the nesting, tool and sequence conditions in the relevant windows. |
| 7. | In the Main window, click the Auto Execute button to perform the nesting process. |
| 8. | The nesting result, and the NC code, will be displayed in the result view. |
| 9. | Right click the No. cell to open the shortcut menu. Select Save NC Data or Save Schedule to save the data. |
| 10. | Click in the top right corner of the window to exit the program. |

| See: | Dr. ABE Main Window |
| --- | --- |
|  | Basic Dr. ABE Settings |

# Chapter 4: Machine Parameter

Click the Machine Setting  button on the main window to open the Machine Set window. You can specify various machine parameters in this window.

| See: | Machine Parameter Toolbar |
| --- | --- |
|  | Machine Parameter Tree View |
|  | Machine Information |
|  | NC Device Information |
|  | Peripherals |

## 4.1 Machine Parameter Toolbar

| Button | Description |
| --- | --- |
|  | Add a new machine. |
|  | Edit in the selected panel. |
|  | Delete the selected machine. |
|  | Download machine parameters from SDD or MiniSDD. |
|  | Copy machine parameters from specified machine to a new machine. |
|  | Specify the Machine Parameter Server PC to download the machine parameters from. You can also specify the Machine Parameter Server PC in the System panel of the System Setting window. |
|  | Backup or Restore the machine parameters. |

| See: | Machine Parameter Tree View |
| --- | --- |
|  | Machine Information |
|  | NC Device Information |
|  | Peripherals |

## 4.2 Machine Parameter Tree View

|  | Tree View lists the available machines in a hierarchical structure on the left side of the window. Select one machine (e.g.: EM2510) in the tree view to display the detailed information of it. You can click to expand the corresponding item and display its sub-item list. Click to collapse. |
| --- | --- |

| See: | Machine Parameter Toolbar |
| --- | --- |
|  | Machine Information |
|  | NC Device Information |
|  | Peripherals |

## 4.3 Machine Information

| 1. | Click to expand the machine list. |
| --- | --- |
| 2. | Select Machine Information to display the Machine Information panel. |
| 3. | You can check or modify the parameters in the Machine Information panel. |

| See: | Machine Information Panel |
| --- | --- |
|  | Time Study |

| See: | Machine Parameter Toolbar |
| --- | --- |
|  | Machine Parameter Tree View |
|  | NC Device Information |
|  | Peripherals |

### 4.3.1 Machine Information Panel

| Option | Description |
| --- | --- |
| Machine Type | The type of machine that you have defined. The textbox on the right side displays the machine name. |
| Origin | You can input coordinate values in the X, Y, and Z: textboxes to specify the process origin point of the machine. (-9999.99 to 9999.99 mm) |
| Punching Process Range | Specify the punching process range in the X and Y-axis directions. (- 9999.99 to 9999.99 mm) |
| Min | The minimum X and Y limit values for the punching process |
| Max | The maximum X and Y limit values for the punching process |
| Available Pressure (KN) | Specify the maximum available punching pressure. |
| P/F Structure | This option indicates whether a P/F Structure exists. A check mark in the check box indicates the existence of a P/F Structure. |
| Max. Work Thickness | Specify the maximum thickness that can be processed (0.01 to 99.99 mm). |
| Hit Rate | Specify the hit rate of the machine (1 to 9999 HPM). |
| Stroke per Minute | Specify the number of strokes per minute (1 to 9999 SPM). |
| Max. Nibbling Pitch | Specify the maximum nibbling pitch (0.01 to 99.9 mm). |
| Max. Nibbling Angle | Specify the maximum nibbling pitch angle when nibbling an arc by using auto index (0.00 to 99.99 degree). |
| Turret Name | All the turrets associated with the machine are displayed in the drop-down list. |
| Storage Name | All the storages associated with the machine are displayed in the drop-down list. It is only available for the machine with PDC. |
| Multi-Tapping | This option indicates whether multi-tapping exists. If it is set to Yes, then you must specify the tapping information. |
| NC Driver File Path | This drop-down list displays the path and file name of the machine driver file. |
| Clamp |  |
| Max. Setting Position | Specify the maximum limit position when placing the clamps. (0.0 to 999.99 mm). |
| Positioner | Specify whether a repositioning clamp exists. |
| Min. Space | Specify the minimum space between two auto avoidance clamps. |
| Auto Avoidance Clamp | This option indicates whether auto avoidable clamps exist. Note: If you remove the check mark from the Yes/No: check box, the Min. Space option will be disabled as well. |
| Y-Direction Offset Amount | Define the offset amount in the Y-direction when using offset clamps. |
| Y- Direction Dead Zone | Define the dead zone range in Y-direction when MERK is used. |
| Repositioning | This option indicates whether the repositioning function is supported when MERK is used. |
| Air Blower | Specify whether the air-blow function is available. If the machine type is VIPROS, this option does not appear because it is set to On automatically for a VIPROS machine. |
| M Codes | If the Air Blower is enabled, you can specify the starting and ending M codes. |
| Energy Save | Specify whether to enable Energy Save mode. If the machine type is NCT, this option does not appear. |
| M Codes | If the Energy Save is enabled, you can specify the starting and ending M codes. |
| Time Study | Click the Time Study button to display the Process Time Addition Info window where you can specify the process time settings. See: Time Study. |

| See: | Time Study |
| --- | --- |

### 4.3.2 Time Study

The Process Time Addition Info window will appear after you click the Time Study button in the Machine Information panel. The options in this window allow you to specify the process time settings.

| Option | Description |
| --- | --- |
| Various Parameters (Actual#) |  |
| Multi Tapping | This option is not available for the moment. |
| Tap in Turret | This option is not available for the moment. |
| Burring | This option is not available for the moment. |
| Forming | This option is not available for the moment. |
| PDC/PDC2 Tool Change | The time to change the PDC/PDC2 tool |
| Others (0~4) | This option is not available for the moment. |
| Various Parameters (Integer) |  |
| Process Speed | Specify the turret running mode. (1 to 4) If you set the Process Speed to 1, the turret will run with the highest speed. |
| Others (0~4) | This option is not available for the moment. |
| M-code | This option is not available for the moment. |
| Time | This option is not available for the moment. |
| Apply | This option is not available for the moment. |
| Delete | This option is not available for the moment. |
| Number | This option is not available for the moment. |
| M-Code | This option is not available for the moment. |
| Time | This option is not available for the moment. |

| See: | Machine Information Panel |
| --- | --- |

## 4.4 NC Device Information

Select NC Device Information to display the NC Device Information panel.

| Option | Description |
| --- | --- |
| NC Device Name | This text box will display the NC device name and specify when a machine is registered. |
| NC Data Unit | You can define the NC program data unit by selecting the Metric or Inch option button. |
| Point | This option allows you to decide whether the NC program uses the decimal point. (If the decimal point does not exist, 100 will be regarded as 1.00). |
| Digit within Point | You can specify the digit within point by selecting the items in the list box. |
| Input Integer | This item indicates whether integer is input. If you select Yes, the integer data input with aliases is converted to standard data. If the process machine is a laser machine, ignore this item. |
| Max. Macro Memory Amount | Specify the maximum number of macro characters that can be stored in the U-V macro (0 to 32000). If the NC device is the FS- 16, this item is disabled. |
| Pattern Memory | You can specify the number of patterns that can be stored (0 to 99). |
| Address Memory | You can specify the number of addresses that can be stored. This item can be defined only when using the F3000C or other NC devices that can store a limited number of addresses. If the NC device cannot store any addresses, set this item to 0. |
| Memory Space | Define the memory space of the NC device. |
| G25 Power | This option allows you to specify the output of G25. This option decides which G code, G25 or G27, will be output for the first reposition during NC data generation. If Yes is selected, G25 is output for the first reposition during NC program generation and G27 will be used for the second time. If No is selected, G27 will be output for all the repositioning. |
| CPU Type | The type of CPU the machine uses. |
| Max. Punch | Specify the number of trial punches. For the first step machine, 5000 is defined; for the second step machine, 10000 is defined. |
| User Memory | Specify the memory space of the NC device with the tape length (0 to 9999). |
| Max. File Register Amount | Specify the maximum number of files that can be registered in the NC device (0 to 32767). |
| Output Arc | Specify the output type of arc for laser machine. |
| R | Output the arc with R, and if the arc angle is greater than 180 degrees, output it with I and J. |
| I J | Output the arc using I, J (I is the X-axis dimension from the start point of the arc to the end point; J is the Y-axis dimension from the start point of the arc to the end point). |
| User Macro Version | Define the version of the user macro (3.0 to 5.0). If the NC device is the FS-16, ignore this item. |
| 3.0 | Machine without the Z-axis |
| 4.0 | Machine with the Z-axis |
| 5.0 | High-speed format。 |
| Axis Move Mode | This option allows you to determine the method for moving the laser head axis. |
| Fixed | Move with fixed angle. |
| Direct | Direct move. |

| See: | Machine Parameter Toolbar |
| --- | --- |
|  | Machine Parameter Tree View |
|  | Machine Information |
|  | Peripherals |

## 4.5 Peripherals

Click   to expand the Peripherals list.

| See: | Clamp Information |
| --- | --- |
|  | Holder Information |
|  | MJC |
|  | IJP |
|  | Loading/Unloading Device |
|  | Work Chute Information |
|  | Take Out Information |
|  | Tapping Information |

| See: | Machine Parameter Toolbar |
| --- | --- |
|  | Machine Parameter Tree View |
|  | Machine Information |
|  | NC Device Information |

### 4.5.1 Clamp Information

Select Clamp Information to display the Clamp Information panel.

| Option | Description |
| --- | --- |
| Number | The number of clamps. There is specific set of parameter for each clamp, including Type, Clamp Axis, Clamping Width and Length, Placement Position X and Y, Placement Position Limit X and Y, Senor Placement Position, Senor Size X and Y, Dead Zone X and Y. |
| ON/OFF | You can select which set of parameters the system will use by placing a check mark in the ON/OF: checkbox. You can add additional clamps using the Add Clamp button and specifying the parameters. You can remove parameters using the Delete Clamp button. |
| Type | You can click the down arrow to open the drop down list and select clamp type: Thin Sheet, Thick Sheet, Offset or Small. |
| Clamp Axis | The direction of clamp placement: X or Y. |
| Clamping Width and Length | You can define the width and length of the clamp. |
| Placement Position X and Y | You can define the X and Y position where the clamp is placed. |
| Placement Position Limit X and Y | You can define X and Y position to define the placement of clamp. |
| Sensor Placement Position | You can change the sensor position by selecting the options in the list box. There are four options: None, Left, Right and Bi-directional. |
| Sensor Size X and Y | You can define X and Y size of the sensor. |
| Dead Zone X and Y | You can specify the Dead Zone by typing X and Y coordinates. |
| Button | Description |
| Add Clamp | Click this button to add a new clamp parameter. |
| Delete Clamp | Select a set of parameters that you want to delete and then click the Delete Clamp button. The system will prompt you to confirm. Click Yes to confirm and to delete the parameters. |
| Refresh | Click the Refresh button after modifying the parameter to apply the new setting. |

| See: | Holder Information |
| --- | --- |
|  | MJC |
|  | IJP |
|  | Loading/Unloading Device |
|  | Work Chute Information |
|  | Take Out Information |
|  | Tapping Information |

### 4.5.2 Holder Information

Select Holder Information to display the Holder Information panel.

| Option | Description |
| --- | --- |
| 1st, 2nd and 3rd | Place a check mark in the corresponding check box to make modifications to the holders. |
| Type | Select the type of the holder by choosing the option from the drop-down list. |
| Size | Specify X and Y size of the work holder (0.00 to 99.99). |
| Position | Specify X and Y position of the work holder (- 999.99 to 999.99). |

| See: | Clamp Information |
| --- | --- |
|  | MJC |
|  | IJP |
|  | Loading/Unloading Device |
|  | Work Chute Information |
|  | Take Out Information |
|  | Tapping Information |

### 4.5.3 MJC

MJC is an acronym for Micro Joint Cutter.

Micro joints are tabs that you can place on the part corners or along the part perimeters.

These uncut sections prevent the parts from falling out of the sheet.

The MJC device is used to remove micro joints after the punch process is complete.

Select MJC to display the MJC panel.

| Option | Description |
| --- | --- |
| MJC | If a MJC device is provided, place a check mark in the Yes/No: check box. Remove the check mark if there is no MJC device. |
| Work and Part | This section allows you to specify the properties of the sheets and parts. |
| Work Thickness | Specify the minimum and maximum thickness of the sheet for processing. |
| Work Size X/Y | Specify the minimum and maximum dimension of the sheet in X/Y direction. |
| Min. Part Size X/Y | Specify the minimum dimension of the part in X/Y direction. The part size is specified by rectangular size of the part shape. |
| Cutter | This section allows you to specify the offset of the cutter in X and Y directions. A cutter is used to pick up the parts with joints. |
| Micro Joint | Joints on corner. |
| Wire Joint | Joints on line. |
| Special Tool Joint | Joints processed by specific tools. |
| Driver Type | Select one driver type from the drop-down list. |
| Cutter Size X/Y | Input value to specify the dimension of cutter in X and Y direction. |
| Upper Cutter Size X/Y | Input value to specify the dimension of upper cutter in X and Y direction. |

| See: | Clamp Information |
| --- | --- |
|  | Holder Information |
|  | IJP |
|  | Loading/Unloading Device |
|  | Work Chute Information |
|  | Take Out Information |
|  | Tapping Information |

### 4.5.4 IJP

IJP is an acronym for Ink Jet Printer.

The IJP is used to print information on the parts.

Select IJP to display the IJP panel.

| Option | Description |
| --- | --- |
| IJP | If an IJP is provided, place a check mark in the Yes/No: checkbox. |
| NO | There are three sets of parameters available. You can set the parameters in IJP panel of Peripheral preference. |
| Maker | The manufacturer code for the IJP device. |
| Max String Size X/Y | These fields are used to specify the maximum string size in X/Y direction. The following figure indicates the string size in X/Y direction: |
| Max String Number | This field is used to specify the maximum string number in a line. |
| Line Feed Character | This field is used to specify the character used for line feeds. Then the character is the code for the beginning of a new line. For example, if you specify “//” as the line feed character, and then input “123//4567//890” for the ink-jet marking string, the IJP will print: |
| Max Number of Lines | This field is used to specify the maximum number of lines that can be printed at one time. |
| String Pitch X, Y | These fields are used to specify the pitch between strings in the X/Y direction. The following figure indicates the string pitch in the X/Y direction. |
| Raster Size ID | Specify the character size that will be sent to the Ink Jet Printer. The Ink Jet Printer determines the character size and pitch for printing according to the raster size information and string size information. (This is used when hole interference is checked in Simulation. The actual character size is determined by this information.) |
| String Size ID | Character size information that is sent to Ink Jet Printer. |

| See: | Clamp Information |
| --- | --- |
|  | Holder Information |
|  | MJC |
|  | Loading/Unloading Device |
|  | Work Chute Information |
|  | Take Out Information |
|  | Tapping Information |

### 4.5.5 Loading/Unloading Device

Select Loading/Unloading Device to display the Loading/Unloading Device panel.

| Option | Description |
| --- | --- |
| Tandem Device Type | You can select the tandem device type provided in the list box and the presence/absence of the automatic material carryout function. |
| Thickness Command M-Code | You can define the M code and its corresponding range of material thicknesses. When the machine is required to output the M-Code for the thickness, the corresponding pre-defined M-Code is used for target material according to the range of material thickness. For example, if the material thickness is 0.50, then the code will be 22. |
| End Position M-Code | You can define the M code and its corresponding range of material X size. When the machine is required to output the end position M-Code, the pre-defined M-Code will be used for target material according to the range of material X size. For example, if the material X size is 1000.00 the end position M code will be 55. |
| Pad Group Definition M-Code | You can define the M code and its corresponding range of material X, Y size. When the machine is required to output M-Code for the pad group, the pre-defined M-Code will be used for the target material according to the range of material X, Y sizes. For example, if the material size X is1900 and material size Y is 1000, the M code will be 322. (If dimension is the same as the input value, it is defined as "within".) |

| See: | Clamp Information |
| --- | --- |
|  | Holder Information |
|  | MJC |
|  | IJP |
|  | Work Chute Information |
|  | Take Out Information |
|  | Tapping Information |

### 4.5.6 Work Chute Information

Select Work Chute Information to display the Work Chute Information panel.

| Option | Description |
| --- | --- |
| 1st and 2nd | If there is only one work chute, place a check mark in the 1st check box. If there are two work chutes, place check marks in both the 1st and 2nd check boxes. Check the option to enable the corresponding work chute information. |
| Size X and Y | Specify the work chute X and Y size (0.00 to 9999.99). |
| Replacement Position X and Y | Specify the work chute X and Y position. This option indicates the displacement from the punch center to the upper right point of the work chute. (- 999.99 to 9999.99). |
| Dwell Time | Specify the dwell time. This is the time when the work chute opens to the time when it closes (0.00 to 9999.99). |
| Start M Code | Specify the M code for opening the work chute (0 to 999). |
| End M Code | Specify the M code for closing the work chute (0 to 999). |
| Dead Zone Position X and Y | Specify X and Y position of the work chute dead zone. |
| Dead Zone Area X and Y | Specify X and Y position of the dead zone area. |

| See: | Clamp Information |
| --- | --- |
|  | Holder Information |
|  | MJC |
|  | IJP |
|  | Loading/Unloading Device |
|  | Take Out Information |
|  | Tapping Information |

### 4.5.7 Take Out Information

Select Take-out Information to display the Take-out Information panel.

The options in this panel allow you to define take-out type, unloading code, stacking table information, and the arm information.

| Option | Description |
| --- | --- |
| Taking Out | Specify whether the machine is equipped with an unloading device. A check mark in the Yes/No: checkbox indicates that the machine is equipped with an unloader. Remove the check mark if your machine is not equipped with an unloader/stacking device. |
| Type of Taking Out |  |
| Type of Taking Out | Select a TK type from the drop-down list. The are two types of TK devices, PartRemoverII and Hyper TK. |
| Taking Out Direction | Specify the direction in which TK device carries out parts. |
| Unloading M Code |  |
| Unloading Skeleton Sheet M Code | Specify the M code for unloading the skeleton sheet. For example, 58. |
| Unloading Micro Joint Sheet M Code | Specify the M code for unloading the micro joint sheet. For example, 59. |
| Skeleton to Scrap Shear M Code | Specify the M code for skeleton to scrap shear. For example, 57. |
| Stacking Scheme |  |
| Maximum Height | Specify the maximum height for stacking parts in the table. |
| Table Size X and Y | Specify the X and Y dimensions of the table. |
| Maximum Weight | Specify the maximum weight for stacking parts on the table. |
| Arm information |  |
| Minimum Arm Opening | Specify the minimum space between the TK arms. |
| Maximum Arm Opening | Specify the maximum space between the TK arms. |
| Arm X and Y Size | Specify the X, Y arm size. |
| M Code of Taking Out | Specify the Pickup M code. The options in this section are only available for hyper TK device. |
| Vacuum > Cut > Pickup | The M code that instructs the machine to vacuum the part and then perform the last cutting process only in the Y-axis. |
| Cut > Vacuum > Pickup | The M code that instructs the machine to perform the last cutting process in both X and Y-axis and then vacuum the part. |
| Pickup M Code | The M code that instructs the machine to pick up the part. |
| M Code For Moving Waiting Position | The M code that instructs the machine to move the arm to the waiting position, and it can shorten the time to move the arms. |
| PR/TK Parameter |  |
| XHome | The distance in X-direction from the punch center to home positon of the X-axis (mm). |
| XWait | The distance in X-direction from the tool center line to suction cup arm (mm). |
| Xstack0 | The distance in X-directon from the punch center to where the stacking area begins (mm). |
| YPickMax | The maximum distance in Y-direction from the tool center line to suction cup arm B that PR can pick-up (mm). |
| YAHome | The distance in Y-direction from the tool center line to suction cup arm A home position (mm). |
| XPickMin | The minimum distance in X-dirtection from the punch center to where PR can pick-up (mm). |
| YBHome | The distance in Y-direction from the tool center line to suction cup arm B home position (mm). |
| Information of Station | Specify the information of places to stack the parts. The options in this table are only available for the Hyper TK device. |
| Name | Specify the name of the place to stack the parts. |
| Station Type | Specify how to take out the parts. There are three options, Work Chute, Pallet and Conveyor. |
| M Code | Define the M code (0~9999) to take out the parts. |
| Min X | The minimum X dimension of the parts that can be taken out |
| Max X | The maximum X dimension of the parts that can be taken out |
| Min Y | The minimum Y dimension of the parts that can be taken out |
| Max Y | The maximum Y dimension of the parts that can be taken out |

| See: | Clamp Information |
| --- | --- |
|  | Holder Information |
|  | MJC |
|  | IJP |
|  | Loading/Unloading Device |
|  | Work Chute Information |
|  | Tapping Information |

### 4.5.8 Tapping Information

Select Tapping Information to display the Tapping Information panel.

| Option | Description |
| --- | --- |
| Check Boxes 1 through 8 | Place a check mark in the check box to activate the corresponding tapping options. |
| Placement Position |  |
| Size | The tapping M diameter. |
| X | The X position of the tapping placement position. The X value is measured from the punch center. |
| Y | The Y position of the tapping placement position. The Y value is measured from the punch center. |
| Dead Zone |  |
| X | The length of the dead zone in the X direction. The center is measured from the center of the clamp. |
| Y | The height of the dead zone in the Y direction. The Y direction is measured from the material end point. |
| M Code |  |
| Start | The starting M code for the tapping process. |
| End | The ending M code for the tapping process. |

| See: | Clamp Information |
| --- | --- |
|  | Holder Information |
|  | MJC |
|  | IJP |
|  | Loading/Unloading Device |
|  | Work Chute Information |
|  | Take Out Information |

# Chapter 5: Material Parameter

Click the Material Management button in the main window to open the Dr.ABE Material Management window. There are three panels: Material Type Information, Sheet Information and Tube Material Information.

| See: | Material Manager Toolbar |
| --- | --- |
|  | Material Type Information |
|  | Sheet Information |
|  | Tube Material Information |

## 5.1 Material Manager Toolbar

| Button | Description |
| --- | --- |
|  | Click New button to create new Material Type, Sheet Information or Tube Material Information parameters. |
|  | Click Edit button to modify the selected Material or Sheet information parameters. |
|  | Click Delete button to remove the selected Material or Sheet information from the list. |
|  | Click Get Data from SDD or MiniSDD button to download sheet information from SDD or MiniSDD. |
|  | Click Options button specify the Material Parameter Server PC. |
|  | Click Backup/Restore button to backup or restore Material type information, sheet information and tube material information. |

| See: | Create a Material Type |
| --- | --- |
|  | Edit a Material Type |
|  | Delete a Sheet Information |
|  | Download Material Type From AP100 |
|  | Option |
|  | Backup and Restore Material |

| See: | Material Type Information |
| --- | --- |
|  | Sheet Information |
|  | Tube Material Information |

### 5.1.1 Create a Material Type

| To create a material type, |
| --- |
| 1. | Click Mat. Type Information tab first and then click New button on the toolbar to enable the textboxes on the right side of the window. |
| 2. | Specify name and values accordingly in the Material Type, Specific Gravity and Tensile Strength: textboxes for the new material. |
| 3. | Click Add button to add the new material information into the Mat. Type Information list. |
| 4. | Now the new material is available in the Material Type: drop-down list when you edit in the Sheet Information tab or Tube Material Information tab. |

| See: | Edit a Material Type |
| --- | --- |
|  | Delete a Sheet Information |
|  | Download Material Type From AP100 |
|  | Option |
|  | Backup and Restore Material |

### 5.1.2 Edit a Material Type

| To edit a material type, |
| --- |
| 1. | Select the material type that you want to modify in the Mat. Type Information list. |
| 2. | Click Edit button on the toolbar to enable the textboxes on the right side of the window. |
| 3. | Modify the name or values in the Material Type, Specific Gravity and Tensile Strength: textboxes. |
| 4. | Click Modify button to save your changes and continue to edit the next material type. |
| 5. | Click Done to finish. |

| See: | Create a Material Type |
| --- | --- |
|  | Delete a Sheet Information |
|  | Download Material Type From AP100 |
|  | Option |
|  | Backup and Restore Material |

### 5.1.3 Delete a Sheet Information

| To delete a sheet information, |
| --- |
| 1. | Click the Sheet Information tab and select the sheet information that you want to delete from the list. |
| 2. | Click Delete button on the toolbar. The Dr. ABE Material Management dialog will appear and prompt you to confirm. Click OK to remove the sheet from the list or click Cancel to cancel. |

| See: | Create a Material Type |
| --- | --- |
|  | Edit a Material Type |
|  | Download Material Type From AP100 |
|  | Option |
|  | Backup and Restore Material |

### 5.1.4 Download Material Type from AP100

| To download material types from AP100, |
| --- |
| 1. | Click Get Data from SDD or MiniSDD button. The Material Parameter Download window will appear: |
| 2. | Select Only download material code (Sheet Code) of AP100. The material code of AP100 will be downloaded into the Dr. ABE Material Manager. |
| 3. | Select Download AP100 material type, then register the material code of each type in Standard Sheet Registration window to download all the AP100 material types. The Standard Sheet Register window will appear. |
| 4. | Click OK to download the material types with check mark(s) into the Dr. ABE Material Manager. |
| 5. | Click Sheet Size Definition button to display the Sheet Size Define window. You can define different sheet sizes, codes and quantities for the same material type in the window. |
| 6. | Click OK. The third one has been registered to this material type. |

| See: | Create a Material Type |
| --- | --- |
|  | Edit a Material Type |
|  | Delete a Sheet Information |
|  | Option |
|  | Backup and Restore Material |

### 5.1.5 Option

| 1. | Click Options button on the toolbar to display the Options window. |
| --- | --- |
| 2. | Specify the new server name in the Material Parameter Serve PC: textbox. Click OK to confirm, or click Cancel to cancel. |

| See: | Create a Material Type |
| --- | --- |
|  | Edit a Material Type |
|  | Delete a Sheet Information |
|  | Download Material Type From AP100 |
|  | Backup and Restore Material |

### 5.1.6 Backup and Restore Material

This option allows you to easily backup and restore the material information.

Click the Backup Restore  button on the toolbar to display the Dr. ABE System Backup&Restore Material window.

| See: | How to Backup Material |
| --- | --- |
|  | How to Restore Material |

| See: | Create a Material Type |
| --- | --- |
|  | Edit a Material Type |
|  | Delete a Sheet Information |
|  | Download Material Type From AP100 |
|  | Option |

#### 5.1.6.1 How to Backup Material

| 1. | In the Dr. ABE Backup&Restore Material window, click the item(s) that you want to backup in the Items to Backup section. |
| --- | --- |
| 2. | Click the Browse button next to the File Name: text box to display the Choose a backup file window. To overwrite an existing backup zip file, navigate to the destination folder and select it. To create a new backup zip file, navigate to the destination folder and specify a name in the File name: textbox. Then, click Open to close the window. |
| 3. | The specified name will appear in the File Name: textbox. Click the Backup button to perform the backup process and make the backup zip file to the destination folder. |

| See: | How to Restore Material |
| --- | --- |

#### 5.1.6.2 How to Restore Material

| 1. | In the Dr. ABE Backup&Restore Material window, click the item(s) that you want to restore in the Items to Restore section. |
| --- | --- |
| 2. | Click the Browse button next to the File Name: text box to display the Choose a backup file window. Navigate to the destination folder and choose the backup zip file that you want to restore. Then, click Open to close the window. |
| 3. | The specified name will appear in the File Name: textbox. Click the Restore button to perform the restore process. The material information will be restored to the program. |

| See: | How to Backup Material |
| --- | --- |

## 5.2 Material Type Information

The Material Type Information panel will list all the available material types.

You can create, edit, delete and download the material types.

| Column Title | Description |
| --- | --- |
| Material Type | The name of the material type. |
| Specific Gravity | The specific gravity of a material. The specific gravity is the ratio of the density of a substance to the density of another substance (such as pure water) taken as a standard when both densities are obtained by weighing in air. |
| Tensile Strength | The tensile strength of the material. Tensile strength is the greatest longitudinal stress that a substance can bear before failure. |

| See: | Material Manager Toolbar |
| --- | --- |
|  | Sheet Information |
|  | Tube Material Information |

## 5.3 Sheet Information

The Sheet Information panel allows you to view all of the information associated with a sheet. You can also create, edit, delete and download sheet information.

| Column Title | Description |
| --- | --- |
| Sheet Code | The Sheet Code: textbox displays the sheet code. |
| Material Type | The Material Type: textbox displays the material type that was specified in the Material Type Information panel. |
| Thickness | The Thickness: textbox displays the material thickness specified upon the material registration. You can use the up and down arrow to edit the value or type a value in the textbox. |
| Material Name | Type the material name in this textbox. |
| Sheet Size X/Y | The horizontal and vertical dimension of the sheet specified upon the material registration. |
| Qty. | This textbox displays the quantity of the sheets specified upon the registration. |
| Price | The unit price of the sheet. You can type a new price in the textbox. |
| Grain Direction | The direction of the sheet texture: Vertical, Horizontal. |
| Comment | Type the comments for the material in this textbox. |
| Special Information | This section allows you to specify special information for the material. There are three options you can select from the drop-down list. None, Coated and Colored Steel. |
| Sheet Type | This option allows you to specify the different sheet types. Click the arrow button and select the type from the drop-down list: Standard, Remnant, Skeleton or Sketch. |
| Priority | Define the priority for the material. |
| Skeleton File Path | This option is used to specify the file path of sheet registered as skeleton material. Only XML file that is generated as a result of the nesting process is used. |
| Sheet Profile | This section is used to preview the profile of the sheet that can be used. The white area represents the sheet. |

| See: | Standard, Remnant, Skeleton and Sketch Materials |
| --- | --- |
|  | How to Create a Remnant Sheet |
|  | How to Create a Skeleton Sheet |

| See: | Material Manager Toolbar |
| --- | --- |
|  | Material Type Information |
|  | Tube Material Information |

### 5.3.1 Standard, Remnant, Skeleton and Sketch Materials

There are four types of material: Standard, Remnant, Skeleton and Sketch.

Each sheet type is with a different color in the material table.

A remnant is an unused rectangular area of a sheet due to the results of the nesting process. The remnant will be registered in material management after saving the NC data.

A skeleton is the remaining material after the part(s) on the sheet is/are removed. The remainder of the sheet can be reused to increase sheet utilization.

Sketch material is a sheet that has the same X/Y size as that of the part, i.e., there can only be one part per sheet. The method used to process only the notches and holes is known as the sketch process, and the material used at that time is called the sketch material.

| See: | How to Create a Remnant Sheet |
| --- | --- |
|  | How to Create a Skeleton Sheet |

### 5.3.2 How to Create a Remnant Sheet

| 1. | Click the Nesting button to display the Nesting window, and then click the Material Selection tab to display the Material Selection panel. |
| --- | --- |
| 2. | Select Create Remnant in the Reusable Sheet section, and then define the Pitch, Min X Size and Min Y Size values. |
| 3. | The remnant will be created if the remainder of the sheet matches the specified conditions after processing. |
| 4. | The created Remnant sheet will be listed in the Material Management window after you save the NC data. |

| See: | Standard, Remnant, Skeleton and Sketch Materials |
| --- | --- |
|  | How to Create a Skeleton Sheet |

### 5.3.3 How to Create a Skeleton Sheet

| 1. | Click the Nesting button to display the Nesting window, and then click the Material Selection tab to display the Material Selection panel. |
| --- | --- |
| 2. | Select Create Skeleton Sheet in Reusable Sheet section, and then specify the Max Utilization value. |
| 3. | The skeleton sheet will be created if the remainder of the sheet matches the specified condition after processing. The Skeleton sheet will be listed in the Material Management window after you save the NC data. |

| See: | Standard, Remnant, Skeleton and Sketch Materials |
| --- | --- |
|  | How to Create a Remnant Sheet |

## 5.4 Tube Material Information

The Tube Material Information panel allows you to view all the material information for tube processing.

You can also create, edit and delete the tube material information.

| Column Title | Description |
| --- | --- |
| Pipe Name | The name of the pipe material. |
| Material Type | The Material Type: textbox displays the material type that was specified in the Material Type Information panel. |
| Thickness | The Thickness: textbox displays the material thickness specified upon the material registration. You can type a value in the textbox to define the thickness of material. |
| Pipe Type | Two pipe types can be selected: Round or Square. |
| Length | The Pipe Length text box is used to specify the length of the pipe. |
| Width | The Width: textbox is used to specify the width of the pipe. |
| Height | The Height: textbox is used to specify the height of the pipe. |
| Corner Radius | The Corner Radius: textbox is used to specify the corner radius of the pipe. |
| Seam Position | Select the position of the pipe seam. |
| Comment | Type comments for the pipe material in this textbox. |
| Profile | This section is used to preview the profile of the pipe material. |

| See: | Material Manager Toolbar |
| --- | --- |
|  | Material Type Information |
|  | Sheet Information |

# Chapter 6: System Setting

Click the System Setting  button in the Dr. ABE main window to display the System Setting window.

The options in this window allow you to set all your preferences for Dr. ABE.

Click OK to accept the changes and close the window.

Click Cancel to close the window without saving any changes.

| See: | View |
| --- | --- |
|  | System |
|  | Option |

## 6.1 View

Click the View tab in the System Setting window to display the View panel.

This panel allows you to configure the overall views for CAD Data Drawing, Main Window and Result View.

| See: | Main Window |
| --- | --- |
|  | CAD Data Drawing |
|  | Drawing |
|  | Information Area |
|  | Zoom |
|  | Utilization Setting |

| See: | System |
| --- | --- |
|  | Option |

### 6.1.1 Main Window

The options in this section allow you to define the system settings, such as the machine and material parameters and message display.

Machine Manager Setting

Dr. ABE is compatible with AP100. If MiniSDD or SDD is installed on your PC, two machine parameter databases are available: Dr. ABE and AP100.

If Dr. ABE Machine Manager is selected from the drop-down list, the Dr. ABE machine manager will display in the Machine Set window.

If SDD Machine Manager is selected, the AP100 machine manager will display in the Machine Manager window. The machine parameter in AP100 will be downloaded to the Dr. ABE machine parameter after you close the window.

Note: Select whether to download machine parameter from SDD or MiniSDD.

Material Manager

Dr. ABE is compatible with AP100. If MiniSDD or SDD is installed on your PC, two material parameter databases are available: Dr. ABE and AP100.

If Dr. ABE Material Manager is selected, the Dr. ABE Material Management window will display.

If SDD Material Manager is selected, the AP100 material manager will display in the Material Manager window. After you close the window, the material parameter in the AP100 will be downloaded to the Dr. ABE material manager.

Note: Select whether to download material parameter from SDD or MiniSDD.

Message at the Completion of Automatic Processing

The default message is “Complete!!” You can type other message in the textbox.

| See: | CAD Data Drawing |
| --- | --- |
|  | Drawing |
|  | Information Area |
|  | Zoom |
|  | Utilization Setting |

### 6.1.2 CAD Data Drawing

|  | This section is used to define the display format of CAD data drawing. The available formats are unfolded drawing and 3D drawing. |
| --- | --- |

The difference between 3D and Unfolded

| 1. | In the main window: |
| --- | --- |
|  | 3D |  |
|  | Unfolded |  |
| 2. | In the Nesting Schedule: |
|  | 3D |  |
|  | Unfolded |  |

| See: | Main Window |
| --- | --- |
|  | Drawing |
|  | Information Area |
|  | Zoom |
|  | Utilization Setting |

### 6.1.3 Drawing

The options in this section control the display view of the nesting result.

| Option | Description |
| --- | --- |
| Quality | The system will display a result drawing of high quality, but this will increase the running time. |
| Speed | The system will display a simple result drawing that will reduce the running time. This option is selected by default. |
| View Y Size | Define the default width of Result View area after auto execution. |
| Display Setting | Click this button to display the Display Setting window. You can select different colors to display the elements in the result drawing. |
| Expand All is done after Automatic | This option is used to control whether you can open and close all generated sheet layouts at one time. |
| Max Number of Open Sheets | Define the maximum number of generated sheets layouts that you can open at one time. |
| Zoom in The Part Edit Display to | Type value in the nearby box to define the magnifying dimension for window in which you can edit part. |

| See: | View Y Size |
| --- | --- |
|  | Difference between Quality and Speed |
|  | Display Different Colour for Elements on the Part |
|  | Expand all is down after automatic |

| See: | Main Window |
| --- | --- |
|  | CAD Data Drawing |
|  | Information Area |
|  | Zoom |
|  | Utilization Setting |

#### 6.1.3.1 View Y Size

| Define the default width of Result View area after auto execution. |
| --- |
| 1. | Set the View Y Size to 300. |
| 2. | Click Auto Execution button to display Result View. |
| 3. | Set the View Y Size to 200. |
| 4. | Click Auto Execution button. Display Result View. |

| See: | Difference between Quality and Speed |
| --- | --- |
|  | Display Different Colour for Elements on the Part |
|  | Expand all is done after automatic |

#### 6.1.3.2 Difference between Quality and Speed

The following pictures indicate the difference between Quality and Speed.

The result view in Quality mode is as below.

The result view in Speed mode is as below.

| See: | View Y Size |
| --- | --- |
|  | Display Different Colour for Elements on the Part |
|  | Expand all is done after automatic |

#### 6.1.3.3 Display Different Colors for the Elements on the Part

Click the Display Setting button, the Display Setting window displays.

In this window, you can specify different colors for the items in the table.

You can select the item by placing the check mark in the check box, and click the color cell to display the palette to change the color.

| Quality Mode | Speed Mode |
| --- | --- |

| Items | Description |
| --- | --- |
| Items | The name of the item that you can specify the colour. |
| Colour | The colour that is used to display the item in the result view. |
| Special Options |  |
| Punch Tool is Transparent | Select this option and punch tools will be displayed in construction line in the result view. This option is only available for punch machines. |
| By Process After | Select this option to enable the Process After colour settings. |
| Setting | Click this button to display the Display Setting of Process After window. In this window, you can click the square box to display the colour palette and change the colour for the corresponding Process After method. The system will use the specified colour to display the objects that will be processed by the corresponding process after method. |
| Background Colour | Specify the background colour in the result view. |

Example

| 1. | In the Quality Mode, the default colour of Lead In is green. In the result view, the Lead In is displayed in green. |
| --- | --- |
| 2. | Change the Lead In colour to blue. |
| 3. | Now the lead in is displayed in blue in the Result View. |
| 4. | In the Process After Cutting window, select Machine Stop from the process: drop-down list as the end value of the inner loop process: |
| 5. | In the Display Setting window, select By Process After and then click Setting button to open the Display Setting of Process After window. In this window, you can set red for the Machine Stop. |
| 6. | You can see the result is as follow. The inner loop appears in red. |

| See: | View Y Size |
| --- | --- |
|  | Difference between Quality and Speed |
|  | Expand all is done after automatic |

#### 6.1.3.4 Expand All is Done after Automatic

| This option is used to control whether you can open and close all generated sheet layouts at one time. |
| --- |
| 1. | When the Expand All is Down after Automatic: check box remains empty, |
| 2. | The sheet layouts would not display after auto-execution. |
| 3. | When you place a check mark in the Expand All is Down after Automatic: check box, |
| 4. | The sheet layouts will display after auto-execution. |

| See: | View Y Size |
| --- | --- |
|  | Difference between Quality and Speed |
|  | Display Different Colour for Elements on the Part |

### 6.1.4 Information Area

The options in the Information Area allow you to define which information panels will display in the Result View, and the X size of the information area.

The available information panels include: Parts Info, Error List and NC Data.

The selected information will display in the Result View.

| See: | Main Window |
| --- | --- |
|  | CAD Data Drawing |
|  | Drawing |
|  | Zoom |
|  | Utilization Setting |

### 6.1.5 Zoom

You can define the magnification proportion of Zoom operation in the Result View.

| Option | Description |
| --- | --- |
| Zoom In Ratio | Each magnifying operation will enlarge graphic by the percentage specified here. |
| Zoom Out Ratio | Each reducing operation will reduce graphic by the percentage specified here. |
| Auto Scale Clearance Value | This option allows you to define the display margin in Auto Scale operation. For example, if you set 10% as the Auto Scale Clearance Value, the distance from parts with bounding box to the four boundaries of result display area will be not less than 10% when you use Auto Scale. |
| Auto Scale Clearance Value of Error | This option allows you to define the clearance value of the errors that display in the Result View. For example, you set 10% as the clearance of displayed error. Click Error Information from the Error List to find the corresponding error in the part. The error will be displayed as follow. The distance from the error section with a bounding box to the one of four boundaries that is the most close to the error section is 10%. |
| When you set Auto Scale Clearance Value to 10%, the system will display the parts as follows. |
| When you set Auto Scale Clearance Value of Error to 10%, the system will display the parts as follow. |

| See: | Main Window |
| --- | --- |
|  | CAD Data Drawing |
|  | Drawing |
|  | Information Area |
|  | Utilization Setting |

### 6.1.6 Utilization Setting

|  | Click this button to open the Utilization Setting window. You can specify whether to consider holes when calculating the sheet utilization. |
| --- | --- |

Example

| 1. | We will process the following part with an inner loop. |
| --- | --- |
| 2. | If we place a check mark in the Holes Include: check box. (Tool Include: check box remains empty) After auto execution, it shows the utilization is 10.498%, and the inner loop area is included and tool area is excluded when calculating the sheet utilization. |
| 3. | If we remove the check marks from both the Holes Include: check box and the Tool Include: check box, after auto execution, it shows the utilization is 5.863%. Both the inner loop area and the tool area are excluded when calculating the sheet utilization. |
| 4. | If we place check marks in both the Tool Include: check box and Holes Include: check box, after auto execution, it shows the utilization is 11.406%, and both the inner loop area and tool area are included when calculating the sheet utilization. |
| 3. | If we remove the check mark from the Holes Include: check box and place a check mark in the Tool Include: check box, after auto execution, it shows the utilization is 6.771%, and the inner loop area is excluded and the tool area is included when calculating the sheet utilization. |

| See: | Main Window |
| --- | --- |
|  | CAD Data Drawing |
|  | Drawing |
|  | Information Area |
|  | Zoom |

## 6.2 System

Click the System tab to display the System panel.

This panel consists of six sections: System Setting, System Information, License Registration, System Backup and Restore, Parameter Processing and Preference Frame Current Folder.

| See: | System Setting |
| --- | --- |
|  | System Information |
|  | License Registration |
|  | System Backup & Restore |
|  | Preference Frame Current Folder |
|  | Parameter Processing |
|  | Access Information Manager |

| See: | View |
| --- | --- |
|  | Option |

### 6.2.1 System Setting

The options in this section allow you to specify the basic settings for the system, such as the Import Unit, Display Unit, Language, Database and Simulation.

| Option | Description |
| --- | --- |
| Import Unit | This option is used to specify the import unit. The available units are Metric and Inch. |
| Display Unit | This option is used to specify the display unit. The available units are Metric and Inch. |
| Language | This option is used to set the system language. The available languages are Japanese, English, Simplified Chinese, Korean, German, Spanish, French and Italian. |
| Database | Select the database to load parts from: MiniSDD, SDD or File. |
| Simulation | This option allows you to determine which program will be used for simulation: AP100Global, AP100, LINEA5 or Dr. ABE Blank. |
| Version | This option is used to display the version. |
| CAD Editor | This option is used to specify the CAD Editor. The available CAD Editor is AP100 and FabriCAD. |
| Initial Part Number | You can specify an initial value. The value will be the default quantity of the parts. See: Initial Part Number. |
| Sheet Select By | Two options are used to define whether the system will determine the sheet by the material name. See: System Determines Sheet by Material Name. |
| Use Wizard for Sheet Size/Name | If this option is selected, the Sheet Name Set window will display in auto execution that allows you to choose a sheet used for processing. See: Use Wizard for Sheet Size/Name. |

| See: | Initial Part Number |
| --- | --- |
|  | System Determining Sheet by Material Name |
|  | Use Wizard for Sheet Size/Name |

| See: | System Information |
| --- | --- |
|  | License Registration |
|  | System Backup & Restore |
|  | Preference Frame Current Folder |
|  | Parameter Processing |
|  | Access Information Manager |

#### 6.2.1.1 Initial Part Number

| 1. | This value is the default quantity of the parts. For example, if you type 6 in the Initial Part Number: textbox |
| --- | --- |
| 2. | Click OK to apply the setting. The value you specified will display as the default Part Quantity in the main window. The initial quantity of the parts loaded from the database will be six (6). The part quantity can be modified in the Part Quantity column of the Nesting Schedule window. |

| See: | System Determining Sheet by Material Name |
| --- | --- |
|  | Use Wizard for Sheet Size/Name |

#### 6.2.1.2 System Determining Sheet by Material Name

| The options here allow you to determine the way to select the sheet, by Material Name or by Material/Thickness. |
| --- |
| 1. | When the Material Name option is selected, you can select the material by the material name registered in the Material Manager. |
| 2. | When the Material/Thickness option is selected, you can select the material by the material type and thickness. |

| See: | Initial Part Number |
| --- | --- |
|  | Use Wizard for Sheet Size/Name |

#### 6.2.1.3 Use Wizard for Sheet Size/Name

| If this option is selected, the Sheet Name Set window will appear during auto execution, prompting you to select which sheet should be used for processing. |
| --- |
| 1. | Place a check mark in the Use Wizard for Sheet Size/Name check box. |
| 2. | The Sheet Name Set window will appear after you click the Auto Execute button. |
| 3. | All the material types (Standard, Remnant, Skeleton) with the material type and thickness you set at Nesting Plan are listed in the table. Select one material to use for processing. If all of the materials are checked, the system will select a material according to Material Selection Priority. You can also add new materials or copy a specific material by using Add New Sheet and Copy button. |
| 4. | Select a material, and click OK to continue the auto execution. |
| 5. | The system uses a remnant to process according to the settings. |

| See: | Initial Part Number |
| --- | --- |
|  | System Determining Sheet by Material Name |

### 6.2.2 System Information

This section lists the version and server of the Dr. ABE components that have been installed.

| See: | System Setting |
| --- | --- |
|  | License Registration |
|  | System Backup & Restore |
|  | Preference Frame Current Folder |
|  | Parameter Processing |
|  | Access Information Manager |

### 6.2.3 License Registration

You can register the license in two ways.

You can click the Registration button or the Enter Locking Code button to register the licenses before running the program.

Click the Registration button to open the Locate "Amada Key" window.

Browse to the folder containing the license file and select it.

Click Open to register the license.

Click the Enter Locking Code button to open the Nesting License Information window.

Click   and navigate to the folder containing the license code.

Select the file and click Open to register the license.

Note:

If you do not register the license, the following message will appear when you are running the program.

Please click Registration(R) or Enter Locking Code (E) to register the license first.

| See: | System Setting |
| --- | --- |
|  | System Information |
|  | System Backup & Restore |
|  | Preference Frame Current Folder |
|  | Parameter Processing |
|  | Access Information Manager |

### 6.2.4 System Backup and Restore

It is very important to backup parameters on a regular basis.

The System Backup/Restore section allows you to easily backup and restore the parameters.

Click the Backup & Restore button to display the Dr. ABE System Backup/Restore window.

| See: | How to Backup the Parameters |
| --- | --- |
|  | How to Restore the Parameters |

| See: | System Setting |
| --- | --- |
|  | System Information |
|  | License Registration |
|  | Preference Frame Current Folder |
|  | Parameter Processing |
|  | Access Information Manager |

#### 6.2.4.1 How to Backup the Parameters

| 1. | Click the item(s) in the Items to backup section that you want to backup. You can also click Select All under the list to select all the items. |
| --- | --- |
| 2. | Click the Browse button next to the File: textbox to navigate to the backup destination folder. The system will assign the default name of "back". You can also specify an alternate backup file name in the Choose a backup file window. |
| 3. | Click the Backup button to backup the files. The system will perform the backup process. |

| See: | How to Restore the Parameters |
| --- | --- |

#### 6.2.4.2 How to Restore the Parameters

| 1. | Click the Browse button to open the Choose a backup file window. |
| --- | --- |
| 2. | Navigate to the destination folder and locate the backup file. |
| 3. | Click Open to select the backup file. |
| 4. | In the Items to restore section, uncheck the items that you do not want to restore or just use the default settings. The system will select all the items to restore by default. |
| 5. | Click the Restore button to restore the files. |

| See: | How to Backup the Parameters |
| --- | --- |

### 6.2.5 Preference Frame Current Folder

Specify the path of the folder where the preference files are saved. You can click  button to select another folder to save the preference files.

| See: | System Setting |
| --- | --- |
|  | System Information |
|  | License Registration |
|  | System Backup & Restore |
|  | Parameter Processing |
|  | Access Information Manager |

### 6.2.6 Parameter Processing

The options in the Parameter Processing section allow you to specify when and where to download the machine and material parameters.

You can also control whether to decrease the sheet quantity when saving the NC program and the Skeleton/Remnant material.

| Option | Description |
| --- | --- |
| Machine Parameter Server PC | Specify the PC address to download the machine parameters |
| Material Parameter Server PC | Specify the PC address to download the material parameters See: Download Material Type from AP100 |
| SDD Parameter Automatic Download | Select this option to automatically download parameter from SDD. You can select the version of SDD from the drop-down list behind. |
| MiniSDD Parameter Automatic Download | Select this option to automatically download parameter from MiniSDD. |
| At the time of | Select the preferred download time of the parameters. |
| Starting of Dr. ABE | If you select this option, the system will automatically download the machine and material parameter from the database when Dr. ABE is launched. |
| Execution of Automatic Processing | If you select this option, the system will automatically download the machine or material parameter from the database when automatic processing is executed. |
| Server Location | This section is used to display the server name or path. |
| Decrease Sheet Quantity when Save NC | If you select this option, when automatically executing the process and saving the NC data, system will decrease the sheet quantity in the Material Manager window automatically. |
|  | See: Decrease Sheet Quantity when Save NC |
| Select Skeleton/Remnant to Save when Save NC | If you select this option, when automatically executing the process and saving the NC data, system will add the created skeleton/remnant information to the Material Manager window. |
|  | See: Select Skeleton/Remnant to Save when Save NC |

| See: | Decrease Sheet Quantity When Save NC |
| --- | --- |
|  | Select Skeleton/Remnant to save when saving NC |

| See: | System Setting |
| --- | --- |
|  | System Information |
|  | License Registration |
|  | System Backup & Restore |
|  | Preference Frame Current Folder |
|  | Access Information Manager |

#### 6.2.6.1 Decrease Sheet Quantity When Save NC

| To decrease the sheet quantity when saving an NC program: |
| --- |
| 1. | For example, in the Material Manager window, the quantity of the sheet A1050 is 100. |
| 2. | Select the Decrease Sheet Quantity When Save NC option. |
| 3. | One sheet is used in the processing. |
| 4. | Save NC. |
| 5. | The quantity of A1050 is decreased to 99. |
| 6. | If you do not select Decrease Sheet Quantity When Save NC, sheet quantity will remain the same after one piece of sheet is used. |

| See: | Select Skeleton/Remnant to save when saving NC |
| --- | --- |

#### 6.2.6.2 Select Skeleton/Remnant to Save when Saving NC

| 1. | Load several parts from the database. |
| --- | --- |
| 2. | In the Material Selection panel of the Nesting window, select Create Skeleton Sheet under Reusable Sheet, and define the preferred Max Utilization. |
| 3. | Select the Select Skeleton/Remnant to Save when Save NC option in the System panel. |
| 4. | Save the NC data after auto-execution. |
| 5. | The Save Confirmation dialog box appears, prompting you to check the skeleton/remnant that needs to be saved. Click the Save button. |
| 6. | Open the Material Manager window. Notice that the new skeleton was created. |

| See: | Decrease Sheet Quantity When Save NC |
| --- | --- |

### 6.2.7 Access Information Manager

|  | Click the Access Information Manager button to open the Access Information Manager window. VPSS Access Information Manager is an application for managing Connection Information for the VPSS Solution. |
| --- | --- |

| See: | System Setting |
| --- | --- |
|  | System Information |
|  | License Registration |
|  | System Backup & Restore |
|  | Preference Frame Current Folder |
|  | Parameter Processing |

## 6.3 Option

The options in this panel allow you to use the third-party’s application to load and export the plan files of other formats.

This panel consists of four sections: Start Module before Conversion, Start Module after Conversion, Open SDD Part Conversion and Interface File Setting.

| Option | Description |
| --- | --- |
| Start Module before Conversion | This option allows you to specify an application to convert the plan files and load into Dr ABE. See: Example 1 |
| Start Module after Conversion | This option allows you to specify an application to convert the plan files of Dr ABE into the plan files supported by the programs of other company. See: Example 2 |
| Open SDD Part Conversion | This option allows you to specify an application to open when you are to open part from SDD. See: Example 3 |
| Interface File Setting | In this section, you can specify the CSV format to output the nesting plan and nesting result. In production process, you can load the nesting result file as a CSV format to control part schedule. |
| Plan File Setting | This option allows you to define plan file format. There are two options below: Amada CSV Format and Custom. |
|  | Amada CSV Format | When AMADA CSV Format is selected, the CSV format used in the WinNEST for AMADA will be applied. |
|  | Custom | Select a form from Custom: drop-down list. You may also click the Detail button to open the Option window. See: Option window |
| Output Plan File | This option allows you to define output format for the plan file. There are two options below: Amada CSV Format and Custom. |
|  | Amada CSV Format | When AMADA CSV Format is selected, the CSV format used in the WinNEST for AMADA will be applied. |
|  | Custom | Select a form from Custom: drop-down list. You may also click the Detail button to open the Setting of Outputting Result File window. See: Setting of Outputting Result File window. |

Example 1

| 1. | Place a check mark in the check box to enable the conversion function. |
| --- | --- |
| 2. | Click Browse button to open the Select Convert Module dialog box. |
| 3. | Select an execution file for conversion. |
| 4. | When you are to open a schedule in the Nesting Schedule window, the specified application will be started. |

Example 2

| 1. | Place a check mark in the check box to enable the conversion function. |
| --- | --- |
| 2. | Click Browse button to open the Select Convert Module dialog box. |
| 3. | Select an execution file for conversion. |
| 4. | Right-click in the part result view screen to open the shortcut menu and select Save Schedule/Output Report or Save NC Data |
| 5. | Select either of the above two options, the specified application will be started. |

Example 3

| 1. | Place a check mark in the check box to enable the conversion function. |
| --- | --- |
| 2. | Click Browse button to open the Select Convert Module dialog box. |
| 3. | Select an execution file for conversion. |
| 4. | Then when you open part from SDD, the specified application will be started. |

Note:

You can open part from SDD in the following three ways.

| Method 1 | In the Avon Data Selection Dialog window, select a part and click Open button. |
| --- | --- |
| Method 2 | In Dr.ABE main window, click the Nesting Schedule button to open the Nesting Schedule window. In this window, click Part button. The Avon Data Selection Dialog window appears. |
| Method 3 | In the Manual Edit toolbar, click Add Part button to open Add Part screen. Select SDD and the Avon Data Selection Dialog window will appear. |

| See: | Option Window |
| --- | --- |
|  | Setting of Outputting Result File Window |

| See: | View |
| --- | --- |
|  | System |

### 6.3.1 Option window

| Option | Description |
| --- | --- |
| Custom | You can make the setting to define the CSV file format. There are five types. |
| Starting Reading Line | Sometimes some data in the CSV file does not need to be read. In this case, you can define from which line to begin to read the data. |
| Text Qualifier | Define text qualifier used to identifying each item in the CSV. There are three options: Double Quotation Mark, Single Quotation Mark and None. |
| Delimiters | Define in the CSV file which kind of mark will be used as delimiters: Tab, Semicolon, Comma, Space, Other (type other marks needed in the textbox directly). |
| Part Path | Select the part path here. Note: Your computer should be shared for remote loading. |
| Save Part Name | This option allows you to load parts by part name |
| Save Part File Path | This option allows you to load parts by part file path. |
| Treat Consecutive Delimiters as One | If this option is checked, several consecutive delimiters will be regarded as one. |
| Plan Items | Define contents in the CSV file. Select items from Plan items list and then click the Add button to output it into the CSV file. Select items from Item and sequence of one record list and then click the Delete button to remove it. Click the priority button to change the order of the selected items. |

| See: | Setting of Outputting Result File Window |
| --- | --- |

### 6.3.2 Setting of Outputting Result File window

| Option | Description |
| --- | --- |
| Setting of Outputting | Click arrow button to select a form you want to customize. |
| Text Qualifier | Define text qualifier used to identifying each item in the CSV. There are three options: Double Quotation Mark, Single Quotation Mark and None. |
| Delimiters | Define in the CSV file which kind of mark will be used as delimiters: Tab, Semicolon, Comma, Space, Other (type other marks needed in the Other: text box directly). |
| Output Setting |  |
| Output Part and Sheet | Select this option to output part and sheet information. |
| Output Sheet Only | Select this option to output sheet information. |
| Sheet Record | You can define display format for sheet record. Define contents in the CSV file. Select items from Plan items list and then click the Add button to output it into the CSV file. Select items from Item and sequence of one record list and then click the Delete button to remove it. Click the priority button to change the order of the selected items. |
|  | Note: Sheet name cannot be deleted. |
| Record Type | Type the record type in this text box as a sheet mark in the CSV file. |
| Part Record | You can define display format for part record. Define contents in the CSV file. Select items from Plan items list and then click the Add button to output it into the CSV file. Select items from Item and sequence of one record list and then click the Delete button to remove it. Click the priority button to change the order of the selected items. |
|  | Note: Part name cannot be deleted. |
| Record Type | Type the record type in this text box as a part mark in the CSV file. |

Example:

| 1. | Place a check mark in Output Plan File: check box and select Amada CSV format. |
| --- | --- |
| 2. | Right-click in the nesting result view to open the shortcut menu. Select Save NC Data. |
| 3. | It outputs as follow, |
| 4. | Select Custom in the Output Plan File and set as follows. |
| 5. | The output is as follow: |

| See: | Option Window |
| --- | --- |

# Chapter 7: CAD Data Load

This chapter introduces the way to load CAD data into nesting and how to specify the part quantities.

If necessary, you can establish a connection with the server and load CAD data from the database.

Note:

Dr. ABE supports the databases such as SDD and MiniSDD. You can also import the CAD files stored on your local hard drive.

See: Database

| See: | How to Load CAD Data |
| --- | --- |
|  | Methods for Specifying the Part Quantity |
|  | How to Establish a Connection with a Server |

## 7.1 How to Load CAD Data

Method 1: Drag-and-drop the CAD data to the CAD DATA Load button.

| 1. | Locate the parts using Windows Explorer or use some alternative methods to list files. |
| --- | --- |
| 2. | Select the file. Press and hold the left mouse button. |
| 3. | Move the mouse pointer over the CAD Data Load button and then release it. The selected parts will appear in the Main window. |
| 4. | Type the part quantity in the Part Quantity: text box and then click the button to push it into the nesting schedule. |

Method 2: Drag-and-drop Data to the Nesting Schedule button.

| 1. | Locate the parts using the Windows Explorer or use some alternative methods to list files. |
| --- | --- |
| 2. | Select the file. Press and hold the left mouse button. |
| 3. | Move the pointer over the Nesting Schedule button and then release the left mouse button. The part file is loaded into the Nesting Schedule. |
|  | Note: Any quantity information that is included in the part is transferred to the Nesting Schedule. If there is no quantity information associated with the part file, the quantity of the parts will be the default quantity. |

Method 3: Using the CAD Data Load Button

| 1. | Click the CAD Data Load button to open the Avon Data Selection Dialog window. |
| --- | --- |
| 2. | Select one or more parts and then click Open to close the window and return to the main window. |

| See: | Methods for Specifying the Part Quantity |
| --- | --- |
|  | How to Establish a Connection with a Server |

## 7.2 Methods for Specifying the Part Quantity

Method 1: Type the quantity in the Part Quantity: text box after loading the part from CAD Data.

Method 2: Change the number in the Nesting Schedule window. Type the quantity in the Part Quantity cell.

| See: | How to Load CAD Data |
| --- | --- |
|  | How to Establish a Connection with a Server |

## 7.3 How to Establish a Connection with a Server

| 1. | Click the CAD Data button in the main window to open the Avon Data Selection Dialog window. |
| --- | --- |
| 2. | Click the Add Server button. The Add/Remove Server window appears. |
| 3. | Input the server name or address in the Server Name or IP Address: text box and then click the Add button. The server is added to the list. |
| 4. | Select a server name and click Remove button to remove the server name from the list. . |
|  | Click OK to save the changes. Click Cancel to exit without saving to the Avon Data Selection Dialog window. |

| See: | How to Load CAD Data |
| --- | --- |
|  | Methods for Specifying the Part Quantity |

# Chapter 8: Nesting Plan

Click the Nesting Plan button in the main window after the parts are loaded from the database to open the Nesting Schedule window. The nesting plan allows you to define the part properties for each part, including the quantity, priority, material type, material selection, etc.

| See: | Parts Properties Summary |
| --- | --- |
|  | Menus |
|  | Toolbars |
|  | My Nesting Plan |
|  | Parts List |
|  | Parts Properties |
|  | Parts Properties Advanced |

## 8.1 Parts Properties Summary

| 1. | Load parts into the Nesting Plan, and then click Nesting Plan button to display the corresponding window. |
| --- | --- |
| 2. | Select a part and double-click it to display the Parts Properties window. You can also right- click the part and select Edit Part Properties from the shortcut menu to display the Parts Properties window. |
|  | Double-click |
|  | Right-click |
| 3. | Define the part properties in the Parts Properties window. |
| 4. | Click OK to confirm the settings and to return to the Nesting Schedule window. |
|  | Click Cancel button to exit the window without saving. |
|  | Click Apply to apply the settings you have specified for the part. |
|  | Click Apply to save the setting after you have made the settings for the selected part. And then click the Previous (P) or Next (N) buttons to edit the previous or next part in the Nesting Plan. |
|  | Click the Advanced button to open the Parts Properties Advanced window. |

| See: | Menus |
| --- | --- |
|  | Toolbars |
|  | My Nesting Plan |
|  | Parts List |
|  | Parts Properties |
|  | Parts Properties Advanced |

## 8.2 Menus

|  | The menu bar consists of six options: File, Edit, View, Insert, Tool and Help. These options allow you to edit the nesting plan. |
| --- | --- |

| See: | File |
| --- | --- |
|  | Edit |
|  | View |
|  | Insert |
|  | Tool |
|  | Help |

| See: | Parts Properties Summary |
| --- | --- |
|  | Toolbars |
|  | My Nesting Plan |
|  | Parts List |
|  | Parts Properties |
|  | Parts Properties Advanced |

### 8.2.1 File Menu

The options on the File menu allow you to create, open, add, save and print a plan.

|  | Option Description New Erase all the existing data in the nesting schedule and create a new plan. Open Open a nesting schedule that was previously saved. Save Save the current nesting schedule. Save As… Save the current nesting schedule with a new name. Add Plan Add a plan. Print Print the nesting schedule. Material Manager Open the Material Manager window, and you can add, delete, or modify the material. See Material Manager Exit Close the Nesting Schedule window and return to main window. |
| --- | --- |

| See: | Edit |
| --- | --- |
|  | View |
|  | Insert |
|  | Tool |
|  | Help |

### 8.2.2 Edit Menu

The options on the Edit menu allow you to edit the assemblies and parts in the plan.

|  | Option | Description |
| --- | --- | --- |
|  | Undo | Reverse the previous operation. |
|  | Redo | Repeat the previously un-done action. |
|  | Cut | Cut the selected assembly or part to the clipboard. |
|  | Copy | Copy the selected assembly or part to the clipboard. |
|  | Paste | Paste the assembly or part that you previously cut or copied to the clipboard to the selected assembly. |
|  | Delete | Delete the selected part. |
|  | Select All | Select all the parts in your selected assembly. |
|  | Merge of the Same Part | Merge the same parts in the same assembly. |
|  | Parts Properties | Open Parts Properties window. Please refer to Parts Properties. |
|  | Sort By Input Order | Sort the inputted parts according to their input order. |

| See: | File |
| --- | --- |
|  | View |
|  | Insert |
|  | Tool |
|  | Help |

### 8.2.3 View Menu

The options on the View menu allow you to choose the display mode of the parts.

|  | Option Description Details Displays detailed information of the selected parts. Details + Graphics Displays detailed information and graphics of the selected parts. Thumbnail Displays thumbnails of the selected parts. |
| --- | --- |

Examples:

If you select the Details option, the parts are displayed as follows:

If you select the Details + Graphics option, the parts will be displayed as follows:

If you select the Thumbnail option, the parts are displayed as follows:

| See: | File |
| --- | --- |
|  | Edit |
|  | Insert |
|  | Tool |
|  | Help |

### 8.2.4 Insert Menu

The options of the Insert menu allow you to insert a plan, assembly or a part into the current plan.

|  | Option Description Assembly This option will insert a previously saved assembly to your selected assembly. Part This option will insert a part from the CAD database to the plan. File This option will insert a CAD file to your selected assembly, such as *.dwg, *.dxf, and *.iga. |
| --- | --- |

| See: | File |
| --- | --- |
|  | Edit |
|  | View |
|  | Tool |
|  | Help |

### 8.2.5 Tool Menu

|  | The options in the Tools menu allow you to specify the default part setting, the format to save the part information, etc. |
| --- | --- |

| Option | Description |
| --- | --- |
| Default Setting | Select Default Setting and the Parts Properties window appears. |
|  | You can define the part information and save it as default setting in this window. Click the Advanced button to open the Parts Properties Advanced window. You can define and save the default advanced part information. For contents in the two windows, see Parts Properties. |
| Option | Select Option from menu to display the Option window. In this window, you can define the format of *.CSV file. See To save a plan as CSV file. |
| Assembly Manager | This function is currently unavailable. |

Options in the CSV File Setting Panel

| Option | Description |
| --- | --- |
| Amada CSV Format | When AMADA CSV Format is selected, the CSV format used in the WinNEST for AMADA will be applied. |
| Custom | When Custom is selected, setting options are activated. You can make the setting to define the CSV file format. Form1-Form 5 are available. |
| Starting reading line | Sometimes some data in the CSV file does not need to be read. In this case, you can define from which line to begin to read the data. |
| Text qualifier | Define text qualifier used to identifying each item in the CSV. Three options: Double Quotation Mark, Single Quotation Mark and None. |
| Delimiters | Define in the CSV file which kind of mark will be used as delimiters: Tab, Semicolon, Comma, Space, Other (type other marks as needed in the textbox directly). |
| Treat consecutive delimiters as one | If this option is checked, several consecutive delimiters will be regarded as one. |
| Part Path | Select the part path here. If Save part name is selected, the system will load parts by part name; if Save part file path is selected, the system will load parts by part file path. Note: The PC should be shared for remote loading. |
| Plan Items | Define contents in the CSV file. Select items from Plan items and then click Add button to output it into the CSV file; select items from Item and sequence of one record and then click Delete button to remove it. Click the priority button to change the order of the selected items. |
| Number | Use number to display part priority. |
| Character | Use character to display part priority. The system will automatically convert the character into number to judge part priority. |

Options in the Conversion Process Setting panel

| Options | Descriptions |
| --- | --- |
| Start Module before Conversion | Use the third-party’s application to load the plan files of other formats, such as the plan file created by the program of Toshiba. See: Option panel in the System Setting window |
| Carry Out Conversion when Loading Plan | Place a check mark in the check box to enable the conversion function |
| Conversion Process Application | Specify the third-party’s application. You can click the Browse button to locate application to convert the plan file. |

To save a plan as a CSV file:

| 1. | Select Amada CSV format. It outputs as follows: |
| --- | --- |
| 2. | Select Custom and set as follows. |
| 3. | The output is as follows: |

| See: | File |
| --- | --- |
|  | Edit |
|  | View |
|  | Insert |
|  | Tool |
|  | Help |

### 8.2.6 Help Menu

|  | Select Nesting Plan Help from the Help menu to open the help system. |
| --- | --- |

| See: | File |
| --- | --- |
|  | Edit |
|  | View |
|  | Insert |
|  | Tool |
|  | Help |

## 8.3 Toolbars

The toolbars can enhance your interaction with the system. Each button on the toolbar is associated with an option or command. You can click toolbar buttons to execute commands and functions rather than navigate the menus for options. You should study all the tool buttons on each toolbar and display those toolbars that you consider the most useful.

File Toolbar

|  | New |
| --- | --- |
|  | Open |
|  | Save |
|  | Print |

Edit Toolbar

|  | Undo |
| --- | --- |
|  | Redo |
|  | Cut |
|  | Copy |
|  | Paste |
|  | Delete |
|  | Parts Properties |
|  | Sort By Input Order |

View Toolbar

|  | View |
| --- | --- |
|  | Note: Click the thumbnail to define the view. See View Menu. |

Insert Toolbar

|  | Assembly |
| --- | --- |
|  | Part |

Others

| Button | Description |
| --- | --- |
|  | Automatically nest different parts on one sheet if there is enough space. |
|  | Nest different parts on different sheets respectively. |
|  | This textbox displays the name of the selected assembly. Different assemblies can share the same name. You can modify or type a new name in the Assembly Name text box. |
|  | Comments on the selected assembly. |
|  | Lot quantity of the selected assembly. |
|  | Note: Total Quantity of Parts = Lot Quantity of Assembly × Parts Quantity. |

| See: | Parts Properties Summary |
| --- | --- |
|  | Menus |
|  | My Nesting Plan |
|  | Parts List |
|  | Parts Properties |
|  | Parts Properties Advanced |

## 8.4 My Nesting Plan

|  | Right-click in the My Nesting Plan area to open the shortcut menu. There are eleven options on the shortcut menu: New, Expand All, Expand, Collapse, Insert Empty Assembly, Delete Assembly, Insert Part, Delete Line, Cut, Copy and Paste. |
| --- | --- |

| Option | Description |
| --- | --- |
| New | Create a new nesting schedule. |
| Expand All | Expand the selected assemblies, including the subassemblies and display all the parts. Parts in the subassembly of the selected assembly will also display. See Expand All. |
| Expand | Expand the selected assembly and display parts and subassemblies directly under the selected assembly. Parts in the subassembly of the selected assembly will not display. See Expand. |
| Collapse | Collapse the selected assembly and hide all the parts from view. See Collapse. |
| Insert Empty Assembly | Insert an empty assembly in the selected assembly. See Inserting an Assembly. |
| Delete Assembly | Erase the selected assembly. If you select this option, the system will delete the selected assembly without any confirmation. |
| Insert Part | Load a part from the specified database and insert it to the assembly. See: To insert a part. |
| Delete Line | Delete a selected part. |
| Cut | Cut the selected part or assembly and paste it to the clipboard. |
| Copy | Copy the selected part or assembly to the clipboard. |
| Paste | Paste the part or assembly from the clipboard. |

Example:

| Expand All |
| --- |
| 1. Select an assembly and choose Expand All from the shortcut menu. | 2. The selected assembly expands and displays all its subassemblies (including all the parts in them) and parts. |
| Expand |
| 1. Select an assembly and choose Expand from the shortcut menu. | 2. The selected assembly expands and shows its subassembly and parts. |
| Collapse |
| 1. Select an assembly that was previously expanded and choose Collapse from the shortcut menu. | 2. The selected assembly will collapse. The parts are hidden from view. |
| Inserting an Assembly |
| 1. | Select an assembly and right-click to open the shortcut menu. |
| 2. | Select Insert Empty Assembly and an empty assembly will be inserted in the selected assembly. |
| Inserting a Part |
| 1. | Select an assembly and right-click to open the shortcut menu. |
| 2. | Select Insert Part to open the Avon Data Selection window. |
| 3. | Select one or more parts and click Open. The newly loaded parts will display in the selected assembly. |

| See: | Parts Properties Summary |
| --- | --- |
|  | Menus |
|  | Toolbars |
|  | Parts List |
|  | Parts Properties |
|  | Parts Properties Advanced |

## 8.5 Parts List

The Parts List table lists the basic part information.

| Column Title | Description |
| --- | --- |
| No. | Parts number which is assigned by system. |
| CAD | CAD information. |
| CAM | CAM information. |
| Part Quantity | The quantity of the parts. |
| Part Comment | The part comment loaded from the SDD database. |
| Part Name | The name of the part. |
| Material Type | The type of material. |
| Material Thickness | The thickness of material. |
| Weight (g) | The weight of the parts. |
| Unfold X/ Y Size | The dimensions in X and Y-axis of the unfolding drawings of the parts. |
| Rectangle Area | The outer rectangle area of the unfolding drawing of the parts. Rectangle Area = Unfold X x Unfold Y. |
| Area Without Holes | For the parts with inner loops, the dimension displays here is the total area excluding inner loop area. |
| Area With Holes | For the parts with inner loops, the dimension displays here is the total area including inner loop area. |
| Filler Quantity | The quantity of filler parts. |
| Process Date | The process date of parts. Click the cell to show the arrow button. Click the arrow to open the drop-down calendar and select the process date. |
| Due Date | The due date of parts. Click the cell to show the arrow button. Click the arrow to open the drop-down calendar and select the due date. |

Notes:

| 1. | You can click the column headings to sort the parts by ascending or descending order of the column data. |
| --- | --- |
| 2. | You can right-click the column title to display a shortcut menu, and then select the column items you want the system to display. |

To change the column item

| 1. | Right click the column title to open the following shortcut menu: |
| --- | --- |
| 2. | The options with check marks appear as column titles in the table. You can remove the check mark to hide the corresponding information from the table. |
| 3. | You can select More… to open the following window to add items to display that are not in the list. |

Define Display Items Window Buttons

| Button | Description |
| --- | --- |
| Add | Add items in All Items column to Item to Display column. |
| Delete | Delete item from Item to Display column. |
| OK | Save the changes and return to Nesting Plan window. |
| Cancel | Cancel the operation and return to the Nesting Plan window. |
| Up | Move upward the selected item in the list. |
| Down | Move downward the selected item in the list. |

| See: | Shortcut Menu |
| --- | --- |
| See: | Parts Properties Summary |
|  | Menus |
|  | Toolbars |
|  | My Nesting Plan |
|  | Parts Properties |
|  | Parts Properties Advanced |

### 8.5.1 Shortcut Menu

|  | Select a part in the Parts List area to highlight it. Right-click to display the shortcut menu. There are ten options on the shortcut menu: Edit Parts Properties, Cut, Copy, Paste, Delete, Select All, Row Height, Light Attribute Edit, Update CAD Data and To CAD Editor. |
| --- | --- |

Shortcut Menu Options

| Option | Description |
| --- | --- |
| Edit Parts Properties | Select this option to open the Parts Properties window in which you can edit part attribute. |
| Cut | Select this option to cut the selected part to the clipboard. |
| Copy | Select this option to copy the selected part to the clipboard. |
| Paste | Select this option to paste the part previously cut or copied to the clipboard to the selected assembly. |
| Delete | Select this option to delete the selected part. |
| Select All | Select this option to select all the parts displayed in this table. |
| Row Height | Type a value in the Row Height textbox to define the height of rows of the part list table. |
| Light Attribute Edit | Light Attribute Editor allows you to assign lead in/out, Wire joint, Corner joint to the patterns, and then save them as attribute data |
| Update CAD Data | Select this command to overwrite the original data in CAD Editor and update modified data into Nesting Plan. |
| To CAD Editor | Transfer the selected part to CAD mode. Which CAD editor you will transfer into depends on your setting in System Setting. |

| See: | Light Attribute Editor |
| --- | --- |

### 8.5.2 Light Attribute Editor

In the Light Attribute Editor window, you can make settings about the lead in/out, joint, sequence, cut condition and end value to the pattern selected and save the result as SY3 file.

Menu Bar

|  | Option | Description |
| --- | --- | --- |
|  | Open | Load a SY3 or SY5 file to edit. |
|  | Save | Save the currently opened file. |
|  | Save All | Save all opened files. |
|  | Save As | Save the current opened file with a new name. |
|  | Close | Close the currently opened file. |

|  | Option | Description |
| --- | --- | --- |
|  | Undo | Reverse the previous operation. |
|  | Redo | Repeat the previously un-done action. |

|  | Option | Description |
| --- | --- | --- |
|  | Zoom out | Select this option to reduce the view. |
|  | Zoom In | Select this option to magnify the view. |
|  | Zoom Restore | Select this option to fit the pattern to the window. |

|  | Option | Description |
| --- | --- | --- |
|  | Insert | This function is not available at this moment |

Toolbar

| Standard New Open Save Save All Insert Redo Undo Close | View Zoom in Zoom out Zoom Restore Options |
| --- | --- |

The Options window

|  | Specify the display unit and the interface language. |
| --- | --- |

#### 8.5.2.1 To Assign attribute data to a pattern

| 1. | Load a part into the Nesting Plan. |
| --- | --- |
| 2. | Select the part from the part list and right-click to display the shortcut menu. Select the Light Attribute Editor option to display the Light Attribute Editor window. |
| 3. | About Lead in/Out . It is not available for EM machine. |
| 4. | About Joint |
|  | You can click the Joint button and move the pointer to the work area to assign joints. A white ball on the pattern indicates the joint position. Click the pointer to assign the joint when it moves to the desired position. |
|  | You can place a check mark in the Both sides corner tab check box. |
|  | Move the pointer to the corner to assign corner joints. |
| 5. | About Cut Condition |
|  | You can click the Cut Condition button to display the Parameter panel. There are ten kinds of cutting condition and two cutting directions to select from. |
|  | Select the outer loop in left section and the loop selected becomes yellow. |
|  | Select E005 from the Cutting Condition drop-down list, and CCW from the Direction drop-down list. |
|  | If you select the outer loop and then place a check mark in the Non-Tool assign check box, the system won’t assign tools on the selected pattern. |
| 6. | About End Value |
|  | You can click the End Value button to display the Parameter panel. There are four end values to select from. Select an object and then select Machine Stop from Process: drop-down list. |
| 7. | You can click the Remove button to delete the selected joint. |
| 8. | After editing, you can select Save As from the File menu to save the result as a SY3 file or click the Close button to close the window. |
| 10. | You will notice that a symbol mark appears in the CAD column, indicating the existence of SY3 file. |

## 8.6 Parts Properties

Select a part in the Parts List to highlight it, and then double-click to open the Parts Properties window. The options in this window allow you to edit the properties of the part.

| See: | Part Name and Comment |
| --- | --- |
|  | Select Data |
|  | Quantity |
|  | Dates |
|  | Material |
|  | Process |
|  | Nesting |
|  | Change Check box |

| See: | Parts Properties Summary |
| --- | --- |
|  | Menus |
|  | Toolbars |
|  | My Nesting Plan |
|  | Parts List |
|  | Parts Properties Advanced |

### 8.6.1 Part Name and Comment

The part name and comment will appear in this section. You can change the comment by typing new text. When several parts are selected, asterisks (*) will appear in the fields.

| See: | Select Data |
| --- | --- |
|  | Quantity |
|  | Dates |
|  | Material |
|  | Process |
|  | Nesting |
|  | Change Check box |

### 8.6.2 Select Data

This section is used to specify the type of data the system will use when processing parts. Different icons will appear in the CAD cell to indicate the different file types.

| Option | Description |
| --- | --- |
| Pattern | Select this option and the system will use the CAD pattern to process. |
| Attribute Data | Select this option and the system will use the SY3 file to process. |
| Assignment Data | Select this option and the system will use the SY5 file to process. |

Note:

You can specify data priority using the following method if data exists for several parts.

To specify the data priority:

| 1. | Select Default Settings on the Tool menu in Nesting Schedule window. The Parts Properties window displays. |
| --- | --- |
| 2. | You can specify the priority order of calling data by clicking the upward or downward arrow. The assignment on the top of the list has the highest priority. |

| See: | Part Name and Comment |
| --- | --- |
|  | Quantity |
|  | Dates |
|  | Material |
|  | Process |
|  | Nesting |
|  | Change Check box |

### 8.6.3 Quantity

This section is used to specify the quantity of parts, filler parts and prototypes. If you set the part quantity as 5~20, the quantity of filler parts will be the balance of 5 and 20, or 15.

If you set the part quantity as 1 to 1, no filler parts will be specified.

If the first quantity is larger than the second quantity, the second quantity will update to be the same as the first one after you click OK.

To set prototype condition: please refer to Prototype Condition.

| See: | Part Name and Comment |
| --- | --- |
|  | Select Data |
|  | Dates |
|  | Material |
|  | Process |
|  | Nesting |
|  | Change Check box |

### 8.6.4 Dates

The options in the Dates section are used to specify the start and end time of the process.

| Option | Description |
| --- | --- |
| Process | The starting date and time of process. |
| Due | The due date and time of process. |
| Change | See Change Check Box. |

Adjusting the Date

| 1. | You can click the arrow to open the calendar and click the right or left arrows to change the month and year. |
| --- | --- |
| 2. | Select a date from the calendar and date will appear in the field. |

Adjusting the Time

| 1. | Click the hour, minute or second to highlight it. |
| --- | --- |
| 2. | Click the up and down arrow buttons to change the time or type the time in the field using the HH:MM:SS format. |

How Dates Affect the Process

| 1. | Load two parts that use the same material type from the database. The two parts are nested on one sheet after you use the Auto Execute option. |
| --- | --- |
| 2. | Open the Nesting Plan window and specify a process date for one part, and a later date for the remaining part in Dates section. The process date for the two parts is different. Enable Grouping nesting by selecting Process Date in the Group window. |
| 3. | Click the Auto Execute button in the main window and note the result. The two parts are nested on two different sheets. |

| See: | Part Name and Comment |
| --- | --- |
|  | Select Data |
|  | Quantity |
|  | Material |
|  | Process |
|  | Nesting |
|  | Change Check box |

### 8.6.5 Material

This section is used to specify the material type, thickness and name. To change them, you could click the arrow button to open the drop-down list and select a type or thickness.

If you select sheet by Material Name, you can select the material by the material name registered in the Material Manager.

If you select sheet by Material/Thickness, you can select material by the material type and thickness. See: System Determining Sheet by Material Name

| See: | Part Name and Comment |
| --- | --- |
|  | Select Data |
|  | Quantity |
|  | Dates |
|  | Process |
|  | Nesting |
|  | Change Check box |

### 8.6.6 Process

|  | This section is used to display the turret layout. |
| --- | --- |
|  | Place a check mark in [De-Burring ON/OF] to assign deburring tool automatically. See Deburring Place a check mark in [SLOT AUTOON/OFF] check box to assign slot tools automatically. See: Slot2&3 |

| See: | Part Name and Comment |
| --- | --- |
|  | Select Data |
|  | Quantity |
|  | Dates |
|  | Material |
|  | Nesting |
|  | Change Check box |

### 8.6.7 Nesting

The options in this section are used to specify nesting priority, rotation and common line cutting.

| Option | Description |
| --- | --- |
| Priority | This item is used to specify the layout priority of parts. Please refer to Defining the Part Priority. |
| Group ID | This item is used to specify group ID for parts. Please refer to Defining the Group ID for the Parts. |
| Rotation | This section is used to specify whether parts are allowed to rotate when nesting. Please refer to Rotation with different condition. |
| Not Allowed | If you select this option, parts are not allowed to rotate when nesting. |
| Free | If you select this option, parts can rotate freely when nesting. This function helps to increase sheet utility. Note: To enable Common Cut and Pair functions, you need to select Free from the Rotation combo box. |
| Use Sheet’s Grain Angle+-180 Degrees | If you select this option, parts will rotate at the sheet’s grain angle +-180 degrees. |
| Use Sheet’s Grain Direction | If you select this option, the parts will rotate according to the grain direction of the sheet specified in the Material Manager window. If the grain direction is horizontal, the parts will rotate at 0 or 180 degrees. If the grain direction is vertical, the parts will rotate at 90 or 270 degrees. |
| Rotate 90 Degrees | If you select this option, the parts will rotate at 90 degrees. |
| Common Line Cutting | If you select this option, the machine system will allow common line cutting. Please refer to Different result of the Common Line Cutting. |
| Grid | Common-cut or common-punch grid parts. To use this function, you should select Joint as the End Value |
| X direction | Common-cut or common-punch the X-axis edges of the parts. |
| Y direction | Common-cut or common-punch the Y-axis edges of the parts. |
| ALA Logic | If you select this option, the system can common-cut parts that the system originally can’t common-cut by rotating or reversing a certain degree. This option will save the sheet and reduce the process time. This unavailable for EM machine. |
| ALA Logic (Pair By Rotation) | If the part quantity is more than 2, If you select this option, them in pair. This unavailable for EM machine. |
| Different Part | If you select this option, the system will common-cut different parts. This unavailable for EM machine. |
| Fixed Qty X/Y | Specify the parts quantity in X and Y Axis in a grid. |
| Change | See: Change check box |

| See: | Defining the Part Priority |
| --- | --- |
|  | Defining the Group ID for Parts |
|  | Rotation with Different Condition |
|  | Different Result of the Common Line Cutting |

| See: | Part Name and Comment |
| --- | --- |
|  | Select Data |
|  | Quantity |
|  | Dates |
|  | Material |
|  | Process |
|  | Change Check box |

#### 8.6.7.1 Defining the Part Priority

| 1. | Specify the processing starting point and direction as follows. |
| --- | --- |
| 2. | Define different priorities for these two different parts respectively. The priority of the larger one is set to 3; the priority of the smaller one is set to 4. The larger one has higher priority and it is nested first after auto execution. |
| 3. | If the priority of the larger part is 4 and the priority of the smaller part is 3, the smaller part is nested first. |

Note:

If you select the Give Higher Priority to Group of Small Parts in the Group window, the system will ignore the priority you set in the Part Properties window and strictly nest smaller parts at first.

| See: | Defining the Group ID for Parts |
| --- | --- |
|  | Rotation with Different Condition |
|  | Different Result of the Common Line Cutting |

#### 8.6.7.2 Defining the Group ID for Parts

| 1. | Define different Group ID for two different parts. The Group ID of first part is set to 2 and that of the second one is set to 3. |
| --- | --- |
| 2. | Define the Grouping Priority as follows. |
| 3. | The parts with different Group IDs will be nested on different sheets. The parts whose Group ID is 2 will be nested first. |

| See: | Defining the Part Priority |
| --- | --- |
|  | Rotation with Different Condition |
|  | Different Result of the Common Line Cutting |

#### 8.6.7.3 Rotation with Different Condition

In nesting section, click Rotation arrow button to display the drop-down list. Select one option to change the part rotation during the nesting process.

If Not Allowed is selected, the parts will not be rotated during the process.

If Free is selected, parts will be rotated according to the other system settings.

If Use Sheet’s Grain Angle+-180 Degrees is selected,

When the grain direction is vertical, the result is as follows.

If Use Sheet’s Grain Angle is selected,

When the grain direction is vertical, the result is as follows.

If Rotate 90 Degrees is selected, parts will be rotated 90 degrees.

| See: | Defining the Part Priority |
| --- | --- |
|  | Defining the Group ID for Parts |
|  | Different Result of the Common Line Cutting |

#### 8.6.7.4 Different Result of the Common Line Cutting

When Common Line Cutting is checked, six kinds of common cut methods are activated. Grid, X direction, and Y direction are available for punch machine.

When Grid is selected, specify the grid quantity in Part Properties window.

The parts will be processed as follows.

When X direction is selected, specify the grid quantity in Part Properties window as following:

Parts will be processed as follows:

When Y direction is selected, specify the grid quantity in Part Properties window as following:

Parts will be processed as follows:

| See: | Defining the Part Priority |
| --- | --- |
|  | Defining the Group ID for Parts |
|  | Rotation with Different Condition |
|  | Different Result of the Common Line Cutting |

### 8.6.8 Change Check Boxes

When you select multiple parts with different conditions for editing, the Change check boxes will become active. If you need to change any of the conditions, place a check mark in the corresponding check box to activate the condition for modification. The modifications will be applied to all the selected parts.

Example

| 1. | Place a check mark in the Change Qty check box and specify the options as follows: |
| --- | --- |
| 2. | Part quantity will be changed as follows. |

| See: | Part Name and Comment |
| --- | --- |
|  | Select Data |
|  | Quantity |
|  | Dates |
|  | Material |
|  | Process |
|  | Nesting |

## 8.7 Parts Properties Advanced

Click Advanced button and Parts Properties Advanced window appears. You can specify Special Information, Size Definition, Code Definition, Sketch Nesting and User Define in this window.

| See: | Material |
| --- | --- |
|  | Special Information |
|  | Size Definition |
|  | Code Definition |
|  | Nesting |
|  | Process and User Define |
|  | Taking Out Station |
|  | Taking Out Part Grid as One Part |

| See: | Parts Properties Summary |
| --- | --- |
|  | Menus |
|  | Toolbars |
|  | My Nesting Plan |
|  | Parts List |
|  | Parts Properties |

### 8.7.1 Material

The options in this section are the same as those in the Material section in the Part Properties window.

| See: | Special Information |
| --- | --- |
|  | Size Definition |
|  | Code Definition |
|  | Nesting |
|  | Process and User Define |
|  | Taking Out Station |
|  | Taking Out Part Grid as One Part |

### 8.7.2 Special Information

The options in this section are used to specify special information for the material.

| Option | Description |
| --- | --- |
| Auto | If you select this option, the system will select the optimum sheet size from sheet database. The Size Definition and Code Definition section will be disabled. |
| Standard | If you select this option, the system will only select standard sheets for cutting. Remnant and skeleton sheets are not available. |
| Fix | If you select this option, you should define the material type in the drop-down list. |
| None | Common type of the material will be used. |
| Coated | Coated steel material will be used. |
| Colored Steel | Colored steel material will be used. |

| See: | Material |
| --- | --- |
|  | Size Definition |
|  | Code Definition |
|  | Nesting |
|  | Process and User Define |
|  | Taking Out Station |
|  | Taking Out Part Grid as One Part |

### 8.7.3 Size Definition

The options in this section are used to specify the correct size of the sheet. These options are only available when you select Standard or Fix in the Special Information section.

| Option | Description |
| --- | --- |
| Auto | If you select this option, the system will select a suitable sheet size automatically. |
| Fix | If you select this option, the size table is enabled. You can then select a specific sheet size. The system will only use the specified size during the process. |

| See: | Material |
| --- | --- |
|  | Special Information |
|  | Code Definition |
|  | Nesting |
|  | Process and User Define |
|  | Taking Out Station |
|  | Taking Out Part Grid as One Part |

### 8.7.4 Code Definition

This section is used to set the code of the material. It is only available when you select Fix in Size Definition section.

| Option | Description |
| --- | --- |
| Auto | If you select this option, the system will select the sheet code automatically. |
| Fix | This option is used to specify sheet code. You can select a sheet code from the drop-down list. |

| See: | Material |
| --- | --- |
|  | Special Information |
|  | Size Definition |
|  | Nesting |
|  | Process and User Define |
|  | Taking Out Station |
|  | Taking Out Part Grid as One Part |

### 8.7.5 Nesting

|  | This section is used to specify nesting type. |
| --- | --- |

| Option | Description |
| --- | --- |
| Standard | Standard nesting will be used. |
| Sketch Nesting | Sketch nesting will be used. |
| Grid | If you select this option, parts will be nested as a grid. Part quantity setting will be ignored. |

| See: | Standard Nesting |
| --- | --- |
|  | Sketch Nesting |
|  | Grid Nesting |

| See: | Special Information |
| --- | --- |
|  | Size Definition |
|  | Code Definition |
|  | Process and User Define |
|  | Taking Out Station |
|  | Taking Out Part Grid as One Part |

#### 8.7.5.1 Standard Nesting

If you select Standard, the parts will be nested as follows:

| See: | Sketch Nesting |
| --- | --- |
|  | Grid Nesting |

#### 8.7.5.2 Sketch Nesting

Note:

Make sure that there is suitable sketch material in the Material Manager before you use the Sketch Nesting option. If necessary, create sketch material.

Example:

| 1. | There is 350 x 250 sketch material in the Material Manager: |
| --- | --- |
| 2. | If the part size is 300 x 200, you need to set the maximum tolerance for the sketch material in the Nesting window. |
| 3. | Select the Sketch Nesting option. |
| 4. | The parts will be nested as follows: |

| See: | Standard Nesting |
| --- | --- |
|  | Grid Nesting |

#### 8.7.5.3 Grid Nesting

If you select the Grid option, the parts will be nested as follows:

| See: | Standard Nesting |
| --- | --- |
|  | Sketch Nesting |

### 8.7.6 Process and User Define

The options in this section are unavailable if only Dr. ABE Blank is installed on the PC. The options can only be used when other software products, such as FabriTRAK, are loaded on your computer. For example, if you load a CSV file generated by FabriTRAK, some of the user-defined parameters would appear in the fields of this section.

| See: | Material |
| --- | --- |
|  | Special Information |
|  | Size Definition |
|  | Code Definition |
|  | Nesting |
|  | Taking Out Station |
|  | Taking Out Part Grid as One Part |

### 8.7.7 Taking Out Station

This section is used to specify Taking Out information. The options in this section are not available unless you have enabled TK device in the Machine Set window. See: Taking Out Information

| Option | Description |
| --- | --- |
| Station | You can only select None for EM machine. |
| Taking Out the Part Grid as One Part | Enable this option and the system will grid the parts in groups, and treat the parts in one group as one part and then performs taking out process. Note: Only the same parts can be nested and gridded in one group. |
| Specify Quantity X, Y | Specify the number of parts along the X-axis and Y-axis. |
| Part-Spacing | Specify the part spacing of the grid in the X and Y direction. Note: The value you specify here is only effective when the system treats several parts as a grid and performs taking out process. |

| See: | Material |
| --- | --- |
|  | Special Information |
|  | Size Definition |
|  | Code Definition |
|  | Nesting |
|  | Process and User Define |
|  | Taking Out Part Grid as One Part |

### 8.7.8 Taking Out Part Grid as One Part

Sometimes the parts we have processed are too small and cannot be taken out.  The Taking Out Part Grid as One Part option allows the system to grid the small parts in groups, and then takes them out.

To take out small parts in groups

| 1. | We will nest 20 small parts. |
| --- | --- |
| 2. | Enable TK device in the Taking-out Information |
| 3. | In the Peripherals window, place a check mark in the Taking Out On/Off check box to enable taking out conditions. |
| 4. | Select Joint and TK Station 1 as the process after method. |
|  | Note: We must select Joint as the process after method for the small parts, otherwise system cannot take out the part grid as one part. |
| 5. | Open the Parts Properties window, click the Advanced button and specify the settings as follows. |
| 6. | After auto execution, the nesting result is as follows. |

| See: | Material |
| --- | --- |
|  | Special Information |
|  | Size Definition |
|  | Code Definition |
|  | Nesting |
|  | Process and User Define |
|  | Taking Out Station |

# Chapter 9: Preference File Window

The options in the Preference windows are used to specify the default parameters for system operations. For example, if you click the Nesting Preference button in the main Dr. ABE window, the corresponding preference window will appear.

| See: | Preference Window Overview |
| --- | --- |
|  | Preference Window Menu |
|  | Preference Window Toolbar |

## 9.1 Preference Window Overview

The Preference window consists of three panes: Tree View, Preference File and Display Area. In the Tree View pane, you can select a machine and its corresponding preference files in the upper Preference File pane will display. The information of the selected preference file will appear in the lower Display Area.

| See: | Splitter Bars |
| --- | --- |
|  | Tree View Pane |
|  | Preference File Pane |
|  | Display Area Pane |

| See: | Preference Window Menu |
| --- | --- |
|  | Preference Window Toolbar |

### 9.1.1 Splitter Bars

The panes in Preference window are separated by splitter bars. To adjust the display area of each pane, just click and hold the corresponding splitter bar and drag it to the desired location. Release the mouse button when you have finished resizing the pane.

| See: | Tree View Pane |
| --- | --- |
|  | Preference File Pane |
|  | Display Area Pane |

### 9.1.2 Tree View Pane

Tree view provides an expandable view about all the available resources.

| See: | Splitter Bars |
| --- | --- |
|  | Preference File Pane |
|  | Display Area Pane |

| See: | Hierarchical Structure |
| --- | --- |
|  | Shortcut Menu |

#### 9.1.2.1 Hierarchical Structure

|  | The Tree View presents a hierarchical view of all the available resources. The minus box before an icon indicates that its subordinate items are displayed. For example, in the right figure, the My Preference node displays the available machines, Public folder and Recycle Bin. |
| --- | --- |
|  | In the picture above, the plus box before Public folder indicates there are subordinate items. Click the minus box before the icon and all the subfolders will collapse, while clicking the plus box, all the sub items will expand as follows. |

| See: | Shortcut Menu |
| --- | --- |

#### 9.1.2.2 Shortcut Menu

Right-click an icon in the Tree View to display the shortcut menu. If necessary, you can navigate the cascading menu system to select menu options. The shortcut options you can select are dependent on the icons you select. For example, if you select a FO machine, you can only create the preference files about Laser machine, while options about punch and combination machines are not activated. If you right-click My Preference icon, you can only select the Machine Folder and Collapse options. See: Create a new machine folder

| Option | Description |
| --- | --- |
| Expand | Expand the subordinate items. It will change into Collapse mode if no further information in the folder is selected. |
| New | The New submenu consists of options that allow you to create new folders and corresponding preference files. |
|  | Note: The Machine Folder, Material Type Folder, Thickness Folder and Laser Material Name Folder options only create new folders in the Tree View pane. The remaining options are used to create files in the Preference File pane. |
| Cut | Cut the selected item to the clipboard. |
| Copy | Copy the selected item to the clipboard. |
| Paste | Paste the items previously copied or cut to the clipboard to the desired place. |
| Delete | Delete the selected item. |
| Rename | Rename the selected item. |

Note:

In the Public folder, only Turret Type and Turret Type (PDC) options have shortcut menus. These shortcut options are used to create a new turret type preference file.

The folders and files deleted in the Preference window are transferred to the Recycle Bin. Right-click the Recycle Bin icon to display the shortcut menu.

| Option | Description |
| --- | --- |
| Expand | Display all the items in the recycle bin |
| Delete | Delete all the items in the recycle bin. |
| Restore | Restore the selected item to its original place. |
| Restore All | Restore all the deleted items to their original places. |
| Empty Recycle Bin | Empty all the items in the Recycle Bin. |

To create a new machine folder:

| 1. | Select My Preference icon and right-click to display the shortcut menu. |
| --- | --- |
| 2. | Select New to Machine Folder. |
| 3. | In the MachineName window, select the Machine Type and Machine Name from the drop-down list, and then click Add button to add the machine folder to the Tree View. Note: You can only add the machine folders for the machines that have been registered in the Machine Manager while have no corresponding machine folders. |
| 4. | A new machine folder LCXI is added to the Tree View. |

| See: | Hierarchical Structure |
| --- | --- |

### 9.1.3 Preference File Pane

|  | You can use two methods to display preference files: Details and Icon. The menu is used to toggle between Detail and Icon view. The Preference File pane lists all the available files. You can double-click a file to open it. You can also create, delete and rename new preference file. |
| --- | --- |
|  | When the Details option is selected. |
|  | When the Icon option is selected. |

| See: | Creating a New File |
| --- | --- |
|  | Preference File Shortcut Menu |

|  | Splitter Bars |
| --- | --- |
|  | Tree View Pane |
|  | Display Area Pane |

#### 9.1.3.1 Creating a New File

Select an icon in the Tree View, such as EM2510, and then right click to open the shortcut menu. Select New to Nesting Preference. A new Nesting Preference file will appear in the Preference File pane. The new file name will be New by default.

| See: | Preference File Shortcut Menu |
| --- | --- |

#### 9.1.3.2 Preference File Shortcut Menu

|  | Select a file from Preference File pane and right-click to display the shortcut menu. |
| --- | --- |

| Option | Description |
| --- | --- |
| Cut | Cut the file to the clipboard. |
| Copy | Copy the file to the clipboard. |
| Paste | Paste the copied file from the clipboard. |
| Delete | Delete the file. |
| Rename | This option allows you to rename the selected item in the pane. |
| Set Default | This option will set the selected file as default when there are several preference files of the same kind in the Preference File pane. |

| See: | Creating a New File |
| --- | --- |

### 9.1.4 Display Area Pane

When you click a file in the Preference File pane, the Display Area will update and allow you to view the contents. You can use vertical or horizontal scroll bars to navigate through the sections. You can also double-click the preference file to open the corresponding window.

| See: | Splitter Bars |
| --- | --- |
|  | Tree View Pane |
|  | Preference File Pane |

## 9.2 Preference Window Menu

|  | The menu bar consists of five menus: File, Edit, Tools, Window and Help. |
| --- | --- |

| See: | Preference Window Overview |
| --- | --- |
|  | Preference Window Toolbar |

| See: | File |
| --- | --- |
|  | Edit |
|  | Tools |
|  | Window |
|  | Help |

### 9.2.1 File

| Option | Description |
| --- | --- |
| New | Select an option from the New submenu to create the relevant file. |
|  | Note: Some options are disabled under certain conditions. |
| Save | Click Save to save the settings made in the current file. |
| Save All | Click Save All to save all the settings made in all files. |
| Close | Close the current Preference window. |

| See: | Edit |
| --- | --- |
|  | Tools |
|  | Window |
|  | Help |

### 9.2.2 Edit

|  | The options on the Edit menu allow you to edit the folders or files. You can Redo and Undo the operations, cut, copy, delete or rename the files. The options in this menu have the same functions as those in the shortcut menu in the Preference File window |
| --- | --- |

| See: | File |
| --- | --- |
|  | Tools |
|  | Window |
|  | Help |

### 9.2.3 Tools

|  | The options on the Tools menu allow you to change the display settings. You can change the interface languages or hide the toolbar. |
| --- | --- |

| Option | Description |
| --- | --- |
| Option | Select Tools to Option to open the Option window. You could check or modify the system settings. See: Option window. |
| Tool Bars |  |
| Standard | Place a check mark before the Standard option to display the standard toolbar. |
| View | Place a check mark before the View option to display the View toolbar. |

Option Window

| Option | Description |
| --- | --- |
| System Setting | Specify the system unit and language. |
| Display Unit | Two units are available: Metric and Inch. |
| Language | The available languages are Japanese, English and Chinese (PRC). |
| Save Confirmation Setting | If Display Save Confirmation Window is selected, when you close the Preference window, a Save Confirmation window will display; if Don’t Display Save Confirmation Window is selected, no confirmation messages will display. |
| Current Folder | The path of the folder where the preference files are saved. Click button to browse folder to change the default folder to save the preference files. |
| The Priority of Folder of Same Level | The priority of folders of same level, you can clicking the up and down arrow button to change the priority. |

| See: | File |
| --- | --- |
|  | Edit |
|  | Window |
|  | Help |

### 9.2.4 Window

|  | The currently opened file or folder names will appear on the Window drop-down list. A check mark next to a folder or file name will indicate that its corresponding window is active. |
| --- | --- |

| See: | File |
| --- | --- |
|  | Edit |
|  | Tools |
|  | Help |

### 9.2.5 Help

|  | Select Preference Help from the Help menu, or press <F1>, to open the on-line help reference. |
| --- | --- |

| See: | File |
| --- | --- |
|  | Edit |
|  | Tools |
|  | Window |

## 9.3 Preference Window Toolbar

The toolbar can enhance your interaction with the system. Each button on the toolbar corresponds to a command on the menu. You may prefer to click buttons to execute commands and functions, rather than navigate the menus.

Standard Toolbar

|  | New |
| --- | --- |
|  | Undo |
|  | Redo |
|  | Cut |
|  | Copy |
|  | Paste |
|  | Delete |
|  | Save |
|  | Save All |
|  | Help |
|  | Backup&Restore |

View Toolbar

|  | View |
| --- | --- |

Note:

Click the arrow button next to the New button to open the drop-down menu. You can select to create new folder and files.

Click the arrow button next to the View button to display a drop-down menu from which you can select whether to display the preference files in detail or as icons.

If you select Details, all the preference files will display as follows.

If you select Icon, all the preference files will be display as follows.

| See: | Preference Window Overview |
| --- | --- |
|  | Preference Window Menu |

# Chapter 10: Nesting Preference

The Nesting Preference window allows you to define the various nesting parameters to process parts. The system will use these parameters to nest the parts as efficiently as possible when you use the Auto Execute option.

To open the nesting window:

| 1. | Click the Nesting Preference button in the Dr. ABE window to open the Preference window. |
| --- | --- |
| 2. | Select an EM machine name (such as the EM2510) from the Tree View pane on the left. |
| 3. | Double-click the Nesting icon in the Preference File pane to open the Nesting window. The Nesting window consists of six panels: Nesting Logic 1, Nesting Logic 2, Initial Clamp Position, Part-Spacing/Nesting Border, Material Selection and Share to Size. |

| See: | Nesting Logic 1 |
| --- | --- |
|  | Nesting Logic 2 |
|  | Initial Clamp Position |
|  | Part-Spacing/Nesting Border |
|  | Material Selection |
|  | Share to Size |

## 10.1 Nesting Logic 1

In Nesting Logic 1 panel, you can review and modify the basic settings for nesting, such as Nesting Type, Pattern Setting and the Start Point/Direction.

| See: | Nesting Type |
| --- | --- |
|  | Pattern Setting |
|  | Start Point/Direction |

| See: | Nesting Logic 2 |
| --- | --- |
|  | Initial Clamp Position |
|  | Part-Spacing/Nesting Border |
|  | Material Selection |
|  | Share to Size |

### 10.1.1 Nesting Type

|  | This section allows you to specify whether parts are nested according to the individual shapes or the overall part boundaries. |
| --- | --- |

| Option | Description |
| --- | --- |
| Free Shape | If you select this option, the parts will be nested with its own shape. The system will nest the parts with the best utilization. |
| Rectangle | If you select this option, the parts will be nested with an outer rectangle. Within the range of the outer rectangle, system will not nest other parts even though there is blank area. |
|  | Note: If you select Rectangle, the Common Line Cutting option is disabled. |

Example:

| 1. | For example, you want to nest the following part: |
| --- | --- |
| 2. | If you select Free Shape, system will use the part shape as a parameter in the nesting process. The system will adjust the layout to achieve the best sheet utilization and nest the part instances as follows: |
| 3. | If you select Rectangle, the system will calculate a rectangular zone according to the overall part size and include the part within the rectangle: |
|  | The system will nest the parts as follows: |

| See: | Pattern Setting |
| --- | --- |
|  | Start Point/Direction |

### 10.1.2 Pattern Setting

|  | This section is used to specify the nesting order by the area, the dimension in the X-axis or Y-axis or production schedule. |
| --- | --- |

| Option | Description |
| --- | --- |
| Special | The system will ignore the priority setting in the Nesting Plan and nest parts. |
| Area | Parts with a larger area will be nested first. |
| X-Axis | The parts having a greater dimension along the horizontal axis will be nested first. |
| Y-Axis | The parts having a greater dimension along the vertical axis will be nested first. |
| Production Schedule | If Production Schedule is selected, parts will be nested according to the priority set in the Nesting Plan. The higher the production priority, the lower the nesting priority. See: How to nest parts by Production Schedule |

| See: | Nesting Parts by the Production Schedule |
| --- | --- |

| See: | Nesting Type |
| --- | --- |
|  | Start Point/Direction |

#### 10.1.2.1 Nesting Parts by the Production Schedule

| 1. | Set a different Group ID for each part, but set the same priority for the parts in the Nesting Plan. |
| --- | --- |
| 2. | Enable the Group Nesting function in the Group window. |
| 3. | Select Production Schedule in the nesting window. |
| 4. | The three parts are nested on three sheets according to the Group ID. |
| 5. | Set the same Group ID for all the parts, but set a different Priority for each part in the Nesting Plan window: Part A (Priority: 2), Part B (Priority: 3) and Part C (Priority: 4). The nesting result displays as follows: |

### 10.1.3 Start Point/Direction

|  | The options in this section are used to specify the start point and nesting direction. You could select a start point and direction by clicking corresponding point or arrow. The selected start point will become yellow and the selected direction arrow will become green. |
| --- | --- |
|  | You can shift the parts along the horizontal, vertical and diagonal axis. Click the directional arrow in the graphic below Shift After Nesting to specify the shift direction. The selected direction arrow will become green. |
| If you select a shift direction under Shift After Nesting, the Maximum Dimension for X Shifting or Maximum Dimension for Y Shifting text boxes become available. You can specify the maximum dimensions to shift the parts in the direction selected. |
| Note: If the X or Y value of the boundary box of all the nested parts is less than the X or Y shift value you have specified, parts will be shifted in that direction. The boundary box (the outer rectangle) is indicated in red: |

| See: | How to Define the Start Point/Direction |
| --- | --- |
|  | Example of Shift After Nesting |

| See: | Nesting Type |
| --- | --- |
|  | Pattern Setting |

#### 10.1.3.1 How to Define the Start Point/Direction

| 1. | If you specify the following starting point and direction: |
| --- | --- |
|  | The nesting result will be as follows: |
| 2. | If you specify the starting point and direction as below: |
|  | The nesting result will be as follows: |
| 3. | If you specify the starting point and direction as below: |
|  | The nesting result would be as follows: |
| 4. | If you specify the starting point and direction as below: |
|  | The nesting result will be as follows: |

| See: | Example of Shift After Nesting |
| --- | --- |

#### 10.1.3.2 Example of Shift After Nesting

| 1. | The Start Point/Direction is set as follows. See: Start Point/Direction |
| --- | --- |
| 2. | If Shift After Nesting is not selected, the nesting result will be as follows. |
|  | The part size is as follows. |
|  | And the dimension of the outer rectangle of the four parts will be as follows: |
| 3. | If Shift After Nesting in the X direction is enabled, and the maximum shifting value set at 700, which is greater than the X value of the outer rectangle, the nesting result will be as follows: |
|  | Select Y direction. The maximum shifting value set as 200, also. The parts will be shifted in the Y direction. |
|  | Select X and Y direction. Type 700 as the maximum shifting value for X direction and 200 for Y direction. The parts will be shifted both in X and Y direction. |

| See: | How to Define the Start Point/Direction |
| --- | --- |

## 10.2 Nesting Logic 2

Click the Nesting Logic 2 tab to activate the Nesting Logic 2 panel. In this panel you can specify the parameters for the part grid, the dead zone avoidance, the part rotation pitch, the pair and part in part function, and the line gap that can be ignored.

| See: | Grid Pattern |
| --- | --- |
|  | Nest Around Clamps |
|  | Part Rotation |
|  | Utilization |

| See: | Nesting Logic 1 |
| --- | --- |
|  | Initial Clamp Position |
|  | Part-Spacing/Nesting Border |
|  | Material Selection |
|  | Share to Size |

### 10.2.1 Grid Pattern

|  | This section is used to activate the part grid function. If you select Enable Part Grid option, system will nest the same parts as a grid. |
| --- | --- |

Example

If Enable Part Grid is selected, the system will create part grids while nesting the same parts:

If Enable Part Grid is disabled, the system won’t grid the parts when nesting:

| See: | Nest Around Clamps |
| --- | --- |
|  | Part Rotation |
|  | Utilization |

### 10.2.2 Nest Around Clamps

|  | Usually, the system will avoid nesting the parts on the clamp or dead zone to avoid any damage to the machine head or machine. However, if repositioning is available, you can nest parts in the clamp area or dead zones for better sheet utilization. The three options within the Nest Around Clamps section are used to specify whether to avoid clamps, the clamp area and dead zone. |
| --- | --- |

| Option | Description |
| --- | --- |
| Neglect Clamps | If you select this option, the system will ignore the clamp and dead zone information while nesting. It is not recommended unless repositioning is enabled. |
| Avoid Clamp Areas | If you select this option, the system will nest the parts around the clamps and avoid the clamp areas. |
| Avoid Dead Zones | If you select this option, the machine system will avoid the clamp dead zones when nesting. |

| See: | Grid Pattern |
| --- | --- |
|  | Part Rotation |
|  | Utilization |

### 10.2.3 Part Rotation

|  | You can select a number from the Rotation Pitch drop-down list to define the incremental angle for the part rotation. Specifying a rotation pitch for nesting will greatly reduce the nesting calculation time. If you select Auto, the system will rotate the part to any angle. If you select a number, the system will rotate the part incrementally according to the multiple you selected. For example, if you select 2, the rotation angle will be 4, 6, 8, 10 etc. The system will use the degree that results in the best sheet utilization. Selecting 1 will have the same effect as selecting Auto. |
| --- | --- |

| See: | Grid Pattern |
| --- | --- |
|  | Nest Around Clamps |
|  | Utilization |

### 10.2.4 Utilization

This section is used to specify methods to increase sheet utilization including Pair and Part in Part nesting.

| Option | Description |
| --- | --- |
| Pair | This option is used to nest the parts as pairs. Some irregular-shaped parts nested as pairs will result in better sheet utilization. |
| Part In Part | This option allows you to nest parts inside the cutouts of other parts. This will increase the sheet utilization. |
|  | Note: To enable Part In Part, you need to set the correct spacing between parts in the horizontal and vertical direction. |
| Minimum Cutout Edge Length | Type a value in the text box to define the length of the shortest edge of cutout. If the shortest edge is smaller than this value, the system will not nest parts into the cutout. |

| See: | Pair Example |
| --- | --- |
|  | Part In Part Example |

| See: | Grid Pattern |
| --- | --- |
|  | Nest Around Clamps |
|  | Part Rotation |

#### 10.2.4.1 Pair Example

Note: To enable Pair, you need to select Free from the Rotation drop-down list in the Parts Properties window.

If the Pair option is enabled, system will nest the parts as follows:

If the Pair option is disabled, system will nest the parts as follows:

| See: | Part In Part Example |
| --- | --- |

#### 10.2.4.2 Part in Part Example

| 1. | You want to nest two different parts on the sheet. One of the parts is larger and has a large cutout. The dimension of the cutout is 400 x 300. |
| --- | --- |
| 2. | Place a check mark in the Part In Part check box to enable the option. Type 250 in the Minimum Cutout Edge Length text box. |
| 3. | The smaller parts are nested within the cutout of the larger part after auto execution: |
| 4. | Type 400 in the Minimum Cutout Edge Length text box. |
| 5. | In this example, one of lines of the cutout is 300, which is smaller than Minimum Cutout Edge Length you specified. The smaller parts will not be nested within the cutout of the larger part: |

| See: | Pair Example |
| --- | --- |

## 10.3 Part-Spacing and Nesting Border

Click the Part-Spacing/Nesting Border tab to activate the Part Spacing/Nesting Border panel. In this panel, you can specify the part spacing and sheet margins.

To specify the part space and sheet margin, type values in the corresponding text boxes to define the part spacing.

| Option | Description |
| --- | --- |
| S | The spacing between parts. The value you specify is the horizontal and vertical spacing between the parts. |
| L | The distance between the leftmost part and the left sheet border. |
| R | The distance between the rightmost part and the right sheet border. |
| T | The distance between the topmost part and the top sheet border. |
| B | The distance between the bottommost part and the bottom sheet border. |

| See: | Advance |
| --- | --- |

| See: | Nesting Logic 1 |
| --- | --- |
|  | Nesting Logic 2 |
|  | Initial Clamp Position |
|  | Material Selection |
|  | Share to Size |

### 10.3.1 Advance

Place a check mark in the Advance check box to display the Advance table. You can specify the part spacing and nesting borders for material of different types and thickness.

Example:

| 1. | Set the spacing for two different kinds of material: 10 for AL material and 20 for CRS material: |
| --- | --- |
| 2. | Load two kinds of parts into the Nesting Plan. Select AL and CRS as the types of the sheet respectively. |
| 3. | The system will nest the Part 2 on the CRS material, and the part spacing is 20. |
| 4. | The system will nest Part 1 on the AL material, and the part spacing is 10. |

## 10.4 Initial Clamp Position

Click the Initial Clamp Position tab to activate the Initial Clamp Position panel. The options in this panel allow you to specify number of clamps and the clamp locations.

| See: | Number of Clamp |
| --- | --- |
|  | Absolute |
|  | Advance |

| See: | Nesting Logic 1 |
| --- | --- |
|  | Nesting Logic 2 |
|  | Part-Spacing/Nesting Border |
|  | Material Selection |
|  | Share to Size |

### 10.4.1 Number of Clamp

|  | Type the number of clamps in the text box, or use the spin controls to specify the number of clamps. The maximum number of clamps is determined by the settings in the Machine Set window. The range is from 0 to 4. |
| --- | --- |

| See: | Absolute |
| --- | --- |
|  | Advance |

### 10.4.2 Absolute

Use the Absolute option to edit the X value or horizontal position of the clamps in the diagram. The clamp locations are all measured relative to the left edge of the sheet. For example, the illustration below indicates that there are two clamps. The position of the first clamp is 300.00, while the position of the second is set at 800.00.

| See: | Number of Clamp |
| --- | --- |
|  | Advance |

### 10.4.3 Advance

The Advance option is used to define clamp parameters for different materials. The following table will appear after you select Advance:

| Column Title | Description |
| --- | --- |
| EQ. | The equation relationship between Sheet Size X and its value. |
| Sheet Size X | The X value of the sheet. |
| Base 1 (or 2…) | The reference of the clamp position. |
| MatLeft | The X-axis distance from the clamp to the left side of the material. |
| MatRight | The X-axis distance from the clamp to the right side of the material. |
| Origin | The X-axis value from the clamp to the origin. |
| Max Process Right | The maximum process range to the right of the material. |
| NO.1 (or 2…) | The distance to clamp NO.1 (or 2…). |
| Value 1 (or 2…) | The value of the clamp position relative to Base 1 (or 2…). |
|  | Note: If Absolute is selected, the settings for clamps in this section will be available for all the materials. |

Example:

| 1. | If you specify the clamp positions as follows: |
| --- | --- |
| 2. | Check the settings you have made in the Machine Set window. The settings should match those you have made in the Initial Clamp Position panel. |
| 3. | The nesting result will be as follows. |
| 4. | If Advance is selected, you can specify unique settings for different sheets. For example, you can specify the number of clamps first, and then use the Advance table for details. |
| 5. | The different clamp settings will be applied to the material of different sizes: |

| See: | Number of Clamp |
| --- | --- |
|  | Absolute |

## 10.5 Material Selection

Click the Material Selection tab to activate the Material Selection panel. The options in this panel allow you to specify the material type to be used and determine the utilization of reusable sheets.

| See: | Automatic Material Selection |
| --- | --- |
|  | Reusable Sheet |

| See: | Nesting Logic 1 |
| --- | --- |
|  | Nesting Logic 2 |
|  | Initial Clamp Position |
|  | Part-Spacing/Nesting Border |
|  | Share to Size |

### 10.5.1 Automatic Material Selection

The options in the Automatic Material Selection section allow you to specify the material type, selection and sketch material priority.

| See: | Material Selection Priority |
| --- | --- |
|  | Selection Priority |
|  | Use Sketch Material for Non-Sketch Parts |
|  | Don’t nest parts inside skeleton area |

| See: | Reusable Sheet |
| --- | --- |

#### 10.5.1.1 Material Selection Priority

|  | The options in this section are used to specify the priority of three material types: Skeleton, Remnant and Standard. You can select the type of the material to be processed by placing a check mark in the corresponding check box. If all the material types are selected, you can click up and down arrows to adjust the priorities. |
| --- | --- |

Example:

| 1. | If you select all the material types and specify the priority order as follows: |
| --- | --- |
|  | The Standard sheet (3000x1000) will be used. |
| 2. | If you select all the material types and specify their priorities as follows: |
|  | The Skeleton sheet (3000x1000) will be used. |
| 3. | If you select all the material types and specify their priorities as follows: |
|  | The Remnant sheet (3000x840) will be used. |

Note:

Make sure that the material types exist in the Material Setting, and Auto (auto select material) in the Part Properties Advanced window has been selected.

| See: | Selection Priority |
| --- | --- |
|  | Use Sketch Material for Non-Sketch Parts |
|  | Don’t nest parts inside skeleton area |

#### 10.5.1.2 Selection Priority

This section is used to select sheet utilization.

| Option | Description |
| --- | --- |
| Best Sheet Utilization | If you select this option, the system will check all the materials to find the material of the best utilization. |
| Do Not Consider Utilization | If you select this option, the system will not consider utilization but to select material according to the material type priorities. |
| Exceed Minimum Utilization | If you select this option, the Minimum Utilization text box is enabled. Type a value in the text box to specify the minimum utilization. The system will select the material that exceeds the minimum utilization. |

| See: | Material Selection Priority |
| --- | --- |
|  | Use Sketch Material for Non-Sketch Parts |
|  | Don’t nest parts inside skeleton area |

#### 10.5.1.3 Use Sketch Material for Non-Sketch Parts

|  | If you select this option, the sketch material will be available for regular nesting of smaller non-sketch parts. The sketch material will be processed in the same method with the standard material. If you remove the check mark from the check box, the sketch material will only be available when you nest sketch parts. |
| --- | --- |

| See: | Material Selection Priority |
| --- | --- |
|  | Selection Priority |
|  | Don’t nest parts inside skeleton area |

#### 10.5.1.4 Don’t nest parts inside skeleton area

|  | If you select this option, the system won’t nest parts inside the skeleton area. If you remove the check mark from the check box, the system will nest parts inside the skeleton area if necessary. |
| --- | --- |

| See: | Material Selection Priority |
| --- | --- |
|  | Selection Priority |
|  | Use Sketch Material for Non-Sketch Parts |

### 10.5.2 Reusable Sheet

This section is used to specify the type of reusable sheet that the system will create after completing a nest job. You have the option of creating skeleton sheets or remnant sheets.

| Options | Description |
| --- | --- |
| None | If you select this option, no reusable sheet will be created. |
| Create Skeleton Sheet | If you select this option, skeleton sheet will be created if sheet utilization is less than the max utilization. See: How to Create a Skeleton Sheet. |
| Max Utilization | Specify maximum utilization of skeleton sheet. You can type a value in the text box or click the up and down arrow buttons to adjust the value. |
| Create Remnant | If you select this option, remnant sheet will be created. See: How to Create a Remnant Sheet. |
| Pitch | Define the incremental value for the remnant creation. For example, if the Pitch value is set to 20, Mini X Size is set to 100, the possible remnant X size will be 100, 120, 140, 160, etc. |
| Mini X Size | Specify the minimum X dimension of the remnant. |
| Mini Y Size | Specify the minimum Y dimension of the remnant. |
| End Value | Define the end value for remnant creation. M00 (Machine Stop), Wire Joint and Micro Joint are available. |
| Joint Quantity | Type a value to define the joint quantity. |
| Joint Value | Type a value to define the width of joint. |
| Process | This option is used for Combo machine only. When processing machine is Combo machine, you can select whether uses laser or punching process method to create the remnants. |
| Type | Specify the method to create the remnant. |
| Horizontal Cut | To create a remnant sheet in the X direction. |
| Vertical Cut | To create a remnant sheet in the Y direction. |
| T Cut | To create remnants in the X and Y direction both. |
| Rectangle Cut | To create remnants of rectangle shape. |
| Detailed Setting | Click the Detailed Setting button to open the Joint Setting window. You can make detailed setting for joints. See: Joint Setting window. |

| See: | How to Create a Skeleton Sheet |
| --- | --- |
|  | How to Create a Remnant Sheet |

| See: | Automatic Material Selection |
| --- | --- |

### 10.5.3 Joint Setting Window

In the Material Selection section, click Detailed Setting button to open the Joint Setting window. You can specify the Remnant Type, Tool Size, Joint Interval, etc.

| Option | Description |
| --- | --- |
| Remnant Type | Click to select how to cut the remnant. When a different item is selected a different graph will displays, allowing you to define the Material adjustment amount, Maximum Joint interval and Process Direction. Horizontal Cut Vertical Cut T Cut Rectangle Cut |
| Material adjustment amount | Type a value in the textbox to define the place to start creating the remnant. This value represents the distance from the process-starting place to the sheet edge. If you select Laser as the process method, a positive value means the machine will overcut the material, while a negative value indicates the machine will undercut the material. |
| Maximum Joint interval | Type a value in the textbox to define the maximum distance between joints, when multiple joints are placed. |
| Process Direction | Click the arrow button to define the processing direction. The selected arrow button will turn green. |
| Nesting Border | Specify the distance between the sheet edge and the remnant edge. |
| Nesting Border Set | Use the settings in the Part-Spacing/Nesting Border panel to specify the distance between the sheet edge and the remnant edge. See: Part-Spacing and Nesting Border |
| Value | Type a value to distance between the sheet edge and the remnant edge. |

### 10.5.4 How to Create Skeleton Sheet

| 1. | Select Create Skeleton Sheet under Reusable Sheet and define the Maximum Utilization as 50. |
| --- | --- |
| 2. | The sheet utilization is only 10.094%. |
| 3. | The system creates the skeleton sheet and stores it in the Material Manager after saving the NC data. |

| See: | Reusable Sheet |
| --- | --- |

### 10.5.5 How to Create a Remnant Sheet

| 1. | In the Reusable Sheet section, specify the settings as follows. |
| --- | --- |
| 2. | Click the Detailed Setting button, and specify the settings as follows. See: Joint Setting Window |
| 3. | The system will create the remnant in the X direction. |
| 4. | And the system will generate M00 in the NC code. |
| 5. | If you specify the settings in the Reusable Sheet section as follows: |
|  | The nesting result will be as follows: |
| 6. | If you specify the settings in the Reusable Sheet section as follows: |
|  | The nesting result will be as follows: |
| 7. | If you specify the settings in the Reusable Sheet section as follows: |
|  | The nesting result will be as follows: |

| See: | Reusable Sheet |
| --- | --- |

## 10.6 Share to Size

Click the Share to Size tab to activate the Share to Size panel. In this panel, you can set the tolerance for sketch material, select the sketch type and specify joint settings.

| See: | Sketch Material Tolerance |
| --- | --- |
|  | Sketch Type |
|  | Joint |

| See: | Nesting Logic 1 |
| --- | --- |
|  | Nesting Logic 2 |
|  | Initial Clamp Position |
|  | Part-Spacing/Nesting Border |
|  | Material Selection |

### 10.6.1 Sketch Material Tolerance

|  | This section is used to specify the sketch material tolerance. |
| --- | --- |

In the following illustration, the blue pattern represents the part, and the red pattern represents the sketch sheet.

| Text Box | Description |
| --- | --- |
| X | If the distance in X-axis between sketch material and the part is not within the tolerance range, the material will not be used for sketch nesting. |
| + | Specify the maximum tolerance value in the X- axis. |
| – | Specify the minimum tolerance value in the X -axis. |
| Y | If the distance in Y-axis between sketch material and the part is not within the tolerance range, the material will not be used for sketch nesting. |
| + | Specify the maximum tolerance value in the Y- axis. |
| – | Specify the minimum tolerance value in the Y -axis. |

Notes:

| 1. | If you want to use sketch material for nesting, make sure sketch material has been stored in the Material Manager if necessary, define the sketch material in the Material Manager. |
| --- | --- |
| 2. | Sketch Nesting should be selected in the Part Properties Advanced window. |

Example:

| 1. | The following part has the dimensions of 300 x 200. |
| --- | --- |
| 2. | If you specify all the tolerance to zero, no tolerance will be allowed for the sketch nesting. |
|  | Only the sketch material of that is exactly 300 x 200 can be used for nesting the part. |
| 3. | If you specify the following tolerance values: |
|  | The sketch material of 350 x 250 can be used for nesting the part. |
| 4. | If you specify the following tolerance values: |
|  | The material that is smaller than the part size will be used because a shortage of 0.5 is allowed in the X size. |

| See: | Sketch Type |
| --- | --- |
|  | Joint |

### 10.6.2 Sketch Type

The options in the Sketch Type section allow you to specify conditions to process the remainder of the sheet having a size that is very close to the part and, having a Y size that is within the tolerance range, and having an X size greater than part.

| Option | Description |
| --- | --- |
| The Material Whose X Sizes do not Correspond is Used | You must select this option to activate the options below. |
| Punch Out if Distance < = | If the distance between part and material is smaller than the value in this text box, the remainder will be punched out. |
| Shift to Center if Distance > = | If the distance between part and material is greater than the value in this text box, the part will be shifted to the center of material. |
| Shift if Element is Not Vertical | If the longitudinal line of part is not vertical, type value in the text box to define the shift distance. |

Example:

| 1. | Use a 500 x 400 sketch material to nest a 300x 300 part. Specify the tolerance as follows: |
| --- | --- |
| 2. | The result is as follows. |
| 3. | Select Shift to Center if Distance is > = and type 10 in the text box. |
| 4. | The result is as follows. |
| 5. | If the part contains lines that are not vertical, you can shift it by the value you set. |
| 6. | The result is as follows. |

| See: | Sketch Material Tolerance |
| --- | --- |
|  | Joint |

### 10.6.3 Joint

This section is used to define the placement of joints on the cutting line. You can only place joints on straight cutting lines.

| Option | Description |
| --- | --- |
| Joint Interval Max | Type value in the text box to define the maximum distance between joints, when multiple joints are placed. |
| Process Direction | Click or to define the processing direction. The selected arrow button will turn green. |
| Material Adjustment Amount | Type a value in the textbox to define the place to start creating the remnant. This value represents the distance from the process-starting place to the sheet edge. If you select Laser as the process method, a positive value means the machine will overcut the material, while a negative value indicates the machine will undercut the material. |

Example:

| 1. | Set the Maximum Joint Interval to 50 and the Material Adjustment Amount to 10. The result on the right indicates that the system did not overcut the material. 10 |
| --- | --- |
| 2. | Set the Maximum Joint Interval to 100 and the Material Adjustment Amount to 5. The result on the right shows the system lengthens the path and overcuts the material. |

| See: | Sketch Material Tolerance |
| --- | --- |
|  | Sketch Type |

# Chapter 11: Tool Assignment

The Tool Assignment window provides options to set the preference for tool assignment. You can specify the methods by which the system processes the parts, the detailed tool assignment conditions, etc.

To open the Tool Assignment window:

| 1. | Click any Preference button in the Dr. ABE main window to display the Preference window. |
| --- | --- |
| 2. | In the Tree View, select the EM machine under My Preference. |
| 3. | Double-click the Tool Assign icon in the Preference File pane to display the Tool Assignment window. |
|  | Tool Assignment window contains the following tabs. Calculation provides options to set punch conditions. Tooling Pattern provides options to specify the methods to process the holes based on the shape and size. |

| See: | Calculation |
| --- | --- |
|  | Tooling Pattern |
|  | Edit of Template |

## 11.1 Calculation

The Calculation panel lists the basic assignment conditions. And you can click the Advance button to open Tool Assign Condition window and set the preferences for tool assignment.

| Option | Description |
| --- | --- |
| Nibbling Overlap | Specify the maximum and minimum tool overlap when nibbling is performed. |
| Protrude | Specify the maximum protrusion value when assigning tools to the notch. |
| Acute Angle Protrude | Specify the maximum protrusion value when assigning tools to slanted lines. |
| Tool Width | Specify the maximum and minimum size of the tools that will be used to process the perimeters. |
| Part Overlap | Specify the minimum and maximum protrusion value when assigning tools to process lines. |
| Punch Across Notch | Specify the maximum width of the notches that can be treated as lines for tool assignment |
| Micro Tab Width/ Wire Tab Width | Specify the joint amount. |
| Nibbling | When Nibbling is performed, specify the tool pitch or scallop height. The system will automatically calculate the pitch based on the scallop height. ※When the nibbling pitch is defined for a tool, the specified tool value will be applied. |
| Pitch | Specify the pitch. |
| Height | Specify the scallop height. |
| Auto | The system will automatically adjust the tool pitch or scallop height. |
| RE Tool Overlap | Specify the minimum overlap value when the several RE tools are assigned to a line. |
| SQ Tool Overlap | Specify the minimum overlap value when the several SQ tools are assigned to a line. |
| Ignore Trace Punching | Specify the size of the notches that will be punched out. |
| Min(W<=) | If the width is less than the specified value, the system will punch the notch. |
| L>WX | If length is larger than the specified times of the width, the system will punch the notch. |
| Tool Search | Specify the conditions to search tools. |
| Rotate Tool in Turret | The angle of the tools specified in the turret can be changed and tools can be used. |
| Inventory | Use all the tools registered in the tool inventory. |
| Only Single Hit | Only search the tool inventory for the single hit tool. |
| Assign |  |
| Allow Different Tool | Different tool assignments are allowed for the same part. |
| Only Part Rotate | When the same part is rotated and nested, different assignments are allowed. |
| Pressure Check | This function is not available for this moment. |
| Check the maximum tool | This function is not available for this moment. |
| Check the minimum tool | This function is not available for this moment. |
| Tool Size/Mat-Thickness>= | This function is not available for this moment. |

| See | Main |
| --- | --- |
|  | Tool Lap Value |
|  | Assignment |
|  | Joint |
|  | Contouring Assignment |
|  | Slit &V Notch |
|  | De-burring |
|  | Slot2&3 |

| See | Tooling Pattern |
| --- | --- |
|  | Edit of Template |

### 11.1.1 Main

Click Main tab in the Tool Assign Condition window to open Main panel. You can set preferences for line unification, assignment changing, turret generation, auto index, and pressure check.

| Option | Description |
| --- | --- |
| Unification | The options in the Unification section allow you to determine whether to process the two line segments as one. If you enable this option, the two lines that are separated by a notch, as indicated in the graphic to the left, will be considered as a single line by the system. See: Process multiple Line Segment as One Segment |
| Process Line Unification | Place a check mark in the check box to treat two line segments as one for the tool assignment. |
| Max Length | If the width of the notch is less than the Max Length specified here, the system will ignore it and continue to process the perimeter as a line |
| Process Inclined Line | Place a check mark in the check box to treat two inclined line segments as one for the tool assignment. |
| Assign |  |
| Assignment Change of the Same Part | Select this to change the assignment of the same part |
| When Part is Rotated | Select this to change assignment when part is rotated. |
| Search for Stock Tools | Select this option to search the tool inventory for suitable tools. See: Search for Stock Tools |
| Perimeter Process | Search for tools in the tool inventory to process the perimeter. |
| CR Tool | Search for RC tools in the tool inventory. |
| Slit | Search for tools in the tool inventory to process the slit. |
| Hole (Single Hit) | Search for tools in the tool inventory to single-hit the holes. |
| De-burring | Search for De-burring tools in the inventory. |
| Others | Search for tools in the tool inventory process other patterns. |
| The Internal Angle of Turret can be Changed | Select this option, and the system will change the angle of the tools in the stations to process the patterns if the tools are not fixed in the stations. See: Change the Tool Angle to Process |
| Perimeter Process | Change the tool angle to process the perimeters. |
| CR Tool | Change the tool angle of CR tools to process the patterns. |
| Slit | Change the tool angle to process the slits. |
| Hole (Single Hit) | Change the tool angle to single-hit the holes. |
| De-burring | Change the tool angle to de-bur the pattern. |
| Others | Change the tool angle to process other patterns. |
| Allow Die Change of Locked Station | Select this option and dies can be changed for the tools defined as Fixed in the turret. See: Change the Die Clearance of the Fixed Station |
| Select Tool from Turret by Priority | Select this option, and the tools installed in the turret will be assigned with higher priority. |
| Auto Index |  |
| Non AI Station is Used by Priority | If tools of the same size and shape are used at 0 degree or 90 degree, AI tools are used with higher priority. Select Non AI Station is Used by Priority, if the system uses two tools of the same size to process the parts at 0 degree and 90 degree, AI station won’t be used, and the system will add the two tools to the ordinary stations for the tool assignment. See: Non AI Station is used with higher Priority |
| Pressure Check | The options here allow you to decide whether to check pressure or not. If the tool is too big compared with the material thickness, the sheet will be possibly misshaped; if the tool is too small compared with the material thickness, the tool will be possibly damaged. So we need to check the pressure. |
| Check the maximum tool | Check the tool tonnage to decide whether the tool can be assigned to process the thick material. |
| Check the minimum tool | Check the tool size to decide whether the tool can be assigned to process the thick material. If Either size X or size Y is less than the minimum tool size, this tool cannot be assigned. Minimum Tool Size= Material Thickness x Coefficient (The value you typed in the Tool Size/ Thickness>= : textbox) |
| Tool Size/Material Thickness >= | Type a value in the text box to define the relations between the tool size and material thickness. For example, if you type 2 in the text box, the tools whose sizes are less than 2 times of the material thickness won’t be assigned. |

| See | Process multiple Line Segments as One Segment |
| --- | --- |
|  | Search for Stock Tools |
|  | Change the Tool Angle to Process |
|  | Change the Die Clearance of the Fixed Station |
|  | Non AI Station is used with higher Priority |

| See | Tool Lap Value |
| --- | --- |
|  | Assignment |
|  | Joint |
|  | Contouring Assignment |
|  | Slit &V Notch |
|  | De-burring |
|  | Slot2&3 |

#### 11.1.1.1 Process multiple Line Segments as One Segment

| 1. | Let’s take the following part for example. |
| --- | --- |
| 2. | Remove the check mark from Process Line Unification check box, and the system will process this part as follows. Lines and notches are processed respectively. |
| 3. | Place a check mark in the Process Line Unification check box, and set the Max Length to 25, the system will treat two horizontal lines as one kind for tool assignment. It is the same with those two vertical lines. |
| 4. | Place a check mark in the Process Incline Line check box, the system will process the part as follows, two inclined lines will be treated as one for the tool assignment. |
| 5. | If you set the Max Length to 15, the system will process this part as follows. Only the two inclined lines are treated as one line for the tool assignment. |

| See | Search for Stock Tools |
| --- | --- |
|  | Change the Tool Angle to Process |
|  | Change the Die Clearance of the Fixed Station |
|  | Non AI Station is used with higher Priority |

#### 11.1.1.2 Search for Stock Tools

In the Turret Generation section, we can specify whether to search the tool inventory for the tool assignment.

Example

| 1. | Let’s take the following part for example. |
| --- | --- |
| 2. | Specify the Turret Generation conditions as follows. |
| 3. | The system will only search the turret for tools, since no CR tools are installed in the turret stations, the system will use a RO tool to process the corner radius. |
| 4. | Place a check mark in the CR Tool check box, and the system will search the tool inventory and use a CR tool to process the corner radius. |
| 5. | Lets’ take another part for example. |
| 6. | Specify the Turret Generation conditions as follows. |
| 7. | The system will only search the turret for tools, since there is no specific tool in the turret to process slit, the system will use a 10X2 RE tool to punch the slit and the inner hole. |
| 8. | Place a check mark in the Slit check box, and the system will search the tool inventory for the slit tools. The system will use a 10X2 RE tool to process the inner hole and a 5X2 RE tool to process the slit. |

| See | Process multiple Line Segments as One Segment |
| --- | --- |
|  | Change the Tool Angle to Process |
|  | Change the Die Clearance of the Fixed Station |
|  | Non AI Station is used with higher Priority |

#### 11.1.1.3 Change the Tool Angle to Process

Select The Internal Angle of Turret can be Changed option, and the system will change the angle of the tools in the stations to process the patterns if these tools are not fixed.

Example

| 1. | We will process the following 200x80 rectangle part. |
| --- | --- |
| 2. | There are two RE Tools in the stations, The process angle of the 110x6 RE tool is defined to 0 and 90, and its process angle in the turret is set to 90. See: Process Angle The process angle of the other 50x6 RE tool is defined to 90, and its process angle in the turret is set to 90. |
| 3. | In the Turret Generation section, specify the setting as follows. |
| 4. | The system will use the 50X6 RE tool to process the vertical lines, but the system will not process the horizontal lines because none of the available tools has the proper process angle. |
| 5. | Place a check mark in the Perimeter Process check box, |
| 6. | The system will change the process angle of the tools in the turret for the tool assignment. The system will assign the 110x6 RE tool to the horizontal lines. |

| See | Process multiple Line Segments as One Segment |
| --- | --- |
|  | Search for Stock Tools |
|  | Change the Die Clearance of the Fixed Station |
|  | Non AI Station is used with higher Priority |

#### 11.1.1.4 Change the Die Clearance of the Fixed Station

Clearance is defined as the gap or space between the punch and die. The clearance has a major effect on the finished products, as well as tool wear. Material thickness, types of material and types of tools being used should be all considered in establishing proper clearance.

Different material requires different clearance for tool assignment. The tool assignment features check the die clearance before assigning each tool, and only the tools with the proper clearance will be assigned to process the corresponding material.  See: Clearance

Select Allow Die Change of Locked Station, and the system will change the die of the tools in the fixed stations during the tool assignment.

Example

| 1. | Let’s take an 80x80 part for example. Two kinds of material (SPC, A1050) will be used. Two kinds of material require different clearance for tool assignment. About the material clearance. See: Clearance |
| --- | --- |
| 2. | There are two RE tools in the fixed station. |
|  | The clearances for both RE tools are set to 0.2. See: Clearance |
| 3. | Allow Die Change of Locked Station is not selected. As a result, the RE tools can only be assigned to process the SPC material. No tools are assigned to the A1050 material. |
|  | The error message indicates the tool clearance doesn’t match the material clearance setting. |
| 4. | Allow Die Change of Locked Station is selected. The system will automatically change the die clearance for the tool assignment, As a result, the RE tools are assigned to process both the SPC and A1050 material. The tool clearance for SPC material is 0.2, while the tool clearance for A1050 material is changed to 0.3. |

| See | Process multiple Line Segments as One Segment |
| --- | --- |
|  | Search for Stock Tools |
|  | Change the Tool Angle to Process |
|  | Non AI Station is used with higher Priority |

#### 11.1.1.5 Non AI Station is used with higher Priority

If tools of the same size and shape are used at 0 degree and 90 degree respectively, AI tools are used with higher priority. Select Non AI Station is Used by Priority, AI station won’t be used, and the system will add the tools to the ordinary stations for the tool assignment.

Example:

| 1. | Let’s take a 200x100 part for example. The system will assign the following two RE tools to process the part. The process angles for both tools are set to 0 and 90. And both tools can be used as Auto Index tools. |
| --- | --- |
| 2. | If Non AI Station is used with higher Priority is selected, the system will add these tools to two ordinary stations for the tool assignment. |
| 3. | If Non AI Station is used with higher Priority is not selected, the system will put one RE tool to the AI station during the tool assignment. |

| See | Process multiple Line Segments as One Segment |
| --- | --- |
|  | Search for Stock Tools |
|  | Change the Tool Angle to Process |
|  | Change the Die Clearance of the Fixed Station |

### 11.1.2 Tool Lap Value

The options in the Tool Lap Value panel allow you to specify the minimum overlap value or length percentage of tools. The smaller value will be used as the minimum tool lap value. The system will only assign the tools that match the minimum overlap value or length percentage to process inner holes.

| Option | Description |
| --- | --- |
| Square |  |
| Minimum | Specify the minimum overlap value or length percentage of square tools. |
| Rectangle |  |
| Minimum | Specify the minimum overlap value or length percentage of rectangle tools. |
| Round Punch |  |
| Nibbling Lap Value | Specify the minimum overlap value or length percentage of RO tools for the nibbling process. |
| Punch Out Lap | Specify the minimum overlap value or length percentage of RO tools for the punch out process. |
| Etc… |  |
| Minimum | Specify the minimum overlap value or length percentage of tools other than square tools, rectangle tools, and RO tools. |
| Nibbling Pitch |  |
|  | Note: The setting in Nibbling Pitch section is not available if you define the pitch value for the tool in Attribute 1 panel. See: Special Pitch |
| Pitch | Specify the distance between tool hits when nibbling. |
|  | Note: The Pitch value should always be greater than the sheet thickness except Contouring tools and De-burring tools. |
| Scallop Height | The scallop height is the distance formed by the scallop of nibbling tools. For round tools, Scallop Height allows you to define the height of the scallop formed during nibbling. The smaller the value, the smaller the scallop. And system will automatically calculate the nibbling pitch. |
| Auto | Select this to activate Default MIN option and Default MAX option |
| Default MIN | Select this and input a value in the MIN DX: text box, the system will calculate the default minimum pitch value. |
| Default MAX | Select this and input a value in the MAX DX: text box, the system will calculate the default maximum pitch value. |
|  | MIN Pitch=Tool X Size*Input value% MAX Pitch=Tool X Size*Input value% As for tools of special shape, the longer side of the tool is tool X size. |

| See | Main |
| --- | --- |
|  | Assignment |
|  | Joint |
|  | Contouring Assignment |
|  | Slit &V Notch |
|  | De-burring |
|  | Slot2&3 |

### 11.1.3 Assignment

It is not always possible for the system to assign tools that can exactly fit the part perimeters, holes or slits for the punching process. Sometimes protrusions occur after the parts are processed. The options in the Assignment panel allow you to define the protrusion conditions for the tool assignment.  In the condition table, you can select a cell and type a value to modify.  You can right-click any blank area to open a shortcut menu, and select Add to add a new blank row, or select Delete to remove the selected row from the condition table.

| Option | Description |
| --- | --- |
| Slit | Specify the conditions to punch the slits, and it can prevent the slit area from being extremely slim. See: Slit Tool Assignment |
| Length (B) | The depth range of slit area. |
| Minimum Width (A) | The minimum width between tools that process slot. |
| Protrusion Value 1 | Specify the Min/Max protrusion value for Perimeter B assignment, as well as the Min/Max width of the tools used to process the perimeters. See: Perimeter Tool Assignment |
| Length (B) | The range of the perimeter length. |
| Protrusion (A) | The range of the protrusion. |
| Width (C) | The width range of the tools to be assigned. |
| Perimeter Protrusion Value 2 (Angle=0 or 90) | Specify the notch depth (B) and the maximum protrusion value (A) to assign single hit tools to process the notch. Note: For notch tool assignment, the system will first search for a single tool to process the pattern, if no such a single tool matches the conditions, the system will assign tools to shear-proof the slit based on the Slit conditions, if no tools match the slit conditions, the system will process the patterns using a punch grid. See: Tool Assignment for the Vertical or Horizontal Notch |
| Length (B) | The range of the notch depth |
| Protrusion (A) Max | The maximum protrusion value |
| Perimeter Protrusion Value 3 (Angle! =0 or 90) | Specify the tool assignment line length (B) and the maximum protrusion value (A) to assign single hit tools to process the notch with an angle. Note: For inclined notch tool assignment, the system will first search for a single tool to process the pattern, if no such a single tool matches the conditions, the system will assign tools to shear-proof the slit based on the Slit conditions, if no tools match the slit conditions, the system will process the patterns using a punch grid. See: Tool Assignment for Slanted Notch |
| Length (B) | The range of the notch tool assignment length. |
| Protrusion (A) Max | The maximum protrusion value. |

| See | Main |
| --- | --- |
|  | Tool Lap Value |
|  | Joint |
|  | Contouring Assignment |
|  | Slit &V Notch |
|  | De-burring |
|  | Slot2&3 |

| See: | Slit Tool Assignment |
| --- | --- |
|  | Perimeter Tool Assignment |
|  | Tool Assignment for the Vertical or Horizontal Notch |
|  | Tool Assignment for Slanted Notch |

#### 11.1.3.1 Slit Tool Assignment

| 1. | We will process the following part with a slit of 60x40. |
| --- | --- |
| 2. | In the Assignment tab of the Tool Assign Condition window, specify the Slit conditions as follows. |
| 3. | The system will assign a RE tool (20x5) to process the slit based on the Slit settings. |
| 4. | If you set the Minimum Width (A) to 60. |
|  | Since no tools match the conditions for the slit tool assignment, the system will use an SQ tool (10 x 10) to punch-grid the slit. |

| See | Perimeter Tool Assignment |
| --- | --- |
|  | Tool Assignment for the Vertical or Horizontal Notch |
|  | Tool Assignment for Slanted Notch |

#### 11.1.3.2 Perimeter Tool Assignment

| 1. | We will process the following part. |
| --- | --- |
| 2. | In the Assignment tab of the Tool Assign Condition window, specify the Protrusion Value 1 conditions as follows. |
| 3. | The system will assign the following tools to process the part. |
|  | The system assigns a RE tool (30x3) to process Perimeter 2, and assigns a RE tool (28x2.5) to process Perimeter 1, their protrusion value is as follows, larger than 2, less than 3. |
|  | For Perimeter 3, 4, 5, and 6, since none of their length matches the condition, the protrusion value is 0 for the tool assignment. |
| 4. | If we specify the Protrusion Value 1 settings as follows. |
| 5. | The system will assign the following tools to process the part. |
|  | The system assigns a RE tool (30x3) to process Perimeter 2, and assigns a RE tool (28x2.5) to process Perimeter 1, their protrusion value is as follows, larger than 2, less than 3. |
|  | And the system assigns a RE tool (110x6) to process Perimeter 3, and assigns a RE tool (70x5) to process Perimeter 4, their protrusion value is as follows, larger than 5, less than 6. |
| 6. | If we specify the Protrusion Value 1 settings as follows. Change the Minimum Width to 3. |
| 7. | The system will assign the following tools to process the part. The RE tool (28x2.5) is replaced with a RE tool (28 x3.5). |

| See: | Slit Tool Assignment |
| --- | --- |
|  | Tool Assignment for the Vertical or Horizontal Notch |
|  | Tool Assignment for Slanted Notch |

#### 11.1.3.3 Tool Assignment for the Vertical or Horizontal Notch

| 1. | We will process the following part. |
| --- | --- |
| 2. | If we specify the Perimeter Protrusion Value 2 (Angle=0 or 90) settings as follows. |
|  | The system will assign the following tools to process the part. A RE tool (30x10) is assigned to single-hit the notch. The protrusion value is 2. |
| 3. | If we set the Protrusion (A) Max to 1, |
|  | Since no tools match the settings defined in the Slit and Perimeter Protrusion Value 2 (Angle=0 or 90) table, the system will use a SQ tool (10x100) to punch-grid the notch. |

| See: | Slit Tool Assignment |
| --- | --- |
|  | Perimeter Tool Assignment |
|  | Tool Assignment for Slanted Notch |

#### 11.1.3.4 Tool Assignment for Slanted Notch

| 1. | We will process the following part. |
| --- | --- |
| 2. | If we specify the Perimeter Protrusion Value 3 (Angle! =0 or 90) settings as follows. |
|  | The system will assign the following tools to process the part. A RE tool (20x5) is assigned to single-hit the notch. The protrusion value is 5.657. |
| 3. | However, if we specify the Perimeter Protrusion Value 3 (Angle! =0 or 90) settings as follows. |
|  | The system will ignore the conditions in this table, and process the slit by using the conditions defined in the Slit table. |

| See: | Slit Tool Assignment |
| --- | --- |
|  | Perimeter Tool Assignment |
|  | Tool Assignment for the Vertical or Horizontal Notch |

### 11.1.4 Joint

The options in the Joint tab of the Tool Assign Condition window allow you to specify the joint width and set conditions to assign special tools to create joints.

| Option | Description |
| --- | --- |
| Joint | Specify the width of micro joint and wire joints. |
| Width of Micro Joint | The width of the micro joints. |
| Width of Mire Joint | The width of the wire joints. |
| Special Tool |  |
| Assign Special Tool for Joint | Place a check mark in the check box to create joints with special tools. See: Use Special Tool to Create Joints |
| Only for Wire Joint | Only assign tools to create wire joints, not to create micro joints. |
| One Side | If you select this option, only one side of the special tool could be used to create joints. When One Side is selected, four angles, 0, 90, 180 and 270 degrees, are available. |
| Two Sides | If you select this option, two sides of the special tool could be used to create joints. When Two Sides is selected, only 0-degree and 90-degree angles are available. |
| Width of Micro Joint | The width of the micro joints. |
| Width of Mire Joint | The width of the wire joints. |
| Management Name | The name of the special tool used to create joints. You can type the tool name in the cell directly. It must be consistent with the name of the special tool you have registered in the tool inventory. |
| Process Angle | The angle of the special tool for punching process. |
| Length (A) | The distance between the center point and the left-most point of the tool. |
| Length (B) | The distance between the center point and the right-most point of the tool. |
| Length (C) | The distance between the center point and the uppermost point of the tool. |
| Length (D) | The distance between the center point and the lowest edge of the tool. |
| Lap (%) | The overlap percentage. The system will determine the overlap value using this formula: Overlap= Lap (%) x Tool Total Length |
| Use Auto Index | Place a check mark in the check box to place joints tools in the AI stations. Note: If you have specified two special tools or more, and select Use Auto Index, only one special tool (The default tool angle is 0) will be assigned to create joints. |

| See: | Use Special Tool to Create Joints |
| --- | --- |

| See | Main |
| --- | --- |
|  | Tool Lap Value |
|  | Assignment |
|  | Contouring Assignment |
|  | Slit &V Notch |
|  | De-burring |
|  | Slot2&3 |

#### 11.1.4.1 Use Special Tool to Create Joints

| 1. | We will use the following special tool to create joints. |
| --- | --- |
| 2. | If we specify the Special Tool settings as follows. The process angle of the SP tool is set to 0 degree. |
| 3. | The system will assign this SP tool to create joints as follows. |
|  | If we set the process angle of the SP tool to 90 degrees. |
|  | The system will assign this SP tool to create joints as follows. |
| 4. | If you place a check mark in the Use Auto Index check box, |
|  | The system will add the SP tool to the AI station and create joints as follows. |

### 11.1.5 Contouring Assignment

Contouring Assignment provides options to specify the conditions to assign contouring tools to process the line, Arc Inside, and Arc Outside.

| Option | Description |
| --- | --- |
| Assign Tools to the Pattern Specified | This function is not available now. |
| Assign to the Line | Assign contouring tools to the line. You can specify the length range for contouring tool assignment. |
| Only Assigned to the Slanted Line | Only assign contouring tools to the slant line |
| Display Warning Message | When contouring tools are assigned, warning message appears in result view. |
| Assign to Arc Inside | Assign contouring tools to process the inside of the arc. You can specify the length and radius range for contouring tool assignment. |
| Display Warning Message | When contouring tools are assigned, warning message appears in result view. |
| Assign to Arc Outside | Assign contouring tools to process the outside of the arc. |
| Display Warning Message | When contouring tools are assigned, warning message appears in result view. |

Example

| 1. | We will process the following part. |
| --- | --- |
| 2. | A 3x3 RO tool is used as the contouring tool. |
| 3. | Specify the Contouring Assignment settings as follows. |
| 4. | The system will assign the 3x3 RO contouring tool to process the slanted line and two arcs. |

| See | Main |
| --- | --- |
|  | Tool Lap Value |
|  | Assignment |
|  | Joint |
|  | Slit &V Notch |
|  | De-burring |
|  | Slot2&3 |

### 11.1.6 Slit & V Notch

The options in the Slit & V Notch tab of the Tool Assign Condition window allow you to specify the conditions for slit and V notch tool assignment.

| Option | Description |
| --- | --- |
| Slit |  |
| Use Tolerance | Place a check mark in the check box to activate this section and the system will assign tools to process slit by considering tolerance. |
| Part-Spacing of Slit Process W <= | You can type a value in the text box to specify the maximum width of the slit that tolerance setting will be applied. If the notch width is less than the maximum width you have specified, the system will assign tools that meet the tolerance range to process the slit. |
| Tolerance | Specify the tolerance for slit tool assignment. |
| Assign Pattern | Select tool assignment method. |
|  | Select this option and the system will assign the tool to process the slit as the left figure indicates, the tool placement center and slit center share the same X coordinate. |
|  | Select this option and the system will assign the tool to process one side of the longer perimeter segment of the slit as the left figure indicates. |
|  | Select this option and the system will assign the tool to process one side of the shorter perimeter segment of the slit as the left figure indicates. |
| Tool Select | Select to use RO, RE or SQ tool to process the slit. |
| V Notch |  |
| Assign V Notch Portion | Place a check mark in the check box to activate this section. |
| Assign Pattern | Select tool assignment method. |
|  | Select this option, and the system will assign tools to process the V notch as follows. |
|  | Select this option and the system will make the tool center point correspond to V notch acuate portion. |
|  | Select RO tool, the system will assign tools to process the V notch as follows. |
|  | Select RE&SQ tool, the system will assign tools to process the V notch as follows. |
|  | Select this option and the system will make the tool bottom edge correspond to V notch acuate portion. |
|  | Select RO tool, the system will assign tools to process the V notch as follows. |
|  | Select RE&SQ tool, the system will assign tools to process the V notch as follows. |
| Tool Select | Select to use RO, RE or SQ tool to process the V notch. And specify the maximum size of the tools to be used. |
| RO | Select RO tool to process the V notch |
| X Size <= | Type value in the X Size <=: text box to specify the maximum diameter of the RO tools that can be assigned. |
| Extend Assign | Place a check mark in the check box and type a value in the Extend Assign: text box to specify the range in which the system can assign nibbling with RO tool. |
| RE&SQ | Select RE&SQ tool to process the V notch |
| X Size <= | Type value in the X Size <= and Y Size <= text boxes to specify the maximum X/Y dimensions of the RE or SQ tools that can be assigned. |
| Y Size <= |  |

| See | Main |
| --- | --- |
|  | Tool Lap Value |
|  | Assignment |
|  | Joint |
|  | Contouring Assignment |
|  | De-burring |
|  | Slot2&3 |

| See | Process the Slit |
| --- | --- |

#### 11.1.6.1 Process the Slit

| 1. | There is a part with a slit whose width is 1. Tolerance is set as 1.5. Make setting as following to allow tolerance when processing slit. |
| --- | --- |
| 2. | Select RO tool to process slit. |
| 3. | A RO 2.2 is used to process slit. The system will use different processing mode according to your selection. |
| 4. | Select RE& SQ tool to process slit. |

### 11.1.7 De-burring

The options in the De-burring tab of the Tool Assign Condition window allow you to specify the conditions for de-burring tool assignment.

| Option | Description |
| --- | --- |
| De-burring |  |
| Enable Deburring Tool Processing During Outer Shape Processing | Place a check mark in the check box and then the system will assign de-burring tool to process the outer shape of the part. |
| Imbalanced Processing | Place a check mark in the check box to enable imbalanced processing. |
| Enable Deburring Tool Processing During Hole Processing | Place a check mark in the check box and then the system will assign de-burring tool to process the hole of the part. |
| Imbalanced Processing | Place a check mark in the check box to enable imbalanced processing. |
| Disable Deburring when size | Place a check mark in the check box and type a value in the X<=: text box and Y<=: text box, the system will not assign De-burring tool to process hole whose X dimension or Y dimension is equal to or smaller than the value. |
| Wire joint compensation amount | Place a check mark in the check box and type a value in the text box to specify the compensation value of wire joint. |
| Micro joint compensation amount | Place a check mark in the check box and type a value in the text box to specify the compensation value of micro joint. |
| It Is Allowed To Assign Tool At Straight Line Portion De-burring-Round | Place a check mark in the check box and the system will use RO de-burring tool to process straight line. |
|  | SQ Deburring Tool | RO Deburring Tool |
|  | If you place the check mark, the result is the following |
| Only Diagonal Line Is Allowed | Place a check mark in the check box and the system will use RO de-burring tool to process only inclined line. |
|  | If you place the check mark, the result is the following |
| Perform The Fixed Process Sequence To Joint G90 and De-burring | Normally, the process sequence of Joint and Deburring process is the following: Joint G90 -> De-burring. But if you place a check mark in the check box, the system will perform the fixed process sequence to Joint G90 and Deburring. The process sequence is: De-burring -> Joint G90 |

Note:

To enable this function, you should make corresponding setting in Parts Properties.  Place a check mark in the De-Burring ON/OFF check box.

| See | Main |
| --- | --- |
|  | Tool Lap Value |
|  | Assignment |
|  | Joint |
|  | Contouring Assignment |
|  | Slit &V Notch |
|  | Slot2&3 |

### 11.1.8 Slot2&3

The options in the Slot2&3 tab of the Tool Assign Condition window allow you to specify the conditions to assign slot tool.

SLOT2&3 tool is delicate, and it can be easily broken due to various reasons such as processing direction and lap amount of each tool path. Hence, it is necessary to assign tools o that tools ill not be broken in case of performing assignment automatically.

| Option | Description |
| --- | --- |
| Slot2&3 |  |
| Use slot tool at the time of skip-process on outer shape | Place a check mark in the check mark in the check box and you can make detailed settings for using slot tool at the time of skip-process on outer shape. |
|  | Slot tool can be only used to process the outer perimeter of the part. Holes and slots are not the targets. Line that has already had assignment is not a target. In the picture below, red lines represent lines assigned with slot tools. |
| Minimum Assigned Element Length | Type a value in the text box to specify the minimum length. If the line length is smaller than the value, the system will not assign slot tool to process it. |
| Stating/Ending Point Overlap Amount | Type a value in the text box to specify the overlap amount of starting /ending point. The minimum value is 0.001mm and the maximum value is 99.999mm. |
|  | The overlap value is 0.0001mm | The overlap value is 8mm |

Note:

To assign slot tools, you should make corresponding settings in Parts Properties. Place a check mark in the [SLOT AUTO ON/OFF] check box.

| See | Main |
| --- | --- |
|  | Tool Lap Value |
|  | Assignment |
|  | Joint |
|  | Contouring Assignment |
|  | Slit &V Notch |
|  | De-burring |

## 11.2 Tooling Pattern

The Tooling Pattern panel provides options to specify the conditions to process holes based on the shape and size. The Tolerance options allow you to specify whether to apply tolerance settings to tool assignment.

If tolerance setting is applied, select Value option and specify the tolerance range for the tool assignment.

You can click Advance button to open the Shape Condition window to specify the detailed settings based on shape and size. Shape Condition window consists two panels:  Tool Style and Match To Line.

You can also remove the check mark and specify the tool assignment priority for the specified template.

| See: | Simple Tool Assignment Setting for the Specified Template |
| --- | --- |
|  | Fit Tool Style Panel |
|  | Match To Line |

| See: | Calculation |
| --- | --- |
|  | Edit of Template |

### 11.2.1 Simple Tool Assignment Setting for the Specified Template

In the Tool Pattern panel, we can specify the tool assignment priority based on the template shape.

This panel lists seven system template patterns, and they are RO, RE, RR, OB, DD, SD and Irregular Hole. As the following picture indicates, for the irregular hole tool assignment, the method of punching out the pattern has the highest priority, while for the rest 6 patterns, single-hit will be first considered for the tool assignment.

You can click Advance button to open the Shape Condition window to specify the detailed settings based on shape and size.

To set the tool assignment priority based on the shape:

| 1. | Remove the check mark from the check box before Advance, and click a pattern to open the Pattern List window. For example, if you click the RO pattern, The Pattern List will display all the tool assignments for the round hole. Different patterns represent different tool assignments. For example, represents single-hit tool assignment. |
| --- | --- |
| 2. | In the Pattern List window, select one pattern, and click button to change the position, the pattern on the top left corner of the list indicates the corresponding tool assignment has the highest priority. As the following window shows, RO tool B assignment has the highest priority for the round hole process. Click to save the settings. |
| 3. | The patterns in the Tool Pattern update, as we can see, the RO pattern has changed, showing that RO tool B assignment has the highest priority for the round hole process. |

### 11.2.2 Fit Tool Style Panel

The Fit Tool Style panel provides options to set the preference for the tool assignment based on the shape and size. You can select one pattern and specify the tooling methods based on the sizes. You can also create new template patterns to meet your own needs if necessary.

| Panel Area | Description |
| --- | --- |
| Hole Pattern List | Display the information registers in the standard system pattern and templates. |
| The Info. of the Pattern Being Selected | Display the information of the template pattern being selected. Such as Name, Comment, Type, and Dimensions. This section displays the template dimensions. There are usually two dimensions: X and Y, but some special templates have a R dimension, such as RR and CR. |
| Assignment Pattern List | Display candidate patterns with tools assigned. |
| Edit Template | Create and modify the template pattern. See Edit Of Template |
| Detail Setting | Set pattern size and define the tool assignment condition. The higher ID level is, the higher the priority will be. The system will apply the conditions from top to bottom. |
| Priority Pattern ID Level | Specify the tool assignment priorities. |

| See: | Hole Pattern List |
| --- | --- |
|  | Pattern Information and Assignment Pattern List |
|  | Template Detail Settings |

| See: | Simple Tool Assignment Setting for the Specified Template |
| --- | --- |
|  | Match To Line |

#### 11.2.2.1 Hole Pattern List

Hole Pattern List shows all the available templates. You can click the downward button and select the pattern type to display.

| Drop-down List Item | Description |
| --- | --- |
| All | Display all the templates. |
| System | Only display the system templates. |
| Hole | Only display the hole templates. |
| Notch | Only display the notch templates. |
| Corner Notch | Only display the corner notch templates. |

Right-click the Template list area to open a shortcut menu. The options on this shortcut menu allow you to add, delete, insert or edit the system template data

| Shortcut Option | Description |
| --- | --- |
| Add of Template Data | When the pattern you need doesn’t exit in the pattern list, you can select Add of Template Data to append data to the bottom of the list. |
| Delete of Template Data | Delete the selected template. |
| Insert of Template Data | Select Insert of Template Data to insert a pattern before the selected row. |
| Edit of Template Data | When there are not enough patterns with tools assigned, you can select Edit of Template to modify the template selected. Note: System Template cannot be edited. |

| See: | Pattern Information and Assignment Pattern List |
| --- | --- |
|  | Template Detail Settings |

#### 11.2.2.2 Pattern Information and Assignment Pattern List

Pattern Information area displays the relevant information of the template selected. And the Assignment Pattern List displays all the relevant tool assignment methods.

| See: | Hole Pattern List |
| --- | --- |
|  | Template Detail Settings |

#### 11.2.2.3 Template Detail Settings

In the Detail Setting section, you can specify the conditions for the tool assignment of the selected template.

| Column | Description |
| --- | --- |
| Symbol | The dimensions of the template. Click Symbol cell to open a drop-down list and there are seven options in the drop-down list. |
|  | Note: These options vary with templates. For a RE, OB, SD, DD and Irregular Hole templates of system type, you can set the dimension conditions for X and Y values; For a RR template, you can set dimension conditions for X, Y and R values. While for a RO template, you can only specify the X dimension conditions. A, B, C and D values are available for template other than System type. |
| Eq. | Specify the relationship between the shape to be processed with the dimension value you typed in Value cells. There are six options: < (less than), <= (less than or equal to), > (greater than). >= (greater than or equal to), == (equal to), and != (unequal to). |
| Value | Specify the reference dimension value. |

In the Priority Pattern ID Level area, you can select one tool assignment and specify the tool assignment priority number by typing number in the cell. The lowest priority number indicates the highest tool assignment priority. If the dimensions of a part match the corresponding dimension settings, the system will assign tools to process based on the defined tool assignment priorities.

Example

| 1. | We will process the following part. The diameter of Hole A is 16 and the diameter of Hole B is 32. |
| --- | --- |
| 2. | In the Fit Tool Style panel, we select the RO template and specify the detail settings as follows. |
| 3. | Since the diameter of Hole A matches Condition 1, the system will first consider tool assignment A and search tools to single-hit the hole. If no tools are available, the system will consider using other methods to process the hole based on the tool assignment priority. Here a 16x16 RO tool is used to process Hole A. The diameter of Hole B match Condition 2, the system will first search tools to single-hit the hole, if no tools are available, the system will consider other tool assignment based on the tool assignment priority you have set. Because RO tools can be assigned to single-hit Hole B, the system will use tool assignment E based on the tool assignment priority you have set. The system will arrange an 8x8 RO to nibble Hole B. |
| 4. | If we set the tolerance as follows in the Tooling Pattern panel. |
|  | The system will use a 30 RO tool to single-hit Hole B. |

| See: | Hole Pattern List |
| --- | --- |
|  | Pattern Information and Assignment Pattern List |

### 11.2.3 Match To Line

The Match To Line panel provides options to set the preference for the SP tool to process the line segments (Single Hit, Punch Out).

| Option | Description |
| --- | --- |
| Match to Line | Place a check mark to Assign specified SP to process the perimeters (Single Hit, Punch Out). |
| It Process before Template | Select It Process Before Template option and template settings will be applied with higher priority. |
| It process After Template | Select It Process After Template option and the settings defined here are of higher priority when tools are assigned. |
| List of Tool | The List of special tools. |
| Add | Add a special tool from the tool inventory. See: Tool Inventory |
| Delete | Delete the special tool. |
| Tool Information | The information of the SP tool being selected. |
| Shape | Tool shape. |
| Range | Tool guide ranges. |
| X/Y/R Size | The X/Y/R size of the tool. |
| Shape Sub Code | Supplemental information for contouring tools, nesting tools, etc. |
| Comment | Tool comments |
| Assign Setting | Specify the conditions to assign SP tool to process the patterns. |
| Inner | Assign the SP tool to process the inner loops. |
| Outer | Assign the SP tool to process the outer perimeters. |
| For Acute | Place a check mark in the For Acute check box to assign special tools with acute angles to process parts with angles. The SP tools selected will only be assigned for angle processes. |
| Cancel All | Cancel all the previous operations. |
| Save | Save the modifications. |

| See: | Simple Tool Assignment Setting for the Specified Template |
| --- | --- |
|  | Fit Tool Style Panel |

#### 11.2.3.1 Assign SP Tool to Process Line Segment

In the Match To Line panel, we can specify the conditions to assign SP tool to process the parts.

| 1. | We will process the following part. The arc radius is 10. |
| --- | --- |
| 2. | In the Match To Line panel, click Add to open the Tool window, select one SP tool and click Add to add the SP tool to the List of Tool table. |
| 3. | In the Assign Setting preview area, click one element to be used to process the part. The selected element will be highlighted in red. If the selected element of the SP tool matches the pattern, the system will assign the SP tool to process this pattern. |
| 4. | Place a check mark in the Outer check box to assign the SP tool to process the outer perimeter. Type the assignment pattern name in the text box, and then click Save. The specified assignment pattern will be displayed in the column on the right. You can specify more than one assignment pattern to meet your needs. The icons in this column represent the assignments that have been registered for each tool. Click an assignment, and its corresponding setting information will be displayed on the left. |
| 5. | Since the selected element of the SP tool share the same radius with the Arc. The system will assign the SP tool to process the arc by the specified pattern element. |

## 11.3 Edit of Template

In the Fit Tool Style panel, click Edit of Template button to open List Of Template window.  You can select an existed template in the template list or input the template name directly in the File Name: text box, and then click Edit button to open Template pane to edit the template. If you select an exited template in the template list, the name of the selected template appears automatically in the File Name: text box.

You can also type a new name in the File Name: text box to create a new blank template and then click Edit button to open Template pane to edit the new template.

| Option | Description |
| --- | --- |
|  | In this drop-down list, you can select which type of template you want to display in the list below. Select All to display all templates; Select Hole to display Hole template; Select Notch to display Notch template and select Corner Notch to display Corner Notch template. |
|  | In the template list area, you can select the template you want to edit. The name of the selected template will appear in the File Name: text box automatically and then click Edit button to open Template pane to edit it. |
| File Name | You can type the name of an exited template and click Edit button to open Template pane to edit it. |
|  | You can also type a new name to create a new template and click Edit button to open Template pane to edit it. Example: 123.notch “123” represents name. “notch” represents type. If you don’t input the template type, the default type is Hole. |
| Edit | Click this button to open Template pane. |
| Cancel | Click this button to cancel your setting and exit List Of Template window. |

| See: | Template Pane |
| --- | --- |
|  | Pattern Pane |

| See: | Calculation |
| --- | --- |
|  | Tooling Pattern |

### 11.3.1 Template Pane

In the List OF Template window, click Edit button to open Template pane. Here you can edit an exited template or create a new template.

| See: | Template Menu |
| --- | --- |
|  | Template Toolbar |
|  | Template Icon |
|  | Template Parameter |
|  | Shape Edit area |
|  | Generate data |
|  | Edit of Path |
|  | Edit of Elements |
|  | Edit Additional Elements Information |

| See: | Pattern Pane |
| --- | --- |

#### 11.3.1.1 Template Menu

The menu bar contains four items. If you select an item, a list of associated command options appears. You can use the mouse to navigate the menu by pointing and clicking the desired option.

| See: | Template Toolbar |
| --- | --- |
|  | Template Icon |
|  | Template Parameter |
|  | Shape Edit area |
|  | Generate data |
|  | Edit of Path |
|  | Edit of Elements |
|  | Edit Additional Elements Information |

#### 11.3.1.2 Template Toolbar

The toolbars can enhance your interaction with the program. Each toolbar corresponds to each menu. The buttons on the toolbars are associated with the commands found on the menus. You may find it easier to recognize and associate a particular toolbar button with a function than navigate a menu.

| File Toolbar |
| --- |
|  | Create a new template |
|  | Open an exited template. Click this button to open the List Of Template window. You can select an exited template in the template list area or input the name of an exited template directly in the File Name: text box, and then click Edit button to open it. You can also click Open CAD button to open a CAD file. |
|  | Download .prm files from AP100 |
|  | Save template |
| Edit Toolbar |
| The following eight buttons are basic edit buttons. |
|  | Cancel the previous operation. |
|  | Repeat the previously un-done action. |
|  | Cut the specified object |
|  | Copy the specified object |
|  | Paste the object that you previously cut or copied to the clipboard |
|  | Delete the specified object |
|  | Draw dimension line |
|  | Example: |
|  | 1. | The following is a basic shape of template without dimension. |
|  | 2. | Click and then the mouse becomes a cross-shape pointer in the Shape Edit area. A message appears prompting you to designate the first point of dimension line. |
|  | 3. | Select a point on the shape as the first point of dimension line. If you select the starting point, the middle point or the end point of an element as the first point of dimension line, a green point will appear automatically. |
|  | 4. | Click to confirm the first point and then drag the cross-shape pointer to select the second point. The first point becomes red and a green point will move with the pointer. A message appears prompting you to designate the second point of dimension line. |
|  | 5. | Click to confirm the second point. A number appears to designate the dimension between the two points. |
|  | 6. | You can also use letter to designate the dimension by pressing or key and selecting A, B, C or D in the text box. Generally, the first dimension will be designated A. Letter “A” will appear instead of the number. |
|  | 7. | To avoid overlap, you can drag the dimension line left or right, upwards or downwards according to actual condition. |
|  | 8. | You can also move the pointer to change the position of the designating letter (or number). |
|  | 9. | If you use number to designate the dimension, just click to finish your operation. If you use letter to designate the dimension by selecting in the text box, click or press <Enter> key to finish your operation. |
|  | 10. | Use the same way to designate other dimensions. |
|  | 11. | The designating dimension line is corresponding with the reference sizes in Parameter pane. You can click the arrow button next to each text box to select a name for the reference size or type a name for it. For Reference Size A and B, the default names are SMAXX and SMAXY respectively. |
|  | 12. | Referece Size A,B, C and D are associated with the optoins of Symbol column in Shape Condition window. See Symbol (Bookmark) |
|  | Select all elements of the basic shape, including dimension lines. |
| The following four buttons are drawing buttons. |
|  | Select command. Use the pointer to draw a frame, and the object in the frame will be selected. |
|  | Draw lines (one by one). When you finish drawing, click to exit. |
|  | Draw continuous line. After finishing drawing, right-click and select Pointer to confirm your operation or click directly to confirm your operation. |
|  | Draw arc. When you finish drawing, click to exit. |
| The following nine buttons are main editing buttons. |
|  | Rotate the selected element. |
|  | Example: |
|  | 1. | Select an element as rotating object and click . In the Shape Edit area, the mouse becomes a cross-shape pointer. A message appears prompting you to designate a basic point. Click to confirm a basic point. |
|  | 2. | Drag the pointer and you can see a dashed line rotate round the basic point. The value in the text box updates automatically to remind you the rotate angle when you drag the pointer. Also you can press or key and then type rotate angle directly in the text box. |
|  | 3. | Click to confirm your operation if you are satisfied with the rotation. (Press <Enter> key to confirm your operation if you rotate the element by typing value in the text box.) A dialog box appears asking you whether to remain the original object. |
|  | 4. | Click Yes to remain the original object. Click NO to delete the original object. |
|  | Mirror the selected element. |
|  | Example: |
|  | 1. | Select an element as rotating object and click . In the Shape Edit area, the mouse becomes a cross-shape pointer. A message appears prompting you to designate the first point of mirror line. Click to confirm the first point. |
|  | 2. | A message appears prompting you to designate the second point of the mirror line. Click to confirm the second point. A dialog box appears asking you whether to remain the original object, as appears in rotating operation. Click Yes to remain the original object. Click NO to delete the original object. |
|  | Create tangent corner radius. When you finish drawing, click to exit. |
|  | Click and a message appears prompting you to select the first object. A text box appears and you can press or key and then type a value in it to specify the radius length. At the same time, a message appears prompting you to select the second object. A tangent corner radius will be created when you finish selecting the second object. |
|  | Create inner corner radius. When you finish drawing, click to exit. |
|  | Use the same way as you create tangent corner radius to create inner corner radius. |
|  | Create outer corner radius. When you finish drawing, click to exit. |
|  | Use the same way as you create tangent corner radius to create outer corner radius. |
|  | Line grid |
|  | Example: |
|  | 1. | Select an object and click . In the Shape Edit area, the mouse becomes a cross-shape pointer. A message appears prompting you to input grid number in the text box. Type a value in it and press <Enter> key to confirm. |
|  | 2. | After input the value, click to confirm a base point. Drag the pointer to form grid and the values in the two text boxes update automatically. You can also type values in them respectively. (Press<Tab> key to switch between the two boxes.) |
|  | 3. | Click to confirm your operation. (Press <Enter> key to confirm your operation if you type values directly.) |
|  | Parallel grid |
|  | Use the same way as you create line grid to create parallel grid. Under this circumstance, you should first input grid number in X direction and then input grid number in Y direction in the boxes appearing during your operation. |
|  | Annular grid |
|  | Example |
|  | 1. | Select an object and click . In the Shape Edit area, the mouse becomes a cross-shape pointer. A message appears prompting you to designate a base point. |
|  | 2. | Click to designate a base point and then drag the pointer or type values in the text boxes to specify grid length, angle and number respectively. |
|  | 3. | Confirm your operation by using the same way as you do to confirm line grid. |
|  | Arc grid |
|  | Use the same way as you create annular grid to create parallel grid. |
|  | Trim the selected element |
|  | Example: |
|  | 1. | Suppose we want to trim the redundant sections of the two overlong lines in the following pattern to form a triangle. |
|  | 2. | Click and the mouse becomes a cross-shape pointer in Shape Edit area. A message appears prompting you to select an object. |
|  | 3. | Draw a frame with the pointer to select the whole pattern. Right click to confirm and the pattern selected becomes red. |
|  | 4. | Click to select the pattern you want to trim and the selected pattern will be trimmed. Click to confirm. |
|  | Extend an element to another element. |
|  | Example: |
|  | 1. | In the following basic shape, select E5. |
|  | 2. | Click and the mouse becomes a cross-shape pointer in the shape edit area. A message appears prompting you to select an object to extend. |
|  | 3. | Select E2 as the object to extent and you will see that E2 is extended to E5. Click to confirm and exit this mode. |
|  | Frame line. The system can recognize notch and corner notch easily by using frame line. |
|  | How to create frame line |
|  | 1. | Take the following corner notch as an example |
|  | 2. | Click and the mouse becomes a cross-shape pointer in the Pattern Edit area. A message appears prompting you to select a frame line. Select one frame line and then select the other one by using the same way. The green line and orange line are frame lines. Click to confirm your operation. |
|  |  | Note: In Part Edit mode, when you select to save template, the system will generate frame lines automatically if you select notch or corner notch as template type to save. |
|  | Elongate an element. |
|  | Example: |
|  | 1. | Click and the mouse becomes a cross-shape pointer in the Shape Edit area. A message appears prompting you to select an object to elongate. |
|  | 2. | Select an object, such as E3. A message appears prompting you to enter elongating value in the text box. You can also drag the pointer to elongate ad the value in the text box will update automatically. |
|  | 3. | Press <Enter> key to confirm your operation if you type values in the text box directly. Click to confirm your operation if you elongate by dragging the pointer directly. At last, you should click to exit this mode. |
| View Buttons |
|  | Display grid in the Shape Edit area. |
|  | Display relationship between elements. |
|  |  | Parallel |
|  |  | On the same line |
|  |  | Vertical |
|  |  | Horizontal |
|  |  | Right angle |
|  |  | Same size |
|  | Display elements |
|  | Display points |
|  | Display align dimension |
|  | Maximize all the basic shape to fit the Shape Edit area |

| See: | Template Menu |
| --- | --- |
|  | Template Icon |
|  | Template Parameter |
|  | Shape Edit area |
|  | Generate data |
|  | Edit of Path |
|  | Edit of Elements |
|  | Edit Additional Elements Information |

#### 11.3.1.3 Template Icon

The left part of the Template pane is Shape Display area. You can right-click the icons here to add or delete pattern.

|  | The first icon is the basic shape of the template. Right-click it and select Add to add a new template-processing pattern. |
| --- | --- |
|  | The following icons represent different processing patterns. Right-click any one and select Add to add a new processing method or select Delete to delete the processing method. |

| See: | Template Menu |
| --- | --- |
|  | Template Toolbar |
|  | Template Parameter |
|  | Shape Edit area |
|  | Generate data |
|  | Edit of Path |
|  | Edit of Elements |
|  | Edit Additional Elements Information |

#### 11.3.1.4 Template Parameter

|  | The options in this section allow you to specify the template parameter: Rotation, Flip, Dimension Line, Element Number and Path Number. |
| --- | --- |

| Option | Description |
| --- | --- |
| Rotation | Place a check mark in the Rotation check box if you want the template to rotate to match the parts when processing. |
| Flip | Place a check mark in the Flip check box if you want the template to flip to match the parts when processing. |
| Type1 | The options in this section allow you to specify the template type that you want to create. |
| Type 2 | The options in this section allow you to specify whether the template consists of a single path or multiple paths. But now the system can only support single path. |
| Name | The name of the template. |
| Comment | The comment of the template. |
| Generate Data | After finish drawing or editing in the Shape Edit area, click this button to generate element and path data. |
| Detail | Place a check mark in the Detail check box to display Edit of Path pane, Edit of Element pane and Edit Additional Element Information pane. |
| Add | Click Add button to enter another Template pane to edit template-processing method. |
| Apply | Click Apply button to apply the shape in Shape Edit area as a template. |
| Reset | Click Reset button to redraw basic shape in the Shape Edit area. |

| See: | Template Menu |
| --- | --- |
|  | Template Toolbar |
|  | Template Icon |
|  | Shape Edit area |
|  | Generate data |
|  | Edit of Path |
|  | Edit of Elements |
|  | Edit Additional Elements Information |

#### 11.3.1.5 Shape Edit area

You can draw or edit the shape of a template in Shape Edit area by using the icons on the toolbar. Right click to open a short-cut menu and you can also draw or edit by selecting options on the short-cut menu.

| See: | Template Menu |
| --- | --- |
|  | Template Toolbar |
|  | Template Icon |
|  | Template Parameter |
|  | Generate data |
|  | Edit of Path |
|  | Edit of Elements |
|  | Edit Additional Elements Information |

#### 11.3.1.6 Generate data

After finishing drawing or editing in the Shape Edit area, click the Generate Data button to generate data in the Edit of Path, Edit of Element and Edit Additional Element Information tables.

| See: | Template Menu |
| --- | --- |
|  | Template Toolbar |
|  | Template Icon |
|  | Template Parameter |
|  | Shape Edit area |
|  | Edit of Path |
|  | Edit of Elements |
|  | Edit Additional Elements Information |

#### 11.3.1.7 Edit of Path

| Option | Description |
| --- | --- |
| Standard Shape | This option is currently unavailable. |
| Basic Coordinates X | This option is currently unavailable. |
| Basic Coordinates Y | This option is currently unavailable. |
| Start Point Min/Max Increased Angle | To define the range of the increased angle of start point (the angle between the first line and the horizontal line). |
| Start Point Increased Angle Mark | Specific angle mark for the specific angle range. Click the cell and the Increased Angle Mark window will appear. If the angle is 90, the corresponding mark should be 4. |
| End Point Min/Max Increased Angle | To define the range of the increased angle of end point (the angle between the last line and the horizontal line). |
| End Point Increased Angle Mark | Specify the angle mark for the specific angle range. Click the cell and following window appears. If the angle is 90, the corresponding mark should be 4. |
| Line Element Number | The number of line element. |
| Arc Element Number | The number of arc element. |
| Consult Path Number | This option is currently unavailable. |
| Standard Shape X Shape | This option is currently unavailable. |
| Standard Shape Y Size | This option is currently unavailable. |

| See: | Template Menu |
| --- | --- |
|  | Template Toolbar |
|  | Template Icon |
|  | Template Parameter |
|  | Shape Edit area |
|  | Generate data |
|  | Edit of Elements |
|  | Edit Additional Elements Information |

#### 11.3.1.8 Edit of Elements

| Option | Description |
| --- | --- |
| #ID | The element number. |
| Element Type | The type of element. |
| Increased angle min | The minimum increased angle. |
| Increased angle max | The maximum increased angle. |
| Increased angle mark | The mark of increased angle. |
| Parallel number | The number of parallel element. |
| Same line | The number of the same line. |
| Same length | The number of the same length element. |

| See: | Template Menu |
| --- | --- |
|  | Template Toolbar |
|  | Template Icon |
|  | Template Parameter |
|  | Shape Edit area |
|  | Generate data |
|  | Edit of Path |
|  | Edit Additional Elements Information |

#### 11.3.1.9 Edit Additional Elements Information

The information that appears in the Edit Additional Element Information table is coincident with the selected element. The information that displays for a line will be different from that of an arc.

In the following example, a Line has been selected in the drawing area. The Edit of Elements table displays the basic information for the line. If you select any element ID# in the Edit of Elements table, the corresponding information will appear in the Edit Additional Elements Information table.

| Option | Description |
| --- | --- |
| #ID | The element identification number. |
| Min Line Length | The minimum line length. The default value is 0. You can double-click to edit it. |
| Max Line Length | The maximum line length. The default value is 9999. You can double-click to edit it. |
| If you select an Arc in the drawing area, the corresponding information for the selected arc is listed in the Edit Additional Element Information window. |

| Option | Description |
| --- | --- |
| #ID | The element identification number. |
| Radius Min/Max | To define the range of the arc radius. |
| Arc Start Angle Min/Max | To define the range of the arc start angle. |
| Arc Start Angle Mark | The mark of arc start angle. If you click the cell, the Increased Angle Mark window will appear. |
| Arc Center Angle Min/Max | To define the range of the arc center angle. |
| Arc Center Angle Mark | The mark of arc center angle. If you click the cell, the Increased Angle Mark window will appear. |
| Rotation Direction | To define rotation direction of the arc is clockwise or counter-clockwise. |

| See: | Template Menu |
| --- | --- |
|  | Template Toolbar |
|  | Template Icon |
|  | Template Parameter |
|  | Shape Edit area |
|  | Generate data |
|  | Edit of Path |
|  | Edit of Elements |

### 11.3.2 Pattern Pane

After generating data, you can click Add button to open Pattern Edit pane and begin edit pattern. You can also right-click the basic shape icon or pattern icon in Shape Display area and select Add to open Pattern Edit pane and begin edit pattern.

In Pattern Edit pane, you can assign tools directly to the selected element or you can assign tools by using assistant lines. See Draw Assistant Line

Example:

| 1. | Take the following pattern as an example. This is an irregular pattern and we happen to have a special tool of the same shape as the pattern. |
| --- | --- |
| 2. | Under this circumstance, we click Single Hit button directly in the right Basic Shape Pattern pane. The special tools exited will be listed automatically below the Basic Shape Pattern pane. Select the tool that matches the pattern. |
| 3. | In the Pattern Edit area, the tool appears automatically and will move as the mouse moves. |
| 4. | Click to Select a point as base point and click Single Hit button again. Then the selected special tool is assigned to single hit the pattern. |
| 5. | You can also assign to process it line by line. Select a line element in the pattern. |
| 6. | Select RO as tool type and then select Shear Proof in the Basic Shape Pattern pane. |
| 7. | The system will assign a RO tool to shear proof the line element. |
| 8. | Use the same will to assign to process other lines. The system will assign a RO tool to shear proof the pattern line by line. |
| 9. | Click Apply button to save it. |

Draw Assistant Line

| 1. | Take the following template as an example. In the pattern edit mode, right-click and select Draw Assistant Line. |
| --- | --- |
| 2. | The mouse becomes a cross-shape pointer and a message appears prompting you to design the first point of the assistant line. |
| 3. | Another message appears prompting you to designate the next point of the assistant line and click to designate. You can also input the length and angle of the assistant line directly in the text boxes and click to confirm. |
| 4. | In this example, we use an assistant line to divide the shape into two rectangles. Right-click and select Decompose Pattern to confirm your operation. |
| 5. | Sleeting Select Edge option. |
|  | Note: Select Edge is selected by default. |
| 6. | Select two lines to define the range. |
| 6. | Specify tool shape and select a basic shape pattern in the right pane. If you select SQ as tool shape and Rectangle as basic shape pattern, the system will use SQ tool to process this rectangle area. |
| 7. | Use the same way to assign tools to the other part of. |
| 8. | You can use different color to display the assignment. Choose Select Base Shape. |
| 9. | Select one base shape in the Pattern Edit area and right-click. Select Set Color. |
|  | Note: You can select Delete to delete this assignment here. |
| 10 | The Color dialog appears. Select one color and click OK. |
| 11. | The result is the following. |
| 12. | The system will generate data automatically in the Base Shape table |

| See: | Tool Assignment Pane |
| --- | --- |
|  | Basic Shape |
|  | Shape Data |

| See: | Template Pane |
| --- | --- |

#### 11.3.2.1 Tool Assignment Pane

| Option | Description |
| --- | --- |
|  | You can specify tool you wanted in this pane. |
|  | You can select basic shape pattern in this pane. Rectangle, Triangle, Arc Internal and Arc External belong to sketch process and you can choose to punch out in Shape Data. See Shape Data |
| Name | The name of the template. |
| End Value | Specify the end value. There are four options here: None, M00, Work Chute and Joint. Only None and M00 are available. |
| Comment | Type any comment in the textbox. |
| Element Separation | This option is currently unavailable. |
| Assign Changeable | This option is currently unavailable. |
| Add | If you select an exited pattern in the left pattern list area, click this button to add a new pattern. |
| Apply | Click this button to apply pattern. |
| Reset | Click this to exit this pane and return to the previous one. |

| See | Basic Shape |
| --- | --- |
|  | Shape Data |

#### 11.3.2.2 Basic Shape

The information in the table is generated automatically after you created the process template.

| Option | Description |
| --- | --- |
| Type | The type of the pattern. |
| Sequence ID | The ID of the sequence. |
| Continuous Sequence | The ID of the continuous sequence. |
| Interference flag | Place a check mark in the check box and the system will check interference automatically. This option is currently unavailable. |
| Sketch process | To use the sketch material to process. |
| Start Point | The start point of the sketch process. This option is currently unavailable. |
| Direction | The direction of the sketch process. This option is currently unavailable. |
| Normal Process | Use the normal material to process. |
| Start Point | The start point of the normal process. This option is currently unavailable. |
| Direction | The direction of the normal process. This option is currently unavailable. |
| Extrusion |  |
| Left | Place a check mark here and the system will execute extrusion on the left of the selected basic shape. |
| Right | Place a check mark here and the system will execute extrusion on the right of the selected basic shape. |

| See: | Tool Assignment Pane |
| --- | --- |
|  | Shape Data |

#### 11.3.2.3 Shape Data

| The Shape Data table will list the information of the selected item type in the Base Shape table. The options in Shape Data table vary with the type of item selected in the Base Shape table. |
| --- |
| If you select Rectangle: |
| Option | Description |
| Sequence ID | The ID of the sequence. |
| Tool Shape | Display the tool shape. |
| Punch Out flag | Place a check mark here and the system will execute punch out to process this basic shape. |
| 1-4 | X and Y point of the four points of the rectangle. The system will use the four points indicate L1-L4 Coordinate. |
| L1-L3 Tolerance | The range of the L1-L4 extrusion. |
| L1-L4 Coordinates | The Coordinate of the L1-L4. |

| If you select Triangle: |
| --- |
| Option | Description |
| Sequence ID | The ID of the sequence. |
| Tool Shape | Display the tool shape. |
| Punch Out flag | Place a check mark here and the system will execute punch out to process this basic shape. |
| P1-P3 Coordinates | The Coordinate of P1-P3. |
| L1-L3 Tolerance | The tolerance value of L1-L3. |
| L1-L3 Extended | The range of the L1-L3 extrusion |
| L1-L4 Coordinates | The Coordinate of the L1-L4. |

| If you select Single Hit: |
| --- |
| Option | Description |
| Sequence ID | The ID of the sequence. |
| Tool Shape | Display the tool shape. |
| ManagementName | The name of the tool |
| Method to Decide Coordinates | This option is currently unavailable. |
| BaseX | The X Coordinate of the base point. |
| BaseY | The Y Coordinate of the base point. |
| Offset X | The X offset value of the center point of the pattern. |
| Offset Y | The Y offset value of the center point of the pattern. |
| X Range | The range of tool X size. |
| Y Range | The range of tool Y size. |
| R Range | The range of tool R size. |
| Angle | The angle of the tool. |
| Select M Code | This option is currently unavailable. |

| If you select Line: |
| --- |
| Option | Description |
| Sequence ID | The ID of the sequence. |
| Pattern | Place a check mark here and the system will execute punch out to process this basic shape. |
| Tool Shape | X and Y point for arc center. |
| ManagementName | The name of the tool |
| Start Point | X and Y point for start point. |
| End Point | X and Y point for end point. |
| Start Point Method Decide Coordinate | This option is currently unavailable. |
| End Point Method Decide Coordinate | This option is currently unavailable. |
| Tool X Range | The range of tool X size. |
| Tool Y Range | The range of tool Y size. |
| Tool R Range | The range of tool R size. |
| Tool Angle | The angle of the tool. |

| If you select Shear Proof: |
| --- |
| Option | Description |
| Sequence ID | The ID of the sequence. |
| Tool Shape | Place a check mark here and the system will execute punch out to process this basic shape. |
| Slitting On/Off | This option is currently unavailable. |
| P1-P2 Coordinates | The Coordinate of P1-P3. |
| Start Point Extrusion | The range of the start point extrusion. |
| End Point Extrusion | The range of the end point extrusion. |
| Wire Joint Number | The number of wire joint |
| Wire Joint Assignment Type | Assignment type of wire joint |
| Process Coordinate | Processing coordinate |
| Tool Size X | The range of tool X size. |
| Tool Size Y | The range of tool Y size. |

| If you select Arc Shear Proof: |
| --- |
| Option | Description |
| Sequence ID | The ID of the sequence. |
| ToolShape | X and Y point for arc center. |
| Arc Base | The X and Y point of arc base point |
| Start Point | X and Y point of start point. |
| End point | X and Y point of endpoint. |
| Rotation Direction | The direction of the rotation. |
| Internal/External Process | Type internal or external process. |
| Start Point Extrusion | The range of the start point extrusion. |
| End Point Extrusion | The range of the end point extrusion. |
| Wire Joint Number | The number of wire joint |
| Wire Joint Layout Position | Layout position of wire joint |

| If you select Arc Internal: |
| --- |
| Option | Description |
| Sequence ID | The ID of the sequence. |
| Punch Out (Slug- Out Area) | Place a check mark here and the system will execute punch out to process this basic shape. |
| Arc Center | X and Y point for arc center. |
| Start Point | X and Y point for start point. |
| End Point | X and Y point for end point. |
| Rotation Direction | The direction of the rotation. |
| Start Point Extrusion | The range of the start point extrusion. |
| End Point Extrusion | The range of the end point extrusion. |
| If you select Arc External, the options is the same with Arc Internal |

| See: | Tool Assignment Pane |
| --- | --- |
|  | Basic Shape |

# Chapter 12: Sequence

The Punch Sequence window allows you to set the processing sequence, the clamp setting, the clamp avoidance, the repositioning, and the part-grid sequence.

| To open the Punch Sequence window: |
| --- |
| 1. | Click the Punch Sequence Preference button in the Dr. ABE main window to open the Preference window. |
| 2. | Select an EM machine in the Tree View pane. The preference icons of the EM machine appear in the Preference File pane. |
| 3. | Double-click the Sequence icon in the Preference File pane. The Punch Sequence window displays. |

| See: | Sequence |
| --- | --- |
|  | Clamp Setting |
|  | Clamp Avoidance |
|  | Repositioning |
|  | Part-Grid |

## 12.1 Sequence

The options in the Punch Sequence panel allow you to specify the parameters for the punch sequence.

| See: | Part as Process Unit |
| --- | --- |
|  | For Reducing Bits of Vinyl |
|  | AI Tool Angle Sort |
|  | Tool Sorting |
|  | Process Unit Sorting |

| See: | Clamp Setting |
| --- | --- |
|  | Clamp Avoidance |
|  | Repositioning |
|  | Part-Grid |

### 12.1.1 Part as Process Unit

|  | The options in the Part as Process Unit panel allow you to specify either the entire sheet or the individual parts as the sequencing unit. |
| --- | --- |

| Option | Description |
| --- | --- |
| Sheet | This option will instruct the system to process the whole sheet as a single unit. If you select this option, all the parts will be processed on a pattern-by-pattern basis. |
| Each Part | This option will instruct the system to process each individual part as a unit. If you select this option, the system will process the parts on the sheet sequentially. |
| Machine Stop for Prototype | If you place a check mark in this check box, the system will generate an M00 program stop after the machine finishes processing prototype part on a pattern-by-pattern basis. |
| Process Prototype Part by Part | If you place a check mark in this check box, the system will process the prototype part by part. |
| Output only one M00 | If you place a check mark in this check box, the system will generate an M00 program stop after the machine finishes processing all prototypes. |
| Process Order | The options in the Process Order pane allow you to define the sequence priority to process patterns. |

| See: | Sheet and Each Part |
| --- | --- |
|  | Machine Stop for Prototype |
|  | Process Order |

| See: | For Reducing Bits of Vinyl |
| --- | --- |
|  | AI Tool Angle Sort |
|  | Tool Sorting |
|  | Process Unit Sorting |

#### 12.1.1.1 Sheet and Each Part

| The following demonstrates the difference between the Sheet and Each Part options. |
| --- |
| 1. | Select Sheet. |
| 2. | The sequence is as follows: |
| 3. | Select Each Part. |
| 4. | The sequence is as follows: |

| See: | Machine Stop for Prototype |
| --- | --- |
|  | Process Order |

#### 12.1.1.2 Machine Stop for Prototype

| To use this option: |
| --- |
| 1. | Set the prototype quantity in the Part Properties window. |
| 2. | Place a check mark in the Machine Stop for Prototype check box. |
| 3. | The system will process the prototype part on a pattern-by-pattern basis and generate an M00 program stop each time the machine finishes processing a prototype part. |
| 4. | Place a check mark in the Process Prototype Part by Part check box. |
| 5. | The system will process the prototype part by part and generate an M00 program stop each time machine finishes processing a prototype part. |
| 6. | Place a check mark in the Output only one M00 check box. |
| 7 | The system will process the prototype part by part and generate only one M00 program stop after machine finishes processing all prototype parts. |
| 8. | Remove a check mark in the Process Prototype Part by Part check box. |
| 9. | The system will process the prototype part on a pattern-by-pattern and generate only one M00 program stop after machine finishes processing all prototype part. |
|  | Note: |
|  | The system will take the shortest tool path into consideration during processing. |

| See: | Sheet and Each Part |
| --- | --- |
|  | Process Order |

#### 12.1.1.3 Process Order

The options in the Process Order panel allow you to specify the process order.

Example:

| 1. | Select Forming Down |
| --- | --- |
| 2. | Click the upward arrow to change the process order of Forming Down. |

| See: | Sheet and Each Part |
| --- | --- |
|  | Machine Stop for Prototype |

### 12.1.2 For Reducing Bits of Vinyl

|  | The options in the For Reducing Bits of Vinyl pane allow you to make settings for reducing bits of vinyl. |
| --- | --- |
|  | You can type a value in the following text box to specify the amount of movement. The escape amount is the multiple of tool length. If you type 2 in the textbox, escape amount is 2 times of tool size. |
|  | You can place a check mark in the following check boxes to define the direction. |

| See: | Part as Process Unit |
| --- | --- |
|  | AI Tool Angle Sort |
|  | Tool Sorting |
|  | Process Unit Sorting |

### 12.1.3 AI Tool Angle Sort

In the AI Tool Angle Sort panel, you can specify the way to use the tool in the AI stations to process the patterns.

| Option | Description |
| --- | --- |
| All Range | Place a check mark in the All Range check box, and the system will use the AI tools to process the patterns by angle. |
|  | Example; |
|  | We assign an AI tool to process the following patterns. |
|  | If All Range is selected, the system will use the AI tools to process the patterns by angle. |
|  | If All Range is not selected, the system will use the AI tools to process the patterns based on the shortest path |
| Range A - Range F | Select the options, and the system will use the AI tools of the corresponding ranges to process the patterns by angle. |

Note:

To enable the AI Tool Angle Sort function, you must remove the check mark from the C Axis Sort Off check box. See: C Axis Sort Off

| See: | Part as Process Unit |
| --- | --- |
|  | For Reducing Bits of Vinyl |
|  | Tool Sorting |
|  | Process Unit Sorting |

### 12.1.4 Tool Sorting

When the tools in the same sequence group have the same sequence number, select Angle of Turret, the system will use the tools by the order of the Turret Angle. The tools placed in the stations of smaller turret angles will be used first, which reduces the turret rotation time for the process.

Example

| 1. | We will process the following part. |
| --- | --- |
| 2. | We will use the following RO tools to single hit the inner loops. These tools are in the same sequence group and have the same sequence number. |
| 3. | These tools are placed in the following turret stations, T104, T303, T107, T206 and T112. Among all these stations, T303 has the smallest turret angle, while T112 has the largest turret angle. |
| 4. | If Angle of Turret is not selected, the system will automatically sequence the inner loops as follows. |
| 5. | If Angle of Turret is enabled, the system will process the inner loops in the following sequence. As the following NC code indicates, tools in the turret of smaller angles are used earlier. |

If the tools are placed in the stations of the same turret angle, if you only select Angle of Turret and don’t select Mix, the system will assign those tools in the order of the inner track, center track and outer track. If you select Mix, the tools of the same turret angle will have the same priority. In this case, the system will process the parts based on the shortest process time.

| See: | Part as Process Unit |
| --- | --- |
|  | For Reducing Bits of Vinyl |
|  | AI Tool Angle Sort |
|  | Process Unit Sorting |

### 12.1.5 Process Unit Sorting

|  | The options in the Process Unit Sorting pane allow you to specify the process unit sorting. |
| --- | --- |

| Option | Description |
| --- | --- |
| Tool Order Logic | If you select this option, the system will sort the process unit by tool order logic. |
| Last Tool Logic | If you select this option, the system will sort the process unit by last tool logic. |

| See: | Part as Process Unit |
| --- | --- |
|  | For Reducing Bits of Vinyl |
|  | AI Tool Angle Sort |
|  | Tool Sorting |

## 12.2 Clamp Setting

Clamps are used to fasten the sheet on the worktable. The options in this panel allow you to specify the clamp conditions during the sequence.

| See: | Clamp Removal (Clamp # 3) |
| --- | --- |
|  | Clamp Position Change |

| See: | Sequence |
| --- | --- |
|  | Clamp Avoidance |
|  | Repositioning |
|  | Part-Grid |

### 12.2.1 Clamp Removal (Clamp # 3)

|  | For a machine with three clamps, this section is used to determine whether the third clamp can hold nothing during the reposition. |
| --- | --- |

Example

| 1. | If you place a check mark in the check box to allow the third clamp to hold nothing during the reposition. The system will process the parts as follows. All the parts in the sheet will be processed. |
| --- | --- |
|  | Before the reposition After the reposition |
| 2. | If you remove the check mark from the check box, the system won’t allow the third clamp to hold nothing after the reposition. As a result, some patterns might not be processed. |
|  | Before the reposition After the reposition |

| See: | Clamp Position Change |
| --- | --- |

### 12.2.2 Clamp Position Change

|  | The options in this section allow you to define how to change the clamp position. |
| --- | --- |

| Option | Description |
| --- | --- |
| Initial Position (User-Defined Coordinates) | If this option is selected, the system will apply the initial clamp settings defined in the Clamp information panel of the Machine Set window. And the initial clamp position settings in the Initial Clamp Position panel of the Nesting window will be used. When the reposition is performed, the system will only generate G25 and G27 to instruct the machine to perform reposition. |
| Auto Calculation (Fixed During the Process) | This option is usually for customers having Multi Tapping device. When the tapping tool is used, system will first perform a clamp position change (G05) before punching. Then G25 or G27 will be generated for the repositioning. |
| Auto Calculation (Movements Exist in G05) | Select this option, the system will instruct the machine to change the clamp position or perform reposition to process the parts, and the system will try to generate G05 to instruct the machine to process the parts first. |

Example

| 1. | If Auto Calculation (Movements Exist in G05) is not selected, the system will instruct the machine to perform reposition to process the parts in the dead zone area. |
| --- | --- |
|  | Before the reposition | After the reposition |
| 2. | If Auto Calculation (Movements Exist in G05) is selected, the system will generate G05 command, and the machine will change the clamp position to process the parts in the dead zone area. |
|  | Before the clamp position is changed | After the clamp position is changed |

| See: | Clamp Removal (Clamp # 3) |
| --- | --- |

## 12.3 Clamp Avoidance

The options in the Punch Clamp Setting panel will instruct the system to avoid the dead zones while processing. In the Clamp Position Change panel, you can specify the distance the sheet will move to prevent the clamp from passing through the turret.

| See: | Avoid DZ |
| --- | --- |
|  | Clamp Position Change |

| See: | Sequence |
| --- | --- |
|  | Clamp Setting |
|  | Repositioning |
|  | Part-Grid |

### 12.3.1 Avoid DZ

|  | Place a check mark in the Avoid DZ check box, and the system will instruct the machine to perform reposition to avoid the dead zones. |
| --- | --- |

| Option | Description |
| --- | --- |
| Avoid DZ | Select this option, and the system will generate data to instruct the machine to avoid the dead zones. |
| Track Check | Select this option, and the system will add the track offset value (40mm) to Dead Zone value of each range, and perform repositions to avoid Dead Zones. 300 Track：0 mm (Tool offset-40＋Track offset 40) 200 Track：40 mm (Tool offset 0＋ Track offset 40) 100 Track：80 mm (Tool offset 40＋ Track offset 40) |

Example

| 1. | Parts are nested as follows, and some parts are nested close to the clamps. |
| --- | --- |
| 2. | If Avoid DZ is not selected, the system processes the parts without reposition, and tools might get damaged during the process. |
| 3. | If Avoid DZ is selected, the system will process those parts that are out of the dead zones first. |
|  | Then the system will perform reposition and continue to process those parts not finished. In this way, the system can prevent the tools getting damaged while processing the parts in the dead zones. |

| See: | Clamp Position Change |
| --- | --- |

### 12.3.2 Clamp Position Change

To prevent the clamp from passing through the turret, specify the movement path based on G70 (No Punch).

Before the clamp passes through the area specified in each track, the system will output G70 to instruct the machine to avoid the specified area.

Example

| 1. | Specify the conditions as follows. |
| --- | --- |
| 2. | Two parts are nested around the clamp as the following illustration indicates. The distance from the center of the hole pattern to the sheet edge is 69. The system will assign a round tool in station T303 (Which is on the outer track) to process this hole. |
| 3. | Since the distance from the center of the hole pattern to the sheet edge is 69, greater than the 60. The machine will move the sheet directly to allow the same tool to process the next hole as the following illustration shows. No collisions will happen between the tool and clamp during the process. |
| 4. | If the same parts are nested around the clamp as follows, but the distance from the center of the hole pattern to the sheet edge is 59, and the system will assign the same tool in station T303 to process these two holes, |
| 5. | Since the distance from the center of the hole pattern to the sheet edge is 59, less than the 60. If the machine moves the sheet directly, collision might occur, and tools and clamps might get damaged. Therefore the system will generate G70 to instruct the machine to move the sheet the distance 160 in the Y-axis during the process. |
|  | In this way, no collisions will happen between the tools and clamps during the process. |

| See: | Avoid DZ |
| --- | --- |

## 12.4 Repositioning

The repositioning is the movement of the clamps to avoid over travel and dead zones. Machines use clamps to shift the sheet to process the parts that are out of a processing range. In the Repositioning panel, you can define the reposition type, processing direction, etc.

| See: | Repositioning Type |
| --- | --- |
|  | Process Majority of Parts |
|  | Process Direction |
|  | Return to First Position |

| See: | Sequence |
| --- | --- |
|  | Clamp Setting |
|  | Clamp Avoidance |
|  | Part-Grid |

### 12.4.1 Repositioning Type

The options in the Repositioning Type section determine whether to process the parts within the same reposition or to divide the parts when repositioning.

| See: | Minimum |
| --- | --- |
|  | No Divide of Parts |

| See: | Process Majority of Parts |
| --- | --- |
|  | Process Direction |
|  | Return to First Position |

#### 12.4.1.1 Minimum

If you select Minimum in the Repositioning Type section, the system will attempt to process the sheet by using the fewest repositions. The machine will process the parts within the process range first, then reposition the sheet, and then process the parts within the second process range. If there are still parts to be processed, the system repositions the sheet again until all the parts are processed.

In the following example, the machine processes all the parts within the dashed rectangle before the reposition.

The machine will then process all the remaining parts after the reposition.

However, for parts whose location is divided by the dashed line, some segments of the parts are processed before the reposition and the remaining after the reposition.

The part within the red rectangle will be used to illustrate the process before and after the reposition.

For the part in the red rectangle, before the reposition, the machine will process the patterns as follows. The green entities are the segments that are processed.

The Machine will process this segment:

It will then process the next segment.

Finally it will process this segment.

After the reposition, the machine will process the segments of the part as follows. The green entities are the segments that are processed after the repositioning.

The machine will first process this segment.

It will then process with the next segment.

Finally it will process this segment.

| See: | No Divide of Parts |
| --- | --- |

#### 12.4.1.2 No Divide of Parts

If you select No Divide of Parts in the Repositioning Type section, none of the parts will be divided to process before and after a repositioning, but more repositions are needed.

For example, you can select Minimum to process the following parts with just one reposition.

The machine processes all the parts within the dashed rectangle before the reposition.

The machine processes the remaining parts after the reposition.

If you select No Divide of Parts, none of the parts will be divided to process before and after a reposition.

The machine will process the parts as indicated by the red rectangle before the reposition.

The machine will continue to process the parts as indicated by the red rectangle after the first reposition.

The machine will finish processing all the remaining parts after the second reposition.

| See: | Minimum |
| --- | --- |

### 12.4.2 Process Majority of Parts

Whether you select Minimum or No Divide of Parts in Repositioning Type section, some patterns may be located in the process range overlap area. The options in the Process Majority of Parts section allow you to specify how to process those patterns in the overlap area.

| Option | Description |
| --- | --- |
| Before | Process the patterns located in the process range overlap area before the reposition is performed. |
| After | Process the patterns located in the process range overlap area after the reposition is performed. |

Example

| 1. | In the following diagram, the white rectangle indicates the process range before the reposition and the green rectangle indicates the range after the reposition. Some patterns are located in the overlap area. |
| --- | --- |
| 2. | If you select Before under Process Majority of Parts, those patterns will be processed before the reposition is performed. |
| 3. | If you select After under Process Majority of Parts, those patterns will be processed after the reposition is performed. |

| See: | Repositioning Type |
| --- | --- |
|  | Process Direction |
|  | Return to First Position |

### 12.4.3 Process Direction

The options in the Process Direction section allow you to specify whether to process from the left to the right or from the right to the left while repositioning.

| Option | Description |
| --- | --- |
| Left to Right | Select this option, and parts will be processed from the left to the right. The parts in the original process range will be processed before the reposition. |
| Right to Left | Select this option, and parts will be processed from the right to the left. The system will generate a G27 reposition command first before processing the parts. |

Example

| If you select Left to Right, |
| --- |
| 1. | The parts in the original process range will be processed first. |
| 2. | After the first reposition, the parts in the process range will be processed. |
| 3. | After the second reposition, all the remaining parts will be processed. |
| If you select Right to Left, |
| 1. | The following picture shows the original process range before reposition. |
| 2. | The system will execute reposition first. After the reposition is performed, the process range will be as follows, and parts in this process range will be processed first. |
|  | After the second reposition, parts in this process range will be processed. |
|  | After the third reposition, the remaining parts will be processed. |

| See: | Repositioning Type |
| --- | --- |
|  | Process Majority of Parts |
|  | Return to First Position |

### 12.4.4 Return to First Position

If you place a check mark in the Return to First Position check box, after processing all the parts, the system will generate a G27 command to instruct the holders to release the sheet and return the clamps to the original position.

| See: | Repositioning Type |
| --- | --- |
|  | Process Majority of Parts |
|  | Process Direction |

## 12.5 Part-Grid

In the Part-Grid panel, you can specify the conditions to process part grid, and decide whether to output the specific M code in the UV macro commands or not.

| See: | Part-Grid Conditions |
| --- | --- |
|  | Output Outside of UV |

| See: | Sequence |
| --- | --- |
|  | Clamp Setting |
|  | Clamp Avoidance |
|  | Repositioning |

### 12.5.1 Part-Grid Conditions

|  | In this section, you can specify whether to output G98 in the NC code, and you can also define the starting position and process direction for processing the part grid. |
| --- | --- |

| Option | Description |
| --- | --- |
| Output Part-Grid | Output G98 in the NC code to indicate the use of part grid macros. |
|  | Note: You must open the Nesting window, click Nesting Logic 2 tab and place a check mark in the Enable Part Grid check box under Grid Pattern to enable the function. |
| Start Position | Specify the starting position to process the part grid. |
|  | Option Description Top left Output Q3 to instruct the machine to process the part grid from the top left. Top Right Output Q4 to instruct the machine to process the part grid from the top right. Bottom Left Output Q1 to instruct the machine to process the part grid from the bottom left. Bottom Right Output Q2 to instruct the machine to process the part grid from the bottom right. |
| Auto | Select Auto option, and the position close to the end point of the previous process will be used as the starting point. |
| Process Direction | Specify the preferred process direction of the part grid. Option Description X-Axis Output G75 to instruct the machine to process the part grid along X-axis. Y-Axis Output G76 to instruct the machine to process the part grid along Y-axis. |
| Auto | Select Auto option, and the process direction defined in the Start Point/Direction section in the Nesting Logic panel will be used as the process direction to process the part grid. See: Start Point/Direction |

Example

| 1. | In the Nesting logic 2 panel of the Nesting window, place a check mark in the Enable Part Grid check box. |
| --- | --- |
| 2. | In the Part-Grid panel of the Sequence window, specify the settings as follows. |
| 3. | The system will generate the following NC code commands, |
|  | And process the part grid as follows. |

| See: | Output Outside of UV |
| --- | --- |

### 12.5.2 Output Outside of UV

|  | You can select to place check marks in check boxes TNO, Axis Speed and the M Code (Air blow, Energy-Save, Press Pattern, P&F, Mild Mode, Work Chute Closed Code). The selected codes will be included in the UV macro commands. Note: The condition to output UV macro commands outside is that the inside of UV macro is created by tool of the same type. |
| --- | --- |

Example

| 1. | Place check marks in Air Blower, Energy-Save, Press Pattern and P&F check boxes. |
| --- | --- |
| 2. | When part grids are processed, the system will output the following code commands. |

| See: | Part-Grid Conditions |
| --- | --- |

# Chapter 13: NC Generate

You can click the NC Generate Preference button  on the main window to open the Preference window.  In the Preference window, select a punch machine (e.g. EM2510) from the left Tree View pane, and then click the NC icon in the top Preference File pane to display the NC Generate window.

In this window, these options allow you to specify conditions for the NC code generation.

As soon as you select an item of the parameter, the note with description on the right will update.

| See: | Material |
| --- | --- |
|  | Loading / Unloading Device |
|  | Loading / Unloading Thickness M-Code |
|  | Loading / Unloading End Position M-Code |
|  | Output work size comment at the end of G92 command line |
|  | Use Line Number |
|  | Use Setup Sheet |
|  | Setup Sheet |
|  | Output G93 |
|  | Percent After G50 |
|  | Clear Macros |

## 13.1 Material

| Place a check mark in the check box and type a value in the right-side cell. The input value indicates the type of the material. (0=SPC, 1=SUS, 2=AL) |
| --- |
|  | For example, G06 line in the NC code indicates the material information. A indicates that the thickness is 1.0. B indicates that the type of the material is AL. |

| See: | Loading / Unloading Device |
| --- | --- |
|  | Loading / Unloading Thickness M-Code |
|  | Loading / Unloading End Position M-Code |
|  | Output work size comment at the end of G92 command line |
|  | Use Line Number |
|  | Use Setup Sheet |
|  | Setup Sheet |
|  | Output G93 |
|  | Percent After G50 |
|  | Clear Macros |

## 13.2 Loading / Unloading Device

|  | This option allows you to output an M code for a Loading/Unloading Device. If the machine is equipped with a loading/unloading device, place a check mark in the LOADING/UNLOADING DEVICE (1=YES 0=NO) check box to output the M code. The system will output an M33 indicated as the NC code to the left. |
| --- | --- |
| Note: Make sure a loading / unloading device is selected from the Tandem Device Type: drop-down list in the Machine Set window. |

| See: | Material |
| --- | --- |
|  | Loading / Unloading Thickness M-Code |
|  | Loading / Unloading End Position M-Code |
|  | Output work size comment at the end of G92 command line |
|  | Use Line Number |
|  | Use Setup Sheet |
|  | Setup Sheet |
|  | Output G93 |
|  | Percent After G50 |
|  | Clear Macros |

## 13.3 Loading / Unloading Thickness M-Code

If you enable this option, the system will generate the Loading/Unloading Thickness M-code based on the pre-defined code settings.

Note:

To output the Loading/Unloading Thickness M-code, first place a check mark in the LOADING/UNLOADING DEVICE (1=YES 0=NO) check box.

Example

| 1. | Specify the NC generate settings as below. |
| --- | --- |
| 2. | Select Cycle Loader (ASR-CR, ASR-M) from the Tandem Device Type: drop-down list. The material thickness is 1 in this case, |
| 3. | The system will output an M24 indicated as the NC code to the left. |

| See: | Material |
| --- | --- |
|  | Loading / Unloading Device |
|  | Loading / Unloading End Position M-Code |
|  | Output work size comment at the end of G92 command line |
|  | Use Line Number |
|  | Use Setup Sheet |
|  | Setup Sheet |
|  | Output G93 |
|  | Percent After G50 |
|  | Clear Macros |

## 13.4 Loading / Unloading End Position M-Code

If you enable this option, the system will generate the Loading / Unloading End Position M-Code based on the pre-defined code settings.

Note:

To output the Loading/Unloading End Position M-Code, first place a check mark in the LOADING/UNLOADING DEVICE (1=YES 0=NO) check box.

Example

| 1. | Specify the NC generate settings as below |
| --- | --- |
| 2. | Select Cycle Loader (ASR-CR, ASR-M) from the Tandem Device Type: drop-down list. The blank sheet size is 2438*1219 in this case, |
| 3. | The system will output an M57 indicated as the NC code to the left. |

| See: | Material |
| --- | --- |
|  | Loading / Unloading Device |
|  | Loading / Unloading Thickness M-Code |
|  | Output work size comment at the end of G92 command line |
|  | Use Line Number |
|  | Use Setup Sheet |
|  | Setup Sheet |
|  | Output G93 |
|  | Percent After G50 |
|  | Clear Macros |

## 13.5 Output work size comment at the end of G92 command line

|  | Place a check mark in the check box to enable the system to display minimum work size comment at the end of G92 command line, as (X54.Y88.) in the left picture. |
| --- | --- |
| See: | Material |
|  | Loading / Unloading Device |
|  | Loading / Unloading Thickness M-Code |
|  | Loading / Unloading End Position M-Code |
|  | Use Line Number |
|  | Use Setup Sheet |
|  | Setup Sheet |
|  | Output G93 |
|  | Percent After G50 |
|  | Clear Macros |

## 13.6 Use Line Number

|  | Place a check mark in the check box to enable the system to output the line numbers at the beginning of each command line. Line number starts with N, and follows with a sequential number as indicated in the left picture. |
| --- | --- |

| See: | Material |
| --- | --- |
|  | Loading / Unloading Device |
|  | Loading / Unloading Thickness M-Code |
|  | Loading / Unloading End Position M-Code |
|  | Output work size comment at the end of G92 command line |
|  | Use Setup Sheet |
|  | Setup Sheet |
|  | Output G93 |
|  | Percent After G50 |
|  | Clear Macros |

## 13.7 Use Setup Sheet

|  | Place a check mark in the check box to enable the system to output the setup sheet information in the NC code. You can also decide where to display the setup sheet information: on top of the NC code, or at the bottom of it. See: Setup Sheet |
| --- | --- |

| See: | Material |
| --- | --- |
|  | Loading / Unloading Device |
|  | Loading / Unloading Thickness M-Code |
|  | Loading / Unloading End Position M-Code |
|  | Output work size comment at the end of G92 command line |
|  | Use Line Number |
|  | Setup Sheet |
|  | Output G93 |
|  | Percent After G50 |
|  | Clear Macros |

## 13.8 Setup Sheet

This option works with Use Setup Sheet option together to define the output position of the setup sheet information.

|  | Place a check mark in the check box to display the Sheet Setup Information on top of the NC code. |
| --- | --- |
|  | Otherwise the information will be at the bottom if you remove the check mark. |

| See: | Material |
| --- | --- |
|  | Loading / Unloading Device |
|  | Loading / Unloading Thickness M-Code |
|  | Loading / Unloading End Position M-Code |
|  | Output work size comment at the end of G92 command line |
|  | Use Line Number |
|  | Use Setup Sheet |
|  | Output G93 |
|  | Percent After G50 |
|  | Clear Macros |

## 13.9 Output G93

|  | Place a check mark in the check box to enable the system to output G93 line indicating the layout preference point of local coordinate system. |
| --- | --- |

| See: | Material |
| --- | --- |
|  | Loading / Unloading Device |
|  | Loading / Unloading Thickness M-Code |
|  | Loading / Unloading End Position M-Code |
|  | Output work size comment at the end of G92 command line |
|  | Use Line Number |
|  | Use Setup Sheet |
|  | Setup Sheet |
|  | Percent After G50 |
|  | Clear Macros |

## 13.10 Percent After G50

|  | Place a check mark in the check box to enable the system to generate a percent symbol (%) as the end-of-record code. During the process of the data transmission, a percent symbol indicates the end of the transmission. |
| --- | --- |

| See: | Material |
| --- | --- |
|  | Loading / Unloading Device |
|  | Loading / Unloading Thickness M-Code |
|  | Loading / Unloading End Position M-Code |
|  | Output work size comment at the end of G92 command line |
|  | Use Line Number |
|  | Use Setup Sheet |
|  | Setup Sheet |
|  | Output G93 |
|  | Clear Macros |

## 13.11 Clear Macros

|  | When you place a check mark in the check box, only U1/V1 statements will be generated for the part grid macros as is shown in the left picture. |
| --- | --- |
|  | If you clear the check mark, successive U/V statements (U1/V1, U2/V2, U3/V3…) will be generated for the part grid macros as is shown in the left picture. |

| See: | Material |
| --- | --- |
|  | Loading / Unloading Device |
|  | Loading / Unloading Thickness M-Code |
|  | Loading / Unloading End Position M-Code |
|  | Output work size comment at the end of G92 command line |
|  | Use Line Number |
|  | Use Setup Sheet |
|  | Setup Sheet |
|  | Output G93 |
|  | Percent After G50 |

# Chapter 14: Process After

In the Process After window you can specify the methods to process the parts after the cutting process is finished.

You may want to separate the parts from the sheet, process the part corners, keep joints or use work chute to retrieve parts or scraps, etc.

To display the Process After window:

| 1. | In the Preference window, select a punch machine (e.g. EM2510) and double-click the Process After icon to display the Process After window. |
| --- | --- |

| See: | Process After Cutting Table |
| --- | --- |
|  | Joint |

## 14.1 Process After Cutting Table

The Process After Cutting table allows you to specify the next process that will occur after the system completes a cutting process.

You may want to drop parts into the work chute, generate a machine stop, or unload the parts.

Process After Cutting Table Columns

| Items | Description |
| --- | --- |
| Object | Specify the object that the settings will be applied to. There’s only the Outer option available in punch machines. An outer loop is the perimeter of a part as the following red pattern indicates. |
| X/Y | The dimensions of the object. There are seven options: X, Y, R, CPX, Area, Length and Width. See: X/Y/R/CPX/Area/Length/With Explanation |
| EQ | Specify the relationship between the option in X/Y column and the values in Value1/2. There are five options: <= (less than or equal to), >= (greater than or equal to), = (equal to), < (less than) and > (greater than). |
| Value 1/2 | Specify the reference dimension value. |
| Process | Specify a process method for the patterns that match the settings defined in the Process after Cutting section. |
| Joint | Keep joints after processing. |
| Chute Tool | Select Chute Tool as the end value. Some special tools can work as the chute tools to perform the final hit. The options in the Detail Setting window allow you to specify the settings for the special tool you have assigned to separate the part from the sheet. |
| Machine Stop | M00 is generated after processing. |
| None | No specific end value. |
| Joint Name | The name of the joint condition |
| Z Value | This option is useless for punch machines. |

| See: | X/Y/R/CPX/Area/Length/Width Explanation |
| --- | --- |

| See: | Joint |
| --- | --- |

### 14.1.1 X/Y/R/CPX/Area/Length/Width Explanation

| X is the dimension along the X-axis. |
| --- |
| Y is the dimension along the Y-axis. |
| R is the radius of the outer part perimeter. |
| CPX is a quotient of the total perimeter length divided by the overall rectangular perimeter. The following example illustrates the CPX calculation formula: |
| Total Perimeter = 560 | Total Rectangular = 400 |
| CPX=Total Perimeter/Total Rectangular = 560/400 = 1.4 |
| Area is the area within the out part perimeter. |
| Length is the long side of the part. |
| Width is the wide side of the part. |

## 14.2 Joint

In the Process After window, you can specify the conditions to control joint assignment.

In this section, you can select the Fixed Position option to fix the joint position, or select Auto Position to let the system automatically assign joints based on the setting you have defined.

What’s more, you can save your joint settings for the purpose of future use.

| See: | Fixed Position |
| --- | --- |
|  | Auto Position |
|  | Basic Joint Setting |
|  | Joint Type Table |
|  | Detailed Joint Setting |
|  | Joint Setting Condition |

| See: | Process After Cutting Table |
| --- | --- |

### 14.2.1 Fixed Position

To fix the joint position:

| 1. | Select the Fixed Position option, and the Joint section will change as follows. |
| --- | --- |
| 2. | Move the pointer into the Search Position from work area. |
| 3. | Click along the pattern perimeter to decide the joint position. After each mouse click, a red point displays which represents the joint position. Click the red point again to remove the joint. |

Note:

If we specify the joint position as the following Picture A, when the system assigns joints to the pattern like Picture B, it will search for the joint position in the top middle, and then assign the proper joints based on the joint type priority. In this case, since micro joint has the highest priority, micro joints will be assigned to the pattern as Picture C.

If you select the Fixed Position option, you cannot define the joint quantity.

But the quantity shown in the Min Joint QTY: textbox will change accordingly each time you change the joints in the Search Position from area.

| See: | Auto Position |
| --- | --- |
|  | Basic Joint Setting |
|  | Joint Type Table |
|  | Detailed Joint Setting |
|  | Joint Setting Condition |

### 14.2.2 Auto Position

In the joint section, select the Auto Position option to select a position from which the system will begin to assign the joint.

To specify the starting position to start joint assignment:

| 1. | Select the Auto Position option, and the Joint section will change as follows. |
| --- | --- |
| 2. | Move the pointer into the Search Position from work area. |
| 3. | Click one corner to specify the position from which the system will start to assign joints. A red point will display to indicate the starting position. |

| See: | Fixed Position |
| --- | --- |
|  | Basic Joint Setting |
|  | Joint Type Table |
|  | Detailed Joint Setting |
|  | Joint Setting Condition |

### 14.2.3 Basic Joint Setting

If you select the Auto Position option, you can specify the basic setting to assign joints, such as the minimum joint quantity, the minimum distance between joints, and the maximum distance between the corner joints.

| See: | Min Distance between Corner |
| --- | --- |
|  | Min Distance between Wire |
|  | Min Joint Qty |
|  | Max Distance between Corner Joint |

| See: | Fixed Position |
| --- | --- |
|  | Auto Position |
|  | Joint Type Table |
|  | Detailed Joint Setting |
|  | Joint Setting Condition |

#### 14.2.3.1 Min Distance between Corner

Specify the minimum distance between the corner joints.

If the distance between two corner joints is less than the specified value, the system will automatically remove one joint.

Example

| 1. | We will assign joints to a 100*50 REC part. |
| --- | --- |
| 2. | Select Joint as the process method. |
| 3. | Specify the basic joint settings as follow. |
| 4. | 8 joints will be assigned to the pattern as follow. |
| 5. | If you type 60 in the Min Distance between Corner: text box, only 6 joints will be assigned to the pattern. 2 corner joints are removed in order to meet the condition you have specified. |

| See: | Min Distance between Wire |
| --- | --- |
|  | Min Joint Qty |
|  | Max Distance between Corner Joint |

#### 14.2.3.2 Min Distance between Wire

Specify the minimum distance between the wire joints.

If the distance between two wire joints is less than the value specified, the system will automatically remove one joint.

For example, if you specify the Min Distance as 10, but the Pitch is only 8, then one joint will be removed.

See the illustrations as below.

Min Distance = 10, but Pitch = 8

One joint is removed.

Example

| 1. | We will assign joints to a 100*50 part. |
| --- | --- |
| 2. | Select Joint as the process method. |
| 3. | Specify the basic joint settings as follow. |
| 4. | 10 joints will be assigned to the pattern as follow. |
| 5. | Type 40 in the Min Distance between Wire: text box, only 8 joints will be assigned to the pattern. 2 wire joints are removed in order to meet the condition you have specified. |

| See: | Min Distance between Corner |
| --- | --- |
|  | Min Joint Qty |
|  | Max Distance between Corner Joint |

#### 14.2.3.3 Min Joint Qty

Specify the minimum joint quantity.

| See: | Min Distance between Corner |
| --- | --- |
|  | Min Distance between Wire |
|  | Max Distance between Corner Joint |

#### 14.2.3.4 Max Distance between Corner Joint

Specify the maximum distance between corner joints.

If the distance between two corner joints is greater than the value set in the Max Distance for Corner Joint text box, one more corner joint will be added among them.

| See: | Min Distance between Corner |
| --- | --- |
|  | Min Distance between Wire |
|  | Min Joint Qty |

### 14.2.4 Joint Type Table

|  | Specify the priority of joint types. The joints with higher priority will be assigned first. You can select one joint type and click or to change its priority. The joint type at the top of the table has the highest priority. |
| --- | --- |

| See: | Fixed Position |
| --- | --- |
|  | Auto Position |
|  | Basic Joint Setting |
|  | Detailed Joint Setting |
|  | Joint Setting Condition |

### 14.2.5 Detailed Joint Setting

Besides the basic joint settings, you can click the Detail button and specify the details in the Detail Setting window.

| See: | Common Setting |
| --- | --- |
|  | Corner Joint Setting |
|  | Wire Joint Setting |
|  | Chute Setting |

| See: | Fixed Position |
| --- | --- |
|  | Auto Position |
|  | Basic Joint Setting |
|  | Joint Type Table |
|  | Joint Setting Condition |

#### 14.2.5.1 Common Settings

Options in the Common panel allow you to define the common joint assignment conditions.

| Option | Description |
| --- | --- |
| Ignore CAD Joint | If the joints were assigned to the parts during the CAD designing phase, place a check mark in the check box to enable the system ignore these information, and assign joints based on the settings in Process After Cutting Table. Remove the check mark from the Ignore CAD Joint: check box, if the joints were assigned to the parts during the CAD designing phase, the system will use these joints, and this setting is with higher priority than the joint settings in Process After Cutting Table. |
| Center of Gravity has higher Priority | When you place a check mark in the Center of Gravity has Higher Priority: check box, the system will consider the center of gravity of the part when assigning joints. |
| Display Warning when Joints are Unbalanced | This function is not available yet. |
| Range of Searching Joint Position | You can define the range for searching a proper position to place joints. |
| Position Priority | Click the arrow button to open the drop-down list. You can select a position from the list to place the joint. |
| Length Side | Place joints on the length side of part. |
| Width Side | Place joints on the width side of part. |
| Longer Edge | Place joints on the longer side of two edges. |
| Notch Avoid Length | Specify the conditions to assign joints to the specified notch. If the width of a notch is less than or equal to the value you type in the text box, no joint will be assigned to the notch. |
|  | Note: Normally, no tabs would be assigned to the notch. Only when the width of the notch is at least 10 times longer than the height, joints will then be assigned to the notch. |

| See: | Corner Joint Setting |
| --- | --- |
|  | Wire Joint Setting |
|  | Chute Setting |

#### 14.2.5.2 Corner Joint Settings

The options in the Corner Joint panel allow you to specify the corner joint location conditions.

You can specify the application of joints according to the corner type and arc size.

| Option | Description |
| --- | --- |
| 90 Degree Corner | Specify the corner joint location at the 90-degree corner. There are three options: Both Sides, One Side and None. |
| Both Sides | Place the joint on both sides of the corner. |
| One Side | Place the joint on one side of the corner. |
| None | When None is selected, no joint will be assigned to the corner. |
| Non-90 Degree | Specify the corner joint location at Non-90 degree corners. There are three options: One Side, Both Sides and None. |
| One Side | Place the joint on one side of the corner. |
| Both Sides | Place the joint on both sides of the corner. |
| None | When None is selected, no joint will be assigned to the corner. |
| Corner of Arc Line | Specify the corner joint location at the corner of arc and line. |
| One Side On Line | Place the corner joint on the line side of the corner of arc and line. |
| Both Sides | Place the corner joint on both sides of the corner of arc and line. |
| None | When None is selected, no corner joint will be assigned. |
| No corner joint when line <= | If the length of one line is less than or equal to the value you type in the text box, no corner joint will be assigned to that line. |
| Exclude C notch from Min Length Setting | If this option is selected, the C notch will be excluded from the minimum line joint assignment restriction. In other words, even though the C notch length is less than or equal to the value you defined in the No corner joint when line <=: text box, joint can be assigned on it. |
| No Corner Joint when Length of Arc <= | If the length of the arc is less than or equal to the value you type in the text box, no corner joint will be assigned to the arc. |
| No Corner Joint when Angle of Corner <= | This option allows you to specify the conditions to assign joints to the corner angle. If the angle of a corner is less than or equal to the value you type in the text box, no joint will be assigned to the corner. |

| See: | Common Setting |
| --- | --- |
|  | Wire Joint Setting |
|  | Chute Setting |

#### 14.2.5.3 Wire Joint Setting

The options in the Wire Joint panel allow you to specify the wire joint location conditions.

| Option | Description |
| --- | --- |
| Wire Joint Close to Corner | The options in this section allow you to specify the conditions to assign wire joints close to the corner. |
| Offset Amount | The value in this text box determines the distance between the corner vertex and the place to assign wire joints. |
| Punch Length | Select this option to place the wire joint in the position with the tool length distance to the corner vertex. |
| Corner with CR tool is Exception | Place a check mark in the check box so that there will be no joint offset when CR tool is used to process the CR line. |
| No Wire Joint when Line <= | If the length of the line is less than or equal to the value you type in the text box, no wire joint will be assigned to that line. |
| No Wire Joint when Length of Arc <= | If the length of the arc is less than or equal to the value you type in the text box, no corner joint will be assigned to that arc. |

| See: | Common Setting |
| --- | --- |
|  | Corner Joint Setting |
|  | Chute Setting |

#### 14.2.5.4 Chute Setting

Some special tools can work as the chute tools to perform the final hit.

The options in the Chute Tool panel allow you to specify the settings for the special tool you have assigned to separate the part from the sheet.

| Option | Description |
| --- | --- |
| Cut X | The dimension of the chute tool in the X-axis. |
| Cut Y | The dimension of the chute tool in the Y-axis. |
| Offset Y | The distance from the center of the die to the position of the final hit. |
| Tool Name | The name of the chute tool. The name of the chute tool should exactly match the name of the special tool in the tool inventory. |

| See: | Common Setting |
| --- | --- |
|  | Corner Joint Setting |
|  | Wire Joint Setting |

### 14.2.6 Joint Setting Condition

In the Joint panel, you can specify the joint settings and save the information for future use. You can also name your joint setting conditions and make modifications.

If you select Joint as the process after method, you can click the arrow button to display all the predefined conditions in the drop-down list.

Select one condition and click Apply to apply the joint settings.

To name a new joint setting condition, click New and type the name in the text box.

To save the joint setting conditions, click Save.

To delete a joint setting condition, select one joint condition from the drop-down list and click Delete.

| See: | Fixed Position |
| --- | --- |
|  | Auto Position |
|  | Basic Joint Setting |
|  | Joint Type Table |
|  | Detailed Joint Setting |

# Chapter 15: Peripherals

The options in the Peripherals window allow you to specify the parameters for the peripherals of a machine. In the Dr. ABE main window, select a machine from the machine list and click one preference button to open the Preference window. In the Preference File pane, double-click the Peripherals icon to open the Peripherals window. The window consists of seven panels: MJC, Taking Out, MJC/IJP Sequence, IJP, Taking Out Sequence, Edge Detection and Schedule.

| See: | MJC |
| --- | --- |
|  | Taking Out |
|  | MJC/IJP Sequence |
|  | IJP |
|  | Part Removal Sequence |
|  | Schedule |

## 15.1 MJC

MJC is an acronym for Micro Joint Cutter. The MJC device is used to remove the micro joints when the process is complete. MJC settings can be defined in the panel below.

| See: | MJC Setting |
| --- | --- |

| See: | Taking Out |
| --- | --- |
|  | MJC/IJP Sequence |
|  | IJP |
|  | Part Removal Sequence |
|  | Schedule |

### 15.1.1 MJC Setting

|  | Place a check mark in the Yes/No check box to enable the MJC settings. The MJC data is saved as .sy2 file with the IJP data. |
| --- | --- |

Note:

MJC device in the Machine Set window must be enabled first. See: To enable the MJC device

To enable the MJC device

| 1. | In Dr ABE main window, click the Machine Setting button to open the Machine Set window. |
| --- | --- |
| 2. | Select a punch machine (e.g. EM2510), and select MJC in the Peripherals subfolder. |
| 3. | Click the Edit button on the toolbar to edit in the MJC device panel. |
| 4. | Place a check mark in the MJC Yes/No check box to enable the MJC device. |

## 15.2 Taking Out

The TK device is a machine that uses vacuum cups or magnets to remove processed parts from sheet and place them on a stacking pallet.

These options in the Taking Out panel allow you to specify the conditions to remove and place.

| Note: |  |
| --- | --- |
| 1. | Only when you place a check mark in Taking Out Yes/No check box, is this panel available. See Taking Out Information in the Machine Set window. |
| 2. | Select PartRemoverП option from Type of Taking Out: drop-down list |

| See: | Taking Out Conditions |
| --- | --- |
|  | Stack Distance |
|  | Taking Out |

| See: | MJC |
| --- | --- |
|  | MJC/IJP Sequence |
|  | IJP |
|  | Part Removal Sequence |
|  | Schedule |

### 15.2.1 Taking Out Conditions

The options in the Taking Out Conditions section allow you to specify the axis moving speed of the taking out device.

| Option | Description |
| --- | --- |
| Taking Out On/Off | Place a check mark in the Taking Out On/Off check box to enable the Taking Out options. |
| Speed | Specify the axis speed of the TK device. There are three options: Top Speed (F1), Middle (F2) and Slow (F3). The speed information will be saved in the *.sy2 file. |
| Down When Stack Part | This option allows the machine lower the arm when collecting parts. |
| Skeleton to Scrap Shear | This option allows the system to output an M code at end of NC data for scrap shear and the skeleton material will be carried to a scrap shear device. |

| See: | Stack Distance |
| --- | --- |
|  | Taking Out |

### 15.2.2 Stack Distance

The options in the Stack Distance section allow you to specify the part spacing and the stacking border for stacking parts on the table.

| Option | Description |
| --- | --- |
| Auto Stack On | This option allows you to perform the automatic stacking process. |
|  | Example: |
|  | There are three sheets you want to stack. If you remove a check mark from the Auto Stack On check box and execute Do Stack, the parts on one sheet will be stacked on one table. The parts on the three sheets will be stacked on three tables. |
|  | If you place a check mark in the Auto Stack On check box and execute Do Stack, the parts on the three sheets will be stacked on one table. The system will try to stack as many parts as possible on the table. |
| The Balance of One Table | Place a check mark in this option and the TK device will place parts in balanced layout to stabilize the pallet. |
|  | Remove a check mark in this option. TK device will stack the same parts by overlapping them in one group regardless of pallet balance. |
| Stacking Scheme Type | Select a stacking pallet type from Stacking Scheme Type: drop-down list. There are four types available. The stacking scheme type information will be saved in the *.sy2 file. |
| X= Y= | Type a value in the text box to specify the space between the parts in the X and Y directions. |
| L = R = U = B = | Type a value in the text box to specify the minimum distance between the part border and the pallet edge. |

| See: | Taking Out Conditions |
| --- | --- |
|  | Taking Out |

### 15.2.3 Taking Out

|  | The TK device uses vacuum cups or magnets to take out parts. You can use the vacuum system to remove either ferrous or non-ferrous materials, however, magnets cannot take out non-ferrous materials. It is necessary to specify which material type magnets CAN take out. The Taking Out section allows you to list and specify the ferrous material types that the TK device can take out. |
| --- | --- |

Example

| 1. | Click the Select from Mat. Parameter button to display the Material Type window. |
| --- | --- |
| 2. | Select a material type by placing a check mark in the material type check box. |
| 3. | Click OK to continue. And the selected material type is displayed in the Taking Out table. |
| 4. | In the Taking Out table, you can right-click the row header and select New from the shortcut menu. |
| 5. | A new blank row is added to the end of the Material Type column, and you can type the material name in it. |
| 6. | To delete a material type, simple select a material type, and right-click to open the shortcut menu, and then select Delete. |

| See: | Taking Out Conditions |
| --- | --- |
|  | Stack Distance |

## 15.3 MJC/IJP Sequence

The options in MJC/IJP Sequence panel allow you to determine the MJC/IJP sequence in relation to the part layout.

| Option | Description |
| --- | --- |
| Start Position/Direction | Click the arrow in Start Point/Direction section to specify the MJC/IJP starting point and process direction. The green arrow indicates the selected starting point and process direction. |
| Width for Sequence | This option allows you to determine the division number for sequence. |
|  | Place a check mark in the Width for Sequence check box and type a value in the text box to divide the process area into equal districts. System will perform MJC/IJP process in the first district and then the adjacent district based on the settings defined in the Start Point/Direction section. |
|  | Note: Whether to process the part in one district is determined by the location of the center of the part. If the center point of the part is located within the district in which the system is processing, the part will be processed. |
|  | Example: |
|  | Start Position: Upper Right Direction: X axis See picture below. Red arrows indicate the process sequence. |
|  | If you remove a check mark from this check box, system will perform Macro Joint cutting (MJC) and marking (IJP) process based on the shortest path from specified starting point. |
|  | Example: |
|  | Starting Point: Upper Right See picture below. Red arrows indicate the process sequence. |

| See: | MJC |
| --- | --- |
|  | Taking Out |
|  | IJP |
|  | Part Removal Sequence |
|  | Schedule |

## 15.4 IJP

IJP is an acronym for Ink Jet Printer. The IJP device is used to print part information on parts.

The setting information is saved as a *.sy2 file together with MJC data. In the IJP panel, you can specify what need printing: part name, comment, part size, due date, process date, etc.

| See: | IJP Setting |
| --- | --- |
|  | IJP Position |
|  | IJP Strings |

| See: | MJC |
| --- | --- |
|  | Taking Out |
|  | MJC/IJP Sequence |
|  | Part Removal Sequence |
|  | Schedule |

### 15.4.1 IJP Setting

|  | Place a check mark in Yes/No check box to enable the IJP settings. Click the down-arrow button to open the drop-down list of IJP device numbers and select the device you want to use from the list. Normally, there are three devices and you can specify them in the Machine Set window. Each device has its corresponding IJP information, such as maker, max string size X/Y, max string number, etc. |
| --- | --- |

Note:

You must enable the IJP device in the Machine Set window first. See: To enable the IJP device

To enable the IJP device

| 1. | In Dr ABE main window, click the Machine Setting button to open the Machine Set window. |
| --- | --- |
| 2. | Select a punch machine (e.g. EM2510), and select IJP in the Peripherals subfolder. |
| 3. | Click the Edit button on the toolbar to edit in the IJP device panel. |
| 4. | Place a check mark in the IJP Yes/No check box to enable the IJP device. |

| See: | IJP Position |
| --- | --- |
|  | IJP Strings |

### 15.4.2 IJP Position

|  | You can specify the IJP position in this IJP Position section. |
| --- | --- |

| Option | Description |
| --- | --- |
| Auto | If you select Auto, the system will calculate and determine where system will print the IJP information on the part automatically. Click the rectangle to specify the IJP printing position. The selected rectangle will become green. |
|  | Suppose the rectangle in the bottom right corner is selected. |
|  | The rectangle with two diagonal lines will display at the bottom right corner of the part. This white rectangle is where the IJP information will be printed. |
|  | Right-click the part layout area to open the shortcut menu and select Save MJC Data. All IJP information you specify will be saved in the *.sy2 file as follows. |
| Fix Position | Select Fix Position to instruct IJP device to print the part information you specify in an area of the part according to the settings based on the Position X and Position Y: text boxes. |
|  | For example: |
|  | The IJP information will be printed in the position of the part as follows. |

| See: | IJP Setting |
| --- | --- |
|  | IJP Strings |

### 15.4.3 IJP Strings

You can specify the items you want to print on the part in the IJP Strings section.

Double click an item in the list to add it to the text box below. You can also type common part information you want in the text box directly. The information of the selected items will be printed on the part.

| Option | Description |
| --- | --- |
| Part Name | Print the part name. |
| Comment | Print the part comment. |
| Size of Part | Print the part size. |
| Due Date | Print the due date of the part. |
| Process Date | Print the process date of the part. |
|  | More information about items above, See Part List in the Nesting Plan window. |
| User #1 - User #5 | Print the User # 1 to User # 5 strings that you previously defined in the Nesting Plan window. See User Define in the Nesting Plan window. |
| Line Feed | The Line Feed code is used to divide strings into several rows. See Line Feed Character in the Machine Set window. |

| See: | IJP Setting |
| --- | --- |
|  | IJP Position |

## 15.5 Part Removal Sequence

These options in the Part Removal Sequence section allow you to specify the sequence to take out parts.

Note:

Only when you place a check mark in Taking Out Yes/No check box, is this panel available. See Taking Out Information in the Machine Set window.

| Option | Description |
| --- | --- |
| Start Position/Direction | Click an arrow in the Start Point/Direction section to specify the starting point and direction to take out parts. You have eight choices: left-top corner along X axis, left-top corner along Y axis, right-top corner along Y axis, right-top corner along Y axis, right-bottom corner along Y axis, right-bottom corner along Y axis, left-bottom corner along X axis, left-bottom corner along X axis. |
| Single Direction | Place a check mark in the Single Direction check box to take out parts from one direction. |
| Width for Sequence | Place a check mark in the Width for Sequence check box to divide the process area into equal smaller areas. The system will take out the parts in the first area and then the adjacent area based on the settings defined in the Start Point/Direction section. |
|  | Type a value ranging from 1 to 10 in the text box below to specify how many sections you will divide into. The blue arrow indicates process direction. |
| Repositioning Area Direction | Specify the reposition direction by selecting X or Y option from the drop down list. |
| Slow Down Axis Movement | Specify the speed (F2~F4) of worktable movement for last perimeter punch before last hit. In that case, parts may avoid being damaged during processing. If remove the check mark, default speed is F1. If F1 is full speed, F2 indicates 75% of F1, F3 is 50% and F4 indicates 25%. |
| When Cutting Outer Perimeter | This option allows you to apply setting defined in the Slow Down Axis Movement option to speed of worktable movement each time last outer perimeter punch before last hit for each part is preformed. |
| Specify Clamp Area | This option allows you to specify an area in which worktable movement speed needs to be slow down for hits before last hit . Once the edge of the tool touches this area , speed of worktable movement will be specified according to setting defined in the Slow Down Axis Movement option. When this option is selected, a text box inside picture below will be available. |
|  | Type a value to specify a distance away from the edge of sheet to form an area in which the speed of worktable movement will be slow down. |

| See: | MJC |
| --- | --- |
|  | Taking Out |
|  | MJC/IJP Sequence |
|  | IJP |
|  | Schedule |

## 15.6 Schedule

After finishing a work order, the system will place the processed sheet in the MARS system and then generate a new schedule. A signal may be generated to instruct MARS to exchange pallet automatically before a new schedule is created.

These options in this panel allow you to determine how to create a signal for pallet exchange.

| Items | Description |
| --- | --- |
| Output accumulation pallet exchange instruction | Place a check mark in this check box to activate pallet exchange function. |
|  | Select First Line or Last Line from drop down list to determine in which system will create a pallet exchange signal. |

| See: | MJC |
| --- | --- |
|  | Taking Out |
|  | MJC/IJP Sequence |
|  | IJP |
|  | Part Removal Sequence |

# Chapter 16: Group

The Group window allows you to set the Grouping Priority for parts.

You can also specify the group conditions to process Prototype, TK, and Filler Parts.

To open the Group window:

In the Preference window, select a punch machine (e.g. EM2510) and double-click the Group icon to display the Group window.

| See: | Grouping Priority |
| --- | --- |
|  | Prototype Condition |
|  | TK Process Type |
|  | Filler Parts |

## 16.1 Grouping Priority

The options in the Grouping Priority section allow you to specify the conditions to group parts during the nesting process.

| Option | Description |
| --- | --- |
| Grouping Priority | Select one option from the Grouping Priority: drop-down list to specify the grouping condition. |
| Process Date | The system will group the parts according to the process date. Parts of different process dates will be processed on different sheets. |
| Due Date | The system will group the parts according to the due date. Parts of different due dates will be processed on different sheets. |
| Give Higher Priority to Product Unit | The system will group the parts in the same assembly and process them together. |
| Give Higher Priority to Prototypes | The system will process prototypes first, and then the other parts on other sheets. |
| None | Parts will not be grouped during the nesting process. |
| Strictly Enforce Grouping Priority | Place a check mark in this check box to enable the system strictly apply the grouping priorities that you have defined. Only the parts that meet the same grouping conditions will be processed on the same sheet. Note: The check mark is placed in the check box by default. The grouping priority will NOT take effect when the check mark is removed. |
| Give Higher Priority to Group of Small Parts | As a rule, the system will always nest the larger parts before the smaller ones. If you place a check mark in this check box, the system will nest the smaller parts first, and ignore the priority settings you made in the Nesting Plan. See Priority under Nesting for details. |

Example:

| 1. | In the four parts below, Part A, C, and D have the same process date, while Part B has a later one. |
| --- | --- |
| 2. | In the Group window, select Process Date from the Grouping Priority: drop-down list and make sure a check mark is in the Strictly Enforce Grouping Priority: check box. |
| 3. | Click the Auto Execute button to perform the nesting process. As in the result, the parts with the earlier process date (Part A, C, D) are laid out on the first sheet, and Part B with a later process date is laid out on the second sheet. Note: On the first sheet, the larger parts are laid out first. |
| 4. | In the Group window, select Process Date from the Grouping Priority: drop-down list and place check marks in both the Strictly Enforce Grouping Priority: check box and the Give Higher priority to Group of Small Parts: check box. |
| 5. | Click the Auto Execute button to perform the nesting process. As in the result, now the parts with the same process date are still laid out on the first sheet, however, the smaller parts are laid out prior to the bigger ones. Part B is still laid out on the second sheet due to its later process date. |

| See: | Prototype Condition |
| --- | --- |
|  | TK Process Type |
|  | Filler Parts |

## 16.2 Prototype Condition

The options in the Prototype Condition section allow you to define the prototype conditions so as to decide whether to put the prototype parts into the total part quantity or not.

| Option | Description |
| --- | --- |
| Nest One Product Unit | During the nesting process, the prototype quantity will be the quantity of the parts in the assembly instead of the quantity specified in the Part Properties window. |
| Prototype Quantity is Included | The prototype quantity will be included in the total part quantity. The quantity of the prototype is the exact quantity you set in the Parts Properties window. |
| Prototype Quantity Extra | The prototype quantity will be excluded from the total quantity of parts. The quantity of the prototype is the exact quantity you set in the Parts Properties window. |

Example:

| 1. | Select Nest One Product Unit in the Prototype Condition section. |
| --- | --- |
| 2. | In the Sequence panel of the Sequence preference window, place a check mark in the Machine Stop for Prototype: check box and also make sure the Output only one M00: check box remains empty so that M00 command line will be generated in the NC code for each completed prototype part. |
| 3. | Open the Nesting Schedule window. Specify the assembly lot, part quantity and prototype quantity as follow. |
| 4. | Click the Auto Execute button to perform the nesting process. As in the result, the system laid out 6 parts in 3 lots. 2 parts are treated as prototypes as 2 M00 command lines indicated in the NC code. The prototype quantity is exactly the same as the part quantity of each assembly. |
| 5. | Select Prototype Quantity is Included in the Prototype Condition section. |
| 6. | Click the Auto Execute button to perform the nesting process. As in the result, the system also laid out 6 parts in 3 lots, but only 1 part among them is treated as the prototype as only 1 M00 command line indicated in the NC code. |
| 7. | Select Prototype Quantity Extra in the Prototype Condition section. |
| 8. | Click the Auto Execute button to perform the nesting process. As in the result, an extra part is laid out as the prototype in addition to the 6 parts in 3 lots. 1 M00 command line is generated in the NC code to indicate that 1 prototype is processed. |

| See: | Grouping Priority |
| --- | --- |
|  | TK Process Type |
|  | Filler Parts |

## 16.3 TK Process Type

The options in the TK Process Type section allow you to specify how to layout micro-joint-parts and TK carry-outable parts in sheets.

Note:

This section is only available when the punch machine is equipped with TK device.

| Option | Description |
| --- | --- |
| Put a frame on a micro-joint-part | This option is NOT available for EM machines currently. |
| Layout a micro-joint-part in the different sheet | Layout micro-joint-parts and TK-parts on the different sheet. |
| Layout a micro-joint-part and TK-part in the same sheet. | Layout micro-joint-parts and TK-parts on the same sheet as usual. |

| See: | Grouping Priority |
| --- | --- |
|  | Prototype Condition |
|  | Filler Parts |

## 16.4 Filler Parts

The options in the Filler Parts section allow you to specify the conditions for filler parts.

The system will attempt to nest the filler parts on the sheet to improve the sheet utilization. You can define the filler parts in the Parts Properties window.

Note:

For sheets that can be reused, the filler parts will not be assigned.

| Option | Description |
| --- | --- |
| None | No filler part will be nested even though you have specified filler parts in the Parts Properties window. |
| Quantity Specified for Each Part | The quantity of the filler parts will be decided based on the filler parts defined for each part. When the system is nesting the filler parts, it will ignore the lots. Note: The maximum filler part quantity for each part will not exceed the defined quantity. |
| Total Quantity for the Assembly | The quantity of the filler parts will be decided based on the filler parts defined for each part and the assemblies. Note: The maximum filler part quantity for each part will not exceed the filler quantity x assembly quantity. |
| Give Equal Priority to all Filler Parts | All the filler parts, ignoring the size and priority you specified in the Parts Properties window, will have the same priority. Note: This function is currently unavailable. |

To specify filler parts:

| 1. | Open the Nesting Schedule window. You can define the filler part quantity by typing in the Filler Quantity column. |
| --- | --- |
| 2. | You can also specify filler part quantity in the Parts Properties window by typing in the Part: text boxes. The filler part quantity is the difference of the right side value minus the left side value. As in the example below, the filler part quantity is 3. (5–2=3). |

To nest filler parts on sheets,

| 1. | Load Part A and Part B and specify the nesting schedule as follow. |
| --- | --- |
| 2. | Click the Auto Execute button to perform the nesting process. The parts will be laid out as follow. |
| 3. | Now type 1 in the Filler Quantity column for Part B in the Nesting Schedule window. |
| 4. | Select None in the Filler Parts section. |
| 5. | Click the Auto Execute button to perform the nesting process. The parts will be laid out as follow without change. Although we have specified 1 in the Filler Quantity column for Part B, no Part B is laid out as filler part in the empty space on the sheet because None is selected. |
| 6. | Now select Quantity Specified for Each Part in the Filler Parts section. |
| 7. | Click the Auto Execute button to perform the nesting process. The parts will be laid out as follow. 1 Part B is laid out as the filler part in the empty space on the sheet. The quantity of the filler parts is exactly the same as the quantity specified in the Nesting Schedule window. |
| 8. | Now type 2 in the Filler Quantity column for Part B in the Nesting Schedule window. |
| 9. | Select Total Quantity for the Assembly in the Filler Parts section. |
| 10. | Click the Auto Execute button to perform the nesting process. The parts will be laid out as follow. 4 Part B are laid out as the filler parts in the empty space on the sheet. The quantity of the filler parts is decided by the assembly lot quantity and the filler quantity part that you specified in the Nesting Schedule window. (2*2=4) |

| See: | Grouping Priority |
| --- | --- |
|  | Prototype Condition |
|  | TK Process Type |

# Chapter 17 Clearance

Clearance is defined as a gap or space between the punch and die. For example, if you are using a 10.3mm die with a 10mm punch, the clearance is 10.3mm-10mm=0.3mm. The clearance has a major effect on the quantity of the finished product as well as tool wear. Improper clearances may result in the excessive breakaway and tool wear, secondary shear and bur and damaged tooling.  Material thickness, types of material and types of tools being used should be all considered in establishing proper clearance. You can specify Clearance parameter in Clearance window.

| To open the Clearance window: |
| --- |
| 1. | Click the NC Generate Preference button on the main window to open the Preference window. |
| 2. | Select a punch machine (such as EM2510) in the Tree View pane, and then double-click the Clearance icon in the Preference File pane to display the Clearance window. |

## 17.1 Clearance Setting

In the Clearance Setting table, you can directly type information in it to define the clearance for each material type. Click the last row in the table to expand a new row.

| Option | Description |
| --- | --- |
| Material | Type the material type here. |
| Thickness (Min-Max) | Type value in the cells to define the thickness range of this material type. |
| Clearance (Min-Max) | Type a value in the cell to define the clearance range of this material within the defined thickness range. Range: 0~999.999, Initial value: 0.0. |
| Clearance Selection (Min/Max) | If you place a check mark in the check box, the system will select tool within defined clearance range according to the following sequence: from tool of larger clearance to tool of smaller clearance. If you clear the check mark in the check box, the system will select tool within defined clearance range according to the following sequence: from tool of smaller clearance to tool of larger clearance. |
| Process Speed | You can select a process speed in the drop-down list. There are four options. F1 represents the highest speed. |

Example:

| 1. | Set the material clearance as follows: |
| --- | --- |
| 2. | There is a RE 110X6 in the tool inventory. If you do not set any die clearance for this tool. |
| 3. | The tool can be assigned to both kinds of material type. |
| 4. | Set 20 as the die clearance of this tool. |
| 5. | In this case, the tool RE 110X6 can be assigned to SECC but cannot assigned to SPC. Another tool is assigned to SPC. The system will assign another tool to process the part of SPC material. |

# Chapter 18: Turret Layout

The Tool Inventory window lists the tools that are available for your machines. You can update your tool inventory as you purchase new tools or remove broken tools. You can import tools to update your tool inventory or modify the tool information to meet your needs.

To open the TurretLayout window

| 1. | Click one preference button on the Dr. ABE main window to open the Preference window. In the Tree View pane, click EM2510. |
| --- | --- |
| 2. | In the Preference File pane, double-click one turret file icon , such as, HA445E, to open the TurretLayout window. |

Note:

In the Preference File pane, if there are several turret layouts, you can right-click one turret layout file, and select Set Default and the system will use this turret layout file by default.

To create a Turret layout file

| 1. | In the Machine Set window, specify the turret type for the EM machine. See Turret Name |
| --- | --- |
| 2. | In the Tree View pane, right-click EM2510 under My Preference, select New to Turret Layout Preference option to create a turret layout file. |
| 3. | A new turret layout file is created in the Preference File pane. |

Note:

- You can select New to Turret Layout(PDC) Preference to create a Turret Layout(PDC) file  in the Preference File pane.

- Before you create a Turret Layout (PDC) file, you must select a storage type for the machine. See: Storage Name

| See: | Import AP100 Turret Layout |
| --- | --- |
|  | TurretLayout Window |
|  | Turret Section |

## 18.1 Import AP100 Turret Layout

You can select EM2510 under My Preference in the Tree View pane, right-click and select Import Turret layout to import a turret layout file.

Import the Turret Layout files for the specified machine

| 1. | In the System Setting window, select SDD Parameter Automatic Download and type Apserver in the Data Server PC(AP100/PCL): text box to specify the PC to download the parameters. See: Parameter Processing |
| --- | --- |
| 2. | In the Tree View pane, select EM2510 under My Preference. Right-click and select Import Turret Layout. |
| 3. | Click OK to continue. |
| 4. | In the ToolInventory Setting window, select HA445 and click OK to continue. You can select more than one turret file at a time. |
| 5. | A turret layout file HA445 is imported to Dr ABE blank. |

| See: | TurretLayout Window |
| --- | --- |
|  | Turret Section |

## 18.2 TurretLayout Window

The TurretLayout window is a graphical representation of all the tools and stations available for your machine.

The turret section displays the information for each station, such as Station, Range, Shape, Size X, Size Y, etc.  You can add tools to the turret. You can display the stations by Shape or by Range. See: Turret Type

Note:

You can also display the turret station (PDC) in this window. See: Turret Type (PDC)

The Tool Inventory section lists the information for each tool in the inventory, such as Shape, Size, Type, Air Blower, etc. You can display the tools by Shape or by Range. You can import tools to update your inventory or modify the tool information to meet your needs. See: Tool Inventory

| See: | Import AP100 Turret Layout |
| --- | --- |
|  | Turret Section |

## 18.3 Turret Section

The turret section displays the information for each station, such as Station, Range, Shape, Size X, Size Y, etc.  You can add tools to the turret. You can display the stations by Shape or by Range.

About the details for Turret (PDC), please refer to Turret Type (PDC)

| See: | Turret Section Toolbar |
| --- | --- |
|  | Range and Shape buttons |
|  | View Buttons |
|  | T No. |
|  | Search Stations |
|  | Turret Picture |
|  | Turret Station List |

| See: | Import AP100 Turret Layout |
| --- | --- |
|  | TurretLayout Window |

### 18.3.1 Turret Section Toolbar

The buttons on the toolbar allow you to display the stations based on the shape and range. You can select the method to display the Turret, Turret list, or Inventory.

| See: | Range and Shape buttons |
| --- | --- |
|  | View Buttons |
|  | T No. |
|  | Search Stations |
|  | Turret Picture |
|  | Turret Station List |

### 18.3.2 Range and Shape buttons

Click a range buttons to display turret stations of that range. The  button is selected by default and stations of all the ranges will be displayed.

Click a shape button to display the tools of that shape. The  button is selected by default and tools of all the shapes will be displayed.

| See: | Turret Section Toolbar |
| --- | --- |
|  | View Buttons |
|  | T No. |
|  | Search Stations |
|  | Turret Picture |
|  | Turret Station List |

### 18.3.3 View Buttons

|  | Option Description Turret Display the turret. Turret Inventory Display the turret and tool inventory. Inventory Display the tool inventory. Turret List Display the list of turret stations. Turret Picture + list Display the turret illustration and the list of the turret stations. Turret Picture Display the turret illustration. |
| --- | --- |

| See: | Turret Section Toolbar |
| --- | --- |
|  | Range and Shape buttons |
|  | T No. |
|  | Search Stations |
|  | Turret Picture |
|  | Turret Station List |

### 18.3.4 T No.

|  | In the T No. text box, you can type the number of the station you want to locate. Click the T NO. arrow button to display the drop- down list. Option Description All Display all the stations Blank Station Display all the stations without tools added. Station with tool Display all the stations with tools added. Fixed Station Display all the fixed stations. Note: If a station with a tool assigned is set to Fixed, no other tools are allowed to assign to it. If an empty station is set to Fixed, no tools are allowed to assign to it. Free Station Display all the free stations |
| --- | --- |

| See: | Turret Section Toolbar |
| --- | --- |
|  | Range and Shape buttons |
|  | View Buttons |
|  | Search Stations |
|  | Turret Picture |
|  | Turret Station List |

### 18.3.5 Search Stations

Click Search button  to open the Advanced Filter window. The options in this window allow you to filter the results by Name, Shape, Range, etc. For example, if you type a C in the Range text box, and the system will search the current turret and list the stations that are installed tools of C range.

| See: | Turret Section Toolbar |
| --- | --- |
|  | Range and Shape buttons |
|  | View Buttons |
|  | T No. |
|  | Turret Picture |
|  | Turret Station List |

### 18.3.6 Turret Picture

|  | The turret illustration shows the turret layout. The system uses different colors to show the station status. The pink color indicates the station has been assigned a tool. The green color indicates this station has been assigned candidate tools. The orange color indicates a tool has been assigned to the station, and meanwhile candidate tools are also assigned to the same station. The blue color is used to highlight the station being selected. You can specify the turret layout in two methods, Turret Load Setting and Effective Station Setting. |
| --- | --- |

| Option | Description |
| --- | --- |
| Turret Load Setting | Specify the turret tools by using the Tool Inventory. See: Assign tools in the Turret Load Setting mode |
| Effective Station Setting | Specify tools that will be used with higher priority in the turret station. See: Assign tools in the Effective Station Setting mode |

| See: | Assign tools in the Turret Load Setting mode |
| --- | --- |
|  | Assign tools in the Effective Station Setting mode |

| See: | Turret Section Toolbar |
| --- | --- |
|  | Range and Shape buttons |
|  | View Buttons |
|  | T No. |
|  | Search Stations |
|  | Turret Station List |

#### 18.3.6.1 Assign tools in the Turret Load Setting mode

| 1. | In the TurretLayout window, select Turret Load Setting, and then select one tool in the tool inventory section. |
| --- | --- |
| 2. | Drag and drop the selected tool to the desired station in the station list, for example, Station 217. |
|  | The selected tool is assigned to Station 217. |
| 3. | You can also directly drag and drop the tool to the desired station in the Turret picture. For example, Station 217. |
|  | As the following picture indicates, the selected tool is assigned to Station 217. |

Note:

Tools can only be assigned to the stations of the same ranges unless adapter is used.

| See: | Assign tools in the Effective Station Setting mode |
| --- | --- |

#### 18.3.6.2 Assign tools in the Effective Station Setting mode

| 1. | In the TurretLayout window, select Effective Station Setting, and then select one tool in the tool inventory section. |
| --- | --- |
| 2. | Drag and drop the station to the desired station in the turret station list. For example, Station 107, If you drop the tool to the row marked with an asteroid, the selected tool will be regarded as one candidate tool. You can assign more than one candidate tool to the same station. |
|  | Note: You can right-click one candidate tool, and select Remove Effective Setting to remove the candidate tool from the station. You can right-click one tool in the Tool Inventory list and select Assign Station to display the Station Selection window, click to select one station, and the selected tool be treated as the candidate tool for that station. |
| 3. | You can drag and drop a tool to the yellow row of the desired station, for example, Station 107, to add the tool to that station. |
| 4. | You can also directly drag and drop the tool to the desired station in the Turret picture. For example, Station 217. |
| 5. | As the following picture indicates, the selected tool is assigned to Station 217. |

| See: | Assign tools in the Turret Load Setting mode |
| --- | --- |

### 18.3.7 Turret Station List

The turret station lists the detailed information for each station, such as the station range, dead zone range, etc. You can display the stations by Station Range, select the items to display, or modify the station dead zones, etc. See: Turret Type Window Items

In the turret station list, right click to display the shortcut menu.

| Option | Description |
| --- | --- |
| Remove Tool | Select this option to remove the tool from the station. |
| Set Fix | Select this option to set the fix. |
| Remove Fix | Select this option to remove the fix. |
| Assign Station | Assign a turret station to the selected the storage on PDC. See: Assign Station to a Storage |
| Detach Station | Break the link between the turret station and the storage on PDC. |
| Remove Effective Setting | Remove the candidate tools from the selected stations. |

Assign Station to Storage

| 1. | In the Preference window, double-click one Turret Layout (PDC) icon in the Preference File pane to open the TurretLayout window. |
| --- | --- |
| 2. | In the In the turret station list, select Storage 601, and right click to display the shortcut menu. |
| 3. | In the Assign Station window, select Station 107 and click OK to continue. |
| 4. | As you can see Station 107 is assigned to Storage 601. |
|  | Note: You can select Storage 601, right-click and select Detach Station to break the link between Station 107 and Storage 601. |
| See: | Turret Section Toolbar |
|  | Range and Shape buttons |
|  | View Buttons |
|  | T No. |
|  | Search Stations |
|  | Turret Picture |

# Chapter 19: Dead Zone

The Dead Zone window lists all the available station ranges, and you can add, delete or modify the station ranges. The station range will be considered during the sequencing. If a tool hit is too close to the clamps, and the tool guide might collide with the clamps, repositions will occur.

To open the Dead Zone window,

| 1. | Click any preference button in the main window to display the Preference window. |
| --- | --- |
| 2. | In the Tree View, select Dead Zone under Public to display the Dead Zone icon in the Preference File pane. |
| 3. | Click the DeadZone icon to open the Dead Zone window. |
|  | Option Description DZNo The number of the dead zone range. X Size of Range The X dimension of the dead zone range. Usually, it is the diameter of the guide. Y Size of Range The Y dimension of the dead zone range. Usually, it is the diameter of the guide. |
| 4. | You can right-click any where in the window and select Append to add a new range. And you can select Delete to delete the range you have highlighted. |

| See: | Dead Zone of the Station |
| --- | --- |

## 19.1 Dead Zone of the Station

The dead zone of each station is different from the clamp dead zone specified in the Machine Set window. You can determine whether the system will perform reposition to prevent a tool hit or cutting path from entering the dead zone.

Example

| 1. | In the Preference window, select Turret Type under Public, and double-click one turret type (e.g. HA445E) in the Preference File pane to display the Turret Type window. |
| --- | --- |
| 2. | The Turret Type window lists the detailed station information, such as Station, Range, Dead zone range, etc. |
|  | Note: You can select one station, right-click and select Append Dead Zone from the shortcut menu. In the DeadZone window, select one station range and click OK. The selected station range will be applied to the station specified. |
| 3. | Let’s take Station 224 for example. We notice that the Y dimension of the Station 224 (DZY) or the guide diameter is 116.665. If the tool in this station is assigned to process a pattern. To prevent the tool guide colliding with the clamps, the minimum distance of the tool hit center from the material edge will be DZ Y/2 + Clamp Length. In this case, the minimum distance will be DZ Y/2 + Clamp Length=116/2 + 10=68. See: Clamp Information |
| 4. | In the Preference window, select a punch machine (e.g. EM2510), and double-click the Sequence icon to display the Punch Sequence window. |
| 5. | In the Punch Sequence window, click the Clamp Avoidance tab. |
| 6. | Place a check mark in the Avoid DZ: check box. And the system will consider the dead zone area during the sequencing. |
| 7. | If the distance from the tool hit center to the material edge is less than 68, as the following left picture shows, the system will automatically perform a reposition during the process. |
|  | Before Reposition After Reposition |
| 8. | If the distance from the tool hit center to the material edge is more than 68, as the following picture shows, no reposition will occur. |

# Chapter 20: Schedule

The Schedule window allows you to specify names for the sheets, schedules, and to specify the schedule priority.

To open the Schedule window,

| 1. | In the Dr. ABE main window, click the Schedule Preference button to open the Preference window. |
| --- | --- |
| 2. | In the Preference File pane, double-click the Schedule icon to display the Schedule window. This window has three panels, Sheet Name, Schedule Name and Scheduling Priority panel. |

| See: | Sheet Name |
| --- | --- |
|  | Schedule Name |
|  | Scheduling Priority |

## 20.1 Sheet Name

The options in the Sheet Name panel allow you to configure the sheet names for the schedule. You can choose the items that constitute the sheet name, assign a name automatically, or specify a special name.

| See: | Sheet Name Items |
| --- | --- |
|  | Nesting Name |
|  | Date |
|  | Sequence Number |
|  | For Combination Process, Change Sheet Name Based on the Machine |
|  | Sheet Name |

| See: | Schedule Name |
| --- | --- |
|  | Scheduling Priority |

### 20.1.1 Sheet Name Items

|  | In the Sheet Name Items list, you can select the items to constitute the sheet name. The selected items will appear in the Sheet Name text box. |
| --- | --- |

| Items | Description |
| --- | --- |
| Nesting Name | The name of the nesting schedule. You can assign different nesting names to distinguish between the nest jobs. See Nesting Name. |
| Process Date | The date to process part. If a part has a different processing date, the earliest date will be used. |
| Deadline | The part process due date. If a part has different process deadlines, the earliest one will be used. |
| Machine Name | The machine name. |
| Material Name | The material name. |
| Thickness | The sheet thickness. |
| Today’s Date | The current date. |
| Sequence Number | Select this item and the system will use a series of sequential numbers to name the sheets. Make sure to type a starting sequence number in the Start Number: text box. See Sequence Number. |
|  | Note: This item is selected by default and cannot be removed from the Sheet Name: text box. See Sheet Name |
| Material Type | The material type. |

| See: | Nesting Name |
| --- | --- |
|  | Date |
|  | Sequence Number |
|  | For Combination Process, Change Sheet Name Based on the Machine |
|  | Sheet Name |

### 20.1.2 Nesting Name

This section allows you to specify the nesting names. The nesting will refer to the result of one single auto execution of the system that processes one or more sheets.

| Option | Description |
| --- | --- |
| Auto Assign | Select this option to use a number as the nesting name. |
|  | Notes: |
|  | 1. You can only type a number in the Auto Assign: text box. |
|  | 2. If you select this option, the system will automatically update the nesting name and assign it to the next nesting after you save the NC data of the nesting result. And the schedule name will change accordingly if the Nesting Name option is selected to constitute the schedule name. See Schedule Name for details. |
| Special Name | Select this option to use a special string as the nesting name. You can type a nesting name in the text box or select a name from the drop down list. |
|  | Note: When you type a number in the Special Name: text box, the system will regard it as characters. No changes will be made to create the next nesting name even though you save the NC data of the current nesting. |

Example

| 1. | In the Sheet Name panel, specify the conditions as follow. |
| --- | --- |
| 2. | The sheet names are 10001, 10002, and 10003 after the nesting process is completed. |
| 3. | Click the Main Preference button to open the System Setting window and change the database to File and then return to the main window. Select the nesting results and right-click the row headings to display the shortcut menu. Select Save NC data from the menu to display the Input O Number dialog box. |
| 4. | In the Input O Number dialogue box, type a number and click OK to continue. |
| 5. | In the Browse For Folder window, navigate and select the destination folder to save the NC data file. Click OK. |
| 6. | Click the Auto Execute button again, and in the result view you will find the sheet names are changed: 20004, 20005 and 20006. |

| See: | Sheet Name Items |
| --- | --- |
|  | Date |
|  | Sequence Number |
|  | For Combination Process, Change Sheet Name Based on the Machine |
|  | Sheet Name |

### 20.1.3 Date

This section allows you to specify the date format. Y = Year, M = Month and D = Date.

Example

| 1. | In the Sheet Name panel, specify the conditions as follow. |
| --- | --- |
| 2. | The sheet name will be as follows after the nesting process is completed. |

| See: | Sheet Name Items |
| --- | --- |
|  | Nesting Name |
|  | Sequence Number |
|  | For Combination Process, Change Sheet Name Based on the Machine |
|  | Sheet Name |

### 20.1.4 Sequence Number

This section allows you to specify the starting sequence number. The Sequence Number item is selected by default and the "&[Sequence Number]" cannot be removed from the Sheet Name text box.

Example

| 1. | In the Sheet Name panel, specify the conditions as follow. |
| --- | --- |
| 2. | The sheet names are as follows after the nesting process is complete. |

| See: | Sheet Name Items |
| --- | --- |
|  | Nesting Name |
|  | Date |
|  | For Combination Process, Change Sheet Name Based on the Machine |
|  | Sheet Name |

### 20.1.5 For Combination Process, Change Sheet Name Based on the Machine

If you use both the FO and EM machines to process the same sheet, and if you enable this option, the system will assign two different names to the same sheet. This option is only valid for combination machines.

| See: | Sheet Name Items |
| --- | --- |
|  | Nesting Name |
|  | Date |
|  | Sequence Number |
|  | Sheet Name |

### 20.1.6 Sheet Name

Select one item from the Sheet Name Items list, and the selected item will appear in the Sheet Name:  text box. You can also edit the contents if necessary.

Notes:

- The Sequence Number item is selected by default and the "&[Sequence Number]" cannot be removed from the Sheet Name: text box.

- If you select the Nesting Name item from the Sheet Name Items list, you should define the nesting name. See Nesting Name.

- You cannot use the following characters, such as   \, /, :, *, ?, ", <, >, or |, to specify the sheet name.

Example

| 1. | Select the Material Name item in the Sheet Name Items list, and it will appear in the Sheet Name: text box. |
| --- | --- |
| 2. | You can type strings in the Sheet Name: text box. For example, type AAAA in the text box. |
| 3. | Click OK to close the Schedule window. |
| 4. | The sheet name will be as the follow after the nesting process is complete. |

| See: | Sheet Name Items |
| --- | --- |
|  | Nesting Name |
|  | Date |
|  | Sequence Number |
|  | For Combination Process, Change Sheet Name Based on the Machine |

## 20.2 Schedule Name

The options in the Schedule Name panel allow you to configure the schedule names for the schedule. You can choose the items that constitute the schedule name, and specify the starting number and date format.

| See: | Schedule Name Items |
| --- | --- |
|  | Number |
|  | Date |
|  | Schedule Name |

| See: | Sheet Name |
| --- | --- |
|  | Scheduling Priority |

### 20.2.1 Schedule Name Items

|  | In the Schedule Name Items list, you can select the items to constitute the schedule name. The selected item will appear in the Schedule Name: text box. |
| --- | --- |

| Option | Description |
| --- | --- |
| Nesting Name | The name of the nesting schedule. You can assign different names to distinguish from the different nest jobs. See Nesting Name. |
| Process Date | The date to process part. If different processing dates are assigned to one part, the earliest date will be used. |
| Deadline | The part process due date. If different process deadlines are assigned to one part, the earliest one will be used. |
| Machine Name | The machine name. |
| Material Name | The material name. |
| Thickness | The sheet thickness. |
| Today's Date | The current date. |
| Number | Select this item and the system will use a series of numbers to name the sheet. Make sure to type a starting number in the Start Number: text box. See Number |
|  | Note: This item is selected by default and cannot be removed from the Sheet Name: text box. See Schedule Name |
| Material Type | The material type. |

| See: | Number |
| --- | --- |
|  | Date |
|  | Schedule Name |

### 20.2.2 Number

|  | This section allows you to specify the starting sequence number. The Number item is selected by default and the "&[No]" cannot be removed from the Schedule Name: text box. |
| --- | --- |

Example

| 1. | In the Schedule Name panel, select the Nesting Name item. |
| --- | --- |
| 2. | Click the Sheet Name tab to activate the Sheet Name panel. |
| 3. | Specify the conditions as follow. |
| 4. | Click OK and perform the nesting process. The sheet names will be as follow. |
| 5. | In the result list, select and right-click one row heading to display the shortcut menu. Select Save Schedule Data from the menu to display the Save Schedule window. |
| 6. | In the Save Schedule window, the default schedule name is AAAA0001, which consists of the nesting name and the sequence number that you defined. You can modify the schedule name in the text box. |

| See: | Schedule Name Items |
| --- | --- |
|  | Date |
|  | Schedule Name |

### 20.2.3 Date

|  | This option allows you to define the date format: Y = Year, M = Month and D = Date. |
| --- | --- |

Example

| 1. | In the Schedule Name panel, specify the conditions as follow. |
| --- | --- |
| 2. | Auto Execute the nesting. |
| 3. | Select and right-click a row heading in the Result list to open the shortcut menu. |
| 4. | Select Save Schedule Data from the menu to display the Save Schedule window. |
| 5. | The default schedule name is 200608020001, which consists of the current date and the sequence number. You can also modify the name in the text box. |

| See: | Schedule Name Items |
| --- | --- |
|  | Number |
|  | Schedule Name |

### 20.2.4 Schedule Name

Select one item from the Schedule Name Items list, and the item selected will appear in the Schedule Name: text box. You can also edit the contents if necessary.

Notes:

- The Number item is selected by default and the "&[No]" cannot be removed from the Sheet Name: text box.

- If you select the Nesting Name item from the Schedule Name Items list, you should define the nesting name. After you save the NC data of the nesting result, the system will automatically change the nesting name to create a new nesting name for the new nesting process. And the schedule name will change accordingly. See Nesting Name

Example

| 1. | In the Schedule Name panel, specify the conditions as follow. |
| --- | --- |
| 2. | In the Sheet Name panel, specify the Nesting Name settings as follow. |
| 3. | Select the nesting results after the nesting process is complete. Right-click the row heading to open the shortcut menu. Select Save NC data from the menu to display the Input O Number dialog box. |
| 4. | In the Input O Number dialogue box, type a number and click OK to continue. |
| 5. | In the Browse For Folder window, navigate and select the destination folder to save the NC data file. Click OK. |
| 6. | Select the nesting results and right-click the row heading to open the shortcut menu. Select Save Schedule data from the menu to display the Save Schedule window. |
| 7. | In the Save Schedule window, the default schedule name is 10001, which consists of the nesting name and the sequence number. Click OK to save the schedule data. |
| 8. | In the Dr. ABE main window, click the Auto Execute button to repeat the nesting process. After the nesting process is performed, select the nesting results and right-click the row headings to open the shortcut menu. Select Save Schedule data from the menu to display the Save Schedule window. |
| 9. | In the Save Schedule window, you will find the default schedule name becomes 20001. The system has automatically changed the nesting name to create the new schedule name. |

| See: | Schedule Name Items |
| --- | --- |
|  | Number |
|  | Date |

## 20.3 Scheduling Priority

In the Scheduling Priority panel, you can define the priorities to sequence the schedules (sheets).

| See: | Priority |
| --- | --- |
|  | Get Information from NC data |

| See: | Sheet Name |
| --- | --- |
|  | Schedule Name |

### 20.3.1 Priority

In the priority list, you can choose items used to sequence the schedules (sheets) by placing check marks in the check boxes of the priority items. You can click the arrow buttons along the right to sort the schedules (sheets) by the ascending or descending order. You can also click the arrow buttons below the list to move the selected item upward or downward in the list.

Notes:

- The higher the position of the item, the higher the priority.

- Only the Laser Material Name, Material Thickness, Material Type and Material Size items are currently available.

| Option | Description |
| --- | --- |
| Clearance | Sequence the schedules (sheets) by the clearance value of the punching tools. This option is not available for the moment. |
| Material Thickness | Sequence the schedules (sheets) by the material thickness. |
| Material Size | Sequence the schedules (sheets) by the material size. |
| Material Type | Sequence the schedules (sheets) by the material type. If you place a check mark in the check box of this option, set the ascending order as the sort order, the system will sort the schedules (sheets) by the material type, and in the order of Sketch, Skeleton and Standard. If the sort order is the descending order, the system will sort the schedules (sheets) in the order of Standard, Skeleton and Sketch. |
| Shorten the Combination Process Time | Sequence the schedules (sheets) to reduce the combination processing time. This option is not available for the moment. |
| Tool Layout Name | Sequence the schedules (sheets) by the tool layout name of the punch. |
| Tool Setup | Sequence the schedules (sheets) by the tool setup. When a tool setup is required for the same tool layout in punching, configure the tool setup. This option is not available for the moment. |
| Laser Material Name | Sequence the schedules (sheets) by the material name to determine the laser cutting conditions. |
| Laser Lens Type | Sequence the schedules (sheets) by the lens type for the laser processing. This option is not available for the moment. |

Example

| 1. | In the Priority list, place a check mark in the Material Size: check box. |
| --- | --- |
| 2. | You will use three sheets of different sizes and types during the nesting process. |
| 3. | In the Dr. ABE main window, click the Auto Execute button to perform the nesting process. You will find the nesting schedules are sorted by the material size in the ascending order. |
| 4. | Return to the Scheduling Priority panel; click the button to change it into , and then save the change. |
| 5. | In the Dr. ABE main window, click the Auto Execute button to perform the nesting process. You will find the nesting schedules are sorted by the material size in the descending order. |

| See: | Get Information from NC data |
| --- | --- |

### 20.3.2 Get Information from NC Data

This option allows you to import the material and tool information from the NC data.

| See: | Priority |
| --- | --- |

# Chapter 21: Tool Inventory

The Tool Inventory window lists the tools that are available for your machines. You can update your tool inventory as you purchase new tools or remove broken tools. You can import tools to update your tool inventory or modify the tool information to meet your needs.

To open the tool inventory window

| 1. | Click one preference button on the Dr. ABE main window to open the Preference window. In the Tree View pane, click Sub Inventory under Public. |
| --- | --- |
| 2. | In the Preference File pane, double-click the ToolInventory icon to open the SubInventory window. |
| See: | SubInventory Window |
|  | Tool Inventory Table |
|  | Tool Inventory Table Shortcut Menu |
|  | Tool Window |

## 21.1 SubInventory Window

The SubInventory window is a graphical representation of all the tools available for your machine. The Tool Inventory table lists the information for each tool in the inventory, such as Shape, Size, Type, Air Blower, etc. You can display the tools by Shape or by Range. You can import tools to update your inventory or modify the tool information to meet your needs.

| See: | SubInventory Window Toolbar |
| --- | --- |
|  | Range and Shape buttons |
|  | Import Buttons |
|  | View Buttons |
|  | Advanced Filter Window |
|  | Machine Type |

| See: | Tool Inventory Table |
| --- | --- |
|  | Tool Inventory Table Shortcut Menu |
|  | Tool Window |

### 21.1.1 SubInventory Window Toolbar

The buttons on the toolbar allow you to display the tools based on the shape and range. You can import AP100 tools or import the tool designs saved in DXF/DWG format and convert them into SP/FM tools.

| See: | Range and Shape buttons |
| --- | --- |
|  | Import Buttons |
|  | View Buttons |
|  | Advanced Filter Window |
|  | Machine Type |

### 21.1.2 Range and Shape buttons

Click a range button to display tools of that range. The  button is selected by default and tools of all the ranges will be displayed.

Click a shape button to display the tools of that shape. The  button is selected by default and tools of all the shapes will be displayed.

| See: | SubInventory Window Toolbar |
| --- | --- |
|  | Import Buttons |
|  | View Buttons |
|  | Advanced Filter Window |
|  | Machine Type |

### 21.1.3 Import Buttons

|  | The import buttons allow you to import AP100 tools, export or import the inventory information. And you can also import the tool designs saved in DXF/DWG format and convert them into SP/FM tools. |
| --- | --- |

| Button | Description |
| --- | --- |
| Import Global Inventory | Import AP100 tools into the Dr. ABE tool inventory. See: Import Ap100 tools into Dr ABE tool inventory |
| Import Global SP/FM Shapes | Import AP100 tools into the Dr. ABE tool inventory. See: Import Ap100 SP/FM tools into Dr. ABE tool inventory |
| Import File | Import the *.xml files of tool inventory |
| Export File | Export the tool inventory as *. xml files. |
| Import DXF/DWG SP/FM Shapes | Import the tool designs saved in DXF/DWG format and convert them into SP/FM tools. See: Import DXF/DWG SP/FM Shapes |

| See: | Import AP100 tools into Dr ABE tool inventory |
| --- | --- |
|  | Import Ap100 SP/FM tools into Dr. ABE tool inventory |
|  | Import DXF/DWG SP/FM Shapes |

| See: | SubInventory Window Toolbar |
| --- | --- |
|  | Range and Shape buttons |
|  | View Buttons |
|  | Advanced Filter Window |
|  | Machine Type |

#### 20.1.3.1 Import AP100 tools into Dr ABE tool inventory

| 1. | In the System Setting window, type the PC name or address in the Data Server PC (AP100/PCL): text box to specify the PC from which we will download the AP100 tools. See: Parameter Processing |
| --- | --- |
| 2. | Specify the group to import tools. Click the Import Global Inventory button. |
| 3. | Click OK to continue. |
|  | If you click Original, the following window displays, and you can specify the button and specify the initial tool angles after the tools are imported. If the tool angle is not defined, the default tool angle will be 0 degree. |
| 4. | AP100 tools are successfully imported into Dr. ABE tool inventory. |

| See: | Import Ap100 SP/FM tools into Dr. ABE tool inventory |
| --- | --- |
|  | Import DXF/DWG SP/FM Shapes |

#### 20.1.3.2 Import Ap100 SP/FM tools into Dr. ABE tool inventory

| 1. | In the System Setting window, type the PC name or address in the Data Server PC (AP100/PCL): text box to specify the PC from which we will download the AP100 SP/FM tools. See Parameter Processing |
| --- | --- |
| 2. | Specify the group to import tools. Click the Import Global SP/FM Shapes button. |
| 3. | In the Tool Load window, select one SP or FM tool, and click Open to continue. Note: You can select more than one tool each time. |
| 4. | SP and FM tools are successfully imported into Dr. ABE tool inventory. |

| See: | Import AP100 tools into Dr ABE tool inventory |
| --- | --- |
|  | Import DXF/DWG SP/FM Shapes |

#### 20.1.3.3 Import DXF/DWG SP/FM Shapes

| 1. | In the SubInventory window, Specify the group to import tools and then click Import DXF/DWG SP/FM Shapes button. |
| --- | --- |
| 2. | Browse and select the DXF file to import. After specifying the Tool Center Position and Type of Tool, click Open to continue. |
|  | Options Descriptions Tool Center Point Image Center CAD data center will be the punch center. Image Point One point of the CAD graphic will be the punch center. Coordinate X=0 Y=0 The coordinates (0.0) of the CAD graphic will be the punch center. Auto Condition Setup Setup the conditions to import the CAD files. See: Auto Correction Condition Setup Type of Tool SP Select this option to convent the CAD file into special tool. Forming Select this option to convent the CAD file into forming tool. |
| 3. | This DXF file is imported into the tool inventory and converted to a FM tool. |

| See: | Import AP100 tools into Dr ABE tool inventory |
| --- | --- |
|  | Import Ap100 SP/FM tools into Dr. ABE tool inventory |

### 21.1.4 View Buttons

|  | You can select the way to display the tools and tool information. |
| --- | --- |

| Option | Description |
| --- | --- |
| Tool List | List all the available tools. |
| Tool List +Property | List all the available tools, and display the Tool window. You can select a tool and display its detailed tool information in the Tool window. See: The Tool Window |

| See: | SubInventory Window Toolbar |
| --- | --- |
|  | Range and Shape buttons |
|  | Import Buttons |
|  | Advanced Filter Window |
|  | Machine Type |

### 21.1.5 Advanced Filter Window

Click Search to open the Advanced Filter window. The options in this window allow you to filter the results by Name, Shape, Range, etc. For example, if you place a check mark in the Nibbling check box and select Turret as the tool type. The system will search the current tool inventory and display all the nibbling tools of Turret type.

| See: | SubInventory Window Toolbar |
| --- | --- |
|  | Range and Shape buttons |
|  | Import Buttons |
|  | View Buttons |
|  | Machine Type |

### 21.1.6 Machine Type

|  | Select a machine to display its tool inventory. |
| --- | --- |

| See: | SubInventory Window Toolbar |
| --- | --- |
|  | Range and Shape buttons |
|  | Import Buttons |
|  | View Buttons |
|  | Advanced Filter Window |

## 21.2 Tool Inventory Table

The Tool Inventory table lists information for each tool, such as the Sequence, Shape, Range, Type, etc. You can display the tools by Shape or by Range. The shortcut options allow you to sort, copy, edit the tools, etc.

Tools are categorized into 10 groups. Tools in Gr1 have the highest priority during the tool assignment, while tools in Gr10 have the lowest priority.

Tool Inventory Table Columns

| Column Title | Description |
| --- | --- |
| ID | The ID number of the tool. It is automatically assigned by the system. |
| Name | The tool name. |
| Enable | A check mark indicates the corresponding tool can be assigned. The removal of the check mark will disable the tool assignment. |
| Sequence | The Sequence column displays the sequence numbers of the tools. Tools with smaller sequence numbers will have higher priority than the tools in the same sequence group during the assignment. |
| Shape | Tool shape. |
| Range | The tool guide range. Tool guide ranges from A to M. A tool cannot be placed in a station unless both ranges can match. |
|  | A | 0 to 12.7 mm | B and G | 12.7 mm to 31.75mm |
|  | C and H | 31.75mm to 50.8mm | D | 50.8mm to 88.9 mm |
|  | E | 88.9 mm to 101.6 mm | F | 101.6 to 152.4 mm |
|  | M | More than 152.4 mm |  |  |
| Size X | The X size of the tool. |
| Size Y | The Y size of the tool. |
| Size R | The radios of the corner of RR and CR tools. Size R is specific for RR and CR tools. The following figures indicate the R dimension for these tool types. |
|  | CR Tool | RR Tool |
| Type | Select the type of station that the tool will be placed. Currently only Turret and Attached Tapping options work. |
| Air Blower | If air blower tool exists, place a check mark in the check box. Note: To use this function, you must enable the Air Blower function first. See: Air Blower |
| Shape Sub Code | Supplemental information for contouring tools, nesting tools, etc. Note: When the shape is SQ/OB/CR: Standard, Slot, Nesting When the shape is TP: TPII, TP Unit, TP Tool When the shape is SP： Key, Non-Key, Slot II, Burring Tool (RE/SQ), Burring Tool (RO) When the shape is FM: Key, Non-Key, Slot II When the shape is triangle: Isosceles triangle, Right triangle and others. ※After importing SP/FM/TR, specify the shape sub code. |
| Energy Save Tooling | If NEX tool exists, place a check mark in the check box. Note: To use this function, you must enable the Energy Save function first. See: Energy Save |
| Comment | Tool comments |

Note:

Right-click the column header. And select the item to display by placing a check mark in the corresponding check box.

You can click the Customize. option to display the Tool Inventory Item window. You can place a check mark before the item and display it. You can select one item and click  or button to change its position in the inventory table. You can type a value in the Width of Select Column (in pixels): text box to specify the column width.

| See: | SubInventory Window |
| --- | --- |
|  | Tool Inventory Table Shortcut Menu |
|  | Tool Window |

## 21.3 Tool Inventory Table Shortcut Menu

|  | In the Tool Inventory table, right-lick to open the shortcut menu. The options on the shortcut menu allow you to edit, sort, copy, and append the parts. You can also batch modify the part sequences. Option Description Edit Group Specify the tools of the selected group as standard tools or forming tools. Auto Sort Sort the tools Append Append a new tool to the selected group. The tool window displays the Tool Name, Shape, Size, Guide, etc. See: The Tool Window Copy Use the tool information of the selected tool and create a new tool in the same group. A unique ID will be automatically assigned to the new tool. Linked Copy Use the tool information of the selected tool and create a new associated tool in the same group. The modification of either the original tool or the associated tool will be automatically reflected on the other. Edit Display the Tool window to edit the tool information. See: The Tool Window Delete Delete the tool selected. Remove Link Remove the links between the associated tool and the original tool. Same Sequence Select this option, and all the selected tools will be assigned the same sequence number. Sequence Select this option, and the system will automatically use the consequential numbers to define the sequence numbers for the selected parts. Assign Station Assign the station to the selected tool. See: Assign Station to a Storage |
| --- | --- |

| See: | Edit Group |
| --- | --- |
|  | Auto Sort |

| See: | SubInventory Window |
| --- | --- |
|  | Tool Inventory Table |
|  | Tool Window |

### 21.3.1 Edit Group

Inventory tools can be classified into 10 groups, from Gr1 to Gr10. When sorting tools, tools in Gr1 will be sorted with higher priority.

Right-click one sequence group, and select Edit Group to display the Tool Group Condition window.

Tool Group Condition Options

| Option | Description |
| --- | --- |
| Standard | Specify the tools in this group as standard tools. |
| Downward Forming Process Group | Specify the tools in this group as downward forming tools. And the system will process the parts from the clamped side to the opposite side as the following picture shows. |
| Include All One Direction Tool with in | Type a value in the text box to specify the process range width. The system will process all the parts within that range in one direction. |
| Forming Process Group | Specify the tools in this group as upward forming tools. When you define the tools as upward forming tools, the system will process the parts as follows. The system will perform repositions to avoid damaging the parts. |
| Process the Pre-punch Hole at the Same Time | Select this option, and the system will perform pre-punch hole during the process. |
|  | If this option is not selected, the system will process the parts as follows. |
|  | If this option is selected, the system will process the parts as follows. |
| Repositioning before Grouping Tool Processes | Select this option, and the system will perform reposition before conducting forming process. For example, if the system uses the RO tools in Gr1, RE tools in Gr2 and forming tools in Gr7 to process the following parts, select this option, and the system will process the parts as follows. The symbol indicates the downward forming process. |

| See: | Auto Sort |
| --- | --- |

### 21.3.2 Auto Sort

In the Tool Inventory Table, right-click one sequence group, and select Auto Sort to display the AutoSort Setting window. You can sort the registered tools based on the auto sort settings.

| Option | Description |
| --- | --- |
| Set Priority | Specify the sort orders. |
| Shape=> Size | Select this option, and the system will sort the tools by Shape, and then by Range. |
| Size=> Shape | Select this option, and the system will sort the tools by Range, and then by Shape. |
| Shape Sequence | Specify the sequence to sort the tools by Shape. The system will sort the tools from the shape on the top to the shape on the bottom. |
| Size Sequence | Specify the sequence to sort the tools by Range. The system will sort the tools from the range on the top to the range on the bottom. |
| Auto No. Step | Specify the incremental value for the sequence numbers when sorting the tools. |
| Apply to All Groups | Select this option to apply the Auto Sort Settings to all the groups. |

Example

| 1. | In the Tool Inventory Table, the tools in Gr2 are displayed as follows. |
| --- | --- |
| 2. | Select group 2, and right-click to display the shortcut menu. Select Auto Sort to display the AutoSort Setting window. |
| 3. | In the AutoSort Setting window, specify the settings as follows. |
| 4. | Since tools in group are all RO tools, the system will sort the tools by range from A to C, and the sequence numbers are reset with the incremental step value of 2, and the starting number is 2 |

| See: | Edit Group |
| --- | --- |

## 21.4 Tool Window

To display the Tool window, you can double-click the tool ID of certain tool, or right-click on the Tool Inventory table, and select Edit from the shortcut menu.

The tool window allows you to append or modify the tool information. It displays the Tool Name, Shape, Size, Guide, Tool Type, Sub Code, and other information.

| See: | Basic Information |
| --- | --- |
|  | Attribute 1 |
|  | Attribute 2 |
|  | Codes |
|  | PDC Operation |

| See: | SubInventory Window |
| --- | --- |
|  | Tool Inventory Table |
|  | Tool Inventory Table Shortcut Menu |

### 21.4.1 Basic Tool Information

The Basic Tool Information section of the Tool window display the basic tool information, such as Tool Name, Shape, Size, Guide, Tool Type, Sub Code, etc.

| Option | Description |
| --- | --- |
| Tool Name | The tool name. |
| Shape | Tool shape. |
| Guide | The tool guide. Tool guide ranges from A to M. A tool cannot be placed in a station unless both ranges can match. |
|  | A | 0 to 12.7 mm | B | 12.7 mm to 31.75mm |
|  | C | 31.75mm to 50.8mm | D | 50.8mm to 88.9 mm |
|  | E | 88.9 mm to 101.6 mm | F | 101.6 to 152.4 mm |
|  | M | More than 152.4 mm |  |  |
| Size X | The X size of the tool. |
| Size Y | The Y size of the tool. |
| Size R | The radius of the corner of RR and CR tools. Size R is specific for RR and CR tools. The following figures indicate the R dimension for these tool types. |
|  | CR Tool | RR Tool |
| Comment | Tool comments |
| Air Blower | If air blower tool exists, place a check mark in the check box. Note: To use this function, you must enable the Air Blower function first. See: Air Blower |
| Tool Type | Select the type of station that the tool will be placed. Currently only Turret and Attached Tapping options work. |
| Sub Code | Supplemental information for contouring tools, nesting tools, etc. Note: When the shape is SQ/OB/CR: Standard, Slot, Nesting When the shape is TP: TPII, TP Unit, TP Tool When the shape is SP: Key, Non-Key, Slot II, Burring Tool (RE/SQ), Burring Tool (RO) When the shape is FM: Key, Non-Key, Slot II When the shape is triangle: Isosceles triangle, Right triangle and others. ※After importing SP/FM/TR, specify the shape sub code. |
| Share Setting | Share the same tool conditions among the machines that use the same machine drivers. See: Share the tool conditions among machines |
| NEX | If NEX tool exists, place a check mark in the check box. Note: To use this function, you must enable the Energy Save function first. See: Energy Save |
| Enable | A check mark indicates the corresponding tool can be assigned. The removal of the check mark will disable the tool assignment. |

| See: | Attribute 1 |
| --- | --- |
|  | Attribute 2 |
|  | Codes |
|  | PDC Operation |

#### 21.4.1.1 Share the tool conditions among machines

The Share Setting button in the basic tool information section allows you to share the same tool conditions among machines that use the same machine drivers

Example

| 1. | We have two EM machines, EM-111 and EM2510. |
| --- | --- |
| 2. | Select Sub Inventory under Public to display ToolInventory file icon in the Preference File pane. |
| 3. | Double-click the ToolInventory file icon to display the SubInventory window. |
| 4. | Double-click the ID cell of one tool to display the Tool window. The Tool window lists all the available punch and combination machines. Click the tab of one machine, for example, EM2510 machine. And then click Share Setting button. |
| 5. | The Share Setting lists the machines that have the same machine driver as EM2510 machine. Select the machine you want to share the tool conditions. Click Close to continue. |
| 6. | EM2510 and EM-111 share the same tab, which means both machines share the same tool conditions. |
|  | Note: You can click Share Setting button, and remove the check mark from the check box of the shared machines to stop sharing the tool conditions. |

### 21.4.2 Attribute 1

The options in the Attribute 1 panel allow you to specify the tool conditions. You can specify whether adapter can be used or not when placing a tool in the station with a larger range, You can specify the Max Lap Amount for the tool assignment, and you can specify the usage of the tool, for example, whether the tool can be used as a nibbling tool or not.

| Option | Description |
| --- | --- |
| Allow Use Adapter | When we place a tool in a station, the tool range (or the guide range) should match the station range, otherwise the tool cannot be installed properly. Select this option if sleeve can be used to place tools of one range to the stations of larger range. |
| Shear Angle | Place a check mark in the check box if the tool can be used as a shearing tool. You can specify the shearing angle in the text box. Note: This option is only available for RE, RO, RR and SQ tools. If a shearing tool has shear angle, it can reduce the punch pressure and the chances that tools get damaged when processing thick material will be small. |
|  | A tool without shear angle A tool with shear angle |
| Allow use Shorter Edge | This option is only available for rectangle tools. When shearing or punch a line, the system will use the longer edge of the tool to process. |
|  | If this option is selected, the system will use the shorter edge of this rectangle tool to process if no other appropriate tools can be used. |
| Max Lap Amount (%) | Specify the maximum overlap percentage for the rectangle and square tools. Note: If the tool length x (1+1-A%) is less than the line length, the tool can be assigned. If the tool length x (1+1-A%) is more than the line length, the tool cannot be assigned to process the line. |
| Sheet Saver | When a tool is assigned to process a pattern, to prevent the tool guide colliding with the clamps, the minimum distance from the tool hit center to the material edge will be DZ Y/2 + Clamp Length, otherwise the system will have to perform repositions to avoid colliding. This option is available for the nesting tools. Sheet Saver allows us to type a value in the text box to shorten the minimum distance mentioned above, so that reposition can be avoided. See: Specify the Sheet Saver for the nesting tools to avoid reposition |
| Nibbling | Select this option, and the selected tool can be used as a nibbling tool. You can type a value in the text box to specify the pitch value. |
| Match Tool Shape | Select this option to make the SP tool match the pattern. |
| Special Pitch | You can type a value in the text box to specify the pitch for nibbling process. Note: If the Special pitch is not defined here, the system will use the pitch settings defined in Tool Lap Value windows. |
| Punch Pierce | Select this option, and the selected tool can be used to perform piercing process. |
| Only Slit & Single Hit | Select this option, the tool selected can only be assigned to punch slit and perform single hit. |
| Auto Index | Select this option, and the selected tool can be placed in the AI-Station. |

| See: | Basic Information |
| --- | --- |
|  | Attribute 2 |
|  | Codes |
|  | PDC Operation |

#### 21.4.2.1 Specify the Sheet Saver for the nesting tools to avoid reposition

For the nesting tools, you can type a value in the Sheet Saver text box to shorten the minimum distance from the tool hit center to the material edge, so that reposition can be avoided. See: Sheet Saver

Example

| 1. | To process the following line segments close to the clamp, the system will assign the tool of Station 224 of E range to process. We notice that the Y dimension of the Station 224 (DZY) or the guide diameter is 116.665. If the tool in this station is assigned to process a pattern. To prevent the tool guide colliding with the clamps, the minimum distance from the tool hit center to the material edge will be DZ Y/2 + Clamp Length. In this case, the minimum distance will be DZ Y/2 + Clamp Length=116.665/2 + 10=68.333. While the actual distance from the tool hit center to the sheet edge is 65, therefore the system will perform a reposition when processing the line segments. Note: You must place a check mark in the Avoid DZ check box in the Clamp Avoidance tab of the PunchSequence window. |
| --- | --- |
|  | Before Reposition After Reposition |
| 2. | If we put a nesting tool in the same station to process the same patterns. |
| 3. | When the system assign the same tool to process the line segments, although the distance from the tool hit center to the sheet edge is still 68, while the minimum distance has changed to DZ Y/2 + Clamp Length - Sheet Saver=116.665/2 + 10 - 40=28.333. The system will process the following line segments without repositioning. |

Note:

| 1. | Only RE, RR and OB tools can be defined as nesting tool. |
| --- | --- |
| 2. | If a tool is defined as the nesting tool, and Sheet Saver has been specified, the minimum distance that the reposition won’t be conducted will vary with the tool hit angle. |
|  | Let’s take the tool in the station of E range for example. The Sheet Saver is set to 40. |
|  | If the tool hit angle is 0 degree, the minimum distance will be 116.665/2 –40 +10=28.333 | If the tool hit angle is 90 degree, Sheet Saver setting has no effect on the minimum distance, which will be 116.665/2 +10=58.333 | If the tool hit angle is 145 degree, the minimum distance will be 116.665/2.8=41.667 |

| See: | Basic Information |
| --- | --- |
|  | Attribute 1 |
|  | Attribute 2 |
|  | Codes |
|  | PDC Operation |

### 21.4.3 Attribute 2

The options in Attribute 2 panel allow you to specify the clearance, process angle, sequence group, sequence number and other settings for a tool. In addition, you can also specify the process direction, starting point for each tool in the Advance window.

| Option | Description |
| --- | --- |
| Clearance | Specify up to 5 die clearances for the tool selected. |
|  | Selecting the proper die clearance is very important. The die clearance affects tool life, tonnage requirements and the burr. Meanwhile it varies with the material thickness. |
| Process Angle | Specify available angles for a tool. And the tool can only be used in the specified angles for the punching process. |
| C Axis Sort Off | Place a check mark to disable the C Axis Sort function, and the system won’t use the selected tool to process the parts by angle. See AI Tool Angle Sort in the Punch Sequence panel of CombinationSequence window. |
| Escape | This option is used for forming down tools. The system will generate G70 to instruct the machine to shift the sheet without punching. |
| Proc. Gr. | Edit the Sequence Group of the tools selected. |
| Order | Edit the Sequence No of the tool selected. |
| Advance | Click the Advance button to open the Customize window. You can specify the Start Position, Direction for the tool selected. See: The Customize Window |

| See: | Basic Information |
| --- | --- |
|  | Attribute 1 |
|  | Codes |
|  | PDC Operation |

#### 21.4.3.1 The Customize Window

Click the Advance button in the Attribute 2 panel to open the Customize window. You can specify the Start Position, Direction for the tool selected.

| Option | Description |
| --- | --- |
| Start Position | Specify the starting position for the tool selected. If you remove the check mark from the Start Position check box, the system will automatically determine the starting position according to the shortest path. |
| Direction | Specify the process direction for the tool selected. |
|  | If you remove the check mark from the Direction check box, the system will determine the process direction according to the shortest path. |
| X | Process the patterns in the X direction. |
| Y | Process the patterns in the Y direction. |
| One Direction | Select this option, and the system will process the patterns in one direction. It is strongly recommended to select this option for the forming down tool, so that the system can prevent the die of the forming down tool going into the forming parts. |
| Divide Sheet for Optimize | This option is used to divide the processing range into equal areas for the sequence. The system will punch the patterns in the first area and then will process the patterns in the adjacent area according to the direction specified in the Direction section. |
|  | Note: The Number of Divide option is only available when you select either X or Y direction in the Direction section. |

Example

| 1. | We will assign a RO tool to process the holes with a single hit. In the Tool Inventory table, select this RO tool and edit the process conditions in the Customize window. |
| --- | --- |
| 2. | If you specify the Start Position as follows. |
| 3. | The system will process the holes as follows. |

### 21.4.4 Codes

The options in the Codes tab allow you to specify the M code value and the output location when the selected tool is assigned to process the patterns.

| Item | Description |
| --- | --- |
| ON/OFF | Place a check mark in the corresponding check box if you want to specify the value and location for an M code. |
| Name | The name of the M code See: M Code |
| Value 1/Value 2 | Specify the output value. |
| Code Output Time | Select the position to output M code. Select Before to output the code before the corresponding tool is assigned. Select After to output the code after the corresponding tool is assigned. Select After All to output the code after the last hit of the corresponding tool is performed. |
| Material Setting | Specify the M code based on the material and thickness. You can select the material by placing a check mark in the corresponding check box. Type the Min Thickness and Max Thickness in the corresponding cells. The system will output the corresponding M codes based on the material and the thickness you have defined. |
| View Details | Click this button to display all the M codes and the relevant options in the Details of Codes Setting window. |

| See: | Basic Information |
| --- | --- |
|  | Attribute 1 |
|  | Attribute 2 |
|  | PDC Operation |

#### 21.4.4.1 M Codes

In the Codes tab, you can specify the value and location to output the M code when the corresponding tool is assigned to process the patterns.

| Code | Description |
| --- | --- |
| FEED RATE (1-4) | Specify the axis feed rate for the selected tool. The system will generate F1 to F4 in the NC code to control the feed rate. F1 is the fastest rate while F4 is the slowest. The system will generate the F code at the selected location each time the tool is assigned. Note: If you do not enable this function, the system will only generate the default feed rate F1. When the tool to which you have assigned a feed rate has finished punching, the system will generate F1 to restore the machine to the default condition. |
| FEED RATE CANCEL (F1) | Cancel the feed rate you have specified and return the feed rate to F1. |
| MILD MODE ON M120 | Select this option to turn on the acceleration/deceleration control in the X/Y axis. |
| MILD MODE OFF M121 | Select this option to turn off the acceleration/deceleration control in the X/Y axis. |
| PUNCH W/FLAT EDGE (M500) | Generate an M500 to specify the punching mode with a standard punch of a flat edge. |
| PUNCH WITH SHEAR ANGLE (M501) | Generate M501 to specify the punching mode with a standard punch having a shear angle. |
| PROGRAM STOP | Output an M00 program stop to stop the machine during operation. A stop sign appears on the sheet at the location of the last hit. |
| OPT PROGRAM STOP | Output an optional M01 stop command in the desired location of a program. A stop sign appears on the sheet at the location of the last hit. M01 is similar to M00. OPT PROGRAM STOP requires intervention from the machine operator. The machine will stop operation when it executes M01 command, and the operator must press the Opt Stop Key on the NC control panel to continue the process. |
| PUNCH DELAY ON (M08) | Generate M08 to enable a punch delay for the tool. Punch Delay Mode is mainly used for forming process, marking and knockout. It is also used for processing thick sheets. If you want to disable the punch delay after the tool is assigned, select PUNCH DELAY OFF or PRESS MODE CANCEL (M13) for the selected tool. |
| PUNCH DELAY OFF (M09) | Generate M09 to cancel the punch delay for the tool. |
| PRESSURE IGNORE ON (M694) | The system uses pressure sensor to detect the completion of the sheet process. Select this option and the system will generate M694 to instruct the machine to ignore the signal from the pressure sensor, and the machine will keep punching the sheet with a decelerated speed until the punch contacts the die. If you want to disable the Pressure Ignore function after the tool is assigned, select PRESSURE IGNORE OFF or PRESS MODE CANCEL (M13) for the selected tool. |
| PRESSURE IGNORE OFF (M695) | Generate M695 to cancel the pressure ignore mode after the tool is assigned. |
| FORMING MODE + M08 (M510-M559, M800-M999) | Specify the M code for the selected forming tool. The M code value ranges from 510 to 559 and from 800 to 999. Select this option, and when this forming tool is used, the system will generate the corresponding M Code and M08. |
|  | Note: Do not select FORMING MODE + M08 (M510-M559, M800-M900) and FORMING MODE - M08 (M510-M559, M800-M900) at the same time. This option is only available for the forming tools |
| FORMING MODE - M08 (M510-M559, M800-M999) | Specify the M code for the selected forming tool. The M code value ranges from 510 to 559 and from 800 to 999. Select this option, and when this forming tool is used, the system will generate the corresponding M Code and M08 is not generated. |
|  | Note: Do not select FORMING MODE + M08 (M510-M559, M800-M900) and FORMING MODE - M08 (M510-M559, M800-M900) at the same time. This option is only available for the forming tools |
| MARKING MODE + M08 (M560-M569) | Specify the M code for the selected marking tool. It allows you to mark parts using center punch tools. You can use the tools to mark characters on the sheet. The M code range value ranges from 560 to 569. The codes specified here will be used as the standard Marking Code. Select this option, and when this marking tool is used, the system will generate the corresponding M Code and M08. |
|  | Note: Do not select MARKING MODE + M08 (M560-M569) and MARKING MODE - M08 (M560-M569) at the same time. This option is only available for the CP (Center Punch) tools. |
| MARKING MODE - M08 (M560-M569) | Specify the M code for the selected marking tool. It allows you to mark parts using center punch tools. You can then use the tools to mark characters on the sheet. The M code value ranges from 560 to 569. The codes specified here will be used as the standard Marking Code. Select this option, and when this marking tool is used, the system will generate the corresponding M Code and M08 is not generated. |
|  | Note: Do not select MARKING MODE + M08 (M560-M569) and MARKING MODE - M08 (M560-M569) at the same time. This option is only available for the CP (Center Punch) tools. |
| KNOCK OUT MODE + M08 (M502-M505)(M570-M575) | Specify the M code for knockout tools. The M code value ranges from 502 to 505 and from 570 to 575. Please refer to your programming manual for more information. Select this option, and when this knockout tool is used, the system will generate the corresponding M Code and M08. |
|  | Note: If you need to cancel the knock out mode after the corresponding tool is assigned, select PRESS MODE CANCEL and select the After All as the Code Output Time. |
| KNOCK OUT MODE - M08 (M502-M505)(M570-M575) | Specify the M code for knockout tools. The M code value ranges from 502 to 505 and from 570 to 575. The M code value for some machines ranges from 570 to 575. Please refer to your programming manual for more information. Select this option, and when this knockout tool is used, the system will generate the corresponding M Code and M08 is not generated. |
|  | Note: If you need to cancel this mode after the tool is used, select PRESS MODE CANCEL and select After All as the Code Output Time. |
| PRESS MODE CANCEL (M13) | Generate an M13 to cancel the press modes for the selected tool. Press Modes are modes defined for a specific tool, such as MILD MODE, PUNCH DELAY, PRESSURE IGNORE, etc. |
| DWELL TIME G04 | Select this option to generate the G code of dwell time. |
| SLOTTING MODE (M506-M509) | Select this option to generate the slotting mode code. |
| SURFACE TABLE FUNCTIONALITY ON (M288) | Generate an M288 to instruct the machine to move the table downwards, so that there will be no interference with the turret rotation and axis movement for the downward forming process. |
|  | Note: If you want to disable this function after the corresponding tool is used, select SURFACE TABLE FUNCTIONALITY OFF (M289) or PRESS MODE CANCEL (M13) for the selected tool. |
| SURFACE TABLE FUNCTIONALITY OFF (M289) | Generate an M289 to cancel the Surface Table Functionality for the selected tool. |
| OUTPUT M687 AFTER FORMING | Select this option to output M687 after forming. |
| P & FM code | Specify the M code for the forming conditions. The M code value ranges from 590 to 592, and each represents one of the following forming conditions. M590: Punch moves and die doesn’t. M591: Punch moves and Die also moves. M592: Die moves and Punch doesn’t. Before using this option, please select P/F Structure in Machine Set window, and specify the FORMING MODE + M08 (M510-M559) and PRESS MODE CANCEL (M13). |

### 21.4.5 PDC Operation

The options in this panel allow you to specify the tool type relevant to PDC operation.

| Option | Description |
| --- | --- |
| Ordinary | Define the ordinary tools are defined as resident tools, which will remain in the turret after punching |
| Non-resident | Define the tool as a non-resident tool, which will return to the PDC when punching process is done. If several non-resident tools (the same range) are used to process one sheet, all these non-resident tools will have the same station number. |
| Substitute | Define the tool as a substitute tool. After the punching process is performed, and the non-resident tool returns to PDC, the substitute tools will be placed in the turret so that no stations will be empty. These substitute tools have higher priority to be used for the sheet. |

| See: | Basic Information |
| --- | --- |
|  | Attribute 1 |
|  | Attribute 2 |
|  | Codes |

# Chapter 22: Remnant/Skeleton Name

The Remnant/Skeleton window allows you to specify the names for remnant and skeleton material.

To open the Remnant/Skeleton window:

| 1. | Click any preference button in the main window to display the Preference window. |
| --- | --- |
| 2. | In the Tree View pane, select Remnant/Skeleton Name under Public. |
| 3. | In the Preference File pane, double-click the Remnant/Skeleton Name icon to display the Remnant/Skeleton Name window. This window has two panels: the Remnant Name panel and the Skeleton panel. |

| See: | Remnant Name |
| --- | --- |
|  | Skeleton Name |

## 22.1 Remnant Name

The options in the Remnant panel allow you to configure the names for the remnants.

You can choose the items that constitute the remnant name, assign a name automatically, or specify a special name.

| See: | Remnant Name Items |
| --- | --- |
|  | Special Name |
|  | Date Format |
|  | Sequence Number |
|  | Remnant Name |

### 22.1.1 Remnant Name Items

|  | In the Sheet Name Items list, you can select the items to constitute the remnant name. The selected items will appear in the Remnant Name: text box. |
| --- | --- |

| Items | Description |
| --- | --- |
| Special Name | You can type a specify name in the text box to define the remnant name. |
| Machine Name | The name of the machine |
| Material Name | The name of the material. |
| Thickness | The thickness of the sheet. |
| Rectangle X | The X dimension of the remnant. |
| Rectangle Y | The Y dimension of the remnant. |
| Rectangle Area | The rectangle area of the remnant |
| Create Date | The date when the remnant is created. |
| Sequence No | Select this item and the system will use a series of sequential numbers to name the remnants. Make sure to type a starting sequence number in the Start Number: text box. See: Sequence Number |
| Material Type | The material type. |
| Sheet name | The sheet name. |

| See: | Special Name |
| --- | --- |
|  | Date Format |
|  | Sequence Number |
|  | Remnant Name |

### 22.1.2 Special Name

To use the Special Name to define the remnant names, you must select Special Name from the Remnant Name Items list.

You can type a special name in the text box or select a name from the drop down list.

Note:

When you type a number in the Special Name: text box, the system will regard it as characters. No change will be made to create the next remnant name.

| See: | Remnant Name Items |
| --- | --- |
|  | Date Format |
|  | Sequence Number |
|  | Remnant Name |

### 22.1.3 Date Format

To use Data Format to define the remnant names, you must select Data Format from the Remnant Name Items list.

You can specify the date format. Y = Year, M = Month and D = Date.

| See: | Remnant Name Items |
| --- | --- |
|  | Special Name |
|  | Sequence Number |
|  | Remnant Name |

### 22.1.4 Sequence Number

This section allows you to specify the starting sequence number.

The Sequence Number item is selected by default and the "&[Sequence NO]" cannot be removed from the Remnant Name: text box.

| See: | Remnant Name Items |
| --- | --- |
|  | Special Name |
|  | Date Format |
|  | Remnant Name |

### 22.1.5 Remnant Name

Select one item from the Remnant Name Items list, and the selected item will appear in the Remnant Name: text box.

You can also edit the contents if necessary.

Notes:

- The Sequence Number item is selected by default and the "&[Sequence NO]" cannot be removed from the Remnant Name: text box.

- You cannot use the following characters, such as   \, /, :, *, ?, ", <, >, or |, to specify the remnant name.

Example

| 1. | In the Remnant Name panel, select the following items to constitute the remnant name. Set the Sequence Number to 0001. |
| --- | --- |
| 2. | In the Preference window, double-click the Nesting icon to display the Nesting window. Click Material Selection tab, and select Create Remnant and Vertical Cut in the Reusable Sheet area. |
| 3. | Load parts as follow, and assign different Part ID to those parts so that those parts will be nested in three sheets. |
| 4. | After auto execution, select all the three sheets. Right-click and select Save NC data from the shortcut menu. |
| 5. | Specify the O number, and click OK to continue. |
| 6. | After specifying the place to save the NC data, a Save Confirmation window displays. Click Save to continue |
| 7. | The remnants that the system created are saved in the Material Manager window. Their names are made up of the creation data, special name, the X size of the remnant and the sequence number. |

| See: | Remnant Name Items |
| --- | --- |
|  | Special Name |
|  | Date Format |
|  | Sequence Number |

## 22.2 Skeleton Name

The options in the Skeleton panel allow you to configure the names for the skeletons.

You can choose the items that constitute the skeleton name, assign a name automatically, or specify a special name.

| See: | Skeleton Name Items |
| --- | --- |
|  | Special Name |
|  | Date Format |
|  | Sequence Number |
|  | Skeleton Name |

### 22.2.1 Skeleton Name Items

|  | In the Skeleton Name Items list, you can select the items to constitute the skeleton name. The selected items will appear in the Skeleton Name: text box. |
| --- | --- |

| Items | Description |
| --- | --- |
| Special Name | You can type a specify name in the text box to define the skeleton name. |
| Machine Name | The name of the machine |
| Material Name | The name of the material. |
| Thickness | The thickness of the sheet. |
| Rectangle X | The X dimension of the skeleton. |
| Rectangle Y | The Y dimension of the skeleton. |
| Rectangle Area | The rectangle area of the skeleton |
| Create Date | The date when the skeleton is created. |
| Sequence No | Select this item and the system will use a series of sequential numbers to name the skeletons. Make sure to type a starting sequence number in the Start Number: text box. See: Sequence Number |
| Material Type | The material type. |
| Sheet name | The sheet name. |

| See: | Special Name |
| --- | --- |
|  | Date Format |
|  | Sequence Number |
|  | Skeleton Name |

### 22.2.2 Special Name

To use the Special Name to define the skeleton names, you must select Special Name from the Skeleton Name Items list.

You can type a special name in the text box or select a name from the drop down list.

Note:

When you type a number in the Special Name: text box, the system will regard it as characters. No changes will be made to create the next skeleton name.

| See: | Skeleton Name Items |
| --- | --- |
|  | Date Format |
|  | Sequence Number |
|  | Skeleton Name |

### 22.2.3 Date Format

To use Data Format to define the remnant names, you must select Data Format from the Skeleton Name Items list.

You can specify the date format. Y = Year, M = Month and D = Date.

| See: | Skeleton Name Items |
| --- | --- |
|  | Special Name |
|  | Sequence Number |
|  | Skeleton Name |

### 22.2.4 Sequence Number

This section allows you to specify the starting sequence number.

The Sequence Number item is selected by default and the "&[Sequence NO]" cannot be removed from the Skeleton Name: text box.

| See: | Skeleton Name Items |
| --- | --- |
|  | Special Name |
|  | Date Format |
|  | Skeleton Name |

### 22.2.5 Skeleton Name

Select one item from the Skeleton Name Items list, and the selected item will appear in the Remnant Name: text box. You can also edit the contents if necessary.

Notes:

- The Sequence Number item is selected by default and the "&[Sequence NO]" cannot be removed from the Skeleton Name: text box.

- You cannot use the following characters, such as   \, /, :, *, ?, ", <, >, or |, to specify the skeleton name.

Example

| 1. | In the Skeleton Name panel, select the following items to constitute the skeleton name. Set the Sequence Number to 0001. |
| --- | --- |
| 2. | In the Preference window, double-click the Nesting icon to display the Nesting window. Click Material Selection tab, and select Create Skeleton Sheet in the Reusable Sheet area. |
| 3. | Load parts in three different sheets, and assign different Part ID to those parts so that those parts will be nested in three sheets. |
| 4. | After auto execution, select all the three sheets. Right-click and select Save NC data from the shortcut menu |
| 5. | Specify the O number, and click OK to continue. |
| 6. | After specify the place to save the NC data, a Save Confirmation window displays. Click Save to continue. |
| 7. | The skeletons that the system created are saved in the Material Manager window. Their names are made up of the special name, creation data, and the sequence number. |

| See: | Skeleton Name Items |
| --- | --- |
|  | Special Name |
|  | Date Format |
|  | Sequence Number |

# Chapter 23: Turret Type

You can create a new turret type file to meet your special needs, and modify the current turret specification in the Turret Type window.

To open the Turret Type window

| 1. | Click the Punch Tool Assign Preference button in the main window to open the Preference window. |
| --- | --- |
| 2. | In the left Tree View pane, select next to the Public to expand submenu and click Turret Type. |
| 3. | In the Preference File pane, click one turret file to open the Turret Type window. |

| See: | Turret Type Window Items |
| --- | --- |
|  | Create or Remove a Turret Type |
|  | Adding or Deleting a Station |
|  | Append or Remove a Dead Zone |

## 23.1 Turret Type Window Items

The Turret Type window lists information for each station, such as the station range, dead zone range, etc. You can display the stations by Station Range and modify station settings.

Toolbar Buttons

Click one button to display the stations of specified range, click All to display all the stations.

Turret Type Table Columns

| Column Title | Description |
| --- | --- |
| ID | Display the ID number of the station. It is automatically assigned by the system. |
| Station | Display the station number. |
| Location | Display the location of station. 1 indicates the station is on the inner track, 2 indicates the station is on the center track, while 3 indicates the station is on the outer track. |
| Original | Place a check mark in this check box, which indicates this station is the original station. The turret angle of the original station is 0. |
|  | Note: |
|  | Only one station can be set as original station. |
| Range | Select the station size from drop-down list. Usually the station size range are specified as follows: |
|  | A | 0 to 0.5 inch | B and G | 0.5 to 1.250 inch |
|  | C and H | 1.250 to 2.000 inch | D and I | 2.000 to 3.500 inch |
|  | E and J | 3.500 to 4.500 inch | F and K | 4.500 to 6.000 inch |
|  | M | 6.000 to 999.999 inch |  |  |
|  | Note: G, H, I, J, K are for the AI (Auto-Index) Stations. |
| OTX | Display the X-axis distance between the station position and the original point. Usually it is set to 0. |
| OTY | Display the Y-axis distance between the station position and the original point. Usually for Amada machines, it is 40 for the station on the inner track, 0 for the station on the center track, and –40 for the station on the outer track. |
| AI | Place a check mark in this check box, which indicates this station is an Auto Index station. |
| Key | Place a check mark in this check box, which indicates this station is a keyed station. Only shaped tools, such as rectangle and square tools, can be installed in keyed stations. Non-keyed stations are available for round, center punch and burring tools. |
| ATCZone | Select the ATC zone from drop-down list for each station, if the machine is equipped with ATC. |
| Exchange | Display the station number when tools are exchanged. |
| Type | Select a station type from drop-down list. Usually Turret is selected for NCT machines. |
| Turret Angle | Display the station angle. The angle of the original station is 0 degree. |
| DZ | Display the dead zone number. See: Dead Zone of the Station |
| DZX | Display the X range of the Dead Zone. |
| DZY | Display the Y range of the Dead Zone. |

| See: | Create or Remove a Turret Type |
| --- | --- |
|  | Adding or Deleting a Station |
|  | Append or Remove a Dead Zone |

## 23.2 Create or Remove a Turret Type

To create a new empty turret type file

| 1. | Select the Turret Type under Public in the left Tree View pane. |
| --- | --- |
| 2. | Right-click to display the shortcut menu. Select New to Turret Type Preference. |
| 3. | A new turret type file “New “ is created. You can rename the file and click it to display the correlative information in the Display Area pane where you can add stations. See: Adding or Delete a Station. |

To remove a turret type:

| 1. | In the top Preference File pane, right click a turret type you want to delete and a shortcut menu will display. |
| --- | --- |
| 2. | Select Delete and a message box will appear. |
| 3. | Click OK button. |

| See: | Turret Type Window Items |
| --- | --- |
|  | Adding or Deleting a Station |
|  | Append or Remove a Dead Zone |

## 23.3 Adding or Deleting a Station

Click a turret type in the Preference File pane and the correlative stations information will display in the Display Area pane below. Alternatively you can double click a turret type, the Turret Type window will appear.

Double-click the Station cell in the last row, and type a number to define the station number. After specifying the relevant station information, click <Enter> to confirm your changes

Note:

The station number you type must be unique; otherwise the system will display following warning message.

To delete a station, right click the station you desire and a shortcut menu will appear.

Select Delete and a message box will prompt.

Click Yes button to delete the selected station.

| See: | Turret Type Window Items |
| --- | --- |
|  | Create or Remove a Turret Type |
|  | Append or Remove a Dead Zone |

## 23.4 Append or Remove a Dead Zone

In the Turret Type window, you can append or remove a dead zone for a station.

Right click a station you desire and a shortcut menu appear.

| Shortcut Menu Option | Description |
| --- | --- |
| Append Dead Zone | Select this option to display the Dead Zone window, where you can add or modify a dead zone range for a station. |
|  | Select a dead zone and click Add button to assign the dead zone for the selected station. |
| Remove Dead Zone | Select this option to delete the dead zone settings for the selected station. A message box will prompt. |
|  | Click Yes button to confirm. |

| See: | Turret Type Window Items |
| --- | --- |
|  | Create or Remove a Turret Type |
|  | Adding or Deleting a Station |

# Chapter 24: Turret Type (PDC)

You can create a new turret type file to meet your special needs, and modify the current turret specification in the Turret Type (PDC) window.

To Open the Turret Type (PDC) window

| 1. | Click the Punch Tool Assign Preference button in the main window to open the Preference window. |
| --- | --- |
| 2. | In the left Tree View pane, select next to the Public to expand submenu and click Turret Type (PDC). |
| 3. | In the Preference File pane, click one turret file to open the Turret Type (PDC) window. |

| See: | Turret Type (PDC) Window Items |
| --- | --- |
|  | Create or Remove a PDC Turret Type |
|  | Adding or Deleting a PDC Station |
|  | Append or Remove a Dead Zone |

## 24.1 Turret Type (PDC) Window Items

The Turret Type (PDC) window lists information for each station, such as the Location, Range, Location Angle, etc. You can display the stations by Station Range and modify station settings.

Toolbar Buttons

Click one button to display the stations of specified range, click All to display all the stations.

Turret Type Table Columns

| Column Title | Description |
| --- | --- |
| ID | Display the ID number of the PDC station. It is automatically assigned by the system. |
| Station | Display the station number of PDC storage. |
| Location | Display the location number of the PDC stations. There are 9 locations. |
| Range | Specify the station size. Usually the station sizes are as follows: |
|  | A | 0 to 0.5 inch | B and G | 0.5 to 1.250 inch |
|  | C and H | 1.250 to 2.000 inch | D and I | 2.000 to 3.500 inch |
|  | E and J | 3.500 to 4.500 inch | F and K | 4.500 to 6.000 inch |
|  | M | 6.000 to 999.999 inch |  |  |
|  | Note: |
|  | G, H, I, J, K are for the AI (Auto-Index) Stations. |
| Type | Select a station type from drop-down list. |
| OTX | Display the X-axis distance between the origin point and the storage position. |
| OTY | Display the Y-axis distance between the origin point and the storage position |
| Key | Place a check mark in this check box, which indicates that this station is a keyed station. Only shaped tools, such as rectangles and squares, can be installed in keyed stations. Non-keyed stations are available for round, center punch and burring tools. |
| Location Angle | Display the location station angle. The angle of the original station is 0 degree. |
| DZ | Display the Dead Zone number |
| DZX | Display the X range of the Dead Zone. |
| DZY | Display the Y range of the Dead Zone. |

| See: | Create or Remove a PDC Turret Type |
| --- | --- |
|  | Adding or Deleting a PDC Station |
|  | Append or Remove a Dead Zone |

## 24.2 Create or Remove a PDC Turret Type

To create a new empty turret type (PDC) file

| 1. | Select the Turret Type (PDC) under Public in the left Tree View pane. |
| --- | --- |
| 2. | Right-click to display the shortcut menu. Select New to Turret Type (PDC) Preference. |
| 3. | A new turret type file “New “ is created. You can rename the file and click it to display the correlative information in the Display Area pane where you can add stations. See: Adding or Deleting a PDC Station. |

To remove a turret type (PDC):

| 1. | In the top Preference File pane, right click a turret type you want to delete and a shortcut menu will display. |
| --- | --- |
| 2. | Select Delete and a message box will appear. |
| 3. | Click OK button. |

| See: | Turret Type (PDC) Window Items |
| --- | --- |
|  | Adding or Deleting a PDC Station |
|  | Append or Remove a Dead Zone |

## 24.3 Adding or Deleting a PDC Station

Click a turret type in the Preference File pane and the correlative stations information will display in the Display Area pane below. Alternatively you can double click a turret type, the Turret Type (PDC) window will appear.

Double-click the Station cell in the last row, and type a number to define the station number. After specifying the relevant station information, click <Enter> to confirm your changes

Notes:

The station number you type must be unique; otherwise the system will display a warning message.

To delete a station, right click the station you desire and a shortcut menu will appear.

Select Delete and a message box will prompt.

Click Yes button to delete the selected station.

| See: | Turret Type (PDC) Window Items |
| --- | --- |
|  | Create or Remove a PDC Turret Type |
|  | Append or Remove a Dead Zone |

## 24.4 Append or Remove a Dead Zone

In the Turret Type (PDC) window, you can append or remove a dead zone for a station.

Right click a station you desire and a shortcut menu appear.

| Option | Description |
| --- | --- |
| Append Dead Zone | Select this option to display the Dead Zone window, where you can add or modify a dead zone range for a station. |
|  | Select a dead zone and click Add button to assign the dead zone for the selected station. |
| Remove Dead Zone | Select this option to delete the dead zone settings for the selected station. A message box will prompt. |
|  | Click Yes button. |

| See: | Turret Type (PDC) Window Items |
| --- | --- |
|  | Create or Remove a PDC Turret Type |
|  | Adding or Deleting a PDC Station |

# Chapter 25: Result View

The main window will expand and display the results when the nesting process is complete.

In the Result View area, you can preview many nesting details, such as utilization, time study and the sheet layout, etc.

You can also manually edit the nesting result and generate new NC code here until you are satisfied.

Example

| 1. | Right-click the Auto Execute button in the main window and select Auto Execute (Nesting) from the shortcut menu, the system will run in sheet mode. Alternatively, you can select Make Sheet in the Nesting Schedule window or click the Auto Execute button directly to perform the same action. |
| --- | --- |
|  | The following window appears when the sheet mode nesting process is complete. |
| 2. | Right-click the Auto Execute button and select Auto Execute (Individual Part) from the shortcut menu, the system will run in part mode. Alternatively, you can select Make Part in the Nesting Schedule window to perform the same action. |
|  | The following window appears when the part mode nesting process is complete. |
| 3. | Right-click the Auto Execute button and select Auto Execute (Pre-Nesting) from the shortcut menu, the system will run in pre-nesting mode. |
|  | The following window appears when the pre-nesting process is complete. |

| See: | Nesting Result List |
| --- | --- |
|  | Part Layout Shortcut Options |
|  | Information Panel |

## 25.1 Nesting Result List

Nesting Result List displays various nesting information, such as Sheet Name, Material Type, Sheet Size, Utilization, Time Study, etc.

You can arrange the column headings order by dragging and dropping them.

You can also right-click on any column heading to display the shortcut menu and decide which items you would like to display on the Nesting Result List.

See: Column Heading Shortcut Menu

| Column Heading | Description |
| --- | --- |
| No | The number of the nesting result. Select a No cell. The selected cell will be highlighted. Then right-click this cell to display the shortcut menu. The options on the menu allow you to save NC data, schedule or display other nesting information, etc. See: No. Column Shortcut Menu |
| Mouse Position | Display the coordinates of the current mouse pointer in the layout area. |
| Sheet Name | The name of the sheet. You can specify the sheet name in the Schedule Preference window. See: Sheet Name |
| Result | The result of the nesting process. Either the star or the tick symbol indicates the nesting is successful. The exclamation symbol indicates there are errors during the process. You can click the exclamation symbol to display the Warning Information window. See: Warning Information Window |
|  | Or |  |
|  | Nesting successful | Nesting error |
| Utilization | The utilization rate of the sheet. |
| Time Study | The total time of processing the sheet. You can click the cell to display the Time Study Information window and view the detailed time information. See: Time Study Information Window |
| Qty. | The quantity of the sheet that will have the same nesting results. You can click the cell and specify the quantity by typing an integer directly or using the up/down arrow button. |
| Machine | The name of the machine that is used to process the sheet. |
| Mat. Code | The code of the material. |
| Mat. Type | The type of the material. |
| Thickness | The thickness of the material. |
| Distance Between Two Points | The distance between the two points that you click in the part layout area. |
| Sheet X | The horizontal dimension of the sheet. |
| Sheet Y | The vertical dimension of the sheet. |
| Due Date | The due date of the process. |
| Process Date | The start date of the process. |
| Setup Info. #1 | Display the Turret Name. |
| Setup Info. #2 | It is NOT available now for punch machines. |
| Setup Info. #3 | Display the Material Name. |
| Setup Info. #4 | Display the Sheet Comment. |
| Setup Info. #5 | It is NOT available now for punch machines. |

| See: | The No. Column Heading Shortcut Menu |
| --- | --- |
|  | The Column Heading Shortcut Menu |
|  | The Warning Information Window |
|  | The Time Study Information Window |

| See: | Part Layout Shortcut Options |
| --- | --- |
|  | Information Panel |

### 25.1.1 The No. Column Heading Shortcut Menu

In the nesting result list of sheet mode, select and right-click one cell in the No. Column to display the shortcut menu.

The options on the menu allow you to save NC data, schedule and display other nesting information, etc.

In the nesting result list of part mode, select and right-click one cell in the No. Column to display the shortcut menu.

The options on the menu allow you to save the NC data, schedule and the tool assignment of the part as *.SY5 file, etc.

| Option | Description |
| --- | --- |
| Save NC data | Save the NC data. See: Save NC data |
| Save Sy4 | Save all current nesting results except the preferences. See: Save SY4 |
| Save Schedule/Output Report | Save the nesting result schedule. See: Save Schedule/Output Report |
| Output Report | This option allows you to decide which information to output by placing a check mark in the corresponding check box in the Report Output window. You can also right-click to display the shortcut menu in the part layout area, and then select Output Report to open the Report Output window. See: Output Report |
| Delete Sheet | Delete the sheet you have selected. See: Delete Sheet |
| Display Material Info | Display the Material Info. See: Display Material Info. |
| Display Plan Info | Display the Plan Info. See: Display Plan Info |
| Row Height | Adjust the height of the row. See: Row Height |
| Save Part | Save the tool assignment information for the part to the database you have selected. See: Save Part |
| Save SY5 as File | Save the tool assignment information for the part as a *.SY5 file. See: Save SY5 as File |
| Save Sy5 to NestingPlan | Save the tool assignment information for the part to the nesting plan. A symbol will appear in the CAD column of the Nesting Schedule window. |

| See: | Save NC data |
| --- | --- |
|  | Save Sy4 |
|  | Save Schedule/Output Report |
|  | Output Report |
|  | Delete Sheet |
|  | Display Material Info. |
|  | Display Plan Info. |
|  | Row Height |
|  | Save Part |
|  | Save SY5 as File |

| See: | The Column Heading Shortcut Menu |
| --- | --- |
|  | The Warning Information Window |
|  | The Time Study Information Window |

#### 25.1.1.1 Save NC Data

Select Save NC data from the menu to save the NC data.

Note:

You can save the NC data either to the disk or to the database. See: System Setting

To save the NC data,

| 1 | Select Save NC data from the menu. |
| --- | --- |
| 2 | If you select File in the Database: drop-down list in the System Setting window, the Input O Number dialog will appear. Place a check mark in the O Number check box and type an O Number in the text box, then click OK to proceed. You can also decide whether to save another *.SY2 file together with the NC data by placing a check mark in the Save SY2 check box. |
|  | Note: If you select MiniSDD or SDD in the Database: drop-down list in the System Setting window, different windows will display. See: System Setting |
| 3 | The Browse For Folder dialog appears. Navigate to the destination folder, and click OK to save. |

| See: | Save Sy4 |
| --- | --- |
|  | Save Schedule/Output Report |
|  | Output Report |
|  | Delete Sheet |
|  | Display Material Info. |
|  | Display Plan Info. |
|  | Row Height |
|  | Save Part |
|  | Save SY5 as File |

#### 25.1.1.2 Save SY4

Select Save Sy4 from the menu to save Sy4.

To save Sy4,

| 1. | Select Save Sy4 from the menu. |
| --- | --- |
| 2. | If you select File in the Database: drop-down list in the System Setting window, the Save As dialog will appear. Navigate to the destination folder and specify a name in the File name: text box, and then click Save to finish. |
|  | Note: If you select MiniSDD or SDD in the Database: drop-down list in the System Setting window, different windows will display. See: System Setting |

| See: | Save NC data |
| --- | --- |
|  | Save Schedule/Output Report |
|  | Output Report |
|  | Delete Sheet |
|  | Display Material Info. |
|  | Display Plan Info. |
|  | Row Height |
|  | Save Part |
|  | Save SY5 as File |

#### 25.1.1.3 Save Schedule/Output Report

Select Save Schedule/Output Report from the menu to save the schedule and output the report.

To save the schedule,

| 1. | Select Save Schedule/Output Report from the menu. |
| --- | --- |
| 2. | The Save Schedule window will appear. Specify a name in the Schedule Name: text box and place a check mark in the Save Schedule check box, then click OK to proceed. |
| 3. | If you select File in the Database: drop-down list in the System Setting window, the Browse For Folder dialog will appear. Navigate to the destination folder, and click OK to finish. |
|  | Note: If you enable Save the Turret Information function in the Save Schedule window, the Save Turret window will appear prior to the Browse For Folder dialog. Jiust click OK to continue. |
|  | Note: If you select MiniSDD or SDD in the Database: drop-down list in the System Setting window, different windows will display. See: System Setting |

To output the report,

| 1. | Select Save Schedule/Output Report from the menu. |
| --- | --- |
| 2. | The Save Schedule window will appear. Specify a name in the Schedule Name: text box and place a check mark in the Report Output check box to open the output item list. Place check marks in the check box of each item you want to output, then click OK to proceed. |
| 3. | The Report window appears. You can preview different report pages by clicking the corresponding items in the Report tree view pane. |
| 4. | Select Export from the File menu or click Export icon on the shortcut bar directly. The Browse For Folder dialog appears. Navigate to the destination folder, and click OK to output the report. |
|  | Note: You can also select Output Report from the shortcut menu to perform the same action. See: Output Report |

| Option | Description |
| --- | --- |
| Schedule Name | Specify the schedule name. The system will automatically create a schedule name according to the settings defined in the Schedule window. |
| Sheet List | The sheet list displays the nesting information for all the sheets. You can place check marks in the Select column to select sheets. You can also right-click the column heading to display the shortcut menu and place check marks before the items you want to display in the Sheet List. See: Nesting Result List |
| Report Output | Place a check mark in Report Output check box to display the following options. You can decide what report to be output by placing a check mark in the corresponding check box. See: Output Report |
| XML Output | Place a check mark in XML Output check box to output the XML information. |
| Save the Turret Information | You can select to save the turret information automatically or manually. |
|  | If you select the Automatic option, click the Detail button to continue. |
|  | The Save the Turret Information dialog box appears. You can select to overwrite the original turret settings or save the turret settings as the new. Then click OK to continue. |
|  | If you select the Manual Select option, click the Select button to continue. |
|  | The Save the Turret Information window appears. You can place a check mark before the turret item that you want to save. You can also select to input the turret name at the bottom left. Then click OK to continue. |
| Select All | Click this button to select all the sheets in the Sheet List. |
| Reset All | Click this to deselect all the sheets. |
| OK | Click this button to save the schedule data. |
| Cancel | Click this button to cancel all the settings you have made. |

| See: | Save NC data |
| --- | --- |
|  | Save Sy4 |
|  | Output Report |
|  | Delete Sheet |
|  | Display Material Info. |
|  | Display Plan Info. |
|  | Row Height |
|  | Save Part |
|  | Save SY5 as File |

#### 25.1.1.4 Output Report

Select Output Report from the menu to output the report.

To output the report,

| 1. | Select Output Report from the menu. |
| --- | --- |
| 2. | The Output Report window appears. Specify a name in the Schedule Name: text box and place check marks in the check box of each item you want to output, then click OK to proceed. |
| 3. | The Report window appears. You can preview different report pages by clicking the corresponding items in the Report tree view pane. |
| 4. | Select Export from the File menu or click Export icon on the shortcut bar directly. The Browse For Folder dialog appears. Navigate to the destination folder, and click OK to output the report. |

| See: | Save NC data |
| --- | --- |
|  | Save Sy4 |
|  | Save Schedule/Output Report |
|  | Delete Sheet |
|  | Display Material Info. |
|  | Display Plan Info. |
|  | Row Height |
|  | Save Part |
|  | Save SY5 as File |

#### 25.1.1.5 Delete Sheet

Select Delete Sheet from the menu to delete the selected sheets.

To delete sheets,

| 1. | Select the numbers of the sheet in the No. column that you want to delete. Right-click to open the shortcut menu and select Delete Sheet. |
| --- | --- |
| 2. | A warning message will appear. |
| 3. | Select Delete after saving the missing part plan to delete sheets after saving. Select Delete Sheets to delete sheets without saving. Select Cancel to cancel the operation. |

| See: | Save NC data |
| --- | --- |
|  | Save Sy4 |
|  | Save Schedule/Output Report |
|  | Output Report |
|  | Display Material Info. |
|  | Display Plan Info. |
|  | Row Height |
|  | Save Part |
|  | Save SY5 as File |

#### 25.1.1.6 Display Material Info

Select Display Material Info from the menu to display the material information.

To display material information,

| 1. | Select Display Material Info from the menu. |
| --- | --- |
| 2. | The Material Info window will appear. You can view various material information here and sort by clicking the corresponding column heading. |

| See: | Save NC data |
| --- | --- |
|  | Save Sy4 |
|  | Save Schedule/Output Report |
|  | Output Report |
|  | Delete Sheet |
|  | Display Plan Info. |
|  | Row Height |
|  | Save Part |
|  | Save SY5 as File |

#### 25.1.1.7 Display Plan Info

Select Display Plan Info from the menu to display the plan information.

To display plan information,

| 1. | Select Display Plan Info from the menu. |
| --- | --- |
| 2. | The Plan Info window will display. You can view the plan information for the parts and sort by clicking the corresponding column heading. |

| Column Heading | Description |
| --- | --- |
| No | The number of the part. |
| Part Name | The part name. |
| Size | The part size. |
| Plan Qty (A) | The quantity of the parts scheduled to be processed. |
| Result Qty (B) | The quantity of the parts actually processed. |
| B-A | The value of Result Qty (B) minus Plan Qty (A). |
| Filler Part | The filler parts quantity that defined for the part. |
| Comment | The comments for the part. |

| See: | Save NC data |
| --- | --- |
|  | Save Sy4 |
|  | Save Schedule/Output Report |
|  | Output Report |
|  | Delete Sheet |
|  | Display Material Info. |
|  | Row Height |
|  | Save Part |
|  | Save SY5 as File |

#### 25.1.1.8 Row Height

Select Row Height to open the Row Height dialog and adjust the height of the row.

To open the dialog and adjust the row height,

| 1. | Select Row Height from the menu. |
| --- | --- |
| 2. | The Row Height dialog appears. Type a value in the Row Height: text box to change the height of the row. Click OK to save. |

| See: | Save NC data |
| --- | --- |
|  | Save Sy4 |
|  | Save Schedule/Output Report |
|  | Output Report |
|  | Delete Sheet |
|  | Display Material Info. |
|  | Display Plan Info. |
|  | Save Part |
|  | Save SY5 as File |

#### 25.1.1.9 Save Part

Select Save Part from the part mode shortcut menu to save the tool assignment information for the part.

To save part,

| 1. | Select Save Part from the part mode shortcut menu. |
| --- | --- |
| 2. | If you select File in the Database: drop-down list in the System Setting window, the Browse For Folder dialog will appear. Navigate to the destination folder, and click OK to save. |
|  | Note: If you select MiniSDD or SDD in the Database: drop-down list in the System Setting window, different windows will display. See: System Setting |

| See: | Save NC data |
| --- | --- |
|  | Save Sy4 |
|  | Save Schedule/Output Report |
|  | Output Report |
|  | Delete Sheet |
|  | Display Material Info. |
|  | Display Plan Info. |
|  | Row Height |
|  | Save SY5 as File |

#### 25.1.1.10 Save SY5 as File

Select Save SY5 as File from the part mode shortcut menu to save the tool assignment information for the part as a *.sy5 file.

To save SY5 as file,

| 1. | Select Save SY5 as File from the part mode shortcut menu. |
| --- | --- |
| 2. | The Browse For Folder dialog will appear. Navigate to the destination folder, and click OK to save the tool assignment information for the part as an SY5 file. |

| See: | Save NC data |
| --- | --- |
|  | Save Sy4 |
|  | Save Schedule/Output Report |
|  | Output Report |
|  | Delete Sheet |
|  | Display Material Info. |
|  | Display Plan Info. |
|  | Row Height |
|  | Save Part |

### 25.1.2 The Column Heading Shortcut Menu

In the nesting result list, you can right-click any column heading to display this shortcut menu. You can place check marks before the options in the menu to display them in the nesting result list.

| 1. | Select More… from the shortcut menu to display the Choose Details window. |
| --- | --- |
| 2. | You can place check mark before the item you want to display and change their positions in the nesting result list. You can also type a value in the Width of Selected Column (in pixels): text box to specify the column width for the selected items. |
| See: | The No. Column Heading Shortcut Menu |
|  | The Warning Information Window |
|  | The Time Study Information Window |

### 25.1.3 The Warning Information Window

| Or | If the nesting process is successful, the star or the tick symbol will appear in the Result column. |
| --- | --- |
|  | If any error occurs, the exclamation symbol will appear. |
|  | You can click the exclamation symbol to open the Warning window. |
|  | Click one cell to locate the corresponding error in the layout area. You can modify the settings according to the error information. See: Error No. |

| See: | The No. Column Heading Shortcut Menu |
| --- | --- |
|  | The Column Heading Shortcut Menu |
|  | The Time Study Information Window |

### 25.1.4 The Time Study Information Window

Click one Time Study cell to display the Time Study Information window.

The window lists the detailed time information and the punch tool usage information during the process.

| See: | The No. Column Heading Shortcut Menu |
| --- | --- |
|  | The Column Heading Shortcut Menu |
|  | The Warning Information Window |

| See: | Part Layout Shortcut Options |
| --- | --- |
|  | Information Panel |

## 25.2 Part Layout Shortcut Options

In the Nesting Result list, you can click the plus button  to display the part layout you have specified. You can also click  to hide the display.

In the Part layout area of the sheet mode, you can right-click to display the shortcut menu. The options on the shortcut menu allow you to view the part layout and make manual adjustments.

In the Part layout area of the part mode, you can right-click to display the shortcut menu. The options on the shortcut menu allow you to view the individual part layout and make manual adjustments.

| Option | Description |
| --- | --- |
| Zoom In | When you select this option, the mouse pointer becomes a crosshair. Move the pointer into the layout area and click to zoom in. You can also draw a frame and zoom in the selected area. To change the zoom in ratio. See: Zoom In Ratio |
| Zoom Out | When you select this option, the mouse pointer becomes a zoom pointer. Move the pointer into the layout area and click to zoom out. You can also draw a frame and zoom out the selected area. To change the zoom out ratio. See: Zoom Out Ratio |
|  | Note: You can also use the mouse wheel to zoom in or out. |
| Move | When you select this option, the mouse pointer becomes a move pointer. Move the pointer into the layout area and hold on the left mouse button to move the sheet. |
| Zoom All | Select this option to display the entire sheet to fit the part layout area. |
| Auto Scale | Select this option to display all the parts to fit the part layout area. |
| Maximize Window | Select this option to maximize the current layout area window. |
| Shorten | Select this option to restore the maximized layout area window. |
| Display | Select the options in the Display submenu to display the corresponding information in the layout area. |
| Display All Parts Drawing For Grid | Select this option to display all parts drawing for grid in Auto-Execute (Pre-Nesting) Mode. |
|  | Place the check mark |
|  | Remove the check mark |
| Move | Select this option to display the movement path of the punch tool. |
| Arrow of Direction | This function is NOT available for punch machines. |
| Sequence Number | Select this option to display the processing sequence number. |
| Parts Number | Select this option to display the parts number. Same numbers indicate the same parts. |
| Error No | Select this option to display the error numbers. See: The Warning Information Window |
| Detect Scrap | Select this option to enable the system start scrap detection. |
|  | 1. The Detect Scrap window will appear during this process. |
|  | 2. Once the detection is done, all the scraps will be highlighted and marked with a sequential number in the layout area. |
|  | 3. The Scrap Information window will appear and list all the scraps. You can choose one item to locate the corresponding scrap in the layout area. |
|  | This window indicates there is no scrap detected. |
| Bend Line Mark | Select this option to display the bend line mark. |
| Macro Pattern Direction | This function is NOT available for punch machines. |
| Joint Mark | Select this option to display the joint mark. |
| Print Result View | To make settings for the Print Result View option: |
|  | 1. In the part layout area, you can right-click to display the shortcut menu. Select Print Result View to open the Print window. |
|  | 2. Click Properties… tab to display the Properties window. After making settings, click OK to continue. |
|  | 3. Then you can click OK to print the result view. |
|  | Option | Description |
|  | Printer | Specify the printer information, such as name, status, type, where, and comment. |
|  | Print Range | Specify the print range. You can select to print all pages or specific pages. |
|  | Copies | Specify the number of copies by typing in exact number or scrolling the arrow buttons. |
|  | Properties… | Specify the printer properties in the aspects of advanced, paper/quality, finishing, effects, and destination. |
| Save Schedule/Output Report | To save the schedule/output report: |
|  | 1. In this window, you can specify the schedule name and save the scheduling information for one sheet or several sheets. You can also decide the information to be output and the method to save the turret information. After making settings, click OK to continue. |
|  | 2. The Save Turret dialog box appears. Click OK to continue. |
|  | 3. The Browse for Folder dialog box appears. Navigate to the destination folder. |
|  | Note: Depending on the database you select (SDD, MiniSDD or File), different windows will display. See: System Setting |
|  | 4. Click OK to save the schedule and output report information. |
|  | Option | Description |
|  | Schedule Name | Specify the schedule name. The system will automatically create a schedule name according to the settings defined in the Schedule window. |
|  | Sheet List | The sheet list displays the nesting information for all the sheets. You can place check marks in the Select column to select sheets. You can also right-click the column heading to display the shortcut menu and place check marks before the items you want to display in the Sheet List. See: Nesting Result List |
|  | Report Output | Place a check mark in Report Output check box to display the following options. You can decide what report to be output by placing a check mark in the corresponding check box. See: Output Report |
|  | XML Output | Place a check mark in XML Output check box to output the XML information. |
|  | Save the Turret Information | You can select to save the turret information in the automatic or manual way. |
|  |  | If you select the Automatic option, click the Detail button to continue. |
|  |  | The Save the Turret Information dialog box appears. You can select to overwrite the original turret settings or save the turret settings as the new. Then click OK to continue. |
|  |  | If you select the Manual Select option, click the Select button to continue. |
|  |  | The Save the Turret Information window appears. You can place a check mark before the turret item that you want to save. You can also select to input the turret name at the bottom left. Then click OK to continue. |
|  | Select All | Click this button to select all the sheets in the Sheet List. |
|  | Reset All | Click this to deselect all the sheets. |
|  | OK | Click this button to save the schedule data. |
|  | Cancel | Click this button to cancel all the settings you have made. |
| Output Report | See: Output Report |
| Save NC Data | Save the NC data for the nesting process. See Save NC data |
| Save MJC Data | Select this option to save the data of MJC, IJP, TK, etc. See Save MJC data |
| Do Stack | This option is used to execute the mode that is used to remove parts. You must define the Take Out options in the Machine Set window before you can use the Do Stack option on the shortcut menu. See Do Stack |
| To AP100 CAM | This function is not available for the moment. |
| To Simulation | Select this option to go to FabriSIM or AP100, which is the simulation program you selected in the System Setting window, to perform the NC program simulation. |
| Display Parts Info | Select this option to display the Part Info window, which displays the part information of the selected sheet such as the part size, the quantity of the parts scheduled to be processed, the quantity of the parts actually processed, etc. In the Part Info. window, click the Save Missing Part Plan button to save the part into an Assemble or another ideal folder. When you place check marks in the Consider the quantity of sheets processed and register the part quantity when saving the missing part plan check box, the system will consider the sheet quantity when saving the part plan. For example, the part quantity is 5 and the sheet quantity is 3, so the saved part quantity is 5X3 =15. |
| Display Plan Info | Displays the part information, such as the quantity of the parts that are scheduled to process and the quantity of the parts actually processed. See Display Plan Info. |
| Display Group Tools | Display the list of group tools. All of the tools are on the generated turret for this sheet processing. Select this option to display the ToolList For Schedule window. This window shows the schedule information, such as Machine Name, Material Name, Material Size, Turret Stations, and tools used for each sheet. See: ToolList For Schedule |
| Display Tools Info | Display the tools and tool information used. |
| Sequence Setting | Select to display Sequence Setting window. More details see: Sequence |
| Tool Sequence Setting | To make settings for the Tool Sequence Setting window: |
|  | 1. You can right-click the part layout area to display the shortcut menu. Then select Tool Sequence Setting option to open the Tool Sequence Setting window. |
|  | 2. You can click the Grouping button to group the selected tools. And you can click the Ungroup button to cancel the grouping. |
|  | 3. You can change the Tool Sort by click the upward arrow or downward arrow . |
|  | 4. You can define the Start Position or End Position by selecting one from the following five radio options. |
|  | 5. You can select the direction from the Direction drop-down list: Auto, X or Y. You can see the divide number of sheet. And you can also play the check mark in One Direction and AI Sort by Angle check box. |
|  | 6. After finishing settings, you can click OK to continue. |
|  | 7. The following dialog box appears. You can click Yes to resequence now. |
| Begin TK Edit | This function is used to edit TK and IJP. Before using this function, you should enable TK and IJP device for the machine. See Begin TK Edit |
| Save SY5 In Sheet | You can save the tool assignment information of the part as a *.SY5 file in the Result View list. To save SY5 in sheet: |
|  | 1. In the Nesting Result list, click the plus button to display the part layout you have specified. In the part layout area, right-click to display the shortcut menu and select Save SY5 in sheet. |
|  | 2. Click one part to open the Save As window (the pattern of the part you select will turn orange) and select the destination folder in Save in dialog. Name the file you want to save in the File name dialog box and click Save button. |
|  | Note: Depending on the database you select (SDD, MiniSDD or File), different windows will display. See: System Setting |
| Edit | Select this option to go to the Manual Edit Mode. See Manual Edit Mode |
| Save the Part | Save the part nesting result as a SY5 file. |
| Manual Tool Assign | Get in the Manual Tool Assignment mode, and the options in the shortcut menu allow you to edit the tool assignment of the part. See Manual Tool Assignment |

| See: | Save MJC Data |
| --- | --- |
|  | Do Stack |
|  | Begin TK Edit |

| See: | Nesting Result List |
| --- | --- |
|  | Information Panel |

### 25.2.1 Save MJC Data

In the result view, you can select Saving MJC Data from the shortcut menu to save the MJC, IJP, and TK data.

Note:

Make sure you have selected File as the Database type in the System Setting window.

Example

| 1. | Open the Machine Set window. And enable the MJC, IJP and TK devices. |
| --- | --- |
| 2. | Specify the relevant settings in the Peripherals window. |
| 3. | Perform the auto execution to process the parts. |
| 4. | Click the number of the sheet. Right-click the part layout area to open the shortcut menu and select Save MJC Data. The Save As dialog box appears. Navigate to the folder where you want to save the NC data. Type an appropriate name in the File name: text box and then click Save. The data will be saved with the filename extension of *.SY2. |

| See: | Do Stack |
| --- | --- |
|  | Begin TK Edit |

### 25.2.2 Do Stack

If TK device is available, you can select Do Stack from the part layout shortcut menu to manually edit the position to stack parts, and then save the changes to the *.SY2 file.

Example

| 1. | In the Machine Set window, navigate to the Take-Out Information panel under Peripherals. Place a check mark in the Taking Out check box, and select PartRemoverll from the Type of Taking Out: drop-down list. |
| --- | --- |
| 2. | Specify the Maximum Height, Table Size X and Y and Maximum Weight in Stacking Height section. |
| 3. | In the Peripherals window, click the Taking Out tab, and place a check mark in the Taking Out On/Off check box. |
| 4. | In the Process After Cutting table of Prcess After Preference, select TK as the process after methods. |
| 5. | After performing the auto execution, right-click the part layout and select Do Stack. |
| 6. | The CompStackInterface window displays the places to stack the parts. You can drag and drop the parts to the desired position, and click OK to save your changes. |

| See: | Save MJC Data |
| --- | --- |
|  | Begin TK Edit |

### 25.2.3 Begin TK Edit

This function is used to edit TK and IJP. Before using this function, you should enable TK and IJP device in the Machine Set window, and select TakeOut as the process after method. See: Taking Out Conditions and IJP

To edit TK Settings

| 1. | Right-click in the part layout area, and select Begin TK edit to switch to the TK edit mode. |
| --- | --- |
| 2. | Part name is listed on the left side of the Edit Pickup/IJP window. Select the part you want to edit and the star symbol before the part name becomes blue when you edit the part. Note: Pickup Edit option is selected by default. |
| 3. | Drag the TK arm to the proper position, and click the Vacuum cups with which you want to absorb the part. You can re-click the active vacuum cups to deselect. |
| 4. | Click OK to close the window. Right-click and select End TK Edit to finish the operation. |

To edit IJP

| 1. | Right-click in the part layout area, and select Begin TK edit to switch to open Edit Pickup/IJP window.. |
| --- | --- |
| 2. | Select IJP Edit. |
| 4. | Move the pointer over the IJP, drag it to the ideal place. |
| 5. | Click OK to close the window. Right-click and select End TK Edit to finish the operation. |

| See: | Edit of Pickup/IJP Information window |
| --- | --- |

#### 25.2.3.1 Edit of Pickup/IJP Information window

In the Edit of Pickup/IJP Information window, you can change the IJP position. And you can also specify the TK arm position, and decide which cups or magnets will be used to absorb the parts. See: Begin TK Edit

| Items | Descriptions |
| --- | --- |
|  | Vacuum cups available |
|  | The vacuum cups that have been selected to absorb the part. |
|  | Magnet available |
|  | The Magnets cups that have been selected to absorb the part. |
| Single ARM Move | Select this option, and you can move one TK arm at a time. |
| Both ARM Move | Select this option, and you can move both TK arms at the same time. |
| VX | VX is the horizontal spacing, measured from the part origin (Lower left corner) to the origin of the left arm (Lower left corner). |
| VY | VY is the vertical spacing, measured up or down from the part origin (Lower left corner) to the origin of the left arm (Lower left corner). |
| VDIS1 | VDIST is the distance measured from the one side of one arm to the corresponding side of the other arm. |
| VDIS2 | This is not available now. |
| Increment | Increment value to alter VX, VY or VDIS1 |
| Auto Detect | Automatically decides how to pick up the part. |
| Ignore Hole | Place a check mark in the check box and type a value in the Size: text box, the system will ignore hole whose largest dimension is equal or smaller than the value in the text box. |
| IJP Edit | Edit the IJP position |
| PickUp Edit | Edit the pick up conditions. |
| An edit result is reflect in the same part in all sheets | Apply the modification results to the same parts in all the sheets. |
| An edit result is reflect in the same part on the same sheet | Apply the modification results to the same parts on the current sheet. |
| None | Only apply the modification results to the current parts. |

| See: | Save MJC Data |
| --- | --- |
|  | Do Stack |

## 25.3 Information Panel

The Information Panel is located along the right side of the Parts Layout area. In this panel, you can view the parts’ information, the error information and the NC code.

| See: | The Parts Information Panel |
| --- | --- |
|  | The Error List Panel |
|  | The NC Panel |

| See: | Nesting Result List |
| --- | --- |
|  | Part Layout Shortcut Options |

### 25.3.1 The Parts Information Panel

| 1. | You can click the Parts Info tab to display the part information. You can drag the scroll bar to show all information: No., part quantity, part comment, part name, material type, material thickness, material name, weight, unfold X size, unfold Y size, rectangle area, area with holes, area without holes, group ID and priority. |
| --- | --- |
| 2. | You can right-click the column area to select options in the shortcut menu. |
|  | Note: You can also right-click the part layout area to display the shortcut menu, and select Display Parts Info to display the Parts Info window. |

| See: | The Error List Panel |
| --- | --- |
|  | The NC Panel |

### 25.3.2 The Error List Panel

After displaying the parts layout, you can click the Error List tab to display the error information. See Warning Information Window

| See: | The Parts Information Panel |
| --- | --- |
|  | The NC Panel |

### 25.3.3 The NC Panel

After displaying the parts layout, you can click the NC tab to display the NC information. In this panel you can edit the NC program.

To edit an NC program:

| 1. | Right click the NC program area to display the shortcut menu. Select Edit Mode to get into the Edit mode to modify the code. |
| --- | --- |
| 2. | In the Edit mode, edit the NC program. |
| 3. | After editing the NC program, right-click the NC program area to display the shortcut menu. Select Save and End the Modification to save the changes. Select Ignore and End the Modification to exit the Edit Mode without saving the changes. |

| See: | The Parts Information Panel |
| --- | --- |
|  | The Error List Panel |

# Chapter 26 Manual Edit Mode

Except for various intelligent settings, Dr.ABE Blank allows you to edit part layout manually by switching to Manual Edit Mode.

After auto execution, you can right-click on the Part Layout area in the sheet mode to open shortcut menu, and select Edit from the shortcut menu to enter the Manual Edit mode.

| See: | Move |
| --- | --- |
|  | Remove |
|  | Sequence Edit |
|  | Part Grid |
|  | Change Material |
|  | Remnant Edit |
|  | Confirm Schedule Tool |
|  | Confirm/Display Setting |
|  | Add Parts |
|  | Reposition Command |
|  | Add New Sheet |
|  | Option |

## 26.1 Manual Edit Mode Shortcut Menu

Right-click part layout area in the Manual Edit mode, a shortcut menu will appear.

| Option | Description |
| --- | --- |
| Zoom In | Select this option to magnify the view of the selected area. |
| Zoom Out | Select this option to reduce the view of the selected area, allowing you to see more of the sheet area. |
| Move | Select this option to move the part. |
| Zoom All | Select this option to get an entire view of the sheet. |
| Auto Scale | Select this option to display all the parts to fit the view. |
| Maximize Window | Select this option to cover the window to full screen. |
| Shorten | Select this option to restore the maximized window. |
| Display Parts Info | Select this option to display the information of the parts nested on the sheet you have specified. The Parts Info window displays the part name, part quantity, part comment, material name, material type, material thickness, weight, size, group ID, priority etc. See Part Properties |
| Undo | Select this option to cancel your last operation. |
| Redo | Select this option to execute your last operation again. |
| Show part outside profile only | Select this option to display part outside profile only. As for complex part, you may use this option to reduce memory usage of the system. |

## 26.2 Manual Edit Mode Parameter Panel

There are toolbar and parameter section in the Parameter panel. The toolbar consists of Sheet Edit toolbar and Part Edit toolbar (Click Part Edit button to show Part Edit toolbar and enter Part Edit mode.). The Parameter section is where you can specify detailed settings for each option in the toolbar.

| Icon | Button Name | Description |
| --- | --- | --- |
|  | Confirm/Display Setting | This option allows you to display and confirm part/trace/pattern specified. |
|  | Move | This option allows you to move, rotate and copy part as you set in Parameter section. |
|  | Add Part | This option allows you to add part from SDD or file. |
|  | Remove | This option allows you to delete part or trace. |
|  | Part Edit | Click this button to enter Part Edit mode. |
|  | Remnant Edit | This option allows you to cut/edit remnant for better utilization purpose. |
|  | Change Material | This option allows you to change size, sheet code for material. |
|  | Part Grid | This option allows you to specify the conditions to process part grid. |
|  | Sequence Edit | This option allows you to define the sequence to process the parts. |
|  | Reposition Command | This option allows you to add reposition in sheet for clamp. |
|  | Confirm Schedule Tool | This option allows you to check tools in use and station status of a sheet or a schedule. |
|  | Add New Sheet | This option allows you to append a new sheet when you are editing a sheet. |
|  | Option | This option allows you to select whether specified message displays or not when exiting Edit mode, control window size and check collision. |

## 26.3 Move

In the Manual Edit mode, click  button to open the Rotate/Move/Copy the Part panel.

These options allow you to layout parts in sheet manually to utilize material best.

| Option | Description |
| --- | --- |
| Move Pitch X | Move part to specified position in X direction. You can click the arrow button next to Move Pitch X: text box to specify the value or type a value in the box directly. See Move part |
| Move Pitch Y | Move part to specified position in Y direction. You can click the arrow button next to Move Pitch Y: text box to specify the value or type a value in the box directly. See Move part |
| Rotate Pitch | Rotate part by specified angle. Click the arrow button next to the Rotate Pitch: text box to change degree or type a value in box. See Rotate part |
| Copy the Part | Place a check mark in this option to copy specified part. See Copy part |
| Adjacent Mode | If you select this option, the system will move the part to the ideal place that is adjacent to a part or the sheet border. In this case, the sheet will be processed economically. You cannot, however, move the part to overlap the other parts or move it off the sheet. |
| Display Part-Spacing | This option is not available now. |
|  | Generally the system will nest parts according to settings specified in Nest Preference. Here you can redefine space between parts by the following options. After setting, you can click Nest Again button to nest parts. |
| Extending Direction | Select this option to determine extending direction after nesting again. You can select Direction X, Direction Y and Both Sides. |
|  | Note: |
|  | This function is only available for rectangle nesting in Nesting Logic 1. See Nesting Logic 1 |
| Common Width | This option is used to define space between parts when you nest parts. You can click arrow button next to Common Width: text box to change common width or type space value in the box. |
|  | This option is used to calculate common width between parts automatically for optimum utilization of sheet. |
| Nest Again | Click this option to execute nesting according to settings above. See Nest Again |

Move a Part

| 1. | Select one part you want to move in Part Layout area. |
| --- | --- |
| 2. | Select or type a value in Move Pitch X: drop-down list to set the move distance of X direction. |
| 3. | Click or button and the system will move the specified part right or left. |
|  | Note: |
|  | You can also click or to move part upwards or downwards. |
| 4. | You can also select the part you want to move and hold down the left mouse button to drag the highlighted part to a position you want directly when the point shape turns into Move Point. |

Rotate a Part

| 1. | Select one part you want to rotate in part layout area. |
| --- | --- |
| 2. | Select or type a value in Rotate Pitch: text box to set the rotate angle. |
| 3. | Click button to rotate the part clockwise to specified degree. Or click button to rotate the part counter-clockwise to the specified degree |
| 4. | If Part rotation affects tool assignment and end value, the following message box will appear. |
| 5. | Place a check mark in Change to the angle that ensures tool assignment check box and select a degree, then click OK button. The part will be rotated to the degree specified here. |
| 6. | Remove a check mark in Change to the angle that ensures tool assignment check box to rotate part according to setting you specify in Rotate Pitch: text box. |
| 7. | You can also move pointer into the center point of part you want to rotate. Rotate part to any degree directly when the pointer shape turns into Rotate Point. The number next to Rotate Point indicates the rotation degree. |

Copy a Part

| 1. | Place a check mark in Copy the Part check box and select part you want to copy. |
| --- | --- |
| 2. | Hold down the left mouse button. When the point shape turns into, you can drag the copied part to a position you want. |

How to nest again

| 1. | Specify the settings as follows. |
| --- | --- |
| 2. | Click Nest Again button. Parts will be nested again. |
|  | Original nesting result | After nesting again |
| 3. | Specify the settings as follows. |
| 4. | Click Nest Again button and the system will nest parts again. |
|  | Original nesting result | After nesting again |
| 5. | Specify the settings as follows. |
| 6. | Click Nest Again button. Parts will be nested again. |
|  | Original nesting result | After nesting again |

## 26.4 Remove

In the Manual Edit mode, click button to open the Delete Part panel.

These options allow you to remove parts.

| Item | Description |
| --- | --- |
| Delete Object |  |
| Inside Frame | Select this option to delete the parts within the specified frame. See To delete part inside the specified frame |
| Outside Frame | Select this option to delete the parts outside the specified frame. See To delete part outside the specified frame |
| Mouse Command |  |
| All Selection | The selecting frame must include the whole part. See All Selection |
| Partial Selection | The part is selected though it is not completely included in the selecting frame. See Partial Selection |
| Select Same Parts At the Same Time | Place a check mark in the check box. If you select one, other same parts can also be selected. See Select Same Part at the Same Time |
| Only Same Angle | Place a check mark in the check box. If you select one, other same parts with the same angle can also be selected. See Only Same Angle |
|  | Click this button to execute deleting process. |

To delete part inside the specified frame

| 1. | Select Inside Frame |
| --- | --- |
| 2. | Click and drag the mouse to form a frame. |
| 3. | The part within the frame is selected and becomes orange. Click button or <Delete> key to delete. |

To delete part outside the specified frame

| 1. | Select Outside Frame |
| --- | --- |
| 2. | Click and drag the mouse to form a frame. |
| 3. | The parts outside the frame are selected and become orange. Click button or <Delete> key to delete. |

All Selection

| 1. | Select Inside Frame and All Selection |
| --- | --- |
| 2. | Click and drag the mouse to form a frame. The frame must cover the parts to be selected completely. |
| 3. | The parts within the frame are selected and become orange. Click button or <Delete> key to delete. |

Partial Selection

| 1. | Select Inside Frame and Partial Selection. |
| --- | --- |
| 2. | Click and drag the mouse to form a frame. It is not necessary for the frame to cover the parts to be selected completely. |
| 3. | The parts can be selected although the frame does not cover them completely. Click button or <Delete> key to delete. |

Select Same Part at the Same Time

| 1. | Place a check mark in the Select Same Parts At the Same Time check box. |
| --- | --- |
| 2. | Drag the mouse to form the white frame and use this frame to enclose one part. |
| 3. | The other same parts are selected |

Only Same Angle

| 1. | If you place a check mark in the Only Same Angle check box. |
| --- | --- |
| 2. | Drag the mouse to form the white frame and use this frame to enclose one part. |
| 3. | Other same parts with the same angle are selected |

## 26.5 Sequence Edit

In the Manual Edit mode, click  button to open the Sequence Command in Sheet panel.

These options in the Sequence Command in Sheet panel allow you to define the sequence to process the part and then take it out.

| Note: |
| --- |
| To activate this option, the following steps must be taken. |
| Step 1. | Assign TakeOut process to specified object in Process After Cutting table of Process After preference. |
| Step 2. | Place a check mark in Taking Out On/Off check box in the Take Out panel of Peripherals preference. |

### 26.5.1 Specify the range

Select the Specify the Range option to activate Specify the Range option.

You can divide the process area into equal districts , parts will be processed and taken out in the first district and then the adjacent district.

| Item | Description |
| --- | --- |
|  | Click this button to apply the settings. |
|  | Click the Details button to display the Sequence Setting window, which is the same as the Sequence window in Preference. You can specify the setting to sequence the parts in detail. See Sequence |
| Starting Position | Specify the starting position to sequence the parts. There are four options, Upper Right, Lower Right, Upper Left and Lower Left. |
|  | If you select Upper Right, the part in the upper right corner of the sheet will be processed first. |
|  | If you select Upper left, the part in the upper left corner of the sheet will be processed first. |
| Sheet Division Direction | Specify the direction to process the parts. There are four options, Direction X, Direction Y, Single Direction X, and Single Direction Y. |
|  | Specify the settings as follows and click Execute button. |
|  | The system will sequence the parts as follows. |
|  | Specify the settings as follows and click Execute button, |
|  | The system will sequence the parts as follows. All the parts in each division area will be processed in the same direction. |
| Sheet Division Quantity | This option allows you to type or select a number in Sheet Division Command: text box to divide the part layout area into equal areas for the processing sequence. The system will process the parts in the first area, and then go on to process the parts in the adjacent area. |
|  | The system will divide the part layout area based on the Direction settings. For example, if you select Direction X or Single Direction X, and type 3 in the Sheet Division Command: text box, the system will divide the part layout area as follows. |
|  | The system will divide the part layout area based on the Direction settings. For example, if you select Direction Y or Single Direction Y, and type 3 in the Sheet Division Command: text box, the system will divide the part layout area as follows. |

### 26.5.2 Mouse Command

Select the Mouse Command option to activate mouse command.

You can use mouse to click the parts to specify their process sequence directly. Alternatively you can place a check mark in Insert check box to change the sequence of two parts selected. The part number in the left part layout area will update automatically.

| Items | Description |
| --- | --- |
|  | Click this button to complete the modification. |
|  | Click this button to cancel your previous operation. |
|  | Click this button to give up all the modifications and restore the process sequence to its original state. |
| Insert | Place a check mark in the check box to enable the Insert functions. |
| Before | Select this option and click the first part, then click the second part. In that case, the sequence of the second part you click will be processed earlier than the first one. |
| After | Select this option and click the first part, then click the second part. In that case, the sequence of the second part you click will be processed later than the first one. |

Example

| 1. | Parts have been processed in the left part layout area as follows. |
| --- | --- |
| 2. | Select Mouse Command option. |
| 3. | Click the 23rd part. The part frame will be red and number on the part will become 1. |
| 4. | Click the rest part in order and system will assign the sequential number to each part. |
| 5. | Click Complete button. The part frame will restore to be yellow. |
| 6. | Place a check mark in the Insert check box and select Before option. |
| 7. | Click the fourth part first. |
| 8. | Click the fifth part. The fifth part will be processed earlier than the fourth part and the numbers on the part will update respectively. |
| 9. | Click Complete button to confirm. |

### 26.5.3 List Command

Select the List Command option to activate list command.

In this section, the name of all parts in the same process area will be listed by processing sequence and the numbers indicate their sequence. You can select one part name in the list and click upward button or downward button  to change the sequence. Meanwhile your changes will be reflected in the left part layout area.

## 26.6 Part Grid

In the Manual Edit mode, click  button to open the Part Grid panel.

These options allow you to select more than one part to create part grid or perform common punching process.

| Item | Description |
| --- | --- |
| Grid Parts Method | There are two options in drop down list: General Grid Parts, Common Punch. |
| General Grid Parts | Select this option to perform part grid. See General Grid Parts |
| Common Punch | Select this option to perform common line punch. See Common Punch |
| Output G98 | Place a check mark in this option and the system will output G98 to instruct the machine to process the grid. Output G98 in the NC code to indicate the use of part grid macros. System uses this macro when the same part will be processed. |
| Nesting Priority Direction | There are two options: X First and Y First. If you select X first, system will nest parts in X coordinate first. Otherwise system will nest parts in Y coordinate first. |
| Nesting Reference Position | These options in drop down list are used to specify nesting start point. The drop down list has four options: Bottom Left, Bottom Right, Top Left and Top Right. |
|  | Select X first option in Nesting Priority Direction. In following illustrations, the green line with arrow indicates process direction. |
|  | Bottom Left | Bottom Right |
|  | Top Left | Top Right |
| Part-Spacing | This option allows you to type or select the horizontal space and vertical space between parts. Default space value is defined in Part Spacing/Nesting Border of Nesting preference. |
| Quantity | This option allows you to type or select the number of the horizontal or vertical repetitions for the part. |
| Total | This option displays total number of grid part in part layout area. |
|  | Click this button to calculate the optimum part numbers in the sheet automatically. |
|  | Click this button to cancel current operation before execution |
|  | Click this button to start current nesting. |
|  | Click this icon to switch between Release Group and Group. Select Release Group you cannot choose different parts to execute part grid. |
|  | This option allows you to choose different part to execute part gird. |

General Part Grid

| 1. | Click part you want in the left part layout area. When part frame becomes green, it indicates that the part is selected. |
| --- | --- |
| 2. | Select General Grid Parts from Grid Parts Method: drop down list. |
| 3. | Specify Nesting Priority Direction and Nesting Reference Position to determine process direction and process start point. |
| 4. | Click arrow button next to Quantity option to change number in X/Y coordinate. Also you can type part number in Quantity X/Y: text box. |
| 5. | Click arrow button next to Part-Spacing option to reduce or increase space between parts, if necessary. |
| 6. | Place a check mark in Output G98 check box to generate G98 in NC code. |
| 7. | Following illustration show part grid result according to settings you specify above. |
| 8. | Click Execute button to complete current operation. |

Common Punch

| 1. | Select Common Punch from Grid Parts Method: drop down list. |
| --- | --- |
| 2. | Select the part grid you want to common-cut and the selected part grid will be green. |
| 3. | Select a cutting tool you want to use to cut the common line. The selected tool in Y-axis will be blue and the selected tool in X-axis becomes orange. |
| 4. | Click Execute button, or right click to open shortcut menu and click Complete option. Parts with common line will be processed as follows. |

## 26.7 Change Material

In the Manual Edit mode, click  button to open the Change Sheet Size panel.

These options allow you to change the size of the sheet by inputting size or selecting other sheet code.

### 26.7.1 Change material by auto-calculation

The Auto Calculation button is designed to calculate the part size automatically and generate a new sheet whose size matches the parts the most. The adjusted dimension of the sheet will be displayed in Width: text box and Height: text box.

| 1. | Parts are nested in the sheet as follows. The green rectangle indicates the original sheet whose size is 900x650. |
| --- | --- |
| 2. | Click Auto Calculation button in parameter panel. The newly generated sheet is shown in the green rectangle, while the red rectangle indicates the original sheet. |
| 3. | Meanwhile the new size is displayed in the in Width: text box and Height: text box. |
| 4. | Click the button to apply the changes and the system will use a 236x260 sheet to nest the parts. |

### 26.7.2 Input size to change material

You can directly stretch the sheet in the left part layout area to change the sheet size, alternatively you can type or select a size in Width: text box and Height: text box.

| 1. | When the pointer becomes, drag the pointer to move sheet border to wherever you want. The newly generated sheet is shown in the green rectangle, while the red rectangle indicates the original sheet. |
| --- | --- |
| 2. | As you drag the border, the values directly in the Width: text box and Height: text box in the right panel update automatically to reflect the changes. |
|  | You can also type or select the values in the Width: text box and Height: text box to specify the sheet size, |
| 3. | Click the button to apply the changes and the system will use a 453x342 sheet to nest the parts. |

### 26.7.3 Select sheet code to change material

Select the Sheet Code option to activate the Sheet Code section.

| Items | Description |
| --- | --- |
| Sheet Code | Click this drop down list to display all sheets that have the same thickness and material type as the sheet in use. |
| Rotate Sheet | This option allows you to rotate the sheet selected according to sheet code. |
|  | Note: |
|  | Only when the Sheet Type is Remnant, is this option available. See Sheet Information |
| Rotate Angle drop down list | Place a check mark in the Rotate Sheet check box to activate this option and select a degree from Rotate Angle: drop down list. There are four options: 0 degree, 90 degree, 270 degree, 360 degree. |

| Note: | A warning message will appear if the sheet size is not big enough. |
| --- | --- |

## 26.8 Remnant Edit

In the Manual Edit mode, click button to open the Remnant Cutting/Edit panel.

These options are designed to specify punch method, process after value and joint amount to generate remnant. You can also assign size range of tool to process remnant.

| Item | Description |
| --- | --- |
|  | Place a check mark in this check box to activate Add Remnant function. |
| Cutting Method | This option is used to define which remainder of the sheet will be created as a remnant. |
| Vertical | Select this option to create a remnant sheet with a vertical cutting. |
| Horizontal | Select this option to create a remnant sheet with a horizontal cutting. |
| T Cut-Vertical Left | Select this option to create a remnant with shape cutting. |
| T Cut-Vertical Right | Select this option to create a remnant with shape cutting. |
| T Cut-Horizontal Top | Select this option to create a remnant with shape cutting |
| T Cut-Horizontal Bottom | Select this option to create a remnant with shape cutting. |
| Rectangle | Select this option to create a rectangle shape remnant. |
| L shape | This option is used to create an L shape remnant. There are four optional shapes and click the icon next to this option to change shape. |
|  | When a cutting method is selected, a different graph comprised of various parameters will appear in the upper area of the panel. |
|  | This graph is where you can define distances from process-starting point or process-ending point to the sheet edge, distances between cutting line and sheet edge, and specify the process direction. |
|  | You can type or select a value in these text boxes. Alternatively, you can move the pointer to the green line and drag the line in any direction when the pointer changes into a double-headed arrow. With the movement of the pointer on the sheet, these values in these text boxes update. |
|  | The remnant in the following illustration is generated according to settings above. |
|  | Note: |
|  | A positive value means the machine will over cut the material, while a negative value indicates the length of the material the machine fail to cut. |
| Process After Cutting | Specify a process after method from the drop down list. See Process After |
| Joint Amount | Type or select a value in this text box to specify joint amount. This option will be available only when Micro Joint or Wire Joint is selected in Process After Cutting: drop down list. |
| Joint Number | This option will be available only when Micro Joint or Wire Joint is selected in Process After Cutting: drop down list. |
| Horizontal | Type or select a value to specify quantity of joint you want to create in X direction. |
| Vertical | Type or select a value to specify quantity of joint you want to create in Y direction. |
| Tool Size X/Y | These options allow you to specify size range of tool that is used to cut the remnant. Type or select a value in the first box to define the minimum value and a value in the second box to define the maximum value. Tool with X/Y size within this range will be used to process remnant. |
|  | This option is used to delete specified cutting line. Move the pointer to the cutting line until the line becomes orange and click to select it, and then click Delete button. |

Note:

If the cutting line intersects with clamp as follows. When you click button, a warning message box will appear.

## 26.9 Confirm Schedule Tool

In the Manual Edit mode, click button to open the ToolList For Schedule window.

This window consists of five elementary sections: Toolbar, Schedule list, Turret and tool information table, Turret image and Display Station.

These options allow you to review the schedule information, such as Machine Name, Material Name, Material Size, Turret Stations, and tools used for each sheet.

### 26.9.1 Toolbar

There are four toolbars in this section: Range toolbar, Shape toolbar, Search toolbar and View button.

#### 26.9.1.1 Range toolbar

Click a range buttons to display turret stations of that range. The  button is selected by default and stations of all the ranges will be displayed. More information, See Range and Shape button

#### 26.9.1.2 Shape toolbar

Click a shape button to display the tools of that shape. The  button is selected by default and tools of all the shapes will be displayed. More information, See Range and Shape button

#### 26.9.1.3 Search toolbar

| Button | Description |
| --- | --- |
|  | Click Search button to open the Advanced Filter window. |
|  | These options in this window allow you to filter the results by Name, Shape, Range, etc. For example, if you type a C in the Range: text box, and the system will search the current turret and list the stations that are installed tools of C range. |
|  | In the Schedule List pane, right-click to open the Display Setting window. Alternatively you can click in the toolbar to show this window. |
|  | There are three panels: Situation Color, Schedule Color and Sheet Color. These options in this window allow you to set the colors for corresponding Station Situation, Schedule and Sheet. |

#### 26.9.1.4 View menu

You can click the View menu and select the way to display tools and turret.

|  | Option | Description |
| --- | --- | --- |
|  | Used tool only | Display the tools used. |
|  | Tool for sheet | Select this option, and the system will display Sheet Tool columns on the right and show which tools are used for each sheet. |
|  | Tool for schedule | Display the tool for the schedule specified. |
|  | Turret Image | Select this option to display the Turret image. See Turret Image Pane |

### 26.9.2 Schedule list

The Schedule list on the left of the window displays the schedule information.

|  | Shows the Machine Name. Shows the Material Name and Material Size. Shows the schedule. Shows the sheet. |
| --- | --- |

You can click one  item to display all the tools used for the corresponding schedule or click one  item to show all the tools for the corresponding sheet.

### 26.9.3 Turret and tool information table

The turret and tool information table list all the stations and tools in use.

Right-click the column heading and select or remove the check marks to show or hide the corresponding columns.

You can also select Customize to open the Tool Inventory Item window.

Select the item in the list and click the upward/downward button to change the displaying order. You can type a value in Width of Select Column: text box to adjust the width of column selected in the Tool Inventory Item window.

| Column Title | Description |
| --- | --- |
| Station | This option displays the station number. |
| Situation | The Situation column shows the station status for the tool assignment. |
| Origin | The same tool is used in the same station to process the current sheet. |
| Create | A new tool is added to this station. |
| Exchange | A new tool is added to the station to replace the previous one. |
| Rotate | The tool is rotated |
| Move | A new tool is added to the station, and the previous tool is moved to other station |
| Exchange Die | The die is changed. |
| Remove Tool | The tool is removed from the station. |
| Range | This option displays the range of the turret from A to M. Only those tools with dimension ranges matching the station ranges can be placed in the turret. |
| Tool ID | Display the tool identification numbers. Each tool ID is unique and cannot be changed. The tool ID is used as a reference when the system is searching for a specific tool from the stock. |
| Name | The user-defined tool names appear in this column. The user specifies the name when registering the tool in the inventory. |
| Shape | The tool shapes are listed in this column. The basic tool shapes are Round (RO), Square (SQ), Rectangle (RE), Rounded Corner Rectangle (RR), Corner Radius (CR) and Obround (OB). There are also Special (SP), Tapping (TP) and other tool shapes. |
| X | The X dimension of the tool. |
| Y | The Y dimension of the tool. |
| R | The R dimensions of RR and CR tools. Size R is specific for RR and CR tools. The following figures indicate the R dimension for these tools. |
| Clearance | This option displays the clearance of die. |
| Angle | This option displays the angle of the station in the turret. |
| Key | The check mark before a station indicates this station is a keyed station. Shaped tools, such as rectangle and square tools, can only be installed in keyed stations. Non-keyed stations are available for round, center punch and burring tools. |
| Fixed | The Fixed indicates that the tool is installed in a fixed station. The system considers the tool as a permanent fixture within the station and will not remove it or replace it with alternate tools. You can manually remove the tool from the turret. |

### 26.9.4 Turret Image pane

When you click View button to expand menu and place a check mark before the turret image option, a turret illustration appears in the right of window.

The turret illustration shows the turret layout. The situation of the station is shown with color defined in the Situation Color panel of Display Setting window. The blue color is used to highlight the station being selected.

### 26.9.5 Display Station option

These options at the bottom of the window allow you to define stations of which type will be listed in the table.

| Option | Description |
| --- | --- |
| All Stations | List all the stations on the turret. |
| Empty Stations | List the blank stations. |
| Used Stations | List the stations on which there is no tool. |
| Fixed Stations | List the stations on which there is always the same tool. |
|  | Note: |
|  | If a station with a tool assigned is set to Fixed, no other tools are allowed to assign to it. If an empty station is set to Fixed, no tools are allowed to assign to it. |
| Free Stations | List the stations in which different tools can be installed. |

## 26.10 Confirm/Display Setting

In the Manual Edit mode, click  button to open the Confirm/ Display Setting panel.

These options allow you to check information about part, trace and pattern.

| Item | Description |
| --- | --- |
| Part | Selected Part to display the basic information of the selected part, including Part Name, Size X, Size Y, Sheet Pattern Quality and Weight. |
| Trace | Select Trace to display the information of the selected trace, including Pattern, Base Point X, Base Point Y, C-axis Value, T No, Management Name, Shape, Angle, Dim X, Dim Y, Axis Speed, M Code and Delay. |
| Pattern | Select Pattern to display CAD information of the selected line. |
| Every Hit View | If you select this option, all the tool hits will display in pattern processed. |
|  | Every Hit View disabled. | Every Hit View enabled. |
| Process Direction | Place a check mark in the check box, the system will mark the process direction with arrows. |
| Display Tools by Color | Place a check mark in the check box, the system will use color to display either tools of specified shape or the specified tool. |
| Detail | You can customize color to display tool shape and individual tool. See Example |
|  | Note: |
|  | This function takes effect only when the Display Tools by Color option is selected. |
| Tool Shape | This option allows you to define tools of different shape with different color. All tool shapes are listed in the Tool Shape window. |
| Individual Setting | This option allows you to define specified tools with different color. The tools and tool information used in the current process are listed in the Individual Setting window. |

Example:

| 1. | Click Detail button and the Tool Shape window appears by default. |
| --- | --- |
| 2. | Click the cell before SQ to open Color dialog. |
| 3. | Select one color and click OK |
| 4. | The cell you clicked will show the color you set in Color dialog. |
| 5. | Click Preview button to reflect immediately the changes to pattern processed by specified tool shape. Click OK to finish the setting. |
| 6. | Place a check mark in the Display Tools by Color check box and patterns processed by SQ tool are displayed by color you selected. |

## 26.11 Add Parts

In the Manual Edit mode, click  button to open the Add Part panel.

These options allow you to append new part from SDD/MiniSDD database or by opening file.

Note:

| 1. | You can add various type of part, such as .DXF, .DWG, .PRT, .IGA, .SY4, .BMF and the like. |
| --- | --- |
| 2. | You can load more than one part at a time. |

### 26.11.1 Add parts by opening a file

Click File option in the Add Part panel to open the File Open Dialog window.

Select a file and click the Open button, a part you desire will be added on the existing sheet. Alternatively you can click the Search button from toolbar at the top of the window to look for a part you want to add.

| Item | Description |
| --- | --- |
| File Name | Displays the file name of the part selected currently. |
| Files of Type | Select a file type from drop down list to appear. |
| Material Type | Type a material type in this text box. |
| Thickness | Type a material thickness in this text box. |
| Unit | Select a thickness unit from drop down list. There are two options: Inch and Metric. |
| Show Preview | This option allows you to view the drawing of the part selected currently. |
|  | Click this button to open the Search window. |
|  | In this window, you can look for parts according to conditions you specify. |

### 26.11.2 Add parts from SDD database

Click SDD option in Add Part panel to open the Avon Data Selection Dialog window.

| Item | Description |
| --- | --- |
|  | : Indicates that it is a Sy4 file : Indicates that it is a Sy5 file : Indicates that it contains .IGA file : Indicates that it contains a file from AP100 : Indicates that it contains a NC data file. |
| Add Server | Click this button to open the Add/Remove Server window. |
|  | In this window, you can add server to system. |
| Data Type | Select a data type to display in the part list. |
| All Data | Displays all parts information. |
| Diagram/NC Data | Displays parts information either with diagram or with NC data. |
| Allow Diagram Data | Displays parts information with diagram data only. |
| No NC Data | Displays parts information without NC data. |
|  | Click the Find button to open the Find Data window. |
|  | In this window, you can specify the condition to search part. |
|  | Click this button to hide the 3D and unfold drawing to extend the part list section. |
|  | Click the 3D and unfold diagram button to display three-dimensions and two-dimensions drawing in the right of window. |
|  | Click this button to open the Option window. |
|  | In this window, you can specify decimal number and language. |
| Part No. | Displays the name of the part selected currently. |
|  | Place a check mark in this check box and system list Sy4 files only. |
|  | Place a check mark in this check box and click the Open button, the Input Quantity window appears. |
|  | In this window, you can type a number in Part NO.: text box to specify part quantity you want to add directly. Alternatively, you can click the 0~9 Number button to enter part quantity. Click OK to confirm. |
|  | Select a part from the part list and click the Add button, the Selected Parts window appears. |
|  | If necessary, change quantity for a selected part or remove a selected part, and then click the Open button to add parts to the current sheet. |
|  | Select a part from the part list and click the Open button in Avon Data Selection Dialog window to add the part to the current sheet. |

Note:

If you select MiniSDD in System Setting, the MiniSDD Read window will be the following when you select SDD to add parts.

Example:

| 1. | After auto execution, the system nests the parts as follows. Right-click on the nesting part layout area and select Edit to switch to the Manual Edit mode. |
| --- | --- |
| 2. | Click button to open Add Part panel and select File or SDD option. |
| 3. | Select a part you want to add and click the Open button. |
|  | Note: |
|  | If the material/thickness of the added part is different from that of the existing part, the following dialog appears. |
| 4. | A new part appears in the working area. |
| 5. | Click to exit the Add Part panel and return to the Move panel. |
| 6. | Drag and drop the newly added part to the desired place. |

## 26.12 Reposition Command

In the Manual Edit mode, click button to open the Indicate Reposition panel.

The repositioning is the movement of the clamps to avoid over-travel and dead zones. Machines use clamps to shift the sheet to process the parts that are out of a processing area. A reposition refers to the processing area of specified clamp.

### 26.12.1 Basic Reposition Operation

These options allow you to add/remove a reposition, edit the reposition movement values, modify the holder positions, and change the reposition positions.

#### 26.12.1.1 Confirm Reposition

Click Confirm Reposition button to open the Confirm Reposition screen.

Example:

| 1. | Right click the cell of the No. column of the original clamp and select Add to add a new reposition. |
| --- | --- |
| 2. | In the Part Layout area, drag the mouse to move the new reposition to the position you desire. Click to confirm the position. |
|  | Click again to confirm the position of the holder. |
|  | Each reposition is assigned a number that appears along the bottom. |
| 3. | In the Parameter panel on the right, correlative data will update automatically. |
| 4. | Select No.2 reposition and type values to change the data directly. |
|  | Changes will be reflected in the left Part Layout area. |
| 5. | Alternatively you can click one number to select one reposition and the selected reposition in Part Layout turns to white. |
| 6. | Click the Amount button. |
|  | In the Part Layout area, the original reposition turns to yellow and a new reposition is shown with white color. Drag and drop the new reposition to any place you desire. |
| 7. | Select one reposition and then click Holder button. |
|  | In the Part Layout area, drag the mouse to move the selected holder to a new position. |
| 8. | You can also right click the cell of the No. column of one reposition to open a shortcut menu and then select Insert option to insert a new reposition before the selected reposition. |
|  | The number of new reposition will take place the number of the selected reposition, meanwhile the selected reposition is assigned a new number in sequence. |
| 9. | You can also remove an existing reposition by selecting Remove option in a shortcut menu except for No.1 reposition. |

#### 26.12.1.2 Manual Reposition

Click Manual Reposition button to clear all the existed repositions except No.1 reposition. A dialog appears when you click this button, reminding you the settings you made will be canceled.

You can click OK button to remove reposition you add and Cancel button to return to Confirm Reposition screen. When you click OK, the Manual Reposition screen will be available.

In this screen, you can add new repositions and edit them as you do in the Confirm Reposition screen.

If you want to switch to the Confirm Reposition screen, the following dialog will appear.

### 26.12.2 Divide Reposition

Click Divide button to open the Divide section.

These options in the section are used to split one process into two processes.

| Item | Description |
| --- | --- |
|  | Select a horizontal trace and then click this button when selected trace becomes blue. In the left Part Layout area, and a vertical line appears. Drag mouse to move this line in horizontal direction to any place you desire. |
|  | Right click to open a shortcut menu and select Complete to divide the selected trace as follows. |
|  | Select a vertical trace and then click this button when selected trace becomes blue. In the left Part Layout area, a horizontal line appears. Drag mouse to move this line in vertical direction to any place you desire. Right click to open a shortcut menu and select Complete to divide the selected trace. |
|  | This function is not available now. |
|  | Place a check mark to divide part-grid, and then the corresponding Divide Part-Grid section appears as follows. |
|  | This option is used to divide part grid in horizontal direction. Select a part and click this button when the part frame becomes blue. In the left Part Layout area, a vertical line appears. Drag mouse to move this line in vertical direction to any place you desire. |
|  | Right click to open a shortcut menu and select Complete to execute division as follows. |
|  | This option is used to divide part grid in vertical direction. Select a part and click this button when the part frame becomes blue. In the left Part Layout area, a horizontal line appears. Drag mouse to move this line in horizontal direction to any place you desire. |
|  | Right click to open a shortcut menu and select Complete to execute division as follows. |

Note:

Which grid the part belongs to is decided by the center point of each part. The part will be placed in the grid in which its center point is located.

### 26.12.3 Group Reposition

As for the trace located in the position where work zones overlap with each other or one another, system can process the trace in one of repositions automatically. Also you can insert this trace to another reposition. Click Group button to open the Group section.

Suppose there are two repositions in the left Part Layout area as follows. The color of the trace is corresponding to that of process area. The red trace will be processed in the No.1 reposition, while the yellow trace will be processed in the No.2 reposition.

Select a trace that can be processed in either of the two repositions and the selected trace will be blue.

Select No.2 reposition in the right Parameter panel, and then click the Insert to the selected reposition group button.

This trace turns to yellow. It indicates that the trace will be processed in No.2 reposition.

## 26.13 Add New Sheet

In the Manual Edit mode, click  button to open the Add New Sheet panel.

These options are used to append a new sheet when you are editing a sheet.

Example:

| 1. | Select Input Material option to activate the Input Material section. |
| --- | --- |
| 2. | Select and type value in the text box to define Material Type, Thickness, Size X and Size Y directly. |
| 3. | Alternatively you can select Sheet Code option to activate the Sheet Code section. |
| 4. | Click arrow button to select a new sheet from drop down list which containing sheets that have the same thickness as the original sheet has. |
| 5. | Place a check mark in the Rotate Sheet check box and select different angles to rotate the sheet, if necessary. |
|  | Note: |
|  | Only when material of remnant type is selected, is Rotate Sheet check box available. |
| 6. | When you clickbutton, a newly generated sheet with settings you have specified in Parameter panel will display on the left of window. |

## 26.14 Option

In the Manual Edit mode, click button to open the Option window.

Those options are designed to decide whether to display specified message when you plan to exit Manual Edit mode.

| Item | Description |
| --- | --- |
| Do not display message of applying to part when exiting edit mode | Place a check mark in the check box, the system will not display the message of applying to part when you click button. You can make detailed setting in the following drop-down list. The system will execute it automatically. |
|  | If you clear a check mark in the check box, the system will display the following message after you save the setting and exit Manual Edit mode. Then the following dialog appears when you save the setting and exit Manual Edit mode You may make detailed setting in the Reflect Edit Result window. |
|  | Item | Description |
|  |  | Select this option to apply the editing result to the part you are editing. |
|  |  | Select this option to make detailed settings. There are four groups to select. |
|  |  | Apply the editing result to the same part with the same angle in the current sheet. |
|  |  | Apply the editing result to the same part in the current sheet. |
|  |  | Apply the editing result to the same part with the same angle in all sheets. |
|  |  | Apply the editing result to the same part in all sheets. |
| Do not display message after selecting cancel command | Place a check mark in the check box, the system will not display the message of applying to part when you click button. The system will ignore or save changes automatically when you click button by selecting an option from the following drop-down list. |
|  | If you clear a check mark in the check box, the system will display the following message when you want to cancel the command. |
|  | Click Yes button, the system will end your editing by ignoring the setting you have made. |
|  | Click No button, the system will end your editing by saving the setting you have made. |
|  | Click Cancel button, the system will return to editing mode. |
|  | Place a check mark in Don’t ask me again check box and click Yes/No button. At the same time the system will place a check mark in Do not display message after selecting cancel command check box automatically in the Option window. |
| Do not display message if space is not enough when add parts | Place a check mark in the check box, the system will not display the message when the space is not enough to add part. |
| Use command of editing single part to maximize window | Place a check mark in the check box and click Part Edit button, the system will expand AICAM main window so that it covers the full screen. |
| Window returns to the initial size after editing is complete | Place a check mark in the check box, the maximized window will restore to its previous size after you exit the manual edit mode. |
| Release the Command of not display message after version updated | Place a check mark in this check box, system will not keep the settings of Don’t Display Message you have specified in previous version during version update. |
| Collision check when moving parts | Place a check mark in this check box, the following message will prompt when parts move and collision happens. |

| Take the following part as an example: |
| --- |
| 1. | In Option window, place a check mark in the check box and select Inside Same Sheet and Part of Same Angle in Auto Apply: drop-down list. |
| 2. | Click OK to close the Option window. |
| 3. | In the Manual Edit toolbar, click Part Edit button to enter Part Edit mode. On the left part layout, select one part and add two joints. See Joint Edit |
| 4. | Click button to save the setting. Two joints are automatically added to the part in the same sheet and with the same angle. |

# Chapter 27: Manual Tool Assignment

In Part Edit mode, you can edit manually part by part.

If you select Auto Execute (Nesting) to perform nesting process, you can select Edit from the shortcut menu to enter the Sheet Edit mode. In the Manual Edit Mode, you can click  (Part Edit) button from the toolbar to switch to Part Edit mode.

If you select Auto Execute (Individual Part) to perform nesting process, you can select Manual Tool Assign from the shortcut menu to enter the Part Edit mode directly.

| See: | Part Edit Mode Shortcut Menu |
| --- | --- |
|  | Part Edit Mode Parameter Panel |
|  | Confirm/Display Setting |
|  | Save Template |
|  | Delete Trace |
|  | Joint Edit |
|  | End Value |
|  | Change the Tool Assignment |
|  | Assign Tool Lines |
|  | Layout Between Single Hit |
|  | Merge |
|  | Stretch |
|  | Shift |
|  | Direct Assignment |
|  | Move/Copy Tool |
|  | Apply Assignment to the Same Inner |
|  | Fix Process Order |
|  | Change the Nibble Pitch |
|  | Show Tool |
|  | Option |

## 27.1 Part Edit Mode Shortcut Menu

Right-click part layout area in the Part Edit mode, a shortcut menu will appear.

| Option | Description |
| --- | --- |
| Zoom In | Select this option to magnify the view of the selected area. |
| Zoom Out | Select this option to reduce the view of the selected area, allowing you to see more of the sheet area. |
| Move | Select this option to move the part. |
| Zoom All | Select this option to get an entire view of the sheet. |
| Auto Scale | Select this option to display all the parts to fit the view. |
| Maximize Window | Select this option to cover the window to full screen. |
| Shorten | Select this option to restore the maximized window. |
| Display Parts Info | Select this option to display the information of the parts nested on the sheet you have specified. The Parts Info window displays the part name, part quantity, part comment, material name, material type, material thickness, weight, size, group ID, priority etc. See Part Properties |
| Undo | Select this option to cancel your last operation. |
| Redo | Select this option to execute your last operation again. |

## 27.2 Part Edit Mode Parameter Panel

There are toolbar and parameter section in the Parameter panel. The toolbar consists of Sheet Edit toolbar and Part Edit toolbar (Click Part Edit button to show Part Edit toolbar and enter Part Edit mode.). The Parameter section is where you can specify detailed settings for each option in the toolbar.

| Icon | Button Name | Description |
| --- | --- | --- |
|  | Confirm/Display Setting | This option allows you to display and confirm part/trace/pattern specified. |
|  | Save Template | This option allows you to save settings as template and use this template to process similar pattern in the future more conveniently. |
|  | Delete Trace | This option allows you to delete specified process trace. |
|  | Joint Edit | This option allows you add or edit joint. |
|  | End Value | This option allows you to modify the process after methods for the laser process. |
|  | Change the Tool Assignment | This option allows you to modify tool assignment for specified pattern. |
|  | Assign Tools-Lines | This option allows you to assign single D or double D tools to specified line. |
|  | Layout Between Single Hit | This option allows you to assign single hit tools to the pattern composed of intersection line. |
|  | Merge | This option allows you to assign tools to match tool element with pattern element. |
|  | Stretch | This option allows you to lengthen process path along moving direction and modify process angle on pattern-by-pattern basis. |
|  | Shift | This option allows you to move tool along the pattern edge in positive or negative direction. |
|  | Direct Assignment | This option allows you to assign tool of specified shape to punch out. |
|  | Move/Copy Tool | This option allows you to move or copy the specified tool assignment. |
|  | Apply Assignment to the Same Inner | This option allows you to apply the assignment in specified inner to all the same inner or the same inner you specify. |
|  | Fix Sequence Order | This option allows you to fix the sequence in processing one loop. |
|  | Change the Nibbling Pitch | This option allows you to modify moving pitch when nibbling tool is processing pattern. |
|  | Show Tool | This option allows you to view the tool assigned in specified pattern. |
|  | Option | This option is the same with that in Sheet Edit Toolbar. |

## 27.3 Confirm/Display Setting

Select  to open Confirm/Display Setting panel on the right side of the window.

| 1. | Take the following part as an example. |
| --- | --- |
| 2. | Select Part in Parameter panel on the right side of the window to display the selected part parameters, including part name, size, sheet pattern quantity and weight. Example: |
| 3. | Select Trace in Parameter panel on the right side of the window to display the selected trace parameters, including pattern, base point coordinates, process length, process angle, tool length, tool width, C-axis value, T No, management name, shape, angle, dim coordinates, axis speed, M code and delay. Example: |
| 4. | Select Pattern in Parameter panel on the right side of the window to display the selected pattern parameters, including start point coordinates, end point coordinates, length and angle. Example: |

## 27.4 Save Template

You can use this function to save the assignment for the parts as template.

The template can be used in the future to process similar patterns more conveniently.

In part edit mode, select the part you want to save and then click  on the toolbar to open the Save Template panel on the right side of the window.

You may select one from the two options below,

| Option | Description |
| --- | --- |
| Part Assignment Data | Select this option to save the part assignment data as SY5. See: Save Part Assignment Data |
| Template | Select this option to save template. See: Save Template |

Save Part Assignment Data

| 1. | Select Part Assignment Data option to save as SY5. |
| --- | --- |
| 2. | The corresponding Parameter panel will appear below. Select File in Save Type: drop-down list and then click Save button. |
|  | Note: Select/Remove Assignment button is NOT available. |
| 3. | The Save As window appears. Specify a name in the File name: text box and click Save button to save the assignment data as an SY5 file. |
|  | Note: You can also select SDD or MiniSDD from the Save Type: drop-down list to save the SY5 information into the corresponding database. |

Save Template

| 1. | Select Template option to save as template. |
| --- | --- |
| 2. | The corresponding Parameter panel will appear below. |
| 3. | Select the elements you want to save, such as lines, holes, or notches, etc. The selected elements will be highlighted. |
| 4. | Click Save button in the right Parameter panel to display the List Of Template window. Alternatively, you can right-click the layout area and select Complete. |
| 5. | Specify a name for the template in the File Name: text box and click Save button to save the template. The Template window will then display. You can make further edit for the saved templates in this window. See: Edit of Template |

## 27.5 Delete Trace

In Part Edit mode, select  to open Delete Trace panel to delete the selected trace.

| Item | Description |
| --- | --- |
| Delete Object | Define the object you want to delete. |
| Inside Frame | Select this option to delete the parts within the specified frame. |
| Outside Frame | Select this option to delete the parts outside the specified frame. |
| Mouse Command | Define the command of the mouse. |
| All Selection | The selecting frame must include the whole part. |
| Partial Selection | The part is selected though it is not completely included in the selecting frame. |

| 1. | Take the following part as an example. Select Inside Frame. Draw a frame with the mouse to cover a trace. The trace inside the frame is selected. |
| --- | --- |
| 2. | Click the delete button or press the Delete key to delete the selected object. |
| 3. | Click to save settings or click to cancel settings. |

## 27.6 Joint Edit

In Part Edit mode, select  to open Add/Edit Tab panel to edit joints manually.

| Item | Description |
| --- | --- |
| Distance from End Point | Define the offset value of the joint. You can type the value directly or click the button to change the value. |
| Wire Joint | Define the width of the wire joint. |
| Micro Joint | Define the width of the micro joint. Note: You cannot add a corner joint to a corner unless the distance from the end point is set to 0. |
| Both Sides Corner Joint | Add the micro joints on both sides of the corner. If you don’t place a check mark in this check box, the system will assign the joint on one corner side only. |
| Tab Type | Type of tab. You can select joint type from the drop-down list. Only Common Tab is available. |
| Process Joint at Last | If you place a check mark in this check box, the system will process joint at last. |
| Use Joint Tool | If you place a check mark in this check box, the masked options will be enabled, and you can select the Special or Standard option. If you select the Special option, the Dr. ABE dialog box appears, and you can click OK to continue. |
|  | The Tool Assign Condition window appears. You can set the special tool joint conditions in Joint panel. |
| Lap Rate | Type a value in the text box to specify the overlap percentage. The system will determine the overlap value using this formula: Overlap= Lap (%) x Tool Total Length |
| Adjust Amount | Type a value in the text box to specify the overlap amount. |

| 1. | Take the following part as an example. |
| --- | --- |
| 2. | A red point appears on the selected line. You can move the pointer to the desired position. |
|  | Note: If there’s no tool exist, the Please select the tool for joint tool assign window appears, and you should select one for joint tool assign from the tool list first. |
| 3. | Click the line to add the wire joint. |
| 4. | Adding a micro joint is similar to adding a wire joint. When the red pointer reaches the corner, its colour turns orange, signifying that it has become a corner joint. |
| 5. | Click to add the micro joint. |
| 6. | If you want to add joints to both sides, place a check mark in the box before Both Sides Corner Joint. You can select the tab type in the drop-down list at the bottom right. |
| 7. | If you want to delete the joint, click it. The selected joint will be highlighted. Click the Delete button . The selected joint will be removed. |
| 8. | Select a joint to highlight it. Then you can specify the parameters, such as distance from end point, wire joint and micro joint by typing values in the text boxes or clicking the arrow buttons next to the text box to change the original values. The changes will be reflected on the drawing respectively. You can continue to edit other joints in the same way. |
|  | The original situation |
|  | The changed situation |

## 27.7 End Value

Select to open End Value panel on the right side of the window.

| Option | Description |
| --- | --- |
| Type |  |
| Machine Stop | M00 is generated after processing. |
| Joint | Keep joints after processing. |
| Chute Tool | Some special tools can work as the chute tools to perform the final hit. |
| None | No specific end value. |
| Axis Speed (F1-F4) | Select a speed option from the drop-down list to specify the feed rate for removing parts. There are four options. The selection of a particular option will determine the code output in the NC program. For example, if you select F1, the system will output a feed rate value of F1 for the device. |
| Move Amount | Specify the move amount by scrolling the arrow or typing in the exact value. |
| Chute Tool Setting | When you select Chute Tool option, the following parameters will spear. |
| Cut X/Y | The dimension of the chute tool in the X/Y-axis. |
| Offset Y | The distance from the center of the die to the position of the final hit. |

| 1. | Take the following part as an example. In the Process After Cutting table, specify Machine Stop as the method to deal with the part after cutting. |
| --- | --- |
| 2. | In the Part Edit mode, click to open the End Value panel. Machine Stop is selected by default as the end value. |
|  | . |
| 3. | Click to open Add/Edit Tab panel. Assign tabs to the part as follows. See: Joint Edit |
| 4. | Click to open the End Value panel again and select Joint Edit |
| 5. | Regenerate the NC code and the system will process the part as follows. |

## 27.8 Change the Tool Assignment

You can use this function to manually change the tool assignment for the part.

In Part Edit mode, click  on the toolbar to open Change the Tool Assignment panel on the right side of the window.

Note:

When you click  on the toolbar, the Turret Info window will appear as well so that you can select tools from the list in this window.

You may select one of the two options below,

| Option | Description |
| --- | --- |
| Single Hit Center | Change single hit tools. See: To change single hit tools |
| Line | Change line tools. See: To change line tools |

To change single hit tools,

| 1. | Click Single Hit Center button in the Parameter panel. |
| --- | --- |
| 2. | Select the tool you want to use in the Turret Info window that appeared previously. In this instance, select a RO tool of ID number 26. |
| 3. | Then click the single hit tool tracks that you want to change in the layout area. The selected tool tracks will be highlighted. Right-click in the layout area and select Complete. |
| 4. | All the selected single hit tracks will be changed into the RO tool tracks that you specified. |
| 5. | If you want to specify the angle for a certain tool, you need to put this tool on an AI station before select it. In this case, put the SP tool of ID number 15 on an AI station and select it. |
| 6. | Now both the Axis C Value of AI Tool: textbox and Keep the Unchanged C Value: check box are enabled in the Parameter panel. |
|  |  | Note: C Value refers to the angle of the tool. When the Axis C Value of AI Tool: textbox is enabled, the default value in it is 0, which is the default angle of the tool. |
| 7. | Remain 0 in the Axis C Value of AI Tool: textbox. Then select the two RO tools on the left side. Right click and select Complete. The two RO tools are changed into the SP tools with default angle. |
| 8. | Type 225 in the Axis C Value of AI Tool: textbox. Then select the two RO tools on the right side. Right click and select Complete. The two RO tools are changed into the SP tools with angle of 225. |
| 9. | If you place a check mark in the Keep the Unchanged C Value: check box, the Axis C Value of AI Tool: textbox will be disabled. |
| 10. | Then select all the 5 single hit tools and Complete. The center RO tool is now changed into the SP tool with default angle, while the other 4 SP tools on both sides keep their angles unchanged. |

To change line tools,

| 1. | Click Line button in the Parameter panel. |
| --- | --- |
| 2. | Select the tool you want to use in the Turret Info window that appeared previously. In this instance, select a SQ tool of ID number 6. |
| 3. | Then click the line tool tracks that you want to change in the layout area. The selected tool tracks will be highlighted. Right-click in the layout area and select Complete. |
| 4. | The selected line track will be changed into the SQ tool track that you specified. |

## 27.9 Assign Tool Lines

You can use this function to assign the tools to process lines by shear proof.

In Part Edit mode, click  on the toolbar to open Assign Tools-Lines panel on the right side of the window.

Note:

When you click  on the toolbar, the Turret Info window will appear so that you can select tools from the list in this window.

|  | There are two textboxes above the Parameter panel. The value in the left side textbox is the tool starting position protrusion value. The value in the right side textbox is the tool ending position protrusion value. |
| --- | --- |
|  | For instance, we specify 30 in the left textbox, and 50 in the right textbox. After select a tool from the Turret Info window and assign it on a line, the line will now be processed with the specified protrusion value. |
| Note: If there is a joint at the starting/ending position of a line, the specified protrusion value will be invalid. |

In the Parameter panel, you may select either Shear Proof (G66) or Lap Amount (G28) to assign the tools, and when you finish the edit and regenerate NC data, G66 or G28 NC command line will be output accordingly.

| See: | Shear Proof (G66) |
| --- | --- |
|  | Lap Amount (G28) |

Shear Proof (G66)

| When you select this option, the Parameter panel will display as below, |
| --- |
| Option | Description |
| Pitch | Specify the pitch value in the Pitch: textbox when the tool is used for nibbling process |
| Slot Last Tool Pitch | Specify the last pitch value in the Slot Last Tool Pitch: textbox for a slotting type tool. |
| Imbalance Flag | This function is only available when a deburring tool is selected. The Imbalance Flag: checkbox is empty by default. In this circumstance, you can only assign the deburring tool on the line with the exact same tool width. For instance, when a RE 5 x 2 deburring tool is selected, we can only assign it on a line with the exact tool width of either 5 or 2. Otherwise, an error message window will display. |
|  | But when you place a check mark in the Imbalance Flag: checkbox, the deburring tool can then be assigned on any line with a tool width that is not less than the shorter side of the deburring tool. For instance, when a RE 5 x 2 deburring tool is selected, now we can assign it on any line as long as its tool width is not less than 2. |
| Collision Check | Place a check mark in the Collision Check: checkbox to enable the function. You may select either Auto or Manual option to check the collision. |
| Auto | Select this to execute collision check automatically. |
| Manual | Select this to execute collision check manually. |
| Collision Ins. | Click this to activate Manual Collision Check. |
|  | Example: |
|  | 1. | Specify the extrusion value as follows: |
|  | 2. | Assign a tool on the specified line. |
|  | 3. | Collision occurs as the following illustration shows. The punch process extends the line edge and interferences with the pattern. |
|  | 4. | Place a check mark in the Collision Check check box and select Auto. |
|  | 5. | The system will check the collisions for the tool assignment, and automatically make changes. |
|  | 6. | If you select Manual, collision also occurs when you finish assigning tool. |
|  | 7. | Click Collision Ins. Button in the right panel.(The Collision Ins. button switches to Collision End button automatically) |
|  | 8. | Move the pointer over the following line segment. |
|  | 9. | Click the line segment, and the system will automatically shorten the punch path. |
|  | 10 | Use the same way to modify the other side and click End Collision button to confirm your modification. |
| Assignment Side | Click the Assignment Side button to shift the tool assignment side along the process direction. There are four options: Auto, Left side, Online and Right side. You can click the button to switch among these four options. |
| Correction during Single Hit | This option enables you to make correction for a single hit tool assignment. |
|  | Suppose both protrusion values are set to 0 (no protrusion), click the Correction during Single Hit button to shift among CE, LF, and LB to make correction for a single hit tool assignment. |
|  |  | Centered by default. No correction. |
|  |  | Correction is made by front-end alignment of the tool. |
|  |  | Correction is made by back-end alignment of the tool. |

Lap Amount (G28)

| When you select this option, the Parameter panel will display as below, |
| --- |
| Option | Description |
| Lap | Specify the overlap value for the tool in the Lap: textbox |
| Layout of Ending Point Correction | Normally, the protrusion occurs more or less in each assignment. This option allows you to make correction for the last hit with no regard of the lap value you have specified so that the protrusion can be avoided. |
|  | In the circumstance that the lap value is set to 27, if the Layout of Ending Point Correction: checkbox remains empty, the tool will be assigned according to the lap value you have specified. The protrusion occurs as the picture indicates below. |
|  | But if you place a check mark in the Layout of Ending Point Correction: checkbox, then the last hit of the assignment will be adjusted with no regard of the lap value you have specified. The protrusion is avoided as the picture indicates below. |
| Select End Punch | Place a check mark in the Select End Punch: textbox, then when you click in the layout area to assign the tool, the window below will display. |
|  | The window lists all the tools on the current turret. Choose a tool from the list as the last punch tool and click OK to proceed. Now the line is processed with assignment of the last punch tool you have just chosen. |

## 27.10 Layout Between Single Hit

In the Part Edit mode, you can click Layout Between Single Hit to assign a tool to single hit the pattern of two intersecting lines.

The Turret Info window appears.

This window is where you can select a tool from the tool list to process the area two lines intersect. When a tool is assigned to the left working area manually, the turret information of the tool in the Turret Info window turns to red, which indicate that this tool is in use.

Note:

Only the type of “RO”,”RE”,”SQ”,”OB”,”RR” tool can be assigned.

Example

| 1. | We will single-hit the pattern of two intersecting lines. |
| --- | --- |
| 2. | Select a tool in the Turret Info window. |
| 3. | Move the pointer into the left working area, click one line and then click the other line to assign the single-hit tool. |

## 27.11 Merge

Select to open Merge panel on the right side of the window.

| 1. | Take the following part as an example. We will assign a tool to process the following inclined line. |
| --- | --- |
| 2. | Select a tool in the Turret Information panel. |
| 3. | Move into the working area, right-click and select Merge. The Select assign edge window appears. |
| 4. | Click to select a tool edge. The cross indicates the base point for the tool assignment. |
| 5. | Move the pointer over the inclined line. Move the pointer close to the end point of the inclined line to specify the base point for the tool assignment. |
| 6. | Click to assign the tool. The specified tool edge is assigned to process the selected inclined line, and the base point of both tool and inclined segment matches. |

## 27.12 Stretch

In the Part Edit mode, click Stretch button to open the Stretch panel on the right side of window.

This panel allows you to lengthen or shorten process path of a straight line/a curve on a pattern-by-pattern basis.  There are two methods:

| Method 1. | Just drag and drop the mouse to shift the tool along the moving path. |
| --- | --- |
| Method 2. | Select or type a value in the Tool Stretch Amount: text box to specify an adjustment amount based on the Input Method option. |

| Option | Description |
| --- | --- |
| Tool Select | Specify the base point to move the selected tool along the tool path. |
| End Point | Use the end point of the tool as the base point to adjust the process path. The red point in the following picture indicates the base point and the value in Tool Stretch Amount is 0, which indicate that the selected tool is placed in the original position. |
| Center | Use the center point of the tool as the base point to adjust the process path. The red point in the following picture indicates the base point and the value in Tool Stretch Amount is 0, which indicate that the selected tool is placed in the original position. |
| Input Method | These options become available only when you are adjusting the process path on the arc. |
| Angle | Adjust the process path by modifying the angle value. |
| Circle Length | Adjust the process path by modifying the arc length. |
| Tool Stretch Amount | As you move the pointer, the value in this text box will update automatically to reflect change you have made. Alternatively you can select or type the value to adjust the process path. |
|  | Notes: |
|  | Only when a tool on pattern is selected, is this text box available. If you are adjusting the process path on the lines, select or type a value in the text box to specify the distance to move the tool. If you are adjusting the process path on the arc, select or type a value in the text box to specify the degree or arc length to move the tool. A positive value implies that the tool path will be lengthened, while a negative value reveals that you want to shorten the tool path. |

| See: | Adjust the process path on the lines |
| --- | --- |
|  | Adjust the process path on the arcs |

### 27.12.1 Adjust the process path on the lines

| 1. | On the left part layout area, there is a pattern as follows. |
| --- | --- |
| 2. | Select End Point and move a pointer into the working area. |
| 3. | Click the tool you want to move, and then drag it along the tool path to adjust the tool size when the tool become blue. |
| 4. | When you are satisfied with tab size, click the left mouse button again to complete. |
| 5. | The value in Tool Stretch Amount: text box will reflect change you have made automatically. You can also select or type a value in this text box to specify the distance the tool will elongate from the base point. |

| See: | Adjust the process path on the arcs |
| --- | --- |

### 27.12.2 Adjust the process path on the arcs

| 1. | Move the pointer to the tool on the arc. The blue dash line will appear, which indicate that you can drag the pointer to adjust the process path. |
| --- | --- |
| 2. | Drag the pointer along the process path to desired point. |
| 3. | If you are satisfied with the tab angle, click the left mouse button again to complete. |
| 4. | Meanwhile, the Input method option on the right side of window become available, so you can select a method to adjust the process path accurately. |
| 5. | The value in Tool Stretch Amount: text box will reflect change you have made automatically. |
| 6. | You can also select or type a value in the Tool Stretch Amount: text box to specify the angle, the tool path of this angle will be deleted/added. |

| See: | Adjust the process path on the lines |
| --- | --- |

## 27.13 Shift

In the Part Edit mode, click Shift button to open the Shift panel on the right side of window.

This panel allows you to move the process path of a straight line/a curve on a pattern-by-pattern basis.  There are two methods:

| Method 1. | Just drag and drop the mouse to move the tool along the moving path. |
| --- | --- |
| Method 2. | Select or type a value in the Shift Amount: text box to specify a movement amount based on the Input Method option. |

| Option | Description |
| --- | --- |
| Tool Select | Specify the base point to move the selected tool along the tool path. |
| End Point | Use the end point of the tool as the base point to move the process path. The red point in the following picture indicates the base point and the value in Shift Amount is 0, which indicate that the selected tool is placed in the original position. |
| Center | Use the center point of the tool as the base point to move the process path. The red point in the following picture indicates the base point and the value in Shift Amount is 0, which indicate that the selected tool is placed in the original position. |
| Input Method | These options become available if you are moving the process path on the arc. |
| Angle | Select this option and type a degree in Shift Amount option, The specified process path will be rotated by this angle. |
| Circle Length | Select this option and type an arc length in Shift Amount option, The specified process path will be moved by this arc length. |
| Shift Amount | As you move the pointer, the value in this text box will update automatically to reflect change you have made. Alternatively you can select or type the value to move the process path. |
|  | Notes: |
|  | Only when a tool on pattern is selected, is this text box available. If you are moving the process path on the lines, select or type a value in the text box to specify the distance to move the tool. If you are moving the process path on the arc, select or type a value in the text box to specify the angle or arc length to move the tool. |

| See: | Move the process path on the lines |
| --- | --- |
|  | Move the process path on the arcs |

### 27.13.1 Move the process path on the lines

| 1. | On the left Part Layout area, there is a pattern as follows. |
| --- | --- |
| 2. | Select End Point and move a pointer into the working area. |
| 3. | Click the tool you want to move, and then drag it along the tool path to move the tool when the tool becomes blue. |
| 4. | When you are satisfied with new position, click the left mouse button again to complete. |
| 5. | The value in Shift Amount: text box will reflect change you have made automatically. You can also select or type a value in this text box to specify the distance the tool will move from the base point. |
|  | Note: |
|  | A positive value in the Shift Amount option implies that movement is along the plus X/Y axis, while a negative value reveals that you want to move the tool path along the minus X/Y axis. |

| See: | Move the process path on the arcs |
| --- | --- |

### 27.13.2 Move the process path on the arcs

| 1. | Move the pointer to the tool on the arc. The blue dash line will appear, which indicates that you can drag the pointer to move the process path. |
| --- | --- |
| 2. | Drag the pointer along the process path to desired point. |
| 3. | If you are satisfied with new position, click the left mouse button again to complete. |
| 4. | Meanwhile, the Input method option on the right side of window become available, so you can select a method to move the process path accurately. |
| 5. | The value in Shift Amount: text box will reflect change you have made automatically. |
| 6. | You can also select or type a value in the Shift Amount: text box to specify the angle, the tool will turn by specified degree clockwise/counter-clockwise. |
|  | Note: |
|  | A positive value in the Shift Amount option implies that specified process path rotates clockwise, while a negative value indicates that you turn the process path counter-clockwise. |

| See: | Move the process path on the lines |
| --- | --- |

## 27.14 Direct Assignment

In the Part Edit mode, Click Direct Assignment button to open the Direct Assignment panel with the Turret Info dialog on the left side of the window.

The Direct Assignment option allows you to place common patterns on the part without adding geometry. Select a tool from the Turret Info dialog, and then select a type to create the patterns. You can define a Direct Assignment region by drawing the pattern on the part or sheet. The selected tool is then assigned to punch out the region.

| See: | Assignment between 2 points |
| --- | --- |
|  | Diagonal Assignment |
|  | Parameter Assignment |
|  | Hole Assignment |

### 27.14.1 Assignment between 2 points

Click to activate the Assignment between 2 Points panel.

The panel allows you to set the conditions for protrusion value, pitch, punch side, and the base point for single-hit assignment.

| Options | Description |
| --- | --- |
| Text boxes | These two text boxes allow you to specify the protrusion value. The value in the left text box indicates the protrusion at the starting point side of process path, while the value in the right reveals the protrusion at the ending point side. |
| Pitch | This option is used to specify the distance between tool hits when nibbling or shearing. |
|  | Note: |
|  | When shearing or nibbling process is executed, this option will be available. |
| Assignment Side | This option is used to specify the position to assign tools to process the open path. Every time you click this button, the image of the button will change. There are four choices: Left Side, Right Side, On Line, Auto. |
| Left Side | Place the tool to the left side of the pattern in the process direction. |
| On Line | Place the tool on the center of the pattern. |
| Right Side | Place the tool to the right side of the pattern in the process direction. |
| Auto | System will place the tool to the optimum position automatically |
| Correction During Single Hit | When a single hit is assigned, it is set at the center of the specified line. Click [LF], [CE], and [LB] to rearrange a tool at a position based on the start and end points. Every time you click this button, the image of the button will change. |
| CE | Assign the tool to single-hit the pattern. The tool center and pattern center will match. |
| LB | Assign the tool to single-hit the pattern from the starting point of the process path. |
| LF | Assign the tool to single-hit the pattern from the end point of the process path. |

| See: | Diagonal Assignment |
| --- | --- |
|  | Parameter Assignment |
|  | Hole Assignment |

### 27.14.2 Diagonal Assignment

Click  to activate the Diagonal Assignment panel.

This option allows you to assign a RE or SQ tool to cutout the inside part of the rectangle or square formed by two points of the diagonal. You can select or type a value in the Input C-axis Value to specify the angle of the pattern.

Example:

| 1. | Select a tool from the Turret Info window. |
| --- | --- |
| 2. | Select or type a value in the Input C-axis Value: text box. |
| 3. | Move the pointer to the left part layout area and click the left button of mouse to define the first point, and then drag it to shape a blue rectangle frame. |
| 4. | Click again to assign the specified tool to the pattern. |

| See: | Assignment between 2 points |
| --- | --- |
|  | Parameter Assignment |
|  | Hole Assignment |

### 27.14.3 Parameter Assignment

Click  to activate the Parameter Assignment panel.

| Option | Description |
| --- | --- |
| Pattern | Click arrow button to open a drop-down list. There are five patterns to choose. These options under the Pattern: drop down list will update as you select different pattern. |
| Direct Single Hit | Assign tools to single-hit pattern. |
| Line Pattern LAA | Assign tools as line at angle pattern. |
|  | Pitch | Select or type the distance between tools. |
|  | Quantity | Select or type the number of hits. |
|  | Pattern Angle | Select or type an angle for tilting pattern. |
|  | Include Standard Position | Place a check mark in this check box to determine whether base hit (first hit) is included or not. |
|  |  | Not Checked | Checked |
| Pattern Grid | Assign tools as grid pattern. |
|  | Prior Direction | Select the X or Y direction for processing priority. |
|  | Pitch | Pitch X and Y for tool hits for X and Y-axis. |
|  | Quantity | Specify the number of tool hits for X and Y-axis. |
|  | Pattern Angle | Select or type an angle for tilting pattern. |
|  | Include Standard Position | Place a check mark in this check box to determine whether base hit (first hit) is included or not. |
|  |  | Not Checked | Checked |
| Arc ARC | Assign tools as Arc pattern. |
|  | Radius | Radius of the pattern. |
|  | Starting Angle | Specify the starting angle for the pattern. |
|  | Pitch Angle | Angle pitch between tool hits. |
|  | Quantity | Specify the number of tool hits. |
|  | Fixed Tool Angle | When AI tool is selected, this option is available. |
|  |  | Not Checked | Checked |
| Round BHC | Assign tools as bold hole circle (BHC) pattern. |
|  | Radius | Radius of the pattern. |
|  | Starting Angle | Specify the starting angle for the pattern. |
|  | Quantity | Specify the number of tool hits. |
|  | Fixed Tool Angle | When AI tool is selected, this option is available. |
|  |  | Not Checked | Checked |
| Tool Standard Position | Specify a reference point as the first hit. |
| AI Tool Angle | Select or type a tilting degree for AI tool. |

| See: | Assignment between 2 points |
| --- | --- |
|  | Diagonal Assignment |
|  | Hole Assignment |

### 27.14.4 Hole Assignment

Click  to activate the Hole Assignment panel.

This panel allows you to specify the way to punch out the hole.

| Option | Description |
| --- | --- |
|  | The round hole is processed as follows. |
|  | The round hole is processed as follows. |
|  | Click this option, and then select a tool from the Please select the tool that are assigned in the middle window. |
|  | Click OK button and the round hole are processed as follows. |

| See: | Assignment between 2 points |
| --- | --- |
|  | Diagonal Assignment |
|  | Parameter Assignment |

## 27.15 Move/Copy Tool

You can use this function to move/rotate/reverse the tracks.

In part edit mode, click  on the toolbar to open Move/Copy Track panel on the right side of the window.

You may select one of the three options below,

| Option | Description |
| --- | --- |
| Move | Move the selected tracks in Move mode. Move the duplicates of the selected tracks in Copy mode. See: To move |
| Rotate | Rotate the selected tracks in Move mode. Rotate the duplicates of the selected tracks in Copy mode. See: To rotate |
| Reverse | Reverse the selected tracks in Move mode. Reverse the duplicates of the selected tracks in Copy mode. See: To reverse |
| Note: To switch between the Move and Copy mode, you can click the Move or Copy button in the parameter panel of each option. |

To move,

|  | Select Move option. The panel on the right side of the window will display as below. You can select either Specify the Standard Point or Specify X/Y Move Amount to move the selected tracks. |
| --- | --- |
| A1. | Select Specify the Standard Point option in Move mode from the Parameter panel. |
| A2. | Select the tracks that you want to move. The selected tracks will be highlighted. Right-click in the layout area and select Complete from the shortcut menu. |
| A3. | Click in the layout area to specify a standard point for the original tracks. Then, the current position of your mouse pointer will be the standard point for the imaginary tracks that appear. Move the mouse pointer to move the imaginary tracks. |
| A4. | Once you find the ideal place, click in the layout area to confirm the operation. |
| A5. | Click the Move button to switch to the Copy mode. In this case, we specify 2 in the enabled textbox on the right side of the button. |
| A6. | Now after the standard point is specified, 2 duplicates of the imaginary tracks will appear. |
| A7. | Once you find the ideal place, click in the layout area to finish copying. 2 duplicates of the selected tracks will be made without moving the originals. |
| B1. | You can also select Specify X/Y Move Amount from the Parameter panel to move the selected tracks. |
| B2. | The (X/(Y section will be enabled. Specify the move amount in the (X and (Y: textbox respectively. In this case, we specify 350 for (X, and specify –50 for (Y. |
| B3. | Select the tracks you want to move. Then right-click in the layout area and select Complete from the shortcut menu. The imaginary tracks will appear at the ( position that you have specified. |
| B4. | Click in the layout area to confirm the operation. |
| B5. | Click the Move button to switch to the Copy mode. In this case, we specify 3 in the enabled textbox on the right side of the button. |
| B6. | Now after we select Complete from the shortcut menu, 3 duplicates of the imaginary tracks will appear. Each duplicate is at the specified ( position in accordance with the previous one. Click in the layout area to confirm the operation and make the duplicates without moving the originals. |

To rotate,

|  | Select Rotate option. The panel on the right side of the window will display as below. |
| --- | --- |
| 1. | Select the tracks you want to rotate in the move mode. The selected tracks will be highlighted. Right-click in the layout area and select Complete from the shortcut menu. |
| 2. | Click in the layout area to specify a center point. The imaginary tracks will appear then and rotate with the moving angle of the mouse pointer. At the same time, the figure in the Rotation Angle: textbox will automatically update according to the current rotation angle of the imaginary tracks. |
| 3. | Once you find the ideal place, click in the layout area to rotate the tracks. |
|  | Alternatively, you can type a value into the Rotation Angle: textbox directly and press <Enter> to rotate the tracks. |
| 4. | Click the Move button to switch to the Copy mode. In this case, we specify 3 in the enabled textbox on the right side of the button. |
| 5. | Now after the center point is specified, 3 duplicates of the imaginary tracks will appear. Each duplicate is at the position of the ( angle amount in accordance with the previous one. |
| 6. | In this case, we specify 90 in the Rotation Angle: textbox and then press <Enter>. 3 duplicates of the selected tracks are made without moving the original. |

To reverse,

|  | Select Reverse option. The panel on the right side of the window will display as below. You can select either Specify the Standard Point or Axis Position to reverse the selected tracks. |
| --- | --- |
| A1. | Select Specify the Standard Point option in Move mode from the Parameter panel. Then click X Axis button. |
| A2. | Select the tracks that you want to reverse. The selected tracks will be highlighted. Right-click in the layout area and select Complete from the shortcut menu. |
| A3. | Click in the layout area to specify a standard point. The imaginary tracks will appear at the reverse position along the X-axis of the standard point. |
| A4. | If you click Y Axis button in the Parameter panel, the imaginary tracks will appear at the reverse position along the Y-axis of the standard point. |
| A5. | If you click Slant button in the Parameter panel, the current mouse pointer and the specified standard point will form a line. The imaginary tracks will appear at the reverse position along this line. Move the mouse pointer to move this line so that the position of the imaginary tracks will be changed accordingly. |
| A6. | Once you find the ideal place, click in the layout area to reverse the tracks. |
|  | X Axis | Y Axis | Slant |
| A7. | Click the Move button to switch to the Copy mode. You can reverse only one duplicate each time without moving the original tracks. |
|  | Note: In Reverse option, when you click the Move button to switch to Copy mode, the textbox on the right side of the button will NOT be enabled. In the Copy mode of Reverse option, only one duplicate can be made each time. |
| B1. | You can also select Axis Position from the Parameter panel to reverse the selected tracks. Click X Axis button as well. |
| B2. | Select the tracks that you want to reverse. The selected tracks will be highlighted. Right-click in the layout area and select Complete from the shortcut menu. |
| B3. | A horizontal line will appear across the current mouse pointer. The imaginary tracks will appear at the reverse position along this horizontal line. Move the mouse pointer to move this line so that the position of the imaginary tracks will be changed accordingly. |
| B4. | If you click Y Axis button in the Parameter panel, a vertical line will appear across the current mouse pointer. The imaginary tracks will appear at the reverse position along this vertical line. Move the mouse pointer to move this line so that the position of the imaginary tracks will be changed accordingly. |
|  | Note: The Slant button is NOT available when you select Axis Position. |
| B5. | Once you find the ideal place, click in the layout area to reverse the tracks. |
|  | X Axis | Y Axis |
| B6. | Click the Move button to switch to the Copy mode. You can reverse only one duplicate each time without moving the original tracks. |

## 27.16 Apply Assignment to the Same Inner

You can use this function to apply the assignment of an inner to the other same inners.

Same Inners refer to the inners with same shape and size, but may with different assignment.

In part edit mode, click  on the toolbar to open Apply Assignment to the Same Inner panel on the right side of the window.

You may select one of the two options below,

| Option | Description |
| --- | --- |
| All Holes | Apply the assignment of the selected inner to all the other same inners. See: To apply to all the same inners |
| Specified Hole | Apply the assignment of the selected inner to the specified same inners. See: To apply to the specified same inners |

To apply to all the same inners,

| 1. | Select All Holes in the Parameter panel. |
| --- | --- |
| 2. | Move the mouse pointer on one inner. All the same inners will be highlighted together automatically. |
| 3. | In this case, only the inner at the right side has two joints. Now we want to apply the assignment of two joints to all the other same inners. |
| 4. | Click the inner at the right side and then click the Apply button in the Parameter panel. Now all the same inners are with the two joints assignment. |

To apply to the specified same inners,

| 1. | Select Specified Hole in the Parameter panel. |
| --- | --- |
| 2. | In this case, only the inner on the right side has no joint. Now we want to apply the no joint assignment to the four inners in the lower row. |
| 3. | Click the inner on the right side and then click the four inners in the lower row. Finally, click the Apply button in the Parameter panel. Now all the four inners in the lower row are with no joint assignment. |

## 27.17 Fix Process Order

You can use this function to manually modify and fix the process order in each loop.

Note:

You can only modify and fix the process order in a single loop at one time.

In part edit mode, click  on the toolbar to open the Fix Process Order panel on the right side of the window.

Note:

The Fix Between Loops: check box is placed with a check mark by default so that the function section below is enabled. Removing the check mark will disable the function section.

Example

| 1. | In this result view, the part is processed in the following order. But now we want to modify the order for it. |
| --- | --- |
| 2. | Move the mouse pointer to the layout area, and click the elements one by one in the new order you want. |
|  | Note: For punch machines, there is always a last process element in the part. So you cannot modify the process order for it. The color of the last processing element will be highlighted according to the color you have specified. See: Color of Fix Process Order |
|  | Note: You can click Process Direction Change button to change the process direction for the selected element. |
| 3. | Click Create button to fix the order you have modified. The color of the fixed elements will be highlighted according to the color you have specified. See: Color of Fix Process Order |
| 4. | Select any of the fixed element and use or button to confirm the new process order. If you are still not satisfied, you can select the fixed elements and then click the Release button to cancel the modification for them. |
| 5. | Regenerate the NC code. Now the part will be processed in the order you have just specified. |
|  | Note: If you place a check mark in the Same Tooling Selection: check box, when you select any of the elements with the same tooling, all of them will be highlighted together at the same time. |

Color of Fix Process Order

| 1. | Click a color square to open the palette for the corresponding item. |
| --- | --- |
| 2. | Select a color for the item that you want it to display in the layout area. In this case, we select Yellow for Fix Process Order. |
| 3. | Now, the Fix Process Order color square becomes Yellow. The fixed elements in the layout area are in yellow accordingly. |

## 27.18 Change the Nibble Pitch

You can use this function to manually change the nibbling pitch.

In Part Edit mode, click  on the toolbar to open Change Nibbling Pitch panel on the right side of the window.

| 1. | Select the nibbling track that you want to change in the layout area. The selected track will be highlighted. The values in the Nibbling Pitch: textbox and Height: textbox will update according to the selected nibbling track. |
| --- | --- |
| 2. | You may either select Nibbling Pitch or Height option in the parameter panel to enable the textbox on the right side. Type a valid value in the enabled textbox and click the Apply button to change. |
|  | Note: The values of Nibbling Pitch and Height are interrelated. When you specify either of them and click Apply, the other will change accordingly. |

## 27.19 Show Tool

In Part Edit mode, click  on the toolbar to display the Turret Info window.

You can view the current turret and tools usage information in this window.

## 27.20 Option

In the Part Edit mode, click button to open the Option window.

Those options are designed to decide whether to display specified message when you plan to exit Part Edit mode.

| Item | Description |
| --- | --- |
| Do not display message of applying to part when exiting edit mode | Place a check mark in the check box, the system will not display the message of applying to part when you click button. You can make detailed setting in the following drop-down list. The system will execute it automatically. |
|  | If you clear a check mark in the check box, the system will display the following message after you save the setting and exit Manual Edit mode. Then the following dialog appears when you save the setting and exit Manual Edit mode You may make detailed setting in the Reflect Edit Result window. |
|  | Item | Description |
|  |  | Select this option to apply the editing result to the part you are editing. |
|  |  | Select this option to make detailed settings. There are four groups to select. |
|  |  | Apply the editing result to the same part with the same angle in the current sheet. |
|  |  | Apply the editing result to the same part in the current sheet. |
|  |  | Apply the editing result to the same part with the same angle in all sheets. |
|  |  | Apply the editing result to the same part in all sheets. |
| Do not display message after selecting cancel command | Place a check mark in the check box, the system will not display the message of applying to part when you click button. The system will ignore or save changes automatically when you click button by selecting an option from the following drop-down list. |
|  | If you clear a check mark in the check box, the system will display the following message when you want to cancel the command. |
|  | Click Yes button, the system will end your editing by ignoring the setting you have made. |
|  | Click No button and the system will end your editing by saving the setting you have made. |
|  | Click Cancel button, the system will return to editing mode. |
|  | Place a check mark in Don’t ask me again check box and click Yes/No button. At the same time the system will place a check mark in Do not display message after selecting cancel command check box automatically in the Option window. |
| Do not display message if space is not enough when add parts | Place a check mark in the check box, the system will not display the message when the space is not enough to add part. |
| Use command of editing single part to maximize window | Place a check mark in the check box and click Part Edit button, the system will expand AICAM main window so that it covers the full screen. |
| Window returns to the initial size after editing is complete | Place a check mark in the check box, the maximized window will restore to its previous size after you exit the manual edit mode. |
| Release the Command of not display message after version updated | Place a check mark in this check box, system will not keep the settings of Don’t Display Message you have specified in previous version during version update. |
| Collision check when moving parts | Place a check mark in this check box, the following message will prompt when parts move and collision happens. |

| Take the following part as an example: |
| --- |
| 1. | In Option window, place a check mark in the check box and select Inside Same Sheet and Part of Same Angle in Auto Apply: drop-down list. |
| 2. | Click OK to close the Option window. |
| 3. | In the Manual Edit toolbar, click Part Edit button to enter Part Edit mode. On the left part layout, select one part and add two joints. See Joint Edit |
| 4. | Click button to save the setting. Two joints are automatically added to the part in the same sheet and with the same angle. |

# Chapter 28: Auto Correction Condition Setup

|  | Click the Auto Cleaning Preference button in the main window to display the Autocorrection Condition Setup window. The options in this window allow you to control how the APDOM parses the patterns created in CAD. |
| --- | --- |
| Note: You should make settings in this window for the system to parse the loaded parts before loading them into Dr. ABE. |

| See: | Merge | Fill Gaps |
| --- | --- | --- |
|  | Remove Guidelines | Break |
|  | Get Outer Loop | Extra Entities Removal |
|  | Remove Slot | Small Entities Removal |
|  | Standard Hole Detection | Remove Holes Enclosing Pattern |
|  | Corner Slot | Parts Separation |
|  | Decimal Approximation | Arc Straightening |
|  | Slant Line Removal | Minute Gap Removal |
|  | Polylines To Arc | Special Hole Detection |
|  | Spline to Lines/Arcs | Delete Point |
|  | Ignore Conditions for Large Data |  |

## 28.1 Merge

This option is used to control whether the system parses a line consisting of several line segments into an integrated line or separate lines.

Example

| 1. | The top edge of the following part has a line consists several line segments (as indicated by the red rectangle). |
| --- | --- |
| 2. | If you remove the check mark from the Merge check box, the status of the option becomes Off. |
| 3. | The system will process each of the line segments separately. |
| 4. | If you place a check mark in the Merge check box, the status of the option becomes On. |
| 5. | The system will process the line segments as a single line. |

## 28.2 Fill Gaps

This option is used to control whether to fill the gaps on a pattern drawing. If you set the status of Fill Gaps to On, the system will fill the loop gaps that are within the defined tolerance to make a closed loop. You can specify the tolerance for this option. The minimum value is 0.001.

Example

| 1. | The following part has a gap in the upper right-hand corner. |
| --- | --- |
| 2. | If you remove the check mark from the Fill Gaps check box, the status of this option becomes Off. |
| 3. | Load the part mentioned above to Dr. ABE. Click the Nesting Plan button in the main window to open the Nesting Schedule window. The symbol appears in the CAD column. Click it and then a warning message appears. Dr. ABE will not process this part. The part boundary must be closed. |
| 4. | Place a check mark in the Fill Gap check box, and set a tolerance value in the text box as follows. |
| 5. | The system will close the gap. The part can be processed. |

## 28.3 Remove Guidelines

This option is used to control whether to remove guidelines on a pattern drawing. If you set the status of Remove Guidelines to On, the system will remove the guidelines.

Example

| 1. | You might use guidelines in CAD to locate a pattern. The crosshairs on the following part are used to locate the center points of the inner round holes. |
| --- | --- |
| 2. | If you remove the check mark from the Remove Guidelines check box, the status of the option becomes Off. The system considers these guidelines as open paths. |
| 3. | The system will use guidelines. |
| 4. | If you place a check mark in the Remove Guidelines check box, the status becomes On. |
| 5. | The system will remove the guidelines and will not process them. |

## 28.4 Break

This option is used to control whether to break the intersecting lines to remove the unnecessary line segments. If you set the status of Break to On, the system will break the intersecting entities.

Example

| 1. | A pattern on this part has intersecting lines. |
| --- | --- |
| 2. | When you remove the check mark from the Break check box, the status of this option becomes Off. The system will treat the intersecting lines as open paths. |
| 3. | The result will be as following: |
| 4. | When you place a check mark in the Break check box, the status becomes On. |
| 5. | The system will trim the segments. |

## 28.5 Get Outer Loop

This option is used to control whether to merge two intersecting patterns. If you set the status of Get Outer Loop to On, the system will recognize the outermost loop of the intersecting loops.

Example

| 1. | There are two patterns on this part that overlap. |
| --- | --- |
| 2. | If you remove the check mark from the Get Outer Loop check box, the status of the option becomes Off The system will process the two patterns as two separate loops. |
| 3. | The result will be as following: |
| 4. | If you place a check mark in the Get Outer Loop check box, the status becomes On. |
| 5. | The system will merge the two loops into one using the outermost boundary of the previous two loops. The remaining lines are removed from the part. |

## 28.6 Extra Entities Removal

This option is used to control whether to remove the extra entities. If you set the status of Extra Entities Removal to On, the system will remove the specified extra entities inside or outside parts.  You should define the maximum size of the extra entities to be removed.

Example

| 1. | The following part has extra line entities. |
| --- | --- |
| 2. | If you remove the check mark from the Extra Entities Removal check box, the status of the option becomes Off. |
| 3. | The result will be as following: |
| 4. | If you place a check mark in the Extra Entities Removal check box, the status of the option becomes On. Place a check mark in the Remove remnant(s) inside the fig. check box and type a value in the Max Size: text box to define the maximum entities size to be removed. |
| 5. | The system will remove the extra entities inside the part. |
| 6. | Set the conditions as follows. |
| 7. | The result will be as follows. |
| 8. | Set the conditions as follows. |
| 9. | The result will be as follows. |
| 10. | Set the conditions as follows. |
| 11. | The result will be as follows. |

## 28.7 Remove Slot

This option is used to control whether to remove the open path attached to an outer or inner loop. If the status of Remove Slot is set to On, you can place a check mark in the Outside or Inside check box to remove the open path attached to an inner loop or an outer loop.

Example

| 1. | The following part has open paths attached to the inner loop and outer loop. |
| --- | --- |
| 2. | If you remove the check mark from the Remove Slot check box, the status of this option becomes Off. |
| 3. | The system will process the open paths. |
| 4. | Place a check mark in the Remove Slot check box and then place a check mark in the Outside check box. |
| 5. | The system will remove the open path attached to the outer loop. |
| 6. | Remove the check mark from the Outside check box. Place a check mark in the Inside check box. |
| 7. | The system will remove the open path attached to the inner loop. |
| 8. | Place check marks in both the Outside and Inside check boxes. |
| 9. | The system will remove the open paths attached to the inner and outer loops. |

## 28.8 Small Entities Removal

This option is used to control whether to remove small entities (arcs or lines). If the status of Small Entities Removal is set to On, the system will remove the small entities. You can type a value to define the maximum value of Circle Radius and Line Length to be removed.

Example

| 1. | The following part has a very small entity in the bottom right-hand corner. |
| --- | --- |
| 2. | If you remove the check mark from the Small Entities Removal check box, the status of the option becomes Off. |
| 3. | The result will be as follows. |
| 4. | Place a check mark in the Small Entities Removal check box and then define the maximum value of circle radius as follows. |
| 5. | The small arc is removed. |

## 28.9 Standard Hole Detection

This option is used to control whether to parse the pattern made up of separate lines or arcs as a standard pattern. If the status of Standard Hole Detection is set to On, the system will detect standard holes, such as Rounds, Squares, Rectangles, Obrounds, Rounded Corner Rectangles, Single Ds and Double Ds. You can specify a parameter range for each type of hole. The status can be specified for each type of hole respectively, and will be used for standard hole detection. The default range for each type of hole is 200.

Example

| 1. | The following part has an inner round hole that consists of arcs. |
| --- | --- |
| 2. | If you remove the check mark from the Standard Hole Detection check box, the status of the option becomes Off. |
| 3. | The system process the round hole as a group of arcs and process them one by one. |
| 4. | Place a check mark in the Standard Hole Detection check box and then place a check mark in the Circle check box. You must also enable Use Machine Macro Shape. |
| 5. | The system will treat the inner hole as a standard pattern (hole) and process it. |

## 28.10 Remove Holes Enclosing Pattern

This option is used to control whether to remove the holes enclosing patterns. If the status of Remove Holes Enclosing Pattern is set to On, the system will remove the holes enclosing patterns.

Example

| 1. | The following part has holes enclosed within a triangle pattern. |
| --- | --- |
| 2. | If you remove the check mark from the Remove Holes Enclosing Pattern check box, the status of the option becomes Off. |
| 3. | The system treats the hole enclosing the patterns as an inner loop. |
| 4. | If you remove the check box from the Remove Holes Enclosing Pattern check box, the status becomes On. |
| 5. | The holes enclosing the patterns is removed. |

## 28.11 Corner Slot

This option is used to control whether to process a small circle pattern as a corner slot. If the status of Corner Slot is set to On, the system processes the circle as a corner slot. You can specify the circle radius range for the corner slot.

Example

| 1. | The following part has a circle pattern that encloses the upper right-hand corner. |
| --- | --- |
| 2. | If you remove the check mark from the Corner Slot check box, the status of the option becomes Off. |
| 3. | The system processes the circle as an inner loop. |
| 4. | Place a check mark in the Corner Slot check box and define the maximum circle radius value as follows. |
| 5. | The system will process the pattern as a corner slot. The lines are trimmed to the slot. |

## 28.12 Parts Separation

The option is used to control whether to separate a drawing into two individual parts. If the status of Parts Separation is set to On, the system will separate the combined patterns.

Example

| 1. | You have the following scenario: |
| --- | --- |
| 2. | If you remove the check mark from the Parts Separation check box, the status of the option becomes Off. |
| 3. | Load the part into Dr. ABE. A warning symbol appears in the Nesting Schedule window. |
|  | Click the symbol to display the details. |
| 4. | If you place a check mark in the Parts Separation check box, the status becomes On. |
| 5. | Load the part again. The system now separates the drawing into two individual parts. |

## 28.13 Decimal Approximation

This option is used to define the value digit after decimal, which is read by APDOM. If the status of Decimal Approximation is set to On, type a value to define the effective decimal digits.

Example

| 1. | Place a check mark in the Decimal Approximation check box and type 6 in the Decimal Approximation: text box to define the digit. |
| --- | --- |
| 2. | Check the XML output file after loading the part into Dr. ABE. The decimal digit is 6. The path of XML file is: |
|  | “D:\Program Files\Amada\AI-CAM\AIC_Main\Temp\1900200641185038525” |
| 3. | Type 1 in the text box to define the digit. |
| 4. | Check the XML output file after loading the part into Dr. ABE. The decimal digit is 1. |

## 28.14 Arc Straightening

This option is used to control whether to parse an arc into several lines. If the status of Arc Straightening is set to On, the system will change the arc to straight lines. You can type values to define the Minimum Radius and Tolerance. If the size of the arc exceeds the defined minimum radius, it will be parsed into several straight lines. The Tolerance determines the number of line divisions. The value in the Tolerance: text box is the maximum distance between the straight line and the portion of the arc the system replaces with the straight line.

Example

| 1. | You have the following scenario: |
| --- | --- |
| 2. | If you remove the check mark from the Arc Straightening check box, the status of the option will be Off. |
| 3. | The result is as follows. The arc remains. |
| 4. | If you place a check mark in the Arc Straightening check box and define the Minimum Radius and Tolerance as follows: |
| 5. | The system will divide the arc into four straight lines. |

## 28.15 Slant Line Removal

This option is used to control whether to remove the slant line. If the status for Slant Line Removal is set to On, the system will remove the slant line. You should type a value to define the Step Height. If the slant height is within this range, the system will replace the slant line with a straight line.

Example

| 1. | You have the following scenario. The part consists of a slant or inclined line. |
| --- | --- |
| 2. | If you remove the check mark from the Slant Line Removal check box, the status of the option becomes Off. |
| 3. | The result is as follows. The slant line remains. |
| 4. | If you place a check mark in the Slant Line Removal check box and then define the Step Height as follows: |
| 5. | The result is as follows. The slant line is replaced with a straight line. |

## 28.16 Minute Gap Removal

This option is used to control whether to remove the small gaps on a part drawing. If the status of Minute Gap Removal is set to On, the system will remove the small gap. You can type values to define the Range and Line Length.

Note: To use this option, you should place a check mark in the Fill Gaps check box first.

Example

| 1. | There is a small gap on the part. |
| --- | --- |
| 2. | If you remove the check mark from the Minute Gap Removal check box, the status of the option becomes Off. |
| 3. | After you load the part into Dr. ABE, a warning symbol appears in the Nesting Schedule window. |
|  | Click the symbol to display the details. |
| 4. | If you place check marks in both the Fill Gaps check box and the Minute Gap Removal check box, the status of the option becomes On. Type a value in the Line Length and Range: text boxes respectively. |
| 5. | The result is as follows. |

## 28.17 Polylines To Arc

This option is used to control whether to merge several lines into an arc. If the status of Polylines To Arc is set to On, the system will merge the polylines into an arc. You can type a value to define the Maximum Line Length. If the line length is equal to or less than the defined maximum length, the system will merge the line.

Example

| 1. | You have the following scenario: |
| --- | --- |
| 2. | If you remove the check mark from the Polylines To Arc check box, the status of the option becomes Off. |
| 3. | The result is as follows. |
| 4. | If you place a check mark in the Polylines To Arc check box and then define the Max. Line Length as follows: |
| 5. | The system will merge the lines into an arc. |

## 28.18 Special Hole Detection

If the status of Special Hole Detection is set to On, the system will detect the special holes.

Click the Setup Condition for Special Shape Hole button to open the Setup Conditions for Special Hole Type window. The options in this window allow you to define the special hole detection condition.

## 28.19 Spline to Lines/Arcs

This option is used to control whether and how to parse a spline into lines/arcs. You can also select a Spline Explode Mode and define whether to write to APDOM.

Example

| 1. | There is a spline inside the following part. |
| --- | --- |
| 2. | Different NC codes will be output when you select different Spline Explode Mode. |
| 3. | If you place a check mark in the Write to APDOM check box, the system will write all of the spline parsing information into APDOM. |
| 4. | If you remove the check mark from the Write to APDOM check box, the system will not write any information about the spline parsing into APDOM. |

## 28.20 Delete Point

This option is used to control whether to delete all of the points or some of the points inside the inner loops and outside the outer loops.

Example

| 1. | You have the following scenario. |
| --- | --- |
| 2. | When you select Delete All Points, the system will delete all of the points. |
| 3. | When you select Only delete outside of figure or inside of the hole, only the points outside the outer loop and inside the inner loop will be deleted. |

## 28.21 Ignore Conditions for Large Data

If the status of Ignore Conditions for Large Data is set to On, all conditions will be ignored, when the given data containing more than 10000 entities.

The following are exceptions:

- Spline To Lines/Arcs (Coarse mode will be used)

- Decimal Approximation also will be used only if the user has selected it.

| See: | Merge | Fill Gaps |
| --- | --- | --- |
|  | Remove Guidelines | Break |
|  | Get Outer Loop | Extra Entities Removal |
|  | Remove Slot | Small Entities Removal |
|  | Standard Hole Detection | Remove Holes Enclosing Pattern |
|  | Corner Slot | Parts Separation |
|  | Decimal Approximation | Arc Straightening |
|  | Slant Line Removal | Minute Gap Removal |
|  | Polylines To Arc | Special Hole Detection |
|  | Spline to Lines/Arcs | Delete Point |

# Index

A

Absolute	204

Access Information Manager	102

Add New Sheet	677

Add Parts	660

Add parts by opening a file	660

Add parts from SDD database	662

Add Parts in the Edit Mode	653

Adding a New PDC Station	550

Adding a New Station	543

Adjust the process path on the arcs	730

Adjust the process path on the lines	729

Advance	202, 205

Advanced Filter Window	496

AI Tool Angle Sort	343

Append or Remove a Dead Zone	545

Apply Assignment to the Same Inner	759

Arc Straightening	810

Assign SP Tool to Process Line Segment	294

Assign Tool Lines	715

Assign tools in the Effective Station Setting mode	452

Assign tools in the Turret Load Setting mode	449

Assignment	249

Assignment between 2 points	737

Attribute 1	513

Attribute 2	518

Auto Correction Condition Setup	774

Auto Position	390

Auto Sort	505

Automatic Material Selection	209

Avoid Dead Zone	351

B

Backup and Restore Material	51

Basic Dr.ABE Settings	16

Basic Joint Setting	392

Basic Operation	16

Basic Reposition Operation	668

Basic Shape	331

Basic Tool Information	508

Begin TK Edit	600

Break	783

C

CAD Data Drawing	69

CAD Data Load	115

Calculation	231

Change a Part Layout in Adjacent Mode	619

Change Check Boxes	158

Change Material	636

Change material by auto-calculation	637

Change Sheet Size	636

Change the Die Clearance of the Fixed Station	242

Change the Nibble Pitch	767

Change the Tool Angle to Process	240

Change the Tool Assignment	708

Clamp Avoidance	350

Clamp Information	29

Clamp Position Change	349, 352

Clamp Removal (Clamp #) 3	348

Clamp Setting	347

Clear Macros	383

Clearance	435

Clearance Setting	435

Code Definition	162

Codes	522

Combi-Sequence	335

Common Settings	397

Confirm Reposition	668

Confirm Schedule Tool	647

Confirm/Display Setting	653, 688

Contouring Assignment	265

Corner Joint Settings	398

Corner Slot	803

Create a Material Type	45, 46

Create a New PDC Turret Type	548

Create a New Turret Type	542

Creating a New File	176

D

Date	469, 476

Date Format	530, 535

Dates	149

Dead Zone	459

Dead Zone of the Station	460

De-burring	274

Decimal Approximation	808

Decrease Sheet Quantity When Save NC	100

Defining the Group ID for Parts	155

Defining the Part Priority	154

Delete a Sheet Information	48

Delete Point	823

Delete Sheet	571

Delete Trace	695

Detailed Joint Setting	396

Diagonal Assignment	739

Difference between Quality and Speed	73

Different Result of the Common Line Cutting	156

Direct Assignment	736

Display Area Pane	177

Display Different Colors for the Elements on the Part	74

Display Material Info	572

Display Plan Info	572

Display Station option	653

Divide Reposition	673

Do Stack	598

Download Material Type from AP100	49, 50, 55

Dr.ABE Main Window	16

Drawing	70

E

Edit	179

Edit a Material Type	46, 47

Edit Additional Elements Information	320

Edit Group	501

Edit Menu	122

Edit Mode Parameter Panel	612

Edit Mode Shortcut Menu	611

Edit of Elements	319

Edit of Path	318

Edit of Pickup/IJP Information window	602

Edit of Template	296

End Value	705

Example of Shift After Nesting	194

Expand All is Done after Automatic	78

Extra Entities Removal	787

F

File	178

File Menu	121

Fill Gaps	777

Filler Parts	430

Fit Tool Style Panel	285

Fix Process Order	763

Fixed Position	389

For Combination Process, Change Sheet Name Based on the Machine	471

For Reducing Bits of Vinyl	342

G

Generate data	317

Get Information from NC Data	485

Get Outer Loop	785

Getting Started	15

Grid Nesting	165

Grid Pattern	196

Group	422

Group Reposition	676

Grouping Priority	422

H

Help	181

Help Menu	130

Hierarchical Structure	171

Holder Information	31

Hole Assignment	744

Hole Pattern List	287

How to Backup Material	52

How to Backup the Parameters	95

How to Create a Remnant Sheet	58, 60, 218

How to Create a Skeleton Sheet	60, 62

How to Create Skeleton Sheet	216

How to Define the Start Point/Direction	192

How to Establish a Connection with a Server	117

How to Load CAD Data	115

How to Restore the Parameters	53, 96

I

Ignore Conditions for Large Data	824

IJP	34, 413

IJP Position	416

IJP Setting	414

IJP Strings	417

Import Ap100 SP/FM tools into Dr. ABE tool inventory	491

Import AP100 tools into Dr ABE tool inventory	489

Import AP100 Turret Layout	441

Import Buttons	488

Import DXF/DWG SP/FM Shapes	493

Information Area	80

Information Panel	604

Initial Clamp Position	203

Initial Part Number	88

Input size to change material	638

Insert Menu	123

J

Joint	228, 260, 388

Joint Edit	698

Joint Setting Condition	401

Joint Setting Window	215

Joint Type Table	395

L

Launch Dr.ABE	15

Layout Between Single Hit	723

License Registration	91

Light Attribute Editor	139

List Command	631

Loading / Unloading Device	373

Loading / Unloading End Position M-Code	376

Loading / Unloading Thickness M-Code	374

Loading/Unloading Device	36

M

M Codes	524

Machine Information	22

Machine Information Panel	23

Machine Parameter	21

Machine Parameter Toolbar	21

Machine Parameter Tree View	22

Machine Stop for Prototype	339

Machine Type	497

Main	233

Main Window	65

Manual Edit Mode	610

Manual Remnant Setting Window	625

Manual Reposition	640, 672

Manual Tool Assignment	684, 686

Manual Tool Assignment Shortcut Menu	688

Match To Line	292

Material	151, 160, 373

Material Manager Toolbar	44

Material Parameter	43, 44

Material Selection	208

Material Selection Priority	210

Material Type Information	55, 56

Max Distance between Corner Joint	395

Menus	121

Merge	725, 775

Methods for Specifying the Part Quantity	116

Min Distance between Corner	392

Min Distance between Wire	393

Min Joint Qty	395

Minimum	357

Minute Gap Removal	815

MJC	32, 403

MJC Setting	404

MJC/IJP Sequence	411, 413

Mouse Command	629

Move	613

Move the process path on the arcs	734

Move the process path on the lines	733

Move/Copy Tool	745

My Nesting Plan	132

N

NC Device Information	26

NC Generate	372

Nest Around Clamps	197

Nesting	152, 162

Nesting Logic 1	185

Nesting Logic 2	196

Nesting Name	466

Nesting Parts by the Production Schedule	189

Nesting Plan	118

Nesting Preference	184

Nesting Result List	556

Nesting Type	186

No Divide of Parts	359

Non AI Station is used with higher Priority	244

Number	474

Number of Clamp	204

O

Option	50, 103, 679, 769

Option window	107

Output G93	381

Output Outside of UV	370

Output Report	569

P

Pair Example	200

Parameter Assignment	740

Parameter Processing	98

Part as Process Unit	337

Part Edit Mode Parameter Panel	687

Part Edit Mode Shortcut Menu	686

Part Grid	632

Part in Part Example	200

Part Layout Shortcut Options	579

Part Name and Comment	147

Part Removal Sequence	418

Part Rotation	198

Part-Grid	366

Part-Grid Conditions	367

Parts List	136

Parts Properties	145

Parts Properties Advanced	159

Parts Properties Summary	119

Parts Separation	805

Part-Spacing and Nesting Border	201

Pattern Information and Assignment Pattern List	288

Pattern Pane	323

Pattern Setting	188

PDC Operation	527

Percent After G50	382

Perimeter Tool Assignment	253

Peripherals	28, 29, 403

Polylines To Arc	817

Preference File Pane	175

Preference File Shortcut Menu	176

Preference File Window	169

Preference Frame Current Folder	98

Preference Window Menu	178

Preference Window Overview	169

Preference Window Toolbar	181

Priority	483

Process	152

Process After	385

Process After Cutting Table	385

Process and User Define	166

Process Direction	363

Process Majority of Parts	361

Process multiple Line Segments as One Segment	236

Process Order	342

Process the Slit	273

Process Unit Sorting	346

Prototype Condition	425

Q

Quantity	148

Quick Start Guide	15

R

Range and Shape buttons	446, 488

Range toolbar	647

Remnant Edit	641

Remnant Name	529, 531

Remnant Name Items	529

Remnant/Skeleton Name	528

Remove	619

Remove Guidelines	781

Remove Holes Enclosing Pattern	801

Remove Slot	792

Reposition Command	667

Repositioning	355

Repositioning Type	356

Result View	553

Return to First Position	366

Reusable Sheet	213

Rotation with Different Condition	155

Row Height	574

S

Save MJC Data	596

Save NC Data	559

Save Part	574

Save Schedule/Output Report	562

Save SY4	561

Save SY5 as File	575

Save Template	690

Schedule	420, 421, 464

Schedule list	649

Schedule Name	473, 478

Schedule Name Items	474

Scheduling Priority	482

Search for Stock Tools	237

Search Stations	446, 447, 448, 449, 458

Search toolbar	647

Select Data	147

Select sheet code to change material	640

Select Skeleton/Remnant to Save when Saving NC	101

Selection Priority	212

Sequence	336

Sequence Edit	625

Sequence Number	470, 531, 536

Set End Value	763

Set End Value for laser	767

Setting of Outputting Result File window	108

Setup Sheet	380

Shape Data	331

Shape Edit area	317

Shape toolbar	647

Share the tool conditions among machines	510

Share to Size	221

Sheet and Each Part	338

Sheet Information	56, 57

Sheet Name	465, 472

Sheet Name Items	465

Shortcut Menu	138, 171

Show Tool	769

Simple Tool Assignment Setting for the Specified Template	283

Size Definition	161

Skeleton Name	534, 536

Skeleton Name Items	534

Sketch Material Tolerance	222

Sketch Nesting	163

Sketch Type	225

Slant Line Removal	813

Slit & V Notch	269

Slit Tool Assignment	252

Slot2&3	278

Small Entities Removal	796

Special Hole Detection	820

Special Information	161

Special Name	530, 535

Specify the range	626

Specify the Sheet Saver for the nesting tools to avoid reposition	516

Spline to Lines/Arcs	821

Splitter Bars	170

Stack Distance	407

Standard Hole Detection	799

Standard Nesting	163

Standard, Remnant, Skeleton and Sketch Materials	57, 58

Start Point/Direction	191

Stretch Tab	727, 732

SubInventory Window	487

SubInventory Window Toolbar	487

System	85

System Backup and Restore	94

System Determining Sheet by Material Name	88

System Information	91

System Requirements	15

System Setting	64, 86

T

T No	446, 447, 448, 449, 458

Take Out Information	39

Taking Out	405, 409

Taking Out Conditions	406

Taking Out Part Grid as One Part	167

Taking Out Station	166

Tapping Information	41

Template Detail Settings	289

Template Icon	313

Template Menu	298

Template Pane	298

Template Parameter	316

Template Toolbar	299

The Column Heading Shortcut Menu	576

The Customize Window	519

The Error List Panel	606

The NC Panel	607

The No. Column Heading Shortcut Menu	558

The Parts Information Panel	604

The Time Study Information Window	578

The Warning Information Window	578

Time Study	25

TK Process Type	429

To Assign attribute data to a pattern	141

Tool Assignment	230

Tool Assignment for Slanted Notch	259

Tool Assignment for the Vertical or Horizontal Notch	257

Tool Assignment Pane	330

Tool Inventory	485

Tool Inventory Table	497

Tool Inventory Table Shortcut Menu	501

Tool Lap Value	246

Tool Menu	124

Tool Sorting	344

Tool Window	508

Toolbar	647

Toolbars	130

Tooling Pattern	281

Tools	179

Tree View Pane	170

Tube Material Information	62

Turret and tool information table	650

Turret Image pane	652

Turret Layout	438

Turret Picture	449

Turret Section	441, 443, 445

Turret Section Toolbar	446

Turret Station List	456

Turret Type	539

Turret Type (PDC)	546

Turret Type (PDC) Window Items	546

Turret Type Window Items	539

Turret Type Window Short Cut Menu	545

Turret Type(PDC) Window Short Cut Menu	551

TurretLayout Window	444

U

Use Line Number	379

Use Setup Sheet	379

Use Sketch Material for Non-Sketch Parts	212, 213

Use Special Tool to Create Joints	262

Use Wizard for Sheet Size/Name	89

Utilization	198

Utilization Setting	83

V

View	64

View Buttons	447, 495

View menu	649

View Menu	122

View Y Size	72

W

Welcome to Dr. ABE	11

What’s New	12

Window	180

Wire Joint Setting	399, 400

Work Chute Information	37

X

X/Y/R/CPX/Area/Length/Width Explanation	387

Z

Zoom	81