Dr.ABE Operation Manual for EML

November   2007

# Content

Content	2

Chapter 1: Welcome to Dr. ABE	12

Chapter 2: What’s New	13

Chapter 3: Getting Started	16

3.1 System Requirements	16

3.2 Launch Dr.ABE	16

3.3 Quick Start Guide	16

3.3.1 Dr.ABE Main Window	16

3.3.2 Basic Dr.ABE Settings	17

3.3.3 Basic Operation	17

Chapter 4: Machine Parameter	22

4.1 Machine Parameter Toolbar	22

4.2 Machine Parameter Tree View	23

4.3 Machine Information	23

4.3.1 Machine Information Panel	25

4.3.2 Time Study	26

4.4 Laser Information	29

4.5 Cutting Condition	30

4.5.1 Cutting Condition Panel	31

4.5.1.1 How to Create a New Laser Material	32

4.5.1.2 How to Download Cutting Condition from VPSS	34

4.5.1.3 How to Download JKF Files	38

4.5.2 Cutting Condition Details	39

4.5.2.1 Cutting Process Information	40

4.5.2.2 Cutting Pierce Information	41

4.5.2.3 Cutting Edge Information	42

4.5.2.4 Nano Joint	43

4.5.2.5 Append	44

4.5.2.6 Machine Parameter	45

4.5.2.6.1 Line/Arc	45

4.5.2.6.2 Macro Shape	47

4.5.2.6.3 Exception to Averaging	51

4.6 NC Device Information	53

4.7 Peripherals	55

4.7.1 Oscillator	56

4.7.2 Take Out Information	58

4.7.3 Clamp Information	60

4.7.4 Holder Information	62

4.7.5 MJC	63

4.7.6 IJP	64

4.7.7 Loading/Unloading Device	66

4.7.8 Work Chute Information	67

4.7.9 Tapping Information	69

Chapter 5: Material Parameter	71

5.1 Material Manager Toolbar	71

5.1.1 Create a Material Type	72

5.1.2 Edit a Material Type	73

5.1.3 Delete a Sheet Information	75

5.1.4 Download Material Type from AP100	76

5.1.5 Option	77

5.1.6 Backup and Restore Material	78

5.1.6.1 How to Backup Material	79

5.1.6.2 How to Restore Material	80

5.2 Material Type Information	81

5.3 Sheet Information	82

5.3.1 Standard, Remnant, Skeleton and Sketch Materials	84

5.3.2 How to Create a Remnant Sheet	85

5.3.3 How to Create a Skeleton Sheet	87

5.4 Tube Material Information	88

Chapter 6: System Setting	90

6.1 View	90

6.1.1 Main Window	91

6.1.2 CAD Data Drawing	95

6.1.3 Drawing	96

6.1.3.1 View Y Size	98

6.1.3.2 Difference between Quality and Speed	99

6.1.3.3 Display Different Colors for the Elements on the Part	99

6.1.3.4 Expand All is Done after Automatic	103

6.1.4 Information Area	105

6.1.5 Zoom	106

6.1.6 Utilization Setting	108

6.2 System	110

6.2.1 System Setting	111

6.2.1.1 Initial Part Number	112

6.2.1.2 System Determining Sheet by Material Name	112

6.2.1.3 Use Wizard for Sheet Size/Name	113

6.2.2 System Information	115

6.2.3 License Registration	115

6.2.4 System Backup and Restore	118

6.2.4.1 How to Backup the Parameters	119

6.2.4.2 How to Restore the Parameters	120

6.2.5 Preference Frame Current Folder	122

6.2.6 Parameter Processing	122

6.2.6.1 Decrease Sheet Quantity When Save NC	124

6.2.6.2 Select Skeleton/Remnant to Save when Saving NC	125

6.2.7 Access Information Manager	126

6.3 Option	127

6.3.1 Option window	130

6.3.2 Setting of Outputting Result File window	133

Chapter 7: CAD Data Load	140

7.1 How to Load CAD Data	140

7.2 Methods for Specifying the Part Quantity	141

7.3 How to Establish a Connection with a Server	142

Chapter 8: Nesting Plan	144

8.1 Parts Properties Summary	144

8.2 Menus	146

8.2.1 File Menu	146

8.2.2 Edit Menu	147

8.2.3 View Menu	147

8.2.4 Insert Menu	148

8.2.5 Tool Menu	149

8.2.6 Help Menu	155

8.3 Toolbars	155

8.4 My Nesting Plan	157

8.5 Parts List	161

8.5.1 Shortcut Menu	163

8.5.2 Light Attribute Editor	164

8.5.2.1 To Assign attribute data to a pattern	166

8.6 Parts Properties	171

8.6.1 Part Name and Comment	173

8.6.2 Select Data	173

8.6.3 Quantity	174

8.6.4 Dates	175

8.6.5 Material	177

8.6.6 Process	178

8.6.7 Nesting	178

8.6.7.1 Defining the Part Priority	180

8.6.7.2 Defining the Group ID for Parts	181

8.6.7.3 Rotation with Different Condition	181

8.6.7.4 Different Result of the Common Line Cutting	183

8.6.8 Change Check Boxes	184

8.7 Parts Properties Advanced	186

8.7.1 Material	187

8.7.2 Special Information	188

8.7.3 Size Definition	188

8.7.4 Code Definition	189

8.7.5 Nesting	189

8.7.5.1 Standard Nesting	190

8.7.5.2 Sketch Nesting	190

8.7.5.3 Grid Nesting	192

8.7.6 Process and User Define	193

8.7.7 Taking Out Station	193

8.7.8 Taking Out Part Grid as One Part	194

Chapter 9: Preference File Window	196

9.1 Preference Window Overview	196

9.1.1 Splitter Bars	197

9.1.2 Tree View Pane	198

9.1.2.1 Hierarchical Structure	198

9.1.2.2 Shortcut Menu	199

9.1.3 Preference File Pane	202

9.1.3.1 Creating a New File	202

9.1.3.2 Preference File Shortcut Menu	203

9.1.4 Display Area Pane	204

9.2 Preference Window Menu	204

9.2.1 File	205

9.2.2 Edit	206

9.2.3 Tools	206

9.2.4 Window	207

9.2.5 Help	208

9.3 Preference Window Toolbar	208

Chapter 10: Nesting Preference	211

10.1 Nesting Logic 1	212

10.1.1 Nesting Type	213

10.1.2 Pattern Setting	215

10.1.2.1 Nesting Parts by the Production Schedule	216

10.1.3 Start Point/Direction	218

10.1.3.1 How to Define the Start Point/Direction	218

10.1.3.2 Example of Shift After Nesting	220

10.2 Nesting Logic 2	222

10.2.1 Grid Pattern	223

10.2.2 Nest Around Clamps	224

10.2.3 Part Rotation	225

10.2.4 Utilization	225

10.2.4.1 Pair Example	226

10.2.4.2 Part in Part Example	227

10.3 Initial Clamp Position	228

10.3.1 Number of Clamp	229

10.3.2 Absolute	229

10.3.3 Advance	230

10.4 Part-Spacing and Nesting Border	233

10.4.1 Advance	233

10.5 Material Selection	234

10.5.1 Automatic Material Selection	235

10.5.1.1 Material Selection Priority	235

10.5.1.2 Selection Priority	237

10.5.1.3 Use Sketch Material for Non-Sketch Parts	238

10.5.1.4 Don’t nest parts inside skeleton area	238

10.5.2 Reusable Sheet	238

10.5.3 Joint Setting Window	240

10.5.4 How to Create Skeleton Sheet	242

10.5.5 How to Create a Remnant Sheet	243

10.6 Share to Size	247

10.6.1 Sketch Material Tolerance	248

10.6.2 Sketch Type	251

10.6.3 Joint	253

Chapter 11: Tool Assignment	255

11.1 Main	256

11.1.1 Assign	257

11.1.2 Laser Pierce	257

11.1.3 Selection by Overview	261

11.1.3.1 Process the Perimeters	261

11.1.3.2 Process Corner Notch	263

11.1.3.3 Process Notch	264

11.1.4 Percentage of Laser and Punch	265

11.2 Detail Setting	266

11.2.1 Laser/Punch-1 (Perimeter and Notch Setting for Combination Process)	266

11.2.2 Laser/Punch-2 (Line and Arc Setting for Combination Process)	270

11.3 Laser Assignment	274

11.3.1 Lead In/Out /Pierce Panel	274

11.3.1.1 Lead In/Out Table	274

11.3.1.2 Collision Check Tolerance	278

11.3.1.3 Process Pierce First	279

11.3.1.4 The Custom Lead In/Out Definition Window	279

11.3.1.4.1 Creating a Lead-in or Lead-out Type	280

11.3.1.4.2 Editing a Lead-in or Lead-out	284

11.3.1.4.3 Deleting a Lead In or Lead Out	287

11.3.1.4.4 Applying a Lead In or Lead Out	288

11.3.2 Path Assignment Method	290

11.3.2.1 Etch Layout	291

11.3.2.2 Open Path	291

11.3.2.3 Treat an Open Path as a Slit	293

11.3.2.4 Bend Line Etching	295

11.3.2.5 Unfold Reference Line	297

11.3.2.6 Internal-tab Bend	298

11.3.2.7 Use Machine Macro Shape	299

11.3.2.8 Pre-hole of Extrusion or Tapping	301

11.3.2.9 Points	304

11.3.2.10 Marking Setting	307

11.3.2.11 Cut Condition Table	307

11.3.2.12 Reference of Cutting Condition (Size/Shape)	311

11.3.2.13 Rectangle Tube	311

11.3.3 Tab/Corner Process	312

11.3.3.1 Joint length and Lead In/Out length	313

11.3.3.2 Nano Joint	317

11.3.3.3 Corner	317

11.3.3.4 Common Line Cutting	319

11.3.4 Detail	321

11.3.4.1 Lead In& Pierce Details	322

11.3.4.1.1 Decision Method of Lead Position	323

11.3.4.1.2 Decision Method of Lead Length	332

11.3.4.1.3 Detail Setting for Processing Pierce First	333

11.3.4.1.4 Marking Setting for Etching [Count]	335

11.3.4.1.5 Collision Check	337

11.3.4.2 Cutting Condition	340

11.3.4.2.1 Line/Arc	341

11.3.4.2.2 Macro Shape	343

11.3.4.2.3 Exception to Averaging	347

11.3.4.3 Assignment Logic	349

11.4 Calculation	350

11.4.1 Main	353

11.4.1.1 Process multiple Line Segments as One Segment	355

11.4.1.2 Search for Stock Tools	357

11.4.1.3 Change the Tool Angle to Process	359

11.4.1.4 Change the Die Clearance of the Fixed Station	361

11.4.1.5 Non AI Station is used with higher Priority	363

11.4.1.6 Check the maximum tool	364

11.4.1.7 Check the minimum tool	367

11.4.2 Tool Lap Value	368

11.4.3 Assignment	371

11.4.3.1 Slit Tool Assignment	374

11.4.3.2 Perimeter Tool Assignment	375

11.4.3.3 Tool Assignment for the Vertical or Horizontal Notch	378

11.4.3.4 Tool Assignment for Slanted Notch	380

11.4.4 Joint	381

11.4.4.1 Use Special Tool to Create Joints	383

11.4.5 Contouring Assignment	386

11.4.6 Slit & V Notch	390

11.4.6.1 Process the Slit	394

11.4.7 De-burring	395

11.4.8 Slot2&3	399

11.5 Tooling Pattern	402

11.5.1 Simple Tool Assignment Setting for the Specified Template	405

11.5.2 Fit Tool Style Panel	407

11.5.2.1 Hole Pattern List	409

11.5.2.2 Pattern Information and Assignment Pattern List	410

11.5.2.3 Template Detail Settings	410

11.5.3 Match To Line	414

11.5.3.1 Assign SP Tool to Process Line Segment	416

11.6 Edit of Template	418

11.6.1 Template Pane	419

11.6.1.1 Template Menu	421

11.6.1.2 Template Toolbar	421

11.6.1.3 Template Icon	434

11.6.1.4 Template Parameter	436

11.6.1.5 Shape Edit area	437

11.6.1.6 Generate data	437

11.6.1.7 Edit of Path	438

11.6.1.8 Edit of Elements	439

11.6.1.9 Edit Additional Elements Information	440

11.6.2 Template Creation Pane	442

11.6.2.1 Tool Assignment Pane	448

11.6.2.2 Basic Shape	449

11.6.2.3 Shape Data	449

Chapter 12: Combi-Sequence	456

12.1 General Sequence	457

12.1.1 Effect Setting	457

12.1.1.1 Sheet and Each Part	459

12.1.1.2 Machine Stop for Prototype	460

12.1.2 Starting Point/Direction	463

12.1.3 Sequence by Dividing the Sheet	463

12.1.4 Distance Between Tooling	464

12.1.5 Sort of Laser & Punch	465

12.1.6 Sort by Process after Cutting	467

12.2 Repositioning	469

12.2.1 Repositioning Type	470

12.2.1.1 Minimum	470

12.2.1.2 No Divide of Parts	473

12.2.1.3 Method of Dividing Long Parts	475

12.2.2 Minimum Lap Amount	477

12.2.3 Process Majority of Parts	477

12.2.4 Process Direction	479

12.2.5 Return to First Position	482

12.3 Clamp Setting	482

12.3.1 Clamp Removal (Clamp #3)	483

12.3.2 Clamp Position Change	484

12.4 Laser Sequence	485

12.4.1 Sequence Processing Object	486

12.4.2 Change Lead In for Shorten Traverse	488

12.4.3 Flip Macro Pattern for Shorten Traverse	490

12.5 Auto Cutout Avoidance	492

12.5.1 Auto Cutout Avoidance	493

12.5.2 Target Traverse	494

12.5.3 Traverse Setting	496

12.5.3.1 Additional Width (For Material, Process Range)	496

12.5.3.2 Additional Width (Traverse)	497

12.5.3.3 Do Not Avoid if Distance is Greater than Times of Original	498

12.5.3.4 Do Not Avoid if the Distance is Smaller than Times of Original	498

12.5.3.5 Do Not Include the Cutting Bigger Than	498

12.5.3.6 Do Not Avoid Cutout with Joint	501

12.5.4 High-Speed Shutter Less Setting	502

12.6 Punch Clamp Setting	506

12.6.1 Avoid Dead Zone	507

12.6.2 Passage Avoidance in the Turret When Moving Axis	509

12.7 Punch Sequence	512

12.7.1 Angle of Turret	512

12.7.1.1 Mix Sequence within	514

12.7.2 AI Tool Angle Sort	516

12.7.3 Sort Function	517

12.8 Part-Grid	518

12.8.1 Part-Gird Condition	519

12.8.2 Common Line Cutting	522

12.8.3 Output Outside of UV	524

Chapter 13: NC Generate	526

13.1 Material	527

13.2 Use Setup Sheet	528

13.3 Setup Sheet	529

13.4 Output G93	531

13.5 Percent After G50	531

13.6 Output work size comment at the end of G92 command line	532

13.7 Use G42/G42	533

13.8 Z Height M104Zx	534

13.9 Is G01 Continued	534

13.10 Unloading Skeleton M Code	535

13.11 M 108 After M104 Code	537

13.12 Loading/Unloading Device	538

13.13 Loading/ Unloading Thickness M-Code	539

13.14 Loading/ Unloading End Position M-Code	541

Chapter 14: Process After	544

14.1 Process After Cutting Table	545

14.1.1 Object	547

14.1.2 X/Y/R/CPX/Area/Length/Width Explanation	548

14.1.3 How to Output the Z Value	550

14.2 Joint	550

14.2.1 Fixed Position	551

14.2.2 Auto Position	552

14.2.3 Basic Joint Settings	554

14.2.3.1 Min Distance between Corner	554

14.2.3.2 Min Distance between Wire	556

14.2.3.3 Min Joint Qty	558

14.2.3.4 Max Distance for Corner Joint	559

14.2.4 Joint Type Table	561

14.2.5 Detail Settings	561

14.2.5.1 Common Settings	562

14.2.5.2 Corner Joint Settings	566

14.2.5.3 Wire Joint Setting	571

14.2.5.4 Chute (L) Setting	575

14.2.5.5 Chute Setting	577

14.2.6 Joint Setting Conditions	577

14.2.7 Cut Plate	578

Chapter 15: Peripherals	582

15.1 MJC	582

15.1.1 MJC Setting	583

15.1.2 Laser Joint	584

15.2 IJP	585

15.2.1 IJP Setting	586

15.2.2 IJP Position	588

15.2.3 IJP Strings	588

15.3 Parts Removal Sequence	589

15.4 Take Out	590

15.4.1 Taking Out Conditions	590

15.4.2 Stack Distance	591

15.4.3 Taking Out	594

15.5 MJC/IJP Sequence	597

15.6 Schedule	597

Chapter 16: Group	601

16.1 Grouping Priority	601

16.2 Prototype Condition	604

16.3 TK Process Type	608

16.4 Filler Parts	609

Chapter 17 Clearance	614

17.1 Clearance Setting	614

Chapter 18: Turret Layout	618

18.1 Import AP100 Turret Layout	620

18.2 TurretLayout Window	623

18.3 Turret Section	624

18.3.1 Turret Section Toolbar	625

18.3.2 Range and Shape buttons	625

18.3.3 View Buttons	626

18.3.4 T No.	626

18.3.5 Search Stations	627

18.3.6 Turret Picture	628

18.3.6.1 Assign tools in the Turret Load Setting mode	628

18.3.6.2 Assign tools in the Effective Station Setting mode	631

18.3.7 Turret Station List	635

Chapter 19 Dead Zone	638

19.1Dead Zone of the Station	639

Chapter 20: Schedule	643

20.1 Sheet Name	644

20.1.1 Sheet Name Items	645

20.1.2 Nesting Name	645

20.1.3 Date	649

20.1.4 Sequence Number	650

20.1.5 For Combination Process, Change Sheet Name Based on the Machine	651

20.1.6 Sheet Name	651

20.2 Schedule Name	652

20.2.1 Schedule Name Items	653

20.2.2 Sequence Number	654

20.2.3 Date	656

20.2.4 Schedule Name	658

20.3 Scheduling Priority	662

20.3.1 Priority	663

20.3.2 Separate Schedule	665

Chapter 21: Tool Inventory	668

21.1 SubInventory Window	669

21.1.1 SubInventory Window Toolbar	669

21.1.2 Range and Shape buttons	670

21.1.3 Import Buttons	670

21.1.3.1 Import AP100 tools into Dr ABE tool inventory	671

21.1.3.2 Import Ap100 SP/FM tools into Dr. ABE tool inventory	673

21.1.3.3 Import DXF/DWG SP/FM Shapes	675

21.1.4 View Buttons	677

21.1.5 Advanced Filter Window	677

21.1.6 Machine Type	678

21.2 Tool Inventory Table	678

21.3 Tool Inventory Table Shortcut Menu	682

21.3.1 Edit Group	682

21.3.2 Auto Sort	686

21.4 Tool Window	689

21.4.1 Basic Tool Information	689

21.4.1.1 Share the tool conditions among machines	691

21.4.2 Attribute 1	694

21.4.2.1 Specify the Sheet Saver for the nesting tools to avoid reposition	696

21.4.3 Attribute 2	698

21.4.3.1 The Customize Window	699

21.4.4 Codes	702

21.4.4.1 M Codes	704

21.4.5 PDC Operation	706

Chapter 22: Remnant/Skeleton Name	708

22.1 Remnant Name	709

22.1.1 Remnant Name Items	709

22.1.2 Special Name	710

22.1.3 Date Format	710

22.1.4 Sequence Number	711

22.1.5 Remnant Name	711

22.2 Skeleton Name	713

21.2.1 Skeleton Name Items	714

21.2.2 Special Name	715

21.2.3 Date Format	715

21.2.5 Skeleton Name	715

Chapter 23: Turret Type	719

23.1 Turret Type Window Items	719

23.2 Create a New Turret Type	722

23.3 Adding a New Station	723

23.4 Turret Type Window Short Cut Menu	725

Chapter 24: Turret Type (PDC)	726

24.1 Turret Type (PDC) Window Items	726

24.2 Create a New PDC Turret Type	728

24.3 Adding a New PDC Station	730

24.4 Turret Type(PDC) Window Short Cut Menu	731

Chapter 25: Result View	733

25.1 Nesting Result List	736

25.1.1 The No. Column Heading Shortcut Menu	737

25.1.1.1 Save NC Data	739

25.1.1.2 Save SY4	740

25.1.1.3 Save Schedule/Output Report	741

25.1.1.4 Output Report	748

25.1.1.5 Delete Sheet	750

25.1.1.6 Display Material Info	751

25.1.1.7 Display Plan Info	751

25.1.1.8 Row Height	753

25.1.1.9 Save Part	753

25.1.1.10 Save SY5 as File	754

25.1.2 The Column Heading Shortcut Menu	755

25.1.3 The Warning Information Window	757

25.1.4 The Time Study Information Window	757

25.2 Part Layout Shortcut Options	758

25.2.1 Save MJC Data	774

25.2.2 Do Stack	776

25.2.3 Begin TK Edit	778

25.2.3.1 Edit of Pickup/IJP Information window	780

25.3 Information Panel	782

25.3.1 The Parts Information Panel	782

25.3.2 The Error List Panel	784

25.3.3 The NC Panel	785

Chapter 26: Manual Edit Mode	788

26.1 Manual Edit Mode Shortcut Menu	789

26.2 Manual Edit Mode Parameter Panel	791

26.3 Confirm/Display Setting	793

26.4 Move	801

26.5 Add Part	807

26.5.1 Add parts by opening a file	807

26.5.2 Add parts from SDD database	809

26.6 Remove	815

26.7 Remnant Edit	822

26.8 Change Material	831

26.8.1 Change material by auto-calculation	832

26.8.2 Input size to change material	833

26.8.3 Select sheet code to change material	835

26.9 Part Grid	836

26.10 Sequence Edit	844

26.10.1 Specify the range	845

26.10.2 Mouse Command	847

26.10.3 List Command	850

26.11 Reposition Command	850

26.11.1 Basic Reposition Operation	852

26.11.1.1 Confirm Reposition	852

26.11.1.2 Manual Reposition	855

26.12.2 Divide Reposition	856

26.12.3 Group Reposition	860

26.12 Confirm Schedule Tool	861

26.12.1 Toolbar	862

26.12.1.1 Range toolbar	862

26.12.1.2 Shape toolbar	862

26.12.1.3 Search toolbar	862

26.12.1.4 View menu	863

26.12.2 Schedule list	863

26.12.3 Turret and tool information table	864

26.13.4 Turret Image pane	866

26.12.5 Display Station option	867

26.13 Add New Sheet	867

26.14 Option	869

Chapter 27: Manual Tool Assignment	874

27.1 Part Edit Mode Shortcut Menu	876

27.2 Part Edit Mode Parameter Panel	877

27.3 Confirm/Display Setting	879

27.4 Save Template	882

27.5 Delete Trace	888

27.6 Joint Edit	891

27. 7 End Value	899

27.8 Sequence Command in Parts	904

27.9 Lead In Edit	908

27.10 Change the Tool Assignment	917

27.11 Assign Tool-Lines	924

27.12 Layout Between Single Hit	932

27.13 Merge	935

27.14 Stretch	938

27.14.1 Adjust the process path on the lines	940

27.14.2 Adjust the process path on the arcs	941

27.15 Shift	943

27.15.1 Move the process path on the lines	945

27.15.2 Move the process path on the arcs	946

27.16 Direct Assignment	948

27.16.1 Assignment between 2 points	949

27.16.2 Diagonal Assignment	951

27.16.3 Parameter Assignment	952

27.16.4 Hole Assignment	955

27.17 Move/Copy Tool	957

27.18 Apply Assignment the Same Inner	969

27.19 Fix Process Order	969

27.20 Change the Nibbling Pitch	969

27.21 Laser Hole Division	969

27.22 Show Tool	969

27.23 Option	969

Chapter 28: Auto Correction Condition Setup	969

28.1 Merge	969

28.2 Fill Gaps	969

28.3 Remove Guidelines	969

28.4 Break	969

28.5 Get Outer Loop	969

28.6 Extra Entities Removal	969

28.7 Remove Slot	969

28.8 Small Entities Removal	969

28.9 Standard Hole Detection	969

28.10 Remove Holes Enclosing Pattern	969

28.11 Corner Slot	969

28.12 Parts Separation	969

28.13 Decimal Approximation	969

28.14 Arc Straightening	969

28.15 Slant Line Removal	969

28.16 Minute Gap Removal	969

28.17 Polylines To Arc	969

28.18 Special Hole Detection	969

28.19 Spline to Lines/Arcs	969

28.20 Delete Point	969

28.21 Ignore Conditions for Large Data	969

Index	969

# Chapter 1: Welcome to Dr. ABE

Welcome to Dr. ABE. Dr. ABE is a sophisticated application used for sheet metal fabrication. The software allows you to reduce the costs associated with part production and helps to improve your productivity. Dr. ABE is designed to create the most efficient nest jobs according to the settings that you specify. You can also edit and verify the nesting results until you are satisfied with the nesting plan.

Dr. ABE has the following features:

- User-friendly operation. Nearly all operations, from tool assignment to NC code generation are automated.

- Strong nesting functions and high material utilization, logical and appropriate tool assignments, optimized sequencing, etc.

- Flexible compatibility. The software is compatible with most CAD data formats (*.dwg, *.iga, *.dxf, etc.). Dr. ABE also supports the AP100 database system (MiniSDD, SDDJ).

For more information, please refer to the corresponding chapters

# Chapter 2: What’s New

This manual outlines the following new features  in the latest version of the software.

New Features

System Setting                 Multiple Language Support

Support eight languages, such as Japanese, Chinese, Korean, English and four European languages.

System Setting                  CSV Format Support

Support the output of the nesting result and nesting plan in the CSV files.

Machine Setting                Copy Machine Parameter

Support to copy the machine parameter.

Machine Setting                Backup and Restore Machine Parameters

Support to backup or restore the parameters setting for the corresponding machines.

Material Management       Material Manager Multiple Selection

You can select more than one machine and modify sheet information for all the machines you have selected.

Nesting                                   Multiple Figures Nesting Support

Support to combine the multiple figures to generate the figure datas automatically by nesting.

NC Generate Condition        Output G92 to show the process range rectangle size

Output the comments of the min. work size that necessary for processing.

NC Generate Condition         Output G93 to display the coordinate in the AP100 report

Output the AP100 report and display the G93 coordinates.

NC Generate Condition        Output G93 for A Single Part

Support the output of G93 even though only one part is processed.

Result View                            Print the Nesting Result View

Print the nesting result view.

Result View                            Output Report

Output the report from the nesting result view.

Result View                            IJP(Int Jet Printer)Error Message

The data can’t be generated when the output position of IJP was interfered by the hole, then the result view will display the error message.

Result View                            Save Sheet Information

Assignment result can be saved as the sheet information.

Result view                             Save SY4 File

You can save nesting result (nesting plan/common info/condition/machine info/material) except for preference information in SDD/MiniSDD database and save as file after auto

execution.

Result view                             Row Height

You can adjust cell height for better view in result view by typing a value in Row Height: text box.

Result view                            Ignore Hole in TK Edit

Provide the auto detect function with ignoring holes based on the size you have specified.

Peripherals                          TK Process Type

Provide special assignment and process sequence for TK parts.

Peripherals                         Part TK Process Sequence

Consider the final cutting position of the part, before determining the TK sequence.

Combi-Sequence                       Sequence by Dividing the Sheet-Option

Sequence by dividing the sheet on the part layout area.

Combi-Sequence                       Machine Stop for Prototype

You can determine whether system outputs machine stop for prototype or not.

Combi-Sequence                   Output Outside of UV

Select whether the specified M code is included in the UV macro commands or not.

Manual Edit                             Remnant Edit

You can add or edit the Remnant in the manual edit mode.

Manual Edit                             Sequence Edit

You can define the sequence to process the parts.

Manual Edit                             Add New Sheet

You can add the new sheet.

Manual Edit                             Option

You can make the setting in the manual edit view, for example, decide to display the message or not.

Manual Edit                             Reposition Command

You can make the setting of reposition command manually.

Manual Edit                            Change Material

You can change the sheet size and sheet code of material.

Manual Edit                                Part Grid

You can make the setting to generate or edit the data of grid parts.

Manual Edit                               Confirm Schedule Tool

You can check tools in use and station status of a sheet or a schedule.

Manual Tool Assignment          Sequence Command in Parts

You can manually change the process sequence of parts.

Manual Tool Assignment          Laser Hole Division

You can manually make settings to divide laser holes.

Manual Tool Assignment          Change the Nibbling Pitch

You can manually change the nibbling pitch.

Manual Tool Assignment          Apply Assignment to the Same Inner

You can manually apply the assignment same with specified inner to the same inner.

Manual Tool Assignment          Direct Assignment

You can manually place common patterns on the part without adding geometry.

Manual Tool Assignment          Change the Tool Assignment

You can manually change the tool assignment for the part.

Tool Assignment                        De-burring Tool Assignment

Provide functions of assigning de-burring tools automatically.

Tool Assignment                        Slot 2&3 Tool Assignment

Provide functions of assigning slot2&3 tools automatically.

Tool Assignment                      Adding Tool to Turret/PDC/HMX

You can add more than one tool at a time to Turret/PDC/HMX with Turret Layout Setting button.

Tool Assignment                          Reposition Editing Confirm Mode

You can edit reposition manually. You can insert a track to one reposition freely. You can also divide specified trace into two different repositions.

Tool Assignment                       Template

In Edit of Template, improved interface provides you the easier way to edit the template. It is more conveniently to use the new operation flow to add and edit a template.

Tool Assignment                       Assign the Internal-tab Bend Line

You can decide whether to use the Internal-tab bend line for assignment or not.

Enhancement

System Setting               Tool Include

A new check box, Tool Include, is added into the Utilization Setting window of System Setting to consider tool when calculating the sheet utilization.

Parts Properties              De-Burring On/Off or Slot Auto On/Off

Select to enable the options of De-Burring On/Off or Slot Auto On/Off.

Peripherals                      Part Removal Sequence

In Peripheral Preference, the Take Out Sequence panel changes into the Part Removal Sequence panel. These options in the new screen allow you to change the speed of the axis movement in order to avoid destroying the last part.

Clearance                        Addition Parameter to Clearance

New parameters, Clearance Selection and Process Speed, are added into Clearance Preference in order to control clearance exchange order and process speed.

Manual Edit                     Cross Cursor Support

You can specify the coordinate by (Cross Cursor) in the manual edit mode.

Simulation                    Confirm the simulation view of the Nano Joint

Support to confirm the simulation view of the Nano Joint.

Tool Assignment                       Modify the View of Laser Tool Assign

Modify the View of Laser Tool Assign.

Tool Assignment                      Auto Calculate the Min or Max Value for Nibbling Pitch

Get a nibbling pitch range by calculating automatically based on your settings.

Tool Assignment                     Width of Micro Joints and Wire Joints for Special Tool

Specify the width of macro joints and wire joints for SP tools.

TK/IJP Edit                                  Display the list of the TK parts in the sheet

Select the object to edit.

Nesting                                         Take out the Reusable Sheet

Take out the reusable sheet after cutting the remnant.

Nesting                                           Don’t nest parts inside skeleton area

This function in Material Selection panel of Nesting Preference instructs you not to nest smaller parts in the skeleton area near where irregular part has been nested.

Manual Edit                                   Take out the Reusable Sheet

Take out the reusable sheet after cutting the remnant by automatically or manual edit.

Schedule                                         Schedule Assign

Assign the schedule of the corresponding material and thickness.

Schedule                                         Separate Schedule

Select to schedule by turret or material.

Sequence                                         Auto Cutout Avoidance

Define the cutout avoidance settings to instruct the laser head to avoid previously cut holes in the work sheet or part(s).

# Chapter 3: Getting Started

This chapter describes the system requirements, how to launch the system, the main window, the basic settings and the basic workflow.

| See: | System Requirements |
| --- | --- |
|  | Launch Dr.ABE |
|  | Quick Start Guide |

## 3.1 System Requirements

| Hardware | Description |
| --- | --- |
| CPU | Intel Pentium IV, AMD Athlon or higher CPU. |
| Memory | 512 MB RAM minimums, 1024 MB recommended. |
| Hard Disk | 1GB of free hard disk space minimum. |
| CD-ROM | A CD-ROM is required for local installation. |
| Graphic Card | A video card capable of supporting a minimum resolution of 1024 x 768. |
| Software | Description |
| Operating system | Windows 2000 or Windows XP. |
| Network | 1000/100/10Base |

| See: | Launch Dr.ABE |
| --- | --- |
|  | Quick Start Guide |

## 3.2 Launch Dr.ABE

To launch Dr. ABE, select Start to Programs to Amada to Dr. ABE.

| See: | System Requirement |
| --- | --- |
|  | Quick Start Guide |

## 3.3 Quick Start Guide

This section explains the procedure for loading parts, adjusting the nesting schedule, creating nesting layouts and generating NC code. You can review these outlines of the software features for training purposes.

| See: | Dr. ABE Main Window |
| --- | --- |
|  | Basic Dr. ABE Settings |
|  | Basic Operation |

| See: | System Requirements |
| --- | --- |
|  | Launch Dr. ABE |

### 3.3.1 Dr.ABE Main Window

The main window of Dr. ABE is comprised of the following:

| See: | Basic Dr. ABE Settings |
| --- | --- |
|  | Basic Operation |

### 3.3.2 Basic Dr.ABE Settings

When you first launch Dr. ABE, you should perform the following steps:

| 1. | Define the machine parameter. See: Machine Parameter |
| --- | --- |
| 2. | Define the material parameter. See: Material Parameter |
| 3. | Set the system setting. See: System Setting |

| See: | Dr. ABE Main Window |
| --- | --- |
|  | Basic Operation |

### 3.3.3 Basic Operation

| 1. | Once you have installed the program, you can navigate and select the command in the menu (Start to Programs to Amada to Dr. ABE), or double-click the Dr. ABE shortcut icon on the desktop to launch the program. |
| --- | --- |
| 2. | Click the Select Data button to display the Avon Data Selection Dialog window: |
| 3. | Select the part(s) and click Open. |
| 4. | Define the part quantity in the main window and put them into the Nesting Schedule. |
| 5. | Click the Nesting Schedule button to specify the part properties. |
| 6. | Click one Preference button in the main window to display the Preference window. Specify the nesting, tool and sequence conditions in the relevant windows. |
| 7. | In the Main window, click the Auto Execute button to perform the nesting process. |
| 8. | The nesting result, and the NC code, will be displayed in the result view. |
| 9. | Right click the No. cell to open the shortcut menu. Select Save NC Data or Save Schedule to save the data. |
| 10. | Click in the top right corner of the window to exit the program. |

| See: | Dr. ABE Main Window |
| --- | --- |
|  | Basic Dr. ABE Settings |

# Chapter 4: Machine Parameter

Click the Machine Setting button on the main Dr. ABE window to open Machine Set window. The options in this window allow you to specify the various machine parameters.

| See: | Machine Parameter Toolbar |
| --- | --- |
|  | Machine Parameter Tree View |
|  | Machine Information |
|  | Laser Information |
|  | Cutting Condition |
|  | NC Device Information |
|  | Peripherals |

## 4.1 Machine Parameter Toolbar

| Button | Description |
| --- | --- |
|  | Add a new machine. |
|  | Edit the settings in the current panel. |
|  | Delete the selected machine. |
|  | Download the machine parameters stored in the SDD or MiniSDD database. |
|  | Copy machine parameters from specified machine to a new machine. |
|  | Specify machine parameter server PC. |
|  | Backup or Restore the machine parameters. |

| See: | Machine Parameter Tree View |
| --- | --- |
|  | Machine Information |
|  | Laser Information |
|  | Cutting Condition |
|  | NC Device Information |
|  | Peripherals |

## 4.2 Machine Parameter Tree View

|  | The Tree View will present the available machines in a hierarchical, tree-like structure. Select the machine in the hierarchical pane on the left to view the detail information. The Tree View provides an expandable view of all the available resources. You can click the plus box before one item to expand the view and display the sub items. Click the minus box to collapse the view and to hide the sub items. |
| --- | --- |

| See: | Machine Parameter Toolbar |
| --- | --- |
|  | Machine Information |
|  | Laser Information |
|  | Cutting Condition |
|  | NC Device Information |
|  | Peripherals |

## 4.3 Machine Information

| 1. | Click the next to a machine name to expand the machine list. |
| --- | --- |
| 2. | Select Machine Information to display Machine Information panel. |
|  | The options in the Machine Information panel allow you to review and modify machine information. |

| See: | Machine Information Panel |
| --- | --- |
|  | Time Study |
| See: | Machine Parameter Toolbar |
|  | Machine Parameter Tree View |
|  | Laser Information |
|  | Cutting Condition |
|  | NC Device Information |
|  | Peripherals |

### 4.3.1 Machine Information Panel

| Option | Description |
| --- | --- |
| Machine Type | The type of machine that you have defined. The textbox on the right side displays the machine name. |
| Origin | You can input coordinate values in the X, Y, and Z: textboxes to specify the process origin point of the machine. (-9999.99 to 9999.99 mm) |
| Punching Process Range | Specify the punching process range in the X and Y-axis directions. (- 9999.99 to 9999.99 mm) |
| Min | The minimum X and Y limit values for the punching process |
| Max | The maximum X and Y limit values for the punching process |
| Available Pressure (KN) | Specify the maximum available punching pressure. |
| P/F Structure | This option indicates whether a P/F Structure exists. A check mark in the check box indicates the existence of a P/F Structure. |
| Max. Work Thickness | Specify the maximum thickness that can be processed (0.01 to 99.99 mm). |
| Hit Rate | Specify the hit rate of the machine (1 to 9999 HPM). |
| Stroke per Minute | Specify the number of strokes per minute (1 to 9999 SPM). |
| Max. Nibbling Pitch | Specify the maximum nibbling pitch (0.01 to 99.9 mm). |
| Max. Nibbling Angle | Specify the maximum nibbling pitch angle when nibbling an arc by using auto index (0.00 to 99.99 degree). |
| Turret Name | All the turrets associated with the machine are displayed in the drop-down list. |
| Storage Name | All the storages associated with the machine are displayed in the drop-down list. It is only available for the machine with PDC. |
| Multi-Tapping | This option indicates whether multi-tapping exists. If it is set to Yes, then you must specify the tapping information. |
| NC Driver File Path | This drop-down list displays the path and file name of the machine driver file. |
| Clamp |  |
| Max. Setting Position | Specify the maximum limit position when placing the clamps. (0.0 to 999.99 mm). |
| Positioner | Specify whether a repositioning clamp exists. |
| Min. Space | Specify the minimum space between two auto avoidance clamps. |
| Auto Avoidance Clamp | This option indicates whether auto avoidable clamps exist. Note: If you remove the check mark from the Yes/No: check box, the Min. Space option will be disabled as well. |
| Y-Direction Offset Amount | Define the offset amount in the Y-direction when using offset clamps. |
| Y- Direction Dead Zone | Define the dead zone range in Y-direction when MERK is used. |
| Repositioning | This option indicates whether the repositioning function is supported when MERK is used. |
| Air Blower | Specify whether the air-blow function is available. If the machine type is VIPROS, this option does not appear because it is set to On automatically for a VIPROS machine. |
| M Codes | If the Air Blower is enabled, you can specify the starting and ending M codes. |
| Energy Save | Specify whether to enable Energy Save mode. If the machine type is NCT, this option does not appear. |
| M Codes | If the Energy Save is enabled, you can specify the starting and ending M codes. |
| Time Study | Click the Time Study button to display the Process Time Addition Info window where you can specify the process time settings. See: Time Study |

| See: | Time Study |
| --- | --- |

### 4.3.2 Time Study

The Process Time Addition Info window will appear after you click the Time Study button in the Machine Information panel. The options in this window allow you to specify the process time settings. There are two panels: Punching and Laser.

| Common Option | Description |
| --- | --- |
| M-code | This option is used to specify non-standard M-code. |
| Time | This option is used to specify time for non-standard M-code. |
|  | Click this button to add a new line in table below. |
|  | Click this button to delete an existing line in table below. |
| Number | This option displays a sequential number for a M-code. |
| M-Code | This option displays a M-code. |
| Time | This option displays time for a M-code. |

Punching Panel

| Option | Description |
| --- | --- |
| Various Parameters (Actual#) |  |
| Multi Tapping | This option is not available for the moment. |
| Tap in Turret | This option is not available for the moment. |
| Burring | This option is not available for the moment. |
| Forming | This option is not available for the moment. |
| PDC/PDC2 Tool Change | The time to change the PDC/PDC2 tool |
| Others (0~4) | This option is not available for the moment. |
| Various Parameters (Integer) |  |
| Process Speed | Specify the turret running mode. (1 to 4) If you set the Process Speed to 1, the turret will run with the highest speed. |
| Others (0~4) | This option is not available for the moment. |

Laser Panel

| Option | Description |
| --- | --- |
| Various Parameters (Actual#) |  |
| Start Trace Height | The height of the laser head when the machine starts the cutting mode. |
| Return Trace Height (None) | The height that the laser head will be raised when the machine implements the M104 command to cancel the cutting mode |
| Return Trace Height (M00) | The height that the laser head will be raised when the machine implements the M104M00 command to cancel the cutting mode |
| Return Trace Height (M01) | The height that the laser head will be raised when the machine implements the M104M01 command to cancel the cutting mode |
| Return Trace Height (Chute) | This option is not available for the moment. |
| WorkChute ON/OFF Time | This option is not available for the moment. |
| OVS Gap Detect Time | This option is not available for the moment. |
| All –compensation factor | The factor is used to determine the actual process time, which is multiplied by the process time the system calculates. If the factor is 1.5, the process time the system calculates is 100 seconds, so the actual process time will be 150 seconds. |
| Other (0~4) | This option is not available for the moment. |
| Various Parameters (Integer) |  |
| Add Time before starting process | The time before the process starts. If the process time the system calculates is 100 seconds, and the Add Time before starting process is 5 seconds, the actually process time will be 105 seconds. |
| Time to change gas | Time used to change the gas |
| Other (0~4) | This option is not available for the moment. |

| See: | Machine Information Panel |
| --- | --- |

## 4.4 Laser Information

| 1. | Click the to expand the machine list. The Laser Information appears. |
| --- | --- |
| 2. | Select Laser Information to display its corresponding panel. |

| Option | Description |
| --- | --- |
| Laser Process Range | Specify the maximum and minimum (X, Y, Z) coordinates of the laser process limits (- 999.99 to 999.99). |
| Min. Correction Unit | Specify the minimum unit for the cutter compensation (0.0 to 9.999). |
| Laser Head Beam | Specify the diameter of the laser processing head (0.0 to 9999.999). |
| Max. Cutting Speed | Specify the maximum cutting speed (0.0 to 32767). |
| Work holder Fixed Y-Axis | Define the fixed position of the work holder in the Y-axis. |
| Water Nozzle | This option indicates whether the water nozzle exists. A check mark indicates that the machine is equipped with a water nozzle. |
| Clean Cut | This option indicates whether Clean Cut function is supported. A check mark indicates the machine supports this function. |
| Aluminum Cut | This option indicates whether the machine supports Aluminum Cut. A check mark indicates this function is supported. |
| NC Focus Control | This option indicates whether to perform NC focus control. |
| Near Z Axis | This option indicates whether a Z–axis sensor exists. A check mark indicates Z–axis sensor is supported. |
| Assist Gas NC Control | This option indicates whether to perform assist gas NC control. A check mark indicates Assist Gas NC Control will be performed. |
| Output Sub- Blower | Specify whether to output the NC code of assistant air blower device. |
| Skid Origin Position | Specify the X and Y coordinates of the skid origin point. |
| Pitch 1 and 2 | Specify the X and Y pitches of the pincushion where pins are arranged in grid form. Specify Pitch 2 if the pins are arranged in a zigzag form. |
| Reference Point | Input values in Z1, Z2, Z3 and Z4 to specify the reference point position in the Z-axis (0.0 to 9999.99). |
| Table Type | Select the table type from the drop-down list. |
| Z-Axis Type | Select the Z-axis type from the drop-down list. |
| None | Machine without the Z-axis. |
| Flat | 2.5D process machine with the Z-axis (other than the LC series). |
| Helical | 3D process machine. |

| See: | Machine Parameter Toolbar |
| --- | --- |
|  | Machine Parameter Tree View |
|  | Machine Information |
|  | Cutting Condition |
|  | NC Device Information |
|  | Peripherals |

## 4.5 Cutting Condition

| 1. | Click the to expand the machine list. |
| --- | --- |
| 2. | Select Cutting Condition and the Cutting Condition panel displays. |

| See: | Cutting Condition Panel |
| --- | --- |
|  | Cutting Condition Hidden Panel |

| See: | Machine Parameter Toolbar |
| --- | --- |
|  | Machine Parameter Tree View |
|  | Machine Information |
|  | Laser Information |
|  | NC Device Information |
|  | Peripherals |

### 4.5.1 Cutting Condition Panel

The Cutting Condition panel is divided into two panes. The Cutting Condition Set pane on the left will list all the materials with the cutting conditions defined, while the Cutting Condition Not Set pane on the right will list the materials without any cutting conditions defined.

| Column Title | Description |
| --- | --- |
| Laser Material Name | This column displays the material names. |
| Material Type | This column displays the material type. |
| Thickness | This column displays thickness of a material. |
| New | Click the New button to create a new laser material. |
| Delete | Select a material, and click the Delete button to remove it from the list. |
| Download | Click the Download icon to import the cutting condition from the database. |
| JKF | Click JKF button to download *. JKF cutting condition files. |
| JKA | Click JKA button to download *. JKA cutting condition files. |

| See: | How to Create a New Laser Material |
| --- | --- |
|  | How to Download Cutting Conditions from VPSS |
|  | How to Download JKF Files |
| See: | Cutting Condition Hidden Panel |

#### 4.5.1.1 How to Create a New Laser Material

| To create a new laser material: |
| --- |
| 1. | Click the button. |
| 2. | The New Laser Material window will appear. Select or define the Mat. Type, Thickness and Laser Mat. Name. |
| 3. | Click OK. The new material appears in the list. |

| See: | How to Download Cutting Condition from VPSS |
| --- | --- |
|  | How to Download JKF Files |

#### 4.5.1.2 How to Download Cutting Condition from VPSS

| 1. | In the Main Preference window, click the Access Information Manager button. |
| --- | --- |
| 2. | The Access Information Manager window will appear. |
| 3. | Right click the SDD option to open a shortcut menu. Select Add product…. |
| 4. | The Add New Product Dialog window will appear. Select <<New Computer>> from the Computer Name: drop-down list. |
| 5. | The Add New Computer Dialog appears. Type the information in the window. Click OK. |
| 6. | Click OK. A new PC is added to the SDD. |
| 7. | Add a new product to AMNC [COMPLEXER] using the same method. |
| 8. | After you accessed the VPSS, click the Download button in the Condition Setting window to display the following window. |
| 9. | If None is selected, download the cutting condition from AMNC directly. |
| 10. | If SDD or MiniSDD is selected, the cutting condition form AMNC can be downloaded to the SDD or MiniSDD by the VPSS component and then downloaded to Dr. ABE with SDD or MiniSDD cutting condition. |

| See: | How to Create a New Laser Material |
| --- | --- |
|  | How to Download JKF Files |

#### 4.5.1.3 How to Download JKF Files

| To download JKF files: |
| --- |
| 1. | Click the button. |
| 2. | The Open window appears. Select a JKF file. |
| 3. | Click Open. A message displays. When downloading JKF files into Dr. ABE, the original cutting condition will be overwritten. |
| 4. | Click Yes. The JKF file is downloaded into Dr. ABE. |

| See: | How to Create a New Laser Material |
| --- | --- |
|  | How to Download Cutting Condition From VPSS |

### 4.5.2 Cutting Condition Details

In the Cutting Condition Panel, select one laser material and double-click to open the Cutting Condition window. There are five panels: Cutting Process Information, Cutting Pierce Information, Cutting Edge Information, Nano Joint and Append. Click the desired tab to activate a particular panel. The Cutting Process Information panel is active by default.

| See: | Cutting Process Information |
| --- | --- |
|  | Cutting Pierce Information |
|  | Cutting Edge Information |
|  | Nano Joint |
|  | Append |
|  | Machine Parameter |
| See: | Cutting Condition Main Panel |

#### 4.5.2.1 Cutting Process Information

| Item | Description |
| --- | --- |
| Laser Material Name | The name of the material. |
| Mat. Type | The material type for the material. |
| Thickness | The material thickness. |
| Type | The cutting condition type. There are ten types: E001 to E010. |
| Speed | Specify the speed from zero to the maximum cutting speed (mm/second) according to the machine speed. |
| Output | Output an oscillator according to the oscillator specifications (Output the S code from the minimum to the maximum). |
| Frequency | The oscillator frequency based on the oscillator specifications (Output the frequency from the minimum to the maximum in Hz). |
| Duty | The duty according to the oscillator specifications (The duty cycle in % from the minimum to the maximum). |
| Assist Gas |  |
| Kind | The assist gas type (1 to 7 M code). This item depends on the machine specifications. |
| Pressure (Mpa) | The assist gas pressure (0.0 to 25.5 kgf/cm2). |
| Switch Time | The pulse switching time (0.0 to 9.9 seconds). |
| Origin Reposition | The reposition from the reference value (1.5 mm in most cases) on the Z-axis (- 9.9 to 9.9 mm). |
| Diameter | The laser cutter compensation amount (beam radius) (minimum corrective unit to 9.999 mm). This item depends on the machine specifications. |
| Approach Data | Number for approach process (0 or a value from 201 to 205). |
| Edge Data | Number for edge process (0 or a value from 201 to 205). |
| Focus | Focus position (relative to the reference value) (- 9.9 to 9.9). |
| Pulse Type | Pulse waveform. |

| See: | Cutting Pierce Information |
| --- | --- |
|  | Cutting Edge Information |
|  | Nano Joint |
|  | Append |
|  | Machine Parameter |

#### 4.5.2.2 Cutting Pierce Information

Click the Cutting Pierce Information tab to activate the Cutting Pierce Information panel.

| Column Title | Description |
| --- | --- |
| Pierce No. | The number of pierce type. |
| Initial Value |  |
| Output | Piercing output count. This item depends on the oscillator specifications (the minimum to maximum output S code). |
| Frequency | The frequency for piercing (the minimum to maximum frequency in Hz). This item depends on the oscillator specifications. |
| Duty | The duty cycle for piercing (the minimum to maximum duty cycle in %). This item depends on the oscillator specifications. |
| Increment |  |
| Frequency | The frequency for high-speed piercing for a thick sheet (the minimum to maximum frequency in Hz). This item is dependent on the oscillator specifications. |
| Duty | The duty cycle for high- speed piercing for a thick sheet (the minimum to maximum duty cycle in %). This item depends on the oscillator specifications. |
| Step |  |
| Time | Specify the step time for high- speed piercing for thick sheet (0.0 to 9.9). |
| Amount | Specify the number of steps for thick sheet high- speed piercing (0 to 99). |
| Pierce Time | (0.0 to 99.9 seconds) |
| Gas |  |
| Kind | Specify the assist gas type (1 to 7). This item depends on the machine specifications. |
| Pressure (Mpa) | Specify the assist gas pressure (0.0 to 25.5 kgf/cm2). |
| Switch Time | Specify the assist gas switching time (0.0 to 9.9 seconds). |
| Std Reposition | The reposition from the reference value (1.5 mm in general cases) on the Z-axis (- 9.9 to 9.9 mm). |
| Focus | Specify the focus position (relative to the reference position) (- 9.9 to 9.9). |
| Pulse Type | Pulse waveform. |

| See: | Cutting Process Information |
| --- | --- |
|  | Cutting Edge Information |
|  | Nano Joint |
|  | Append |
|  | Machine Parameter |

#### 4.5.2.3 Cutting Edge Information

Click the Cutting Edge Information tab to activate the Cutting Edge Information panel.

| Column Title | Description |
| --- | --- |
| Edge No. | The number of Edge type. |
| Action Angle | Specify the intersecting angle of an edge portion at which you switch to the edge conditions (0 to 180). |
| Pierce |  |
| Output | Output for edge piercing. This item depends on the oscillator specifications (Output S code from the minimum to the maximum). |
| Frequency | The frequency for edge piercing. This item depends on the oscillator specifications (the frequency in Hz from the minimum to the maximum). |
| Duty | The duty cycle for edge piercing. This item depends on the oscillator specifications (The duty cycle in % from the minimum to the maximum). |
| Time | Specify the edge piercing time (0.0 to 99.9 seconds). |
| Gas Pressure (Mpa) | Specify the assist gas pressure for edge piercing (0.0 to 25.59 kgf/cm2). |
| Gas Kind | Specify the assist gas type for edge piercing (1 to 7). This item depends on the machine specifications. |
| Recovery |  |
| Distance | Specify the distance by which recovery from the edge is made in the following conditions. |
| Speed | Specify the recovery speed (0 to 9999 mm/second). |
| Frequency | Recovery frequency. This item depends on the oscillator specifications. |
| Duty | Recovery duty cycle (the minimum to maximum duty cycle in %). This item depends on the oscillator specifications. |

| See: | Cutting Process Information |
| --- | --- |
|  | Cutting Pierce Information |
|  | Nano Joint |
|  | Append |
|  | Machine Parameter |

#### 4.5.2.4 Nano Joint

Click the Nano Joint tab to activate the Nano Joint panel. Type 1 and Type 2 are the Nano Joint processing methods. Please refer to the Nano Joint for details. 801-810 matches the parameters in the Append panel.

| See: | Cutting Process Information |
| --- | --- |
|  | Cutting Pierce Information |
|  | Cutting Edge Information |
|  | Append |
|  | Machine Parameter |

#### 4.5.2.5 Append

Click the Append tab to activate the Append panel. This panel will list the detail parameters from 801-810.

| See: | Cutting Process Information |
| --- | --- |
|  | Cutting Pierce Information |
|  | Cutting Edge Information |
|  | Nano Joint |
|  | Machine Parameter |

#### 4.5.2.6 Machine Parameter

Click the Machine Parameter tab to activate the Machine Parameter panel. These options allow you to specify cutting conditions for individual patterns. You can specify the conditions for the lines/arcs and the macro shapes.

Note:

You can select Machine Parameter under Reference of Cutting Condition (Size/Shape) and select Size/Shape from the Cutting: drop-down list in the Cut Condition table to apply the settings.

| See: | Line/Arc |
| --- | --- |
|  | Macro Shape |
|  | Exception to Averaging |
| See: | Cutting Process Information |
|  | Cutting Pierce Information |
|  | Cutting Edge Information |
|  | Nano Joint |
|  | Append |

##### 4.5.2.6.1 Line/Arc

|  | The Size/Shape (Line/Arc) section allows you to specify the process methods for the lines and arcs. In the ARC table, you can select whether to use arc length or arc radius to define the conditions. |
| --- | --- |

| Column | Description |
| --- | --- |
| EQ. | Specify the relationship between the Line/Arc and Value. There are five options: <= (less than or equal to), >= (greater than or equal to), = (equal to), < (less than) and > (greater than). |
| Value | Specify the reference dimension value. |
| Cutting | Assign the cutting condition (E001—E010) to the elements that match the conditions. |

Example

| 1. | This part has the following dimensions. |
| --- | --- |
| 2. | Select Size/Shape from the Cutting: drop-down list. Select Machine Parameter under Reference of Cutting Condition (Size/Shape) and then specify the settings as follows. |
| 3. | The lines match the condition set in the Line table. E003 is used to process them. The round hole matches the condition set in the ARC table. E004 is used to process it. |

| See: | Macro Shape |
| --- | --- |
|  | Exception to Averaging |

##### 4.5.2.6.2 Macro Shape

The Size/Shape (Macro Shape) section allows you to specify the process methods for the macro patterns. The system supports the following macro shapes: RO (Round), OB (Obround), SQ-REC (Square-Rectangle), SD/DD (Single D/Double D), ARC Slot and Polygon. For each macro shape, you can click the button above the table to select dimension type to specify the cutting conditions.

| Column | Description |
| --- | --- |
| EQ. | Specify the relationship between the pattern dimension and Value. There are five options: <= (less than or equal to), >= (greater than or equal to), = (equal to), < (less than) and > (greater than). |
| Value | Specify the reference dimension value. |
| Cutting | Assign the cutting condition to the patterns that match the condition. The options available are from E001 to E010. |

| Button | Description |
| --- | --- |
| RO | Round |
|  | Click to use the diameter to specify the cutting condition for the round patterns. |
|  | Click to use the radius to specify the cutting condition for the round patterns. |
| OB | Obround |
|  | Click to use the length to specify the cutting condition for the obround patterns. |
|  | Click to use the width to specify the cutting condition for the obround patterns. |
| Polygon | Regular polygon |
|  | Click this button to use the radius of circumference of the polygon to specify the cutting condition for polygons. |
|  | Click this button to use the radius of inscribed circle of the polygon to specify the cutting condition for polygons. |
| SQ-REC | Square-Rectangle |
|  | Click to select the length to specify the cutting condition for the Square-Rectangle patterns. |
|  | Click to use the width to specify the cutting condition for the Square-Rectangle patterns. |
| SD/DD | Single D and Double D |
|  | Click this button to use X direction length of the SD/DD to specify the cutting condition for it. |
|  | Click this button to use Y direction length of the SD/DD to specify the cutting condition for it. |
| ARC Slot | Radius Slot |
|  | Click this button to use the arc length to specify the cutting condition for the arc slot. |
|  | Click this button to use the width to specify the cutting condition for slot. |

Example

| 1. | The following part is used as an example. |
| --- | --- |
| 2. | In the Path Assignment Method panel, place a check mark in the Use Machine Macro Shape check box. The system will process the holes as macros. If you remove the check mark from the check box, the holes will be divided into lines and arcs. |
| 3. | Select Machine Parameter under Reference of Cutting Condition (Size/Shape) and select Size/Shape from the Cutting: drop-down list in the Cutting Condition table |
| 4. | In the Machine Parameter panel, specify the conditions as follows. |
| 5. | The round Hole matches the condition in the RO table. And the system will process it using E003. The obround hole matches condition in the OB table. The system will process it using E004. |

| See: | Line/Arc |
| --- | --- |
|  | Exception to Averaging |

##### 4.5.2.6.3 Exception to Averaging

|  | If you select Avg. in the Cut Condition Table, you can define whether the length of a line is used to calculate the average by typing value in the following text boxes. |
| --- | --- |

| Option | Description |
| --- | --- |
| IA1: Cutting > | Type a value in the IA1: Cutting >: text box to define the minimum value used to calculate the average. |
| IA2: Cutting < | Type a value in the IA2: Cutting <: text box to define the maximum value used to calculate the average. |

Example

| 1. | The part has the following dimensions: |
| --- | --- |
| 2. | In the Cut Condition Table, specify the conditions as follows. |
|  | And specify the Exception to Average settings as follows. |
| 3. | Since no values were specified for IA1, the Avg. value is calculated as follows: (100 + 100 + 100 + 35 + 35 + 30 + 5 +5)/8 = 51.25 The outer loop matches Condition 1, the system will process the outer loop by using E002. |
| 4. | If we change the settings in the Cut Condition table as follows |
|  | And type 6 in the IA1: Cutting >: text box. |
| 5. | The length of two line segments is 5, less than the value in the IA: Cutting >: text box. So the segments won’t be considered in the average calculation, and Avg. value will be calculated as follows: (100 + 100 + 100 + 35 + 35 + 30)/6 ≈ 66.67. E003 is used to process lines that have a length of 5. E002 is used to process the remaining lines. |

| See: | Line/Arc |
| --- | --- |
|  | Macro Shape |

## 4.6 NC Device Information

| 1. | Click the to expend the machine list. The NC Device Information displays. |
| --- | --- |
| 2. | Select the NC Device Information option and the NC Device Information panel displays. |

| Option | Description |
| --- | --- |
| NC Device Name | This text box will display the NC device name and specify when a machine is registered. |
| NC Data Unit | You can define the NC program data unit by selecting the Metric or Inch option button. |
| Point | This option allows you to decide whether the NC program uses the decimal point. (If the decimal point does not exist, 100 will be regarded as 1.00). |
| Digit within Point | You can specify the digit within point by selecting the items in the list box. |
| Input Integer | This item indicates whether integer is input. If you select Yes, the integer data input with aliases is converted to standard data. If the process machine is a laser machine, ignore this item. |
| Max. Macro Memory Amount | Specify the maximum number of macro characters that can be stored in the U-V macro (0 to 32000). If the NC device is the FS- 16, this item is disabled. |
| Pattern Memory | You can specify the number of patterns that can be stored (0 to 99). |
| Address Memory | You can specify the number of addresses that can be stored. This item can be defined only when using the F3000C or other NC devices that can store a limited number of addresses. If the NC device cannot store any addresses, set this item to 0. |
| Memory Space | Define the memory space of the NC device. |
| G25 Power | This option allows you to specify the output of G25. This option decides which G code, G25 or G27, will be output for the first reposition during NC data generation. If Yes is selected, G25 is output for the first reposition during NC program generation and G27 will be used for the second time. If No is selected, G27 will be output for all the repositioning. |
| CPU Type | The type of CPU the machine uses. |
| Max. Punch | Specify the number of trial punches. For the first step machine, 5000 is defined; for the second step machine, 10000 is defined. |
| User Memory | Specify the memory space of the NC device with the tape length (0 to 9999). |
| Max. File Register Amount | Specify the maximum number of files that can be registered in the NC device (0 to 32767). |
| Output Arc | Specify the output type of arc for laser machine. |
| R | Output the arc with R, and if the arc angle is greater than 180 degrees, output it with I and J. |
| I J | Output the arc using I, J (I is the X-axis dimension from the start point of the arc to the end point; J is the Y-axis dimension from the start point of the arc to the end point). |
| User Macro Version | Define the version of the user macro (3.0 to 5.0). If the NC device is the FS-16, ignore this item. |
| 3.0 | Machine without the Z-axis |
| 4.0 | Machine with the Z-axis |
| 5.0 | High-speed format。 |
| Axis Move Mode | This option allows you to determine the method for moving the laser head axis. |
| Fixed | Move with fixed angle. |
| Direct | Direct move. |

| See: | Machine Parameter Toolbar |
| --- | --- |
|  | Machine Parameter Tree View |
|  | Machine Information |
|  | Laser Information |
|  | Cutting Condition |
|  | Peripherals |

## 4.7 Peripherals

| 1. | Click the to expand the machine list. |
| --- | --- |
| 2. | Select Peripherals to expand the list. |

| See: | Oscillator | IJP |
| --- | --- | --- |
|  | Take Out Information | Loading/Unloading Device |
|  | Clamp Information | Work Cute Information |
|  | Holder Information | Tapping Information |
|  | MJC |  |

| See: | Machine Parameter Toolbar |
| --- | --- |
|  | Machine Parameter Tree View |
|  | Machine Information |
|  | Laser Information |
|  | Cutting Condition |
|  | NC Device Information |
|  | Peripherals |

### 4.7.1 Oscillator

| 1. | Click the to expand the machine list. |
| --- | --- |
| 2. | Select the Oscillator option and the Oscillator panel appears. |

| Option | Description |
| --- | --- |
| Oscillator Name | Specify the name of the oscillator. |
| Output (Min) (Max) | Specify the maximum and minimum output values of the oscillator (0 to 9999 W). |
| Pulse | Specify the pulse type. |
| Frequency (Min)(Max) | Specify the maximum and minimum frequencies of the oscillator (0 to 9999 Hz). |
| Duty (Min)(Max) | Specify the maximum and minimum duty cycles of the oscillator (0 to 100%). |

| See: | Take Out Information |
| --- | --- |
|  | Clamp Information |
|  | Holder Information |
|  | MJC |
|  | IJP |
|  | Loading/Unloading Device |
|  | Work Cute Information |
|  | Tapping Information |

### 4.7.2 Take Out Information

Click the Take-out Information option to activate the Take-out Information panel. The options in this panel allow you to define the take-out type, the unloading code, the stacking table information, the arm information, M code of Taking out, and PR/TK parameter.

| Option | Description |
| --- | --- |
| Taking Out | Specify whether the machine is equipped with an unloading device. A check mark in the Yes/No check box indicates that the machine is equipped with an unloader. Remove the check mark if your machine is not equipped with an unloader/stacking device. |
| Type of Taking Out |  |
| Type of Taking Out | Select a TK type from the drop-down list. The are two types of TK devices, PartRemoverII and Hyper TK. |
| Taking Out Direction | Specify the direction in which TK device carries out parts. |
| Unloading M Code |  |
| Unloading Skeleton Sheet M Code | Specify the M code for unloading the skeleton sheet. For example, 58. |
| Unloading Micro Joint Sheet M Code | Specify the M code for unloading the micro joint sheet. For example, 59. |
| Skeleton to Scrap Shear M Code | Specify the M code for skeleton to scrap shear. For example, 57. |
| Stacking Scheme |  |
| Maximum Height | Specify the maximum height for stacking parts in the table. |
| Table Size X and Y | Specify the X and Y dimensions of the table. |
| Maximum Weight | Specify the maximum weight for stacking parts on the table. |
| Arm information |  |
| Minimum Arm Opening | Specify the minimum space between the TK arms. |
| Maximum Arm Opening | Specify the maximum space between the TK arms. |
| Arm X and Y Size | Specify the X, Y arm size. |
| M Code of Taking Out | Specify the Pickup M code. The options in this section are only available for hyper TK device. |
| Vacuum > Cut > Pickup | The M code that instructs the machine to vacuum the part and then perform the last cutting process only in the Y-axis. |
| Cut > Vacuum > Pickup | The M code that instructs the machine to perform the last cutting process in both X and Y-axis and then vacuum the part. |
| Pickup M Code | The M code that instructs the machine to pick up the part. |
| M Code For Moving Waiting Position | The M code that instructs the machine to move the arm to the waiting position, and it can shorten the time to move the arms. |
| PR/TK Parameter | Specify the PR/TK parameter. The options in this section will update when Type of Taking Out: dro- down list in Type of Taking Out section has changed. |
| XHome | The distance in X-direction from the punch center to home position of the X-asix (mm). |
| X Wait | The distance in X-direction between center tool and the arm. |
| X Stack:0 | The distance in X-direction from the punch center to where the stacking area begins (mm). |
| XPickMin | The minimum distance in X-directionfrom the punch centerthat PR can pick-up (mm). |
| YAHome | The distance in Y-direction from the tool center line to suction cup arm A home position (mm). |
| YBHome | The distance in Y-direction from the tool center line to suction cup arm B home position (mm). |
| YPickMax | The maximum distance in Y-direction from the tool center line to suction cup arm B that PR can pick-up (mm). |
| Information of Station | Specify the information of places to stack the parts. The options in this table are only available for the Hyper TK device. |
| Name | Specify the name of the place to stack the parts. |
| Station Type | Specify how to take out the parts. There are three options, Work Chute, Pallet and Conveyor. |
| M Code | Define the M code (0~9999) to take out the parts. |
| Min X | The minimum X dimension of the parts that can be taken out |
| Max X | The maximum X dimension of the parts that can be taken out |
| Min Y | The minimum Y dimension of the parts that can be taken out |
| Max Y | The maximum X dimension of the parts that can be taken out |

| See: | Oscillator |
| --- | --- |
|  | Clamp Information |
|  | Holder Information |
|  | MJC |
|  | IJP |
|  | Loading/Unloading Device |
|  | Work Cute Information |
|  | Tapping Information |

### 4.7.3 Clamp Information

The Clamp Information option is in the Peripherals folder. Select Clamp Information to display the Clamp Information window.

| Option | Description |
| --- | --- |
| Number | The number of clamps. There is specific set of parameter for each clamp, including Type, Clamp Axis, Clamping Width and Length, Placement Position X and Y, Placement Position Limit X and Y, Senor Placement Position, Senor Size X and Y, Dead Zone X and Y. |
| ON/OFF | You can select which set of parameters the system will use by placing a check mark in the ON/OFF box. You can add additional clamps using the Add Clamp button and specifying the parameters. You can remove parameters using the Delete Clamp button. |
| Type | You can click the down arrow to open the drop-down list and select clamp type: Thin Sheet, Thick Sheet, Offset or Small. |
| Clamp Axis | The direction of clamp placement: X or Y. |
| Clamping Width and Length | You can define the width and length of the clamp. |
| Placement Position X and Y | You can define the X and Y position where the clamp is placed. |
| Placement Position Limit X and Y | You can define X and Y position to define the placement of clamp. |
| Sensor Placement Position | You can change the sensor position by selecting the options in the list box. There are four options: None, Left, Right and Bi-directional. |
| Sensor Size X and Y | You can define X and Y size of the sensor. |
| Dead Zone X and Y | You can specify the Dead Zone by typing X and Y coordinates. |
| Button | Description |
| Add Clamp | Click this button to add a new clamp parameter. |
| Delete Clamp | Select a set of parameters that you want to delete and then click the Delete Clamp button. The system will prompt you to confirm. Click Yes to confirm and to delete the parameters. |
| Refresh | Click the Refresh button after modifying the parameter to apply the new setting. |

| See: | Oscillator |
| --- | --- |
|  | Take Out Information |
|  | Holder Information |
|  | MJC |
|  | IJP |
|  | Loading/Unloading Device |
|  | Work Cute Information |
|  | Tapping Information |

### 4.7.4 Holder Information

The Holder Information option is in the Peripheral folder. Click the Holder Information option to display the Holder Information window:

| Option | Description |
| --- | --- |
| 1st, 2nd and 3rd | Place a check mark in the corresponding check box to make modifications to the holders. |
| Type | Select the type of the holder by choosing the option from the drop-down list. |
| Size | Specify X and Y size of the work holder (0.00 to 99.99). |
| Position | Specify X and Y position of the work holder (- 999.99 to 999.99). |

| See: | Oscillator |
| --- | --- |
|  | Take Out Information |
|  | Clamp Information |
|  | MJC |
|  | IJP |
|  | Loading/Unloading Device |
|  | Work Cute Information |
|  | Tapping Information |

### 4.7.5 MJC

MJC is an acronym for Micro Joint Cutter. Microjoints are tabs that you can place on the part corners or along the part perimeters. These uncut sections prevent the parts from falling out of the sheet. The MJC device is used to remove the microjoints after the punching process is complete.

| Option | Description |
| --- | --- |
| MJC | If a MJC device is provided, place a check mark in the Yes/No check box. Remove the check mark if there is no MJC device. |
| Work and Part | This section allows you to specify the properties of the sheets and parts. |
| Work Thickness | Specify the minimum and maximum thickness of the sheet for processing. |
| Work Size X/Y | Specify the minimum and maximum dimension of the sheet in X/Y direction. |
| Min. Part Size | Specify the minimum dimension of the part in X/Y direction. The part size is specified by rectangular size of the part shape. |
| Cutter | This section allows you to specify the offset of the cutter in X and Y directions. A cutter is used to pick up the parts with joints. |
| Micro Joint | Joints on corner. |
| Wire Joint | Joints on line. |
| Special Tool | Joints processed by specific tools. |
| Driver Type | Select one driver type from the drop-down list. |
| Cutter Size X/Y | Input value to specify the dimension of cutter in X and Y direction. |
| Upper Cutter Size X/Y | Input value to specify the dimension of upper cutter in X and Y direction. |

| See: | Oscillator |
| --- | --- |
|  | Take Out Information |
|  | Clamp Information |
|  | Holder Information |
|  | IJP |
|  | Loading/Unloading Device |
|  | Work Cute Information |
|  | Tapping Information |

### 4.7.6 IJP

IJP is an acronym for Ink Jet Printer. The IJP is used to print information on the parts.

| Option | Description |
| --- | --- |
| NO | There are three sets of parameters available. You can set the parameters in IJP panel of Peripheral section. |
| IJP | If an IJP is provided, place a check mark in the Yes/No check box. |
| Maker | The manufacturer code for the IJP device. |
| Max String Size X/Y | These fields are used to specify the maximum string size in X/Y direction. The following figure indicates the string size in X/Y direction: |
| Max String Number | This field is used to specify the maximum string number in a line. |
| Line Feed Character | This field is used to specify the character used for line feeds. Then the character is the code for the beginning of a new line. For example, if you specify “//” as the line feed character, and then input “123//4567//890” for the ink-jet marking string, the IJP will print: |
| Max Number of Lines | This field is used to specify the maximum number of lines that can be printed at one time. |
| String Pitch X, Y | These fields are used to specify the pitch between strings in the X/Y direction. The following figure indicates the string pitch in the X/Y direction. |
| Raster Size ID | Specify the character size that will be sent to the Ink-Jet Printer. The Ink Jet Printer determines the character size and pitch for printing according to the raster size information and string size information. (This is used when hole interference is checked in Simulation. The actual character size is determined by this information.) |
| String Size ID | Character size information that is sent to Ink-Jet Printer. |

| See: | Oscillator |
| --- | --- |
|  | Take Out Information |
|  | Clamp Information |
|  | Holder Information |
|  | MJC |
|  | Loading/Unloading Device |
|  | Work Cute Information |
|  | Tapping Information |

### 4.7.7 Loading/Unloading Device

You can click the Loading/Unloading Device option to display the Loading/Unloading Device panel.

| Option | Description |
| --- | --- |
| Tandem Device Type | You can select the tandem device type provided in the list box and the presence/absence of the automatic material carry-out function. |
| Thickness Command M-Code | You can define the M code and its corresponding range of material thicknesses. When the machine is required to output the M-Code for the thickness, the corresponding pre-defined M-Code is used for target material according to the range of material thickness. For example, if the material thickness is 0.50, then the code will be 22. |
| End Position M-Code | You can define the M code and its corresponding range of material X size. When the machine is required to output the end position M-Code, the pre-defined M-Code will be used for target material according to the range of material X size. For example, if the material X size is 1000.00 the end position M code will be 55. |
| Pad Group Definition M-Code | You can define the M code and its corresponding range of material X, Y size. When the machine is required to output M-Code for the pad group, the pre-defined M-Code will be used for the target material according to the range of material X, Y sizes. For example, if the material size X is1900 and material size Y is 1000, the M code will be 322. (If dimension is the same as the input value, it is defined as "within".) |

| See: | Oscillator |
| --- | --- |
|  | Take Out Information |
|  | Clamp Information |
|  | Holder Information |
|  | MJC |
|  | IJP |
|  | Work Cute Information |
|  | Tapping Information |

### 4.7.8 Work Chute Information

You can select the Work Chute Information option to display the Work Chute Information panel.

| Option | Description |
| --- | --- |
| 1st and 2nd | If there is only one work chute, place a check mark in the 1st check box. If there are two work chutes, place check marks in both the 1st and 2nd check boxes. Check the option to enable the corresponding work chute information. |
| Size X and Y | Specify the work chute X and Y size (0.00 to 9999.99). |
| Replacement Position X and Y | Specify the work chute X and Y position. This option indicates the displacement from the punch center to the upper right point of the work chute. (- 999.99 to 9999.99). |
| Dwell Time | Specify the dwell time. This is the time when the work chute opens to the time when it closes (0.00 to 9999.99). |
| Start M Code | Specify the M code for opening the work chute (0 to 999). |
| End M Code | Specify the M code for closing the work chute (0 to 999). |
| Dead Zone Position X and Y | Specify X and Y of the work chute dead zone position. |
| Dead Zone Area X and Y | Specify X and Y of the dead zone area. |

| See: | Oscillator |
| --- | --- |
|  | Take Out Information |
|  | Clamp Information |
|  | Holder Information |
|  | MJC |
|  | IJP |
|  | Loading/Unloading Device |
|  | Tapping Information |

### 4.7.9 Tapping Information

Select Tapping Information to display the Tapping Information panel.

| Option | Description |
| --- | --- |
| Check Boxes 1 through 8 | Place a check mark in the check box to activate the corresponding tapping options. |
| Placement Position |  |
| Size | The tapping M diameter. |
| X | The X position of the tapping placement position. The X value is measured from the punch center. |
| Y | The Y position of the tapping placement position. The Y value is measured from the punch center. |
| Dead Zone |  |
| X | The length of the dead zone in the X direction. The center is measured from the center of the clamp. |
| Y | The height of the dead zone in the Y direction. The Y direction is measured from the material end point. |
| M Code |  |
| Start | The starting M code for the tapping process. |
| End | The ending M code for the tapping process. |

| See: | Oscillator |
| --- | --- |
|  | Take Out Information |
|  | Clamp Information |
|  | Holder Information |
|  | MJC |
|  | IJP |
|  | Loading/Unloading Device |
|  | Work Chute Information |

# Chapter 5: Material Parameter

Click the Material Management button in the main window to open the Dr.ABE Material Management window. There are three panels: Material Type Information, Sheet Information and Tube Material Information.

| See: | Material Manager Toolbar |
| --- | --- |
|  | Material Type Information |
|  | Sheet Information |
|  | Tube Material Information |

## 5.1 Material Manager Toolbar

| Button | Description |
| --- | --- |
|  | Click New button to create new Material Type, Sheet Information or Tube Material Information parameters. |
|  | Click Edit button to modify the selected Material or Sheet information parameters. |
|  | Click Delete button to remove the selected Material or Sheet information from the list. |
|  | Click Get Data from SDD or MiniSDD button to download sheet information from SDD or MiniSDD. |
|  | Click Options button specify the Material Parameter Server PC. |
|  | Click Backup/Restore button to backup or restore Material type information, sheet information and tube material information. |

| See: | Create a Material Type |
| --- | --- |
|  | Edit a Material Type |
|  | Delete a Sheet Information |
|  | Download Material Type From AP100 |
|  | Option |
|  | Backup and Restore Material |

| See: | Material Type Information |
| --- | --- |
|  | Sheet Information |
|  | Tube Material Information |

### 5.1.1 Create a Material Type

| To create a material type, |
| --- |
| 1. | Click Mat. Type Information tab first and then click New button on the toolbar to enable the textboxes on the right side of the window. |
| 2. | Specify name and values accordingly in the Material Type, Specific Gravity and Tensile Strength: textboxes for the new material. |
| 3. | Click Add button to add the new material information into the Mat. Type Information list. |
| 4. | Now the new material is available in the Material Type: drop-down list when you edit in the Sheet Information tab or Tube Material Information tab. |

| See: | Edit a Material Type |
| --- | --- |
|  | Delete a Sheet Information |
|  | Download Material Type From AP100 |
|  | Option |
|  | Backup and Restore Material |

### 5.1.2 Edit a Material Type

| To edit a material type, |
| --- |
| 1. | Select the material type that you want to modify in the Mat. Type Information list. |
| 2. | Click Edit button on the toolbar to enable the textboxes on the right side of the window. |
| 3. | Modify the name or values in the Material Type, Specific Gravity and Tensile Strength: textboxes. |
| 4. | Click Modify button to save your changes and continue to edit the next material type. |
| 5. | Click Done to finish. |

| See: | Create a Material Type |
| --- | --- |
|  | Delete a Sheet Information |
|  | Download Material Type From AP100 |
|  | Option |
|  | Backup and Restore Material |

### 5.1.3 Delete a Sheet Information

| To delete a sheet information, |
| --- |
| 1. | Click the Sheet Information tab and select the sheet information that you want to delete from the list. |
| 2. | Click Delete button on the toolbar. The Dr. ABE Material Management dialog will appear and prompt you to confirm. Click OK to remove the sheet from the list or click Cancel to cancel. |

| See: | Create a Material Type |
| --- | --- |
|  | Edit a Material Type |
|  | Download Material Type From AP100 |
|  | Option |
|  | Backup and Restore Material |

### 5.1.4 Download Material Type from AP100

| To download material types from AP100, |
| --- |
| 1. | Click Get Data from SDD or MiniSDD button. The Material Parameter Download window will appear: |
| 2. | Select Only download material code (Sheet Code) of AP100. The material code of AP100 will be downloaded into the Dr. ABE Material Manager. |
| 3. | Select Download AP100 material type, then register the material code of each type in Standard Sheet Registration window to download all the AP100 material types. The Standard Sheet Register window will appear. |
| 4. | Click OK to download the material types with check mark(s) into the Dr. ABE Material Manager. |
| 5. | Click Sheet Size Definition button to display the Sheet Size Define window. You can define different sheet sizes, codes and quantities for the same material type in the window. |
| 6. | Click OK. The third one has been registered to this material type. |

| See: | Create a Material Type |
| --- | --- |
|  | Edit a Material Type |
|  | Delete a Sheet Information |
|  | Option |
|  | Backup and Restore Material |

### 5.1.5 Option

| 1. | Click Options button on the toolbar to display the Options window. |
| --- | --- |
| 2. | Specify the new server name in the Material Parameter Serve PC: textbox. Click OK to confirm, or click Cancel to cancel. |

| See: | Create a Material Type |
| --- | --- |
|  | Edit a Material Type |
|  | Delete a Sheet Information |
|  | Download Material Type From AP100 |
|  | Backup and Restore Material |

### 5.1.6 Backup and Restore Material

This option allows you to easily backup and restore the material information.

Click the Backup Restore  button on the toolbar to display the Dr. ABE System Backup&Restore Material window.

| See: | How to Backup Material |
| --- | --- |
|  | How to Restore Material |

| See: | Create a Material Type |
| --- | --- |
|  | Edit a Material Type |
|  | Delete a Sheet Information |
|  | Download Material Type From AP100 |
|  | Option |

#### 5.1.6.1 How to Backup Material

| 1. | In the Dr. ABE Backup&Restore Material window, click the item(s) that you want to backup in the Items to Backup section. |
| --- | --- |
| 2. | Click the Browse button next to the File Name: text box to display the Choose a backup file window. To overwrite an existing backup zip file, navigate to the destination folder and select it. To create a new backup zip file, navigate to the destination folder and specify a name in the File name: textbox. Then, click Open to close the window. |
| 3. | The specified name will appear in the File Name: textbox. Click the Backup button to perform the backup process and make the backup zip file to the destination folder. |

| See: | How to Restore Material |
| --- | --- |

#### 5.1.6.2 How to Restore Material

| 1. | In the Dr. ABE Backup&Restore Material window, click the item(s) that you want to restore in the Items to Restore section. |
| --- | --- |
| 2. | Click the Browse button next to the File Name: text box to display the Choose a backup file window. Navigate to the destination folder and choose the backup zip file that you want to restore. Then, click Open to close the window. |
| 3. | The specified name will appear in the File Name: textbox. Click the Restore button to perform the restore process. The material information will be restored to the program. |

| See: | How to Backup Material |
| --- | --- |

## 5.2 Material Type Information

The Material Type Information panel will list all the available material types.

You can create, edit, delete and download the material types.

| Column Title | Description |
| --- | --- |
| Material Type | The name of the material type. |
| Specific Gravity | The specific gravity of a material. The specific gravity is the ratio of the density of a substance to the density of another substance (such as pure water) taken as a standard when both densities are obtained by weighing in air. |
| Tensile Strength | The tensile strength of the material. Tensile strength is the greatest longitudinal stress that a substance can bear before failure. |

| See: | Material Manager Toolbar |
| --- | --- |
|  | Sheet Information |
|  | Tube Material Information |

## 5.3 Sheet Information

The Sheet Information panel allows you to view all of the information associated with a sheet. You can also create, edit, delete and download sheet information.

| Column Title | Description |
| --- | --- |
| Sheet Code | The Sheet Code: textbox displays the sheet code. |
| Material Type | The Material Type: textbox displays the material type that was specified in the Material Type Information panel. |
| Thickness | The Thickness: textbox displays the material thickness specified upon the material registration. You can use the up and down arrow to edit the value or type a value in the textbox. |
| Material Name | Type the material name in this textbox. |
| Sheet Size X/Y | The horizontal and vertical dimension of the sheet specified upon the material registration. |
| Qty. | This textbox displays the quantity of the sheets specified upon the registration. |
| Price | The unit price of the sheet. You can type a new price in the textbox. |
| Grain Direction | The direction of the sheet texture: Vertical, Horizontal. |
| Comment | Type the comments for the material in this textbox. |
| Special Information | This section allows you to specify special information for the material. There are three options you can select from the drop-down list. None, Coated and Colored Steel. |
| Sheet Type | This option allows you to specify the different sheet types. Click the arrow button and select the type from the drop-down list: Standard, Remnant, Skeleton or Sketch. |
| Priority | Define the priority for the material. |
| Sheet Profile | This section is used to preview the profile of the sheet that can be used. The white area represents the sheet. |

| See: | Standard, Remnant, Skeleton and Sketch Materials |
| --- | --- |
|  | How to Create a Remnant Sheet |
|  | How to Create a Skeleton Sheet |

| See: | Material Manager Toolbar |
| --- | --- |
|  | Material Type Information |
|  | Tube Material Information |

### 5.3.1 Standard, Remnant, Skeleton and Sketch Materials

There are four types of material: Standard, Remnant, Skeleton and Sketch.

Each sheet type is with a different color in the material table.

A remnant is an unused rectangular area of a sheet due to the results of the nesting process. The remnant will be registered in material management after saving the NC data.

A skeleton is the remaining material after the part(s) on the sheet is/are removed. The remainder of the sheet can be reused to increase sheet utilization.

Sketch material is a sheet that has the same X/Y size as that of the part, i.e., there can only be one part per sheet. The method used to process only the notches and holes is known as the sketch process, and the material used at that time is called the sketch material.

| See: | How to Create a Remnant Sheet |
| --- | --- |
|  | How to Create a Skeleton Sheet |

### 5.3.2 How to Create a Remnant Sheet

| 1. | Click the Nesting button to display the Nesting window, and then click the Material Selection tab to display the Material Selection panel. |
| --- | --- |
| 2. | Select Create Remnant in the Reusable Sheet section, and then define the Pitch, Min X Size and Min Y Size values. |
| 3. | The remnant will be created if the remainder of the sheet matches the specified conditions after processing. |
| 4. | The created Remnant sheet will be listed in the Material Management window after you save the NC data. |

| See: | Standard, Remnant, Skeleton and Sketch Materials |
| --- | --- |
|  | How to Create a Skeleton Sheet |

### 5.3.3 How to Create a Skeleton Sheet

| 1. | Click the Nesting button to display the Nesting window, and then click the Material Selection tab to display the Material Selection panel. |
| --- | --- |
| 2. | Select Create Skeleton Sheet in Reusable Sheet section, and then specify the Max Utilization value. |
| 3. | The skeleton sheet will be created if the remainder of the sheet matches the specified condition after processing. The Skeleton sheet will be listed in the Material Management window after you save the NC data. |

| See: | Standard, Remnant, Skeleton and Sketch Materials |
| --- | --- |
|  | How to Create a Remnant Sheet |

## 5.4 Tube Material Information

The Tube Material Information panel allows you to view all the material information for tube processing.

You can also create, edit and delete the tube material information.

| Column Title | Description |
| --- | --- |
| Pipe Name | The name of the pipe material. |
| Material Type | The Material Type: textbox displays the material type that was specified in the Material Type Information panel. |
| Thickness | The Thickness: textbox displays the material thickness specified upon the material registration. You can type a value in the textbox to define the thickness of material. |
| Pipe Type | Two pipe types can be selected: Round or Square. |
| Length | The Pipe Length text box is used to specify the length of the pipe. |
| Diameter | The Diameter: textbox is used to specify the diameter of the pipe. |
| Height | The Height: textbox is used to specify the height of the pipe. |
| Corner Radius | The Corner Radius: textbox is used to specify the corner radius of the pipe. |
| Seam Position | Select the position of the pipe seam. |
| Comment | Type comments for the pipe material in this textbox. |
| Profile | This section is used to preview the profile of the pipe material. |

| See: | Material Manager Toolbar |
| --- | --- |
|  | Material Type Information |
|  | Sheet Information |

# Chapter 6: System Setting

Click the System Setting  button in the Dr. ABE main window to display the System Setting window.

The options in this window allow you to set all your preferences for Dr. ABE.

Click OK to accept the changes and close the window.

Click Cancel to close the window without saving any changes.

| See: | View |
| --- | --- |
|  | System |
|  | Option |

## 6.1 View

Click the View tab in the System Setting window to display the View panel.

This panel allows you to configure the overall views for CAD Data Drawing, Main Window and Result View.

| See: | Main Window |
| --- | --- |
|  | CAD Data Drawing |
|  | Drawing |
|  | Information Area |
|  | Zoom |
|  | Utilization Setting |

| See: | System |
| --- | --- |
|  | Option |

### 6.1.1 Main Window

The options in this section allow you to define the system settings, such as the machine and material parameters and message display.

Machine Manager Setting

Dr. ABE is compatible with AP100. If MiniSDD or SDD is installed on your PC, two machine parameter databases are available: Dr. ABE and AP100.

If Dr. ABE Machine Manager is selected from the drop-down list, the Dr. ABE machine manager will display in the Machine Set window.

If SDD Machine Manager is selected, the AP100 machine manager will display in the Machine Manager window. The machine parameter in AP100 will be downloaded to the Dr. ABE machine parameter after you close the window.

Note: Select whether to download machine parameter from SDD or MiniSDD.

Material Manager

Dr. ABE is compatible with AP100. If MiniSDD or SDD is installed on your PC, two material parameter databases are available: Dr. ABE and AP100.

If Dr. ABE Material Manager is selected, the Dr. ABE Material Management window will display.

If SDD Material Manager is selected, the AP100 material manager will display in the Material Manager window. After you close the window, the material parameter in the AP100 will be downloaded to the Dr. ABE material manager.

Note: Select whether to download material parameter from SDD or MiniSDD.

Message at the Completion of Automatic Processing

The default message is “Complete!!” You can type other message in the textbox.

| See: | CAD Data Drawing |
| --- | --- |
|  | Drawing |
|  | Information Area |
|  | Zoom |
|  | Utilization Setting |

### 6.1.2 CAD Data Drawing

|  | This section is used to define the display format of CAD data drawing. The available formats are unfolded drawing and 3D drawing. |
| --- | --- |

The difference between 3D and Unfolded

| 1. | In the main window: |
| --- | --- |
|  | 3D |  |
|  | Unfolded |  |
| 2. | In the Nesting Schedule: |
|  | 3D |  |
|  | Unfolded |  |

| See: | Main Window |
| --- | --- |
|  | Drawing |
|  | Information Area |
|  | Zoom |
|  | Utilization Setting |

### 6.1.3 Drawing

The options in this section control the display view of the nesting result.

| Option | Description |
| --- | --- |
| Quality | The system will display a result drawing of high quality, but this will increase the running time. |
| Speed | The system will display a simple result drawing that will reduce the running time. This option is selected by default. |
| View Y Size | Define the default width of Result View area after auto execution. |
| Display Setting | Click this button to display the Display Setting window. You can select different colors to display the elements in the result drawing. |
| Expand All is done after Automatic | This option is used to control whether you can open and close all generated sheet layouts at one time. |
| Max Number of Open Sheets | Define the maximum number of generated sheets layouts that you can open at one time. |
| Zoom in The Part Edit Display to | Type value in the nearby box to define the magnifying dimension for window in which you can edit part. |

| See: | View Y Size |
| --- | --- |
|  | Difference between Quality and Speed |
|  | Display Different Colour for Elements on the Part |
|  | Expand all is down after automatic |

| See: | Main Window |
| --- | --- |
|  | CAD Data Drawing |
|  | Information Area |
|  | Zoom |
|  | Utilization Setting |

#### 6.1.3.1 View Y Size

| Define the default width of Result View area after auto execution. |
| --- |
| 1. | Set the View Y Size to 300. |
| 2. | Click Auto Execution button to display Result View. |

| See: | Difference between Quality and Speed |
| --- | --- |
|  | Display Different Colour for Elements on the Part |
|  | Expand all is done after automatic |

#### 6.1.3.2 Difference between Quality and Speed

The following pictures indicate the difference between Quality and Speed.

The result view in Quality mode is as below.

The result view in Speed mode is as below.

| See: | View Y Size |
| --- | --- |
|  | Display Different Colour for Elements on the Part |
|  | Expand all is done after automatic |

#### 6.1.3.3 Display Different Colors for the Elements on the Part

Click the Display Setting button, the Display Setting window displays.

In this window, you can specify different colors for the items in the table.

You can select the item by placing the check mark in the check box, and click the color cell to display the palette to change the color.

| Quality Mode | Speed Mode |
| --- | --- |

| Items | Description |
| --- | --- |
| Items | The name of the item that you can specify the color. |
| Color | The color that is used to display the item in the result view. |
| Special Options |  |
| Punch Tool is Transparent | Select this option and punch tools will be displayed in construction line in the result view. This option is only available for punch machines. |
| By Process After | Select this option to enable the Process After color settings. |
| Setting | Click this button to display the Display Setting of Process After window. In this window, you can click the square box to display the color palette and change the color for the corresponding Process After method. The system will use the specified color to display the objects that will be processed by the corresponding process after method. |
| Background Color | Specify the background color in the result view. |

Example

| 1. | In the Quality Mode, the default color of Lead In is green. In the result view, the Lead In is displayed in green. |
| --- | --- |
| 2. | Change the Lead In color to blue. |
| 3. | Now the lead in is displayed in blue in the Result View. |
| 4. | In the Process After Cutting window, select Machine Stop from the process: drop-down list as the end value of the inner loop process: |
| 5. | In the Display Setting window, select By Process After and then click Setting button to open the Display Setting of Process After window. In this window, you can set red for the Machine Stop. |
| 6. | You can see the result is as follow. The inner loop appears in red. |

| See: | View Y Size |
| --- | --- |
|  | Difference between Quality and Speed |
|  | Expand all is done after automatic |

#### 6.1.3.4 Expand All is Done after Automatic

| This option is used to control whether you can open and close all generated sheet layouts at one time. |
| --- |
| 1. | When the Expand All is Down after Automatic: check box remains empty, |
| 2. | The sheet layouts would not display after auto-execution. |
| 3. | When you place a check mark in the Expand All is Down after Automatic: check box, |
| 4. | The sheet layouts will display after auto-execution. |

| See: | View Y Size |
| --- | --- |
|  | Difference between Quality and Speed |
|  | Display Different Colour for Elements on the Part |

### 6.1.4 Information Area

The options in the Information Area allow you to define which information panels will display in the Result View, and the X size of the information area.

The available information panels include: Parts Info, Error List and NC Data.

The selected information will display in the Result View.

| See: | Main Window |
| --- | --- |
|  | CAD Data Drawing |
|  | Drawing |
|  | Zoom |
|  | Utilization Setting |

### 6.1.5 Zoom

You can define the magnification proportion of Zoom operation in the Result View.

| Option | Description |
| --- | --- |
| Zoom In Ratio | Each magnifying operation will enlarge graphic by the percentage specified here. |
| Zoom Out Ratio | Each reducing operation will reduce graphic by the percentage specified here. |
| Auto Scale Clearance Value | This option allows you to define the display margin in Auto Scale operation. For example, if you set 10% as the Auto Scale Clearance Value, the distance from parts with bounding box to the four boundaries of result display area will be not less than 10% when you use Auto Scale. |
| Auto Scale Clearance Value of Error | This option allows you to define the clearance value of the errors that display in the Result View. For example, you set 10% as the clearance of displayed error. Click Error Information from the Error List to find the corresponding error in the part. The error will be displayed as follow. The distance from the error section with a bounding box to the one of four boundaries that is the most close to the error section is 10%. |
| When you set Auto Scale Clearance Value to 10%, the system will display the parts as follows. |
| When you set Auto Scale Clearance Value of Error to 10%, the system will display the parts as follow. |

| See: | Main Window |
| --- | --- |
|  | CAD Data Drawing |
|  | Drawing |
|  | Information Area |
|  | Utilization Setting |

### 6.1.6 Utilization Setting

|  | Click this button to open the Utilization Setting window. You can specify whether to consider holes when calculating the sheet utilization. |
| --- | --- |

Example

| 1. | We will process the following part with an inner loop. |
| --- | --- |
| 2. | If we place a check mark in the Holes Include: check box. (Tool Include: check box remains empty) After auto execution, it shows the utilization is 10.498%, and the inner loop area is included and tool area is excluded when calculating the sheet utilization. |
| 3. | If we remove the check marks from both the Holes Include: check box and the Tool Include: check box, after auto execution, it shows the utilization is 5.863%. Both the inner loop area and the tool area are excluded when calculating the sheet utilization. |
| 4. | If we place check marks in both the Tool Include: check box and Holes Include: check box, after auto execution, it shows the utilization is 11.406%, and both the inner loop area and tool area are included when calculating the sheet utilization. |
| 3. | If we remove the check mark from the Holes Include: check box and place a check mark in the Tool Include: check box, after auto execution, it shows the utilization is 6.771%, and the inner loop area is excluded and the tool area is included when calculating the sheet utilization. |

| See: | Main Window |
| --- | --- |
|  | CAD Data Drawing |
|  | Drawing |
|  | Information Area |
|  | Zoom |

## 6.2 System

Click the System tab to display the System panel.

This panel consists of six sections: System Setting, System Information, License Registration, System Backup and Restore, Parameter Processing and Preference Frame Current Folder.

| See: | System Setting |
| --- | --- |
|  | System Information |
|  | License Registration |
|  | System Backup & Restore |
|  | Preference Frame Current Folder |
|  | Parameter Processing |
|  | Access Information Manager |

| See: | View |
| --- | --- |
|  | Option |

### 6.2.1 System Setting

The options in this section allow you to specify the basic settings for the system, such as the Import Unit, Display Unit, Language, Database and Simulation.

| Option | Description |
| --- | --- |
| Import Unit | This option is used to specify the import unit. The available units are Metric and Inch. |
| Display Unit | This option is used to specify the display unit. The available units are Metric and Inch. |
| Language | This option is used to set the system language. The available languages are Japanese, English, Simplified Chinese, Korean, German, Spanish, French and Italian. |
| Database | Select the database to load parts from: MiniSDD, SDD or File. |
| Simulation | This option allows you to determine which program will be used for simulation: AP100Global, AP100, LINEA5 or Dr. ABE Blank. |
| Version | This option is used to display the version. |
| CAD Editor | This option is used to specify the CAD Editor. The available CAD Editor is AP100 and FabriCAD. |
| Initial Part Number | You can specify an initial value. The value will be the default quantity of the parts. See: Initial Part Number. |
| Sheet Select By | Two options are used to define whether the system will determine the sheet by the material name. See: System Determines Sheet by Material Name. |
| Use Wizard for Sheet Size/Name | If this option is selected, the Sheet Name Set window will display in auto execution that allows you to choose a sheet used for processing. See: Use Wizard for Sheet Size/Name. |

| See: | Initial Part Number |
| --- | --- |
|  | System Determining Sheet by Material Name |
|  | Use Wizard for Sheet Size/Name |

| See: | System Information |
| --- | --- |
|  | License Registration |
|  | System Backup & Restore |
|  | Preference Frame Current Folder |
|  | Parameter Processing |
|  | Access Information Manager |

#### 6.2.1.1 Initial Part Number

| 1. | This value is the default quantity of the parts. For example, if you type 6 in the Initial Part Number: textbox |
| --- | --- |
| 2. | Click OK to apply the setting. The value you specified will display as the default Part Quantity in the main window. The initial quantity of the parts loaded from the database will be six (6). The part quantity can be modified in the Part Quantity column of the Nesting Schedule window. |

| See: | System Determining Sheet by Material Name |
| --- | --- |
|  | Use Wizard for Sheet Size/Name |

#### 6.2.1.2 System Determining Sheet by Material Name

| The options here allow you to determine the way to select the sheet, by Material Name or by Material/Thickness. |
| --- |
| 1. | When the Material Name option is selected, you can select the material by the material name registered in the Material Manager. |
| 2. | When the Material/Thickness option is selected, you can select the material by the material type and thickness. |

| See: | Initial Part Number |
| --- | --- |
|  | Use Wizard for Sheet Size/Name |

#### 6.2.1.3 Use Wizard for Sheet Size/Name

| If this option is selected, the Sheet Name Set window will appear during auto execution, prompting you to select which sheet should be used for processing. |
| --- |
| 1. | Place a check mark in the Use Wizard for Sheet Size/Name check box. |
| 2. | The Sheet Name Set window will appear after you click the Auto Execute button. |
| 3. | All the material types (Standard, Remnant, Skeleton) with the material type and thickness you set at Nesting Plan are listed in the table. Select one material to use for processing. If all of the materials are checked, the system will select a material according to Material Selection Priority. You can also add new materials or copy a specific material by using Add New Sheet and Copy button. |
| 4. | Select a material, and click OK to continue the auto execution. |
| 5. | The system uses a remnant to process according to the settings. |

| See: | Initial Part Number |
| --- | --- |
|  | System Determining Sheet by Material Name |

### 6.2.2 System Information

This section lists the version and server of the Dr. ABE components that have been installed.

| See: | System Setting |
| --- | --- |
|  | License Registration |
|  | System Backup & Restore |
|  | Preference Frame Current Folder |
|  | Parameter Processing |
|  | Access Information Manager |

### 6.2.3 License Registration

You can register the license in two ways.

You can click the Registration button or the Enter Locking Code button to register the licenses before running the program.

Click the Registration button to open the Locate "Amada Key" window.

Browse to the folder containing the license file and select it.

Click Open to register the license.

Click the Enter Locking Code button to open the Nesting License Information window.

Click   and navigate to the folder containing the license code.

Select the file and click Open to register the license.

Note:

If you do not register the license, the following message will appear when you are running the program.

Please click Registration(R) or Enter Locking Code (E) to register the license first.

| See: | System Setting |
| --- | --- |
|  | System Information |
|  | System Backup & Restore |
|  | Preference Frame Current Folder |
|  | Parameter Processing |
|  | Access Information Manager |

### 6.2.4 System Backup and Restore

It is very important to backup parameters on a regular basis.

The System Backup/Restore section allows you to easily backup and restore the parameters.

Click the Backup & Restore button to display the Dr. ABE System Backup/Restore window.

| See: | How to Backup the Parameters |
| --- | --- |
|  | How to Restore the Parameters |

| See: | System Setting |
| --- | --- |
|  | System Information |
|  | License Registration |
|  | Preference Frame Current Folder |
|  | Parameter Processing |
|  | Access Information Manager |

#### 6.2.4.1 How to Backup the Parameters

| 1. | Click the item(s) in the Items to backup section that you want to backup. You can also click Select All under the list to select all the items. |
| --- | --- |
| 2. | Click the Browse button next to the File: textbox to navigate to the backup destination folder. The system will assign the default name of "back". You can also specify an alternate backup file name in the Choose a backup file window. |
| 3. | Click the Backup button to backup the files. The system will perform the backup process. |

| See: | How to Restore the Parameters |
| --- | --- |

#### 6.2.4.2 How to Restore the Parameters

| 1. | Click the Browse button to open the Choose a backup file window. |
| --- | --- |
| 2. | Navigate to the destination folder and locate the backup file. |
| 3. | Click Open to select the backup file. |
| 4. | In the Items to restore section, uncheck the items that you do not want to restore or just use the default settings. The system will select all the items to restore by default. |
| 5. | Click the Restore button to restore the files. |

| See: | How to Backup the Parameters |
| --- | --- |

### 6.2.5 Preference Frame Current Folder

Specify the path of the folder where the preference files are saved. You can click  button to select another folder to save the preference files.

| See: | System Setting |
| --- | --- |
|  | System Information |
|  | License Registration |
|  | System Backup & Restore |
|  | Parameter Processing |
|  | Access Information Manager |

### 6.2.6 Parameter Processing

The options in the Parameter Processing section allow you to specify when and where to download the machine and material parameters.

You can also control whether to decrease the sheet quantity when saving the NC program and the Skeleton/Remnant material.

| Option | Description |
| --- | --- |
| Machine Parameter Server PC | Specify the PC address to download the machine parameters |
| Material Parameter Server PC | Specify the PC address to download the material parameters See: Download Material Type from AP100 |
| SDD Parameter Automatic Download | Select this option to automatically download parameter from SDD. You can select the version of SDD from the drop-down list behind. |
| MiniSDD Parameter Automatic Download | Select this option to automatically download parameter from MiniSDD. |
| At the time of | Select the preferred download time of the parameters. |
| Starting of Dr. ABE | If you select this option, the system will automatically download the machine and material parameter from the database when Dr. ABE is launched. |
| Execution of Automatic Processing | If you select this option, the system will automatically download the machine or material parameter from the database when automatic processing is executed. |
| Server Location | This section is used to display the server name or path. |
| Decrease Sheet Quantity when Save NC | If you select this option, when automatically executing the process and saving the NC data, system will decrease the sheet quantity in the Material Manager window automatically. |
|  | See: Decrease Sheet Quantity when Save NC |
| Select Skeleton/Remnant to Save when Save NC | If you select this option, when automatically executing the process and saving the NC data, system will add the created skeleton/remnant information to the Material Manager window. |
|  | See: Select Skeleton/Remnant to Save when Save NC |

| See: | Decrease Sheet Quantity When Save NC |
| --- | --- |
|  | Select Skeleton/Remnant to save when saving NC |

| See: | System Setting |
| --- | --- |
|  | System Information |
|  | License Registration |
|  | System Backup & Restore |
|  | Preference Frame Current Folder |
|  | Access Information Manager |

#### 6.2.6.1 Decrease Sheet Quantity When Save NC

| To decrease the sheet quantity when saving an NC program: |
| --- |
| 1. | For example, in the Material Manager window, the quantity of the sheet A1050 is 100. |
| 2. | Select the Decrease Sheet Quantity When Save NC option. |
| 3. | One sheet is used in the processing. |
| 4. | Save NC. |
| 5. | The quantity of A1050 is decreased to 99. |
| 6. | If you do not select Decrease Sheet Quantity When Save NC, sheet quantity will remain the same after one piece of sheet is used. |

| See: | Select Skeleton/Remnant to save when saving NC |
| --- | --- |

#### 6.2.6.2 Select Skeleton/Remnant to Save when Saving NC

| 1. | Load several parts from the database. |
| --- | --- |
| 2. | In the Material Selection panel of the Nesting window, select Create Skeleton Sheet under Reusable Sheet, and define the preferred Max Utilization. |
| 3. | Select the Select Skeleton/Remnant to Save when Save NC option in the System panel. |
| 4. | Save the NC data after auto-execution. |
| 5. | The Save Confirmation dialog box appears, prompting you to check the skeleton/remnant that needs to be saved. Click the Save button. |
| 6. | Open the Material Manager window. Notice that the new skeleton was created. |

| See: | Decrease Sheet Quantity When Save NC |
| --- | --- |

### 6.2.7 Access Information Manager

|  | Click the Access Information Manager button to open the Access Information Manager window. VPSS Access Information Manager is an application for managing Connection Information for the VPSS Solution. |
| --- | --- |

| See: | System Setting |
| --- | --- |
|  | System Information |
|  | License Registration |
|  | System Backup & Restore |
|  | Preference Frame Current Folder |
|  | Parameter Processing |

## 6.3 Option

The options in this panel allow you to use the third-party’s application to load and export the plan files of other formats.

This panel consists of four sections: Start Module before Conversion, Start Module after Conversion, Open SDD Part Conversion and Interface File Setting.

| Option | Description |
| --- | --- |
| Start Module before Conversion | This option allows you to specify an application to convert the plan files and load into Dr ABE. See: Example 1 |
| Start Module after Conversion | This option allows you to specify an application to convert the plan files of Dr ABE into the plan files supported by the programs of other company. See: Example 2 |
| Open SDD Part Conversion | This option allows you to specify an application to open when you are to open part from SDD. See: Example 3 |
| Interface File Setting | In this section, you can specify the CSV format to output the nesting plan and nesting result. In production process, you can load the nesting result file as a CSV format to control part schedule. |
| Plan File Setting | This option allows you to define plan file format. There are two options below: Amada CSV Format and Custom. |
|  | Amada CSV Format | When AMADA CSV Format is selected, the CSV format used in the WinNEST for AMADA will be applied. |
|  | Custom | Select a form from Custom: drop-down list. You may also click the Detail button to open the Option window. See: Option window |
| Output Plan File | This option allows you to define output format for the plan file. There are two options below: Amada CSV Format and Custom. |
|  | Amada CSV Format | When AMADA CSV Format is selected, the CSV format used in the WinNEST for AMADA will be applied. |
|  | Custom | Select a form from Custom: drop-down list. You may also click the Detail button to open the Setting of Outputting Result File window. See: Setting of Outputting Result File window. |

Example 1

| 1. | Place a check mark in the check box to enable the conversion function. |
| --- | --- |
| 2. | Click Browse button to open the Select Convert Module dialog box. |
| 3. | Select an execution file for conversion. |
| 4. | When you are to open a schedule in the Nesting Schedule window, the specified application will be started. |

Example 2

| 1. | Place a check mark in the check box to enable the conversion function. |
| --- | --- |
| 2. | Click Browse button to open the Select Convert Module dialog box. |
| 3. | Select an execution file for conversion. |
| 4. | Right-click in the part result view screen to open the shortcut menu and select Save Schedule/Output Report or Save NC Data |
| 5. | Select either of the above two options, the specified application will be started. |

Example 3

| 1. | Place a check mark in the check box to enable the conversion function. |
| --- | --- |
| 2. | Click Browse button to open the Select Convert Module dialog box. |
| 3. | Select an execution file for conversion. |
| 4. | Then when you open part from SDD, the specified application will be started. |

Note:

You can open part from SDD in the following three ways.

| Method 1 | In the Avon Data Selection Dialog window, select a part and click Open button. |
| --- | --- |
| Method 2 | In Dr.ABE main window, click the Nesting Schedule button to open the Nesting Schedule window. In this window, click Part button. The Avon Data Selection Dialog window appears. |
| Method 3 | In the Manual Edit toolbar, click Add Part button to open Add Part screen. Select SDD and the Avon Data Selection Dialog window will appear. |

| See: | Option Window |
| --- | --- |
|  | Setting of Outputting Result File Window |

| See: | View |
| --- | --- |
|  | System |

### 6.3.1 Option window

In System Setting window, select Custom option in Interface File Setting section and then click Detail button to open Option window.

Option window

| Option | Description |
| --- | --- |
| Custom | You can make the setting to define the CSV file format. There are five types. |
| Starting Reading Line | Sometimes some data in the CSV file does not need to be read. In this case, you can define from which line to begin to read the data. |
| Text Qualifier | Define text qualifier used to identifying each item in the CSV. There are three options: Double Quotation Mark, Single Quotation Mark and None. |
| Delimiters | Define in the CSV file which kind of mark will be used as delimiters: Tab, Semicolon, Comma, Space, Other (type other marks needed in the textbox directly). |
| Part Path | Select the part path here. Note: Your computer should be shared for remote loading. |
| Save Part Name | This option allows you to load parts by part name |
| Save Part File Path | This option allows you to load parts by part file path. |
| Treat Consecutive Delimiters as One | If this option is checked, several consecutive delimiters will be regarded as one. |
| Plan Items | Define contents in the CSV file. Select items from Plan items list and then click the Add button to output it into the CSV file. Select items from Item and sequence of one record list and then click the Delete button to remove it. Click the priority button to change the order of the selected items. |
| Number | Select this, CSV document is recognized as numbers when nesting parts. |
| Character | Select this, CSV document is recognized as characters when nesting parts. Note: The CSV document output by BendCAM is a character string that consists of numbers and letters. When you select Character in CSV setting, the system can automatically change characters into numbers when nesting parts. |

| See: | Setting of Outputting Result File Window |
| --- | --- |

### 6.3.2 Setting of Outputting Result File window

Place a check mark in the Output Plan File check box, and then select Custom option and then click Detail button to open Setting of Outputting Result File window.

| Option | Description |
| --- | --- |
| Setting of Outputting | Click arrow button to select a form you want to customize. |
| Text Qualifier | Define text qualifier used to identifying each item in the CSV. There are three options: Double Quotation Mark, Single Quotation Mark and None. |
| Delimiters | Define in the CSV file which kind of mark will be used as delimiters: Tab, Semicolon, Comma, Space, Other (type other marks needed in the Other: text box directly). |
| Output Setting |  |
| Output Part and Sheet | Select this option to output part and sheet information. |
| Output Sheet Only | Select this option to output sheet information. |
| Sheet Record | You can define display format for sheet record. Define contents in the CSV file. Select items from Plan items list and then click the Add button to output it into the CSV file. Select items from Item and sequence of one record list and then click the Delete button to remove it. Click the priority button to change the order of the selected items. |
|  | Note: Sheet name cannot be deleted. |
| Record Type | Type the record type in this text box as a sheet mark in the CSV file. |
| Part Record | You can define display format for part record. Define contents in the CSV file. Select items from Plan items list and then click the Add button to output it into the CSV file. Select items from Item and sequence of one record list and then click the Delete button to remove it. Click the priority button to change the order of the selected items. |
|  | Note: Part name cannot be deleted. |
| Record Type | Type the record type in this text box as a part mark in the CSV file. |

Example:

| 1. | Place a check mark in Output Plan File: check box and select Amada CSV format. |
| --- | --- |
| 2. | Right-click in the nesting result view to open the shortcut menu. Select Save NC Data. |
| 3. | It outputs as follow, |
| 4. | Select Custom in the Output Plan File and set as follows. |
| 5. | The output is as follow: |

| See: | Option Window |
| --- | --- |

# Chapter 7: CAD Data Load

This chapter introduces the way to load CAD data into nesting and how to specify the part quantities.

If necessary, you can establish a connection with the server and load CAD data from the database.

Note:

Dr. ABE supports the databases such as SDD and MiniSDD. You can also import the CAD files stored on your local hard drive.

See: Database

| See: | How to Load CAD Data |
| --- | --- |
|  | Methods for Specifying the Part Quantity |
|  | How to Establish a Connection with a Server |

## 7.1 How to Load CAD Data

Method 1: Drag-and-drop the CAD data to the CAD DATA Load button.

| 1. | Locate the parts using Windows Explorer or use some alternative methods to list files. |
| --- | --- |
| 2. | Select the file. Press and hold the left mouse button. |
| 3. | Move the mouse pointer over the CAD Data Load button and then release it. The selected parts will appear in the Main window. |
| 4. | Type the part quantity in the Part Quantity: text box and then click the button to push it into the nesting schedule. |

Method 2: Drag-and-drop Data to the Nesting Schedule button.

| 1. | Locate the parts using the Windows Explorer or use some alternative methods to list files. |
| --- | --- |
| 2. | Select the file. Press and hold the left mouse button. |
| 3. | Move the pointer over the Nesting Schedule button and then release the left mouse button. The part file is loaded into the Nesting Schedule. |
|  | Note: Any quantity information that is included in the part is transferred to the Nesting Schedule. If there is no quantity information associated with the part file, the quantity of the parts will be the default quantity. |

Method 3: Using the CAD Data Load Button

| 1. | Click the CAD Data Load button to open the Avon Data Selection Dialog window. |
| --- | --- |
| 2. | Select one or more parts and then click Open to close the window and return to the main window. |

| See: | Methods for Specifying the Part Quantity |
| --- | --- |
|  | How to Establish a Connection with a Server |

## 7.2 Methods for Specifying the Part Quantity

Method 1: Type the quantity in the Part Quantity: text box after loading the part from CAD Data.

Method 2: Change the number in the Nesting Schedule window. Type the quantity in the Part Quantity cell.

| See: | How to Load CAD Data |
| --- | --- |
|  | How to Establish a Connection with a Server |

## 7.3 How to Establish a Connection with a Server

| 2. | Click the Add Server button. The Add/Remove Server window appears. |
| --- | --- |
| 3. | Input the server name or address in the Server Name or IP Address: text box and then click the Add button. The server is added to the list. |
| 4. | Select a server name and click Remove button to remove the server name from the list. . |
|  | Click OK to save the changes. Click Cancel to exit without saving to the Avon Data Selection Dialog window. |

| See: | How to Load CAD Data |
| --- | --- |
|  | Methods for Specifying the Part Quantity |

# Chapter 8: Nesting Plan

Click the Nesting Plan button in the main window after the parts are loaded from the database to open the Nesting Schedule window. The nesting plan allows you to define the part properties for each part, including the quantity, priority, material type, material selection, etc.

| See: | Parts Properties Summary |
| --- | --- |
|  | Menus |
|  | Toolbars |
|  | My Nesting Plan |
|  | Parts List |
|  | Parts Properties |
|  | Parts Properties Advanced |

## 8.1 Parts Properties Summary

| 1. | Load parts into the Nesting Plan, and then click Nesting Plan button to display the corresponding window. |
| --- | --- |
| 2. | Select a part and double-click it to display the Parts Properties window. You can also right- click the part and select Edit Part Properties from the shortcut menu to display the Parts Properties window. |
|  | Double-click |
|  | Right-click |
| 3. | Define the part properties in the Parts Properties window. |
| 4. | Click OK to confirm the settings and to return to the Nesting Schedule window. |
|  | Click Cancel button to exit the window without saving. |
|  | Click Apply to apply the settings you have specified for the part. |
|  | Click Apply to save the setting after you have made the settings for the selected part. And then click the Previous (P) or Next (N) buttons to edit the previous or next part in the Nesting Plan. |
|  | Click the Advanced button to open the Parts Properties Advanced window. |

| See: | Menus |
| --- | --- |
|  | Toolbars |
|  | My Nesting Plan |
|  | Parts List |
|  | Parts Properties |
|  | Parts Properties Advanced |

## 8.2 Menus

|  | The menu bar consists of six options: File, Edit, View, Insert, Tool and Help. These options allow you to edit the nesting plan. |
| --- | --- |

| See: | File |
| --- | --- |
|  | Edit |
|  | View |
|  | Insert |
|  | Tool |
|  | Help |

| See: | Parts Properties Summary |
| --- | --- |
|  | Toolbars |
|  | My Nesting Plan |
|  | Parts List |
|  | Parts Properties |
|  | Parts Properties Advanced |

### 8.2.1 File Menu

The options on the File menu allow you to create, open, add, save and print a plan.

|  | Option Description New Erase all the existing data in the nesting schedule and create a new plan. Open Open a nesting schedule that was previously saved. Save Save the current nesting schedule. Save As… Save the current nesting schedule with a new name. Add Plan Add a plan. Print Print the nesting schedule. Material Manager Open the Material Manager window, and you can add, delete, or modify the material. See Material Manager Exit Close the Nesting Schedule window and return to main window. |
| --- | --- |

| See: | Edit |
| --- | --- |
|  | View |
|  | Insert |
|  | Tool |
|  | Help |

### 8.2.2 Edit Menu

The options on the Edit menu allow you to edit the assemblies and parts in the plan.

|  | Option | Description |
| --- | --- | --- |
|  | Undo | Reverse the previous operation. |
|  | Redo | Repeat the previously un-done action. |
|  | Cut | Cut the selected assembly or part to the clipboard. |
|  | Copy | Copy the selected assembly or part to the clipboard. |
|  | Paste | Paste the assembly or part that you previously cut or copied to the clipboard to the selected assembly. |
|  | Delete | Delete the selected part. |
|  | Select All | Select all the parts in your selected assembly. |
|  | Merge of the Same Part | Merge the same parts in the same assembly. |
|  | Parts Properties | Open Parts Properties window. Please refer to Parts Properties. |
|  | Sort By Input Order | Sort the inputted parts according to their input order. |

| See: | File |
| --- | --- |
|  | View |
|  | Insert |
|  | Tool |
|  | Help |

### 8.2.3 View Menu

The options on the View menu allow you to choose the display mode of the parts.

|  | Option Description Details Displays detailed information of the selected parts. Details + Graphics Displays detailed information and graphics of the selected parts. Thumbnail Displays thumbnails of the selected parts. |
| --- | --- |

Examples:

If you select the Details option, the parts are displayed as follows:

If you select the Details + Graphics option, the parts will be displayed as follows:

If you select the Thumbnail option, the parts are displayed as follows:

| See: | File |
| --- | --- |
|  | Edit |
|  | Insert |
|  | Tool |
|  | Help |

### 8.2.4 Insert Menu

The options of the Insert menu allow you to insert a plan, assembly or a part into the current plan.

|  | Option Description Assembly This option will insert a previously saved assembly to your selected assembly. Part This option will insert a part from the CAD database to the plan. File This option will insert a CAD file to your selected assembly, such as *.dwg, *.dxf, and *.iga. |
| --- | --- |

| See: | File |
| --- | --- |
|  | Edit |
|  | View |
|  | Tool |
|  | Help |

### 8.2.5 Tool Menu

|  | The options in the Tools menu allow you to specify the default part setting, the format to save the part information, etc. |
| --- | --- |

| Option | Description |
| --- | --- |
| Default Setting | Select Default Setting and the Parts Properties window appears. |
|  | You can define the part information and save it as default setting in this window. Click the Advanced button to open the Parts Properties Advanced window. You can define and save the default advanced part information. For contents in the two windows, see Parts Properties |
| Option | Select Option from menu to display the Option window. In this window, you can define the format of *.CSV file. See To save a plan as CSV file. |
| Assembly Manager | This function is currently unavailable. |

Options in the CSV File Setting Panel

| Option | Description |
| --- | --- |
| Amada CSV Format | When AMADA CSV Format is selected, the CSV format used in the WinNEST for AMADA will be applied. |
| Custom | When Custom is selected, setting options are activated. You can make the setting to define the CSV file format. Form1-Form 5 are available. |
| Starting reading line | Sometimes some data in the CSV file does not need to be read. In this case, you can define from which line to begin to read the data. |
| Text qualifier | Define text qualifier used to identifying each item in the CSV. Three options: Double Quotation Mark, Single Quotation Mark and None. |
| Delimiters | Define in the CSV file which kind of mark will be used as delimiters: Tab, Semicolon, Comma, Space, Other (type other marks as needed in the textbox directly). |
| Treat consecutive delimiters as one | If this option is checked, several consecutive delimiters will be regarded as one. |
| Part Path | Select the part path here. If Save part name is selected, the system will load parts by part name; if Save part file path is selected, the system will load parts by part file path. Note: The PC should be shared for remote loading. |
| Plan Items | Define contents in the CSV file. Select items from Plan items and then click Add button to output it into the CSV file; select items from Item and sequence of one record and then click Delete button to remove it. Click the priority button to change the order of the selected items. |
| Number | Use number to display part priority. |
| Character | Use character to display part priority. The system will automatically convert the character into number to judge part priority. |

Options in the Conversion Process Setting panel

| Options | Descriptions |
| --- | --- |
| Start Module before Conversion | Use the third-party’s application to load the plan files of other formats, such as the plan file created by the program of Toshiba. See: Option panel in the System Setting window |
| Carry Out Conversion when Loading Plan | Place a check mark in the check box to enable the conversion function |
| Conversion Process Application | Specify the third-party’s application. You can click the Browse button to locate application to convert the plan file. |

To save a plan as a CSV file:

| 1. | Select Amada CSV format. It outputs as follows: |
| --- | --- |
| 2. | Select Custom and set as follows. |
| 3. | The output is as follows: |

| See: | File |
| --- | --- |
|  | Edit |
|  | View |
|  | Insert |
|  | Tool |
|  | Help |

### 8.2.6 Help Menu

|  | Select Nesting Plan Help from the Help menu to open the help system. |
| --- | --- |

| See: | File |
| --- | --- |
|  | Edit |
|  | View |
|  | Insert |
|  | Tool |
|  | Help |

## 8.3 Toolbars

The toolbars can enhance your interaction with the system. Each button on the toolbar is associated with an option or command. You can click toolbar buttons to execute commands and functions rather than navigate the menus for options. You should study all the tool buttons on each toolbar and display those toolbars that you consider the most useful.

File Toolbar

|  | New |
| --- | --- |
|  | Open |
|  | Save |
|  | Print |

Edit Toolbar

|  | Undo |
| --- | --- |
|  | Redo |
|  | Cut |
|  | Copy |
|  | Paste |
|  | Delete |
|  | Parts Properties |
|  | Sort By Input Order |

View Toolbar

|  | View |
| --- | --- |
|  | Note: Click the thumbnail to define the view. See View Menu. |

Insert Toolbar

|  | Assembly |
| --- | --- |
|  | Part |

Others

| Button | Description |
| --- | --- |
|  | Automatically nest different parts on one sheet if there is enough space. |
|  | Nest different parts on different sheets respectively. |
|  | This textbox displays the name of the selected assembly. Different assemblies can share the same name. You can modify or type a new name in the Assembly Name text box. |
|  | Comments on the selected assembly. |
|  | Lot quantity of the selected assembly. |
|  | Note: Total Quantity of Parts = Lot Quantity of Assembly × Parts Quantity. |

| See: | Parts Properties Summary |
| --- | --- |
|  | Menus |
|  | My Nesting Plan |
|  | Parts List |
|  | Parts Properties |
|  | Parts Properties Advanced |

## 8.4 My Nesting Plan

|  | Right-click in the My Nesting Plan area to open the shortcut menu. There are eleven options on the shortcut menu: New, Expand All, Expand, Collapse, Insert Empty Assembly, Delete Assembly, Insert Part, Delete Line, Cut, Copy and Paste. |
| --- | --- |

| Option | Description |
| --- | --- |
| New | Create a new nesting schedule. |
| Expand All | Expand the selected assemblies, including the subassemblies and display all the parts. Parts in the subassembly of the selected assembly will also display. See Expand All. |
| Expand | Expand the selected assembly and display parts and subassemblies directly under the selected assembly. Parts in the subassembly of the selected assembly will not display. See Expand. |
| Collapse | Collapse the selected assembly and hide all the parts from view. See Collapse. |
| Insert Empty Assembly | Insert an empty assembly in the selected assembly. See Inserting an Assembly. |
| Delete Assembly | Erase the selected assembly. If you select this option, the system will delete the selected assembly without any confirmation. |
| Insert Part | Load a part from the specified database and insert it to the assembly. See: To insert a part. |
| Delete Line | Delete a selected part. |
| Cut | Cut the selected part or assembly and paste it to the clipboard. |
| Copy | Copy the selected part or assembly to the clipboard. |
| Paste | Paste the part or assembly from the clipboard. |

Example:

| Expand All |
| --- |
| 1. Select an assembly and choose Expand All from the shortcut menu. | 2. The selected assembly expands and displays all its subassemblies (including all the parts in them) and parts. |
| Expand |
| 1. Select an assembly and choose Expand from the shortcut menu. | 2. The selected assembly expands and shows its subassembly and parts. |
| Collapse |
| 1. Select an assembly that was previously expanded and choose Collapse from the shortcut menu. | 2. The selected assembly will collapse. The parts are hidden from view. |
| Inserting an Assembly |
| 1. | Select an assembly and right-click to open the shortcut menu. |
| 2. | Select Insert Empty Assembly and an empty assembly will be inserted in the selected assembly. |
| Inserting a Part |
| 1. | Select an assembly and right-click to open the shortcut menu. |
| 2. | Select Insert Part to open the Avon Data Selection window. |
| 3. | Select one or more parts and click Open. The newly loaded parts will display in the selected assembly. |

| See: | Parts Properties Summary |
| --- | --- |
|  | Menus |
|  | Toolbars |
|  | Parts List |
|  | Parts Properties |
|  | Parts Properties Advanced |

## 8.5 Parts List

The Parts List table lists the basic part information.

| Column Title | Description |
| --- | --- |
| No. | Parts number which is assigned by system. |
| CAD | CAD information. |
| CAM | CAM information. |
| Part Quantity | The quantity of the parts. |
| Part Comment | The part comment loaded from the SDD database. |
| Part Name | The name of the part. |
| Material Type | The type of material. |
| Material Thickness | The thickness of material. |
| Weight (g) | The weight of the parts. |
| Unfold X/ Y Size | The dimensions in X and Y-axis of the unfolding drawings of the parts. |
| Rectangle Area | The outer rectangle area of the unfolding drawing of the parts. Rectangle Area = Unfold X x Unfold Y. |
| Area Without Holes | For the parts with inner loops, the dimension displays here is the total area excluding inner loop area. |
| Area With Holes | For the parts with inner loops, the dimension displays here is the total area including inner loop area. |
| Filler Quantity | The quantity of filler parts. |
| Process Date | The process date of parts. Click the cell to show the arrow button. Click the arrow to open the drop-down calendar and select the process date. |
| Due Date | The due date of parts. Click the cell to show the arrow button. Click the arrow to open the drop-down calendar and select the due date. |

Notes:

| 1. | You can click the column headings to sort the parts by ascending or descending order of the column data. |
| --- | --- |
| 2. | You can right-click the column title to display a shortcut menu, and then select the column items you want the system to display. |

To change the column item

| 1. | Right click the column title to open the following shortcut menu: |
| --- | --- |
| 2. | The options with check marks appear as column titles in the table. You can remove the check mark to hide the corresponding information from the table. |
| 3. | You can select More… to open the following window to add items to display that are not in the list. |

Define Display Items Window Buttons

| Button | Description |
| --- | --- |
| Add | Add items in All Items column to Item to Display column. |
| Delete | Delete item from Item to Display column. |
| OK | Save the changes and return to Nesting Plan window. |
| Cancel | Cancel the operation and return to the Nesting Plan window. |
| Up | Move upward the selected item in the list. |
| Down | Move downward the selected item in the list. |

| See: | Shortcut Menu |
| --- | --- |
| See: | Parts Properties Summary |
|  | Menus |
|  | Toolbars |
|  | My Nesting Plan |
|  | Parts Properties |
|  | Parts Properties Advanced |

### 8.5.1 Shortcut Menu

|  | Select a part in the Parts List area to highlight it. Right-click to display the shortcut menu. There are ten options on the shortcut menu: Edit Parts Properties, Cut, Copy, Paste, Delete, Select All, Row Height, Light Attribute Edit, Update CAD Data and To CAD Editor. |
| --- | --- |

Shortcut Menu Options

| Option | Description |
| --- | --- |
| Edit Parts Properties | Select this option to open the Parts Properties window in which you can edit part attribute. |
| Cut | Select this option to cut the selected part to the clipboard. |
| Copy | Select this option to copy the selected part to the clipboard. |
| Paste | Select this option to paste the part previously cut or copied to the clipboard to the selected assembly. |
| Delete | Select this option to delete the selected part. |
| Select All | Select this option to select all the parts displayed in this table. |
| Row Height | Type a value in the Row Height textbox to define the height of rows of the part list table. |
| Light Attribute Edit | Light Attribute Editor allows you to assign lead in/out, Wire joint, Corner joint to the patterns, and then save them as attribute data |
| Update CAD Data | Select this command to overwrite the original data in CAD Editor and update modified data into Nesting Plan. |
| To CAD Editor | Transfer the selected part to CAD mode. Which CAD editor you will transfer into depends on your setting in System Setting. |

| See: | Light Attribute Editor |
| --- | --- |

### 8.5.2 Light Attribute Editor

In the Light Attribute Editor window, you can make settings about the lead in/out, joint, sequence, cut condition and end value to the pattern selected and save the result as SY3 file.

Menu Bar

|  | Option | Description |
| --- | --- | --- |
|  | Open | Load a SY3 or SY5 file to edit. |
|  | Save | Save the currently opened file. |
|  | Save All | Save all opened files. |
|  | Save As | Save the current opened file with a new name. |
|  | Close | Close the currently opened file. |

|  | Option | Description |
| --- | --- | --- |
|  | Undo | Reverse the previous operation. |
|  | Redo | Repeat the previously un-done action. |

|  | Option | Description |
| --- | --- | --- |
|  | Zoom out | Select this option to reduce the view. |
|  | Zoom In | Select this option to magnify the view. |
|  | Zoom Restore | Select this option to fit the pattern to the window. |

|  | Option | Description |
| --- | --- | --- |
|  | Insert | This function is not available at this moment |

Toolbar

| Standard New Open Save Save All Insert Redo Undo Close | View Zoom in Zoom out Zoom Restore Options |
| --- | --- |

The Options window

|  | Specify the display unit and the interface language. |
| --- | --- |

#### 8.5.2.1 To Assign attribute data to a pattern

| 1. | Load a part into the Nesting Plan. |
| --- | --- |
| 2. | Select the part from the part list and right-click to display the shortcut menu. Select the Light Attribute Editor option to display the Light Attribute Editor window. |
| 3. | About Lead in/Out . |
|  | You can click the Lead in/Out button and move the cursor into the work area. A white ball on the pattern indicates the lead position. You can move the cursor to the desired position and click to assign the lead in/out. |
|  | Or you can type a value in the Offset from the edge: text box to specify the position to place the lead in/out. |
|  | And then move the cursor into the work area to assign the lead in/out. |
| 4. | About Joint |
|  | You can click the Joint button and move the pointer to the work area to assign joints. A white ball on the pattern indicates the joint position. Click the pointer to assign the joint when it moves to the desired position. |
|  | You can place a check mark in the Both sides corner tab check box. |
|  | Move the pointer to the corner to assign corner joints. |
| 5. | About Cut Condition |
|  | You can click the Cut Condition button to display the Parameter panel. There are ten kinds of cutting condition and two cutting directions to select from. |
|  | Select the outer loop in left section and the loop selected becomes yellow. |
|  | Select E005 from the Cutting Condition drop-down list, and CCW from the Direction drop-down list. |
|  | If you select the outer loop and then place a check mark in the Non-Tool assign check box, the system won’t assign tools on the selected pattern. |
| 6. | About End Value |
|  | You can click the End Value button to display the Parameter panel. There are four end values to select from. Select an object and then select Machine Stop from Process: drop-down list. |
| 7. | You can click the Remove button to delete the selected joint. |
| 8. | After editing, you can select Save As from the File menu to save the result as a SY3 file or click the Close button to close the window. |
| 10. | You will notice that a symbol mark appears in the CAD column, indicating the existence of SY3 file. |

## 8.6 Parts Properties

Select a part in the Parts List to highlight it, and then double-click to open the Parts Properties window. The options in this window allow you to edit the properties of the part.

| See: | Part Name and Comment |
| --- | --- |
|  | Select Data |
|  | Quantity |
|  | Dates |
|  | Material |
|  | Process |
|  | Nesting |
|  | Change Check box |

| See: | Parts Properties Summary |
| --- | --- |
|  | Menus |
|  | Toolbars |
|  | My Nesting Plan |
|  | Parts List |
|  | Parts Properties Advanced |

### 8.6.1 Part Name and Comment

The part name and comment will appear in this section. You can change the comment by typing new text. When several parts are selected, asterisks (*) will appear in the fields.

| See: | Select Data |
| --- | --- |
|  | Quantity |
|  | Dates |
|  | Material |
|  | Process |
|  | Nesting |
|  | Change Check box |

### 8.6.2 Select Data

This section is used to specify the type of data the system will use when processing parts. Different icons will appear in the CAD cell to indicate the different file types.

| Option | Description |
| --- | --- |
| Pattern | Select this option and the system will use the CAD pattern to process. |
| Attribute Data | Select this option and the system will use the SY3 file to process. |
| Assignment Data | Select this option and the system will use the SY5 file to process. |

Note:

You can specify data priority using the following method if data exists for several parts.

To specify the data priority:

| 1. | Select Default Settings on the Tool menu in Nesting Schedule window. The Parts Properties window displays. |
| --- | --- |
| 2. | You can specify the priority order of calling data by clicking the upward or downward arrow. The assignment on the top of the list has the highest priority. |

| See: | Part Name and Comment |
| --- | --- |
|  | Quantity |
|  | Dates |
|  | Material |
|  | Process |
|  | Nesting |
|  | Change Check box |

### 8.6.3 Quantity

This section is used to specify the quantity of parts, filler parts and prototypes. If you set the part quantity as 5~20, the quantity of filler parts will be the balance of 5 and 20, or 15.

If you set the part quantity as 1 to 1, no filler parts will be specified.

If the first quantity is larger than the second quantity, the second quantity will update to be the same as the first one after you click OK.

To set prototype condition: please refer to Prototype Condition.

| See: | Part Name and Comment |
| --- | --- |
|  | Select Data |
|  | Dates |
|  | Material |
|  | Process |
|  | Nesting |
|  | Change Check box |

### 8.6.4 Dates

The options in the Dates section are used to specify the start and end time of the process.

| Option | Description |
| --- | --- |
| Process | The starting date and time of process. |
| Due | The due date and time of process. |
| Change | See Change Check Box. |

Adjusting the Date

| 1. | You can click the arrow to open the calendar and click the right or left arrows to change the month and year. |
| --- | --- |
| 2. | Select a date from the calendar and date will appear in the field. |

Adjusting the Time

| 1. | Click the hour, minute or second to highlight it. |
| --- | --- |
| 2. | Click the up and down arrow buttons to change the time or type the time in the field using the HH:MM:SS format. |

How Dates Affect the Process

| 1. | Load two parts that use the same material type from the database. The two parts are nested on one sheet after you use the Auto Execute option. |
| --- | --- |
| 2. | Open the Nesting Plan window and specify a process date for one part, and a later date for the remaining part in Dates section. The process date for the two parts is different. Enable Grouping nesting by selecting Process Date in the Group window. |
| 3. | Click the Auto Execute button in the main window and note the result. The two parts are nested on two different sheets. |

| See: | Part Name and Comment |
| --- | --- |
|  | Select Data |
|  | Quantity |
|  | Material |
|  | Process |
|  | Nesting |
|  | Change Check box |

### 8.6.5 Material

This section is used to specify the material type, thickness and name. To change them, you could click the arrow button to open the drop-down list and select a type or thickness.

If you select sheet by Material Name, you can select the material by the material name registered in the Material Manager.

If you select sheet by Material/Thickness, you can select material by the material type and thickness. See: System Determining Sheet by Material Name

| See: | Part Name and Comment |
| --- | --- |
|  | Select Data |
|  | Quantity |
|  | Dates |
|  | Process |
|  | Nesting |
|  | Change Check box |

### 8.6.6 Process

|  | This section is used to display the turret layout and the laser material name of the selected material that is the same as that in the Cutting Condition window. |
| --- | --- |
|  | Place a check mark in [De-Burring ON/OF] to assign deburring tool automatically. See Deburring Place a check mark in [SLOT AUTOON/OFF] check box to assign slot tools automatically. See: Slot2&3 As for the sheet with only TK-parts, the process sequence will be [Punch -> Laser (excluding the final cut) -> Laser Final Cut]. Place a check mark in the Process Forming Down check box the process sequence will be [Punch (excluding down forming) -> Laser (excluding final cut) -> Punch (down forming) -> Laser (final cut)] |

| See: | Part Name and Comment |
| --- | --- |
|  | Select Data |
|  | Quantity |
|  | Dates |
|  | Material |
|  | Nesting |
|  | Change Check box |

### 8.6.7 Nesting

The options in this section are used to specify nesting priority, rotation and common line cutting.

| Option | Description |
| --- | --- |
| Priority | This item is used to specify the layout priority of parts. Please refer to Defining the Part Priority. |
| Group ID | This item is used to specify group ID for parts. Please refer to Defining the Group ID for the Parts. |
| Rotation | This section is used to specify whether parts are allowed to rotate when nesting. Please refer to Rotation with different condition. |
| Not Allowed | If you select this option, parts are not allowed to rotate when nesting. |
| Free | If you select this option, parts can rotate freely when nesting. This function helps to increase sheet utility. Note: To enable Common Cut and Pair functions, you need to select Free from the Rotation combo box. |
| Use Sheet’s Grain Angle+-180 Degrees | If you select this option, parts will rotate at the sheet’s grain angle +-180 degrees. |
| Use Sheet’s Grain Direction | If you select this option, the parts will rotate according to the grain direction of the sheet specified in the Material Manager window. If the grain direction is horizontal, the parts will rotate at 0 or 180 degrees. If the grain direction is vertical, the parts will rotate at 90 or 270 degrees. |
| Rotate 90 Degrees | If you select this option, the parts will rotate at 90 degrees. |
| Common Line Cutting | If you select this option, the machine system will allow common line cutting. Please refer to Different result of the Common Line Cutting. |
| Grid | Common-cut or common-punch grid parts. To use this function, you should select Joint as the End Value |
| X direction | Common-cut or common-punch the X-axis edges of the parts. |
| Y direction | Common-cut or common-punch the Y-axis edges of the parts. |
| ALA Logic | If you select this option, the system can common-cut parts that the system originally can’t common-cut by rotating or reversing a certain degree. This option will save the sheet and reduce the process time. This unavailable for EM machine. |
| ALA Logic (Pair By Rotation) | If the part quantity is more than 2, If you select this option, them in pair. This unavailable for EM machine. |
| Different Part | If you select this option, the system will common-cut different parts. This unavailable for EM machine. |
| Fixed Qty X/Y | Specify the parts quantity in X and Y Axis in a grid. |
| Change | See: Change check box |

| See: | Defining the Part Priority |
| --- | --- |
|  | Defining the Group ID for Parts |
|  | Rotation with Different Condition |
|  | Different Result of the Common Line Cutting |

| See: | Part Name and Comment |
| --- | --- |
|  | Select Data |
|  | Quantity |
|  | Dates |
|  | Material |
|  | Process |
|  | Change Check box |

#### 8.6.7.1 Defining the Part Priority

| 1. | Specify the processing starting point and direction as follows. |
| --- | --- |
| 2. | Define different priorities for these two different parts respectively. The priority of the larger one is set to 3; the priority of the smaller one is set to 4. The larger one has higher priority and it is nested first after auto execution. |
| 3. | If the priority of the larger part is 4 and the priority of the smaller part is 3, the smaller part is nested first. |

Note:

If you select the Give Higher Priority to Group of Small Parts in the Group window, the system will ignore the priority you set in the Part Properties window and strictly nest smaller parts at first.

| See: | Defining the Group ID for Parts |
| --- | --- |
|  | Rotation with Different Condition |
|  | Different Result of the Common Line Cutting |

#### 8.6.7.2 Defining the Group ID for Parts

| 1. | Define different Group ID for two different parts. The Group ID of first part is set to 2 and that of the second one is set to 3. |
| --- | --- |
| 2. | Define the Grouping Priority as follows. |
| 3. | The parts with different Group IDs will be nested on different sheets. The parts whose Group ID is 2 will be nested first. |

| See: | Defining the Part Priority |
| --- | --- |
|  | Rotation with Different Condition |
|  | Different Result of the Common Line Cutting |

#### 8.6.7.3 Rotation with Different Condition

In nesting section, click Rotation arrow button to display the drop-down list. Select one option to change the part rotation during the nesting process.

If Not Allowed is selected, the parts will not be rotated during the process.

If Free is selected, parts will be rotated according to the other system settings.

If Use Sheet’s Grain Angle+-180 Degrees is selected,

When the grain direction is vertical, the result is as follows.

If Use Sheet’s Grain Angle is selected,

When the grain direction is vertical, the result is as follows.

If Rotate 90 Degrees is selected, parts will be rotated 90 degrees.

| See: | Defining the Part Priority |
| --- | --- |
|  | Defining the Group ID for Parts |
|  | Different Result of the Common Line Cutting |

#### 8.6.7.4 Different Result of the Common Line Cutting

When Common Line Cutting is checked, six kinds of common cut methods are activated. Grid, X direction, and Y direction are available for punch machine.

When Grid is selected, specify the grid quantity in Part Properties window.

The parts will be processed as follows.

When X direction is selected, specify the grid quantity in Part Properties window as following:

Parts will be processed as follows:

When Y direction is selected, specify the grid quantity in Part Properties window as following:

Parts will be processed as follows:

| See: | Defining the Part Priority |
| --- | --- |
|  | Defining the Group ID for Parts |
|  | Rotation with Different Condition |
|  | Different Result of the Common Line Cutting |

### 8.6.8 Change Check Boxes

When you select multiple parts with different conditions for editing, the Change check boxes will become active. If you need to change any of the conditions, place a check mark in the corresponding check box to activate the condition for modification. The modifications will be applied to all the selected parts.

Example

| 1. | Place a check mark in the Change Qty check box and specify the options as follows: |
| --- | --- |
| 2. | Part quantity will be changed as follows. |

| See: | Part Name and Comment |
| --- | --- |
|  | Select Data |
|  | Quantity |
|  | Dates |
|  | Material |
|  | Process |
|  | Nesting |

## 8.7 Parts Properties Advanced

Click Advanced button and Parts Properties Advanced window appears. You can specify Special Information, Size Definition, Code Definition, Sketch Nesting and User Define in this window.

| See: | Material |
| --- | --- |
|  | Special Information |
|  | Size Definition |
|  | Code Definition |
|  | Nesting |
|  | Process and User Define |
|  | Taking Out Station |
|  | Taking Out Part Grid as One Part |

| See: | Parts Properties Summary |
| --- | --- |
|  | Menus |
|  | Toolbars |
|  | My Nesting Plan |
|  | Parts List |
|  | Parts Properties |

### 8.7.1 Material

The options in this section are the same as those in the Material section in the Part Properties window.

| See: | Special Information |
| --- | --- |
|  | Size Definition |
|  | Code Definition |
|  | Nesting |
|  | Process and User Define |
|  | Taking Out Station |
|  | Taking Out Part Grid as One Part |

### 8.7.2 Special Information

The options in this section are used to specify special information for the material.

| Option | Description |
| --- | --- |
| Auto | If you select this option, the system will select the optimum sheet size from sheet database. The Size Definition and Code Definition section will be disabled. |
| Standard | If you select this option, the system will only select standard sheets for cutting. Remnant and skeleton sheets are not available. |
| Fix | If you select this option, you should define the material type in the drop-down list. |
| None | Common type of the material will be used. |
| Coated | Coated steel material will be used. |
| Colored Steel | Colored steel material will be used. |

| See: | Material |
| --- | --- |
|  | Size Definition |
|  | Code Definition |
|  | Nesting |
|  | Process and User Define |
|  | Taking Out Station |
|  | Taking Out Part Grid as One Part |

### 8.7.3 Size Definition

The options in this section are used to specify the correct size of the sheet. These options are only available when you select Standard or Fix in the Special Information section.

| Option | Description |
| --- | --- |
| Auto | If you select this option, the system will select a suitable sheet size automatically. |
| Fix | If you select this option, the size table is enabled. You can then select a specific sheet size. The system will only use the specified size during the process. |

| See: | Material |
| --- | --- |
|  | Special Information |
|  | Code Definition |
|  | Nesting |
|  | Process and User Define |
|  | Taking Out Station |
|  | Taking Out Part Grid as One Part |

### 8.7.4 Code Definition

This section is used to set the code of the material. It is only available when you select Fix in Size Definition section.

| Option | Description |
| --- | --- |
| Auto | If you select this option, the system will select the sheet code automatically. |
| Fix | This option is used to specify sheet code. You can select a sheet code from the drop-down list. |

| See: | Material |
| --- | --- |
|  | Special Information |
|  | Size Definition |
|  | Nesting |
|  | Process and User Define |
|  | Taking Out Station |
|  | Taking Out Part Grid as One Part |

### 8.7.5 Nesting

|  | This section is used to specify nesting type. |
| --- | --- |

| Option | Description |
| --- | --- |
| Standard | Standard nesting will be used. |
| Sketch Nesting | Sketch nesting will be used. |
| Grid | If you select this option, parts will be nested as a grid. Part quantity setting will be ignored. |

| See: | Standard Nesting |
| --- | --- |
|  | Sketch Nesting |
|  | Grid Nesting |

| See: | Special Information |
| --- | --- |
|  | Size Definition |
|  | Code Definition |
|  | Process and User Define |
|  | Taking Out Station |
|  | Taking Out Part Grid as One Part |

#### 8.7.5.1 Standard Nesting

If you select Standard, the parts will be nested as follows:

| See: | Sketch Nesting |
| --- | --- |
|  | Grid Nesting |

#### 8.7.5.2 Sketch Nesting

Note:

Make sure that there is suitable sketch material in the Material Manager before you use the Sketch Nesting option. If necessary, create sketch material.

Example:

| 1. | There is 350 x 250 sketch material in the Material Manager: |
| --- | --- |
| 2. | If the part size is 300 x 200, you need to set the maximum tolerance for the sketch material in the Nesting window. |
| 3. | Select the Sketch Nesting option. |
| 4. | The parts will be nested as follows: |

| See: | Standard Nesting |
| --- | --- |
|  | Grid Nesting |

#### 8.7.5.3 Grid Nesting

If you select the Grid option, the parts will be nested as follows:

| See: | Standard Nesting |
| --- | --- |
|  | Sketch Nesting |

### 8.7.6 Process and User Define

The options in this section are unavailable if only Dr. ABE Blank is installed on the PC. The options can only be used when other software products, such as FabriTRAK, are loaded on your computer. For example, if you load a CSV file generated by FabriTRAK, some of the user-defined parameters would appear in the fields of this section.

| See: | Material |
| --- | --- |
|  | Special Information |
|  | Size Definition |
|  | Code Definition |
|  | Nesting |
|  | Taking Out Station |
|  | Taking Out Part Grid as One Part |

### 8.7.7 Taking Out Station

This section is used to specify Taking Out information. The options in this section are not available unless you have enabled TK device in the Machine Set window. See: Taking Out Information

| Option | Description |
| --- | --- |
| Station | You can only select None for EM machine. |
| Taking Out the Part Grid as One Part | Enable this option and the system will grid the parts in groups, and treat the parts in one group as one part and then performs taking out process. Note: Only the same parts can be nested and gridded in one group. |
| Specify Quantity X, Y | Specify the number of parts along the X-axis and Y-axis. |
| Part-Spacing | Specify the part spacing of the grid in the X and Y direction. Note: The value you specify here is only effective when the system treats several parts as a grid and performs taking out process. |

| See: | Material |
| --- | --- |
|  | Special Information |
|  | Size Definition |
|  | Code Definition |
|  | Nesting |
|  | Process and User Define |
|  | Taking Out Part Grid as One Part |

### 8.7.8 Taking Out Part Grid as One Part

Sometimes the parts we have processed are too small and cannot be taken out.  The Taking Out Part Grid as One Part option allows the system to grid the small parts in groups, and then takes them out.

To take out small parts in groups

| 1. | We will nest 20 small parts. |
| --- | --- |
| 2. | Enable TK device in the Taking Out Information. |
| 3. | In the Peripherals window, place a check mark in the Taking Out On/Off check box to enable taking out conditions. |
| 4. | Select Joint and TakeOut as the process after method. |
|  | Note: We must select Joint as the process after method for the small parts, otherwise system cannot take out the part grid as one part. |
| 5. | Open the Parts Properties window, click the Advanced button and specify the settings as follows. |
| 6. | After auto execution, the nesting result is as follows. |

| See: | Material |
| --- | --- |
|  | Special Information |
|  | Size Definition |
|  | Code Definition |
|  | Nesting |
|  | Process and User Define |
|  | Taking Out Station |

# Chapter 9: Preference File Window

The options in the Preference windows are used to specify the default parameters for system operations. For example, if you click the Nesting Preference button in the main Dr. ABE window, the corresponding preference window will appear.

| See: | Preference Window Overview |
| --- | --- |
|  | Preference Window Menu |
|  | Preference Window Toolbar |

## 9.1 Preference Window Overview

The Preference window consists of three panes: Tree View, Preference File and Display Area. In the Tree View, you can select a machine and its corresponding preference files in the upper Preference File pane will display. The information of the selected preference file will appear in the lower Display Area.

| See: | Splitter Bars |
| --- | --- |
|  | Tree View Pane |
|  | Preference File Pane |
|  | Display Area Pane |

| See: | Preference Window Menu |
| --- | --- |
|  | Preference Window Toolbar |

### 9.1.1 Splitter Bars

The panes in Preference window are separated by splitter bars. To adjust the display area of each pane, just click and hold the corresponding splitter bar and drag it to the desired location. Release the mouse button when you have finished resizing the pane.

| See: | Tree View Pane |
| --- | --- |
|  | Preference File Pane |
|  | Display Area Pane |

### 9.1.2 Tree View Pane

Tree view provides an expandable view about all the available resources.

| See: | Splitter Bars |
| --- | --- |
|  | Preference File Pane |
|  | Display Area Pane |

| See: | Hierarchical Structure |
| --- | --- |
|  | Shortcut Menu |

#### 9.1.2.1 Hierarchical Structure

|  | The Tree View presents a hierarchical view of all the available resources. The minus box before an icon indicates that its subordinate items are displayed. For example, in the right figure, the My Preference node displays the available machines, Public folder and Recycle Bin. |
| --- | --- |
|  | In the picture above, the plus box before Public folder indicates there are subordinate items. Click the minus box before the icon and all the subfolders will collapse, while clicking the plus box, all the sub items will expand as follows. |

| See: | Shortcut Menu |
| --- | --- |

#### 9.1.2.2 Shortcut Menu

Right-click an icon in the Tree View to display the shortcut menu. If necessary, you can navigate the cascading menu system to select menu options. The shortcut options you can select are dependent on the icons you select. For example, if you select a FO machine, you can only create the preference files about Laser machine, while options about punch and combination machines are not activated. If you right-click My preference icon, you can only select the Machine Folder and Collapse options. See: Create a new machine folder

| Option | Description |
| --- | --- |
| Expand | Expand the subordinate items. It will change into Collapse mode if no further information in the folder is selected. |
| New | The New submenu consists of options that allow you to create new folders and corresponding preference files. |
|  | Note: The Machine Folder, Material Type Folder, Thickness Folder and Laser Material Name Folder options only create new folders in the Tree View pane. The remaining options are used to create files in the Preference File pane. |
| Cut | Cut the selected item to the clipboard. |
| Copy | Copy the selected item to the clipboard. |
| Paste | Paste the items previously copied or cut to the clipboard to the desired place. |
| Delete | Delete the selected item. |
| Rename | Rename the selected item. |

Note: In the Public folder, only Turret Type and Turret Type (PDC) options have shortcut menus. These shortcut options are used to create a new turret type preference file.

The folders and files deleted in the Preference window are transferred to the Recycle Bin. Right-click the Recycle Bin icon to display the shortcut menu.

| Option | Description |
| --- | --- |
| Expand | Display all the items in the recycle bin |
| Delete | Delete all the items in the recycle bin. |
| Restore | Restore the selected item to its original place. |
| Restore All | Restore all the deleted items to their original places. |
| Empty Recycle Bin | Empty all the items in the Recycle Bin. |

To create a new machine folder:

| 1. | Select My Preference icon and right-click to display the shortcut menu. |
| --- | --- |
| 2. | Select New to Machine Folder. |
| 3. | In the MachineName window, select the Machine Type and Machine Name from the drop-down list, and then click Add button to add the machine folder to the Tree View. Notes: You can only add the machine folders for the machines that have been registered in the Machine Manager while have no corresponding machine folders. |
| 4. | A new machine folder LCXI is added to the Tree View. |

| See: | Hierarchical Structure |
| --- | --- |

### 9.1.3 Preference File Pane

|  | You can use two methods to display preference files: Details and Icon. The menu is used to toggle between Detail and Icon view. The Preference File pane lists all the available files. You can double-click a file to open it. You can also create, delete and rename new preference file. |
| --- | --- |
|  | When the Details option is selected. |
|  | When the Icon option is selected. |

| See: | Creating a New File |
| --- | --- |
|  | Preference File Shortcut Menu |

|  | Splitter Bars |
| --- | --- |
|  | Tree View Pane |
|  | Display Area Pane |

#### 9.1.3.1 Creating a New File

Select an icon in the Tree View, such as EM-L, and then right click to open the shortcut menu. Select New to Nesting Preference. A new Nesting Preference file will appear in the Preference File pane. The new file name will be New by default.

| See: | Preference File Shortcut Menu |
| --- | --- |

#### 9.1.3.2 Preference File Shortcut Menu

|  | Select a file from Preference File pane and right-click to display the shortcut menu. |
| --- | --- |

| Option | Description |
| --- | --- |
| Cut | Cut the file to the clipboard. |
| Copy | Copy the file to the clipboard. |
| Paste | Paste the copied file from the clipboard. |
| Delete | Delete the file. |
| Rename | This option allows you to rename the selected item in the pane. |
| Set Default | This option will set the selected file as default when there are several preference files of the same kind in the Preference File pane. |

| See: | Creating a New File |
| --- | --- |

### 9.1.4 Display Area Pane

When you click a file in the Preference File pane, the Display Area will update and allow you to view the contents. You can use vertical or horizontal scroll bars to navigate through the sections. You can also double-click the preference file to open the corresponding window.

| See: | Splitter Bars |
| --- | --- |
|  | Tree View Pane |
|  | Preference File Pane |

## 9.2 Preference Window Menu

|  | The menu bar consists of five menus: File, Edit, Tools, Window and Help. |
| --- | --- |

| See: | Preference Window Overview |
| --- | --- |
|  | Preference Window Toolbar |

| See: | File |
| --- | --- |
|  | Edit |
|  | Tools |
|  | Window |
|  | Help |

### 9.2.1 File

| Option | Description |
| --- | --- |
| New | Select an option from the New submenu to create the relevant file. |
|  | Note: Some options are disabled under certain conditions. |
| Save | Click Save to save the settings made in the current file. |
| Save All | Click Save All to save all the settings made in all files. |
| Close | Close the current Preference window. |

| See: | Edit |
| --- | --- |
|  | Tools |
|  | Window |
|  | Help |

### 9.2.2 Edit

|  | The options on the Edit menu allow you to edit the folders or files. You can Redo and Undo the operations, cut, copy, delete or rename the files. The options in this menu have the same functions as those in the shortcut menu in the Preference File window |
| --- | --- |

| See: | File |
| --- | --- |
|  | Tools |
|  | Window |
|  | Help |

### 9.2.3 Tools

|  | The options on the Tools menu allow you to change the display settings. You can change the interface languages or hide the toolbar. |
| --- | --- |

| Option | Description |
| --- | --- |
| Option | Select Tools to Option to open the Option window. You could check or modify the system settings. See: Option window. |
| Tool Bars |  |
| Standard | Place a check mark before the Standard option to display the standard toolbar. |
| View | Place a check mark before the View option to display the View toolbar. |

Option Window

| Option | Description |
| --- | --- |
| System Setting | Specify the system unit and language. |
| Display Unit | Two units are available: Metric and Inch. |
| Language | The available languages are Japanese, English and Chinese (PRC). |
| Save Confirmation Setting | If Display Save Confirmation Window is selected, when you close the Preference window, a Save Confirmation window will display; if Don’t Display Save Confirmation Window is selected, no confirmation messages will display. |
| Current Folder | The path of the folder where the preference files are saved. Click button to browse folder to change the default folder to save the preference files. |
| The Priority of Folder of Same Level | The priority of folders of same level, you can clicking the up and down arrow button to change the priority. |

| See: | File |
| --- | --- |
|  | Edit |
|  | Window |
|  | Help |

### 9.2.4 Window

|  | The currently opened file or folder names will appear on the Window drop-down list. A check mark next to a folder or file name will indicate that its corresponding window is active. |
| --- | --- |

| See: | File |
| --- | --- |
|  | Edit |
|  | Tools |
|  | Help |

### 9.2.5 Help

|  | Select Preference Help from the Help menu, or press <F1>, to open the on-line help reference. |
| --- | --- |

| See: | File |
| --- | --- |
|  | Edit |
|  | Tools |
|  | Window |

## 9.3 Preference Window Toolbar

The toolbar can enhance your interaction with the system. Each button on the toolbar corresponds to a command on the menu. You may prefer to click buttons to execute commands and functions, rather than navigate the menus.

Standard Toolbar

|  | New |
| --- | --- |
|  | Undo |
|  | Redo |
|  | Cut |
|  | Copy |
|  | Paste |
|  | Delete |
|  | Save |
|  | Save All |
|  | Help |
|  | Backup&Restore |

View Toolbar

|  | View |
| --- | --- |

Note:

Click the arrow button next to the New button to open the drop-down menu. You can select to create new folder and files.

Click the arrow button next to the View button to display a drop-down menu from which you can select whether to display the preference files in detail or as icons.

If you select Details, all the preference files will display as follows.

If you select Icon, all the preference files will be display as follows.

| See: | Preference Window Overview |
| --- | --- |
|  | Preference Window Menu |

# Chapter 10: Nesting Preference

The Nesting Preference window allows you to define the various nesting parameters to process parts. The system will use these parameters to nest the parts as efficiently as possible when you use the Auto Execute option.

To open the nesting window:

| 1. | Click the Nesting Preference button in the Dr. ABE window to open the Preference window. |
| --- | --- |
| 2. | Select a combo machine name (such as the EM-L) from the Tree View pane on the left. |
| 3. | Double-click the Nesting icon in the Preference File pane to open the Nesting window. The Nesting window consists of six panels: Nesting Logic 1, Nesting Logic 2, Initial Clamp Position, Part-Spacing/Nesting Border, Material Selection and Share to Size. |

| See: | Nesting Logic 1 |
| --- | --- |
|  | Nesting Logic 2 |
|  | Initial Clamp Position |
|  | Part-Spacing/Nesting Border |
|  | Material Selection |
|  | Share to Size |

## 10.1 Nesting Logic 1

In Nesting Logic 1 panel, you can review and modify the basic settings for nesting, such as Nesting Type, Pattern Setting and the Start Point/Direction.

| See: | Nesting Type |
| --- | --- |
|  | Pattern Setting |
|  | Start Point/Direction |

| See: | Nesting Logic 2 |
| --- | --- |
|  | Initial Clamp Position |
|  | Part-Spacing/Nesting Border |
|  | Material Selection |
|  | Share to Size |

### 10.1.1 Nesting Type

|  | This section allows you to specify whether parts are nested according to the individual shapes or the overall part boundaries. |
| --- | --- |

| Option | Description |
| --- | --- |
| Free Shape | If you select this option, the parts will be nested with its own shape. The system will nest the parts with the best utilization. |
| Rectangle | If you select this option, the parts will be nested with an outer rectangle. Within the range of the outer rectangle, system will not nest other parts even though there is blank area. |
|  | Note: If you select Rectangle, the Common Line Cutting option is disabled. |

Example:

| 1. | For example, you want to nest the following part: |
| --- | --- |
| 2. | If you select Free Shape, system will use the part shape as a parameter in the nesting process. The system will adjust the layout to achieve the best sheet utilization and nest the part instances as follows: |
| 3. | If you select Rectangle, the system will calculate a rectangular zone according to the overall part size and include the part within the rectangle: |
|  | The system will nest the parts as follows: |

| See: | Pattern Setting |
| --- | --- |
|  | Start Point/Direction |

### 10.1.2 Pattern Setting

|  | This section is used to specify the nesting order by the area, the dimension in the X-axis or Y-axis or production schedule. |
| --- | --- |

| Option | Description |
| --- | --- |
| Auto Utilization (Loop All Pattern) | The system will check the remaining nesting orders and then select the one that achieves best utilization. |
| Special | The system will ignore the priority setting in the Nesting Plan and nest parts. |
| Area | Parts with a larger area will be nested first. |
| X-Axis | The parts having a greater dimension along the horizontal axis will be nested first. |
| Y-Axis | The parts having a greater dimension along the vertical axis will be nested first. |
| Production Schedule | If Production Schedule is selected, parts will be nested according to the priority set in the Nesting Plan. The higher the production priority, the lower the nesting priority. See: How to nest parts by Production Schedule |

| See: | Nesting Parts by the Production Schedule |
| --- | --- |

| See: | Nesting Type |
| --- | --- |
|  | Start Point/Direction |

#### 10.1.2.1 Nesting Parts by the Production Schedule

| 1. | Set a different Group ID for each part, but set the same priority for the parts in the Nesting Plan. |
| --- | --- |
| 2. | Enable the Group Nesting function in the Group window. |
| 3. | Select Production Schedule in the nesting window. |
| 4. | The three parts are nested on three sheets according to the Group ID. |
| 5. | Set the same Group ID for all the parts, but set a different Priority for each part in the Nesting Plan window: Part A (Priority: 2), Part B (Priority: 3) and Part C (Priority: 4). The nesting result displays as follows: |

### 10.1.3 Start Point/Direction

|  | The options in this section are used to specify the start point and nesting direction. You could select a start point and direction by clicking corresponding point or arrow. The selected start point will become yellow and the selected direction arrow will become green. |
| --- | --- |
|  | You can shift the parts along the horizontal, vertical and diagonal axis. Click the directional arrow in the graphic below Shift After Nesting to specify the shift direction. The selected direction arrow will become green. |
| If you select a shift direction under Shift After Nesting, the Maximum Dimension for X Shifting or Maximum Dimension for Y Shifting text boxes become available. You can specify the maximum dimensions to shift the parts in the direction selected. |
| Note: If the X or Y value of the boundary box of all the nested parts is less than the X or Y shifts value you have specified, parts will be shifted in that direction. The boundary box (the outer rectangle) is indicated in red: |

| See: | How to Define the Start Point/Direction |
| --- | --- |
|  | Example of Shift After Nesting |

| See: | Nesting Type |
| --- | --- |
|  | Pattern Setting |

#### 10.1.3.1 How to Define the Start Point/Direction

| 1. | If you specify the following starting point and direction: |
| --- | --- |
|  | The nesting result will be as follows: |
| 2. | If you specify the starting point and direction as below: |
|  | The nesting result will be as follows: |
| 3. | If you specify the starting point and direction as below: |
|  | The nesting result would be as follows: |
| 4. | If you specify the starting point and direction as below: |
|  | The nesting result will be as follows: |

| See: | Example of Shift After Nesting |
| --- | --- |

#### 10.1.3.2 Example of Shift After Nesting

| 1. | The Start Point/Direction is set as follows. See: Start Point/Direction |
| --- | --- |
| 2. | If Shift After Nesting is not selected, the nesting result will be as follows. |
|  | The part size is as follows. |
|  | And the dimension of the outer rectangle of the four parts will be as follows: |
| 3. | If Shift After Nesting in the X direction is enabled, and the maximum shifting value set at 700, which is greater than the X value of the outer rectangle, the nesting result will be as follows: |
|  | Select Y direction. The maximum shifting value set as 200, also. The parts will be shifted in the Y direction. |
|  | Select X and Y direction. Type 700 as the maximum shifting value for X direction and 200 for Y direction. The parts will be shifted both in X and Y direction. |

| See: | How to Define the Start Point/Direction |
| --- | --- |

## 10.2 Nesting Logic 2

Click the Nesting Logic 2 tab to activate the Nesting Logic 2 panel. In this panel you can specify the parameters for the part grid, the dead zone avoidance, the part rotation pitch, the pair and part in part function, and the line gap that can be ignored.

| See: | Grid Pattern |
| --- | --- |
|  | Nest Around Clamps |
|  | Part Rotation |
|  | Utilization |

| See: | Nesting Logic 1 |
| --- | --- |
|  | Initial Clamp Position |
|  | Part-Spacing/Nesting Border |
|  | Material Selection |
|  | Share to Size |

### 10.2.1 Grid Pattern

|  | This section is used to activate the part grid function. If you select Enable Part Grid option, system will nest the same parts as a grid. |
| --- | --- |

Example

If Enable Part Grid is selected, the system will create part grids while nesting the same parts:

If Enable Part Grid is disabled, the system won’t grid the parts when nesting:

| See: | Nest Around Clamps |
| --- | --- |
|  | Part Rotation |
|  | Utilization |

### 10.2.2 Nest Around Clamps

|  | Usually, the system will avoid nesting the parts on the clamp or dead zone to avoid any damage to the machine head or machine. However, if repositioning is available, you can nest parts in the clamp area or dead zones for better sheet utilization. The three options within the Nest Around Clamps section are used to specify whether to avoid clamps, the clamp area and dead zone. |
| --- | --- |

| Option | Description |
| --- | --- |
| Neglect Clamps | If you select this option, the system will ignore the clamp and dead zone information while nesting. It is not recommended unless repositioning is enabled. |
| Avoid Clamp Areas | If you select this option, the system will nest the parts around the clamps and avoid the clamp areas. |
| Avoid Dead Zones | If you select this option, the machine system will avoid the clamp dead zones when nesting. |

| See: | Grid Pattern |
| --- | --- |
|  | Part Rotation |
|  | Utilization |

### 10.2.3 Part Rotation

|  | You can select a number from the Rotation Pitch drop-down list to define the incremental angle for the part rotation. Specifying a rotation pitch for nesting will greatly reduce the nesting calculation time. If you select Auto, the system will rotate the part to any angle. If you select a number, the system will rotate the part incrementally according to the multiple you selected. For example, if you select 2, the rotation angle will be 4, 6, 8, 10 etc. The system will use the degree that results in the best sheet utilization. Selecting 1 will have the same effect as selecting Auto. |
| --- | --- |

| See: | Grid Pattern |
| --- | --- |
|  | Nest Around Clamps |
|  | Utilization |

### 10.2.4 Utilization

This section is used to specify methods to increase sheet utilization including Pair and Part in Part nesting.

| Option | Description |
| --- | --- |
| Pair | This option is used to nest the parts as pairs. Some irregular-shaped parts nested as pairs will result in better sheet utilization. |
| Part In Part | This option allows you to nest parts inside the cutouts of other parts. This will increase the sheet utilization. |
|  | Note: To enable Part In Part, you need to set the correct spacing between parts in the horizontal and vertical direction. |
| Minimum Cutout Edge Length | Type a value in the text box to define the length of the shortest edge of cutout. If the shortest edge is smaller than this value, the system will not nest parts into the cutout. |

| See: | Pair Example |
| --- | --- |
|  | Part In Part Example |

| See: | Grid Pattern |
| --- | --- |
|  | Nest Around Clamps |
|  | Part Rotation |

#### 10.2.4.1 Pair Example

Note: To enable Pair, you need to select Free from the Rotation drop-down list in the Parts Properties window.

If the Pair option is enabled, system will nest the parts as follows:

If the Pair option is disabled, system will nest the parts as follows:

| See: | Part In Part Example |
| --- | --- |

#### 10.2.4.2 Part in Part Example

| 1. | You want to nest two different parts on the sheet. One of the parts is larger and has a large cutout. The dimension of the cutout is 400 x 300. |
| --- | --- |
| 2. | Place a check mark in the Part In Part check box to enable the option. Type 250 in the Minimum Cutout Edge Length text box. |
| 3. | The smaller parts are nested within the cutout of the larger part after auto execution: |
| 4. | Type 400 in the Minimum Cutout Edge Length text box. |
| 5. | In this example, one of lines of the cutout is 300, which is smaller than Minimum Cutout Edge Length you specified. The smaller parts will not be nested within the cutout of the larger part: |

| See: | Pair Example |
| --- | --- |

## 10.3 Initial Clamp Position

Click the Initial Clamp Position tab to activate the Initial Clamp Position panel. The options in this panel allow you to specify number of clamps and the clamp locations.

### 10.3.1 Number of Clamp

|  | Type the number of clamps in the text box, or use the spin controls to specify the number of clamps. The maximum number of clamps is determined by the settings in the Machine Set window. The range is from 0 to 4. |
| --- | --- |

| See: | Absolute |
| --- | --- |
|  | Advance |

### 10.3.2 Absolute

Use the Absolute option to edit the X value or horizontal position of the clamps in the diagram. The clamp locations are all measured relative to the left edge of the sheet. For example, the illustration below indicates that there are two clamps. The position of the first clamp is 300.00, while the position of the second is set at 800.00.

| See: | Number of Clamp |
| --- | --- |
|  | Advance |

### 10.3.3 Advance

The Advance option is used to define clamp parameters for different materials. The following table will appear after you select Advance:

| Column Title | Description |
| --- | --- |
| EQ. | The equation relationship between Sheet Size X and its value. |
| Sheet Size X | The X value of the sheet. |
| Base 1 (or 2…) | The reference of the clamp position. |
| MatLeft | The X-axis distance from the clamp to the left side of the material. |
| MatRight | The X-axis distance from the clamp to the right side of the material. |
| Origin | The X-axis value from the clamp to the origin. |
| Max Process Right | The maximum process range to the right of the material. |
| NO.1 (or 2…) | The distance to clamp NO.1 (or 2…). |
| Value 1 (or 2…) | The value of the clamp position relative to Base 1 (or 2…). |
|  | Note: If Absolute is selected, the settings for clamps in this section will be available for all the materials. |

Example:

| 1. | If you specify the clamp positions as follows: |
| --- | --- |
| 2. | Check the settings you have made in the Machine Set window. The settings should match those you have made in the Initial Clamp Position panel. |
| 3. | The nesting result will be as follows. |
| 4. | If Advance is selected, you can specify unique settings for different sheets. For example, you can specify the number of clamps first, and then use the Advance table for details. |
| 5. | The different clamp settings will be applied to the material of different sizes: |

| See: | Number of Clamp |
| --- | --- |
|  | Absolute |

## 10.4 Part-Spacing and Nesting Border

Click the Part-Spacing/Nesting Border tab to activate the Part Spacing/Nesting Border panel. In this panel, you can specify the part spacing and sheet margins.

### 10.4.1 Advance

Place a check mark in the Advance check box to display the Advance table. You can specify the part spacing and nesting borders for material of different types and thickness.

Example:

| 1. | Set the spacing for two different kinds of material: 10 for AL material and 20 for CRS material: |
| --- | --- |
| 2. | Load two kinds of parts into the Nesting Plan. Select AL and CRS as the types of the sheet respectively. |
| 3. | The system will nest the Part 2 on the CRS material, and the part spacing is 20. |
| 4. | The system will nest Part 1 on the AL material, and the part spacing is 10. |

## 10.5 Material Selection

Click the Material Selection tab to activate the Material Selection panel. The options in this panel allow you to specify the material type to be used and determine the utilization of reusable sheets.

| See: | Automatic Material Selection |
| --- | --- |
|  | Reusable Sheet |

| See: | Nesting Logic 1 |
| --- | --- |
|  | Nesting Logic 2 |
|  | Initial Clamp Position |
|  | Part-Spacing/Nesting Border |
|  | Share to Size |

### 10.5.1 Automatic Material Selection

The options in the Automatic Material Selection section allow you to specify the material type, selection and sketch material priority.

| See: | Material Selection Priority |
| --- | --- |
|  | Selection Priority |
|  | Use Sketch Material for Non-Sketch Parts |
|  | Don’t nest parts inside skeleton area |

| See: | Reusable Sheet |
| --- | --- |

#### 10.5.1.1 Material Selection Priority

|  | The options in this section are used to specify the priority of three material types: Skeleton, Remnant and Standard. You can select the type of the material to be processed by placing a check mark in the corresponding check box. If all the material types are selected, you can click up and down arrows to adjust the priorities. |
| --- | --- |

Example:

| 1. | If you select all the material types and specify the priority order as follows: |
| --- | --- |
|  | The Standard sheet (3000x1000) will be used. |
| 2. | If you select all the material types and specify their priorities as follows: |
|  | The Skeleton sheet (3000x1000) will be used. |
| 3. | If you select all the material types and specify their priorities as follows: |
|  | The Remnant sheet (3000x840) will be used. |

Note:

Make sure that the material types exist in the Material Setting, and Auto (auto select material) in the Part Properties Advanced window has been selected.

| See: | Selection Priority |
| --- | --- |
|  | Use Sketch Material for Non-Sketch Parts |
|  | Don’t nest parts inside skeleton area |

#### 10.5.1.2 Selection Priority

This section is used to select sheet utilization.

| Option | Description |
| --- | --- |
| Best Sheet Utilization | If you select this option, the system will check all the materials to find the material of the best utilization. |
| Do Not Consider Utilization | If you select this option, the system will not consider utilization but to select material according to the material type priorities. |
| Exceed Minimum Utilization | If you select this option, the Minimum Utilization text box is enabled. Type a value in the text box to specify the minimum utilization. The system will select the material that exceeds the minimum utilization. |

| See: | Material Selection Priority |
| --- | --- |
|  | Use Sketch Material for Non-Sketch Parts |
|  | Don’t nest parts inside skeleton area |

#### 10.5.1.3 Use Sketch Material for Non-Sketch Parts

|  | If you select this option, the sketch material will be available for regular nesting of smaller non-sketch parts. The sketch material will be processed in the same method with the standard material. If you remove the check mark from the check box, the sketch material will only be available when you nest sketch parts. |
| --- | --- |

| See: | Material Selection Priority |
| --- | --- |
|  | Selection Priority |
|  | Don’t nest parts inside skeleton area |

#### 10.5.1.4 Don’t nest parts inside skeleton area

|  | If you select this option, the system won’t nest parts inside the skeleton area. If you remove the check mark from the check box, the system will nest parts inside the skeleton area if necessary. |
| --- | --- |

| See: | Material Selection Priority |
| --- | --- |
|  | Selection Priority |
|  | Use Sketch Material for Non-Sketch Parts |

### 10.5.2 Reusable Sheet

This section is used to specify the type of reusable sheet that the system will create after completing a nest job. You have the option of creating skeleton sheets or remnant sheets.

| Options | Description |
| --- | --- |
| None | If you select this option, no reusable sheet will be created. |
| Create Skeleton Sheet | If you select this option, skeleton sheet will be created if sheet utilization is less than the max utilization. See: How to Create a Skeleton Sheet. |
| Max Utilization | Specify maximum utilization of skeleton sheet. You can type a value in the text box or click the up and down arrow buttons to adjust the value. |
| Create Remnant | If you select this option, remnant sheet will be created. See: How to Create a Remnant Sheet. |
| Pitch | Define the incremental value for the remnant creation. For example, if the Pitch value is set to 20, Mini X Size is set to 100, the possible remnant X size will be 100, 120, 140, 160, etc. |
| Mini X Size | Specify the minimum X dimension of the remnant. |
| Mini Y Size | Specify the minimum Y dimension of the remnant. |
| End Value | Define the end value for remnant creation. M00 (Machine Stop), Wire Joint and Micro Joint are available. |
| Joint Quantity | Type a value to define the joint quantity. |
| Joint Value | Type a value to define the width of joint. |
| Process | This option is used for Combo machine only. When processing machine is Combo machine, you can select whether uses laser or punching process method to create the remnants. |
| Type | Specify the method to create the remnant. |
| Horizontal Cut | To create a remnant sheet in the X direction. |
| Vertical Cut | To create a remnant sheet in the Y direction. |
| T Cut | To create remnants in the X and Y direction both. |
| Rectangle Cut | To create remnants of rectangle shape. |
| Detailed Setting | Click the Detailed Setting button to open the Joint Setting window. You can make detailed setting for joints. See: Joint Setting window. |

| See: | How to Create a Skeleton Sheet |
| --- | --- |
|  | How to Create a Remnant Sheet |

| See: | Automatic Material Selection |
| --- | --- |

### 10.5.3 Joint Setting Window

In the Material Selection section, click Detailed Setting button to open the Joint Setting window. You can specify the Remnant Type, Tool Size, Joint Interval, etc.

| Option | Description |
| --- | --- |
| Remnant Type | Click to select how to cut the remnant. When a different item is selected a different graph will displays, allowing you to define the Material adjustment amount, Maximum Joint interval and Process Direction. Horizontal Cut Vertical Cut T Cut Rectangle Cut |
| Material adjustment amount | Type a value in the textbox to define the place to start creating the remnant. This value represents the distance from the process-starting place to the sheet edge. If you select Laser as the process method, a positive value means the machine will overcut the material, while a negative value indicates the machine will undercut the material. |
| Maximum Joint interval | Type a value in the textbox to define the maximum distance between joints, when multiple joints are placed. |
| Process Direction | Click the arrow button to define the processing direction. The selected arrow button will turn green. |
| Nesting Border | Specify the distance between the sheet edge and the remnant edge. |
| Nesting Border Set | Use the settings in the Part-Spacing/Nesting Border panel to specify the distance between the sheet edge and the remnant edge. See: Part-Spacing and Nesting Border |
| Value | Type a value to distance between the sheet edge and the remnant edge. |

### 10.5.4 How to Create Skeleton Sheet

| 1. | Select Create Skeleton Sheet under Reusable Sheet and define the Maximum Utilization as 50. |
| --- | --- |
| 2. | The sheet utilization is only 10.094%. |
| 3. | The system creates the skeleton sheet and stores it in the Material Manager after saving the NC data. |

| See: | Reusable Sheet |
| --- | --- |

### 10.5.5 How to Create a Remnant Sheet

| 1. | In the Reusable Sheet section, specify the settings as follows. |
| --- | --- |
| 2. | Click the Detailed Setting button, and specify the settings as follows. See: Joint Setting Window |
| 3. | The system will create the remnant in the X direction. |
| 4. | And the system will generate M00 in the NC code. |
| 5. | If you specify the settings in the Reusable Sheet section as follows: |
|  | The nesting result will be as follows: |
| 6. | If you specify the settings in the Reusable Sheet section as follows: |
|  | The nesting result will be as follows: |
| 7. | If you specify the settings in the Reusable Sheet section as follows: |
|  | The nesting result will be as follows: |

| See: | Reusable Sheet |
| --- | --- |

## 10.6 Share to Size

Click the Share to Size tab to activate the Share to Size panel. In this panel, you can set the tolerance for sketch material, select the sketch type and specify joint settings.

| See: | Sketch Material Tolerance |
| --- | --- |
|  | Sketch Type |
|  | Joint |

| See: | Nesting Logic 1 |
| --- | --- |
|  | Nesting Logic 2 |
|  | Initial Clamp Position |
|  | Part-Spacing/Nesting Border |
|  | Material Selection |

### 10.6.1 Sketch Material Tolerance

|  | This section is used to specify the sketch material tolerance. |
| --- | --- |

In the following illustration, the blue pattern represents the part, and the red pattern represents the sketch sheet.

| Text Box | Description |
| --- | --- |
| X | If the distance in X-axis between sketch material and the part is not within the tolerance range, the material will not be used for sketch nesting. |
| + | Specify the maximum tolerance value in the X- axis. |
| – | Specify the minimum tolerance value in the X -axis. |
| Y | If the distance in Y-axis between sketch material and the part is not within the tolerance range, the material will not be used for sketch nesting. |
| + | Specify the maximum tolerance value in the Y- axis. |
| – | Specify the minimum tolerance value in the Y -axis. |

Notes:

| 1. | If you want to use sketch material for nesting, make sure sketch material has been stored in the Material Manager if necessary, define the sketch material in the Material Manager. |
| --- | --- |
| 2. | Sketch Nesting should be selected in the Part Properties Advanced window. |

Example:

| 1. | The following part has the dimensions of 300 x 200. |
| --- | --- |
| 2. | If you specify all the tolerance to zero, no tolerance will be allowed for the sketch nesting. |
|  | Only the sketch material of that is exactly 300 x 200 can be used for nesting the part. |
| 3. | If you specify the following tolerance values: |
|  | The sketch material of 350 x 250 can be used for nesting the part. |
| 4. | If you specify the following tolerance values: |
|  | The material that is smaller than the part size will be used because a shortage of 0.5 is allowed in the X size. |

| See: | Sketch Type |
| --- | --- |
|  | Joint |

### 10.6.2 Sketch Type

The options in the Sketch Type section allow you to specify conditions to process the remainder of the sheet having a size that is very close to the part and, having a Y size that is within the tolerance range, and having an X size greater than part.

| Option | Description |
| --- | --- |
| The Material Whose X Sizes do not Correspond is Used | You must select this option to activate the options below. |
| Punch Out if Distance < = | If the distance between part and material is smaller than the value in this text box, the remainder will be punched out. |
| Shift to Center if Distance > = | If the distance between part and material is greater than the value in this text box, the part will be shifted to the center of material. |
| Shift if Element is Not Vertical | If the longitudinal line of part is not vertical, type value in the text box to define the shift distance. |

Example:

| 1. | Use a 500 x 400 sketch material to nest a 300x 300 part. Specify the tolerance as follows: |
| --- | --- |
| 2. | The result is as follows. |
| 3. | Select Shift to Center if Distance is > = and type 10 in the text box. |
| 4. | The result is as follows. |
| 5. | If the part contains lines that are not vertical, you can shift it by the value you set. |
| 6. | The result is as follows. |

| See: | Sketch Material Tolerance |
| --- | --- |
|  | Joint |

### 10.6.3 Joint

This section is used to define the placement of joints on the cutting line. You can only place joints on straight cutting lines.

| Option | Description |
| --- | --- |
| Joint Interval Max | Type value in the text box to define the maximum distance between joints, when multiple joints are placed. |
| Process Direction | Click or to define the processing direction. The selected arrow button will turn green. |
| Material Adjustment Amount | Type a value in the textbox to define the place to start creating the remnant. This value represents the distance from the process-starting place to the sheet edge. If you select Laser as the process method, a positive value means the machine will overcut the material, while a negative value indicates the machine will undercut the material. |

Example:

| 1. | Set the Maximum Joint Interval to 50 and the Material Adjustment Amount to 10. The result on the right indicates that the system did not overcut the material. 10 |
| --- | --- |
| 2. | Set the Maximum Joint Interval to 100 and the Material Adjustment Amount to 5. The result on the right shows the system lengthens the path and overcuts the material. |

| See: | Sketch Material Tolerance |
| --- | --- |
|  | Sketch Type |

# Chapter 11: Tool Assignment

These options in the Combination Tool Assignment window allow you to set the preference for tool assignment. You can specify the methods the system processes the parts, the detailed tool assignment conditions, etc.

To open the Combination Tool Assignment window:

| 1. | Click any Preference button in the Dr. ABE main window to display the Preference window. |
| --- | --- |
| 2. | In the Tree View, select the EM-L machine under My Preference. |
| 3. | Double-click the COMBI icon in the Preference File pane to display the Combination Tool Assignment window. |
|  | The Combination Tool Assignment window contains the following tabs. Main allows you to set preference for Laser Assignment, methods to process perimeters, corner notch and notch, etc. Calculation allows you to set punch conditions. Tooling Pattern allows you to specify the methods to process the holes based on the shape and size. |

| See: | Main |
| --- | --- |
|  | Detail Setting |
|  | Laser Assignment |
|  | Calculation |
|  | Tooling Pattern |
|  | Edit of Template |

## 11.1 Main

In the Main panel, you can specify the method to process the perimeters, corner notch, and notch. You can define the laser assignment conditions, set preferences for allowing different assignment on the same part.

| See: | Assign |
| --- | --- |
|  | Laser Pierce |
|  | Selection by Overview |
|  | Percentage of Laser and Punch |
| See: | Detail Setting |
|  | Laser Assignment |
|  | Calculation |
|  | Tooling Pattern |
|  | Edit of Template |

### 11.1.1 Assign

| Option | Description |
| --- | --- |
| Allow different Assignment on the Same part | Place a check mark in this check box and the system might use quite different tool assignment to process two same parts. |
| When Part is Rotated | Place a check mark in this check box and the system will rotate part in order to utilize sheet best, though different tool is to be assigned to the two same parts. |

| See: | Laser Pierce |
| --- | --- |
|  | Selection by Overview |
|  | Percentage of Laser and Punch |

### 11.1.2 Laser Pierce

|  | Place a check mark in the Punch Pierce check box, and the system will use a punch tool to pierce during the process. |
| --- | --- |

Set a tool as punch pierce tool

| 1. | In the SubInventory window, double-click the tool you want to use to perform punch pierce process. |
| --- | --- |
| 2. | In the Tool window, place a check mark in the Punch Pierce check box. |
| 3. | In the Combination Tool Assignment window, place a check mark in the Punch Pierce check box. And the system will consider using punch tool to perform pierce process during the process. |
| 4. | The following illustrations indicate a RO tool of 1.3 is used to perform pierce process. |

Notes:

- Theoretically, the system can perform punch pierce within the whole process range, See: Punching Process Range

- But for the tools installed in the outer track or inner track, their punching range is different. When the system perform punch pierce it will takes the OTX and OTY into account. If the punch pierce place is out of the punch tool process range, the system will use laser to pierce instead.

- If several tools are defined as the punch pierce tools, the tools assigned to the sheet have the higher priority, and among these tools the smallest tool is considered first.

Example

| 1. | A RO tool is added to Station 107, which is located in the inner track. And this RO tool is set to work as a punch pierce tool. See: Set a tool as punch pierce tool |
| --- | --- |
|  | Since the RO tool is located in the inner track, its process range will shift 40 along the Y- axis, the grey rectangle area stands for the original machine punch process range, while the blue rectangle represents the punch range of the RO tool in T107. |
| 2. | When the system perform piercing to process the following part, because the Y distance from pierce hole A to the sheet edge is 20, less than 40, the system will use laser to pierce this hole, while the Y distance from pierce hole B to the sheet edge is larger than 40, the system will use punch tool to pierce the hole. |
|  | The system punched pierce hole B The system cut pierce hole A |

| See: | Assign |
| --- | --- |
|  | Selection by Overview |
|  | Percentage of Laser and Punch |

### 11.1.3 Selection by Overview

Selection by Overview provides options allow you to specify the process method for perimeters, notch, and corner notch. You can click Detail Setting button or Laser Assignment button to set the detailed preferences.

| See: | Process the Perimeters |
| --- | --- |
|  | Process Corner Notch |
|  | Process Notch |
| See also: | Assign |
|  | Laser Pierce |
|  | Percentage of Laser and Punch |

#### 11.1.3.1 Process the Perimeters

You can specify the process methods to process the perimeters in the Selection by Overview section.

Example

| 1. | Let’s take the following part for example. |
| --- | --- |
| 2. | Select Laser option under All Perimeters. |
| 3. | In the Process After window, specify the conditions to cut the outer objects. See: Process After Cutting |
| 4. | The system will cut the perimeters as follows. |
| 5. | Select Punch option under All Perimeters. |
| 6. | In the Process After window, specify the conditions to punch the outer objects. |
| 7. | The system will cut the perimeters as follows. |
|  | Notes The settings in the Process After window have a higher priority than the settings of All Perimeters. Therefore if the preferences are not properly set for the punch process, the system will still cut the perimeters. You can select Laser and Punch at the same time, and the system will determine the perimeter process methods based on the corresponding settings in the Process After window. Corner Notch and Notch options won’t be active unless you have selected both Laser and Punch under All Perimeters. |

| See: | Process Corner Notch |
| --- | --- |
|  | Process Notch |

#### 11.1.3.2 Process Corner Notch

You can specify the process methods to process the corner notches in the Selection by Overview section.

Example

| 1. | Let’s take the following part for example. |
| --- | --- |
| 2. | Select Laser under Corner Notch. |
| 3. | Set the proper preferences in Process After Cutting Table of the Process After window. |
| 4. | The system will process the part as follows, and cut the two corner notches by laser. |
| 5. | If you select Punch under Corner Notch. |
| 6. | The system will process the part as follows, and punch the two corner notches. |
| 7. | If you select both Laser and Punch under Corner Notch. |
| 8. | The system will cut or punch the corner notches based on the relevant preferences set in somewhere else. Please refer to the following illustrations. |

| See: | Process the Perimeters |
| --- | --- |
|  | Process Notch |

#### 11.1.3.3 Process Notch

You can specify the process methods to process the notches in the Selection by Overview section.

Example

| 1. | Let’s take the following part for example. |
| --- | --- |
| 2. | Select Laser under Notch and then set the proper preferences in Process After Cutting Table of the Process After window. |
| 3. | The system will process the part as follows, and cut the notch by laser. |
| 4. | If you select Punch under Corner Notch. |
| 5. | The system will process the part as follows, and punch the notch. |
| 6. | If you select both Laser and Punch under Notch. |
| 7. | The system will cut or punch the corner notches based on the relevant preferences set in somewhere else. |

| See: | Process the Perimeters |
| --- | --- |
|  | Process Corner Notch |

### 11.1.4 Percentage of Laser and Punch

The options in this section are not available for this moment.

| See: | Assign |
| --- | --- |
|  | Laser Pierce |
|  | Selection by Overview |

## 11.2 Detail Setting

In the Main tab of Combination Tool Assignment window, click Detail Setting button to open the Detail Setting window, the options here allow you to specify the conditions for combination process.

| See: | Main |
| --- | --- |
|  | Laser Assignment |
|  | Calculation |
|  | Tooling Patterns |
|  | Edit of Template |

### 11.2.1 Laser/Punch-1 (Perimeter and Notch Setting for Combination Process)

In the Laser/Punch-1 panel, you can specify the combination process conditions for perimeter, notch, and corner notch.

| Option | Description |
| --- | --- |
| Perimeter | Specify the combination process for the perimeters. If the perimeter length is within Min and Max length range, and the punch hits in within the max hits specified, the system will punch the perimeters. If the conditions are not met, the system will cut the perimeters. |
|  | Note: This setting is only available for lines. |
|  | Length (A) | Specify the minimum and maximum length for outer perimeter. |
|  | Hits (Max) | Specify the maximum punch hits. |
| Notch and Corner Notch | The system will cut the notch if its width is less than the dimension defined in Length <: text box. If the notch dimension is large than the value defined, the system will punch the notch first. If the length is within Min and Max length range, and the punch hits exceed the max hits specified, the system will decompose the pattern into arcs and lines, and then decide the methods to process the elements based on the following conditions. |
|  | Length (A=L1+L2) | Specify the minimum and maximum length for the notch. |
|  | Hits (Max) | Specify the maximum punch hits. |

Example of Processing Perimeter

| 1. | Let’s take the following part for example. One line segment of the outer perimeter is 35. |
| --- | --- |
| 2. | Select both Laser and Punch under All Perimeter, and then click Detail Setting button to specify the conditions of Perimeter and Line (Angle=0 or Angle=90) as follows. |
|  | Since the system cannot find a tool to punch the line based on the above conditions, the system will cut this line segment instead |
| 3. | If specify the conditions Perimeter and Line (Angle=0 or Angle=90) as follows. The Max hit is set to 1, |
|  | If the system can punch the line segment with no more than 3 punch hits, the system will punch this line segment. |

Example of Processing Notches

| 1. | One notch of the following part is 50x80. Its total length is 180. |
| --- | --- |
| 2. | Select both Laser and Punch under All Perimeter, and then click Detail Setting button to open the Detail Setting window. Type 200 in the Length <: text box. |
| 3. | The system will cut this notch since it’s total length meets the conditions defined above. |
| 4. | If you type 150 in the Length <: text box, |
| 5. | Specify the notch conditions as follows. |
| 6. | If the system can punch the notch with no more than 3 punch hits, the system will punch this notch. |

| See: | Line and Arc Setting for Combination Process |
| --- | --- |

### 11.2.2 Laser/Punch-2 (Line and Arc Setting for Combination Process)

When dimension of pattern in part cannot fall within the setting in the Laser/Punch-1 panel, the pattern is divided into various lines or arcs. System will process these lines or arcs of the pattern according to settings in the Laser/Punch-2 panel.

Click Laser/Punch-2 tab to switch to the Laser/Punch–2 panel.

In Laser/Punch-2 panel, you can specify the combination process conditions for lines and arc. If the line or arc objects meet the conditions defined in this panel, the system will use punch to process. Otherwise laser will be used.

| Option | Description |
| --- | --- |
| Line (Angle=0 or Angle=90) | In this section, you can specify conditions for the vertical or horizontal line. |
| Line (Angle! =0 and Angle! =90) | In this section, you can specify conditions for the oblique line. |
| Arc (Process Outside R) | In this section, you can specify condition for the convex arc. |
| Arc (Process Inside R) | In this section, you can specify condition for the concave arc. |

Example

| 1. | Let’s take the following part for example. |
| --- | --- |
| 2. | If we specify the conditions of Arc (Process inside R) as follows |
| 3. | The system won’t use punch to process the arc. |
| 4. | Type 100 to specify the maximum punch hits. |
| 5. | If the system can punch the arc with no more than 100 punch hits, the system will punch this arc. |

| See: | Perimeter and Notch Settings for Combination Process |
| --- | --- |

| See: | Main |
| --- | --- |
|  | Laser Assignment |
|  | Calculation |
|  | Tooling Pattern |
|  | Edit of Template |

## 11.3 Laser Assignment

Click the Laser Assignment button to open the Laser Tool Assignment window. The options in the Laser Tool Assignment window allow you to specify the cutting parameters, such as the cutting direction, the lead-in/lead-out type, the process type after cutting and the cutting conditions on different paths.

| See: | Main |
| --- | --- |
|  | Detail Setting |
|  | Calculation |
|  | Tooling Pattern |
|  | Edit of Template |

### 11.3.1 Lead In/Out /Pierce Panel

The Lead In/Out /Pierce panel provides options to specify the conditions to assign the lead in, the lead out, the lead length, the lead type, pierce and tolerance to check the collision.

| See: | Lead In/Out Table |
| --- | --- |
|  | Collision Check Tolerance |
|  | Process Pierce First |
|  | The Custom Lead In/Out Definition Window |

| See: | Path Assignment Method |
| --- | --- |
|  | Tab/Corner Process |
|  | Detail Setting Window |

#### 11.3.1.1 Lead In/Out Table

The options in the Lead In/Out table allow you to specify the conditions to assign lead in/out, define the lead in/out type, lead length, as well as pierce type.

| Column Title | Description |
| --- | --- |
| Object | Specify the objects that the lead length settings will be applied to. There are five options: Outer, Inner, Open Path, Slit, All and Common Cut. If you select All, length settings will be applied to all the objects, including the open path, the outer loop, the inner loop, the slit and Common Cut. |
|  | Open Path As the following red patterns indicate, an open path does not create a closed shape. |
|  | Outer An outer loop is the contour or perimeter of a part as the following red pattern indicates. |
|  | Inner An inner loop is the contour or perimeter of a hole or pattern inside a part. |
|  | Common Cut Common cut is common line cutting. When the system uses common cut to process the part perimeters, defects can occur due to overheating. |
|  | Slit A slit is a cut on the outer loop. |
|  | All This option Includes all the open paths, outer loops and inner loops. |
| X/Y | This option Includes all the open paths, outer loops and inner loops. |
| EQ. | Specify the relation between X/Y and Value1/2. There are five options: <= (less than or equal to), >= (greater than or equal to), = (equal to), < (less than) and > (greater than). |
| Value 1/2 | Specify the reference dimension value. |
| Lead In | Specify the lead in length. |
| Lead Out | Specify the lead out length. |
|  | Note: The lead length is fixed for macro patterns. The length settings for the common lead type do not affect the macro. See Use Machine Macro Shape |
| Radius | Specify the radius of arc of the lead in/out. This column is only available when you have selected Distance Between Pierce Position and Part. |
| Over Cut | Specify over cut value of the lead in/out. |
| Offset | Specify the offset value of the lead in/out. |
| Position | Specify the location for the lead-ins/lead-outs. You can click the cell and select one option from the drop-down list. |
| Direction | Specify the direction to cut the specified pattern. You can click the cell and select one option from the drop-down list. |
| Lead In Out | Specify the lead-in/out types. You can specify three types of lead-in/out types and the leftmost one has the highest priority. |
|  | You can select More… to open the Custom Lead In/Out Definition window to modify the existing lead type or create a new one. See: The Custom Lead In/Out Definition Window |
| Pierce Type | The Pierce options allow you to specify the pierce type to process the geometry. There is three pierce types: Laser Pierce, Special Pierce, and None. |
| Laser Pierce | Select Laser Pierce from the Pierce: drop-down list to generate a M103 pierce in the NC code. |
| Special Pierce | Select Special Pierce from the Pierce: drop-down list to define the pierce parameters. The A Value, B Value and Cond (101-103) parameters become available. |
| Value A | Type a value (0 ~ 999) in the cell to specify an existing pierce type that has been configured for the machine. |
| Value B | Type a value (0 ~ 99999.9999) to specify the pierce range. |
| Condition (101-103) | Type 101, 102 or 103 to specify the special pierce to output in the NC code: E101, E102 or E103. |
|  | Example Select Special Pierce from the Pierce: drop-down list. Set the A value to 1, B Value to 2, and Cond (101-103) to 102. The system will output the following NC code. |
| None | If you select None from the Pierce: drop-down list, the system will generate a M103A0 and the system will not use any pierce processing. |

| See: | Collision Check Tolerance |
| --- | --- |
|  | Process Pierce First |
|  | The Custom Lead In/Out Definition Window |

#### 11.3.1.2 Collision Check Tolerance

Collisions may occur between the parts due to the lead length settings, and sometimes the lead-in/lead-out you specified may exceed the process range. You can specify the conditions to check the lead-in/lead-out collisions and the methods to resolve them. See: Collision Check

Type a value in the Collision Check Tolerance: text box to specify the check tolerance. This value defines the radius of the circle from the center of the pierce. In the following illustration, the dashed circle, measured from the radius, represents the collision check tolerance.

If any part is within the circle range of the pierce position, the system considers it a collision with the lead-in/lead-out and will use the settings in the Collision Check table to resolve the problem.

| See: | Lead In/Out Table |
| --- | --- |
|  | Process Pierce First |
|  | The Custom Lead In/Out Definition Window |

#### 11.3.1.3 Process Pierce First

When a thick sheet is used, the common cut process may cause defects. The Process Pierce First option can improve the quality by processing the pierce holes first.

If you place a check mark in the Process Pierce First check box, the system will perform the entire pierce processes first and then begin to process the part. See: Detail Settings for Processing Pierce First

| See: | Lead In/Out Table |
| --- | --- |
|  | Collision Check Tolerance |
|  | The Custom Lead In/Out Definition Window |

#### 11.3.1.4 The Custom Lead In/Out Definition Window

In the Lead In/Out table, you can click one cell in the Lead In Out column and select More … to open the Custom Lead In/Out Definition window.

The Custom Lead In/Out Definition window consists of three panels: On Line, Outside Corner and Inside Corner. You can select, create and modify the lead-in and lead-out types using the options in this window. You can define lead-in/lead-outs for lines and corners.

| See: | Creating a Lead-in or Lead-out Type |
| --- | --- |
|  | Editing a Lead-in or Lead-out |
|  | Deleting a Lead In or Lead Out |
|  | Applying a Lead In or Lead Out |

| See: | Lead In/Out Table |
| --- | --- |
|  | Collision Check Tolerance |
|  | Process Pierce First |

##### 11.3.1.4.1 Creating a Lead-in or Lead-out Type

| To create a lead-in/lead-out: |
| --- |
| 1. | Select More… from the Lead In Out: drop-down list to open the Custom Lead In/Out Definition window. The On Line panel is active. The picture within the red circle indicates the current lead-in/lead-out type. The picture in the blue rectangle is the Drawing Area. |
| 2. | Right-click the drawing area to open a shortcut menu. |
| 3. | Select New from the shortcut menu. |
| 4. | Select a drawing tool. There are three drawing tools: Straight Line, 180-Degree Arc and 90-Degree Arc. |
|  | Straight Line | 180-Degree Arc | 90-Degree Arc |
| 5. | Move the pointer into the drawing area to draw a straight line or arc. |
| 6. | Right-click to open the shortcut menu. |
| 7. | Select Finish the Path to complete the line or arc that you just drew. |
| 8. | Repeat Steps 4, 5, 6 and 7 to complete the remaining lead lines. |
| 9. | Click the Lead In button and then click a line to set it as the lead-in line or click the Lead Out button and then click a line to set it as the lead-out line. |
| 10. | Click or along the bottom of the Drawing Area to specify the direction of the lead-in or lead-out. |
| 11. | Click Save to save the design. The new Lead type that you created will display in the Lead list. |
|  | Notes: |
|  | The lead starting point varies with the lead-in/lead-out positions on the parts. If the lead-in/lead-out is On Line, the starting position will be placed near the arrow button: |
|  | If the lead-in/lead-out is Outside Corner, the starting position is as follows: |
|  | If the lead-in/lead-out is Inside Corner, the starting position is as follows: |

| See: | Editing a Lead-in or Lead-out |
| --- | --- |
|  | Deleting a Lead In or Lead Out |
|  | Applying a Lead In or Lead Out |

##### 11.3.1.4.2 Editing a Lead-in or Lead-out

| To edit a lead-in or lead-out: |
| --- |
| 1. | Select More… from the Lead In Out: drop-down list to open the Custom Lead In/Out Definition window. The On Line panel is active. (The picture within the red circle indicates the current lead-in/lead-out type. The picture in the blue rectangle is the Drawing Area.) |
| 2. | Select a lead-in/lead-out and the lead geometry will appear in the Drawing Area. |
| 3. | Click a lead line in the drawing area to select it. Right-click to open a shortcut menu. Select Delete from the shortcut menu. |
| 4. | The selected segment is deleted. |
| 5. | Select a drawing tool. Move the pointer into the Drawing Area and create a new segment. After drawing all the segments, right-click on the drawing area and select Finish the Path to compete the operation. |
| 6. | Click Lead In and then click a lead line to set it as the lead-in line. The remaining lead line will be defined as the lead-out line. You can also click the Lead Out button to define the lead-out. |
|  | Click or buttons to specify the direction. |
| 7. | You can rename the lead type or click Save to update it. |

| See: | Creating a Lead-in or Lead-out Type |
| --- | --- |
|  | Deleting a Lead In or Lead Out |
|  | Applying a Lead In or Lead Out |

##### 11.3.1.4.3 Deleting a Lead In or Lead Out

| To delete a lead-in or lead-out type: |
| --- |
| 1. | Select More… from the Lead In Out: drop-down list to open the Custom Lead In/Out Definition window. |
| 2. | Select a lead type and right-click to open the shortcut menu. |
| 3. | Select Delete from the shortcut menu. The selected lead type is deleted. |
|  | Notes: You can right-click one lead type in the Lead type list and select Set as Default and the select lead type will be displayed in the Lead In Out column. |

| See: | Creating a Lead-in or Lead-out Type |
| --- | --- |
|  | Editing a Lead-in or Lead-out |
|  | Applying a Lead In or Lead Out |

##### 11.3.1.4.4 Applying a Lead In or Lead Out

| To apply a lead-in or lead-out type: |
| --- |
| 1. | You can click one cell in the Lead In Out column and select one lead type from the drop- down list or select More… from the Lead In Out: drop-down list to open the Custom Lead In/Out Definition window. |
| 2. | Click the On Line, Outside Corner or Inside Corner tab to activate the desired panel. |
| 3. | Select an existing lead-in or lead-out along the top lead type list of the window. |
| 4. | Click OK. The Lead In Out column will update to reflect the selected lead-in/lead-out. |
| 5. | If you selected a lead-in/lead-out type in the On Line panel, the lead-in/lead-out will be as follows: |
| 6. | If you selected a lead-in/lead-out type in the Outside Corner panel, the lead-in/lead-out will be as follows: |
| 7. | If you selected a lead-in/lead-out type in the Inside Corner panel, the lead-in/lead-out will be as follows: |

| See: | Creating a Lead-in or Lead-out Type |
| --- | --- |
|  | Editing a Lead-in or Lead-out |
|  | Deleting a Lead In or Lead Out |

### 11.3.2 Path Assignment Method

The options in Path Assignment Method panel allow you to specify the process methods for various geometry types. You can specify the process methods for the open path, slit, unfold reference line, internal-tab bend line, bend line etching, pre-hole of extrusion/tapping, as well as the cutting conditions for the corner section of the rectangular tube.

| See: | Etch Layout |
| --- | --- |
|  | Open Path |
|  | Treat an Open Path as a Slit |
|  | Bend Line Etching |
|  | Unfold Reference Line |
|  | Internal-tab Bend Line |
|  | Use Machine Macro Shape |
|  | Pre-hole of Extrusion or Tapping |
|  | Points |
|  | Marking Setting |
|  | Cut Condition Table |
|  | Reference of Cutting Condition (Size/Shape) |
|  | Rectangle Tube |

| See: | Lead In/Out /Pierce Panel |
| --- | --- |
|  | Tab/Corner Process |
|  | Detail Setting Window |

#### 11.3.2.1 Etch Layout

Select this option to specify the layer of the geometry to be etched. You must define the layers that you want to etch during the part design phase before you can use this option.

| See: | Open Path |
| --- | --- |
|  | Treat an Open Path as a Slit |
|  | Bend Line Etching |
|  | Unfold Reference Line |
|  | Internal-tab Bend Line |
|  | Use Machine Macro Shape |
|  | Pre-hole of Extrusion or Tapping |
|  | Points |
|  | Marking Setting |
|  | Cut Condition Table |
|  | Reference of Cutting Condition (Size/Shape) |
|  | Rectangle Tube |

#### 11.3.2.2 Open Path

An open path consists of one or several grouped patterns that do not form a closed shape. The Open Path: drop-down list allows you to specify the processing method for open paths: Cutting, Etching or None.

| Examples: |
| --- |
|  | If you select Cutting from the Open Path: drop-down list, the system will cut all the open paths. |
|  | If you select Etching from the Open Path: drop-down list, the system will etch all the open paths. |
|  | If you select None from the Open Path: drop-down list, the system will ignore the paths and not process them. |

| See: | Etch Layout |
| --- | --- |
|  | Treat an Open Path as a Slit |
|  | Bend Line Etching |
|  | Unfold Reference Line |
|  | Internal-tab Bend Line |
|  | Use Machine Macro Shape |
|  | Pre-hole of Extrusion or Tapping |
|  | Points |
|  | Marking Setting |
|  | Cut Condition Table |
|  | Reference of Cutting Condition (Size/Shape) |
|  | Rectangle Tube |

#### 11.3.2.3 Treat an Open Path as a Slit

The Slit option is used to specify a processing range. Place a check mark in the Slit check box to activate the option, and then type a value in the Tolerance: text box to specify the slit value.

The system will check the slit within this range. If the shortest distance from the starting point/end point of the open path to the outer loop is within the tolerance, the open path will be treated as a slit. And the system will process the slit based on the settings in the Cut Condition Table.

Example

| 1. | The following patterns will be used to illustrate the difference between the open path and the slit. |
| --- | --- |
| 2. | If you remove the check mark from the Slit check box, all the inside elements will be considered as the open paths. |
| 3. | Select Line/ARC Length under Decision Method of lead Length in the Lead In & Pierce Details panel. And then specify the lead length as follows in the Lead In/Out Table. |
| 4. | The system will process the elements as follows. |
| 5. | The lead-in length of Open Path 1 is 3, and that of the lead-out is 2. However, the length of lead-in/lead-out for Open Path 2 and 3 has been shortened due to the collision check, and the warning messages display in the result view. Please refer to Collision Check Tolerance for details. |
| 6. | Place a check mark in the Slit check box, and type 5 in the Tolerance: text box. |
| 7. | If you specify a different lead-in/lead-out length for the open path and the slit. |
| 8. | The process result will be as follows. Open Path 1 is still considered as an open path. However, Open Path 2 and 3 are treated as slits, and are assigned the lead-ins/lead-outs of lengths different from those assigned to Open Path 1. |

| See: | Etch Layout |
| --- | --- |
|  | Open Path |
|  | Bend Line Etching |
|  | Unfold Reference Line |
|  | Internal-tab Bend Line |
|  | Use Machine Macro Shape |
|  | Pre-hole of Extrusion or Tapping |
|  | Points |
|  | Marking Setting |
|  | Cut Condition Table |
|  | Reference of Cutting Condition (Size/Shape) |
|  | Rectangle Tube |

#### 11.3.2.4 Bend Line Etching

The Bend Line Etching: drop-down list allows you to specify the conditions to etch the bend lines. You can select one method from the drop-down list to etch the bend lines.

Bend Line Etching Options

| Bend Line Etching (Up Only) | Specify the method to etch the bend up lines. |
| --- | --- |
| Bend Line Etching (Down Only) | Specify the method to etch the bend down lines. |
| Full | Select Full to fully etch the bend lines. |
|  | The following unfold drawing shows the system fully etches the bend up lines when you select Full from the Bend Line Etching (Up Only): drop-down list. |
| Dash | Select Dash to etch the bend lines with dashes. In the L1: text box, you can specify the distance from the part edge to where the etching begins. In the L2: text box, you can specify the length of the etching dashes. |
|  | The following unfold drawing shows the system etches the bend down lines with dashes when you select Dash from the Bend Line Etching (Down Only): drop-down list. |
| Cross | Select Cross to etch the bend lines in the cross shape. In the L1: text box, you can specify the distance from the part edge to the cross. In the L2: text box, you can specify the cross size. |
|  | The following unfold drawing shows the system etches the bend down/up lines in the cross shape when you select Cross from the Bend Line Etching (Down Only) and Bend Line Etching (Up Only): drop-down lists. |
| Cup | Select Cup to etch the bend lines in the cup shape. In the L1: text box, you can specify the distance from the part edge to the cup. In the L2: text box, you can specify the cup size. |
|  | The following unfold drawing shows the system etches the bend down/up lines in the cup shape when you select Cup from the Bend Line Etching (Down Only) and Bend Line Etching (Up Only): drop-down lists. |
| None | If you select None from the drop-down list, no process will be assigned to the bend lines. |
|  | The following unfold drawing shows no process is assigned to the bend lines when you select None from the Bend Line Etching (Down Only) and Bend Line Etching (Up Only): drop-down lists. |

| See: | Etch Layout |
| --- | --- |
|  | Open Path |
|  | Treat an Open Path as a Slit |
|  | Unfold Reference Line |
|  | Internal-tab Bend Line |
|  | Use Machine Macro Shape |
|  | Pre-hole of Extrusion or Tapping |
|  | Points |
|  | Marking Setting |
|  | Cut Condition Table |
|  | Reference of Cutting Condition (Size/Shape) |
|  | Rectangle Tube |

#### 11.3.2.5 Unfold Reference Line

The Unfold Reference Line option allows you to determine whether to assign the etching process to the reference line.

Examples

| 1. | If you select Etching from the Unfold Reference Line: drop-down list, the system will etch all the unfold reference lines on the parts. |
| --- | --- |
| 2. | If you select None from the Unfold Reference Line: drop-down list, the system will ignore all the reference lines and not process them. |

| See: | Etch Layout |
| --- | --- |
|  | Open Path |
|  | Treat an Open Path as a Slit |
|  | Bend Line Etching |
|  | Internal-tab Bend Line |
|  | Use Machine Macro Shape |
|  | Pre-hole of Extrusion or Tapping |
|  | Points |
|  | Marking Setting |
|  | Cut Condition Table |
|  | Reference of Cutting Condition (Size/Shape) |
|  | Rectangle Tube |

#### 11.3.2.6 Internal-tab Bend

The Internal-tab Bend Line option allows you to specify the methods to process Internal-tab Bend Lines.

Example

| 1. | We will process the following pattern with internal-tab bend lines. |
| --- | --- |
| 2. | Select Cutting from the Internal-tab Bend Line: drop-down list and the system will cut the Internal-tab bend line as follows. |

| See: | Etch Layout |
| --- | --- |
|  | Open Path |
|  | Treat an Open Path as a Slit |
|  | Bend Line Etching |
|  | Unfold Reference Line |
|  | Use Machine Macro Shape |
|  | Pre-hole of Extrusion or Tapping |
|  | Points |
|  | Marking Setting |
|  | Cut Condition Table |
|  | Reference of Cutting Condition (Size/Shape) |
|  | Rectangle Tube |

#### 11.3.2.7 Use Machine Macro Shape

The Use Machine Macro Shape option allows you to specify whether to use a macro command to process the pattern. The driver will output a high-level macro code for standard shapes.

Place a check mark in the Break Macro check box and then type a value in the Length > Width X: text box to break the macros with the specified condition.

Note:

You can only use this option for standard patterns that you draw in your CAD/CAM applications. This option is not available for grouped or combined shapes made up of separate elements.

Example

| 1. | We will process the following part, and the rectangle hole and obround hole are standard patterns drawn in CAD designing phrase. |
| --- | --- |
| 2. | Place a check mark in the User Machine Macro Shape check box. |
| 3. | The system will generate the G111 to instruct the machine to process rectangle hole and generate G112 to instruct the machine to process the obround hole. |
| 4. | Place a check mark in the Break Macro check box and type 2 in the Length > Width X: text box. If the length of the standard pattern is greater than 2 times of its width, this pattern will be broken into separate lines or arcs. |
| 5. | The rectangular hole doesn’t match the condition, and the system still generates G111 in the NC code. While the OB hole is broken into lines and arcs to process, because its length is greater than twice of its width. |

| See: | Etch Layout |
| --- | --- |
|  | Open Path |
|  | Treat an Open Path as a Slit |
|  | Bend Line Etching |
|  | Unfold Reference Line |
|  | Internal-tab Bend Line |
|  | Pre-hole of Extrusion or Tapping |
|  | Points |
|  | Marking Setting |
|  | Cut Condition Table |
|  | Reference of Cutting Condition (Size/Shape) |
|  | Rectangle Tube |

#### 11.3.2.8 Pre-hole of Extrusion or Tapping

The Pre-Hole of Extrusion or Tapping options allow you to specify how to process the pre-hole.

Pre-hole of Extrusion or Tapping Options

| Pre-hole of Extension or Tapping | Specify the method to process the pre-holes. |
| --- | --- |
| None | Pre-holes won’t be processed. |
| Process Hole | Select this option and the system will cut the pre-holes. |
| Center Mark | Select Center mark as the pre-hole process method. |
| Center Mark Up | Specify the method to process upward center mark. |
| Center Mark Down | Specify the method to process downward center mark. |
| None | Select this option and the system won’t process the pre-holes. |
| Etching Cross | Select this option and the system will etch a cross as follows. You can type a value in the text box to specify the cross size. |
| Etching Circle | Select this option and the system will etch a circle as follows. You can type a value in the text box to specify the circle size. |
| Etching Pierce | Select this option and the system will generate E010 to process the pre-hole. |
| Pierce | Select this option and the system will pierce the pre-holes. You can select a cutting condition from the drop-down list. |
| Macro (G118) | Select this option, and the system will generate G118 if you select Macro (G118) from the Center Mark: drop-down list. Make sure to specify a value in the Pierce No.: text box. The system will output the pierce cutting condition at the end of the G118 macro command line. |
| Etching Cup | Select this option and the system will etch the pre-hole in a cup shape. You can type a value in the text box to specify the cup size. |

| See: | Etch Layout |
| --- | --- |
|  | Open Path |
|  | Treat an Open Path as a Slit |
|  | Bend Line Etching |
|  | Unfold Reference Line |
|  | Internal-tab Bend Line |
|  | Use Machine Macro Shape |
|  | Points |
|  | Marking Setting |
|  | Cut Condition Table |
|  | Reference of Cutting Condition (Size/Shape) |
|  | Rectangle Tube |

#### 11.3.2.9 Points

Some parts contain points .You can control how to process those points by selecting the options in the Point: drop-down list.

Example

| 1. | If you select None from the Point: drop-down list, the system will not process the points. |
| --- | --- |
| 2. | If you select None+ Warning, the system will not process the points, but warning marks will appear on the points in the result view. |
| 3. | If you select Etching Cross, the system will etch the points in the cross shape. |
|  | Type a value in the Size: text box to define the size of the cross. The result will be as follows. |
| 4. | If you select Etching Circle, the system will etch the points in the circle shape. |
|  | Type a value in the Size: text box to define the size of the circle. The result will be as follows. |
| 5. | If you select Etching Pierce, the system will process the points by etching pierce. |
|  | And E010 will be generated in the NC code. |
| 6. | If Pierce is selected, the points will be pierced. |
|  | You can select one cutting condition from the drop-down list. |
| 7. | If Macro (G118) is selected, and the cutting condition is specified in the text box, the system will generate G118 and the cutting condition in the NC data. |

| See: | Etch Layout |
| --- | --- |
|  | Open Path |
|  | Treat an Open Path as a Slit |
|  | Bend Line Etching |
|  | Unfold Reference Line |
|  | Internal-tab Bend Line |
|  | Use Machine Macro Shape |
|  | Pre-hole of Extrusion or Tapping |
|  | Marking Setting |
|  | Cut Condition Table |
|  | Reference of Cutting Condition (Size/Shape) |
|  | Rectangle Tube |

#### 11.3.2.10 Marking Setting

|  | The options in this section allow you to define the method to process the marking made in the CAD design phase. There are three options: None, Etching and Etching [Count]. |
| --- | --- |

| Option | Description |
| --- | --- |
| None | If you select None from the Marking Setting: drop-down list, the marking strings will not be applied. |
| Etching | If you select Etching from the Marking Setting: drop-down list, the etching process will be used in the marking strings. |
| Etching [Count] | Select Etching [Count] from the Marking Setting: drop-down list to enable the Etching [Count] settings. See: Marking Setting for Etching [Count] |

| See: | Etch Layout |
| --- | --- |
|  | Open Path |
|  | Treat an Open Path as a Slit |
|  | Bend Line Etching |
|  | Unfold Reference Line |
|  | Internal-tab Bend Line |
|  | Use Machine Macro Shape |
|  | Pre-hole of Extrusion or Tapping |
|  | Points |
|  | Cut Condition Table |
|  | Reference of Cutting Condition (Size/Shape) |
|  | Rectangle Tube |

#### 11.3.2.11 Cut Condition Table

The options in the Cut Condition table allow you to define the cutting conditions to process the patterns.

| Column | Description |
| --- | --- |
| Object | The object the cutting condition will be assigned to. There are four types of objects: Outer, Inner, Open Path and All. See Object in Lead Length. |
| X/Y | Specify the dimension of the geometry. There are 6 options, and they are X, Y, Avg., Cpx., IA1, and IA2. |
| X | The overall horizontal dimension of the geometry. |
| Y | The overall vertical dimension of the geometry. |
| Avg. | Avg. refers to the average length of the individual patterns of the geometry. You can control whether the length of the line is used to calculate the average by using Exception to Averaging. |
| CPX | CPX is a quotient. The total perimeter length divided by the overall rectangular perimeter is Cpx. Value. The following example illustrates the Cpx. calculation formula: |
|  | Total Perimeter = 560 |
|  | Total Rectangular = 400 |
|  | 560/400 = 1.4 |
|  | Cpx. = 1.4 |
| IA1/2 | IA stands for Ignore Average. This option is used to define the cutting condition of lines that are not used in the average calculation. So it should be used in combination with Avg. |
| EQ. | Specify the relationship between X/Y column and Value1/2 column. There are five options: <= (less than or equal to), >= (greater than or equal to), = (equal to), < (less than) and > (greater than). |
| Value 1/2 | Specify the reference dimension value. |
| Cutting | The system assigns the cutting condition in this column to the patterns that match the conditions. The available cutting Conditions for Armada's machine are from E001 to E010. If you select Size/Shape, you can define the detailed cutting conditions for segments such as line, arc, RO and OB. See: Reference of Cutting Condition (Size/Shape) |

To define cutting conditions for different patterns

| 1. | This part has the following dimensions: |
| --- | --- |
| 2. | Specify the conditions as follows: |
| 3. | The inner loops match Condition 3. E004 is used to process the inner loops. |
| 4. | The outer loop matches Condition 1 and 2. Because Condition 1 has the higher priority, the system will process the outer loop by using E003. |

| See: | Etch Layout |
| --- | --- |
|  | Open Path |
|  | Treat an Open Path as a Slit |
|  | Bend Line Etching |
|  | Unfold Reference Line |
|  | Internal-tab Bend Line |
|  | Use Machine Macro Shape |
|  | Pre-hole of Extrusion or Tapping |
|  | Points |
|  | Marking Setting |
|  | Reference of Cutting Condition (Size/Shape) |
|  | Rectangle Tube |

#### 11.3.2.12 Reference of Cutting Condition (Size/Shape)

Specify which cutting conditions will be applied to the patterns that match the conditions when Size/Shape is selected in the Cutting column.

| Option | Descriptions |
| --- | --- |
| Detail Option | Select this option and the system will apply the cutting conditions specified in the Cut Condition of the Detail Setting window. |
| Machine Parameter | Select this option and the system will apply the cutting conditions specified in the Cutting Condition Detail window of the Machine Parameter. |

| See: | Etch Layout |
| --- | --- |
|  | Open Path |
|  | Treat an Open Path as a Slit |
|  | Bend Line Etching |
|  | Unfold Reference Line |
|  | Internal-tab Bend Line |
|  | Use Machine Macro Shape |
|  | Pre-hole of Extrusion or Tapping |
|  | Points |
|  | Marking Setting |
|  | Cut Condition Table |
|  | Rectangle Tube |

#### 11.3.2.13 Rectangle Tube

The options in the Rectangular tube section allow you to specify the cutting conditions when processing the corner section of the rectangular tube.

| Option | Description |
| --- | --- |
| Corner A/Y | Specify the cutting condition to process the following corner section if the laser head doesn’t move in the X-axis direction. |
| Corner A/X/Y | Specify the cutting condition to process the following corner section if the laser head move in the X-axis direction. |

| See: | Etch Layout |
| --- | --- |
|  | Open Path |
|  | Treat an Open Path as a Slit |
|  | Bend Line Etching |
|  | Unfold Reference Line |
|  | Internal-tab Bend Line |
|  | Use Machine Macro Shape |
|  | Pre-hole of Extrusion or Tapping |
|  | Points |
|  | Marking Setting |
|  | Cut Condition Table |
|  | Reference of Cutting Condition (Size/Shape) |

### 11.3.3 Tab/Corner Process

The options in this panel allow you to specify the length for micro joints, wire joints, and the length for lead in/out, etc.

You can also specify the conditions to process corners and perform the common line cutting.

| See: | Joint length and Lead-In/Out length |
| --- | --- |
|  | Nano Joint |
|  | Corner |
|  | Common Line Cutting |

#### 11.3.3.1 Joint length and Lead In/Out length

The options in this section allow you to specify the joint length and lead-in/out length.

| Option | Description |
| --- | --- |
| Micro | The Micro tab is actually a micro joint that placed in the corner of the pattern. Type a value in the Micro: text box to specify the tab length. |
|  | For example, if you type 0.5 in the Micro: text box, the system will assign the tab at the corner with the specified length. |
| Wire | A wire tab is a bridge micro joint on a line. Type a value in the Wire: text box to specify the tab length. |
|  | For example, if you type 0.5 in the Wire: text box, the system will assign the tab on a line with the specified length. |
| Lead In/Out Length for the Tab |  |
| Apply Customized Lead In/Out | The system will apply the settings defined in Lead In/Out table to the tabs. |
| Lead In/Out Length | The length of the lead-in/out will be determined by the settings specified in Lead In/Out table. |
| Original Length | The length of the lead-in/out will be determined by the value specified in the Lead In: text box and Lead Out: text box below. |
| Lead In | Type a value to specify the lead-in length. |
| Lead Out | Type a value to specify the lead-out length. |

Example

| 1. | In the Laser Tool Assignment window, click the Lead In/Out/Pierce tab and specify the lead type. See: Applying a Lead In or Lead Out |
| --- | --- |
| 2. | In the Lead In/Out table, specify in the Lead In and Lead Out column as follows. |
| 3. | Click the Detail button and select Line/Arc Length in the Decision Method of Lead Length section of the Lead In&Pierce Details panel. |
| 4. | Now go to the Tab/Corner Process panel, and select Lead In/Out Length. |
| 5. | The system will automatically use the default lead-in/out type during the process, but the lead length is determined by the value defined in the Lead Length table. |
| 6. | If you select Original Length and specify the Lead In and Lead Out length value as follows. |
|  | The system will use the default lead-in/out type, and the lead length will be as follows. |
| 7. | If you place a check mark in the Apply Customized Lead In/Out: check box and select Lead In/Out Length, |
|  | The system will apply the customized Lead In/Out setting to the tab. |
| 8. | If you place a check mark in the Apply Customized Lead In/Out: check box, select Original Length and specify the Lead In and Lead Out length as follows, |
|  | The system will apply the lead type that you have specified in the Lead In Out column, and apply the lead length as follows. |

#### 11.3.3.2 Nano Joint

This section is not available for combo machines.

#### 11.3.3.3 Corner

The options in the Corner section allow you to define processing methods for part corners.

The system will determine the output for each corner according to the angle settings.

| Column | Description |
| --- | --- |
| Object | There is only one option: Angle. |
| EQ. | Specify the relationship between Object and Angle. There are three options: <= (less than or equal to), < (less than) and = (equal to). |
| Angle | Specify the angle degree limit. |
| Type | Select and apply one corner processing method to the corner. There are 6 options: Loop, Triangle, Radius, Exact Stop, Dwell and None. See: Example |
| Value | Specify the length of the corner cutting type. |

Example

| 1. | Type 5 in the Value column to specify the corner cutting length. |
| --- | --- |
| 2. | If you select Loop from the Type: drop-down list, the system will perform the following process. |
| 3. | If you select Triangle from the Type: drop-down list, the system will perform the following process. |
| 4. | If you select Radius from the Type: drop-down list, the system will perform the following process. |
| 5. | If you select Exact Stop from the Type: drop-down list, when the first line of the corner is cut, the system will generate a G00 command line to perform in-position check. |
| 6. | If you select Dwell from the Type: drop-down list, and type a value in the Value column to specify the dwell time, when the first line of the corner is cut, the system will generate a G04 command line to instruct the machine to pause. |
| 7. | If you select None from the Type: drop-down list, the corner will not be processed in any special method. |

#### 11.3.3.4 Common Line Cutting

When the system uses common line cutting to process part perimeters, defects may occur due to overheating.

The options in the Common Line Cutting section allow you to specify the process method for crossroads to avoid overheating.

| Option | Description |
| --- | --- |
| Crossroad Change Cut Condition | Place a check mark in the check box to enable the processing methods to be applied for crossroads. |
| Entrance Cut Condition | Specify the entrance cut condition. |
| Length | Specify the length of the line segment for the entrance cut. |
| Exit Cut Condition | Specify the exit cut condition. |
| Length | Specify the length of the line segment for the exit cut. |

Example

| 1. | The following parts are used as an example. |
| --- | --- |
| 2. | Specify the following conditions in the Common Line Cutting section. |
| 3. | The system will process the parts as follows. |

### 11.3.4 Detail

In the Laser Tool Assignment window, click the Detail button to open the Detail Setting window.

In this window, you can specify Lead-in & Pierce Details, Cutting Condition, and Assignment Logic.

| See | Lead In& Pierce Details |
| --- | --- |
|  | Cutting Condition |
|  | Assignment Logic |

#### 11.3.4.1 Lead In& Pierce Details

The options in the Lead In & Pierce Details panel allow you to specify the conditions to decide the lead position and lead length.

You can also specify the settings for Processing Pierce First, Marking, and Collision Check.

| See | Decision Method of Lead Position |
| --- | --- |
|  | Decision Method of Lead Length |
|  | Detail Setting for Processing Pierce First |
|  | Marking Setting for Etching [Count] |
|  | Collision Check |

##### 11.3.4.1.1 Decision Method of Lead Position

|  | The options in the Decision Method of Lead Position section allow you to specify the positions for lead–ins/outs. |
| --- | --- |

| Option | Description |
| --- | --- |
| Relative to Part | Use part as the reference to determine the lead-in/out position. |
| Relative to Sheet | Use sheet as the reference to determine the lead-in/out position. |
|  | Example |
|  | If you select Center Top from the Position: drop-down list in the Lead In/Out Table, and select Relative to Part, the system will assign the lead in/out as follows. |
|  | Part is not rotated Part is rotated |
|  | If you select Relative to Sheet, the system will assign the lead in/out as follows. |
|  | Part is not rotated Part is rotated |
| Avoid Entity <= | This option allows you to place the lead-in/out in an optimized position according to the processing. If the length of line segment is less than or equal to the value that specified in the Avoid Entity: text box, the system will not place lead in/out on that pattern. Instead, the system will continue to check patterns in the cutting direction until a pattern that matches the condition is found. If none of the patterns match the condition, the system will not assign any lead-in/out. It will display an error message in the result view. |
|  | Example |
|  | The following part is used as an example. The system processes the part perimeter in the CCW direction. If you remove the check mark from the Avoid Entity: check box, the system will assign the lead-in/out according to the settings in the Lead In/Out table. If you place a check mark in the Avoid Entity: check box and type 50 in the Avoid Entity <=: text box, the system will check the line segments in the CCW direction and assign the lead-in/out to the element that matches the condition. If you type 160 in the Avoid Entity <=: text box, as none of the line segments match the condition, the system will not assign any lead-in/out. It will display an error message in the result view. |
| Fixed Lead Position for OB&SQ-REC | The options in this section allow you to specify the lead-in/out position for OB and RE patterns. You can choose to fix the lead position on the long side or on the short side of the pattern. See: Fix Lead Position for OB and SQ-REC Note: To enable this function, make sure Use Machine Macro Shape is enabled first. The system will break OB or RE pattern macro into lines and arcs during the process as indicated in the NC code. |
| Long Side | Fix the oblong and square-rectangle lead position on the long side. |
| Short Side | Fix the oblong and square-rectangle lead position on the short side. |
| At Notch | Place a check mark in the At Notch: check box, and you can select one option to decide when to assign lead in/out on the notch. |
| Priority to Notch | The system will assign the lead-in/out to the notch. |
| Avoid Notch | The system will not assign the lead-in/out to the notch. |
| Corner Offset | Place a check mark in the Corner Offset: check box to shift the lead-in away from the corner. Type a value in the text box to define the offset value. See: To Shift the Lead in/out away from the Corner |
| Corner Radius | If you place a check mark in the Corner Radius: check box, only lead-ins on the corner radius will be shifted. This option is available only if the lead-in type is a corner lead-in and the position selected is one of the corners. |

Fix Lead Position for OB and SQ-REC

If you assign the lead-in/out to the OB and select Long Side, the system will assign the lead-in/out to the OB as indicated in the following table.

The system applies the same logic to RE and SQ patterns.

| Long Side | 0 Degrees | 45 Degrees | 90 Degrees | 135 Degrees |
| --- | --- | --- | --- | --- |
| Center Top |  |  |  |  |
| Center Bottom |  |  |  |  |
| Top Left |  |  |  |  |
| (Top > Left) |  |  |  |  |
| Center Left |  |  |  |  |
| Bottom Left |  |  |  |  |
| (Bottom > Left) |  |  |  |  |
| Top Right |  |  |  |  |
| (Top > Right) |  |  |  |  |
| Center Right |  |  |  |  |
| Bottom Right |  |  |  |  |
| (Bottom > Right) |  |  |  |  |

When you select Short Side, the system will assign the lead in/out to the OB as indicated in the following table.

The system applies the same logic to RE and SQ patterns.

| Short Side | 0 Degrees | 45 Degrees | 90 Degrees | 135 Degrees |
| --- | --- | --- | --- | --- |
| Center Top |  |  |  |  |
| Center Bottom |  |  |  |  |
| Top Left |  |  |  |  |
| (Top > Left) |  |  |  |  |
| Center Left |  |  |  |  |
| Bottom Left |  |  |  |  |
| (Bottom > Left) |  |  |  |  |
| Top Right |  |  |  |  |
| (Top > Right) |  |  |  |  |
| Center Right |  |  |  |  |
| Bottom Right |  |  |  |  |
| (Bottom > Right) |  |  |  |  |

Example

| 1. | The following part is used as an example. |
| --- | --- |
| 2. | Select Top Left from the Position: drop-down list in the Lead In/Out table and select Relative to Part in the Decision Method of Lead Position section. |
| 3. | If you remove the check mark from the Fix Lead Position for OB&SQ-REC: check box, the system will assign a fixed lead-in position. |
| 4. | If you place a check mark in the Fix Lead Position for OB&SQ-REC: check box and select Long Side, the system will assign the lead-in/out as follows. |
| 5. | If you place a check mark in the Fix Lead Position for OB&SQ-REC: check box and select Short Side, the system will assign the lead-in/out as follows. |

To Shift the Lead in/out away from the Corner

| 1. | In the Lead In/Out table, select More… from the Lead In Out: drop-down list to open the Custom Lead In/Out Definition window. |
| --- | --- |
| 2. | Click the Outside Corner tab to open the Outside Corner panel. |
| 3. | Select a lead-in/out type. |
| 4. | Click OK to close the window. |
| 5. | Select Top Left from the Position: drop-down list to assign the lead-in/out to the corner. Select Relative to Part in the Decision Method of Lead Position section. |
| 6. | In the Decision Method of Lead Position section, remove the check mark from the Corner Offset check box. |
|  | The lead-in/out is assigned to the corner as the following pictures indicate. |
| 7. | Place a check mark in the Corner Offset: check box and define the offset value as 10. |
|  | The lead-in/out is assigned to the corner with the offset of 10. |
| 8. | Place check marks in both the Corner Offset and Corner Radius: check boxes and type 10 in the text box. |
|  | The lead in/out is assigned to the corner, and only the lead-in/out on the corner radius is shifted. |

##### 11.3.4.1.2 Decision Method of Lead Length

|  | Specify the methods to determine the lead in/out length. |
| --- | --- |

If you select Line/ARC Length, you must specify the conditions in the Lead In/Out table to define the length of lead-in/out.

The length is measured from the pierce point to the end of the lead line. In this case, the Radius column in the table is not available.

If you select Distance Between Pierce Position and Part, the length of the lead-in/out is the vertical distance between the pierce position and the part border.

You can specify the Radius value in the Lead In/Out table to define the arc radius when the Lead-in/out type contains arc.

Example 1

| 1. | Select Line/ARC Length. Set the length for the Lead In/Lead Out to 5 in the Lead In/Out table. |
| --- | --- |
| 2. | The result is as follows. |
| 3. | Select Distance Between Pierce Position and Part and keep the setting as is. |
| 4. | The result is as follows. |

##### 11.3.4.1.3 Detail Setting for Processing Pierce First

|  | Place a check mark in the Process Pierce First check box in the LeadIn/Out/Pierce panel to enable this section. The system will process all pierces first and then perform other processes. Note: If repositioning is performed, the system will first pierce all holes within the work range. |
| --- | --- |

| Option | Description |
| --- | --- |
| Value A | Place a check mark in the Value A: check box and type a value within 0~999 in the text box to specify an existing pierce type that has been configured for the machine. |
| Value B | Place a check mark in the Value B: check box and type a value within 0~99999.9999 in the text box to specify the pierce range. |
| Condition | Place a check mark in the Condition: check box and select an option (101, 102, or 103) from the drop-down list to specify the special pierce to be output in the NC code: E101, E102 or E103. |
| Machine Stop After Processing the Pierce First | Place a check mark in this check box to enable the system output M00 in the NC code indicating that the machine stops after processing the pierce. |
| NC Comment of End Command | You can type strings in the NC Comment of End Command: text box. The strings will be output with M00 in the NC data. |
|  | Note: You cannot use High-Speed Shutter Less Setting and Process Pierce First at the same time. |

Example

| 1. | Place a check mark in the Process Pierce First: check box. |
| --- | --- |
| 2. | Set Value A to 3. |
| 3. | The pierces are processed first (M103A3). M00 with the comment of "CLEANING" is generated. |

##### 11.3.4.1.4 Marking Setting for Etching [Count]

|  | In the Path Assignment Method panel, select Etching [count] from the Marking Setting: drop-down list to enable this section. The options allow you to etch the strings with a series of numbers according to the Judging Code, Count, Start No. and Fix Digits. |
| --- | --- |
| Option | Description |
| Judging Code | Specify the symbol that will be replaced with numbers. |
| Count | Define the relationship of the numbers. |
| Start No. | Define the start number. |
| Fix Digits | 4 digits will be fixed with no regard of the original number of strings. |

Example

| 1. | If None is selected from the Marking Setting: drop-down list, no marking process will occur. See: Marking Setting |
| --- | --- |
| 2. | If Etching is selected from the Marking Setting: drop-down list, the marking strings will be used in the etching process. |
| 3. | If Etching [count] is selected from the Marking: drop-down list, and if the Marking Setting section is specified in the following way, |
|  | The strings will be etched as follows. The “####” strings will be replaced by an incremental series of numbers. |
|  | The “####” string on the first part is replaced with “0000” |
|  | The “####” string on the last part (14th) is replaced with “0013” |

##### 11.3.4.1.5 Collision Check

Collisions may occur between two neighboring parts due to improper lead length.

Sometimes the specified lead-in/out may exceed the process range.

In the LeadIn/Out/Pierce panel, you can type a value in the Collision Check Tolerance: text box to specify the check tolerance.

This value defines the radius of the circle from the pierce center.

If any part is within the circle range of the pierce position, the system will consider it a collision with the lead-in/out, and will use the settings in the Collision Check table to solve the problem.

The Collision Check table allows you to specify the conditions to check lead-in/out collisions and specify the corresponding method to deal with it.

Select one option and click the   button to change the priority.

The condition on the top of the table has the highest priority.

| Option | Description |
| --- | --- |
| Change Lead Position | If a collision occurs, the system will change the lead-in/out position to avoid it. |
| Change Lead Angle (Changeable =) | If a collision occurs, the system will change the lead-in/out angle to avoid it. You can specify the maximum changeable angle in the Value column. |
| Change Lead Length (Minimum Length =) | If a collision occurs, the system will change the lead-in/out length to avoid it. You can specify the minimum changeable length in the Value column. |
| None | The system will ignore all collisions. |
|  | Note: In the Error Description column, you can select whether to display a warning message or error message in the result view for each collision. When No Display is selected, no warning or error message will be displayed. |

Example

| 1. | Several parts will be nested on a sheet. The lead-in/out length is set to 10 in the Lead In/Out table. Type 7 in the Collision Check Tolerance: check box. The Part Spacing is set to 5. Set None to the highest priority in the Collision Check table. |
| --- | --- |
|  | The system will ignore the collision(s). No changes are made to the lead-ins/outs. |
|  | However, the system will generate error messages. |
| 2. | If Change Lead Position is set to the highest priority, the system will change the lead-in/out position to avoid the collision. |
| 3. | If you set Change Lead Angle to the highest priority, and type 90 in the Value cell to define the maximum changeable degree of the lead angle, the system will change the angle of the lead-in/out. |
| 4. | If you set Change Lead Length to the highest priority, and type 1 in the Value cell to define the minimum changeable lead length, the lead length will be changed from 10 to 7. |

#### 11.3.4.2 Cutting Condition

The options in the Cutting Condition panel allow you to specify cutting conditions for individual patterns.

You can specify the conditions for lines/arcs and other macro shapes.

You can select Details Option under Reference of Cutting Condition (Size/Shape) and select Size/Shape from the Cutting: drop-down list in the Cutting Condition table to apply the settings.

See: Cutting Condition table and Reference of Cutting Condition (Size/Shape)

##### 11.3.4.2.1 Line/Arc

|  | The Size/Shape (Line/Arc) section allows you to specify the process methods for lines and arcs. In the ARC table, you can select whether to use arc length or arc radius to define the condition. Note: This function will not be used unless both Details Option under Reference of Cutting Condition (Size/Shape) and Size/Shape from the Cutting: drop-down list in the Cutting Condition table are selected. See: Cut Condition Table and Reference of Cutting Condition (Size/Shape) |
| --- | --- |

| Column | Description |
| --- | --- |
| EQ. | Specify the relationship between the Line/Arc and Value. There are five options: <= (less than or equal to), >= (greater than or equal to), = (equal to), < (less than) and > (greater than). |
| Value | Specify the reference dimension value. |
| Cutting | Assign the cutting condition (E001—E010) to the elements that match the condition. |

Example

| 1. | This part has the following dimensions. |
| --- | --- |
| 2. | Select Size/Shape from the Cutting: drop-down list in the Cut Condition Table. Select Details Option under Reference of Cutting Condition (Size/Shape) and then specify the settings as follows. |
| 3. | The lines match the condition set in the Line table, so E003 is used to process them. The round hole matches the condition set in the ARC table, so E004 is used to process it. |

##### 11.3.4.2.2 Macro Shape

The Size/Shape (Macro Shape) section allows you to specify the process methods for the macro patterns.

The system supports the following macro shapes: RO (Round), OB (Obround), SQ-REC (Square-Rectangle), SD/DD (Single D/Double D), ARC Slot and Polygon.

For each macro shape, you can select the dimension type to specify the cutting condition by clicking the button above the table.

| Column | Description |
| --- | --- |
| EQ. | Specify the relationship between the pattern dimension and Value. There are five options: <= (less than or equal to), >= (greater than or equal to), = (equal to), < (less than) and > (greater than). |
| Value | Specify the reference dimension value. |
| Cutting | Assign the cutting condition (E001—E010) to the patterns that match the condition. |

| Button | Description |
| --- | --- |
| RO | Round |
|  | Use diameter to specify the cutting condition for round patterns. |
|  | Use radius to specify the cutting condition for round patterns. |
| OB | Obround |
|  | Use length to specify the cutting condition for obround patterns. |
|  | Use width to specify the cutting condition for obround patterns. |
| Polygon | Regular polygon |
|  | Use circumcircle radius of the polygon to specify the cutting condition for polygon patterns. |
|  | Use inscribed circle radius of the polygon to specify the cutting condition for polygon patterns. |
| SQ-REC | Square-Rectangle |
|  | Use length to specify the cutting condition for square-rectangle patterns. |
|  | Use width to specify the cutting condition for square-rectangle patterns. |
| SD/DD | Single D and Double D |
|  | Use X-axis direction length to specify the cutting condition for SD/DD patterns. |
|  | Use Y-axis direction length to specify the cutting condition for SD/DD patterns. |
| ARC Slot | Arc Slot |
|  | Use arc length to specify the cutting condition for arc slot patterns. |
|  | Use arc width to specify the cutting condition for arc slot patterns. |

Example

| 1. | The following part is used as an example. |
| --- | --- |
| 2. | In the Path Assignment Method panel, place a check mark in the Use Machine Macro Shape: check box. The system will process the holes by macros. If you remove the check mark from the check box, the holes will be broken into lines and arcs. |
| 3. | Select Details Option under Reference of Cutting Condition (Size/Shape) and select Size/Shape from the Cutting: drop-down list in the Cutting Condition Table. |
| 4. | In the Cutting Condition panel, specify the conditions as follows. |
| 5. | The round hole matches the condition in the RO table, so the system will process it by E003. The obround hole matches the condition in the OB table, so the system will process it by E004. |

##### 11.3.4.2.3 Exception to Averaging

|  | If you select Avg. in the X/Y column of the Cut Condition Table, you can define whether to use the length of a line to calculate the average by typing value in the following text boxes. |
| --- | --- |

| Option | Description |
| --- | --- |
| IA1: Cutting > | Type a value in the IA1: Cutting >: text box to define the minimum value to be used to calculate the average. |
| IA2: Cutting < | Type a value in the IA2: Cutting <: text box to define the maximum value to be used to calculate the average. |

Example

| 1. | The part has the following dimensions. |
| --- | --- |
| 2. | In the Cut Condition Table, specify the conditions as follows. |
|  | And specify the Exception to Average as follows. |
| 3. | Since no value is specified for IA1, the Avg. value is calculated as follows: (100 + 100 + 100 + 35 + 35 + 30 + 5 +5)/8 = 51.25. Since the outer loop matches Cut Condition 1, the system will process the outer loop by E002. |
| 4. | If we change the setting in the Cut Condition Table as follows. |
|  | And type 6 in the IA1: Cutting >: text box. |
| 5. | The length of two line segments is 5, less than the value in the IA: Cutting >: text box. Therefore the segments will not be considered in the average calculation. The Avg. value will be calculated as follows: (100 + 100 + 100 + 35 + 35 + 30)/6 ≈ 66.67. E003 is used to process the two lines with the length of 5. E002 is used to process the remaining lines. |

#### 11.3.4.3 Assignment Logic

In this panel, you can specify the priority for tool assignment.

The item on the top of the list has the highest priority when the system performs the tool assignment process.

If you place a check mark in the Single Joint Position has high priority: check box, the single joint position will be considered first in the tool assignment process.

## 11.4 Calculation

The Calculation panel lists the basic assignment conditions. And you can click the Advance button to open Tool Assign Condition window and set the preferences for tool assignment.

| Option | Description |
| --- | --- |
| Nibbling Overlap | Specify the maximum and minimum tool overlap when nibbling is performed. |
| Protrude | Specify the maximum protrusion value when assigning tools to the notch. |
| Acute Angle Protrude | Specify the maximum protrusion value when assigning tools to slanted lines. |
| Tool Width | Specify the maximum and minimum size of the tools that will be used to process the perimeters. |
| Part Overlap | Specify the minimum and maximum protrusion value when assigning tools to process lines. |
| Punch Across Notch | Specify the maximum width of the notches that can be treated as lines for tool assignment |
| Micro Tab Width/ Wire Tab Width | Specify the joint amount. |
| Nibbling | When Nibbling is performed, specify the tool pitch or scallop height. The system will automatically calculate the pitch based on the scallop height. ※When the nibbling pitch is defined for a tool, the specified tool value will be applied. |
| Pitch | Specify the pitch. |
| Height | Specify the scallop height. |
| Auto | The system will automatically adjust the tool pitch or scallop height. |
| RE Tool Overlap | Specify the minimum overlap value when the several RE tools are assigned to a line. |
| SQ Tool Overlap | Specify the minimum overlap value when the several SQ tools are assigned to a line. |
| Ignore Trace Punching | Specify the size of the notches that will be punched out. |
| Min(W<=) | If the width is less than the specified value, the system will punch the notch. |
| L>WX | If length is larger than the specified times of the width, the system will punch the notch. |
| Tool Search | Specify the conditions to search tools. |
| Rotate Tool in Turret | The angle of the tools specified in the turret can be changed and tools can be used. |
| Inventory | Use all the tools registered in the tool inventory. |
| Only Single Hit | Only search the tool inventory for the single hit tool. |
| Assign |  |
| Allow Different Tool | Different tool assignments are allowed for the same part. |
| Only Part Rotate | When the same part is rotated and nested, different assignments are allowed. |
| Pressure Check | The options here allow you to decide whether to check pressure or not. If the tool is too big compared with the material thickness, the sheet will be possibly misshaped; if the tool is too small compared with the material thickness, the tool will be possibly damaged. So we need to check the pressure. |
| Check the maximum tool | Check the tool tonnage to decide whether the tool can be assigned to process the thick material. See Check the maximum tool |
| Check the minimum tool | Check the tool size to decide whether the tool can be assigned to process the thick material. If Either size X or size Y is less than the minimum tool size, this tool cannot be assigned. Minimum Tool Size= Material Thickness x Coefficient (The value you typed in the Tool Size/ Thickness>=: textbox) See Check the minimum tool |
| Tool Size/Mat-Thickness>= | Type a value in the text box to define the relations between the tool size and material thickness. For example, if you type 2 in the text box, the tools whose sizes are less than 2 times of the material thickness won’t be assigned. |

| See | Main |
| --- | --- |
|  | Tool Lap Value |
|  | Assignment |
|  | Joint |
|  | Contouring Assignment |
|  | Slit &V Notch |
|  | De-burring |
|  | Slot2&3 |

### 11.4.1 Main

Click Main tab in the Tool Assign Condition window to open Main panel. You can set preferences for line unification, assignment changing, turret generation, auto index, and pressure check.

| Option | Description |
| --- | --- |
| Unification | The options in the Unification section allow you to determine whether to process the two line segments as one. If you enable this option, the two lines that are separated by a notch, as indicated in the graphic to the left, will be considered as a single line by the system. See: Process multiple Line Segment as One Segment |
| Process Line Unification | Place a check mark in the check box to treat two line segments as one for the tool assignment. |
| Max Length | If the width of the notch is less than the Max Length specified here, the system will ignore it and continue to process the perimeter as a line |
| Process Inclined Line | Place a check mark in the check box to treat two inclined line segments as one for the tool assignment. |
| Assign |  |
| Assignment Change of the Same Part | Select this to change the assignment of the same part |
| When Part is Rotated | Select this to change assignment when part is rotated. |
| Search for Stock Tools | Select this option to search the tool inventory for suitable tools. See: Search for Stock Tools |
| Perimeter Process | Search for tools in the tool inventory to process the perimeter. |
| CR Tool | Search for RC tools in the tool inventory. |
| Slit | Search for tools in the tool inventory to process the slit. |
| Hole (Single Hit) | Search for tools in the tool inventory to single-hit the holes. |
| De-burring | Search for De-burring tools in the inventory. |
| Others | Search for tools in the tool inventory process other patterns. |
| The Internal Angle of Turret can be Changed | Select this option, and the system will change the angle of the tools in the stations to process the patterns if the tools are not fixed in the stations. See: Change the Tool Angle to Process |
| Perimeter Process | Change the tool angle to process the perimeters. |
| CR Tool | Change the tool angle of CR tools to process the patterns. |
| Slit | Change the tool angle to process the slits. |
| Hole (Single Hit) | Change the tool angle to single-hit the holes. |
| De-burring | Change the tool angle to de-bur the pattern. |
| Others | Change the tool angle to process other patterns. |
| Allow Die Change of Locked Station | Select this option and dies can be changed for the tools defined as Fixed in the turret. See: Change the Die Clearance of the Fixed Station |
| Select Tool from Turret by Priority | Select this option, and the tools installed in the turret will be assigned with higher priority. |
| Auto Index |  |
| Non AI Station is Used by Priority | If tools of the same size and shape are used at 0 degree or 90 degree, AI tools are used with higher priority. Select Non AI Station is Used by Priority, if the system uses two tools of the same size to process the parts at 0 degree and 90 degree, AI station won’t be used, and the system will add the two tools to the ordinary stations for the tool assignment. See: Non AI Station is used with higher Priority |
| Pressure Check | The options here allow you to decide whether to check pressure or not. If the tool is too big compared with the material thickness, the sheet will be possibly misshaped; if the tool is too small compared with the material thickness, the tool will be possibly damaged. So we need to check the pressure. |
| Check the maximum tool | Check the tool tonnage to decide whether the tool can be assigned to process the thick material. See Check the maximum tool |
| Check the minimum tool | Check the tool size to decide whether the tool can be assigned to process the thick material. If Either size X or size Y is less than the minimum tool size, this tool cannot be assigned. Minimum Tool Size= Material Thickness x Coefficient (The value you typed in the Tool Size/ Thickness>=: textbox) See Check the minimum tool |
| Tool Size/Material Thickness >= | Type a value in the text box to define the relations between the tool size and material thickness. For example, if you type 2 in the text box, the tools whose sizes are less than 2 times of the material thickness won’t be assigned. |

#### 11.4.1.1 Process multiple Line Segments as One Segment

| 1. | Let’s take the following part for example. |
| --- | --- |
| 2. | Remove the check mark from Process Line Unification check box, and the system will process this part as follows. Lines and notches are processed respectively. |
| 3. | Place a check mark in the Process Line Unification check box, and set the Max Length to 25, the system will treat two horizontal lines as one kind for tool assignment. It is the same with those two vertical lines. |
| 4. | Place a check mark in the Process Incline Line check box, the system will process the part as follows, two inclined lines will be treated as one for the tool assignment. |
| 5. | If you set the Max Length to 15, the system will process this part as follows. Only the two inclined lines are treated as one line for the tool assignment. |

#### 11.4.1.2 Search for Stock Tools

In the Turret Generation section, we can specify whether to search the tool inventory for the tool assignment.

Example

| 1. | Let’s take the following part for example. |
| --- | --- |
| 2. | Specify the Turret Generation conditions as follows. |
| 3. | The system will only search the turret for tools, since no CR tools are installed in the turret stations, the system will use a RO tool to process the corner radius. |
| 4. | Place a check mark in the CR Tool check box, and the system will search the tool inventory and use a CR tool to process the corner radius. |
| 5. | Lets’ take another part for example. |
| 6. | Specify the Turret Generation conditions as follows. |
| 7. | The system will only search the turret for tools, since there is no specific tool in the turret to process slit, the system will use a 10X2 RE tool to punch the slit and the inner hole. |
| 8. | Place a check mark in the Slit check box, and the system will search the tool inventory for the slit tools. The system will use a 10X2 RE tool to process the inner hole and a 5X2 RE tool to process the slit. |

#### 11.4.1.3 Change the Tool Angle to Process

Select The Internal Angle of Turret can be Changed option, and the system will change the angle of the tools in the stations to process the patterns if these tools are not fixed.

Example

| 1. | We will process the following 200x80 rectangle part. |
| --- | --- |
| 2. | There are two RE Tools in the stations, The process angle of the 110x6 RE tool is defined to 0 and 90, and its process angle in the turret is set to 90. See: Process Angle The process angle of the other 50x6 RE tool is defined to 90, and its process angle in the turret is set to 90. |
| 3. | In the Turret Generation section, specify the setting as follows. |
| 4. | The system will use the 50X6 RE tool to process the vertical lines, but the system will not process the horizontal lines because none of the available tools has the proper process angle. |
| 5. | Place a check mark in the Perimeter Process check box, |
| 6. | The system will change the process angle of the tools in the turret for the tool assignment. The system will assign the 110x6 RE tool to the horizontal lines. |

#### 11.4.1.4 Change the Die Clearance of the Fixed Station

Clearance is defined as the gap or space between the punch and die. The clearance has a major effect on the finished products, as well as tool wear. Material thickness, types of material and types of tools being used should be all considered in establishing proper clearance.

Different material requires different clearance for tool assignment. The tool assignment features check the die clearance before assigning each tool, and only the tools with the proper clearance will be assigned to process the corresponding material.  See: Clearance

Select Allow Die Change of Locked Station, and the system will change the die of the tools in the fixed stations during the tool assignment.

Example

| 1. | Let’s take an 80x80 part for example. Two kinds of material (SPC, A1050) will be used. Two kinds of material require different clearance for tool assignment. About the material clearance. See: Clearance |
| --- | --- |
| 2. | There are two RE tools in the fixed station. |
|  | The clearances for both RE tools are set to 0.2. See: Clearance |
| 3. | Allow Die Change of Locked Station is not selected. As a result, the RE tools can only be assigned to process the SPC material. No tools are assigned to the A1050 material. |
|  | The error message indicates the tool clearance doesn’t match the material clearance setting. |
| 4. | Allow Die Change of Locked Station is selected. The system will automatically change the die clearance for the tool assignment, As a result, the RE tools are assigned to process both the SPC and A1050 material. The tool clearance for SPC material is 0.2, while the tool clearance for A1050 material is changed to 0.3. |

#### 11.4.1.5 Non AI Station is used with higher Priority

If tools of the same size and shape are used at 0 degree and 90 degree respectively, AI tools are used with higher priority. Select Non AI Station is Used by Priority, AI station won’t be used, and the system will add the tools to the ordinary stations for the tool assignment.

Example:

| 1. | Let’s take a 200x100 part for example. The system will assign the following two RE tools to process the part. The process angles for both tools are set to 0 and 90. And both tools can be used as Auto Index tools. |
| --- | --- |
| 2. | If Non AI Station is used with higher Priority is selected, the system will add these tools to two ordinary stations for the tool assignment. |
| 3. | If Non AI Station is used with higher Priority is not selected, the system will put one RE tool to the AI station during the tool assignment. |

#### 11.4.1.6 Check the maximum tool

Pressure caused by tool = C*Thickness*Tensile/100 (Unit: KN)

C: the perimeter of the tool.

Thickness: the thickness of the material

Tensile: the tensile strength of the material

If the pressure caused by the tool is larger than the pressure that can be afforded by the machine, the system will not assign this tool.

| 1. | Let’s take the following part for example. |
| --- | --- |
| 2. | We use material of SPC type. The thickness is 3.5. |
| 3. | The Tensile Strength of SPC material is 32. |
| 4. | Clear the check box in the Check the maximum tool check box. |
| 5. | The system arranges a RE tool 110x6 to cut the two vertical lines. |
| 6. | Calculate the pressure of the too RE 110x6. The perimeter of the tool is 226. The thickness and tensile strength of the material is 3.5 and 32 respectively. So the pressure is: 232x3.5x32/100=259.84kn. This value is larger than the Available Value of the machine:200kn. So if you place a check mark in the Check the maximum tool check box, the system will not assign tool RE110x6. |
| 7. | Place a check mark in the Check the maximum tool check box. |
| 8. | The system will assign tool RE 705 to cut the two vertical lines. |

| See | Process multiple Line Segments as One Segment |
| --- | --- |
|  | Search for Stock Tools |
|  | Change the Tool Angle to Process |
|  | Change the Die Clearance of the Fixed Station |
|  | Non AI Station is used with higher Priority |
|  | Check the minimum tool |

#### 11.4.1.7 Check the minimum tool

Minimum Tool Size= Material Thickness x Coefficient (The value you typed in the Tool Size/ Thickness>=: textbox)

| 1. | Let’s take the following part as an example. |
| --- | --- |
| 2. | We use material of SPC type. The thickness is 3.5. |
| 3. | Clear the check box in the Check the minimum tool check box. |
| 4. | The system arranges a RE tool 70x5 an RE tool 50x5 to process the part. |
| 5. | Place a check mark in the Check the minimum tool check box and type 2 in the Tool Size>=Material Thickness X: text box. |
| 7. | According the formula, minimum tool size=3.5x2=7. The Y size of the two RE tools is smaller than the value, so the system will arrange another tool, RE 20x7, to process the part. |

### 11.4.2 Tool Lap Value

The options in the Tool Lap Value panel allow you to specify the minimum overlap value or length percentage of tools. The smaller value will be used as the minimum tool lap value. The system will only assign the tools that match the minimum overlap value or length percentage to process inner holes.

| Option | Description |
| --- | --- |
| Square |  |
| Minimum | Specify the minimum overlap value or length percentage of square tools. |
| Rectangle |  |
| Minimum | Specify the minimum overlap value or length percentage of rectangle tools. |
| Round Punch |  |
| Nibbling Lap Value | Specify the minimum overlap value or length percentage of RO tools for the nibbling process. |
| Punch Out Lap | Specify the minimum overlap value or length percentage of RO tools for the punch out process. |
| Etc… |  |
| Minimum | Specify the minimum overlap value or length percentage of tools other than square tools, rectangle tools, and RO tools. |
| Nibbling Pitch |  |
|  | Note: The setting in Nibbling Pitch section is not available if you define the pitch value for the tool in Attribute 1 panel. See: Special Pitch |
| Pitch | Specify the distance between tool hits when nibbling. |
|  | Note: The Pitch value should always be greater than the sheet thickness except Contouring tools and De-burring tools. |
| Scallop Height | The scallop height is the distance formed by the scallop of nibbling tools. For round tools, Scallop Height allows you to define the height of the scallop formed during nibbling. The smaller the value, the smaller the scallop. And system will automatically calculate the nibbling pitch. |
| Auto | Select this to activate Default MIN option and Default MAX option |
| Default MIN | Select this and input a value in the MIN DX: text box, the system will calculate the default minimum pitch value. |
| Default MAX | Select this and input a value in the MAX DX: text box, the system will calculate the default maximum pitch value. |
|  | MIN Pitch=Tool X Size*Input value% MAX Pitch=Tool X Size*Input value% As for tools of special shape, the longer side of the tool is tool X size. |

### 11.4.3 Assignment

It is not always possible for the system to assign tools that can exactly fit the part perimeters, holes or slits for the punching process. Sometimes protrusions occur after the parts are processed. The options in the Assignment panel allow you to define the protrusion conditions for the tool assignment.  In the condition table, you can select a cell and type a value to modify.  You can right-click any blank area to open a shortcut menu, and select Add to add a new blank row, or select Delete to remove the selected row from the condition table.

| Option | Description |
| --- | --- |
| Slit | Specify the conditions to punch the slits, and it can prevent the slit area from being extremely slim. See: Slit Tool Assignment |
| Length (B) | The depth range of slit area. |
| Minimum Width (A) | The minimum width between tools that process slot. |
| Protrusion Value 1 | Specify the Min/Max protrusion value for Perimeter B assignment, as well as the Min/Max width of the tools used to process the perimeters. See: Perimeter Tool Assignment |
| Length (B) | The range of the perimeter length. |
| Protrusion (A) | The range of the protrusion. |
| Width (C) | The width range of the tools to be assigned. |
| Perimeter Protrusion Value 2 (Angle=0 or 90) | Specify the notch depth (B) and the maximum protrusion value (A) to assign single hit tools to process the notch. Note: For notch tool assignment, the system will first search for a single tool to process the pattern, if no such a single tool matches the conditions, the system will assign tools to shear-proof the slit based on the Slit conditions, if no tools match the slit conditions, the system will process the patterns using a punch grid. See: Tool Assignment for the Vertical or Horizontal Notch |
| Length (B) | The range of the notch depth |
| Protrusion (A) Max | The maximum protrusion value |
| Perimeter Protrusion Value 3 (Angle! =0 or 90) | Specify the tool assignment line length (B) and the maximum protrusion value (A) to assign single hit tools to process the notch with an angle. Note: For inclined notch tool assignment, the system will first search for a single tool to process the pattern, if no such a single tool matches the conditions, the system will assign tools to shear-proof the slit based on the Slit conditions, if no tools match the slit conditions, the system will process the patterns using a punch grid. See: Tool Assignment for Slanted Notch |
| Length (B) | The range of the notch tool assignment length. |
| Protrusion (A) Max | The maximum protrusion value. |

| See: | Slit Tool Assignment |
| --- | --- |
|  | Perimeter Tool Assignment |
|  | Tool Assignment for the Vertical or Horizontal Notch |
|  | Tool Assignment for Slanted Notch |

#### 11.4.3.1 Slit Tool Assignment

| 1. | We will process the following part with a slit of 60x40. |
| --- | --- |
| 2. | In the Assignment tab of the Tool Assign Condition window, specify the Slit conditions as follows. |
| 3. | The system will assign a RE tool (20x5) to process the slit based on the Slit settings. |
| 4. | If you set the Minimum Width (A) to 60. |
|  | Since no tools match the conditions for the slit tool assignment, the system will use an SQ tool (10 x 10) to punch-grid the slit. |

#### 11.4.3.2 Perimeter Tool Assignment

| 1. | We will process the following part. |
| --- | --- |
| 2. | In the Assignment tab of the Tool Assign Condition window, specify the Protrusion Value 1 conditions as follows. |
| 3. | The system will assign the following tools to process the part. |
|  | The system assigns a RE tool (30x3) to process Perimeter 2, and assigns a RE tool (28x2.5) to process Perimeter 1, their protrusion value is as follows, larger than 2, less than 3. |
|  | For Perimeter 3, 4, 5, and 6, since none of their length matches the condition, the protrusion value is 0 for the tool assignment. |
| 4. | If we specify the Protrusion Value 1 settings as follows. |
| 5. | The system will assign the following tools to process the part. |
|  | The system assigns a RE tool (30x3) to process Perimeter 2, and assigns a RE tool (28x2.5) to process Perimeter 1, their protrusion value is as follows, larger than 2, less than 3. |
|  | And the system assigns a RE tool (110x6) to process Perimeter 3, and assigns a RE tool (70x5) to process Perimeter 4, their protrusion value is as follows, larger than 5, less than 6. |
| 6. | If we specify the Protrusion Value 1 settings as follows. Change the Minimum Width to 3. |
| 7. | The system will assign the following tools to process the part. The RE tool (28x2.5) is replaced with a RE tool (28 x3.5). |

#### 11.4.3.3 Tool Assignment for the Vertical or Horizontal Notch

| 1. | We will process the following part. |
| --- | --- |
| 2. | If we specify the Perimeter Protrusion Value 2 (Angle=0 or 90) settings as follows. |
|  | The system will assign the following tools to process the part. A RE tool (30x10) is assigned to single-hit the notch. The protrusion value is 2. |
| 3. | If we set the Protrusion (A) Max to 1, |
|  | Since no tools match the settings defined in the Slit and Perimeter Protrusion Value 2 (Angle=0 or 90) table, the system will use a SQ tool (10x100) to punch-grid the notch. |

#### 11.4.3.4 Tool Assignment for Slanted Notch

| 1. | We will process the following part. |
| --- | --- |
| 2. | If we specify the Perimeter Protrusion Value 3 (Angle! =0 or 90) settings as follows. |
|  | The system will assign the following tools to process the part. A RE tool (20x5) is assigned to single-hit the notch. The protrusion value is 5.657. |
| 3. | However, if we specify the Perimeter Protrusion Value 3 (Angle! =0 or 90) settings as follows. |
|  | The system will ignore the conditions in this table, and process the slit by using the conditions defined in the Slit table. |

### 11.4.4 Joint

The options in the Joint tab of the Tool Assign Condition window allow you to specify the joint width and set conditions to assign special tools to create joints.

| Option | Description |
| --- | --- |
| Joint | Specify the width of micro joint and wire joints. |
| Width of Micro Joint | The width of the micro joints. |
| Width of Mire Joint | The width of the wire joints. |
| Special Tool |  |
| Assign Special Tool for Joint | Place a check mark in the check box to create joints with special tools. See: Use Special Tool to Create Joints |
| Only for Wire Joint | Only assign tools to create wire joints, not to create micro joints. |
| One Side | If you select this option, only one side of the special tool could be used to create joints. When One Side is selected, four angles, 0, 90, 180 and 270 degrees, are available. |
| Two Sides | If you select this option, two sides of the special tool could be used to create joints. When Two Sides is selected, only 0-degree and 90-degree angles are available. |
| Width of Micro Joint | The width of the micro joints. |
| Width of Mire Joint | The width of the wire joints. |
| Management Name | The name of the special tool used to create joints. You can type the tool name in the cell directly. It must be consistent with the name of the special tool you have registered in the tool inventory. |
| Process Angle | The angle of the special tool for punching process. |
| Length (A) | The distance between the center point and the left-most point of the tool. |
| Length (B) | The distance between the center point and the right-most point of the tool. |
| Length (C) | The distance between the center point and the uppermost point of the tool. |
| Length (D) | The distance between the center point and the lowest edge of the tool. |
| Lap (%) | The overlap percentage. The system will determine the overlap value using this formula: Overlap= Lap (%) x Tool Total Length |
| Use Auto Index | Place a check mark in the check box to place joints tools in the AI stations. Note: If you have specified two special tools or more, and select Use Auto Index, only one special tool (The default tool angle is 0) will be assigned to create joints. |

| See: | Use Special Tool to Create Joints |
| --- | --- |

#### 11.4.4.1 Use Special Tool to Create Joints

| 1. | We will use the following special tool to create joints. |
| --- | --- |
| 2. | If we specify the Special Tool settings as follows. The process angle of the SP tool is set to 0 degree. |
| 3. | The system will assign this SP tool to create joints as follows. |
|  | If we set the process angle of the SP tool to 90 degrees. |
|  | The system will assign this SP tool to create joints as follows. |
| 4. | If you place a check mark in the Use Auto Index check box, |
|  | The system will add the SP tool to the AI station and create joints as follows. |

### 11.4.5 Contouring Assignment

Contouring Assignment provides options to specify the conditions to assign contouring tools to process the line, Arc Inside, and Arc Outside.

| Option | Description |
| --- | --- |
| Assign Tools to the Pattern Specified | This function is not available now. |
| Assign to the Line | Assign contouring tools to the line. You can specify the length range for contouring tool assignment. |
| Only Assigned to the Slanted Line | Only assign contouring tools to the slant line |
| Display Warning Message | When contouring tools are assigned, warning message appears in result view. |
| Assign to Arc Inside | Assign contouring tools to process the inside of the arc. You can specify the length and radius range for contouring tool assignment. |
| Display Warning Message | When contouring tools are assigned, warning message appears in result view. |
| Assign to Arc Outside | Assign contouring tools to process the outside of the arc. |
| Display Warning Message | When contouring tools are assigned, warning message appears in result view. |

Example

| 1. | We will process the following part. |
| --- | --- |
| 2. | A 3x3 RO tool is used as the contouring tool. |
| 3. | Specify the Contouring Assignment settings as follows. |
| 4. | The system will assign the 3x3 RO contouring tool to process the slanted line and two arcs. |

### 11.4.6 Slit & V Notch

The options in the Slit & V Notch tab allow you to specify the conditions for slit and V notch tool assignment.

| Option | Description |
| --- | --- |
| Slit |  |
| Use Tolerance | Place a check mark in the check box to enable this section. The system will assign tools to process slit by considering tolerance. |
| Part-Spacing of Slit Process W <= | You can type a value in the text box to specify the maximum width of the slit that the tolerance setting will be applied. If the notch width is less than the maximum width you have specified, the system will assign tools that meet the tolerance range to process the slit. |
| Tolerance | Specify the tolerance for slit tool assignment. |
| Assign Pattern | Select tool assignment method. |
|  | The system will assign the tool to process the slit as is indicated in the left picture. The center of the tool and the center of the slit have the same X coordinate. |
|  | The system will assign the tool to process one side of the longer perimeter segment of the slit as is indicated in the left picture. |
|  | The system will assign the tool to process one side of the shorter perimeter segment of the slit as is indicated in the left picture. |
| Tool Select | Select to use RO, RE or SQ tool to process the slit. |
| V Notch |  |
| Assign V Notch Portion | Place a check mark in the check box to enable this section. |
| Assign Pattern | Select tool assignment method. |
|  | The system will assign tools to process the V notch as follows. |
|  | The system will make the tool center point correspond to the V notch pointy portion. |
|  | Select RO tool, the system will assign tools to process the V notch as follows. |
|  | Select RE&SQ tool, the system will assign tools to process the V notch as follows. |
|  | Select this option and the system will make the tool bottom edge correspond to the V notch pointy portion. |
|  | Select RO tool, the system will assign tools to process the V notch as follows. |
|  | Select RE&SQ tool, the system will assign tools to process the V notch as follows. |
| Tool Select | Select to use RO, RE or SQ tool to process the V notch. Specify the maximum size of the tools to be used. |
| RO | Select RO tool to process the V notch |
| X Size <= | Type value in the X Size <=: text box to specify the maximum diameter of the RO tools that can be assigned. |
| Extend Assign | Place a check mark in the check box and type a value in the Extend Assign: text box to specify the range in which the system can assign nibbling process with RO tool. |
| RE&SQ | Select RE&SQ tool to process the V notch |
| X Size <= | Type value in the X Size <= and Y Size <=: text boxes to specify the maximum X/Y dimensions of the RE or SQ tools that can be assigned. |
| Y Size <= |  |

| See | Process the Slit |
| --- | --- |

#### 11.4.6.1 Process the Slit

| 1. | There is a part with a slit. The slit width is 1. Tolerance is set to 1.5. Make the settings as follows to allow tolerance when processing the slit. |
| --- | --- |
| 2. | Select RO tool to process slit. |
| 3. | A RO 2.2 is used to process the slit. The system will use different processing mode according to your selection. |
| 4. | Select RE& SQ tool to process the slit. |

### 11.4.7 De-burring

The options in the De-burring tab of the Tool Assign Condition window allow you to specify the conditions for de-burring tool assignment.

| Option | Description |
| --- | --- |
| De-burring |  |
| Enable Deburring Tool Processing During Outer Shape Processing | Place a check mark in the check box and then the system will assign de-burring tool to process the outer shape of the part. |
| Imbalanced Processing | Place a check mark in the check box to enable imbalanced processing. |
| Enable Deburring Tool Processing During Hole Processing | Place a check mark in the check box and then the system will assign de-burring tool to process the hole of the part. |
| Imbalanced Processing | Place a check mark in the check box to enable imbalanced processing. |
| Disable Deburring when size | Place a check mark in the check box and type a value in the X<=: text box and Y<=: text box, the system will not assign De-burring tool to process hole whose X dimension or Y dimension is equal to or smaller than the value. |
| Wire joint compensation amount | Place a check mark in the check box and type a value in the text box to specify the compensation value of wire joint. |
| Micro joint compensation amount | Place a check mark in the check box and type a value in the text box to specify the compensation value of micro joint. |
| It Is Allowed To Assign Tool At Straight Line Portion De-burring-Round | Place a check mark in the check box and the system will use RO de-burring tool to process straight line. |
|  | SQ Deburring Tool | RO Deburring Tool |
|  | If you place the check mark, the result is the following |
| Only Diagonal Line Is Allowed | Place a check mark in the check box and the system will use RO de-burring tool to process only inclined line. |
|  | If you place the check mark, the result is the following |
| Perform The Fixed Process Sequence To Joint G90 and De-burring | Normally, the process sequence of Joint and Deburring process is the following: Joint G90 -> De-burring. But if you place a check mark in the check box, the system will perform the fixed process sequence to Joint G90 and Deburring. The process sequence is: De-burring -> Joint G90 |

Note:

To enable this function, you should make corresponding setting in Parts Properties.  Place a check mark in the De-Burring ON/OFF check box.

### 11.4.8 Slot2&3

The options in the Slot2&3 tab of the Tool Assign Condition window allow you to specify the conditions to assign slot tool.

SLOT2&3 tool is delicate, and it can be easily broken due to various reasons such as processing direction and lap amount of each tool path. Hence, it is necessary to assign tools o that tools ill not be broken in case of performing assignment automatically.

| Option | Description |
| --- | --- |
| Slot2&3 |  |
| Use slot tool at the time of skip-process on outer shape | Place a check mark in the check mark in the check box and you can make detailed settings for using slot tool at the time of skip-process on outer shape. |
|  | Slot tool can be only used to process the outer perimeter of the part. Holes and slots are not the targets. Line that has already had assignment is not a target. In the picture below, red lines represent lines assigned with slot tools. |
| Minimum Assigned Element Length | Type a value in the text box to specify the minimum length. If the line length is smaller than the value, the system will not assign slot tool to process it. |
| Stating/Ending Point Overlap Amount | Type a value in the text box to specify the overlap amount of starting /ending point. The minimum value is 0.001mm and the maximum value is 99.999mm. |
|  | The overlap value is 0.0001mm | The overlap value is 8mm |

Note:

To assign slot tools, you should make corresponding settings in Parts Properties. Place a check mark in the [SLOT AUTO ON/OFF] check box.

## 11.5 Tooling Pattern

The Tooling Pattern panel provides options to specify the conditions to process holes based on the shape and size.

The Tolerance options allow you to specify whether to apply tolerance settings to tool assignment.

If tolerance setting is applied, select Value option and specify the tolerance range for the tool assignment.

Place a check mark in the check box before the Advance button to activate advanced function. So you can click Advance button to open the Shape Condition window to specify the detailed settings based on shape and size. The Shape Condition window consists of two panels:  Tool Style and Match To Line.

You can also remove the check mark and click the shape to specify the tool assignment priority for the specified template.

| See: | Simple Tool Assignment Setting for the Specified Template |
| --- | --- |
|  | Fit Tool Style Panel |
|  | Match To Line |
| See: | Main |
|  | Detail Setting |
|  | Laser Assignment |
|  | Calculation |
|  | Edit of Template |

### 11.5.1 Simple Tool Assignment Setting for the Specified Template

In the Tool Pattern panel, we can specify the tool assignment priority based on the template shape.

This panel lists seven system template patterns, and they are RO, RE, RR, OB, DD, SD and Irregular Hole. As the following picture indicates, for the irregular hole tool assignment, the method of punching out the pattern has the highest priority, while for the rest 6 patterns, single-hit will be first considered for the tool assignment.

To set the tool assignment priority based on the shape:

| 1. | Remove the check mark from the check box before Advance, and click a pattern to open the Pattern List window. For example, if you click the RO pattern, The Pattern List will display all the tool assignments for the round hole. Different patterns represent different tool assignments. For example, represents single-hit tool assignment. |
| --- | --- |
| 2. | In the Pattern List window, select one pattern, and click button to change the position, the pattern on the top left corner of the list indicates the corresponding tool assignment has the highest priority. As the following window shows, RO tool B assignment has the highest priority for the round hole process. |
| 3. | Click to save the settings and return to the Tooling Pattern panel. |
| 4. | The patterns in the Tool Pattern update, as we can see, the RO pattern has changed, showing that RO tool B assignment has the highest priority for the round hole process. |

### 11.5.2 Fit Tool Style Panel

The Fit Tool Style panel provides options to set the preference for the tool assignment based on the shape and size. You can select one pattern and specify the tooling methods based on the sizes. You can also create new template patterns to meet your own needs if necessary.

| Panel Area | Description |
| --- | --- |
| Hole Pattern List | Display the information registers in the standard system pattern and templates. |
| The Info. of the Pattern Being Selected | Display the information of the template pattern being selected. Such as Name, Comment, Type, and Dimensions. This section displays the template dimensions. There are usually two dimensions: X and Y, but some special templates have a R dimension, such as RR and CR. |
| Assignment Pattern List | Display candidate patterns with tools assigned. |
| Edit Template | Create and modify the template pattern. See Edit Of Template |
| Detail Setting | Set pattern size and define the tool assignment condition. The higher ID level is, the higher the priority will be. The system will apply the conditions from top to bottom. |
| Priority Pattern ID Level | Specify the tool assignment priorities. |

| See: | Hole Pattern List |
| --- | --- |
|  | Pattern Information and Assignment Pattern List |
|  | Template Detail Settings |

| See: | Simple Tool Assignment Setting for the Specified Template |
| --- | --- |
|  | Match To Line |

#### 11.5.2.1 Hole Pattern List

The Hole Pattern List shows all the available templates. You can click the downward button to open drop-down list and select the pattern type to display.

| Drop-down List Item | Description |
| --- | --- |
| All | Display all the templates. |
| System | Only display the system templates. |
| Hole | Only display the hole templates. |
| Notch | Only display the notch templates. |
| Corner Notch | Only display the corner notch templates. |

Right-click the Template list area to open a shortcut menu. The options on this shortcut menu allow you to add, delete, insert or edit the system template data.

| Shortcut Option | Description |
| --- | --- |
| Add of Template Data | When the pattern you need doesn’t exist in the pattern list, you can select Add of Template Data to append data to the bottom of the list. |
| Delete of Template Data | Delete the selected template. |
| Insert of Template Data | Select Insert of Template Data to insert a pattern before the selected row. |
| Edit of Template Data | When there are not enough patterns with tools assigned, you can select Edit of Template to modify the template selected. Notes: The template of system type cannot be edited. |

| See: | Pattern Information and Assignment Pattern List |
| --- | --- |
|  | Template Detail Settings |

#### 11.5.2.2 Pattern Information and Assignment Pattern List

As you select different template in the left Hole Pattern List, the right Assignment Pattern List will display all the relevant tool assignment methods for specified template.

| See: | Hole Pattern List |
| --- | --- |
|  | Template Detail Settings |

#### 11.5.2.3 Template Detail Settings

In the Detail Setting section, you can specify the conditions for the tool assignment of the selected template.

| Column | Description |
| --- | --- |
| Symbol | The dimensions of the template. Click Symbol cell to open a drop-down list and there are seven options in the drop-down list. |
|  | Note: |
|  | These options vary with templates. For a RE, OB, SD, DD and Irregular Hole templates of system type, you can set the dimension conditions for X and Y values; For a RR template, you can set dimension conditions for X, Y and R values. While for a RO template, you can only specify the X dimension conditions. A, B, C and D values are available for template other than System type. |
| Eq. | Specify the relationship between the shapes to be processed with the dimension value you typed in Value cells. There are six options: < (less than), <= (less than or equal to), > (greater than). >= (greater than or equal to), == (equal to), and != (unequal to). |
| Value | Specify the reference dimension value. |

In the Priority Pattern ID Level area, you can select one tool assignment and specify the tool assignment priority number by typing number in the cell. The lowest priority number indicates the highest tool assignment priority. If the dimensions of a part match the corresponding dimension settings, the system will assign tools to process based on the defined tool assignment priorities.

Example

| 1. | We will process the following part. The diameter of Hole A is 16 and the diameter of Hole B is 32. |
| --- | --- |
| 2. | In the Fit Tool Style panel, we select the RO template and specify the detail settings as follows. |
| 3. | Since the diameter of Hole A matches Condition 1, the system will first consider tool assignment A and search tools to single-hit the hole. If no tools are available, the system will consider using other methods to process the hole based on the tool assignment priority. Here a 16x16 RO tool is used to process Hole A. The diameter of Hole B match Condition 2, the system will first search tools to single-hit the hole, if no tools are available, the system will consider other tool assignment based on the tool assignment priority you have set. Because RO tools can be assigned to single-hit Hole B, the system will use tool assignment E based on the tool assignment priority you have set. The system will arrange an 8x8 RO to nibble Hole B. |
| 4. | If we set the tolerance as follows in the Tooling Pattern panel. |
|  | The system will use a 30 RO tool to single-hit Hole B. |

| See: | Hole Pattern List |
| --- | --- |
|  | Pattern Information and Assignment Pattern List |

### 11.5.3 Match To Line

The Match To Line panel provides options to set the preference for the SP tool to process the line segments (Single Hit, Punch Out).

| Option | Description |
| --- | --- |
| Match to Line | Place a check mark in the check box and you can assign specified SP to process the perimeters (Single Hit, Punch Out). |
| It Process before Template | Select It Process After Template option and the settings defined here are of higher priority when tools are assigned. |
| It Process After Template | Select It Process Before Template option and template settings will be applied with higher priority. |
| List of Tool | The List of special tools. |
| Add | Add a special tool from the tool inventory. See: Tool Inventory |
| Delete | Delete the special tool. |
| Tool Information | The information of the SP tool being selected. |
| Shape | Tool shape. |
| Range | Tool guide ranges. |
| X/Y/R Size | The X/Y/R size of the tool. |
| Forming Up/Down | Display the forming up/down type. |
| Shape Sub Code | Supplemental information for contouring tools, nesting tools, etc. |
| Comment | Tool comments |
| Assign Setting | Specify the conditions to assign SP tool to process the patterns. |
| Inner | Assign the SP tool to process the inner loops. |
| Outer | Assign the SP tool to process the outer perimeters. |
| For Acute | Place a check mark in the For Acute check box to assign special tools with acute angles to process parts with angles. The SP tools selected will only be assigned for angle processes. |
| Cancel All | Cancel all the previous operations. |
| Save | Save the modifications. |

| See: | Simple Tool Assignment Setting for the Specified Template |
| --- | --- |
|  | Fit Tool Style Panel |

#### 11.5.3.1 Assign SP Tool to Process Line Segment

In the Match To Line panel, we can specify the conditions to assign SP tool to process the parts.

| 1. | We will process the following part. The arc radius is 10. |
| --- | --- |
| 2. | In the Match To Line panel, click Add to open the Tool window, select one SP tool and click Add to add the SP tool to the List of Tool table. |
| 3. | In the Assign Setting preview area, click one element to be used to process the part. The selected element will be highlighted in red. If the selected element of the SP tool matches the pattern, the system will assign the SP tool to process this pattern. |
| 4. | Place a check mark in the Outer check box to assign the SP tool to process the outer perimeter. Type the assignment pattern name in the text box, and then click Save. The specified assignment pattern will be displayed in the column on the right side. You can specify more than one assignment pattern to meet your needs. The icons in this column represent the assignments that have been registered for each tool. Click an assignment, and its corresponding setting information will be displayed on the left. |
| 5. | Since the selected element of the SP tool share the same radius with the Arc. The system will assign the SP tool to process the arc by the specified pattern element. |

## 11.6 Edit of Template

In the Fit Tool Style panel, click Edit of Template button to open the List Of Template window.  You can select an existed template in the template list or input the template name directly in the File Name: text box, and then click Edit button to open the Template pane to edit the template. If you select an existed template in the template list, the name of the selected template appears automatically in the File Name: text box.

You can also type a new name in the File Name: text box to create a new blank template and then click Edit button to open the Template pane to edit the new template.

| Option | Description |
| --- | --- |
|  | In this drop-down list, you can select which type of template you want to display in the list below. Select All to display all templates; Select Hole to display Hole template; Select Notch to display Notch template and select Corner Notch to display Corner Notch template. |
|  | In the template list area, you can select the template you want to edit. The name of the selected template will appear in the File Name: text box automatically and then click Edit button to open Template pane to edit it. |
| File Name | You can type the name of an existed template and click Edit button to open Template pane to edit it. |
|  | You can also type a new name to create a new template and click Edit button to open Template pane to edit it. Example: 123.notch “123” represents name. “notch” represents type. If you don’t input the template type, the default type is Hole. |
| Edit | Click this button to open the Template pane. |
| Cancel | Click this button to cancel your setting and exit the List Of Template window. |

| See: | Template Pane |
| --- | --- |
|  | Template Creation Pane |

### 11.6.1 Template Pane

In the List OF Template window, click Edit button to open the Template pane. Here you can edit an existed template or create a new template.

| 1. | Template Menu |
| --- | --- |
| 2. | Template Toolbar |
| 3. | Template Icon |
| 4. | Template Parameter |
| 5. | Shape Edit area |
| 6. | Template Parameter |
| 7. | Edit of Path |
| 8. | Edit of Elements |
| 9. | Edit Additional Elements Information |

| See: | Template Menu |
| --- | --- |
|  | Template Toolbar |
|  | Template Icon |
|  | Template Parameter |
|  | Shape Edit area |
|  | Generate data |
|  | Edit of Path |
|  | Edit of Elements |
|  | Edit Additional Elements Information |

#### 11.6.1.1 Template Menu

The menu bar contains four items. If you select an item, a list of associated command options appears. You can use the mouse to navigate the menu by pointing and clicking the desired option.

#### 11.6.1.2 Template Toolbar

The toolbars can enhance your interaction with the program. Each toolbar corresponds to each menu. The buttons on the toolbars are associated with the commands found on the menus. You may find it easier to recognize and associate a particular toolbar button with a function than navigate a menu.

| File Toolbar |
| --- |
|  | Create a new template |
|  | Open an existed template. Click this button to open the List Of Template window. You can select an existed template in the template list area or input the name of an existed template directly in the File Name: text box, and then click Edit button to open it. You can also click Open CAD button to open a *.CAD file. |
|  | Download .prm files from AP100 |
|  | Save template |
| Edit Toolbar |
| The following eight buttons are basic edit buttons. |
|  | Cancel the previous operation. |
|  | Repeat the previously un-done action. |
|  | Cut the specified object |
|  | Copy the specified object |
|  | Paste the object that you previously cut or copied to the clipboard |
|  | Delete the specified object |
|  | Draw dimension line |
|  | Example: |
|  | 1. | The following is a basic shape of template without dimension. |
|  | 2. | Click and then the mouse becomes a cross-shape pointer in the Shape Edit area. A message appears prompting you to designate the first point of dimension line. |
|  | 3. | Select a point on the shape as the first point of dimension line. If you select the starting point, the middle point or the end point of an element as the first point of dimension line, a green point will appear automatically. |
|  | 4. | Click to confirm the first point and then drag the cross-shape pointer to select the second point. The first point becomes red and a green point will move with the pointer. A message appears prompting you to designate the second point of dimension line. |
|  | 5. | Click to confirm the second point. A number appears to designate the dimension between the two points. |
|  | 6. | You can also use letter to designate the dimension by pressing or key and selecting A, B, C or D in the text box. Generally, the first dimension will be designated A. Letter “A” will appear instead of the number. |
|  | 7. | To avoid overlap, you can drag the dimension line left or right, upwards or downwards according to actual condition. |
|  | 8. | You can also move the pointer to change the position of the designating letter (or number). |
|  | 9. | If you use number to designate the dimension, just click to finish your operation. If you use letter to designate the dimension by selecting in the text box, click or press <Enter> key to finish your operation. |
|  | 10. | Use the same way to designate other dimensions. |
|  | 11. | The designating dimension line is corresponding with the reference sizes in Parameter pane. You can click the arrow button next to each text box to select a name for the reference size or type a name for it. For Reference Size A and B, the default names are SMAXX and SMAXY respectively. |
|  | 12. | Referece Size A,B, C and D are associated with the optoins of Symbol column in Shape Condition window. See Symbol (Bookmark) |
|  | Select all elements of the basic shape, including dimension lines. |
| The following four buttons are drawing buttons. |
|  | Select command. Use the pointer to draw a frame, and the object in the frame will be selected. |
|  | Draw lines (one by one). When you finish drawing, click to exit. |
|  | Draw continuous line. After finishing drawing, right-click and select Pointer to confirm your operation or click directly to confirm your operation. |
|  | Draw arc. When you finish drawing, click to exit. |
| The following nine buttons are main editing buttons. |
|  | Rotate the selected element. |
|  | Example: |
|  | 1. | Select an element as rotating object and click . In the Shape Edit area, the mouse becomes a cross-shape pointer. A message appears prompting you to designate a basic point. Click to confirm a basic point. |
|  | 2. | Drag the pointer and you can see a dashed line rotate round the basic point. The value in the text box updates automatically to remind you the rotate angle when you drag the pointer. Also you can press or key and then type rotate angle directly in the text box. |
|  | 3. | Click to confirm your operation if you are satisfied with the rotation. (Press <Enter> key to confirm your operation if you rotate the element by typing value in the text box.) A dialog box appears asking you whether to remain the original object. |
|  | 4. | Click Yes to remain the original object. Click NO to delete the original object. |
|  | Mirror the selected element. |
|  | Example: |
|  | 1. | Select an element as rotating object and click . In the Shape Edit area, the mouse becomes a cross-shape pointer. A message appears prompting you to designate the first point of mirror line. Click to confirm the first point. |
|  | 2. | A message appears prompting you to designate the second point of the mirror line. Click to confirm the second point. A dialog box appears asking you whether to remain the original object, as appears in rotating operation. Click Yes to remain the original object. Click NO to delete the original object. |
|  | Create tangent corner radius. When you finish drawing, click to exit. |
|  | Click and a message appears prompting you to select the first object. A text box appears and you can press or key and then type a value in it to specify the radius length. At the same time, a message appears prompting you to select the second object. A tangent corner radius will be created when you finish selecting the second object. |
|  | Create inner corner radius. When you finish drawing, click to exit. |
|  | Use the same way as you create tangent corner radius to create inner corner radius. |
|  | Create outer corner radius. When you finish drawing, click to exit. |
|  | Use the same way as you create tangent corner radius to create outer corner radius. |
|  | Line grid |
|  | Example: |
|  | 1. | Select an object and click . In the Shape Edit area, the mouse becomes a cross-shape pointer. A message appears prompting you to input grid number in the text box. Type a value in it and press <Enter> key to confirm. |
|  | 2. | After input the value, click to confirm a base point. Drag the pointer to form grid and the values in the two text boxes update automatically. You can also type values in them respectively. (Press<Tab> key to switch between the two boxes.) |
|  | 3. | Click to confirm your operation. (Press <Enter> key to confirm your operation if you type values directly.) |
|  | Parallel grid |
|  | Use the same way as you create line grid to create parallel grid. Under this circumstance, you should first input grid number in X direction and then input grid number in Y direction in the boxes appearing during your operation. |
|  | Annular grid |
|  | Example |
|  | 1. | Select an object and click . In the Shape Edit area, the mouse becomes a cross-shape pointer. A message appears prompting you to designate a base point. |
|  | 2. | Click to designate a base point and then drag the pointer or type values in the text boxes to specify grid length, angle and number respectively. |
|  | 3. | Confirm your operation by using the same way as you do to confirm line grid. |
|  | Arc grid |
|  | Use the same way as you create annular grid to create parallel grid. |
|  | Trim the selected element |
|  | Example: |
|  | 1. | Suppose we want to trim the redundant sections of the two overlong lines in the following pattern to form a triangle. |
|  | 2. | Click and the mouse becomes a cross-shape pointer in Shape Edit area. A message appears prompting you to select an object. |
|  | 3. | Draw a frame with the pointer to select the whole pattern. Right click to confirm and the pattern selected becomes red. |
|  | 4. | Click to select the pattern you want to trim and the selected pattern will be trimmed. Click to confirm. |
|  | Extend an element to another element. |
|  | Example: |
|  | 1. | In the following basic shape, select E5. |
|  | 2. | Click and the mouse becomes a cross-shape pointer in the shape edit area. A message appears prompting you to select an object to extend. |
|  | 3. | Select E2 as the object to extent and you will see that E2 is extended to E5. Click to confirm and exit this mode. |
|  | Frame line. The system can recognize notch and corner notch easily by using frame line. |
|  | How to create frame line |
|  | 1. | Take the following corner notch as an example |
|  | 2. | Click and the mouse becomes a cross-shape pointer in the Pattern Edit area. A message appears prompting you to select a frame line. Select one frame line and then select the other one by using the same way. The green line and orange line are frame lines. Click to confirm your operation. |
|  |  | Note: In Part Edit mode, when you select to save template, the system will generate frame lines automatically if you select notch or corner notch as template type to save. |
|  | Elongate an element. |
|  | Example: |
|  | 1. | Click and the mouse becomes a cross-shape pointer in the Shape Edit area. A message appears prompting you to select an object to elongate. |
|  | 2. | Select an object, such as E3. A message appears prompting you to enter elongating value in the text box. You can also drag the pointer to elongate ad the value in the text box will update automatically. |
|  | 3. | Press <Enter> key to confirm your operation if you type values in the text box directly. Click to confirm your operation if you elongate by dragging the pointer directly. At last, you should click to exit this mode. |
| View Buttons |
|  | Display grid in the Shape Edit area. |
|  | Display relationship between elements. |
|  |  | Parallel |
|  |  | On the same line |
|  |  | Vertical |
|  |  | Horizontal |
|  |  | Right angle |
|  |  | Same size |
|  | Display elements |
|  | Display points |
|  | Display align dimension |
|  | Maximize all the basic shape to fit the Shape Edit area |

#### 11.6.1.3 Template Icon

The left part of the Template pane is the Shape Display area. You can right-click the icons here to add or delete pattern.

|  | The first icon is the basic shape of the template. Right-click it and select Add to add a new template-processing pattern. |
| --- | --- |
|  | The following icons represent different processing patterns. Right-click any one and select Add to add a new processing method or select Delete to delete the processing method. |

#### 11.6.1.4 Template Parameter

|  | The options in this section allow you to specify the template parameter: Rotation, Flip, Dimension Line, Element Number and Path Number. |
| --- | --- |

| Option | Description |
| --- | --- |
| Rotation | Place a check mark in the Rotation check box if you want the template to rotate to match the parts when processing. |
| Flip | Place a check mark in the Flip check box if you want the template to flip to match the parts when processing. |
| Type1 | The options in this section allow you to specify the template type that you want to create. |
| Type 2 | The options in this section allow you to specify whether the template consists of a single path or multiple paths. But now the system can only support single path. |
| Name | The name of the template. |
| Comment | The comment of the template. |
| Generate Data | After finish drawing or editing in the Shape Edit area, click this button to generate element and path data. |
| Detail | Place a check mark in the Detail check box to display Edit of Path pane, Edit of Element pane and Edit Additional Element Information pane. |
| Add | Click Add button to enter another Template pane to edit template-processing method. |
| Apply | Click Apply button to apply the shape in the Shape Edit area as a template. |
| Reset | Click Reset button to redraw basic shape in the Shape Edit area. |

#### 11.6.1.5 Shape Edit area

You can draw or edit the shape of a template in the Shape Edit area by using the icons on the toolbar. Right click to open a short-cut menu and you can also draw or edit by selecting options on the short-cut menu.

#### 11.6.1.6 Generate data

After finishing drawing or editing in the Shape Edit area, click the Generate Data button to generate data in the Edit of Path, Edit of Element and Edit Additional Element Information tables.

#### 11.6.1.7 Edit of Path

| Option | Description |
| --- | --- |
| Standard Shape | This option is currently unavailable. |
| Basic Coordinates X | This option is currently unavailable. |
| Basic Coordinates Y | This option is currently unavailable. |
| Start Point Min/Max Increased Angle | To define the range of the increased angle of start point (the angle between the first line and the horizontal line). |
| Start Point Increased Angle Mark | Specific angle mark for the specific angle range. Click the cell and the Increased Angle Mark window will appear. If the angle is 90, the corresponding mark should be 4. |
| End Point Min/Max Increased Angle | To define the range of the increased angle of end point (the angle between the last line and the horizontal line). |
| End Point Increased Angle Mark | Specify the angle mark for the specific angle range. Click the cell and following window appears. If the angle is 90, the corresponding mark should be 4. |
| Line Element Number | The number of line element. |
| Arc Element Number | The number of arc element. |
| Consult Path Number | This option is currently unavailable. |
| Standard Shape X Shape | This option is currently unavailable. |
| Standard Shape Y Size | This option is currently unavailable. |

#### 11.6.1.8 Edit of Elements

| Option | Description |
| --- | --- |
| #ID | The element number. |
| Element Type | The type of element. |
| Increased angle min | The minimum increased angle. |
| Increased angle max | The maximum increased angle. |
| Increased angle mark | The mark of increased angle. Click this text box to open the Increased Angle Mark dialog. |
|  | Select a desired increased angle mark value and click OK. |
| Parallel number | The number of parallel element. |
| Same line | The number of the same line. |
| Same length | The number of the same length element. |

#### 11.6.1.9 Edit Additional Elements Information

The information that appears in the Edit Additional Element Information table is coincident with the selected element. The information that displays for a line will be different from that of an arc.

In the following example, a Line has been selected in the drawing area. The Edit of Elements table displays the basic information for the line. If you select any element ID# in the Edit of Elements table, the corresponding information will appear in the Edit Additional Elements Information table.

| Option | Description |
| --- | --- |
| #ID | The element identification number. |
| Min Line Length | The minimum line length. The default value is 0. You can double-click to edit it. |
| Max Line Length | The maximum line length. The default value is 9999. You can double-click to edit it. |
| If you select an Arc in the drawing area, the corresponding information for the selected arc is listed in the Edit Additional Element Information window. |

| Option | Description |
| --- | --- |
| #ID | The element identification number. |
| Radius Min/Max | To define the range of the arc radius. |
| Arc Start Angle Min/Max | To define the range of the arc start angle. |
| Arc Start Angle Mark | The mark of arc start angle. If you click the cell, the Increased Angle Mark window will appear. |
| Arc Center Angle Min/Max | To define the range of the arc center angle. |
| Arc Center Angle Mark | The mark of arc center angle. If you click the cell, the Increased Angle Mark window will appear. |
| Rotation Direction | To define rotation direction of the arc is clockwise or counter-clockwise. |

### 11.6.2 Template Creation Pane

After generating data, you can click Add button to open Pattern Edit pane and begin edit pattern. You can also right-click the basic shape icon or pattern icon in the Shape Display area and select Add to open the Pattern Edit pane and begin edit pattern.

In the Pattern Edit pane, you can assign tools directly to the selected element or you can assign tools by using assistant lines. See Draw Assistant Line

Example:

| 1. | Take the following pattern as an example. This is an irregular pattern and we happen to have a special tool of the same shape as the pattern. |
| --- | --- |
| 2. | Under this circumstance, we click Single Hit button directly in the right Basic Shape Pattern pane. The special tools existed will be listed automatically below the Basic Shape Pattern pane. Select the tool that matches the pattern. |
| 3. | In the Pattern Edit area, the tool appears automatically and will move as the mouse moves. |
| 4. | Click to select a point as base point and click Single Hit button again. Then the selected special tool is assigned to single hit the pattern. |
| 5. | You can also assign to process it line by line. Select a line element in the pattern. |
| 6. | Select RO as tool type and then select Shear Proof in the Basic Shape Pattern pane. |
| 7. | The system will assign a RO tool to shear proof the line element. |
| 8. | Use the same will to assign to process other lines. The system will assign a RO tool to shear proof the pattern line by line. |
| 9. | Click Apply button to save it. |

Draw Assistant Line

| 1. | Take the following template as an example. In the pattern edit mode, right-click and select Draw Assistant Line. |
| --- | --- |
| 2. | The mouse becomes a cross-shape pointer and a message appears prompting you to design the first point of the assistant line. |
| 3. | Another message appears prompting you to designate the next point of the assistant line and click to designate. You can also input the length and angle of the assistant line directly in the text boxes and click to confirm. |
| 4. | In this example, we use an assistant line to divide the shape into two rectangles. Right-click and select Decompose Pattern to confirm your operation. |
| 5. | Sleeting Select Edge option. |
|  | Note: Select Edge is selected by default. |
| 6. | Select two lines to define the range. |
| 7. | Specify tool shape and select a basic shape pattern in the right pane. If you select SQ as tool shape and Rectangle as basic shape pattern, the system will use SQ tool to process this rectangle area. |
| 8. | Use the same way to assign tools to the other part of. |
| 9. | You can use different color to display the assignment. Choose Select Base Shape. |
| 10. | Select one base shape in the Pattern Edit area and right-click. Select Set Color. |
|  | Note: You can select Delete to delete this assignment here. |
| 11. | The Color dialog appears. Select one color and click OK. |
| 12. | The result is the following. |
| 13. | The system will generate data automatically in the Base Shape table |

| See: | Tool Assignment Pane |
| --- | --- |
|  | Basic Shape |
|  | Shape Data |

#### 11.6.2.1 Tool Assignment Pane

| Option | Description |
| --- | --- |
|  | You can specify tool you wanted in this pane. |
|  | You can select basic shape pattern in this pane. Rectangle, Triangle, Arc Internal and Arc External belong to sketch process and you can choose to punch out in Shape Data. See Shape Data |
| Name | The name of the template. |
| End Value | Specify the end value. There are four options here: None, M00, Work Chute and Joint. Only None and M00 are available. |
| Comment | Type any comment in the textbox. |
| Element Separation | This option is currently unavailable. |
| Assign Changeable | This option is currently unavailable. |
| Add | If you select an existed pattern in the left pattern list area, click this button to add a new pattern. |
| Apply | Click this button to apply pattern. |
| Reset | Click this to exit this pane and return to the previous one. |

#### 11.6.2.2 Basic Shape

The information in the table is generated automatically after you created the process template.

| Option | Description |
| --- | --- |
| Type | The type of the pattern. |
| Sequence ID | The ID of the sequence. |
| Continuous Sequence | The ID of the continuous sequence. |
| Interference flag | Place a check mark in the check box and the system will check interference automatically. This option is currently unavailable. |
| Sketch process | To use the sketch material to process. |
| Start Point | The start point of the sketch process. This option is currently unavailable. |
| Direction | The direction of the sketch process. This option is currently unavailable. |
| Normal Process | Use the normal material to process. |
| Start Point | The start point of the normal process. This option is currently unavailable. |
| Direction | The direction of the normal process. This option is currently unavailable. |
| Extrusion |  |
| Left | Place a check mark here and the system will execute extrusion on the left of the selected basic shape. |
| Right | Place a check mark here and the system will execute extrusion on the right of the selected basic shape. |

#### 11.6.2.3 Shape Data

| The Shape Data table will list the information of the selected item type in the Base Shape table. |
| --- |
| The Sequence ID displayed in Shape Data table will update with the Sequence ID you select in Basic Shape table. |
| With The type in the Basic Shape table, the Options to be shown in the Shape Data will vary. |
| Single Hit | Line | Shear Proof | Arc Shear Proof |
| Rectangle | Triangle | Arc Internal | Arc External |
| Laser Path |  |  |  |

| Rectangle: |
| --- |
| Option | Description |
| Sequence ID | The ID of the sequence. |
| Tool Shape | Display the tool shape. |
| Punch Out flag | Place a check mark here and the system will execute punch out to process this basic shape. |
| 1-4 | X and Y point of the four points of the rectangle. The system will use the four points indicate L1-L4 Coordinate. |
| L1-L3 Tolerance | The range of the L1-L4 extrusion. |
| L1-L4 Coordinates | The Coordinate of the L1-L4. |

| Triangle: |
| --- |
| Option | Description |
| Sequence ID | The ID of the sequence. |
| Tool Shape | Display the tool shape. |
| Punch Out flag | Place a check mark here and the system will execute punch out to process this basic shape. |
| P1-P3 Coordinates | The Coordinate of P1-P3. |
| L1-L3 Tolerance | The tolerance value of L1-L3. |
| L1-L3 Extended | The range of the L1-L3 extrusion |
| L1-L4 Coordinates | The Coordinate of the L1-L4. |

| Single Hit: |
| --- |
| Option | Description |
| Sequence ID | The ID of the sequence. |
| Tool Shape | Display the tool shape. |
| ManagementName | The name of the tool |
| Method to Decide Coordinates | This option is currently unavailable. |
| BaseX | The X Coordinate of the base point. |
| BaseY | The Y Coordinate of the base point. |
| Offset X | The X offset value of the center point of the pattern. Click this text box to open the Tool Offset Setting dialog. |
| Offset Y | The Y offset value of the center point of the pattern. |
| X Range | The range of tool X size. |
| Y Range | The range of tool Y size. |
| R Range | The range of tool R size. |
| Angle | The angle of the tool. |
| Select M Code | This option is currently unavailable. |

| Line: |
| --- |
| Option | Description |
| Sequence ID | The ID of the sequence. |
| Pattern | Place a check mark here and the system will execute punch out to process this basic shape. |
| Tool Shape | X and Y point for arc center. |
| ManagementName | The name of the tool |
| Start Point | X and Y point for start point. |
| End Point | X and Y point for end point. |
| Start Point Method Decide Coordinate | This option is currently unavailable. |
| End Point Method Decide Coordinate | This option is currently unavailable. |
| Tool X Range | The range of tool X size. |
| Tool Y Range | The range of tool Y size. |
| Tool R Range | The range of tool R size. |
| Tool Angle | The angle of the tool. |

| Shear Proof: |
| --- |
| Option | Description |
| Sequence ID | The ID of the sequence. |
| Tool Shape | Place a check mark here and the system will execute punch out to process this basic shape. |
| Slitting On/Off | This option is currently unavailable. |
| P1-P2 Coordinates | The Coordinate of P1-P3. |
| Start Point Extrusion | The range of the start point extrusion. |
| End Point Extrusion | The range of the end point extrusion. |
| Wire Joint Number | The number of wire joint |
| Wire Joint Assignment Type | Assignment type of wire joint |
| Process Coordinate | Processing coordinate |
| Tool Size X | The range of tool X size. |
| Tool Size Y | The range of tool Y size. |

| Arc Shear Proof: |
| --- |
| Option | Description |
| Sequence ID | The ID of the sequence. |
| ToolShape | X and Y point for arc center. |
| Arc Base | The X and Y point of arc base point. |
| Start Point | X and Y point of start point. |
| End point | X and Y point of endpoint. |
| Rotation Direction | The direction of the rotation. |
| Internal/external Process | Type internal/external process value. |
| Start Point Extrusion | The range of the start point extrusion. |
| End Point Extrusion | The range of the end point extrusion. |
| Wire Joint Number | The number of wire joint. |
| Wire Joint Layout Position | Layout position of wire joint. |

| Arc Internal: |
| --- |
| Option | Description |
| Sequence ID | The ID of the sequence. |
| Punch Out (Slug- Out Area) | Place a check mark here and the system will execute punch out to process this basic shape. |
| Arc Center | X and Y point for arc center. |
| Start Point | X and Y point for start point. |
| End Point | X and Y point for end point. |
| Rotation Direction | The direction of the rotation. |
| Start Point Extrusion | The range of the start point extrusion. |
| End Point Extrusion | The range of the end point extrusion. |

Arc External

If you select Arc External, the options are the same with Arc Internal.

| Laser Path: |
| --- |
| Option | Description |
| Sequence ID | The ID of the sequence. |
| End Value | Select a value from the drop-down list as the End Value to separate finished parts from the sheet. M00, Auto, Chute and Joint are available. |
| Z Axis Height | Type a height value in Z-axis. |
| Rotation Direction | Select a rotation direction from the drop-down list. CC(clockwise) and CCW(counter-clockwise) are available. |
| Element Number | Type a serial number for element. |
| Path Kind | Select a path kind from drop-down list. Open path and Close path are available. |
| Element ID | Displays the ID for element. |
| Start Point X | Displays starting point in X direction. |
| Start Point Y | Displays starting point in Y direction. |
| End Point X | Displays ending point in X direction. |
| End Point Y | Displays ending point in Y direction. |

# Chapter 12: Combi-Sequence

The options in the CombinationSequence window allow you to set the processing sequence, the repositioning, the clamp setting, the cutout avoidance and the part grid sequence, etc.

| To open the CombinationSequence window: |
| --- |
| 1. | Click one preference button in the Dr. ABE main window to open the Preference window. |
| 2. | Select EM-L machine in the Tree View pane. |
| 3. | Double-click the combi-sequence icon in the Preference File pane to display the CombinationSequence window |

| See: | General Sequence |
| --- | --- |
|  | Repositioning |
|  | Clamp Setting |
|  | Laser Sequence |
|  | Auto Cutout Avoidance |
|  | Punch Clamp Setting |
|  | Punch Sequence |
|  | Part-Grid |

## 12.1 General Sequence

The options in the Sequence panel allow you to specify the parameters for the cutting sequence.

| See: | Effect Setting |
| --- | --- |
|  | Starting Point/Direction |
|  | Sequence by Dividing the Sheet |
|  | Distance between Tooling |
|  | Sort of Laser & Punch |
|  | Sort by Process after Cutting |

### 12.1.1 Effect Setting

| The options in the Effect Setting section allow you to specify either the entire sheet or the individual parts as the sequencing unit. |
| --- |
| Option | Description |
| Sheet | This option will instruct the system to process the whole sheet as a single unit. If you select this option, all the parts will be processed on a pattern-by-pattern basis. |
| Laser is Each Part | Select this option, when the system uses laser to process the patterns, the system will perform the cutting process part by part after all the punching processes are finished. |
|  | If Laser is Each Part is selected, the system will performs the cutting process as follows. The system won’t perform cutting process on another part until it has finished all the cutting processes of one part. |
|  | If Laser is Each Part is not selected, the system will performs the cutting process as follows. The system will perform the cutting process pattern by pattern. |
| Each Part | This option will instruct the system to process each individual part as a unit. If you select this option, the system will process the parts on the sheet sequentially. |
| Machine Stop for Prototype | If you place a check mark in this check box, the system will generate an M00 program stop after the machine finishes processing prototype part on a pattern-by-pattern basis. |
| Process Prototype Part by Part | If you place a check mark in this check box, the system will process the prototype part by part. |
| Output only one M00 | If you place a check mark in this check box, the system will generate an M00 program stop after the machine finishes processing all prototypes. |

| See: | Sheet and Each Part |
| --- | --- |
|  | Machine Stop for Prototype |

#### 12.1.1.1 Sheet and Each Part

| The following demonstrates the difference between the Sheet and Each Part options. |
| --- |
| 1. | Select Sheet. |
| 2. | The sequence is as follows: |
| 3. | Select Each Part. |
| 4. | The sequence is as follows: |

| See | Machine Stop for Prototype |
| --- | --- |

#### 12.1.1.2 Machine Stop for Prototype

Set the prototype quantity in the Part Properties window.

Place a check mark in the Machine Stop for Prototype check box.

The system will process the prototype part on a pattern-by-pattern basis and generate an M00 program stop each time the machine finishes processing a prototype part.

Place a check mark in the Process Prototype Part by Part check box.

The system will process the prototype part by part and generate an M00 program stop each time machine finishes processing a prototype part.

Place a check mark in the Output only one M00 check box.

The system will process the prototype part by part and generate only one M00 program stop after machine finishes processing all prototype parts.

Remove a check mark in the Process Prototype Part by Part check box.

The system will process the prototype part on a pattern-by-pattern and generate only one M00 program stop after machine finishes processing all prototype part.

| See: | Sheet and Each Part |
| --- | --- |

| See: | Starting Point/Direction |
| --- | --- |
|  | Sequence by Dividing the Sheet |
|  | Distance between Tooling |
|  | Sort of Laser & Punch |
|  | Sort by Process after Cutting |

### 12.1.2 Starting Point/Direction

The options in the Starting Point/Direction section allow you to select the starting corner and processing direction. Click the desired arrow to specify the starting point and processing direction.

For example, if you select the arrow as follows, the system will process the parts from the top left of the sheet and in the positive X-axis direction.

| See: | Effect Setting |
| --- | --- |
|  | Sequence by Dividing the Sheet |
|  | Distance between Tooling |
|  | Sort of Laser & Punch |
|  | Sort by Process after Cutting |

### 12.1.3 Sequence by Dividing the Sheet

The Sequence by Dividing the Sheet option allows you to divide the sheet into equal areas for the processing sequence. If you place a check mark in this check box, the system will process the parts in the first area, and then go on to process those in the adjacent area in the direction defined in the Starting Point/Direction section. To use this function, you should type a number in the text box next to the option to specify the number of areas the sheet will be divided into.

For example, if you type 5 in the text box, and specify the following starting points and directions, the system will process the sheet as follows.

| See: | Effect Setting |
| --- | --- |
|  | Starting Point/Direction |
|  | Distance between Tooling |
|  | Sort of Laser & Punch |
|  | Sort by Process after Cutting |

### 12.1.4 Distance Between Tooling

The Distance Between Tooling option allows you to specify the distance between the end point of one cutting path and the starting point of the next cutting path. If the distance between the two points is less than the specified value, the system will skip the second path and move to the third path, thereby reducing the heat buildup during the cutting process of small parts.

| For example: |
| --- |
| 1. | If you remove the check mark from the Distance Between Tooling check box, the system will process the parts in the following sequence. |
| 2. | If you place a check mark in the check box and type 60 in the text box next to it, the system will process the parts in the following sequence. |

| See: | Effect Setting |
| --- | --- |
|  | Starting Point/Direction |
|  | Sequence by Dividing the Sheet |
|  | Sort of Laser & Punch |
|  | Sort by Process after Cutting |

### 12.1.5 Sort of Laser & Punch

In Sort of Laser & Punch section, we can specify the sequence to process the parts with outer laser holes, inner laser holes and forming.

In the Process list, you can select one item and click  or  to change the sequence priority, and the item on the top of the list has the highest priority.

Example:

If the sequence setting is defined as follows, Inner Laser Hole has the highest priority,

the system will process the part in the following sequence. The system will first perform all the punch processes first, then go on to cut the inner holes, perform forming process, and finally cut the outer loop.

If the sequence setting is defined as follows, Forming has the highest priority,

the system will process the part in the following sequence.

If the outer loop is processed by punch, and you specify the setting as follows,

the system will process the part in the following sequence. The system will perform all the punch process first, then go on to process the inner loop and perform forming process.

If you specify the setting as follows, and remove the check mark from the Combine Normal Punch with Last Punch Tool check box,

the system will process the part in the following sequence. The system will perform punch process first, then go on to process the inner loop, punch the outer loop, and finally perform forming process.

| See: | Effect Setting |
| --- | --- |
|  | Starting Point/Direction |
|  | Sequence by Dividing the Sheet |
|  | Distance between Tooling |
|  | Sort by Process after Cutting |

### 12.1.6 Sort by Process after Cutting

The options in the Sort By Process After Cutting section allow you to define the sequence priority to process patterns with different process-after-cutting conditions.

Note: Before use this option, please go to the Process After Preference window and specify the Process After Cutting conditions in Process After Cutting Table.

Example

| 1. | The following part is used as an example: |
| --- | --- |
| 2. | Go to the Process After Preference. In the Process after Cutting table, you can specify the conditions as follows. |
| 3. | Therefore the Process-after-Cutting conditions are as follows: The round hole with the diameter 10 is None; the round hole with the diameter 20 is Machine Stop and the round hole with the diameter 30 is Chute 1. |
| 4. | Open the Laser Sequence window. In the Sequence panel, specify the starting point and direction as follows. |
| 5. | If you remove the check marks from the Sort Holes by Process check box and the Sort Outer by Process check box, the sequence will be as follows: |
| 6. | Place a check mark in the Select Sort Holes by Process check box and specify the Process Order as follows. |
| 7. | The system will sequence the holes in the following order according to the Process after Cutting settings and the defined Process Order. Holes that are assigned with Chute 1 process method will be processed first, and then the holes with None, and then Holes with Machine Stop. |

| See: | Effect Setting |
| --- | --- |
|  | Starting Point/Direction |
|  | Sequence by Dividing the Sheet |
|  | Distance between Tooling |
|  | Sort of Laser & Punch |

| See | Repositioning |
| --- | --- |
|  | Clamp Setting |
|  | Laser Sequence |
|  | Auto Cutout Avoidance |
|  | Punch Clamp Setting |
|  | Punch Sequence |
|  | Part-Grid |

## 12.2 Repositioning

The repositioning is the movement of the clamps to avoid over travel and dead zones. Machines use clamps to shift the sheet to process the parts that are out of a processing range. In the Repositioning panel, you can define the reposition type, processing direction, etc.

| See: | Repositioning Type |
| --- | --- |
|  | Minimum Lap Amount |
|  | Process Majority of Parts |
|  | Process Direction |
|  | Return to First Position |

### 12.2.1 Repositioning Type

The options in the Repositioning Type section determine whether to process the parts within the same reposition or to divide the parts when repositioning.

| See: | Minimum |
| --- | --- |
|  | No Divide of Parts |
|  | Method of Dividing Long Parts |

#### 12.2.1.1 Minimum

If you select Minimum in the Repositioning Type section, the system will attempt to process the sheet by using the fewest repositions. The machine will process the parts within the process range first, then reposit the sheet, and then process the parts within the second process range. If there are still parts to be processed, the system reposits the sheet again until all the parts are processed.

In the following example, all the parts are processed with one reposition. The machine processes all the parts within the dashed rectangle before the reposition.

The machine will then process all the remaining parts after the reposition.

However, the parts location where the dashed line passes through is divided. Some segments of the parts are processed before the reposition, and the remaining after the reposition.

The part within the red rectangle will be used to illustrate the process before and after the reposition.

For the part in the red rectangle, before the reposition, the machine will process the patterns as follows. The green entities are the segments that are processed.

The Machine will process this segment:

It will then process the next segment.

Finally it will process this segment.

After the reposition, the machine will process the segments of the part as follows. The green entities are the segments that are processed after the repositioning.

The machine will first process this segment.

It will then process with the next segment.

Finally it will process this segment.

| See: | No Divide of Parts |
| --- | --- |
|  | Method of Dividing Long Parts |

#### 12.2.1.2 No Divide of Parts

If you select No Divide of Parts in the Repositioning Type section, none of the parts will be divided to process before and after a reposition, but more repositions are needed.

For example, you can select Minimum to process the following parts with just one reposition.

The machine processes all the parts within the dashed rectangle before the reposition.

The machine processes the remaining parts after the reposition.

If you select No Divide of Parts, the machine will process all the parts using two repositions, and none of the parts will be divided to process before and after a reposition.

The machine will process the parts as indicated by the red rectangle before the reposition.

The machine will continue to process the parts as indicated by the red rectangle after the first reposition.

The machine will finish processing all the remaining parts after the second reposition.

| See: | Minimum |
| --- | --- |
|  | Method of Dividing Long Parts |

#### 12.2.1.3 Method of Dividing Long Parts

This function is only available for laser process. If you select No Divide of Parts in the Repositioning Type section, the system will ignore the reposition times and process the whole part within the process range. However, parts having a dimension in the X-axis that is greater than the working range cannot be processed. To solve this problem, you can select Sheet or Each Part under Method of Dividing Long Parts to divide the part.

| Option | Description |
| --- | --- |
| Sheet | Select this option to process the whole sheet as a unit. The parts will be processed pattern-by-pattern. For the parts of the same length, the system will divide them at the same X coordinate and then perform process. |
|  | For example, when the following parts are processed, before the reposition, the system will perform the pierce process as indicated by the red points. |
|  | After the reposition, the system will perform the pierce process as indicated by the red points at the same X coordinate, and process the rest segments. |
| Each Part | Select this option to process each individual part as a unit. The system will process the parts part-by-part. For the parts of the same length, system will divide them at the same position of the part, and perform the process. |
|  | For example, when the following parts are processed, before the reposition, the system will perform the pierce process at the following red points. |
|  | After the reposition, the system will perform the pierce process at the following red points, and process the rest segments. |

| See: | Minimum |
| --- | --- |
|  | No Divide of Parts |

| See: | Minimum Lap Amount |
| --- | --- |
|  | Process Majority of Parts |
|  | Process Direction |
|  | Return to First Position |

### 12.2.2 Minimum Lap Amount

This function is only used for laser. The Minimum Lap Amount section allows you to specify the minimum process range overlap before and after the reposition.

In the following diagram, the white rectangle indicates the laser process range before repositioning; the yellow rectangle indicates the process range after the reposition. The red arrow line indicates the overlap amount.

| See: | Repositioning Type |
| --- | --- |
|  | Process Majority of Parts |
|  | Process Direction |
|  | Return to First Position |

### 12.2.3 Process Majority of Parts

Whether you select Minimum or No Divide of Parts under Repositioning Type, some patterns may be located in the process range overlap area. The options in the Process Majority of Parts section allow you to specify how to process those patterns in the overlap area.

| Option | Description |
| --- | --- |
| Before | Process the patterns located in the process range overlap area before the reposition is performed. |
| After | Process the patterns located in the process range overlap area after the reposition is performed. |

Example

| 1. | In the following diagram, the white rectangle indicates the laser process range before the reposition and the green rectangle indicates the range after the reposition. Some patterns are located in the overlap area. |
| --- | --- |
| 2. | If you select Before under Process Majority of Parts, those patterns will be processed before the reposition is performed. |
| 3. | If you select After under Process Majority of Parts, those patterns will be processed after the reposition is performed. |

| See: | Repositioning Type |
| --- | --- |
|  | Minimum Lap Amount |
|  | Process Direction |
|  | Return to First Position |

### 12.2.4 Process Direction

The options in the Process Direction section allow you to specify whether to process from the left to the right or from the right to the left while repositioning.

| Option | Description |
| --- | --- |
| Left to Right | Select this option, and parts will be processed from the left to the right. The parts in the original laser process range will be processed before the reposition. |
| Right to Left | Select this option, and parts will be processed from the right to the left. The system will generate a G27 reposition command first before processing the parts. |

Example

| If you select Left to Right, |
| --- |
| 1. | The parts in the original process range will be processed first. |
| 2. | After the first reposition, the parts in the process range will be processed. |
| 3. | After the second reposition, all the remaining parts will be processed. |
| If you select Right to Left, |
| 1. | The following picture shows the original process range before reposition. |
| 2. | After the reposition is performed, the process range will be as follows, and parts in this process range will be processed first. |
|  | After the second reposition, parts in this process range will be processed. |
|  | After the third reposition, the remaining parts will be processed. |

| See: | Repositioning Type |
| --- | --- |
|  | Minimum Lap Amount |
|  | Process Majority of Parts |
|  | Return to First Position |

### 12.2.5 Return to First Position

If you place a check mark in the Return to First Position check box, after processing all the parts, the system will generate a G27 command to instruct the holders to release the sheet and return the clamps to the original position.

| See: | Repositioning Type |
| --- | --- |
|  | Minimum Lap Amount |
|  | Process Majority of Parts |
|  | Process Direction |

| See: | General Sequence |
| --- | --- |
|  | Clamp Setting |
|  | Laser Sequence |
|  | Auto Cutout Avoidance |
|  | Punch Clamp Setting |
|  | Punch Sequence |
|  | Part-Grid |

## 12.3 Clamp Setting

Clamps are used to fasten the sheet on the worktable. The options in Clamp Setting panel allow you to specify the clamp conditions during the sequence.

| See: | Clamp Removal (Clamp # 3) |
| --- | --- |
|  | Clamp Position Change |

### 12.3.1 Clamp Removal (Clamp #3)

|  | For a machine with three clamps, this section is used to determine whether the third clamp can hold nothing during the reposition. |
| --- | --- |

Example

| 1. | If you place a check mark in the check box to allow the third clamp to hold nothing during the reposition. The system will process the parts as follows. All the parts in the sheet will be processed. |
| --- | --- |
|  | Before the reposition After the reposition |
| 2. | If you remove the check mark from the check box, the system won’t allow the third clamp to hold nothing after the reposition. As a result, some parts might not be processed. |
|  | Before the reposition After the reposition |

| See: | Clamp Position Change |
| --- | --- |

### 12.3.2 Clamp Position Change

|  | The options in this section allow you to define how to change the clamp position. |
| --- | --- |

| Option | Description |
| --- | --- |
| Initial Position (User-Defined Coordinates) | If this option is selected, the system will apply the initial clamp settings defined in the Clamp information panel of the Machine Set window. And the initial clamp position settings in the Initial Clamp Position panel of the Nesting window will be used. When the reposition is performed, the system will only generate G25 and G27 to instruct the machine to perform reposition. |
| Auto Calculation (Fixed During the Process) | This option is usually for customers having Multi Tapping device. When the tapping tool is used, system will first perform a clamp position change (G05) before punching. Then G25 or G27 will be generated for the repositioning. |
| Auto Calculation (Movements Exist in G05) | Select this option, the system will instruct the machine to change the clamp position or perform reposition to process the parts, and the system will try to generate G05 to instruct the machine to process the parts first. |

Example

| 1. | If Auto Calculation (Movements Exist in G05) is not selected, the system will instruct the machine to perform reposition to process the parts in the dead zone area. |
| --- | --- |
|  | Before the reposition After the reposition |
| 2. | If Auto Calculation (Movements Exist in G05) is selected, the system will generate G05 command, and the machine will change the clamp position to process the parts in the dead zone area. |
|  | Before the clamp position is changed After the clamp position is changed |

| See: | Clamp Removal (Clamp # 3) |
| --- | --- |

| See: | General Sequence |
| --- | --- |
|  | Repositioning |
|  | Laser Sequence |
|  | Auto Cutout Avoidance |
|  | Punch Clamp Setting |
|  | Punch Sequence |
|  | Part-Grid |

## 12.4 Laser Sequence

The options in the Laser Sequence panel allow you to specify the parameters for the cutting sequence. You can specify the parameters to put parts into the corresponding process areas during the sequence, and define the setting to shorten the process traverse.

| See: | Sequence Processing Object |
| --- | --- |
|  | Change Lead In for Shorten Traverse |
|  | Flip Macro Pattern for Shorten Traverse |

### 12.4.1 Sequence Processing Object

The options in the Sequence Processing Object section allow you to specify the processing area of the parts spanning two areas on the sheet. You can divide the sheet according to the lead in pierce positions of the parts or the center of processing track.

Example

| 1. | In the General Sequence panel, specify the starting point and direction as follows: |
| --- | --- |
| 2. | Type 4 in the Width for Sequence Division text box to divide the sheet into four areas. |
| 3. | As the following picture indicates, Part 1, Part 2, and Part 5 span Area 1 and Area 2. If you select Pierce Position under Sequence Processing Object, the system will regard Part 1, Part 2, and Part 5 as the parts belonging to Area 1 according to their lead in pierce positions. And the system will sequence the parts as follows. The same process happens to Parts 7, 8, 11 and Parts 13, 14 and 17. |
|  | If you select Center of Processing Track under Sequence Processing Object, the system will locate the parts based on their center points, and assign them to the processing areas where their center points are located. Part 3, 6, 7 span Area 1 and Area 2, but their center points are located in Area 2, so when the system sequence the parts, Part 3, 5, 7 will be put into Area 2. The same process happens to Part 9, 12, 13 and Part 15, 16, 19. |

| See: | Change Lead In for Shorten Traverse |
| --- | --- |
|  | Flip Macro Pattern for Shorten Traverse |

### 12.4.2 Change Lead In for Shorten Traverse

The options in the Change Lead In for Shorten Traverse section allow you to change the Lead in position to shorten the process traverse.

Note: If you remove the check mark from the Change Lead In for Shorten Traverse check box, the system will use the lead-in position defined in the Lead In/Out section to process the parts.

| Option | Description |
| --- | --- |
| Change Lead In for Shorten Traverse | Change the lead-in positions of the standard inner loops. |
| Outer | Change the lead-in position of the outer loop. |
| Irregular Hole | Change the lead in positions of irregular inner holes. |
| Open Path | Change the lead in positions of the open paths. |

Example

| 1. | When you remove the check mark from the Change Lead In for Shorten Traverse check box, |
| --- | --- |
|  | the system will decide the lead in position based on the settings in the Lead In/Out section, and process the patterns as follows. |
| 2. | When you place check marks in the Change Lead In for Shorten Traverse and the Outer check boxes, |
|  | The system will change the lead in position as follows to shorten the process path. |

| See: | Sequence Processing Object |
| --- | --- |
|  | Flip Macro Pattern for Shorten Traverse |

### 12.4.3 Flip Macro Pattern for Shorten Traverse

The traverse for a macro is determined during the part design phase. The system usually processes the macro along the original traverse. However, if you place a check mark in the Flip Macro Pattern for Shorten Traverse check box, the system will use the shortest path to process the parts.

Note: If you break the macro into lines and arcs, this option has no effect on these lines and arcs.

Example

| 1. | Click the Combo ToolAssign Preference button in the main window to open the Preference window. Click the Combi icon to display the Combination Tool Assignment window. Click the Laser Assignment button to open Laser Tool Assignment window. Go to the Path Assignment Method panel. Place a check mark in the Use Machine Macro Shape check box. |
| --- | --- |
| 2. | If you remove the check mark from the Flip Macro Pattern for Shorten Traverse check box, |
|  | the system will process the macros in the following sequence. |
| 3. | If you place a check mark in the Flip Macro Pattern for Shorten Traverse check box, |
|  | The system will process the macros in the following sequence, and the process traverse will be shortened. |

| See: | Sequence Processing Object |
| --- | --- |
|  | Change Lead In for Shorten Traverse |

| See: | General Sequence |
| --- | --- |
|  | Repositioning |
|  | Clamp Setting |
|  | Auto Cutout Avoidance |
|  | Punch Clamp Setting |
|  | Punch Sequence |
|  | Part-Grid |

## 12.5 Auto Cutout Avoidance

Cutout avoidance is used to prevent the laser head from crossing over previously cut holes in the work sheet or part(s). When the laser head moves over these holes, it will move downwards to detect the work sheet. The laser head may touch the edge of the hole and become damaged. In Auto Cutout Avoidance panel, you can define the cutout avoidance settings to instruct the laser head to avoid such holes.

| See: | Auto Cutout Avoidance |
| --- | --- |
|  | Target Traverse |
|  | Traverse Setting |
|  | High-Speed Shutter Less Setting |

### 12.5.1 Auto Cutout Avoidance

The Auto Cutout Avoidance option determines whether to apply cutout avoidance during the sequence. Place a check mark in the Auto Cutout Avoidance check box to enable this function. If you remove the check mark, the sheet is sequenced without any cutout avoidance.

Example

| 1. | If you remove the check mark from the Auto Cutout Avoidance check box, the sequence will be as follows. |
| --- | --- |
| 2. | If you place a check mark in the Auto Cutout Avoidance check box, the system will avoid the cutouts as follows: |

| See: | Target Traverse |
| --- | --- |
|  | Traverse Setting |
|  | High-Speed Shutter Less Setting |

### 12.5.2 Target Traverse

The options in the Target Traverse section allow you to specify which geometry types the laser head will avoid.

| Option | Description |
| --- | --- |
| All Axis Movement | During the cutting process, the system will avoid all the objects, including the inner loops, the outer loops and the open paths, whether etched or not. |
| Etching Patterns Only | The system will avoid all the objects except the etched patterns. |

Example

If you choose to avoid no objects, the result will be as follows.

If you choose to avoid all objects, the result will be as follows.

If you choose to avoid all objects except the etched patterns, the result will be as follows.

| See: | Auto Cutout Avoidance |
| --- | --- |
|  | Target Traverse |
|  | High-Speed Shutter Less Setting |

### 12.5.3 Traverse Setting

The options in the Traverse Setting section allow you to specify the avoidance conditions.

| See: | Additional Width (For Material, Process Range) |
| --- | --- |
|  | Additional Width (Traverse) |
|  | Do Not Avoid if Distance is Greater than [ ] Times of Original |
|  | Do Not include the cutting smaller than X [ ] Y [ ] |
|  | Do Not include the cutting bigger than X [ ] Y[ ] |
|  | Do Not Avoid Cutout with Joint |

#### 12.5.3.1 Additional Width (For Material, Process Range)

This option allows you to define the distance the laser head keeps away from the sheet edge. The laser head will not move to the edge of the sheet because the beam head might get damaged if it moves too close to the edge.

Type a value in the Additional Width (For Material, Process Range): text box. The system will use this value to specify the distance that the laser head should keep away from the sheet edge.

The following diagram shows the avoidance value of Additional Width (For Material, Process Range).

| See: | Additional Width (Traverse) |
| --- | --- |
|  | Do Not Avoid if Distance is Greater than [ ] Times of Original |
|  | Do Not include the cutting smaller than X [ ] Y [ ] |
|  | Do Not include the cutting bigger than X [ ] Y[ ] |
|  | Do Not Avoid Cutout with Joint |

#### 12.5.3.2 Additional Width (Traverse)

This option allows you to specify a border around all of the geometries. The laser head avoids the actual cutout. The laser head might be damaged if it moves too close to the cutout(s). Type a value in the Additional Traverse (Traverse): text box to specify the distance between the laser movement path and the cutout. The red arrow in the following diagram indicates the Additional Traverse (Traverse): text box.

| See: | Additional Width (For Material, Process Range) |
| --- | --- |
|  | Do Not Avoid if Distance is Greater than [ ] Times of Original |
|  | Do Not include the cutting smaller than X [ ] Y [ ] |
|  | Do Not include the cutting bigger than X [ ] Y[ ] |
|  | Do Not Avoid Cutout with Joint |

#### 12.5.3.3 Do Not Avoid if Distance is Greater than Times of Original

Type a value in the text box, and if the specified cutout avoidance traverse is greater than the specified times of the original movement, the system will not perform the cutout avoidance during the cutting process. You can eliminate the excessive traverse by using this option.

| See: | Additional Width (For Material, Process Range) |
| --- | --- |
|  | Additional Width (Traverse) |
|  | Do Not include the cutting smaller than X [ ] Y [ ] |
|  | Do Not include the cutting bigger than X [ ] Y[ ] |
|  | Do Not Avoid Cutout with Joint |

#### 12.5.3.4 Do Not Avoid if the Distance is Smaller than Times of Original

This option allows you control the cutout avoidance according to the minimum X and Y dimensions for patterns. If the object is less than the specified dimensions, the system will not avoid it.

| See: | Additional Width (For Material, Process Range) |
| --- | --- |
|  | Additional Width (Traverse) |
|  | Do Not Avoid if Distance is Greater than [ ] Times of Original |
|  | Do Not include the cutting bigger than X [ ] Y[ ] |
|  | Do Not Avoid Cutout with Joint |

#### 12.5.3.5 Do Not Include the Cutting Bigger Than

This option allows you to control the cutout avoidance according to the maximum X and Y dimensions for patterns. If the object is greater than the specified dimension, the system will not avoid it.

Example

| 1. | The following part is used in this example. Note the dimensions of the inner patterns. |
| --- | --- |
| 2. | If you remove the check mark from the Auto Cutout Avoidance check box, the result will be as follows. |
| 3. | If you place a check mark in the Auto Cutout Avoidance check box and specify the settings as follows: |
| 4. | The system will avoid all the cutouts: |
| 5. | Change the greatest dimension range of cutout that the system is to avoid. |
| 6. | As a result, the system does not avoid the rectangular cutout. |
| 7. | Change the greatest dimension range of cutout that the system is to avoid. |
| 8. | As a result, the system does not avoid any of the cutouts. |

| See: | Additional Width (For Material, Process Range) |
| --- | --- |
|  | Additional Width (Traverse) |
|  | Do Not Avoid if Distance is Greater than [ ] Times of Original |
|  | Do Not include the cutting smaller than X [ ] Y [ ] |
|  | Do Not Avoid Cutout with Joint |

#### 12.5.3.6 Do Not Avoid Cutout with Joint

If there are microjoints applied to the parts, the parts will be removed only after all the work pieces are processed. It is therefore unnecessary for the laser head to travel a greater distance to avoid the cutouts with joints.

Example

| 1. | If you remove the check mark from the Do Not Avoid Cutout with Joint check box, all of the cutouts will be avoided. |
| --- | --- |
| 2. | If you place a check mark in the Do Not Avoid Cutout with Joint check box, the system will not avoid the cutouts with joints. |

| See: | Additional Width (For Material, Process Range) |
| --- | --- |
|  | Additional Width (Traverse) |
|  | Do Not Avoid if Distance is Greater than [ ] Times of Original |
|  | Do Not include the cutting smaller than X [ ] Y [ ] |
|  | Do Not include the cutting bigger than X [ ] Y[ ] |

| See: | Auto Cutout Avoidance |
| --- | --- |
|  | Target Traverse |
|  | High-Speed Shutter Less Setting |

### 12.5.4 High-Speed Shutter Less Setting

The options in the High-Speed Shutter Less Setting section allow you to increase the cutting speed by controlling the rate of the beam head shutter. It is not necessary for the machine to open and close the shutter for each cut when it processes thinner materials.

Note: If you want to enable the high-speed function, please remember to remove the check mark from the Use Machine Macro Shape check box in the Laser Tool Assignment window.

Example

| 1. | If you remove the check mark from the Use High-Speed Shutter Less (Eliminate M103/104) check box, M103/M104 will be generated in processing each loop. |
| --- | --- |
| 2. | If you place a check mark in the Use High-Speed Shutter Less (Eliminate M103/104) check box only, M103/M104 will be generated in processing each part. |
| 3. | If you place check marks in both the Use High-Speed Shutter Less (Eliminate M103/104) check box and the Use High-Speed Shutter Less between Parts check box, M103 will be omitted when the laser head moves from the perimeter to the position to start process. |
| 4. | When no pierce is selected, M103A0 will be generated before lead in processing. In this case, if you remove the check mark from the Use High-Speed Shutter Less (Eliminate M103/104) check box, M103A0 will be generated in processing each loop. |
| 5. | If you place check marks in both the Use High-Speed Shutter Less (Eliminate M103/104) check box and the Use High-Speed Shutter Less for M103A0 check box under the circumstance that no pierce is selected, only one M103A0 will remain in the NC code. Others will be omitted. |

| See: | Auto Cutout Avoidance |
| --- | --- |
|  | Target Traverse |
|  | Traverse Setting |

| See: | General Sequence |
| --- | --- |
|  | Repositioning |
|  | Clamp Setting |
|  | Laser Sequence |
|  | Punch Clamp Setting |
|  | Punch Sequence |
|  | Part-Grid |

## 12.6 Punch Clamp Setting

The options in the Punch Clamp Setting will instruct the system to avoid the dead zones while sequencing.

In the Clamp Position Change panel, you can specify the distance the sheet will move to prevent the clamp from passing through the turret.

| See | Avoid Dead Zone |
| --- | --- |
|  | Passage Avoidance in the Turret When Moving Axis |

### 12.6.1 Avoid Dead Zone

|  | Place a check mark in the Avoid DZ check box, and the system will instruct the machine to perform reposition to avoid the dead zones. |
| --- | --- |

| Option | Description |
| --- | --- |
| Avoid Dead Zone | Select this option, and the system will generate data to instruct the machine to avoid the dead zones. |
| Track Check | Select this option, and the system will add the track offset value (40mm) to Dead Zone value of each range, and perform repositions to avoid Dead Zones. 300 Track：0 mm (Tool offset-40＋Track offset 40) 200 Track：40 mm (Tool offset 0＋ Track offset 40) 100 Track：80 mm (Tool offset 40＋ Track offset 40) |

Example

| 1. | Parts are nested as follows, and some parts are nested close to the clamps. |
| --- | --- |
| 2. | If Avoid Dead Zone is not selected, the system processes the parts without reposition, and tools might get damaged during the process. |
| 3. | If Avoid Dead Zone is selected, the system will process those parts that are out of the dead zones first. |
|  | Then the system will perform reposition and continue to process those parts not finished. In this way, the system can prevent the tools getting damaged while processing the parts in the dead zones. |

| See: | Passage Avoidance in the Turret When Moving Axis |
| --- | --- |

### 12.6.2 Passage Avoidance in the Turret When Moving Axis

To prevent the clamp from passing through the turret, specify the movement path based on G70 (No Punch).

Before the clamp passes through the area specified in each track, the system will output G70 to instruct the machine avoid the area specified.

Example

| 1. | Specify the conditions as follows. |
| --- | --- |
| 2. | Two parts are nested around the clamp as the following illustration indicates. The distance from the center of the hole pattern to the sheet edge is 69. The system will assign a round tool in station T303 (Which is on the outer track) to process this hole. |
| 3. | Since the distance from the center of the hole pattern to the sheet edge is 69, greater than the 60. The machine will move the sheet directly to allow the same tool to process the next hole as the following illustration shows. No collisions will happen between the tool and clamp during the process. |
| 4. | If the same parts are nested around the clamp as follows, but the distance from the center of the hole pattern to the sheet edge is 59, and the system will assign the same tool in station T303 to process these two holes, |
| 5. | Since the distance from the center of the hole pattern to the sheet edge is 59, less than the 60. If the machine moves the sheet directly, collision might occur, and tools and clamps might get damaged. Therefore the system will generate G70 to instruct the machine to move the sheet the distance 160 in the Y-axis during the process. |
|  | In this way, no collisions will happen between the tools and clamps during the process. |

| See | Avoid Dead Zone |
| --- | --- |

| See: | General Sequence |
| --- | --- |
|  | Repositioning |
|  | Clamp Setting |
|  | Laser Sequence |
|  | Auto Cutout Avoidance |
|  | Punch Clamp Setting |
|  | Punch Sequence |
|  | Part-Grid |

## 12.7 Punch Sequence

The options in the Punch Sequence allow you to specify the tool priority and tool assignment conditions.

| See: | Angle of Turret |
| --- | --- |
|  | AI Tool Angle Sort |
|  | Sort Function |

### 12.7.1 Angle of Turret

When the tools in the same sequence group have the same sequence number, select Angle of Turret, the system will use the tools by the order of the turret angle. The tools placed in the stations of smaller turret angles will be used first, which reduces the turret rotation time for the process.

Example

| 1. | We will process the following part. |
| --- | --- |
| 2. | We will use the following RO tools to single hit the inner loops. These tools are in the same sequence group and have the same sequence number. |
| 3. | These tools are placed in the following turret stations, T303, T305, T 206 and T309. Among all these stations, T303 has the smallest turret angle, while T309 has the largest turret angle. |
| 4. | If Angle of Turret is not selected, the system will automatically sequence the inner loops as follows. |
| 5. | If Angle of Turret is enabled, the system will process the inner loops in the following sequence. As the following NC code indicates, tools in the turret of smaller angles are used earlier. |

#### 12.7.1.1 Mix Sequence within

If the tools are placed in the stations of the same turret angle, when you only select Angle of Turret without selecting Mix Sequence within at the same time, the system will assign those tools in the order of the inner track, center track and outer track. If you select Mix Sequence within, the tools of the same turret angle will have the same priority. In this case, the system will process the parts based on the shortest process time.

Example

| 1. | There are following tools in the turret. A RE 9 x 7 tool in station T116, a RO-10 tool in station T217, a SQ-8.5 tool in station T318. and we will use these tools to process the following inner loops: a 9 x 7 rectangle hole, a 10 x 10 round hole and a 8.5 x 8.5 square hole. |
| --- | --- |
| 2. | Station T116, T217 and T318 have the same turret angle. |
| 3. | These three tools are all in Gr1 and have the same sequence number. |
| 4. | In the Main tab of the Tool Assign Condition window, specify the Turret Generation settings as follows. |
| 5. | If Angle of Turret is selected, these three holes are punched in the order of inner track, center track and outer track. |
| 6. | If Angle of Turret and Mix Sequencing with, since the tools of the same turret angle have the same priority, the system will process the inner loops based on the shortest process time. |

| See: | AI Tool Angle Sort |
| --- | --- |
|  | Sort Function |

### 12.7.2 AI Tool Angle Sort

Specify the way to use the tool in the AI stations to process the patterns.

| Option | Description |
| --- | --- |
| All Tool Angle | Place a check mark in the All Tool Angle check box, and the system will use the AI tools to process the patterns by angle. |
|  | Example; |
|  | We assign an AI tool to process the following patterns. |
|  | If All Tool Angle is selected, the system will use the AI tools to process the patterns by angle. |
|  | If All Tool Angle is not selected, the system will use the AI tools to process the patterns based on the shortest path |
| Range A - Range F | Select the options, and the system will use the AI tools of the corresponding ranges to process the patterns by angle. |

Note:

To enable the AI Tool Angle Sort function, you must remove the check mark from the C Axis Sort Off check box. See: C Axis Sort Off

| See: | Angle of Turret |
| --- | --- |
|  | Sort Function |

### 12.7.3 Sort Function

This function is not available at this moment.

| See: | Angle of Turret |
| --- | --- |
|  | AI Tool Angle Sort |

| See: | General Sequence |
| --- | --- |
|  | Repositioning |
|  | Clamp Setting |
|  | Laser Sequence |
|  | Auto Cutout Avoidance |
|  | Punch Clamp Setting |
|  | Part-Grid |

## 12.8 Part-Grid

In the Part-Grid panel, you can specify the conditions to process part grid, define the sequence for common line cutting, and decide whether to output the specific M code in the UV macro commands or not.

| See | Part-Gird Condition |
| --- | --- |
|  | Common Line Cutting |
|  | Output Outside of UV |

#### 12.8.1 Part-Gird Condition

|  | In this section, you can specify whether to output G98 in the NC code, and you can also define the starting position and process direction for processing the part grid. |
| --- | --- |

| Option | Description |
| --- | --- |
| Output Part Grid | Output G98 in the NC code to indicate the use of part grid macros. |
|  | Notes: You must open the Nesting window, click Nesting Logic 2 tab and place a check mark in the Enable Part Grid check box under Grid Pattern to enable the function. |
| Starting Position | Specify the starting position to process the part grid. |
|  | Option | Description |
|  | Top left | Output Q3 to instruct the machine to process the part grid from the top left. |
|  | Top Right | Output Q4 to instruct the machine to process the part grid from the top right. |
|  | Bottom Left | Output Q1 to instruct the machine to process the part grid from the bottom left. |
|  | Bottom Right | Output Q2 to instruct the machine to process the part grid from the bottom right. |
| Auto | Select Auto option, and the place close to the end point of the previous process will be used as the starting point. |
| Process Direction | Specify the preferred process direction of the part grid. |
|  | Option | Description |
|  | X-Axis | Output G75 to instruct the machine to process the part grid along X-axis. |
|  | Y-Axis | Output G76 to instruct the machine to process the part grid along Y-axis. |
| Auto | Select Auto option, and the process direction defined in the Starting Point/Direction section in the General Sequence panel will be used as the process direction to process the part grid. See: Starting Point/Direction |

Example

| 1. | In the Nesting logic 2 panel of the Nesting window, place a check mark in the Enable Part Grid check box. |
| --- | --- |
| 2. | In the Part-Grid panel of the combi-sequence window, specify the settings as follows. |
| 3. | The system will generate the following NC code commands, |
|  | And process the part grid as follows. |

| See: | Common Line Cutting |
| --- | --- |
|  | Output Outside of UV |

#### 12.8.2 Common Line Cutting

|  | Specify the sequence for common line cutting. |
| --- | --- |

| Option | Description |
| --- | --- |
| Start Position | Specify the starting position for common line cutting. |
| Auto | Select this option and the system will specify the start position automatically. |
| Fixed Direction | Select this option, and the system will perform common cutting process always in one direction. |
| Direction to Process First | Specify the direction to perform the common cutting process. |
| X | Perform the common line cutting in the X-axis. |
| Y | Perform the common line cutting in the Y-axis. |
| Longer | Longer common lines will be processed first. |
| Shorter | Shorter common lines will be processed first. |
| Image View | After selecting the starting position and process direction, the preview image will automatically update to reflect the changes. |

Example

| 1. | In the Parts Properties window, place a check mark in the Common Line Cutting check box. |
| --- | --- |
| 2. | In the Part-grid panel of CombinationSequence window, specify the settings as follows: |
|  | The system will perform the common cutting process as follows. |
| 3. | If you specify the settings as follows: |
|  | The system will perform the common cutting process as follows. |

| See | Part-Gird Condition |
| --- | --- |
|  | Output Outside of UV |

#### 12.8.3 Output Outside of UV

|  | If the UV Macro commands contains the commands of only one tool, you can select whether the specified M code is included in the UV macro commands or not. In this way the process time can be shortened. |
| --- | --- |

Example

| 1. | When part grids are processed, the system will output the following NC code commands if TNO is not selected, The M Code about tool number is inside UV. |
| --- | --- |
| 2. | If TNO is selected, M Code about tool number is outside UV |

| See | Part-Gird Condition |
| --- | --- |
|  | Common Line Cutting |

| See: | General Sequence |
| --- | --- |
|  | Repositioning |
|  | Clamp Setting |
|  | Laser Sequence |
|  | Auto Cutout Avoidance |
|  | Punch Clamp Setting |
|  | Punch Sequence |

# Chapter 13: NC Generate

You can click the NC Generate Preference button  on the main window to open the Preference window.  In the Preference window, select a punch machine (e.g. EM2510) from the left Tree View pane, and then click the NC icon in the top Preference File pane to display the NC Generate window.

In this window, these options allow you to specify conditions for the NC code generation.

As soon as you select an item of the parameter, the note with description on the right will update.

| See: | Material |
| --- | --- |
|  | Use Setup Sheet |
|  | Setup Sheet |
|  | Output G93 |
|  | Percent After G50 |
|  | Output work size comment at the end of G92 command line |
|  | Use G42/G42 |
|  | Z Height M104Zx |
|  | Is G01 Continued |
|  | Unload Skeleton M Code |
|  | M108 After M104 Code |
|  | Loading / Unloading Device |
|  | Loading / Unloading Thickness M-Code |
|  | Loading / Unloading End Position M-Code |

## 13.1 Material

| Place a check mark in the check box and type a value in the right-side cell. The input value indicates the type of the material. (0=SPC, 1=SUS, 2=AL) |
| --- |
|  | For example, G06 line in the NC code indicates the material information. A indicates that the thickness is 1.0. B indicates that the type of the material is AL. |

| See: | Use Setup Sheet |
| --- | --- |
|  | Setup Sheet |
|  | Output G93 |
|  | Percent After G50 |
|  | Output work size comment at the end of G92 command line |
|  | Use G42/G42 |
|  | Z Height M104Zx |
|  | Is G01 Continued |
|  | Unload Skeleton M Code |
|  | M108 After M104 Code |
|  | Loading / Unloading Device |
|  | Loading / Unloading Thickness M-Code |
|  | Loading / Unloading End Position M-Code |

## 13.2 Use Setup Sheet

|  | Place a check mark in the check box to enable the system to output the setup sheet information in the NC code. You can also decide where to display the setup sheet information: on top of the NC code, or at the bottom of it. See: Setup Sheet |
| --- | --- |

| See: | Material |
| --- | --- |
|  | Setup Sheet |
|  | Output G93 |
|  | Percent After G50 |
|  | Output work size comment at the end of G92 command line |
|  | Use G42/G42 |
|  | Z Height M104Zx |
|  | Is G01 Continued |
|  | Unload Skeleton M Code |
|  | M108 After M104 Code |
|  | Loading / Unloading Device |
|  | Loading / Unloading Thickness M-Code |
|  | Loading / Unloading End Position M-Code |

## 13.3 Setup Sheet

This option works with Use Setup Sheet option together to define the output position of the setup sheet information.

|  | Place a check mark in the check box to display the Sheet Setup Information on top of the NC code. |
| --- | --- |
|  | Otherwise the information will be at the bottom if you remove the check mark. |

| See: | Material |
| --- | --- |
|  | Use Setup Sheet |
|  | Output G93 |
|  | Percent After G50 |
|  | Output work size comment at the end of G92 command line |
|  | Use G42/G42 |
|  | Z Height M104Zx |
|  | Is G01 Continued |
|  | Unload Skeleton M Code |
|  | M108 After M104 Code |
|  | Loading / Unloading Device |
|  | Loading / Unloading Thickness M-Code |
|  | Loading / Unloading End Position M-Code |

## 13.4 Output G93

|  | Place a check mark in the check box to enable the system to output G93 line indicating the layout preference point of local coordinate system. |
| --- | --- |

| See: | Material |
| --- | --- |
|  | Use Setup Sheet |
|  | Setup Sheet |
|  | Percent After G50 |
|  | Output work size comment at the end of G92 command line |
|  | Use G42/G42 |
|  | Z Height M104Zx |
|  | Is G01 Continued |
|  | Unload Skeleton M Code |
|  | M108 After M104 Code |
|  | Loading / Unloading Device |
|  | Loading / Unloading Thickness M-Code |
|  | Loading / Unloading End Position M-Code |

## 13.5 Percent After G50

|  | Place a check mark in the check box to enable the system to generate a percent symbol (%) as the end-of-record code. During the process of the data transmission, a percent symbol indicates the end of the transmission. |
| --- | --- |

| See: | Material |
| --- | --- |
|  | Use Setup Sheet |
|  | Setup Sheet |
|  | Output G93 |
|  | Output work size comment at the end of G92 command line |
|  | Use G42/G42 |
|  | Z Height M104Zx |
|  | Is G01 Continued |
|  | Unload Skeleton M Code |
|  | M108 After M104 Code |
|  | Loading / Unloading Device |
|  | Loading / Unloading Thickness M-Code |
|  | Loading / Unloading End Position M-Code |

## 13.6 Output work size comment at the end of G92 command line

|  | Place a check mark in the check box to enable the system to display minimum work size comment at the end of G92 command line, as (X54.Y88.) in the left picture. |
| --- | --- |

| See: | Material |
| --- | --- |
|  | Use Setup Sheet |
|  | Setup Sheet |
|  | Output G93 |
|  | Percent After G50 |
|  | Use G42/G42 |
|  | Z Height M104Zx |
|  | Is G01 Continued |
|  | Unload Skeleton M Code |
|  | M108 After M104 Code |
|  | Loading / Unloading Device |
|  | Loading / Unloading Thickness M-Code |
|  | Loading / Unloading End Position M-Code |

## 13.7 Use G42/G42

|  | If necessary, the system must compensate for the diameter of the laser beam. If there is no compensation, the finished parts may be larger or smaller than the intended dimensions. |
| --- | --- |
|  | The Use G41/G42 will adjust the cutting head to one side of the path to compensate for the beam diameter. The code output is either G41 or G42. |
|  | G41 is the left-side beam path compensation to the advanced direction and G42 is the right-side beam path compensation to the advanced direction. In the figure to the left, the red points indicate the diameter of laser beam. |
|  | Whether G41 or G42 is generated in the code depends on the inner loop or the outer loop and the direction of the cut. |
|  | If the system cuts an outer loop in the counter clock-wise direction, the laser beam path will be shifted to the right side of the advanced direction. The system will generate a G42 in the NC code. |
|  | If the system cuts an outer loop in the clockwise direction, the laser beam path will be shifted to the left side of the advanced direction. The system will generate a G41 in the NC code. |
|  | If the system cuts an inner loop in the clockwise direction, the laser beam path will be shifted to the right side of the advanced direction. The system will generate a G42 in the NC code. |
|  | If the system cuts an inner loop in the counter-clockwise direction, the laser beam path will be shifted to the left side of the advanced direction. The system will generate a G41 in the NC code. |

| See: | Material |
| --- | --- |
|  | Use Setup Sheet |
|  | Setup Sheet |
|  | Output G93 |
|  | Percent After G50 |
|  | Output work size comment at the end of G92 command line |
|  | Z Height M104Zx |
|  | Is G01 Continued |
|  | Unload Skeleton M Code |
|  | M108 After M104 Code |
|  | Loading / Unloading Device |
|  | Loading / Unloading Thickness M-Code |
|  | Loading / Unloading End Position M-Code |

## 13.8 Z Height M104Zx

|  | If you place a check mark in the Z Height M104 check box, the system will generate a Z value after the M104. This will close the shutter and raise the cutting head to a specific height after the patterns are cut. The system will generate an M104Zxx, with the xx representing the Z-axis value. |
| --- | --- |
| Note: The Z or height value is specified in the Process After Cutting panel of the Laser Tool Assignment window as below: |

| See: | Material |
| --- | --- |
|  | Use Setup Sheet |
|  | Setup Sheet |
|  | Output G93 |
|  | Percent After G50 |
|  | Output work size comment at the end of G92 command line |
|  | Use G42/G42 |
|  | Is G01 Continued |
|  | Unload Skeleton M Code |
|  | M108 After M104 Code |
|  | Loading / Unloading Device |
|  | Loading / Unloading Thickness M-Code |
|  | Loading / Unloading End Position M-Code |

## 13.9 Is G01 Continued

|  | If you place a check mark in this check box, the system will generate the NC code on the left. G01 won’t be omitted. |
| --- | --- |
|  | If you remove the check mark from this check box, the system will omit the G01 command when the straight-line cutting process is repeated. |

| See: | Material |
| --- | --- |
|  | Use Setup Sheet |
|  | Setup Sheet |
|  | Output G93 |
|  | Percent After G50 |
|  | Output work size comment at the end of G92 command line |
|  | Use G42/G42 |
|  | Z Height M104Zx |
|  | Unload Skeleton M Code |
|  | M108 After M104 Code |
|  | Loading / Unloading Device |
|  | Loading / Unloading Thickness M-Code |
|  | Loading / Unloading End Position M-Code |

## 13.10 Unloading Skeleton M Code

|  | This option allows you to output an M code to unload the skeleton material. To output the unloading skeleton M code, you must place a check mark in the LOADING/UNLOADING DEVICE (1=YES 0=NO) check box. Place a check mark in the Unloading Skeleton M Code check box and type 380 to specify the M code in the cell to the right. The system will output an M380 indicated as the NC code to the left. |
| --- | --- |
| Note: Make sure a loading/Unloading device is selected from the Tandem Device Type drop-down list in the Machine Set window. See: Loading/Unloading Device |

| See: | Material |
| --- | --- |
|  | Use Setup Sheet |
|  | Setup Sheet |
|  | Output G93 |
|  | Percent After G50 |
|  | Output work size comment at the end of G92 command line |
|  | Use G42/G42 |
|  | Z Height M104Zx |
|  | Is G01 Continued |
|  | M108 After M104 Code |
|  | Loading / Unloading Device |
|  | Loading / Unloading Thickness M-Code |
|  | Loading / Unloading End Position M-Code |

## 13.11 M 108 After M104 Code

|  | Place a check mark in the check box, the system will output M108 after M 104 code. |
| --- | --- |
| Note: To output this code, you should select Work Chute as Process After method. |

| See: | Material |
| --- | --- |
|  | Use Setup Sheet |
|  | Setup Sheet |
|  | Output G93 |
|  | Percent After G50 |
|  | Output work size comment at the end of G92 command line |
|  | Use G42/G42 |
|  | Z Height M104Zx |
|  | Is G01 Continued |
|  | Unload Skeleton M Code |
|  | Loading / Unloading Device |
|  | Loading / Unloading Thickness M-Code |
|  | Loading / Unloading End Position M-Code |

## 13.12 Loading/Unloading Device

|  | This option allows you to output an M code for a Loading/Unloading Device. If the machine is equipped with a loading/unloading device, place a check mark in the LOADING/UNLOADING DEVICE (1=YES 0=NO) check box to output the M code. The system will output an M33 indicated as the NC code to the left. |
| --- | --- |
| Note: Make sure a loading/Unloading device is selected from the Tandem Device Type drop-down list in the Machine Set window. See: Loading/Unloading Device |

| See: | Material |
| --- | --- |
|  | Use Setup Sheet |
|  | Setup Sheet |
|  | Output G93 |
|  | Percent After G50 |
|  | Output work size comment at the end of G92 command line |
|  | Use G42/G42 |
|  | Z Height M104Zx |
|  | Is G01 Continued |
|  | Unload Skeleton M Code |
|  | M108 After M104 Code |
|  | Loading / Unloading Thickness M-Code |
|  | Loading / Unloading End Position M-Code |

## 13.13 Loading/ Unloading Thickness M-Code

Place a check mark in the Loading/ Unloading Thickness M-Code check box, and the system will output the thickness M code based on the pre-defined code settings.

Note:

To output the thickness M code, you must place a check mark in the LOADING/UNLOADING DEVICE (1=YES 0=NO) check box.

Example

| 1. | Specify the NC generate settings as follows. |
| --- | --- |
| 2. | Select Cycle Loader (ASR-CR, ASR-M) from the Tandem Device Type drop down list. See Loading/Unloading Device The material thickness is 1. |
| 3. | The system will output the M24 in the NC code. |

| See: | Material |
| --- | --- |
|  | Use Setup Sheet |
|  | Setup Sheet |
|  | Output G93 |
|  | Percent After G50 |
|  | Output work size comment at the end of G92 command line |
|  | Use G42/G42 |
|  | Z Height M104Zx |
|  | Is G01 Continued |
|  | Unload Skeleton M Code |
|  | M108 After M104 Code |
|  | Loading / Unloading Device |
|  | Loading / Unloading End Position M-Code |

## 13.14 Loading/ Unloading End Position M-Code

Place a check mark in the Loading/ Unloading End Position M-Code check box, and the system will output the End Position M code based on the pre-defined code settings.

Note:

To output the End Position M code, you must place a check mark in the LOADING/UNLOADING DEVICE (1=YES 0=NO) check box.

Example

| 1. | Specify the NC generate settings as follows. |
| --- | --- |
| 2. | Select Cycle Loader (ASR-CR, ASR-M) from the Tandem Device Type drop down list. See Loading/Unloading Device The blank sheet size is 2438*1219. |
| 3. | The system will output the M57 in the NC code. |

| See: | Material |
| --- | --- |
|  | Use Setup Sheet |
|  | Setup Sheet |
|  | Output G93 |
|  | Percent After G50 |
|  | Output work size comment at the end of G92 command line |
|  | Use G42/G42 |
|  | Z Height M104Zx |
|  | Is G01 Continued |
|  | Unload Skeleton M Code |
|  | M108 After M104 Code |
|  | Loading / Unloading Device |
|  | Loading / Unloading Thickness M-Code |

# Chapter 14: Process After

In the Process After window you can specify the methods to process the parts after the cutting process is finished. You may want to separate the parts from the sheet, process the part corners, keep joints or use work chute to retrieve parts or scraps, etc.

| To display the Process After window: |
| --- |
| 1. | Select a machine (such as EM-L) in the Dr. ABE main window. Click a preference button, such as Auto Sequence Preference, to display the Preference window. |
| 2. | In the Preference File pane, double-click the ProcessAfter icon to display the Process After window. |

| See | Process After Cutting Table |
| --- | --- |
|  | Joint |

## 14.1 Process After Cutting Table

After finishing cutting an object, specify the process after method for it according to associated condition.

Process After Cutting Table

| Column | Description |
| --- | --- |
|  | You can click the Process Type arrow button and select a process type from the drop down list. And then the table will list all the process after conditions of that type you have selected. |
| Object | Specify the object that the setting will be applied to. ( Inner, Outer, Open Path, All and Notch.) Select All, and settings will be applied to all the objects, including the open path, outer loop, inner loop and notch. See: Object |
| Process Type | The process method to process the object specified. The system will automatically decide the process method based on the Object type and Process After method you have selected. For example, if you select TK Station 1 in the Process column as the process after method, the system will automatically use Laser as the method to process the object you have specified. |
| X/Y | Specify the dimensions of the object. ( X, Y, R, CPX, Area, Width and Length) See: X/Y/R/CPX/Area/Length/With Explanation. |
| EQ | Specify the relationship between the option in X/Y column and the values in Value1/2. There are five options: <= (less than or equal to), >= (greater than or equal to), = (equal to), < (less than) and > (greater than). |
| Value 1/2 | Specify the reference dimension value. |
| Process | Specify a process after method for the objects that match the settings defined in the Process After Cutting table. |
| Joint | Keep joints after processing. |
| Chute 1/2 | Output work chute open/close command. This function is available after you set Workchute Information in the Peripherals of Machine Set window. Place a check mark in the Cut Slug to fit to Cut Plate/Work Chute check box to open associated panel. You can make detailed setting for cutting scraps. See Work Chute Information |
| Machine Stop | M00 is generated after the process if finished.. |
| Chute Tool | It is a kind of special tool used to perform the final hit, and the options in the Chute panel allow you to specify the settings for the special tool you have assigned to separate the part from the sheet. |
| None (Cut Plate) | The cut plate is a static device that is smaller than the work chute. Select this option and the system will cut the remnant sheet to ensure the sheet size is suitable to drop into the cut plate. |
|  | Note: To enable this option, you must place a check mark in the Cut Slug to fit to Cut Plate/Work Chute check box. See: Cut Plate |
| Drop Through | Select this option to do drop through process. |
| TK Station 1-5 | Specify TK device to perform take-out. This function is available after you set Workchute Information in the Peripherals of Machine Set window. See Work Chute Information |
|  | Note: To enable this function, you should place a check mark in the Yes/No check |
| None | The system will do nothing when the cutting process is finished |
| JointName | The name of the joint conditions |
| Z Value | The Z-axis value of the laser head after the work piece has been cut. The driver will generate M104 with the Z value. If no value is input, the system will use the default value--0. |
|  | Note: The settings in the Z Value column will not take effect unless the Z Height option in the NC Generate window is enabled. See: How to Output the Z Value. |

| See | Object |
| --- | --- |
|  | X/Y/R/CPX/Area/Length/With Explanation |
|  | How to Output the Z Value |

| See | Joint |
| --- | --- |

### 14.1.1 Object

There are five types of objects: Open Path, Outer, Inner, Notch and All. Click a cell in the Object column to display the drop-down list. Select the desired object type from the list.

| Option | Description |
| --- | --- |
| Open Path | As the following red patterns indicate, an open path does not create a closed shape. |
| Outer | An outer loop is the contour or perimeter of a part as the following red pattern indicates. |
| Inner | An inner loop is the contour or perimeter of a hole or pattern inside a part. |
| Notch | A notch is a cut on the outer loop |
| All | This option Includes all the open paths, outer loops and inner loops. |

| See: | X/Y/R/CPX/Area/Length/With Explanation |
| --- | --- |
|  | How to Output the Z Value |

### 14.1.2 X/Y/R/CPX/Area/Length/Width Explanation

| X is the dimension along the X-axis. |
| --- |
| Y is the dimension along the Y-axis. |
| R is the radius of the outer part perimeter. |
| CPX is a quotient. It is the total perimeter length divided by the overall rectangular perimeter. The following example illustrates the Cpx. calculation formula: |
| Total Perimeter = 560 | Total Rectangular = 400 |
| 560/400 = 1.4 |
| Cpx. = 1.4 |
| Area: is the area within the out part perimeter |
| Length: the longer side of the part |
| Width: the shorter side of the part |

| See | Object |
| --- | --- |
|  | How to Output the Z Value |

### 14.1.3 How to Output the Z Value

| 1. | Open the NC Generate window in the Preference File pane. |
| --- | --- |
| 2. | Place a check mark in the Z HEIGHT M104Zx (1=YES 0=NO) check box. The number in the right of the row will automatically change to 1. |
| 3. | Open the Laser Tool Assign window. |
| 4. | Define the Process after Cutting conditions as follows. |
| 5. | When machine finishes processing objects, it will raise the laser head by the height specified in the Z Value column. See: Process After Cutting Table |

| See | Object |
| --- | --- |
|  | X/Y/R/CPX/Area/Length/With Explanation |

## 14.2 Joint

In the Process After window, you can specify the conditions to control joint assignment. In this section, you can select the Fixed Position option to fix the joint position, or select Auto Position to let the system automatically assign joints based on the setting you have defined. What’s more, you can save your joint settings for future use.

| See | Fixed Position |
| --- | --- |
|  | Auto Position |
|  | Basic Joint Setting |
|  | Joint Type Table |
|  | Detail Settings |
|  | Joint Setting Condition |
|  | Cut Plate |

### 14.2.1 Fixed Position

In the joint section, select the Fixed Position option to fix the joint position.

To fix the joint position:

| 1. | Select the Fixed Position option to open the associated section as follows. |
| --- | --- |
| 2. | Move the cursor into the Joint Position work area. |
| 3. | Click along the pattern perimeter to decide the joint position. A red circle displays after each mouse click. The red circle represents the joint position. Click the red point again to remove joint. |

| Note: |  |
| --- | --- |
| 1. | If we specify the joint position as the following Picture A, when the system assigns joints to the pattern like Picture B, it will search for the joint position in the top middle, and then assign the proper joints based on the joint type priority. In this case, since micro joint has the highest priority, micro joints will be assigned to the pattern as follows. |
| 2. | If you select the Fixed Position option, you cannot define the joint quantity. But the quantity shown in the Min Joint QTY box will change accordingly each time you change the joints in the Search Position from area. |

### 14.2.2 Auto Position

In the joint section, select the Auto Position option to select a position from which the system will begin to assign the joint.

To specify the starting position to start joint assignment:

| 1. | Select the Auto Position option to open the associated section as follows. |
| --- | --- |
| 2. | Move the cursor into the Search Position from work area. |
| 3. | Click one corner to specify the position from which the system will start to assign joints. A red circle will display to indicate the starting position. Based on the Corner Joint settings in the Joint Detail Setting window, the system will search for the possible positions to assign the micro joints from the upper right corner |
| Note: |
| 1. | When the system searches for the possible positions to assign the micro joints from the upper right corner, and this searching process won’t stop until the searching result matches the Min Joint QTY settings. |
| 2. | Only when the searching result cannot match the Min Joint OTY settings, will the system start to consider the Wire Joint settings in the Joint Detail Setting window and start to search for the possible places to assign wire joints that are close to corner. |
| 3. | If the searching result cannot match the Min Joint OTY settings, the system will search for the possible places to assign wire joints. |
| 4. | If the result does not match the Min Joint OTY settings, No Process will be performed, in other words, no joints will be assigned, error displays in the Result View. |

### 14.2.3 Basic Joint Settings

If you select the Auto Position option, you can specify the basic setting to assign joints, such as the minimum joint quantity, the minimum distance between joints, and the maximum distance between the corner joints.

| See | Min Distance between Corner |
| --- | --- |
|  | Min Distance between Wire |
|  | Min Joint Qty |
|  | Max Distance between Corner Joint |

#### 14.2.3.1 Min Distance between Corner

Specify or select the minimum distance between the corner joints. If the distance between two corner joints is less than the value specified, the system will automatically remove one joint.

Example

| 1. | We will assign joints to a 100*80 part. |
| --- | --- |
| 2. | Select Joint as the process method. |
| 3. | Specify the basic joint settings as follows. |
| 4. | Eight joints will be assigned to the pattern as follows. |
| 5. | Type or select 90 in the Min Distance between Corner: text box. Only 6 joints will be assigned to the pattern. The joints on the top left and bottom right corners are removed. |
| 6. | Let’s change the joint search position as follows. |
| 7. | Only 6 joints will be assigned to the pattern. The joints on the top right and bottom left corners are removed. |

#### 14.2.3.2 Min Distance between Wire

Specify or select the minimum distance between the wire joints. If the distance between two wire joints is less than the value specified, the system will automatically remove one joint.

For example, if you specify the Min Distance as 10, but the pitch is only 8, then one joint will be removed. See the illustrations below.

Min Distance = 10, but Pitch = 8

One joint is removed.

Example

| 1. | We will assign joints to a 100*80 part. |
| --- | --- |
| 2. | Select Joint as the process method. |
| 3. | Specify the basic joint settings as follows. |
| 4. | Ten joints will be assigned to the pattern as follows. |
| 5. | Type or select 50 in the Min Distance between Wire: text box. Only 8 joints will be assigned to the pattern. Two wire joints are removed. |

#### 14.2.3.3 Min Joint Qty

Specify or select the minimum joint quantity.

Example

| 1. | We will assign joints to the following part. |
| --- | --- |
| 2. | Select Joint as the process method. |
| 3. | Specify the basic joint settings as follows. |
| 4. | Four joints will be assigned to the pattern as follows. |
| 5. | Type or select 8 in the Min Joint QTY: text box. |
| 6. | Eight joints will be assigned to the pattern as follows. |

#### 14.2.3.4 Max Distance for Corner Joint

Specify or select the maximum distance between corner joints. If the distance between two corner joints is greater than the value set in the Max Distance for Corner Joint text box, one more corner joint will be added among them in the case that there exist more corners.

Example

| 1. | We will assign joints to the following part. |
| --- | --- |
| 2. | Select Joint as the process method. |
| 3. | Specify the basic joint settings as follows. |
| 4. | Joints will be assigned to the pattern as follows. |
| 5. | Type or select 150 in the Max Distance for Corner Joint: text box, the system will add another joint automatically if there exists a corner between two corners. |

### 14.2.4 Joint Type Table

|  | Specify the priority of joint types. The joints of higher priority will be assigned first. You can select one joint type and click or button to change the priority. The joint type at the top of the table has the highest priority. |
| --- | --- |

### 14.2.5 Detail Settings

Besides the basic joint settings, you can click the Details button and the Detail Setting window displays. This window is where you can specify the detail setting of joints. Clicking tab let you toggle between difference panels. After you finish setting in any panel, click OK to save settings and return to the Process After screen. The panel you exit previously is the default panel next time you enter the Detail Setting window.

| See | Common Setting |
| --- | --- |
|  | Corner Joint Setting |
|  | Wire Joint Setting |
|  | Chute(L) Setting |
|  | Chute Setting |

#### 14.2.5.1 Common Settings

Click Common tab to open the Common panel and you can define the common joint assignment conditions.

| Option | Description |
| --- | --- |
| Ignore CAD Joint | If the joints were assigned to the parts during the CAD designing phase, select this option and the system will ignore the joint information, and assign joints based on the settings in Process After Cutting Table. Remove the check mark from the Ignore CAD Joint check box, if the joints were assigned to the parts during the CAD design phase, the system will use these joints, and this setting is of higher priority than the joint settings in Process After Cutting Table. |
|  | Example: |
|  | 1. | Load two different parts. Part A has 2 joints, while Part B has no joints. |
|  | 2. | Select the Joint option in the Process column. And Type 4 in the Min Joint OTY text box. |
|  | 3. | Select the Ignore CAD Joint option, and the system will assign joints to the parts as follows. |
|  | 4. | Remove the check mark from the Ignore CAD Joint check box, and the system will use the joints assigned during the designing phase and assign the joints to the parts as follows. |
| Center of Gravity has higher Priority | When you place a check mark in the Center of Gravity has Higher Priority check box, the system will consider the center of gravity of the part when assigning joints. |
|  | Example |
|  | 1. | Select the Joint option in the Process column. |
|  | 2. | And Type 4 in the Min Joint OTY: text box. |
|  | 3. | If you place a check mark in the Center of Gravity has Higher Priority check box, the part will be processed as follows. |
|  | 4. | If you remove the check mark from the Center of Gravity has Higher Priority check box, the part will be processed as follows. |
| Display Warning when Joints are Unbalanced | This function is Not available at this moment. |
| Range of Searching Joint Position | If Fix Position option is selected, type a value in the text box to specify the ratio of the part length, and the system will search the specified area from the position where joint is assigned and decide the joint position |
| Position Priority | Click the arrow button to open the list. You can select a position to place the joint from the list. |
| Long Side | Place joints on the length side of part. |
| Width Side | Place joints on the width side of part. |
| Longer Edge | Place joints on the longer side of two edges. |
| Notch Avoid Length | Specify the conditions to assign joints to the specified notch. If the width of a notch is less than or equal to the value you type in the text box, no joints will be assigned to the notch. |
|  | Example |
|  | 1. | Let’s take a part with a 5 x 51 notch for example. |
|  | 2. | Specify the Process After conditions as follows. |
|  | 3. | And Type 8 in the Min Joint OTY: text box. The system will assign joints as follows. One joint is assigned to the notch. Note: Normally, no tabs would be assigned to the notch. Only when the width of the notch is at least 10 times longer than the height, will the joint be assigned to the notch. |
|  | 4. | If you type 52 in the Notch Avoid Length: text box, the system will not assign any joint to the notch because the notch length is less than 52. |

#### 14.2.5.2 Corner Joint Settings

The Corner Joint panel allows you to specify the corner joint location conditions. You can specify the application of joints according to the corner type and arc size.

| Option | Description |
| --- | --- |
| 90 Degree Corner | Specify the corner joint location at the 90-degree corner. There are three options: Both Sides, One Side and None. |
| Both Sides | Place the joint on both sides of the corner. |
| One Side | Place the joint on one side of the corner. |
| None | When None is selected, no joint will be assigned to the corner. |
| Non-90 Degree | Specify the corner joint location at Non-90 degree corners. There are three options: One Side, Both Sides and None. |
| One Side | Place the joint on one side of the corner. |
| Both Sides | Place the joint on both sides of the corner. |
| None | When None is selected, no joint will be assigned to the corner. |
| Corner of Arc Line | Specify the corner joint location at the corner of arc and line. |
| One Side On One Line | Place the corner joint on the line side of the corner of arc and line. |
| Both Sides | Place the corner joint on both sides of the corner of arc and line. |
| None | When None is selected, no corner joint will be assigned. |
| No corner joint when line <= | If the length of one line is less than or equal to the value you type in the text box, no corner joints will be assigned to that line. |
|  | Example |
|  | 1. | A 100 x 80 part is used as an example. |
|  | 2. | Specify the settings in the Process After table as follows. And type 8 in the Min Joint QTY text box. |
|  | 3. | In the Detail Setting window, click the Common tab and select Width Side from the Position Priority: drop down list. In the Corner page, select One Side from the 90 Degree Corner: drop down list. And the system will assign joints as follows. |
|  | 4. | Type 90 in the No corner joint when line <=: text box. The width length of the pattern is only 80, and the corner joints will be removed from the wide side. And the system will assign the joints as follows. |
| Exclude C notch from Min Length Setting | If this option is selected, the C notch will be excluded from the minimum line joint assignment restriction. In other words, even though the C notch length is less than or equal to the value you defined in the No corner joint when line <=: text box, joint can be assigned on it. |
| No Corner Joint when Length of Arc <= | If the length of one arc is less than or equal to the value you type in the text box, no corner joints will be assigned to the arc. |
|  | Example |
|  | 1. | We will load a 100 x 80 rounded corner pattern with 15.7 radius corners. |
|  | 2. | Specify the settings in the Process After table as follows. And type 8 in the Min Joint QTY: text box. |
|  | 3. | In the Joint Detail Setting window, click the Common tab and select Width Side from the Position Priority: drop down list. In the Corner page, select Both Sides from the Corner of Arc&Line: drop down list. And set the No Corner Joint when Length of Arc <= to 0 And the system will assign joints as follows. |
|  | 4. | Type 16 in the No Corner Joint when Length of Arc <=: text box. And the system will assign the joints as follows. |
| No Corner Joint when Angle of Corner <= | This option allows you to specify the conditions to assign joints to the corner angle. If the angle of a corner is less than or equal to the value you type in the text box, no joints will be assigned to the corner. |
|  | Example |
|  | 1. | We will load the following part. |
|  | 2. | Specify the settings in the Process After table as follows. And type 3 in the Min Joint QTY: text box. |
|  | 3. | In the Joint Detail Setting window, In the Corner page, select Both Sides from the 90 Degree Corner: drop down list. Select Both Sides from the Non-90 Degree: drop down list. And type 0 in the No Corner Joint when Angle of Arc <=: text box. The system will assign joints as follows. |
|  | 4. | If you type 45 in the No Corner Joint when Angle of Corner <=: text box, the system will assign joints as follows. |

#### 14.2.5.3 Wire Joint Setting

The Wire Joint panel allows you to specify the wire joint location conditions.

| Option | Description |
| --- | --- |
| Wire Joint Close to Corner | The options in this section allow you to specify the conditions to assign wire joints close to the corner. |
| Offset Amount | The value in this text box determines the distance between the corner vertex and the place to assign wire joint. |
| Punch Length | Select this option, and the wire joint will be placed on the position with the tool length distance to the corner vertex. This function is available for punch machines only. |
| Corner with CR tool is Exception | Select this option, and there will be no joint offset when CR tool is used to process the CR line. |
| No Wire Joint when Line <= | If the length of one line is less than or equal to the value you type in the text box, no wire joints will be assigned to that line. |
|  | Example |
|  | 1. | We will load a 100*80 part. |
|  | 2. | Specify the settings in the Process After table as follows. And type 8 in the Min Joint QTY: text box. In the Joint Type table, set the Wire Joint the highest priority. |
|  | 3. | The system will assign the joints as follows. |
|  | 4. | Type 90 in the No Wire Joint when Line <=: text box. The system will assign joints as follows. No wire joints are assigned to the line that is less than the value specified. |
| No Wire Joint when Length of Arc <= | If the length of one arc is less than or equal to the value you type in the text box, no wire joints will be assigned to that arc. |
|  | Example |
|  | 1. | We will load the following part. |
|  | 2. | Specify the settings in the Process After table as follows. And type 5 in the Min Joint QTY: text box. In the Joint Type table, set the Wire Joint the highest priority. |
|  | 3. | The system will assign the joints as follows. |
|  | 4. | In the Joint Detail Setting window, click the Wire Joint tab, and type 80 in the No Wire Joint when Length of Arc <=: text box. The system will assign joints as follows. No wire joints are assigned to the arc. |
| No Wire Joint when Angle of Corner <= | If the angle of one arc is less than or equal to the value you type in the text box, no wire joints will be assigned to that arc. |
|  | Example |
|  | 1. | We will load the following part. |
|  | 2. | Specify the settings in the Process After table as follows. And type 6 in the Min Joint QTY: text box. |
|  | 3. | Type 0 in the No Corner Joint when Angle of Arc <=: text box. The system will assign joints as follows. |
|  | 4. | If you type 59 in the No Wire Joint when Angle of Corner <=: text box, the system will assign joints as follows. |

#### 14.2.5.4 Chute (L) Setting

In the Detail Setting window, click Chute (L) tab to open the Chute (L) panel to specify the conditions to control the work chute for laser process.

Chute Setting Options

| Option | Description |
| --- | --- |
| Left Margin (A) | Specify the minimum distance between the work chute margin and the part border. |
| Center of gravity offset (B) | Specify the offset amount of center of gravity. |
| After Open Work Chute | Select a machine status after work chute opens. There are three options: None, Machine Stop and Dwell. |
| Dwell Time | Select Dwell from the After Open: drop-down list, and type a value in the Dwell Time: text box to define the pause time for machine. The work chute will not be closed until the dwell time passed. |
| Cutting End Position | Specify the lead in position for part that is processed by using work chute. |
| Rotate Direction | Specify the rotate position |
| Material-taking Size | After cutting the sheet, the system will move the sheet first and then open the chute. Type a value in the boxes to define the move distance. You can type positive or negative value. Positive value indicates plus direction along X/Y axis, while negative value indicates minus direction. |
| X | Specify move distance along the X-axis. |
| Y | Specify move distance along the Y-axis. |
| Rotate Part for Outer Loop Using Chute | Place a check mark in the check box and system will rotate part that is processed by using work chute during the nesting process. |

#### 14.2.5.5 Chute Setting

Some special tools can work as the chute tools to perform the final hit, and the options in the Chute panel allow you to specify the settings for the special tool you have assigned to separate the part from the sheet.

| Option | Description |
| --- | --- |
| Cut X | The dimension of the chute tool in the X-axis. |
| Cut Y | The dimension of the chute tool in the Y-axis. |
| Offset Y | The distance from the center of the die to the position of the final hit. |
| Tool Name | The name of the chute tool. The name of the chute tool should exactly match the name of the special tool in the Tool Inventory. |

### 14.2.6 Joint Setting Conditions

In the Joint panel, you can specify the joint settings and save the information for future use. You can also name your joint setting conditions and make modifications.

If you select Joint as the process after method, you can click the arrow button to display all the predefined conditions, select one condition and click Apply to apply the joint settings.

To name a new joint setting condition, click New and type the name in the text box.

To save the joint setting conditions, click Save.

To delete a joint setting condition, select one joint condition from the drop down list and click Delete.

### 14.2.7 Cut Plate

Select None (Cut Plate) from the drop-down list of the Process to open the Cut Plate/Work Chute panel

| Option | Description |
| --- | --- |
| Cut Slug to fit to Cut Plate/Work Chute | Place a check in the Cut Slug to fit to Cut Plate/Work Chute check box, the system will cut the remnant sheet to ensure the sheet size is suitable to fall into the work chute |
| Cutting Method | Specify the cutting method. There are four types of cutting methods. |
|  | Vertical cutting |
|  | Horizontal cutting |
|  | Cross cutting |
|  | Cup -shape cutting (Forming down) |
| Lead In Method | Specify the method of lead in. There are four types of lead in method. |
|  | Central pierce |
|  | Pierce without lead in |
|  | Pierce with lead in |
|  | Pierce with lead in that has a radius |
| A: Max Size for Slug(X Direction) | The maximum cutting size along the X-axis direction |
| B: Max Size for Slug(Y Direction) | The maximum cutting size along the Y-axis direction |
| C Space for Lead In | The distance between the pierce point and the perimeter of the remnant sheet. |
|  | Note: Cup-shape cutting and central pierce can’t be selected together. |

Detailed description of Cut Slug to fit to Cut Plate/Work Chute panel

| References | A: Max Size for Slug (X Direction) C: Space for Lead In | B: Max Size for Slug (Y Direction) C: Space for Lead In | A: Max Size for Slug (X Direction) B: Max Size for Slug (Y Direction) C: Space for Lead In | A: Max Size for Slug (X Direction) B: Max Size for Slug (Y Direction) C: Space for Lead In |
| --- | --- | --- | --- | --- |

For example:

| 1. | Take the following part as an example: |
| --- | --- |
| 2. | Select relevant options and specify relevant values in the Process After Cutting panel. |
| 3. | Place a check in the Cut Slug to fit to Cut Plate/Work Chute check box. Click cross cutting in Cutting Method and pierce with lead in Lead In Method. Click Apply button to save the setting. |
| 4. | The system will cut slug the holes according to the following processes. |

# Chapter 15: Peripherals

The options in the Peripherals window allow you to specify the parameters for the peripherals of a machine. In the Dr. ABE main window, select a machine from the machine list and click one preference button to open the Preference window. In the Preference File pane, double-click the Peripheral icon to open the Peripherals window. The window consists of six panels: MJC, IJP, Parts Removal Sequence, Take Out, MJC/IJP Sequence and Schedule.

| See: | MJC |
| --- | --- |
|  | IJP |
|  | Parts Removal Sequence |
|  | Take Out |
|  | MJC/IJP Sequence |
|  | Schedule |

## 15.1 MJC

MJC is an acronym for Micro Joint Cutter. The MJC device is used to remove the micro joints after the process is complete. You can define the MJC settings in the following panel.

| See: | MJC Setting |
| --- | --- |
|  | Laser Joint |

| See: | IJP |
| --- | --- |
|  | Parts Removal Sequence |
|  | Take Out |
|  | MJC/IJP Sequence |
|  | Schedule |

### 15.1.1 MJC Setting

|  | The MJC device is used to remove the microjoints after the processing is completed. The MJC data is saved as a *.sy2 file with the IJP data. Place a check mark in the Yes/No check box to enable the MJC settings. |
| --- | --- |
|  | Note: You must first enable the MJC device option in the Machine Set window before you can use this option. |

| To enable the MJC device function: |
| --- |
| 1. | In the Dr. ABE main window, click the Machine Setting button to open the Machine Set window. |
| 2. | Click the desired machine, such as EM-L in the Tree View pane to display the subfolders of the machine, and select MJC in the Peripherals subfolder. |
| 3. | Click the Edit button on the toolbar. The MJC options become available for editing. |
| 4. | Place a check mark in the MJC Yes/No check box to enable the MJC device function. |

| See: | Laser Joint |
| --- | --- |

### 15.1.2 Laser Joint

The Laser Joint cannot be cut utilizing the normal method because there is no space to insert the cutter. The Laser Joint requires a pierce cutout that is greater than the cutter in the X and Y dimension to insert the cutter. The Laser Joint panel allows you to specify the cutout dimensions.

|  | A cutout is required to insert the cutter. |
| --- | --- |
|  | The dimensions of Cutter X and Cutter Y. |

| See: | MJC Setting |
| --- | --- |

## 15.2 IJP

IJP is an acronym for Ink Jet Printer. The IJP device is used to print part information on the parts. The IJP data is saved as a *.sy2 file with the MJC data. In the IJP panel, you can specify whether to print the part name, the comment, the part size, the due date, the process date, etc.

| See: | IJP Setting |
| --- | --- |
|  | IJP Position |
|  | IJP Strings |

| See: | MJC |
| --- | --- |
|  | Parts Removal Sequence |
|  | Take Out |
|  | MJC/IJP Sequence |
|  | Schedule |

### 15.2.1 IJP Setting

|  | The options in the IJP Setting section allow you to enable the IJP function and to select the IJP device. |
| --- | --- |
|  | Note: You must first activate the IJP Yes/No option in the Machine Set window before you use this option in the IJP panel. |
|  | Option | Description |
|  | Yes/No | Place a check mark in the Yes/No check box to enable the IJP function. |
|  | No | Select the IJP device you want to use from the No drop-down list. Usually, you can specify three IJP devices in the Machine Set window. Each device has its own IJP information, such as the Maker, the Max String Size, X/Y and the Max String Number. |

To enable the IJP device function:

| 1. | Click the Machine Parameter button to open the Machine Set window. |
| --- | --- |
| 2. | Select a machine, such as EM-L, and click the IJP item under Peripherals in the Tree View pane to display the IJP panel. |
| 3. | Click the Edit button to edit the IJP options. |
| 4. | Place a check mark in the IJP Yes/No check box to enable the IJP device function. |

| See: | IJP Position |
| --- | --- |
|  | IJP Strings |

### 15.2.2 IJP Position

| The options in the IJP Position section allow you to specify the position of the IJP. You can allow the system to automatically calculate the position or specify a fixed position for the IJP device. |
| --- |
| Option | Description |
| Auto | If you select Auto, the system will calculate and determine the position to print the IJP information automatically. Click the rectangle to specify the IJP printing position. The selected rectangle will become green. |
| Fix Position | Select Fix Position to specify a fixed position to print the IJP information. |
| Position X | Type the X coordinate for the fixed position. |
| Position Y | Type the Y coordinate for the fixed position. |

| See: | IJP Setting |
| --- | --- |
|  | IJP Strings |

### 15.2.3 IJP Strings

| The options in the IJP Strings section allow you to specify the items you want to print on the part. Double click an item in the list to add it to the text box below. Each item that you select will be printed on the part. You can also type the common part information in the text box. |
| --- |
| Option | Description |
| Part Name | Print the part name. |
| Comment | Print the part comment. |
| Size of Part | Print the part size. |
| Due Date | Print the due date of the part. |
| Process Date | Print the process date of the part. |
| User #1 - User #5 | Print User #1 to User #5 that you previously specified in the Nesting Plan window. Please refer to User Define for details of these items. |
| Line Feed | The Line Feed code is used to divide strings into several rows. The Line Feed code is specified in the Machine Set window. |

| See: | IJP Setting |
| --- | --- |
|  | IJP Position |

## 15.3 Parts Removal Sequence

| The options in the Part Removal Sequence panel allow you to specify the sequence to take out parts. |
| --- |
| Option | Description |
| Start Position/Direction | Click an arrow in the Start Point/Direction section to specify the starting point and direction to take out parts. |
| Repositioning Area Direction | Specify the reposition direction by selecting X or Y option from the drop-down list. |
| One Direction | Place a check mark in the One Direction check box, and the system will always take out the parts in one direction. |
| Width for Sequence | Place a check mark in the Width for Sequence check box and type a value in the text box to divide the process area into equal smaller areas. The system will take out the parts in the first area and then the adjacent area based on the settings defined in the Start Point/Direction section. |
| See: | MJC |
|  | IJP |
|  | Take Out |
|  | MJC/IJP Sequence |
|  | Schedule |

## 15.4 Take Out

The options in the Taking Out section allow you to specify the conditions to remove parts and stack them on a storage table.

| See: | Taking Out Conditions |
| --- | --- |
|  | Stack Distance |
|  | Taking Out |

| See: | MJC |
| --- | --- |
|  | IJP |
|  | Parts Removal Sequence |
|  | MJC/IJP Sequence |
|  | Schedule |

### 15.4.1 Taking Out Conditions

| The options in the Taking Out Conditions section allow you to specify the axis movement speed of the taking out device. |
| --- |
| Option | Description |
| Taking Out On/Off | Place a check mark in the Taking Out On/Off check box to enable the Taking Out options. |
| Laser Z Axis Reference Point | Specify the height that the laser head is raised after the final hit is performed. For example, if you type 100 in the text box, and the system will generate Z100 in the NC code. |
| Cutting is Divided | Select this option, and the system will output an M code (For example M383) to instruct the machine to vacuum the part first and then perform the last cutting process in the Y direction. Remove the check mark from the check box, and the system will output an M code (For example M384) to instructs the machine to perform the last cutting process in both X and Y-axis and then vacuum the part. See: Take Out Information |
| Prevent from dropping to the cutting plate | Place a check mark in the check box and input a value in the Part Size<=: text box. The system will prevent the part dropping to the cutting plate if part size is smaller than the value you input. |
| Part Size<= | Specify the part size to execute the above function of preventing part from dropping to the cutting plate. |
| Offset Amount | Specify the offset amount of lead in to execute the above function of preventing part from dropping to the cutting plate. |

### 15.4.2 Stack Distance

| The options in the Stack Distance section allow you to specify the part spacing and the stacking border for stacking parts on the table. |
| --- |
| Option | Description |
| Auto Stack On | Place a check mark in the Auto Stack On check box to perform the automatic stacking process. |
|  | Note: To perform the automatic stacking process, please enable the TK option in the Machine Set window and the Peripherals window. You must also select one option from Station1-Station5 in the Process column of the Process after Cutting table in the Process After window. |
| The Balance of One Table | Select this option and the machine will consider the table balance. This option is not available for the laser machines. |
| Stacking Scheme Type | Specify the stacking pallet type number. There are four types available. The stacking scheme type information will be saved in the *.sy2 file. |
| X= Y= | Type a value in the text box to specify the spacing between the parts in the X and Y directions. |
| L = R = U = B = | Type a value in the text box to specify the distance between the stacking border and the table edge. |

Example

| 1. | There are three sheets you want to stack. |
| --- | --- |
| 2. | If you remove the check mark from the Auto Stack On check box, the parts on one sheet will be stacked on one table. The parts on the three sheets will be stacked on three tables. |
|  | If you place a check mark in the Auto Stack On check box, the parts on the three sheets will be stacked on one table. The system will try to stack as many parts as possible on the table. |

### 15.4.3 Taking Out

|  | The TK uses vacuum cups or magnets to take out parts. You can use the vacuum system to remove both ferrous and non-ferrous materials, but you can only use magnets to remove ferrous materials. The Taking Out section allows you to specify the ferrous material types that the TK can take out. |
| --- | --- |

Example

| 1. | Click the Select from Mat. Parameter button to display the Material Type window. |
| --- | --- |
| 2. | Select a material type by placing a check mark in the Material Type check box. |
| 3. | Click OK to continue. |
| 4. | In the Taking Out section, you can right-click the row header and select New from the shortcut menu. A new blank row is added to the end of the Material Type: drop-down list, and you can type the material name in it. |
| 5. | To delete a material type, just select a material type, right-click to open the shortcut menu, and select Delete. |

## 15.5 MJC/IJP Sequence

| The options in the MJC/IJP Sequence panel allow you to determine the MJC/IJP sequence in relation with the part layout. |
| --- |
| Option | Description |
| Start Position/Direction | Click an arrow in Start Point/Direction section to specify the MJC/IJP starting point and processing direction. |
| Width for Sequence | Place a check mark in the Width for Sequence check box and type a value in the text box to divide the process area into equal smaller areas. The system will perform MJC/IJP process in the first area and then the adjacent area based on the settings defined in the Start Point/Direction section in the panel. |

| See: | MJC |
| --- | --- |
|  | IJP |
|  | Parts Removal Sequence |
|  | Take Out |
|  | Schedule |

## 15.6 Schedule

The options in the Schedule panel instruct the arms to change the pallet when the machine is ready to process a new sheet. You can place a check mark in the Output accumulation pallet exchange instruction check box, and select First Line or Last Line from the drop-down list to create a pallet exchange flag when the system registers the schedule to the SDD database.

Example

| 1. | You want to nest four sheets in a schedule. |
| --- | --- |
| 2. | If you remove the check mark from the Output accumulation pallet exchange instruction check box after defining the Schedule Name and saving the schedule to the SDD database, the system will output 0 in the UPSpcfx column: |
| 3. | If you place a check mark in the Output accumulation pallet exchange instruction check box and select First Line from the drop-down list to the right: |
|  | The system will output 1 in the first line of the UPSpcfx column after you define the Schedule Name and save the schedule to the SDD database. |
| 4. | If you place a check mark in the Output accumulation pallet exchange instruction check box and select Last Line from the drop-down list to the right: |
|  | The system will output 1 in the last line of the UPSpcfx column after you define the Schedule Name and save the schedule to the SDD database. |

| See: | MJC |
| --- | --- |
|  | IJP |
|  | Parts Removal Sequence |
|  | Take Out |
|  | MJC/IJP Sequence |

# Chapter 16: Group

The Group window allows you to set the Grouping Priority for parts.

You can also specify the group conditions to process Prototype, TK, and Filler Parts.

To open the Group window:

In the Preference window, select a punch machine (e.g. EM-L) and double-click the Group icon to display the Group window.

| See: | Grouping Priority |
| --- | --- |
|  | Prototype Condition |
|  | TK Process Type |
|  | Filler Parts |

## 16.1 Grouping Priority

The options in the Grouping Priority section allow you to specify the conditions to group parts during the nesting process.

| Option | Description |
| --- | --- |
| Grouping Priority | Select one option from the Grouping Priority: drop-down list to specify the grouping condition. |
| Process Date | The system will group the parts according to the process date. Parts of different process dates will be processed on different sheets. |
| Due Date | The system will group the parts according to the due date. Parts of different due dates will be processed on different sheets. |
| Give Higher Priority to Product Unit | The system will group the parts in the same assembly and process them together. |
| Give Higher Priority to Prototypes | The system will process prototypes first, and then the other parts on other sheets. |
| None | Parts will not be grouped during the nesting process. |
| Strictly Enforce Grouping Priority | Place a check mark in this check box to enable the system strictly apply the grouping priorities that you have defined. Only the parts that meet the same grouping conditions will be processed on the same sheet. Note: The check mark is placed in the check box by default. The grouping priority will NOT take effect when the check mark is removed. |
| Give Higher Priority to Group of Small Parts | As a rule, the system will always nest the larger parts before the smaller ones. If you place a check mark in this check box, the system will nest the smaller parts first, and ignore the priority settings you made in the Nesting Plan. See Priority under Nesting for details. |

Example:

| 1. | In the four parts below, Part A, C, and D have the same process date, while Part B has a later one. |
| --- | --- |
| 2. | In the Group window, select Process Date from the Grouping Priority: drop-down list and make sure a check mark is in the Strictly Enforce Grouping Priority: check box. |
| 3. | Click the Auto Execute button to perform the nesting process. As in the result, the parts with the earlier process date (Part A, C, D) are laid out on the first sheet, and Part B with a later process date is laid out on the second sheet. Note: On the first sheet, the larger parts are laid out first. |
| 4. | In the Group window, select Process Date from the Grouping Priority: drop-down list and place check marks in both the Strictly Enforce Grouping Priority: check box and the Give Higher priority to Group of Small Parts: check box. |
| 5. | Click the Auto Execute button to perform the nesting process. As in the result, now the parts with the same process date are still laid out on the first sheet, however, the smaller parts are laid out prior to the bigger ones. Part B is still laid out on the second sheet due to its later process date. |

| See: | Prototype Condition |
| --- | --- |
|  | TK Process Type |
|  | Filler Parts |

## 16.2 Prototype Condition

The options in the Prototype Condition section allow you to define the prototype conditions so as to decide whether to put the prototype parts into the total part quantity or not.

| Option | Description |
| --- | --- |
| Nest One Product Unit | During the nesting process, the prototype quantity will be the quantity of the parts in the assembly instead of the quantity specified in the Part Properties window. |
| Prototype Quantity is Included | The prototype quantity will be included in the total part quantity. The quantity of the prototype is the exact quantity you set in the Parts Properties window. |
| Prototype Quantity Extra | The prototype quantity will be excluded from the total quantity of parts. The quantity of the prototype is the exact quantity you set in the Parts Properties window. |

Example:

| 1. | Select Nest One Product Unit in the Prototype Condition section. |
| --- | --- |
| 2. | In the Sequence panel of the Sequence preference window, place a check mark in the Machine Stop for Prototype: check box and also make sure the Output only one M00: check box remains empty so that M00 command line will be generated in the NC code for each completed prototype part. |
| 3. | Open the Nesting Schedule window. Specify the assembly lot, part quantity and prototype quantity as follow. |
| 4. | Click the Auto Execute button to perform the nesting process. As in the result, the system laid out 6 parts in 3 lots. 2 parts are treated as prototypes as 2 M00 command lines indicated in the NC code. The prototype quantity is exactly the same as the part quantity of each assembly. |
| 5. | Select Prototype Quantity is Included in the Prototype Condition section. |
| 6. | Click the Auto Execute button to perform the nesting process. As in the result, the system also laid out 6 parts in 3 lots, but only 1 part among them is treated as the prototype as only 1 M00 command line indicated in the NC code. |
| 7. | Select Prototype Quantity Extra in the Prototype Condition section. |
| 8. | Click the Auto Execute button to perform the nesting process. As in the result, an extra part is laid out as the prototype in addition to the 6 parts in 3 lots. 1 M00 command line is generated in the NC code to indicate that 1 prototype is processed. |

| See: | Grouping Priority |
| --- | --- |
|  | TK Process Type |
|  | Filler Parts |

## 16.3 TK Process Type

The options in the TK Process Type section allow you to specify how to layout micro-joint-parts and TK carry-outable parts in sheets.

Note:

This section is only available when the punch machine is equipped with TK device.

| Option | Description |
| --- | --- |
| Put a frame on a micro-joint-part | This option is NOT available for EM machines currently. |
| Layout a micro-joint-part in the different sheet | Layout micro-joint-parts and TK-parts on the different sheet. |
| Layout a micro-joint-part and TK-part in the same sheet. | Layout micro-joint-parts and TK-parts on the same sheet as usual. |

| See: | Grouping Priority |
| --- | --- |
|  | Prototype Condition |
|  | Filler Parts |

## 16.4 Filler Parts

The options in the Filler Parts section allow you to specify the conditions for filler parts.

The system will attempt to nest the filler parts on the sheet to improve the sheet utilization. You can define the filler parts in the Parts Properties window.

Note:

For sheets that can be reused, the filler parts will not be assigned.

| Option | Description |
| --- | --- |
| None | No filler part will be nested even though you have specified filler parts in the Parts Properties window. |
| Quantity Specified for Each Part | The quantity of the filler parts will be decided based on the filler parts defined for each part. When the system is nesting the filler parts, it will ignore the lots. Note: The maximum filler part quantity for each part will not exceed the defined quantity. |
| Total Quantity for the Assembly | The quantity of the filler parts will be decided based on the filler parts defined for each part and the assemblies. Note: The maximum filler part quantity for each part will not exceed the filler quantity x assembly quantity. |
| Give Equal Priority to all Filler Parts | All the filler parts, ignoring the size and priority you specified in the Parts Properties window, will have the same priority. Note: This function is currently unavailable. |

To specify filler parts:

| 1. | Open the Nesting Schedule window. You can define the filler part quantity by typing in the Filler Quantity column. |
| --- | --- |
| 2. | You can also specify filler part quantity in the Parts Properties window by typing in the Part: text boxes. The filler part quantity is the difference of the right side value minus the left side value. As in the example below, the filler part quantity is 3. (5–2=3). |

To nest filler parts on sheets,

| 1. | Load Part A and Part B and specify the nesting schedule as follow. |
| --- | --- |
| 2. | Click the Auto Execute button to perform the nesting process. The parts will be laid out as follow. |
| 3. | Now type 1 in the Filler Quantity column for Part B in the Nesting Schedule window. |
| 4. | Select None in the Filler Parts section. |
| 5. | Click the Auto Execute button to perform the nesting process. The parts will be laid out as follow without change. Although we have specified 1 in the Filler Quantity column for Part B, no Part B is laid out as filler part in the empty space on the sheet because None is selected. |
| 6. | Now select Quantity Specified for Each Part in the Filler Parts section. |
| 7. | Click the Auto Execute button to perform the nesting process. The parts will be laid out as follow. 1 Part B is laid out as the filler part in the empty space on the sheet. The quantity of the filler parts is exactly the same as the quantity specified in the Nesting Schedule window. |
| 8. | Now type 2 in the Filler Quantity column for Part B in the Nesting Schedule window. |
| 9. | Select Total Quantity for the Assembly in the Filler Parts section. |
| 10. | Click the Auto Execute button to perform the nesting process. The parts will be laid out as follow. 4 Part B are laid out as the filler parts in the empty space on the sheet. The quantity of the filler parts is decided by the assembly lot quantity and the filler quantity part that you specified in the Nesting Schedule window. (2*2=4) |

| See: | Grouping Priority |
| --- | --- |
|  | Prototype Condition |
|  | TK Process Type |

# Chapter 17 Clearance

Clearance is defined as a gap or space between the punch and die. For example, if you are using a 10.3mm die with a 10mm punch, the clearance is 10.3mm-10mm=0.3mm. The clearance has a major effect on the quantity of the finished product as well as tool wear. Improper clearances may result in the excessive breakaway and tool wear, secondary shear and bur and damaged tooling.  Material thickness, types of material and types of tools being used should be all considered in establishing proper clearance. You can specify Clearance parameter in Clearance window.

| To open the Clearance window: |
| --- |
| 1. | Click the NC Generate Preference button on the main window to open the Preference window. |
| 2. | Select a punch machine (such as EM-L) in the Tree View pane, and then double-click the Clearance icon in the Preference File pane to display the Clearance window. |

| See: | Clearance Setting |
| --- | --- |

## 17.1 Clearance Setting

In the Clearance Setting table, you can directly type information in it to define the clearance for each material type. Click the last row in the table to expand a new row.

| Option | Description |
| --- | --- |
| Material | Type the material type here. |
| Thickness (Min-Max) | Type value in the cells to define the thickness range of this material type. |
| Clearance (Min-Max) | Type a value in the cell to define the clearance range of this material within the defined thickness range. Range: 0~999.999, Initial value: 0.0 |
| Clearance Selection (Min/Max) | If you place a check mark in the check box, the system will select tool within defined clearance range according to the following sequence: from tool of larger clearance to tool of smaller clearance. If you clear the check mark in the check box, the system will select tool within defined clearance range according to the following sequence: from tool of smaller clearance to tool of larger clearance. |
| Process Speed | You can select a process speed in the drop-down list. There are four options. F1 represents the highest speed. |

Example:

| 1. | Set the material clearance as follows: |
| --- | --- |
| 2. | There is a RE 110x6 in the tool inventory. If you do not set any die clearance for this tool, |
| 3. | the tool can be assigned to both kinds of material type. |
| 4. | Set 20 as the die clearance of this tool. |
| 5. | In this case, the tool RE 110x6 can be assigned to SECC but cannot be assigned to SPC. Another tool is assigned to SPC. |

# Chapter 18: Turret Layout

The Tool Inventory window lists the tools that are available for your machines. You can update your tool inventory as you purchase new tools or remove broken tools. You can import tools to update your tool inventory or modify the tool information to meet your needs.

To open the TurretLayout window

| 1. | Click one preference button on the Dr. ABE main window to open the Preference window. In the Tree View pane, click EM-L. |
| --- | --- |
| 2. | In the Preference File pane, double-click one turret file icon , such as, HA445E, to open the TurretLayout window. |

Note:

In the Preference File pane, if there are several turret layouts, you can right-click one turret layout file, and select Set Default and the system will use this turret layout file by default.

To create a Turret layout file

| 1. | In the Machine Set window, specify the turret type for the EM-L machine. See Turret Name |
| --- | --- |
| 2. | In the Tree View pane, right-click EM-L under My Preference, select New to Turret Layout Preference option to create a turret layout file. |
| 3. | A new turret layout file is created in the Preference File pane. |

Note:

- You can select New to Turret Layout(PDC) Preference to create a Turret Layout(PDC) file  in the Preference File pane.

- Before you create a Turret Layout (PDC) file, you must select a storage type for the machine. See: Storage Name

| See: | Import AP100 Turret Layout |
| --- | --- |
|  | TurretLayout Window |
|  | Turret Section |

## 18.1 Import AP100 Turret Layout

You can select EM-L under My Preference in the Tree View pane, right-click and select Import Turret layout to import a turret layout file.

Import the Turret Layout files for the specified machine

| 1. | In the System Setting window, select SDD Parameter Automatic Download and type Apserver in the Data Server PC(AP100/PCL): text box to specify the PC to download the parameters. See: Parameter Processing |
| --- | --- |
| 2. | In the Tree View pane, select EM-L under My Preference. Right-click and select Import Turret Layout. |
| 3. | Click OK to continue. |
| 4. | In the ToolInventory Setting window, select HA445 and click OK to continue. You can select more than one turret file at a time. |
| 5. | A turret layout file HA445 is imported to Dr ABE blank. |

| See: | TurretLayout Window |
| --- | --- |
|  | Turret Section |

## 18.2 TurretLayout Window

The TurretLayout window is a graphical representation of all the tools and stations available for your machine.

The turret section displays the information for each station, such as Station, Range, Shape, Size X, Size Y, etc.  You can add tools to the turret. You can display the stations by Shape or by Range. See: Turret Type

Note:

You can also display the turret station (PDC) in this window. See: Turret Type (PDC)

The Tool Inventory section lists the information for each tool in the inventory, such as Shape, Size, Type, Air Blower, etc. You can display the tools by Shape or by Range. You can import tools to update your inventory or modify the tool information to meet your needs. See: Tool Inventory

| See: | Import AP100 Turret Layout |
| --- | --- |
|  | Turret Section |

## 18.3 Turret Section

The turret section displays the information for each station, such as Station, Range, Shape, Size X, Size Y, etc.  You can add tools to the turret. You can display the stations by Shape or by Range.

About the details for Turret (PDC), please refer to Turret Type (PDC)

| See: | Turret Section Toolbar |
| --- | --- |
|  | Range and Shape buttons |
|  | View Buttons |
|  | T No. |
|  | Search Stations |
|  | Turret Picture |
|  | Turret Station List |

| See: | Import AP100 Turret Layout |
| --- | --- |
|  | TurretLayout Window |

### 18.3.1 Turret Section Toolbar

The buttons on the toolbar allow you to display the stations based on the shape and range. You can select the method to display the Turret, Turret list, or Inventory.

| See: | Range and Shape buttons |
| --- | --- |
|  | View Buttons |
|  | T No. |
|  | Search Stations |
|  | Turret Picture |
|  | Turret Station List |

### 18.3.2 Range and Shape buttons

Click a range buttons to display turret stations of that range. The  button is selected by default and stations of all the ranges will be displayed.

Click a shape button to display the tools of that shape. The  button is selected by default and tools of all the shapes will be displayed.

| See: | Turret Section Toolbar |
| --- | --- |
|  | View Buttons |
|  | T No. |
|  | Search Stations |
|  | Turret Picture |
|  | Turret Station List |

### 18.3.3 View Buttons

|  | Option Description Turret Display the turret. Turret Inventory Display the turret and tool inventory. Inventory Display the tool inventory. Turret List Display the list of turret stations. Turret Picture + list Display the turret illustration and the list of the turret stations. Turret Picture Display the turret illustration. |
| --- | --- |

| See: | Turret Section Toolbar |
| --- | --- |
|  | Range and Shape buttons |
|  | T No. |
|  | Search Stations |
|  | Turret Picture |
|  | Turret Station List |

### 18.3.4 T No.

|  | In the T No. text box, you can type the number of the station you want to locate. Click the T NO. arrow button to display the drop- down list. Option Description All Display all the stations Blank Station Display all the stations without tools added. Station with tool Display all the stations with tools added. Fixed Station Display all the fixed stations. Note: If a station with a tool assigned is set to Fixed, no other tools are allowed to assign to it. If an empty station is set to Fixed, no tools are allowed to assign to it. Free Station Display all the free stations |
| --- | --- |

| See: | Turret Section Toolbar |
| --- | --- |
|  | Range and Shape buttons |
|  | View Buttons |
|  | Search Stations |
|  | Turret Picture |
|  | Turret Station List |

### 18.3.5 Search Stations

Click Search button  to open the Advanced Filter window. The options in this window allow you to filter the results by Name, Shape, Range, etc. For example, if you type a C in the Range text box, and the system will search the current turret and list the stations that are installed tools of C range.

| See: | Turret Section Toolbar |
| --- | --- |
|  | Range and Shape buttons |
|  | View Buttons |
|  | T No. |
|  | Turret Picture |
|  | Turret Station List |

### 18.3.6 Turret Picture

|  | The turret illustration shows the turret layout. The system uses different colors to show the station status. The pink color indicates the station has been assigned a tool. The green color indicates this station has been assigned candidate tools. The orange color indicates a tool has been assigned to the station, and meanwhile candidate tools are also assigned to the same station. The blue color is used to highlight the station being selected. You can specify the turret layout in two methods, Turret Load Setting and Effective Station Setting. |
| --- | --- |

| Option | Description |
| --- | --- |
| Turret Load Setting | Specify the turret tools by using the Tool Inventory. See: Assign tools in the Turret Load Setting mode |
| Effective Station Setting | Specify tools that will be used with higher priority in the turret station. See: Assign tools in the Effective Station Setting mode |

| See: | Assign tools in the Turret Load Setting mode |
| --- | --- |
|  | Assign tools in the Effective Station Setting mode |

| See: | Turret Section Toolbar |
| --- | --- |
|  | Range and Shape buttons |
|  | View Buttons |
|  | T No. |
|  | Search Stations |
|  | Turret Station List |

#### 18.3.6.1 Assign tools in the Turret Load Setting mode

| 1. | In the TurretLayout window, select Turret Load Setting, and then select one tool in the tool inventory section. |
| --- | --- |
| 2. | Drag and drop the selected tool to the desired station in the station list, for example, Station 217. |
|  | The selected tool is assigned to Station 217. |
| 3. | You can also directly drag and drop the tool to the desired station in the Turret picture. For example, Station 217. |
|  | As the following picture indicates, the selected tool is assigned to Station 217. |

Note:

Tools can only be assigned to the stations of the same ranges unless adapter is used.

| See: | Assign tools in the Effective Station Setting mode |
| --- | --- |

#### 18.3.6.2 Assign tools in the Effective Station Setting mode

| 1. | In the TurretLayout window, select Effective Station Setting, and then select one tool in the tool inventory section. |
| --- | --- |
| 2. | Drag and drop the station to the desired station in the turret station list. For example, Station 107, If you drop the tool to the row marked with an asteroid, the selected tool will be regarded as one candidate tool. You can assign more than one candidate tool to the same station. |
|  | Note: You can right-click one candidate tool, and select Remove Effective Setting to remove the candidate tool from the station. You can right-click one tool in the Tool Inventory list and select Assign Station to display the Station Selection window, click to select one station, and the selected tool be treated as the candidate tool for that station. |
| 3. | You can drag and drop a tool to the yellow row of the desired station, for example, Station 107, to add the tool to that station. |
| 4. | You can also directly drag and drop the tool to the desired station in the Turret picture. For example, Station 217. |
| 5. | As the following picture indicates, the selected tool is assigned to Station 217. |

| See: | Assign tools in the Turret Load Setting mode |
| --- | --- |

### 18.3.7 Turret Station List

The turret station lists the detailed information for each station, such as the station range, dead zone range, etc. You can display the stations by Station Range, select the items to display, or modify the station dead zones, etc. See: Turret Type Window Items

In the turret station list, right click to display the shortcut menu.

| Option | Description |
| --- | --- |
| Remove Tool | Select this option to remove the tool from the station. |
| Set Fix | Select this option to set the fix. |
| Remove Fix | Select this option to remove the fix. |
| Assign Station | Assign a turret station to the selected the storage on PDC. See: Assign Station to a Storage |
| Detach Station | Break the link between the turret station and the storage on PDC. |
| Remove Effective Setting | Remove the candidate tools from the selected stations. |

Assign Station to Storage

| 1. | In the Preference window, double-click one Turret Layout (PDC) icon in the Preference File pane to open the TurretLayout window. |
| --- | --- |
| 2. | In the In the turret station list, select Storage 601, and right click to display the shortcut menu. |
| 3. | In the Assign Station window, select Station 107 and click OK to continue. |
| 4. | As you can see Station 107 is assigned to Storage 601. |
|  | Note: You can select Storage 601, right-click and select Detach Station to break the link between Station 107 and Storage 601. |
| See: | Turret Section Toolbar |
|  | Range and Shape buttons |
|  | View Buttons |
|  | T No. |
|  | Search Stations |
|  | Turret Picture |

# Chapter 19 Dead Zone

The Dead Zone window lists all the available station ranges, and you can add, delete or modify the station ranges. The station range will be considered during the sequencing. If a tool hit is too close to the clamps, and the tool guide might collide with the clamps, repositions will occur.

To open the Dead Zone window,

| 1. | Click any preference button in the main window to display the Preference window. |
| --- | --- |
| 2. | In the Tree View, select Dead Zone under Public to display the Dead Zone icon in the Preference File pane. |
| 3. | Click the DeadZone icon to open the Dead Zone window. |
|  | Option Description DZNo The number of the dead zone range. X Size of Range The X dimension of the dead zone range. Usually, it is the diameter of the guide. Y Size of Range The Y dimension of the dead zone range. Usually, it is the diameter of the guide. |
| 4. | You can right-click any where in the window and select Append to add a new range. And you can select Delete to delete the range you have highlighted. |

| See: | Dead Zone of the Station |
| --- | --- |

## 19.1Dead Zone of the Station

The dead zone of each station is different from the clamp dead zone specified in the Machine Set window. You can determine whether the system will perform reposition to prevent a tool hit or cutting path from entering the dead zone.

Example

| 1. | In the Preference window, select Turret Type under Public, and double-click one turret type (e.g. HA445E) in the Preference File pane to display the Turret Type window. |
| --- | --- |
| 2. | The Turret Type window lists the detailed station information, such as Station, Range, Dead zone range, etc. |
|  | Note: You can select one station, right-click and select Append Dead Zone from the shortcut menu. In the DeadZone window, select one station range and click OK. The selected station range will be applied to the station specified. |
| 3. | Let’s take Station 224 for example. We notice that the Y dimension of the Station 224 (DZY) or the guide diameter is 116.665. If the tool in this station is assigned to process a pattern. To prevent the tool guide colliding with the clamps, the minimum distance of the tool hit center from the material edge will be DZ Y/2 + Clamp Length. In this case, the minimum distance will be DZ Y/2 + Clamp Length=116/2 + 10=68. See: Clamp Information |
| 4. | In the Preference window, select a combo machine (e.g. EML), and double-click the Sequence icon to display the Punch Sequence window. |
| 5. | In the Punch Sequence window, click the Clamp Avoidance tab. |
| 6. | Place a check mark in the Avoid DZ check box. And the system will consider the dead zone area during the sequencing. |
| 7. | If the distance from the tool hit center to the material edge is less than 68, as the following left picture shows, the system will automatically perform a reposition during the process. |
|  | Before Reposition | After Reposition |
| 8. | If the distance from the tool hit center to the material edge is more than 68, as the following picture shows, no reposition will occur. |

# Chapter 20: Schedule

The Schedule window allows you to specify names for the sheets, schedules, and to specify the schedule priority.

To open the Schedule window,

| 1. | In the Dr. ABE main window, click the Schedule Preference button to open the Preference window. |
| --- | --- |
| 2. | In the Preference File pane, double-click the Schedule icon to display the Schedule window. This window has three panels, Sheet Name, Schedule Name and Scheduling Priority panel. |

| See: | Sheet Name |
| --- | --- |
|  | Schedule Name |
|  | Scheduling Priority |

## 20.1 Sheet Name

The options in the Sheet Name panel allow you to configure the sheet names for the schedule. You can choose the items that constitute the sheet name, assign a name automatically, or specify a special name.

| See: | Sheet Name Items |
| --- | --- |
|  | Nesting Name |
|  | Date |
|  | Sequence Number |
|  | For Combination Process, Change Sheet Name Based on the Machine |
|  | Sheet Name |

| See: | Schedule Name |
| --- | --- |
|  | Scheduling Priority |

### 20.1.1 Sheet Name Items

|  | In the Sheet Name Items list, you can select the items to constitute the sheet name. The selected items will appear in the Sheet Name text box. |
| --- | --- |

| Items | Description |
| --- | --- |
| Nesting Name | The name of the nesting schedule. You can assign different nesting names to distinguish between the nest jobs. See Nesting Name |
| Process Date | The date to process part. If a part has a different processing date, the earliest date will be used. |
| Deadline | The part process due date. If a part has different process deadlines, the earliest one will be used. |
| Machine Name | The machine name. |
| Material Name | The material name. |
| Thickness | The sheet thickness. |
| Today’s Date | The current date. |
| Sequence Number | Select this item and the system will use a series of sequential numbers to name the sheets. Make sure to type a starting sequence number in the Start Number: text box. See Sequence Number. |
|  | Note: This item is selected by default and cannot be removed from the Sheet Name: text box. See Sheet Name |
| Material Type | The material type. |

| See: | Nesting Name |
| --- | --- |
|  | Date |
|  | Sequence Number |
|  | For Combination Process, Change Sheet Name Based on the Machine |
|  | Sheet Name |

### 20.1.2 Nesting Name

This section allows you to specify the nesting names. The nesting will refer to the result of one single auto execution of the system that processes one or more sheets.

| Option | Description |
| --- | --- |
| Auto Assign | Select this option to use a number as the nesting name. |
|  | Notes: |
|  | 1. You can only type a number in the Auto Assign: text box. |
|  | 2. If you select this option, the system will automatically update the nesting name and assign it to the next nesting after you save the NC data of the nesting result. And the schedule name will change accordingly if the Nesting Name option is selected to constitute the schedule name. See Schedule Name for details. |
| Special Name | Select this option to use a special string as the nesting name. You can type a nesting name in the text box or select a name from the drop down list. |
|  | Note: When you type a number in the Special Name: text box, the system will regard it as characters. No changes will be made to create the next nesting name even though you save the NC data of the current nesting. |

Example

| 1. | In the Sheet Name panel, specify the conditions as follow. |
| --- | --- |
| 2. | The sheet names are 10001, 10002, and 10003 after the nesting process is completed. |
| 3. | Click the Main Preference button to open the System Setting window and change the database to File and then return to the main window. Select the nesting results and right-click the row headings to display the shortcut menu. Select Save NC data from the menu to display the Input O Number dialog box. |
| 4. | In the Input O Number dialogue box, type a number and click OK to continue. |
| 5. | In the Browse For Folder window, navigate and select the destination folder to save the NC data file. Click OK. |
| 6. | Save Confirmation window appears. Click Save button to continue. |
| 7. | Click the Auto Execute button again, and in the result view you will find the sheet names are changed: 20004, 20005 and 20006. |

| See: | Sheet Name Items |
| --- | --- |
|  | Date |
|  | Sequence Number |
|  | For Combination Process, Change Sheet Name Based on the Machine |
|  | Sheet Name |

### 20.1.3 Date

This section allows you to specify the date format. Y = Year, M = Month and D = Date.

Example

| 1. | In the Sheet Name panel, specify the conditions as follow. |
| --- | --- |
| 2. | The sheet name will be as follows after the nesting process is completed. |

| See: | Sheet Name Items |
| --- | --- |
|  | Nesting Name |
|  | Sequence Number |
|  | For Combination Process, Change Sheet Name Based on the Machine |
|  | Sheet Name |

### 20.1.4 Sequence Number

This section allows you to specify the starting sequence number. The Sequence Number item is selected by default and the "&[Sequence Number]" cannot be removed from the Sheet Name text box.

Example

| 1. | In the Sheet Name panel, specify the conditions as follow. |
| --- | --- |
| 2. | The sheet names are as follows after the nesting process is complete. |

| See: | Sheet Name Items |
| --- | --- |
|  | Nesting Name |
|  | Date |
|  | For Combination Process, Change Sheet Name Based on the Machine |
|  | Sheet Name |

### 20.1.5 For Combination Process, Change Sheet Name Based on the Machine

If you use both the FO and EM machines to process the same sheet, and if you enable this option, the system will assign two different names to the same sheet. This option is only valid for combination machines.

| See: | Sheet Name Items |
| --- | --- |
|  | Nesting Name |
|  | Date |
|  | Sequence Number |

### 20.1.6 Sheet Name

Sheet Name:  text box. You can also edit the contents if necessary.

Notes:

- The Sequence Number item is selected by default and the "&[Sequence Number]" cannot be removed from the Sheet Name: text box.

- If you select the Nesting Name item from the Sheet Name Items list, you should define the nesting name. See Nesting Name.

- You cannot use the following characters, such as   \, /, :, *, ?, ", <, >, or |, to specify the sheet name.

Example

| 1. | Select the Material Name item in the Sheet Name Items list, and it will appear in the Sheet Name: text box. |
| --- | --- |
| 2. | You can type strings in the Sheet Name: text box. For example, type AAAA in the text box. |
| 3. | Click OK to close the Schedule window. |
| 4. | The sheet name will be as the follow after the nesting process is complete. |

| See: | Sheet Name Items |
| --- | --- |
|  | Nesting Name |
|  | Date |
|  | Sequence Number |
|  | For Combination Process, Change Sheet Name Based on the Machine |

## 20.2 Schedule Name

The options in the Schedule Name panel allow you to configure the schedule names for the schedule. You can choose the items that constitute the schedule name, and specify the starting number and date format.

| See: | Schedule Name Items |
| --- | --- |
|  | Number |
|  | Date |
|  | Schedule Name |

| See: | Sheet Name |
| --- | --- |
|  | Scheduling Priority |

### 20.2.1 Schedule Name Items

|  | In the Schedule Name Items list, you can select the items to constitute the schedule name. The selected item will appear in the Schedule Name: text box. |
| --- | --- |

| Option | Description |
| --- | --- |
| Nesting Name | The name of the nesting schedule. You can assign different names to distinguish from the different nest jobs. See Nesting Name. |
| Process Date | The date to process part. If different processing dates are assigned to one part, the earliest date will be used. |
| Machine Name | The machine name. |
| Material Name | The material name. |
| Thickness | The sheet thickness. |
| Today's Date | The current date. |
| Sequence Number | Select this item and the system will use a series of numbers to name the sheet. Make sure to type a starting number in the Start Number: text box. See Sequence Number |
|  | Note: This item is selected by default and cannot be removed from the Sheet Name: text box. See Schedule Name |
| Material Type | The material type. |
| Planned File Name | The name of the nesting plan. |

| See: | Number |
| --- | --- |
|  | Date |
|  | Schedule Name |

### 20.2.2 Sequence Number

|  | This section allows you to specify the starting sequence number. The Sequence Number item is selected by default and the "&[Sequence Number]" cannot be removed from the Schedule Name: text box. |
| --- | --- |

Example

| 1. | In the Schedule Name panel, select the Nesting Name item. |
| --- | --- |
| 2. | Click the Sheet Name tab to activate the Sheet Name panel. |
| 3. | Specify the conditions as follow. |
| 4. | Click OK and perform the nesting process. The sheet names will be as follow. |
| 5. | In the result list, select and right-click one row heading to display the shortcut menu. Select Save Schedule/Output Report from the menu to display the Save Schedule window. |
| 6. | In the Save Schedule window, the default schedule name is AAAA0001, which consists of the nesting name and the sequence number that you defined. You can modify the schedule name in the text box. |

| See: | Schedule Name Items |
| --- | --- |
|  | Date |
|  | Schedule Name |

### 20.2.3 Date

|  | This option allows you to define the date format: Y = Year, M = Month and D = Date. |
| --- | --- |

Example

| 1. | In the Schedule Name panel, specify the conditions as follow. |
| --- | --- |
| 2. | Auto Execute the nesting. |
| 3. | Select and right-click a row heading in the Result list to open the shortcut menu. |
| 4. | Select Save Schedule/Output Report from the menu to display the Save Schedule window. |
| 5. | The default schedule name is 2007010250001, which consists of the current date and the sequence number. You can also modify the name in the text box. |

| See: | Schedule Name Items |
| --- | --- |
|  | Number |
|  | Schedule Name |

### 20.2.4 Schedule Name

Select one item from the Schedule Name Items list, and the item selected will appear in the Schedule Name: text box. You can also edit the contents if necessary.

Notes:

- The Number item is selected by default and the "&[No]" cannot be removed from the Sheet Name: text box.

- If you select the Nesting Name item from the Schedule Name Items list, you should define the nesting name. After you save the NC data of the nesting result, the system will automatically change the nesting name to create a new nesting name for the new nesting process. And the schedule name will change accordingly. See Nesting Name

Example

| 1. | In the Schedule Name panel, specify the conditions as follow. |
| --- | --- |
| 2. | In the Sheet Name panel, specify the Nesting Name settings as follow. |
| 3. | Select the nesting results after the nesting process is complete. Right-click the row heading to open the shortcut menu. Select Save NC data from the menu to display the Input O Number dialog box. |
| 4. | In the Input O Number dialogue box, type a number and click OK to continue. |
| 5. | In the Browse For Folder window, navigate and select the destination folder to save the NC data file. Click OK. |
| 6. | Select the nesting results and right-click the row heading to open the shortcut menu. Select Save Schedule/Output Report from the menu to display the Save Schedule window. |
| 7. | In the Save Schedule window, the default schedule name is 10001, which consists of the nesting name and the sequence number. Click OK to save the schedule data. |
| 8. | In the Dr. ABE main window, click the Auto Execute button to repeat the nesting process. After the nesting process is performed, select the nesting results and right-click the row headings to open the shortcut menu. Select Save Schedule data from the menu to display the Save Schedule window. |
| 9. | In the Save Schedule window, you will find the default schedule name becomes 20001. The system has automatically changed the nesting name to create the new schedule name. |

| See: | Schedule Name Items |
| --- | --- |
|  | Number |
|  | Date |

## 20.3 Scheduling Priority

In the Scheduling Priority panel, you can define the priorities to sequence the schedules (sheets).

| See: | Priority |
| --- | --- |
|  | Separate Schedule |

| See: | Sheet Name |
| --- | --- |
|  | Schedule Name |

### 20.3.1 Priority

In the priority list, you can choose items used to sequence the schedules (sheets) by placing check marks in the check boxes of the priority items. You can click the arrow buttons along the right to sort the schedules (sheets) by the ascending or descending order. You can also click the arrow buttons below the list to move the selected item upward or downward in the list.

Notes:

- The higher the position of the item, the higher the priority.

- Only the Laser Material Name, Material Thickness, Material Type and Material Size items are currently available.

| Option | Description |
| --- | --- |
| Clearance | Sequence the schedules (sheets) by the clearance value of the punching tools. This option is not available for the moment. |
| Material Type and Thickness | Sequence the schedules (sheets) by the material type and thickness. If you place a check mark in the check box, the system will sort the schedules by material type. For the same type of material, the system will sort the schedule by thickness. |
| Material Size | Sequence the schedules (sheets) by the material size. |
| Sheet Type | Sequence the schedules (sheets) by the material type. If you place a check mark in the check box of this option, set the ascending order as the sort order, the system will sort the schedules (sheets) by the material type, and in the order of Sketch, Skeleton and Standard. If the sort order is the descending order, the system will sort the schedules (sheets) in the order of Standard, Skeleton and Sketch. |
| Shorten the Combination Process Time | Sequence the schedules (sheets) to reduce the combination processing time. This option is not available for the moment. |
| Tool Layout Name | Sequence the schedules (sheets) by the tool layout name of the punch. |
| Tool Setup | Sequence the schedules (sheets) by the tool setup. When a tool setup is required for the same tool layout in punching, configure the tool setup. This option is not available for the moment. |
| Laser Material Name | Sequence the schedules (sheets) by the material name to determine the laser cutting conditions. |
| Laser Lens Type | Sequence the schedules (sheets) by the lens type for the laser processing. This option is not available for the moment. |
| Utilization | Sequence the schedules (sheets) by sheet utilization. |

Example

| 1. | In the Priority list, place a check mark in the Material Size: check box. |
| --- | --- |
| 2. | You will use three sheets of different sizes and types during the nesting process. |
| 3. | In the Dr. ABE main window, click the Auto Execute button to perform the nesting process. You will find the nesting schedules are sorted by the material size in the ascending order. |
| 4. | Return to the Scheduling Priority panel; click the button to change it into , and then save the change. |
| 5. | In the Dr. ABE main window, click the Auto Execute button to perform the nesting process. You will find the nesting schedules are sorted by the material size in the descending order. |

| See: | Separate Schedule |
| --- | --- |

### 20.3.2 Separate Schedule

| Option | Description |
| --- | --- |
| Tool Setup | Place a check mark in the check box, the system will schedule according to turret. |
|  | Remove the check mark. Right click in the Part Layout area after auto execution, select Display Group Tools to open the ToolList For Schedule window. The Schedule list will be the following. |
|  | Place a check mark in the check box, and then the Schedule list will be the following. |
| Material Type/Thickness | Place a check mark in the check box, the system will schedule according to material. |
|  | Remove the check mark. Right click in the Part Layout area after auto execution, select Display Group Tools to open the ToolList For Schedule window. The Schedule list will be the following. |
|  | Place a check mark in the check box, and then the Schedule list will be the following. |
| Note: Place a check mark in the two check boxes, the system will schedule according to both turret and material. |
| Place check mark in the Tool Setup check box and Material Type/Thickness check box at the same time, the Schedule list will be the following. |

| See: | Priority |
| --- | --- |

# Chapter 21: Tool Inventory

The Tool Inventory window lists the tools that are available for your machines. You can update your tool inventory as you purchase new tools or remove broken tools. You can import tools to update your tool inventory or modify the tool information to meet your needs.

To open the tool inventory window

| 1. | Click one preference button on the Dr. ABE main window to open the Preference window. In the Tree View pane, click Sub Inventory under Public. |
| --- | --- |
| 2. | In the Preference File pane, double-click the ToolInventory icon to open the SubInventory window. |
| See: | SubInventory Window |
|  | Tool Inventory Table |
|  | Tool Inventory Table Shortcut Menu |
|  | Tool Window |

## 21.1 SubInventory Window

The SubInventory window is a graphical representation of all the tools available for your machine. The Tool Inventory table lists the information for each tool in the inventory, such as Shape, Size, Type, Air Blower, etc. You can display the tools by Shape or by Range. You can import tools to update your inventory or modify the tool information to meet your needs.

| See: | SubInventory Window Toolbar |
| --- | --- |
|  | Range and Shape buttons |
|  | Import Buttons |
|  | View Buttons |
|  | Advanced Filter Window |
|  | Machine Type |

| See: | Tool Inventory Table |
| --- | --- |
|  | Tool Inventory Table Shortcut Menu |
|  | Tool Window |

### 21.1.1 SubInventory Window Toolbar

The buttons on the toolbar allow you to display the tools based on the shape and range. You can import AP100 tools or import the tool designs saved in DXF/DWG format and convert them into SP/FM tools.

| See: | Range and Shape buttons |
| --- | --- |
|  | Import Buttons |
|  | View Buttons |
|  | Advanced Filter Window |
|  | Machine Type |

### 21.1.2 Range and Shape buttons

Click a range button to display tools of that range. The  button is selected by default and tools of all the ranges will be displayed.

Click a shape button to display the tools of that shape. The  button is selected by default and tools of all the shapes will be displayed.

| See: | SubInventory Window Toolbar |
| --- | --- |
|  | Import Buttons |
|  | View Buttons |
|  | Advanced Filter Window |
|  | Machine Type |

### 21.1.3 Import Buttons

|  | The import buttons allow you to import AP100 tools, export or import the inventory information. And you can also import the tool designs saved in DXF/DWG format and convert them into SP/FM tools. |
| --- | --- |

| Button | Description |
| --- | --- |
| Import Global Inventory | Import AP100 tools into the Dr. ABE tool inventory. See: Import Ap100 tools into Dr ABE tool inventory |
| Import Global SP/FM Shapes | Import AP100 tools into the Dr. ABE tool inventory. See: Import Ap100 SP/FM tools into Dr. ABE tool inventory |
| Import File | Import the *.xml files of tool inventory |
| Export File | Export the tool inventory as *. xml files. |
| Import DXF/DWG SP/FM Shapes | Import the tool designs saved in DXF/DWG format and convert them into SP/FM tools. See: Import DXF/DWG SP/FM Shapes |

| See: | Import AP100 tools into Dr ABE tool inventory |
| --- | --- |
|  | Import Ap100 SP/FM tools into Dr. ABE tool inventory |
|  | Import DXF/DWG SP/FM Shapes |

| See: | SubInventory Window Toolbar |
| --- | --- |
|  | Range and Shape buttons |
|  | View Buttons |
|  | Advanced Filter Window |
|  | Machine Type |

#### 21.1.3.1 Import AP100 tools into Dr ABE tool inventory

| 1. | In the System Setting window, type the PC name or address in the Data Server PC (AP100/PCL): text box to specify the PC from which we will download the AP100 tools. See: Parameter Processing |
| --- | --- |
| 2. | Specify the group to import tools. Click the Import Global Inventory button. |
| 3. | Click OK to continue. |
|  | If you click Original, the following window displays, and you can specify the button and specify the initial tool angles after the tools are imported. If the tool angle is not defined, the default tool angle will be 0 degree. |
| 4. | AP100 tools are successfully imported into Dr. ABE tool inventory. |

| See: | Import Ap100 SP/FM tools into Dr. ABE tool inventory |
| --- | --- |
|  | Import DXF/DWG SP/FM Shapes |

#### 21.1.3.2 Import Ap100 SP/FM tools into Dr. ABE tool inventory

| 1. | In the System Setting window, type the PC name or address in the Data Server PC (AP100/PCL): text box to specify the PC from which we will download the AP100 SP/FM tools. See Parameter Processing |
| --- | --- |
| 2. | Specify the group to import tools. Click the Import Global SP/FM Shapes button. |
| 3. | In the Tool Load window, select one SP or FM tool, and click Open to continue. Note: You can select more than one tool each time. |
| 4. | SP and FM tools are successfully imported into Dr. ABE tool inventory. |

| See: | Import AP100 tools into Dr ABE tool inventory |
| --- | --- |
|  | Import DXF/DWG SP/FM Shapes |

#### 21.1.3.3 Import DXF/DWG SP/FM Shapes

| 1. | In the SubInventory window, Specify the group to import tools and then click Import DXF/DWG SP/FM Shapes button. |
| --- | --- |
| 2. | Browse and select the DXF file to import. After specifying the Tool Center Position and Type of Tool, click Open to continue. |
|  | Options | Descriptions |
|  | Tool Center Point |  |
|  | Image Center | CAD data center will be the punch center. |
|  | Image Point | One point of the CAD graphic will be the punch center. |
|  | Coordinate X=0 Y=0 | The coordinates (0.0) of the CAD graphic will be the punch center. |
|  | Auto Condition Setup | Setup the conditions to import the CAD files. See: Auto Correction Condition Setup |
|  | Type of Tool |  |
|  | SP | Select this option to convent the CAD file into special tool. |
|  | Forming | Select this option to convent the CAD file into forming tool. |
| 3. | This DXF file is imported into the tool inventory and converted to a FM tool. |

| See: | Import AP100 tools into Dr ABE tool inventory |
| --- | --- |
|  | Import Ap100 SP/FM tools into Dr. ABE tool inventory |

### 21.1.4 View Buttons

|  | You can select the way to display the tools and tool information. |
| --- | --- |

| Option | Description |
| --- | --- |
| Tool List | List all the available tools. |
| Tool List +Property | List all the available tools, and display the Tool window. You can select a tool and display its detailed tool information in the Tool window. See: The Tool Window |

| See: | SubInventory Window Toolbar |
| --- | --- |
|  | Range and Shape buttons |
|  | Import Buttons |
|  | Advanced Filter Window |
|  | Machine Type |

### 21.1.5 Advanced Filter Window

Click Search to open the Advanced Filter window. The options in this window allow you to filter the results by Name, Shape, Range, etc. For example, if you place a check mark in the Nibbling check box and select Turret as the tool type. The system will search the current tool inventory and display all the nibbling tools of Turret type.

| See: | SubInventory Window Toolbar |
| --- | --- |
|  | Range and Shape buttons |
|  | Import Buttons |
|  | View Buttons |
|  | Machine Type |

### 21.1.6 Machine Type

|  | Select a machine to display its tool inventory. |
| --- | --- |

| See: | SubInventory Window Toolbar |
| --- | --- |
|  | Range and Shape buttons |
|  | Import Buttons |
|  | View Buttons |
|  | Advanced Filter Window |

## 21.2 Tool Inventory Table

The Tool Inventory table lists information for each tool, such as the Sequence, Shape, Range, Type, etc. You can display the tools by Shape or by Range. The shortcut options allow you to sort, copy, edit the tools, etc.

Tools are categorized into 10 groups. Tools in Gr1 have the highest priority during the tool assignment, while tools in Gr10 have the lowest priority.

Tool Inventory Table Columns

| Column Title | Description |
| --- | --- |
| ID | The ID number of the tool. It is automatically assigned by the system. |
| Name | The tool name. |
| Enable | A check mark indicates the corresponding tool can be assigned. The removal of the check mark will disable the tool assignment. |
| Sequence | The Sequence column displays the sequence numbers of the tools. Tools with smaller sequence numbers will have higher priority than the tools in the same sequence group during the assignment. |
| Shape | Tool shape. |
| Range | The tool guide range. Tool guide ranges from A to M. A tool cannot be placed in a station unless both ranges can match. |
|  | A | 0 to 12.7 mm | B and G | 12.7 mm to 31.75mm |
|  | C and H | 31.75mm to 50.8mm | D | 50.8mm to 88.9 mm |
|  | E | 88.9 mm to 101.6 mm | F | 101.6 to 152.4 mm |
|  | M | More than 152.4 mm |  |  |
| Size X | The X size of the tool. |
| Size Y | The Y size of the tool. |
| Size R | The radios of the corner of RR and CR tools. Size R is specific for RR and CR tools. The following figures indicate the R dimension for these tool types. |
|  | CR Tool | RR Tool |
| Type | Select the type of station that the tool will be placed. Currently only Turret and Attached Tapping options work. |
| Air Blower | If air blower tool exists, place a check mark in the check box. Note: To use this function, you must enable the Air Blower function first. See: Air Blower |
| Shape Sub Code | Supplemental information for contouring tools, nesting tools, etc. Note: When the shape is SQ/OB/CR: Standard, Slot, Nesting When the shape is TP: TPII, TP Unit, TP Tool When the shape is SP： Key, Non-Key, Slot II, Burring Tool (RE/SQ), Burring Tool (RO) When the shape is FM: Key, Non-Key, Slot II When the shape is triangle: Isosceles triangle, Right triangle and others. ※After importing SP/FM/TR, specify the shape sub code. |
| Energy Save Tooling | If NEX tool exists, place a check mark in the check box. Note: To use this function, you must enable the Energy Save function first. See: Energy Save |
| Comment | Tool comments |

Note:

Right-click the column header. And select the item to display by placing a check mark in the corresponding check box.

You can click the Customize. option to display the Tool Inventory Item window. You can place a check mark before the item and display it. You can select one item and click  or button to change its position in the inventory table. You can type a value in the Width of Select Column (in pixels): text box to specify the column width.

| See: | SubInventory Window |
| --- | --- |
|  | Tool Inventory Table Shortcut Menu |
|  | Tool Window |

## 21.3 Tool Inventory Table Shortcut Menu

|  | In the Tool Inventory table, right-lick to open the shortcut menu. The options on the shortcut menu allow you to edit, sort, copy, and append the parts. You can also batch modify the part sequences. Option Description Edit Group Specify the tools of the selected group as standard tools or forming tools. Auto Sort Sort the tools Append Append a new tool to the selected group. The tool window displays the Tool Name, Shape, Size, Guide, etc. See: The Tool Window Copy Use the tool information of the selected tool and create a new tool in the same group. A unique ID will be automatically assigned to the new tool. Linked Copy Use the tool information of the selected tool and create a new associated tool in the same group. The modification of either the original tool or the associated tool will be automatically reflected on the other. Edit Display the Tool window to edit the tool information. See: The Tool Window Delete Delete the tool selected. Remove Link Remove the links between the associated tool and the original tool. Same Sequence Select this option, and all the selected tools will be assigned the same sequence number. Sequence Select this option, and the system will automatically use the consequential numbers to define the sequence numbers for the selected parts. Assign Station Assign the station to the selected tool. See: Assign Station to a Storage |
| --- | --- |

| See: | Edit Group |
| --- | --- |
|  | Auto Sort |

| See: | SubInventory Window |
| --- | --- |
|  | Tool Inventory Table |
|  | Tool Window |

### 21.3.1 Edit Group

Inventory tools can be classified into 10 groups, from Gr1 to Gr10. When sorting tools, tools in Gr1 will be sorted with higher priority.

Right-click one sequence group, and select Edit Group to display the Tool Group Condition window.

Tool Group Condition Options

| Option | Description |
| --- | --- |
| Standard | Specify the tools in this group as standard tools. |
| Downward Forming Process Group | Specify the tools in this group as downward forming tools. And the system will process the parts from the clamped side to the opposite side as the following picture shows. |
| Include All One Direction Tool with in | Type a value in the text box to specify the process range width. The system will process all the parts within that range in one direction. |
| Forming Process Group | Specify the tools in this group as upward forming tools. When you define the tools as upward forming tools, the system will process the parts as follows. The system will perform repositions to avoid damaging the parts. |
| Process the Pre-punch Hole at the Same Time | Select this option, and the system will perform pre-punch hole during the process. |
|  | If this option is not selected, the system will process the parts as follows. |
|  | If this option is selected, the system will process the parts as follows. |
| Repositioning before Grouping Tool Processes | Select this option, and the system will perform reposition before conducting forming process. For example, if the system uses the RO tools in Gr1, RE tools in Gr2 and forming tools in Gr7 to process the following parts, select this option, and the system will process the parts as follows. The symbol indicates the downward forming process. |

| See: | Auto Sort |
| --- | --- |

### 21.3.2 Auto Sort

In the Tool Inventory Table, right-click one sequence group, and select Auto Sort to display the AutoSort Setting window. You can sort the registered tools based on the auto sort settings.

| Option | Description |
| --- | --- |
| Set Priority | Specify the sort orders. |
| Shape=> Size | Select this option, and the system will sort the tools by Shape, and then by Range. |
| Size=> Shape | Select this option, and the system will sort the tools by Range, and then by Shape. |
| Shape Sequence | Specify the sequence to sort the tools by Shape. The system will sort the tools from the shape on the top to the shape on the bottom. |
| Size Sequence | Specify the sequence to sort the tools by Range. The system will sort the tools from the range on the top to the range on the bottom. |
| Auto No. Step | Specify the incremental value for the sequence numbers when sorting the tools. |
| Apply to All Groups | Select this option to apply the Auto Sort Settings to all the groups. |

Example

| 1. | In the Tool Inventory Table, the tools in Gr2 are displayed as follows. |
| --- | --- |
| 2. | Select group 2, and right-click to display the shortcut menu. Select Auto Sort to display the AutoSort Setting window. |
| 3. | In the AutoSort Setting window, specify the settings as follows. |
| 4. | Since tools in group are all RO tools, the system will sort the tools by range from A to C, and the sequence numbers are reset with the incremental step value of 2, and the starting number is 2 |

| See: | Edit Group |
| --- | --- |

## 21.4 Tool Window

To display the Tool window, you can double-click the tool ID of certain tool, or right-click on the Tool Inventory table, and select Edit from the shortcut menu.

The tool window allows you to append or modify the tool information. It displays the Tool Name, Shape, Size, Guide, Tool Type, Sub Code, and other information.

| See: | Basic Information |
| --- | --- |
|  | Attribute 1 |
|  | Attribute 2 |
|  | Codes |
|  | PDC Operation |

| See: | SubInventory Window |
| --- | --- |
|  | Tool Inventory Table |
|  | Tool Inventory Table Shortcut Menu |

### 21.4.1 Basic Tool Information

The Basic Tool Information section of the Tool window display the basic tool information, such as Tool Name, Shape, Size, Guide, Tool Type, Sub Code, etc.

| Option | Description |
| --- | --- |
| Tool Name | The tool name. |
| Shape | Tool shape. |
| Guide | The tool guide. Tool guide ranges from A to M. A tool cannot be placed in a station unless both ranges can match. |
|  | A | 0 to 12.7 mm | B | 12.7 mm to 31.75mm |
|  | C | 31.75mm to 50.8mm | D | 50.8mm to 88.9 mm |
|  | E | 88.9 mm to 101.6 mm | F | 101.6 to 152.4 mm |
|  | M | More than 152.4 mm |  |  |
| Size X | The X size of the tool. |
| Size Y | The Y size of the tool. |
| Size R | The radius of the corner of RR and CR tools. Size R is specific for RR and CR tools. The following figures indicate the R dimension for these tool types. |
|  | CR Tool | RR Tool |
| Comment | Tool comments |
| Air Blower | If air blower tool exists, place a check mark in the check box. Note: To use this function, you must enable the Air Blower function first. See: Air Blower |
| Tool Type | Select the type of station that the tool will be placed. Currently only Turret and Attached Tapping options work. |
| Sub Code | Supplemental information for contouring tools, nesting tools, etc. Note: When the shape is SQ/OB/CR: Standard, Slot, Nesting When the shape is TP: TPII, TP Unit, TP Tool When the shape is SP: Key, Non-Key, Slot II, Burring Tool (RE/SQ), Burring Tool (RO) When the shape is FM: Key, Non-Key, Slot II When the shape is triangle: Isosceles triangle, Right triangle and others. ※After importing SP/FM/TR, specify the shape sub code. |
| Share Setting | Share the same tool conditions among the machines that use the same machine drivers. See: Share the tool conditions among machines |
| NEX | If NEX tool exists, place a check mark in the check box. Note: To use this function, you must enable the Energy Save function first. See: Energy Save |
| Enable | A check mark indicates the corresponding tool can be assigned. The removal of the check mark will disable the tool assignment. |

| See: | Attribute 1 |
| --- | --- |
|  | Attribute 2 |
|  | Codes |
|  | PDC Operation |

#### 21.4.1.1 Share the tool conditions among machines

The Share Setting button in the basic tool information section allows you to share the same tool conditions among machines that use the same machine drivers

Example

| 1. | We have two EM machines, EM-111 and EM2510. |
| --- | --- |
| 2. | Select Sub Inventory under Public to display ToolInventory file icon in the Preference File pane. |
| 3. | Double-click the ToolInventory file icon to display the SubInventory window. |
| 4. | Double-click the ID cell of one tool to display the Tool window. The Tool window lists all the available punch and combination machines. Click the tab of one machine, for example, EM-L machine. And then click Share Setting button. |
| 5. | The Share Setting lists the machines that have the same machine driver as EM2510 machine. Select the machine you want to share the tool conditions. Click Close to continue. |
| 6. | EML and EM-L11 share the same tab, which means both machines share the same tool conditions. |
|  | Note: You can click Share Setting button, and remove the check mark from the check box of the shared machines to stop sharing the tool conditions. |

### 21.4.2 Attribute 1

The options in the Attribute 1 panel allow you to specify the tool conditions. You can specify whether adapter can be used or not when placing a tool in the station with a larger range, You can specify the Max Lap Amount for the tool assignment, and you can specify the usage of the tool, for example, whether the tool can be used as a nibbling tool or not.

| Option | Description |
| --- | --- |
| Allow Use Adapter | When we place a tool in a station, the tool range (or the guide range) should match the station range, otherwise the tool cannot be installed properly. Select this option if sleeve can be used to place tools of one range to the stations of larger range. |
| Shear Angle | Place a check mark in the check box if the tool can be used as a shearing tool. You can specify the shearing angle in the text box. Note: This option is only available for RE, RO, RR and SQ tools. If a shearing tool has shear angle, it can reduce the punch pressure and the chances that tools get damaged when processing thick material will be small. |
|  | A tool without shear angle A tool with shear angle |
| Allow use Shorter Edge | This option is only available for rectangle tools. When shearing or punch a line, the system will use the longer edge of the tool to process. |
|  | If this option is selected, the system will use the shorter edge of this rectangle tool to process if no other appropriate tools can be used. |
| Max Lap Amount (%) | Specify the maximum overlap percentage for the rectangle and square tools. Note: If the tool length x (1+1-A%) is less than the line length, the tool can be assigned. If the tool length x (1+1-A%) is more than the line length, the tool cannot be assigned to process the line. |
| Sheet Saver | When a tool is assigned to process a pattern, to prevent the tool guide colliding with the clamps, the minimum distance from the tool hit center to the material edge will be DZ Y/2 + Clamp Length, otherwise the system will have to perform repositions to avoid colliding. This option is available for the nesting tools. Sheet Saver allows us to type a value in the text box to shorten the minimum distance mentioned above, so that reposition can be avoided. See: Specify the Sheet Saver for the nesting tools to avoid reposition |
| Nibbling | Select this option, and the selected tool can be used as a nibbling tool. You can type a value in the text box to specify the pitch value. |
| Match Tool Shape | Select this option to make the SP tool match the pattern. |
| Special Pitch | You can type a value in the text box to specify the pitch for nibbling process. Note: If the Special pitch is not defined here, the system will use the pitch settings defined in Tool Lap Value windows. |
| Punch Pierce | Select this option, and the selected tool can be used to perform piercing process. |
| Only Slit & Single Hit | Select this option, the tool selected can only be assigned to punch slit and perform single hit. |
| Auto Index | Select this option, and the selected tool can be placed in the AI-Station. |

| See: | Basic Information |
| --- | --- |
|  | Attribute 2 |
|  | Codes |
|  | PDC Operation |

#### 21.4.2.1 Specify the Sheet Saver for the nesting tools to avoid reposition

For the nesting tools, you can type a value in the Sheet Saver text box to shorten the minimum distance from the tool hit center to the material edge, so that reposition can be avoided. See: Sheet Saver

Example

| 1. | To process the following line segments close to the clamp, the system will assign the tool of Station 224 of E range to process. We notice that the Y dimension of the Station 224 (DZY) or the guide diameter is 116.665. If the tool in this station is assigned to process a pattern. To prevent the tool guide colliding with the clamps, the minimum distance from the tool hit center to the material edge will be DZ Y/2 + Clamp Length. In this case, the minimum distance will be DZ Y/2 + Clamp Length=116.665/2 + 10=68.333. While the actual distance from the tool hit center to the sheet edge is 65, therefore the system will perform a reposition when processing the line segments. Note: You must place a check mark in the Avoid DZ check box in the Clamp Avoidance tab of the PunchSequence window. |
| --- | --- |
|  | Before Reposition | After Reposition |
| 2. | If we put a nesting tool in the same station to process the same patterns. |
| 3. | When the system assign the same tool to process the line segments, although the distance from the tool hit center to the sheet edge is still 68, while the minimum distance has changed to DZ Y/2 + Clamp Length - Sheet Saver=116.665/2 + 10 - 40=28.333. The system will process the following line segments without repositioning. |

Note:

| 1. | Only RE, RR and OB tools can be defined as nesting tool. |
| --- | --- |
| 2. | If a tool is defined as the nesting tool, and Sheet Saver has been specified, the minimum distance that the reposition won’t be conducted will vary with the tool hit angle. |
|  | Let’s take the tool in the station of E range for example. The Sheet Saver is set to 40. |
|  | If the tool hit angle is 0 degree, the minimum distance will be 116.665/2 –40 +10=28.333 | If the tool hit angle is 90 degree, Sheet Saver setting has no effect on the minimum distance, which will be 116.665/2 +10=58.333 | If the tool hit angle is 145 degree, the minimum distance will be 116.665/2.8=41.667 |

| See: | Basic Information |
| --- | --- |
|  | Attribute 1 |
|  | Attribute 2 |
|  | Codes |
|  | PDC Operation |

### 21.4.3 Attribute 2

The options in Attribute 2 panel allow you to specify the clearance, process angle, sequence group, sequence number and other settings for a tool. In addition, you can also specify the process direction, starting point for each tool in the Advance window.

| Option | Description |
| --- | --- |
| Clearance | Specify up to 5 die clearances for the tool selected. |
|  | Selecting the proper die clearance is very important. The die clearance affects tool life, tonnage requirements and the burr. Meanwhile it varies with the material thickness. |
| Process Angle | Specify available angles for a tool. And the tool can only be used in the specified angles for the punching process. |
| C Axis Sort Off | Place a check mark to disable the C Axis Sort function, and the system won’t use the selected tool to process the parts by angle. See AI Tool Angle Sort in the Punch Sequence panel of CombinationSequence window. |
| Escape | This option is used for forming down tools. The system will generate G70 to instruct the machine to shift the sheet without punching. |
| Proc. Gr. | Edit the Sequence Group of the tools selected. |
| Order | Edit the Sequence No of the tool selected. |
| Advance | Click the Advance button to open the Customize window. You can specify the Start Position, Direction for the tool selected. See: The Customize Window |

| See: | Basic Information |
| --- | --- |
|  | Attribute 1 |
|  | Codes |
|  | PDC Operation |

#### 21.4.3.1 The Customize Window

Click the Advance button in the Attribute 2 panel to open the Customize window. You can specify the Start Position, Direction for the tool selected.

| Option | Description |
| --- | --- |
| Start Position | Specify the starting position for the tool selected. If you remove the check mark from the Start Position check box, the system will automatically determine the starting position according to the shortest path. |
| Direction | Specify the process direction for the tool selected. |
|  | If you remove the check mark from the Direction check box, the system will determine the process direction according to the shortest path. |
| X | Process the patterns in the X direction. |
| Y | Process the patterns in the Y direction. |
| One Direction | Select this option, and the system will process the patterns in one direction. It is strongly recommended to select this option for the forming down tool, so that the system can prevent the die of the forming down tool going into the forming parts. |
| Divide Sheet for Optimize | This option is used to divide the processing range into equal areas for the sequence. The system will punch the patterns in the first area and then will process the patterns in the adjacent area according to the direction specified in the Direction section. |
|  | Note: The Number of Divide option is only available when you select either X or Y direction in the Direction section. |

Example

| 1. | We will assign a RO tool to process the holes with a single hit. In the Tool Inventory table, select this RO tool and edit the process conditions in the Customize window. |
| --- | --- |
| 2. | If you specify the Start Position as follows. |
| 3. | The system will process the holes as follows. |

### 21.4.4 Codes

The options in the Codes tab allow you to specify the M code value and the output location when the selected tool is assigned to process the patterns.

| Item | Description |
| --- | --- |
| ON/OFF | Place a check mark in the corresponding check box if you want to specify the value and location for an M code. |
| Name | The name of the M code See: M Code |
| Value 1/Value 2 | Specify the output value. |
| Code Output Time | Select the position to output M code. Select Before to output the code before the corresponding tool is assigned. Select After to output the code after the corresponding tool is assigned. Select After All to output the code after the last hit of the corresponding tool is performed. |
| Material Setting | Specify the M code based on the material and thickness. You can select the material by placing a check mark in the corresponding check box. Type the Min Thickness and Max Thickness in the corresponding cells. The system will output the corresponding M codes based on the material and the thickness you have defined. |
| View Details | Click this button to display all the M codes and the relevant options in the Details of Codes Setting window. |

| See: | Basic Information |
| --- | --- |
|  | Attribute 1 |
|  | Attribute 2 |
|  | PDC Operation |

#### 21.4.4.1 M Codes

In the Codes tab, you can specify the value and location to output the M code when the corresponding tool is assigned to process the patterns.

| Code | Description |
| --- | --- |
| FEED RATE (1-4) | Specify the axis feed rate for the selected tool. The system will generate F1 to F4 in the NC code to control the feed rate. F1 is the fastest rate while F4 is the slowest. The system will generate the F code at the selected location each time the tool is assigned. Note: If you do not enable this function, the system will only generate the default feed rate F1. When the tool to which you have assigned a feed rate has finished punching, the system will generate F1 to restore the machine to the default condition. |
| FEED RATE CANCEL (F1) | Cancel the feed rate you have specified and return the feed rate to F1. |
| MILD MODE ON M120 | Select this option to turn on the acceleration/deceleration control in the X/Y axis. |
| MILD MODE OFF M121 | Select this option to turn off the acceleration/deceleration control in the X/Y axis. |
| PUNCH W/FLAT EDGE (M500) | Generate an M500 to specify the punching mode with a standard punch of a flat edge. |
| PUNCH WITH SHEAR ANGLE (M501) | Generate M501 to specify the punching mode with a standard punch having a shear angle. |
| PROGRAM STOP | Output an M00 program stop to stop the machine during operation. A stop sign appears on the sheet at the location of the last hit. |
| OPT PROGRAM STOP | Output an optional M01 stop command in the desired location of a program. A stop sign appears on the sheet at the location of the last hit. M01 is similar to M00. OPT PROGRAM STOP requires intervention from the machine operator. The machine will stop operation when it executes M01 command, and the operator must press the Opt Stop Key on the NC control panel to continue the process. |
| PUNCH DELAY ON (M08) | Generate M08 to enable a punch delay for the tool. Punch Delay Mode is mainly used for forming process, marking and knockout. It is also used for processing thick sheets. If you want to disable the punch delay after the tool is assigned, select PUNCH DELAY OFF or PRESS MODE CANCEL (M13) for the selected tool. |
| PUNCH DELAY OFF (M09) | Generate M09 to cancel the punch delay for the tool. |
| PRESSURE IGNORE ON (M694) | The system uses pressure sensor to detect the completion of the sheet process. Select this option and the system will generate M694 to instruct the machine to ignore the signal from the pressure sensor, and the machine will keep punching the sheet with a decelerated speed until the punch contacts the die. If you want to disable the Pressure Ignore function after the tool is assigned, select PRESSURE IGNORE OFF or PRESS MODE CANCEL (M13) for the selected tool. |
| PRESSURE IGNORE OFF (M695) | Generate M695 to cancel the pressure ignore mode after the tool is assigned. |
| FORMING MODE + M08 (M510-M559, M800-M999) | Specify the M code for the selected forming tool. The M code value ranges from 510 to 559 and from 800 to 999. Select this option, and when this forming tool is used, the system will generate the corresponding M Code and M08. |
|  | Note: Do not select FORMING MODE + M08 (M510-M559, M800-M900) and FORMING MODE - M08 (M510-M559, M800-M900) at the same time. This option is only available for the forming tools |
| FORMING MODE - M08 (M510-M559, M800-M999) | Specify the M code for the selected forming tool. The M code value ranges from 510 to 559 and from 800 to 999. Select this option, and when this forming tool is used, the system will generate the corresponding M Code and M08 is not generated. |
|  | Note: Do not select FORMING MODE + M08 (M510-M559, M800-M900) and FORMING MODE - M08 (M510-M559, M800-M900) at the same time. This option is only available for the forming tools |
| MARKING MODE + M08 (M560-M569) | Specify the M code for the selected marking tool. It allows you to mark parts using center punch tools. You can use the tools to mark characters on the sheet. The M code range value ranges from 560 to 569. The codes specified here will be used as the standard Marking Code. Select this option, and when this marking tool is used, the system will generate the corresponding M Code and M08. |
|  | Note: Do not select MARKING MODE + M08 (M560-M569) and MARKING MODE - M08 (M560-M569) at the same time. This option is only available for the CP (Center Punch) tools. |
| MARKING MODE - M08 (M560-M569) | Specify the M code for the selected marking tool. It allows you to mark parts using center punch tools. You can then use the tools to mark characters on the sheet. The M code value ranges from 560 to 569. The codes specified here will be used as the standard Marking Code. Select this option, and when this marking tool is used, the system will generate the corresponding M Code and M08 is not generated. |
|  | Note: Do not select MARKING MODE + M08 (M560-M569) and MARKING MODE - M08 (M560-M569) at the same time. This option is only available for the CP (Center Punch) tools. |
| KNOCK OUT MODE + M08 (M502-M505)(M570-M575) | Specify the M code for knockout tools. The M code value ranges from 502 to 505 and from 570 to 575. Please refer to your programming manual for more information. Select this option, and when this knockout tool is used, the system will generate the corresponding M Code and M08. |
|  | Note: If you need to cancel the knock out mode after the corresponding tool is assigned, select PRESS MODE CANCEL and select the After All as the Code Output Time. |
| KNOCK OUT MODE - M08 (M502-M505)(M570-M575) | Specify the M code for knockout tools. The M code value ranges from 502 to 505 and from 570 to 575. The M code value for some machines ranges from 570 to 575. Please refer to your programming manual for more information. Select this option, and when this knockout tool is used, the system will generate the corresponding M Code and M08 is not generated. |
|  | Note: If you need to cancel this mode after the tool is used, select PRESS MODE CANCEL and select After All as the Code Output Time. |
| PRESS MODE CANCEL (M13) | Generate an M13 to cancel the press modes for the selected tool. Press Modes are modes defined for a specific tool, such as MILD MODE, PUNCH DELAY, PRESSURE IGNORE, etc. |
| DWELL TIME G04 | Select this option to generate the G code of dwell time. |
| SLOTTING MODE (M506-M509) | Select this option to generate the slotting mode code. |
| SURFACE TABLE FUNCTIONALITY ON (M288) | Generate an M288 to instruct the machine to move the table downwards, so that there will be no interference with the turret rotation and axis movement for the downward forming process. |
|  | Note: If you want to disable this function after the corresponding tool is used, select SURFACE TABLE FUNCTIONALITY OFF (M289) or PRESS MODE CANCEL (M13) for the selected tool. |
| SURFACE TABLE FUNCTIONALITY OFF (M289) | Generate an M289 to cancel the Surface Table Functionality for the selected tool. |
| OUTPUT M687 AFTER FORMING | Select this option to output M687 after forming. |
| P & FM code | Specify the M code for the forming conditions. The M code value ranges from 590 to 592, and each represents one of the following forming conditions. M590: Punch moves and die doesn’t. M591: Punch moves and Die also moves. M592: Die moves and Punch doesn’t. Before using this option, please select P/F Structure in Machine Set window, and specify the FORMING MODE + M08 (M510-M559) and PRESS MODE CANCEL (M13). |

### 21.4.5 PDC Operation

The options in this panel allow you to specify the tool type relevant to PDC operation.

| Option | Description |
| --- | --- |
| Ordinary | Define the ordinary tools are defined as resident tools, which will remain in the turret after punching |
| Non-resident | Define the tool as a non-resident tool, which will return to the PDC when punching process is done. If several non-resident tools (the same range) are used to process one sheet, all these non-resident tools will have the same station number. |
| Substitute | Define the tool as a substitute tool. After the punching process is performed, and the non-resident tool returns to PDC, the substitute tools will be placed in the turret so that no stations will be empty. These substitute tools have higher priority to be used for the sheet. |

| See: | Basic Information |
| --- | --- |
|  | Attribute 1 |
|  | Attribute 2 |
|  | Codes |

# Chapter 22: Remnant/Skeleton Name

The Remnant/Skeleton window allows you to specify the names for remnant and skeleton material.

To open the Remnant/Skeleton window:

| 1. | Click any preference button in the main window to display the Preference window. |
| --- | --- |
| 2. | In the Tree View pane, select Remnant/Skeleton Name under Public. |
| 3. | In the Preference File pane, double-click the Remnant/Skeleton Name icon to display the Remnant/Skeleton Name window. This window has two panels: the Remnant Name panel and the Skeleton panel. |

| See: | Remnant Name |
| --- | --- |
|  | Skeleton Name |

## 22.1 Remnant Name

The options in the Remnant panel allow you to configure the names for the remnants.

You can choose the items that constitute the remnant name, assign a name automatically, or specify a special name.

| See: | Remnant Name Items |
| --- | --- |
|  | Special Name |
|  | Date Format |
|  | Sequence Number |
|  | Remnant Name |

### 22.1.1 Remnant Name Items

|  | In the Sheet Name Items list, you can select the items to constitute the remnant name. The selected items will appear in the Remnant Name: text box. |
| --- | --- |

| Items | Description |
| --- | --- |
| Special Name | You can type a specify name in the text box to define the remnant name. |
| Machine Name | The name of the machine |
| Material Name | The name of the material. |
| Thickness | The thickness of the sheet. |
| Rectangle X | The X dimension of the remnant. |
| Rectangle Y | The Y dimension of the remnant. |
| Rectangle Area | The rectangle area of the remnant |
| Create Date | The date when the remnant is created. |
| Sequence No | Select this item and the system will use a series of sequential numbers to name the remnants. Make sure to type a starting sequence number in the Start Number: text box. See: Sequence Number |
| Material Type | The material type. |
| Sheet name | The sheet name. |

| See: | Special Name |
| --- | --- |
|  | Date Format |
|  | Sequence Number |
|  | Remnant Name |

### 22.1.2 Special Name

To use the Special Name to define the remnant names, you must select Special Name from the Remnant Name Items list.

You can type a special name in the text box or select a name from the drop down list.

Note:

When you type a number in the Special Name: text box, the system will regard it as characters. No change will be made to create the next remnant name.

| See: | Remnant Name Items |
| --- | --- |
|  | Date Format |
|  | Sequence Number |
|  | Remnant Name |

### 22.1.3 Date Format

To use Data Format to define the remnant names, you must select Data Format from the Remnant Name Items list.

You can specify the date format. Y = Year, M = Month and D = Date.

| See: | Remnant Name Items |
| --- | --- |
|  | Special Name |
|  | Sequence Number |
|  | Remnant Name |

### 22.1.4 Sequence Number

This section allows you to specify the starting sequence number.

The Sequence Number item is selected by default and the "&[Sequence NO]" cannot be removed from the Remnant Name: text box.

| See: | Remnant Name Items |
| --- | --- |
|  | Special Name |
|  | Date Format |
|  | Remnant Name |

### 22.1.5 Remnant Name

Remnant Name: text box.

You can also edit the contents if necessary.

Notes:

- The Sequence Number item is selected by default and the "&[Sequence NO]" cannot be removed from the Remnant Name: text box.

- You cannot use the following characters, such as   \, /, :, *, ?, ", <, >, or |, to specify the remnant name.

Example

| 1. | In the Remnant Name panel, select the following items to constitute the remnant name. Set the Sequence Number to 0001. |
| --- | --- |
| 2. | In the Preference window, double-click the Nesting icon to display the Nesting window. Click Material Selection tab, and select Create Remnant and Vertical Cut in the Reusable Sheet area. |
| 3. | Load parts as follow, and assign different Part ID to those parts so that those parts will be nested in three sheets. |
| 4. | After auto execution, select all the three sheets. Right-click and select Save NC data from the shortcut menu. |
| 5. | Specify the O number, and click OK to continue. |
| 6. | After specifying the place to save the NC data, a Save Confirmation window displays. Click Save to continue |
| 7. | The remnants that the system created are saved in the Material Manager window. Their names are made up of the creation data, special name, the X size of the remnant and the sequence number. |

| See: | Remnant Name Items |
| --- | --- |
|  | Special Name |
|  | Date Format |
|  | Sequence Number |

## 22.2 Skeleton Name

The options in the Skeleton panel allow you to configure the names for the skeletons.

You can choose the items that constitute the skeleton name, assign a name automatically, or specify a special name.

| See: | Skeleton Name Items |
| --- | --- |
|  | Special Name |
|  | Date Format |
|  | Sequence Number |
|  | Skeleton Name |

### 22.2.1 Skeleton Name Items

|  | In the Skeleton Name Items list, you can select the items to constitute the skeleton name. The selected items will appear in the Skeleton Name: text box. |
| --- | --- |

| Items | Description |
| --- | --- |
| Special Name | You can type a specify name in the text box to define the skeleton name. |
| Machine Name | The name of the machine |
| Material Name | The name of the material. |
| Thickness | The thickness of the sheet. |
| Rectangle X | The X dimension of the skeleton. |
| Rectangle Y | The Y dimension of the skeleton. |
| Rectangle Area | The rectangle area of the skeleton |
| Create Date | The date when the skeleton is created. |
| Sequence No | Select this item and the system will use a series of sequential numbers to name the skeletons. Make sure to type a starting sequence number in the Start Number: text box. See: Sequence Number |
| Material Type | The material type. |
| Sheet name | The sheet name. |

| See: | Special Name |
| --- | --- |
|  | Date Format |
|  | Sequence Number |
|  | Skeleton Name |

### 22.2.2 Special Name

To use the Special Name to define the skeleton names, you must select Special Name from the Skeleton Name Items list.

You can type a special name in the text box or select a name from the drop down list.

Note:

When you type a number in the Special Name: text box, the system will regard it as characters. No changes will be made to create the next skeleton name.

| See: | Skeleton Name Items |
| --- | --- |
|  | Date Format |
|  | Sequence Number |
|  | Skeleton Name |

### 22.2.3 Date Format

To use Data Format to define the remnant names, you must select Data Format from the Skeleton Name Items list.

You can specify the date format. Y = Year, M = Month and D = Date.

| See: | Skeleton Name Items |
| --- | --- |
|  | Special Name |
|  | Sequence Number |
|  | Skeleton Name |

### 22.2.4 Sequence Number

This section allows you to specify the starting sequence number. The Sequence Number item is selected by default and the "&[Sequence NO]" cannot be removed from the Skeleton Name text box.

| See: | Skeleton Name Items |
| --- | --- |
|  | Special Name |
|  | Date Format |
|  | Skeleton Name |

### 22.2.5 Skeleton Name

Select one item from the Skeleton Name Items list, and the selected item will appear in the Remnant Name: text box. You can also edit the contents if necessary.

Notes:

- The Sequence Number item is selected by default and the "&[Sequence NO]" cannot be removed from the Skeleton Name: text box.

- You cannot use the following characters, such as   \, /, :, *, ?, ", <, >, or |, to specify the skeleton name.

Example

| 1. | In the Skeleton Name panel, select the following items to constitute the skeleton name. Set the Sequence Number to 0001. |
| --- | --- |
| 2. | In the Preference window, double-click the Nesting icon to display the Nesting window. Click Material Selection tab, and select Create Skeleton Sheet in the Reusable Sheet area. |
| 3. | Load parts in three different sheets, and assign different Part ID to those parts so that those parts will be nested in three sheets. |
| 4. | After auto execution, select all the three sheets. Right-click and select Save NC data from the shortcut menu |
| 5. | Specify the O number, and click OK to continue. |
| 6. | After specify the place to save the NC data, a Save Confirmation window displays. Click Save to continue. |
| 7. | The skeletons that the system created are saved in the Material Manager window. Their names are made up of the special name, creation data, and the sequence number. |

| See: | Skeleton Name Items |
| --- | --- |
|  | Special Name |
|  | Date Format |
|  | Sequence Number |

# Chapter 23: Turret Type

You can create a new turret type file to meet your special needs, and modify the current turret specification in the Turret Type window.

To open the Turret Type window

| 1. | Click the Punch Tool Assign Preference button in the main window to open the Preference window. |
| --- | --- |
| 2. | In the left Tree View pane, select next to the Public to expand submenu and click Turret Type. |
| 3. | In the Preference File pane, click one turret file to open the Turret Type window. |

| See: | Turret Type Window Items |
| --- | --- |
|  | Create or Remove a Turret Type |
|  | Adding or Deleting a Station |
|  | Turret Type Window Short Cut Menu |

## 23.1 Turret Type Window Items

The Turret Type window lists information for each station, such as the station range, dead zone range, etc. You can display the stations by Station Range and modify station settings.

Toolbar Buttons

Click one button to display the stations of specified range, click All to display all the stations.

Turret Type Table Columns

| Column Title | Description |
| --- | --- |
| ID | Display the ID number of the station. It is automatically assigned by the system. |
| Station | Display the station number. |
| Location | Display the location of station. 1 indicates the station is on the inner track, 2 indicates the station is on the center track, while 3 indicates the station is on the outer track. |
| Original | Place a check mark in this check box, which indicates this station is the original station. The turret angle of the original station is 0. |
|  | Note: |
|  | Only one station can be set as original station. |
| Range | Select the station size from drop-down list. Usually the station size range are specified as follows: |
|  | A | 0 to 0.5 inch | B and G | 0.5 to 1.250 inch |
|  | C and H | 1.250 to 2.000 inch | D and I | 2.000 to 3.500 inch |
|  | E and J | 3.500 to 4.500 inch | F and K | 4.500 to 6.000 inch |
|  | M | 6.000 to 999.999 inch |  |  |
|  | Note: G, H, I, J, K are for the AI (Auto-Index) Stations. |
| OTX | Display the X-axis distance between the station position and the original point. Usually it is set to 0. |
| OTY | Display the Y-axis distance between the station position and the original point. Usually for Amada machines, it is 40 for the station on the inner track, 0 for the station on the center track, and –40 for the station on the outer track. |
| AI | Place a check mark in this check box, which indicates this station is an Auto Index station. |
| Key | Place a check mark in this check box, which indicates this station is a keyed station. Only shaped tools, such as rectangle and square tools, can be installed in keyed stations. Non-keyed stations are available for round, center punch and burring tools. |
| ATCZone | Select the ATC zone from drop-down list for each station, if the machine is equipped with ATC. |
| Exchange | Display the station number when tools are exchanged. |
| Type | Select a station type from drop-down list. Usually Turret is selected for NCT machines. |
| Turret Angle | Display the station angle. The angle of the original station is 0 degree. |
| DZ | Display the dead zone number. See: Dead Zone of the Station |
| DZX | Display the X range of the Dead Zone. |
| DZY | Display the Y range of the Dead Zone. |

| See: | Create or Remove a Turret Type |
| --- | --- |
|  | Adding or Deleting a Station |
|  | Turret Type Window Short Cut Menu |

## 23.2 Create a New Turret Type

To create a new empty turret type file

| 1. | Select the Turret Type under Public in the left Tree View pane. |
| --- | --- |
| 2. | Right-click to display the shortcut menu. Select New to Turret Type Preference. |
| 3. | A new turret type file “New “ is created. You can rename the file and click it to display the correlative information in the Display Area pane where you can add stations. See: Adding or Delete a Station. |

To remove a turret type:

| 1. | In the top Preference File pane, right click a turret type you want to delete and a shortcut menu will display. |
| --- | --- |
| 2. | Select Delete and a message box will appear. |
| 3. | Click OK button. |

| See: | Turret Type Window Items |
| --- | --- |
|  | Adding or Deleting a Station |
|  | Turret Type Window Short Cut Menu |

## 23.3 Adding a New Station

Click a turret type in the Preference File pane and the correlative stations information will display in the Display Area pane below. Alternatively you can double click a turret type, the Turret Type window will appear.

Double-click the Station cell in the last row, and type a number to define the station number. After specifying the relevant station information, click <Enter> to confirm your changes

Note:

The station number you type must be unique; otherwise the system will display following warning message.

To delete a station, right click the station you desire and a shortcut menu will appear.

Select Delete and a message box will prompt.

Click Yes button to delete the selected station.

| See: | Turret Type Window Items |
| --- | --- |
|  | Create or Remove a Turret Type |
|  | Turret Type Window Short Cut Menu |

## 23.4 Turret Type Window Short Cut Menu

In the Turret Type window, you can append or remove a dead zone for a station.

Right click a station you desire and a shortcut menu appear.

| Shortcut Menu Option | Description |
| --- | --- |
| Append Dead Zone | Select this option to display the Dead Zone window, where you can add or modify a dead zone range for a station. |
|  | Select a dead zone and click Add button to assign the dead zone for the selected station. |
| Remove Dead Zone | Select this option to delete the dead zone settings for the selected station. A message box will prompt. |
|  | Click Yes button to confirm. |

| See: | Turret Type Window Items |
| --- | --- |
|  | Create or Remove a Turret Type |
|  | Adding or Deleting a Station |

# Chapter 24: Turret Type (PDC)

You can create a new turret type file to meet your special needs, and modify the current turret specification in the Turret Type (PDC) window.

To Open the Turret Type (PDC) window

| 1. | Click the Punch Tool Assign Preference button in the main window to open the Preference window. |
| --- | --- |
| 2. | In the left Tree View pane, select next to the Public to expand submenu and click Turret Type (PDC). |
| 3. | In the Preference File pane, click one turret file to open the Turret Type (PDC) window. |

| See: | Turret Type (PDC) Window Items |
| --- | --- |
|  | Create or Remove a PDC Turret Type |
|  | Adding or Deleting a PDC Station |
|  | Turret Type(PDC) Window Short Cut Menu |

## 24.1 Turret Type (PDC) Window Items

The Turret Type (PDC) window lists information for each station, such as the Location, Range, Location Angle, etc. You can display the stations by Station Range and modify station settings.

Toolbar Buttons

Click one button to display the stations of specified range, click All to display all the stations.

Turret Type Table Columns

| Column Title | Description |
| --- | --- |
| ID | Display the ID number of the PDC station. It is automatically assigned by the system. |
| Station | Display the station number of PDC storage. |
| Location | Display the location number of the PDC stations. There are 9 locations. |
| Range | Specify the station size. Usually the station sizes are as follows: |
|  | A | 0 to 0.5 inch | B and G | 0.5 to 1.250 inch |
|  | C and H | 1.250 to 2.000 inch | D and I | 2.000 to 3.500 inch |
|  | E and J | 3.500 to 4.500 inch | F and K | 4.500 to 6.000 inch |
|  | M | 6.000 to 999.999 inch |  |  |
|  | Note: |
|  | G, H, I, J, K are for the AI (Auto-Index) Stations. |
| Type | Select a station type from drop-down list. |
| OTX | Display the X-axis distance between the origin point and the storage position. |
| OTY | Display the Y-axis distance between the origin point and the storage position |
| Key | Place a check mark in this check box, which indicates that this station is a keyed station. Only shaped tools, such as rectangles and squares, can be installed in keyed stations. Non-keyed stations are available for round, center punch and burring tools. |
| Location Angle | Display the location station angle. The angle of the original station is 0 degree. |
| DZ | Display the Dead Zone number |
| DZX | Display the X range of the Dead Zone. |
| DZY | Display the Y range of the Dead Zone. |

| See: | Create or Remove a PDC Turret Type |
| --- | --- |
|  | Adding or Deleting a PDC Station |
|  | Turret Type(PDC) Window Short Cut Menu |

## 24.2 Create a New PDC Turret Type

To create a new empty turret type (PDC) file

| 1. | Select the Turret Type (PDC) under Public in the left Tree View pane. |
| --- | --- |
| 2. | Right-click to display the shortcut menu. Select New to Turret Type (PDC) Preference. |
| 3. | A new turret type file “New “ is created. You can rename the file and click it to display the correlative information in the Display Area pane where you can add stations. See: Adding or Deleting a PDC Station. |

To remove a turret type (PDC):

| 1. | In the top Preference File pane, right click a turret type you want to delete and a shortcut menu will display. |
| --- | --- |
| 2. | Select Delete and a message box will appear. |
| 3. | Click OK button. |

| See: | Turret Type (PDC) Window Items |
| --- | --- |
|  | Adding or Deleting a PDC Station |
|  | Turret Type(PDC) Window Short Cut Menu |

## 24.3 Adding a New PDC Station

Click a turret type in the Preference File pane and the correlative stations information will display in the Display Area pane below. Alternatively you can double click a turret type, the Turret Type (PDC) window will appear.

Double-click the Station cell in the last row, and type a number to define the station number. After specifying the relevant station information, click <Enter> to confirm your changes

Notes:

The station number you type must be unique; otherwise the system will display a warning message.

To delete a station, right click the station you desire and a shortcut menu will appear.

Select Delete and a message box will prompt.

Click Yes button to delete the selected station.

| See: | Turret Type (PDC) Window Items |
| --- | --- |
|  | Create or Remove a PDC Turret Type |
|  | Turret Type(PDC) Window Short Cut Menu |

## 24.4 Turret Type(PDC) Window Short Cut Menu

In the Turret Type (PDC) window, you can append or remove a dead zone for a station.

Right click a station you desire and a shortcut menu appear.

| Option | Description |
| --- | --- |
| Append Dead Zone | Select this option to display the Dead Zone window, where you can add or modify a dead zone range for a station. |
|  | Select a dead zone and click Add button to assign the dead zone for the selected station. |
| Remove Dead Zone | Select this option to delete the dead zone settings for the selected station. A message box will prompt. |
|  | Click Yes button. |

| See: | Turret Type (PDC) Window Items |
| --- | --- |
|  | Create or Remove a PDC Turret Type |
|  | Adding or Deleting a PDC Station |

# Chapter 25: Result View

The main window will expand and display the results when the nesting process is complete.

In the Result View area, you can preview many nesting details, such as utilization, time study and the sheet layout, etc.

You can also manually edit the nesting result and generate new NC code here until you are satisfied.

Example

| 1. | Right-click the Auto Execute button in the main window and select Auto Execute (Nesting) from the shortcut menu, the system will run in sheet mode. Alternatively, you can select Make Sheet in the Nesting Schedule window or click the Auto Execute button directly to perform the same action. |
| --- | --- |
|  | The following window appears when the sheet mode nesting process is complete. |
| 2. | Right-click the Auto Execute button and select Auto Execute (Individual Part) from the shortcut menu, the system will run in part mode. Alternatively, you can select Make Part in the Nesting Schedule window to perform the same action. |
|  | The following window appears when the part mode nesting process is complete. |
| 3. | Right-click the Auto Execute button and select Auto Execute (Pre-Nesting) from the shortcut menu, the system will run in pre-nesting mode. |
|  | The following window appears when the pre-nesting process is complete. |

| See: | Nesting Result List |
| --- | --- |
|  | Part Layout Shortcut Options |
|  | Information Panel |

## 25.1 Nesting Result List

Nesting Result List displays various nesting information, such as Sheet Name, Material Type, Sheet Size, Utilization, Time Study, etc.

You can arrange the column headings order by dragging and dropping them.

You can also right-click on any column heading to display the shortcut menu and decide which items you would like to display on the Nesting Result List.

See: Column Heading Shortcut Menu

| Column Heading | Description |
| --- | --- |
| No | The number of the nesting result. Select a No cell. The selected cell will be highlighted. Then right-click this cell to display the shortcut menu. The options on the menu allow you to save NC data, schedule or display other nesting information, etc. See: No. Column Shortcut Menu |
| Mouse Position | Display the coordinates of the current mouse pointer in the layout area. |
| Sheet Name | The name of the sheet. You can specify the sheet name in the Schedule Preference window. See: Sheet Name |
| Result | The result of the nesting process. Either the star or the tick symbol indicates the nesting is successful. The exclamation symbol indicates there are errors during the process. You can click the exclamation symbol to display the Warning Information window. See: Warning Information Window |
|  | Or |  |
|  | Nesting successful | Nesting error |
| Utilization | The utilization rate of the sheet. |
| Time Study | The total time of processing the sheet. You can click the cell to display the Time Study Information window and view the detailed time information. See: Time Study Information Window |
| Qty. | The quantity of the sheet that will have the same nesting results. You can click the cell and specify the quantity by typing an integer directly or using the up/down arrow button. |
| Machine | The name of the machine that is used to process the sheet. |
| Mat. Code | The code of the material. |
| Mat. Type | The type of the material. |
| Thickness | The thickness of the material. |
| Distance Between Two Points | The distance between the two points that you click in the part layout area. |
| Sheet X | The horizontal dimension of the sheet. |
| Sheet Y | The vertical dimension of the sheet. |
| Due Date | The due date of the process. |
| Process Date | The start date of the process. |
| Setup Info. #1 | Display the Turret Name. |
| Setup Info. #2 | It is NOT available now for punch machines. |
| Setup Info. #3 | Display the Material Name. |
| Setup Info. #4 | Display the Sheet Comment. |
| Setup Info. #5 | It is NOT available now for punch machines. |

| See: | The No. Column Heading Shortcut Menu |
| --- | --- |
|  | The Column Heading Shortcut Menu |
|  | The Warning Information Window |
|  | The Time Study Information Window |

| See: | Part Layout Shortcut Options |
| --- | --- |
|  | Information Panel |

### 25.1.1 The No. Column Heading Shortcut Menu

In the nesting result list of sheet mode, select and right-click one cell in the No. Column to display the shortcut menu.

The options on the menu allow you to save NC data, schedule and display other nesting information, etc.

In the nesting result list of part mode, select and right-click one cell in the No. Column to display the shortcut menu.

The options on the menu allow you to save the NC data, schedule and the tool assignment of the part as *.SY5 file, etc.

| Option | Description |
| --- | --- |
| Save NC data | Save the NC data. See: Save NC data |
| Save Sy4 | Save all current nesting results except the preferences. See: Save SY4 |
| Save Schedule/Output Report | Save the nesting result schedule. See: Save Schedule/Output Report |
| Output Report | This option allows you to decide which information to output by placing a check mark in the corresponding check box in the Report Output window. You can also right-click to display the shortcut menu in the part layout area, and then select Output Report to open the Report Output window. See: Output Report |
| Delete Sheet | Delete the sheet you have selected. See: Delete Sheet |
| Display Material Info | Display the Material Info. See: Display Material Info. |
| Display Plan Info | Display the Plan Info. See: Display Plan Info |
| Row Height | Adjust the height of the row. See: Row Height |
| Save Part | Save the tool assignment information for the part to the database you have selected. See: Save Part |
| Save SY5 as File | Save the tool assignment information for the part as a *.SY5 file. See: Save SY5 as File |
| Save Sy5 to NestingPlan | Save the tool assignment information for the part to the nesting plan. A symbol will appear in the CAD column of the Nesting Schedule window. |

| See: | Save NC data |
| --- | --- |
|  | Save Sy4 |
|  | Save Schedule/Output Report |
|  | Output Report |
|  | Delete Sheet |
|  | Display Material Info. |
|  | Display Plan Info. |
|  | Row Height |
|  | Save Part |
|  | Save SY5 as File |

| See: | The Column Heading Shortcut Menu |
| --- | --- |
|  | The Warning Information Window |
|  | The Time Study Information Window |

#### 25.1.1.1 Save NC Data

Select Save NC data from the menu to save the NC data.

Note:

You can save the NC data either to the disk or to the database. See: System Setting

To save the NC data,

| 1 | Select Save NC data from the menu. |
| --- | --- |
| 2 | If you select File in the Database: drop-down list in the System Setting window, the Input O Number dialog will appear. Place a check mark in the O Number check box and type an O Number in the text box, then click OK to proceed. You can also decide whether to save another *.SY2 file together with the NC data by placing a check mark in the Save SY2 check box. |
|  | Note: If you select MiniSDD or SDD in the Database: drop-down list in the System Setting window, different windows will display. See: System Setting |
| 3 | The Browse For Folder dialog appears. Navigate to the destination folder, and click OK to save. |

| See: | Save Sy4 |
| --- | --- |
|  | Save Schedule/Output Report |
|  | Output Report |
|  | Delete Sheet |
|  | Display Material Info. |
|  | Display Plan Info. |
|  | Row Height |
|  | Save Part |
|  | Save SY5 as File |

#### 25.1.1.2 Save SY4

Select Save Sy4 from the menu to save Sy4.

To save Sy4,

| 1. | Select Save Sy4 from the menu. |
| --- | --- |
| 2. | If you select File in the Database: drop-down list in the System Setting window, the Save As dialog will appear. Navigate to the destination folder and specify a name in the File name: text box, and then click Save to finish. |
|  | Note: If you select MiniSDD or SDD in the Database: drop-down list in the System Setting window, different windows will display. See: System Setting |

| See: | Save NC data |
| --- | --- |
|  | Save Schedule/Output Report |
|  | Output Report |
|  | Delete Sheet |
|  | Display Material Info. |
|  | Display Plan Info. |
|  | Row Height |
|  | Save Part |
|  | Save SY5 as File |

#### 25.1.1.3 Save Schedule/Output Report

Select Save Schedule/Output Report from the menu to save the schedule and output the report.

To save the schedule,

| 1. | Select Save Schedule/Output Report from the menu. |
| --- | --- |
| 2. | The Save Schedule window will appear. Specify a name in the Schedule Name: text box and place a check mark in the Save Schedule check box, then click OK to proceed. |
| 3. | If you select File in the Database: drop-down list in the System Setting window, the Browse For Folder dialog will appear. Navigate to the destination folder, and click OK to finish. |
|  | Note: If you enable Save the Turret Information function in the Save Schedule window, the Save Turret window will appear prior to the Browse For Folder dialog. Just click OK to continue. |
|  | Note: If you select MiniSDD or SDD in the Database: drop-down list in the System Setting window, different windows will display. See: System Setting |

To output the report,

| 1. | Select Save Schedule/Output Report from the menu. |
| --- | --- |
| 2. | The Save Schedule window will appear. Specify a name in the Schedule Name: text box and place a check mark in the Report Output check box to open the output item list. Place check marks in the check box of each item you want to output, then click OK to proceed. |
| 3. | The Report window appears. You can preview different report pages by clicking the corresponding items in the Report tree view pane. |
| 4. | Select Export from the File menu or click Export icon on the shortcut bar directly. The Browse For Folder dialog appears. Navigate to the destination folder, and click OK to output the report. |
|  | Note: You can also select Output Report from the shortcut menu to perform the same action. See: Output Report |

| Option | Description |
| --- | --- |
| Schedule Name | Specify the schedule name. The system will automatically create a schedule name according to the settings defined in the Schedule window. |
| Sheet List | The sheet list displays the nesting information for all the sheets. You can place check marks in the Select column to select sheets. You can also right-click the column heading to display the shortcut menu and place check marks before the items you want to display in the Sheet List. See: Nesting Result List |
| Report Output | Place a check mark in Report Output check box to display the following options. You can decide what report to be output by placing a check mark in the corresponding check box. See: Output Report |
| XML Output | Place a check mark in XML Output check box to output the XML information. |
| Save the Turret Information | You can select to save the turret information automatically or manually. |
|  | If you select the Automatic option, click the Detail button to continue. |
|  | The Save the Turret Information dialog box appears. You can select to overwrite the original turret settings or save the turret settings as the new. Then click OK to continue. |
|  | If you select the Manual Select option, click the Select button to continue. |
|  | The Save the Turret Information window appears. You can place a check mark before the turret item that you want to save. You can also select to input the turret name at the bottom left. Then click OK to continue. |
| Select All | Click this button to select all the sheets in the Sheet List. |
| Reset All | Click this to deselect all the sheets. |
| OK | Click this button to save the schedule data. |
| Cancel | Click this button to cancel all the settings you have made. |

| See: | Save NC data |
| --- | --- |
|  | Save Sy4 |
|  | Output Report |
|  | Delete Sheet |
|  | Display Material Info. |
|  | Display Plan Info. |
|  | Row Height |
|  | Save Part |
|  | Save SY5 as File |

#### 25.1.1.4 Output Report

Select Output Report from the menu to output the report.

To output the report,

| 1. | Select Output Report from the menu. |
| --- | --- |
| 2. | The Output Report window appears. Specify a name in the Schedule Name: text box and place check marks in the check box of each item you want to output, then click OK to proceed. |
| 3. | The Report window appears. You can preview different report pages by clicking the corresponding items in the Report tree view pane. |
| 4. | Select Export from the File menu or click Export icon on the shortcut bar directly. The Browse For Folder dialog appears. Navigate to the destination folder, and click OK to output the report. |

| See: | Save NC data |
| --- | --- |
|  | Save Sy4 |
|  | Save Schedule/Output Report |
|  | Delete Sheet |
|  | Display Material Info. |
|  | Display Plan Info. |
|  | Row Height |
|  | Save Part |
|  | Save SY5 as File |

#### 25.1.1.5 Delete Sheet

Select Delete Sheet from the menu to delete the selected sheets.

To delete sheets,

| 1. | Select the numbers of the sheet in the No. column that you want to delete. Right-click to open the shortcut menu and select Delete Sheet. |
| --- | --- |
| 2. | A warning message will appear. |
| 3. | Select Delete after saving the missing part plan to delete sheets after saving. Select Delete Sheets to delete sheets without saving. Select Cancel to cancel the operation. |

| See: | Save NC data |
| --- | --- |
|  | Save Sy4 |
|  | Save Schedule/Output Report |
|  | Output Report |
|  | Display Material Info. |
|  | Display Plan Info. |
|  | Row Height |
|  | Save Part |
|  | Save SY5 as File |

#### 25.1.1.6 Display Material Info

Select Display Material Info from the menu to display the material information.

To display material information,

| 1. | Select Display Material Info from the menu. |
| --- | --- |
| 2. | The Material Info window will appear. You can view various material information here and sort by clicking the corresponding column heading. |

| See: | Save NC data |
| --- | --- |
|  | Save Sy4 |
|  | Save Schedule/Output Report |
|  | Output Report |
|  | Delete Sheet |
|  | Display Plan Info. |
|  | Row Height |
|  | Save Part |
|  | Save SY5 as File |

#### 25.1.1.7 Display Plan Info

Select Display Plan Info from the menu to display the plan information.

To display plan information,

| 1. | Select Display Plan Info from the menu. |
| --- | --- |
| 2. | The Plan Info window will display. You can view the plan information for the parts and sort by clicking the corresponding column heading. |

| Column Heading | Description |
| --- | --- |
| No | The number of the part. |
| Part Name | The part name. |
| Size | The part size. |
| Plan Qty (A) | The quantity of the parts scheduled to be processed. |
| Result Qty (B) | The quantity of the parts actually processed. |
| B-A | The value of Result Qty (B) minus Plan Qty (A). |
| Filler Part | The filler parts quantity that defined for the part. |
| Comment | The comments for the part. |

| See: | Save NC data |
| --- | --- |
|  | Save Sy4 |
|  | Save Schedule/Output Report |
|  | Output Report |
|  | Delete Sheet |
|  | Display Material Info. |
|  | Row Height |
|  | Save Part |
|  | Save SY5 as File |

#### 25.1.1.8 Row Height

Select Row Height to open the Row Height dialog and adjust the height of the row.

To open the dialog and adjust the row height,

| 1. | Select Row Height from the menu. |
| --- | --- |
| 2. | The Row Height dialog appears. Type a value in the Row Height: text box to change the height of the row. Click OK to save. |

| See: | Save NC data |
| --- | --- |
|  | Save Sy4 |
|  | Save Schedule/Output Report |
|  | Output Report |
|  | Delete Sheet |
|  | Display Material Info. |
|  | Display Plan Info. |
|  | Save Part |
|  | Save SY5 as File |

#### 25.1.1.9 Save Part

Select Save Part from the part mode shortcut menu to save the tool assignment information for the part.

To save part,

| 1. | Select Save Part from the part mode shortcut menu. |
| --- | --- |
| 2. | If you select File in the Database: drop-down list in the System Setting window, the Browse For Folder dialog will appear. Navigate to the destination folder, and click OK to save. |
|  | Note: If you select MiniSDD or SDD in the Database: drop-down list in the System Setting window, different windows will display. See: System Setting |

| See: | Save NC data |
| --- | --- |
|  | Save Sy4 |
|  | Save Schedule/Output Report |
|  | Output Report |
|  | Delete Sheet |
|  | Display Material Info. |
|  | Display Plan Info. |
|  | Row Height |
|  | Save SY5 as File |

#### 25.1.1.10 Save SY5 as File

Select Save SY5 as File from the part mode shortcut menu to save the tool assignment information for the part as a *.sy5 file.

To save SY5 as file,

| 1. | Select Save SY5 as File from the part mode shortcut menu. |
| --- | --- |
| 2. | The Browse For Folder dialog will appear. Navigate to the destination folder, and click OK to save the tool assignment information for the part as an SY5 file. |

| See: | Save NC data |
| --- | --- |
|  | Save Sy4 |
|  | Save Schedule/Output Report |
|  | Output Report |
|  | Delete Sheet |
|  | Display Material Info. |
|  | Display Plan Info. |
|  | Row Height |
|  | Save Part |

### 25.1.2 The Column Heading Shortcut Menu

In the nesting result list, you can right-click any column heading to display this shortcut menu. You can place check marks before the options in the menu to display them in the nesting result list.

| 1. | Select More… from the shortcut menu to display the Choose Details window. |
| --- | --- |
| 2. | You can place check mark before the item you want to display and change their positions in the nesting result list. You can also type a value in the Width of Selected Column (in pixels): text box to specify the column width for the selected items. |
| See: | The No. Column Heading Shortcut Menu |
|  | The Warning Information Window |
|  | The Time Study Information Window |

### 25.1.3 The Warning Information Window

| Or | If the nesting process is successful, the star or the tick symbol will appear in the Result column. |
| --- | --- |
|  | If any error occurs, the exclamation symbol will appear. |
|  | You can click the exclamation symbol to open the Warning window. |
|  | Click one cell to locate the corresponding error in the layout area. You can modify the settings according to the error information. See: Error No. |

| See: | The No. Column Heading Shortcut Menu |
| --- | --- |
|  | The Column Heading Shortcut Menu |
|  | The Time Study Information Window |

### 25.1.4 The Time Study Information Window

Click one Time Study cell to display the Time Study Information window.

The window lists the detailed time information and the punch tool usage information during the process.

| See: | The No. Column Heading Shortcut Menu |
| --- | --- |
|  | The Column Heading Shortcut Menu |
|  | The Warning Information Window |

## 25.2 Part Layout Shortcut Options

In the Nesting Result list, you can click the plus button  to display the part layout you have specified. You can also click  to hide the display.

In the Part layout area of the sheet mode, you can right-click to display the shortcut menu. The options on the shortcut menu allow you to view the part layout and make manual adjustments.

In the Part Layout area of the part mode, you can right-click to display the shortcut menu. The options on the shortcut menu allow you to view the individual part layout and make manual adjustments.

| Option | Description |
| --- | --- |
| Zoom In | When you select this option, the mouse pointer becomes a crosshair. Move the pointer into the layout area and click to zoom in. You can also draw a frame and zoom in the selected area. To change the zoom in ratio. See: Zoom In Ratio |
| Zoom Out | When you select this option, the mouse pointer becomes a zoom pointer. Move the pointer into the layout area and click to zoom out. You can also draw a frame and zoom out the selected area. To change the zoom out ratio. See: Zoom Out Ratio |
|  | Note: You can also use the mouse wheel to zoom in or out. |
| Move | When you select this option, the mouse pointer becomes a move pointer. Move the pointer into the layout area and hold on the left mouse button to move the sheet. |
| Zoom All | Select this option to display the entire sheet to fit the part layout area. |
| Auto Scale | Select this option to display all the parts to fit the part layout area. |
| Maximize Window | Select this option to maximize the current layout area window. |
| Shorten | Select this option to restore the maximized layout area window. |
| Display | Select the options in the Display submenu to display the corresponding information in the layout area. |
| Display All Parts Drawing For Grid | Select this option to display all parts drawing for grid in Auto-Execute (Pre-Nesting) Mode. |
|  | Place the check mark |
|  | Remove the check mark |
| Move | Select this option to display the movement path of the punch tool. |
| Arrow of Direction | This function is NOT available for punch machines. |
| Sequence Number | Select this option to display the processing sequence number. |
| Parts Number | Select this option to display the parts number. Same numbers indicate the same parts. |
| Error No | Select this option to display the error numbers. See: The Warning Information Window |
| Bend Line Mark | Select this option to display the bend line mark. |
| Macro Pattern Direction | This function is NOT available for punch machines. |
| Joint Mark | Select this option to display the joint mark. |
| Show part outside profile only | To only show outside profile of the part. |
|  | checked | unchecked |
| Print Result View | To make settings for the Print Result View option: |
|  | 1. In the part layout area, you can right-click to display the shortcut menu. Select Print Result View to open the Print window. |
|  | 2. Click Properties… tab to display the Properties window. After making settings, click OK to continue. |
|  | 3. Then you can click OK to print the result view. |
|  | Option | Description |
|  | Printer | Specify the printer information, such as name, status, type, where, and comment. |
|  | Print Range | Specify the print range. You can select to print all pages or specific pages. |
|  | Copies | Specify the number of copies by typing in exact number or scrolling the arrow buttons. |
|  | Properties… | Specify the printer properties in the aspects of advanced, paper/quality, finishing, effects, and destination. |
| Save Schedule/Output Report | To save the schedule/output report: |
|  | 1. In this window, you can specify the schedule name and save the scheduling information for one sheet or several sheets. You can also decide the information to be output and the method to save the turret information. After making settings, click OK to continue. |
|  | 2. The Save Turret dialog box appears. Click OK to continue. |
|  | 3. The Browse for Folder dialog box appears. Navigate to the destination folder. |
|  | Note: Depending on the database you select (SDD, MiniSDD or File), different windows will display. See: System Setting |
|  | 4. Click OK to save the schedule and output report information. |
|  | Option | Description |
|  | Schedule Name | Specify the schedule name. The system will automatically create a schedule name according to the settings defined in the Schedule window. |
|  | Sheet List | The sheet list displays the nesting information for all the sheets. You can place check marks in the Select column to select sheets. You can also right-click the column heading to display the shortcut menu and place check marks before the items you want to display in the Sheet List. See: Nesting Result List |
|  | Report Output | Place a check mark in Report Output check box to display the following options. You can decide what report to be output by placing a check mark in the corresponding check box. See: Output Report |
|  | XML Output | Place a check mark in XML Output check box to output the XML information. |
|  | Save the Turret Information | You can select to save the turret information in the automatic or manual way. |
|  |  | If you select the Automatic option, click the Detail button to continue. |
|  |  | The Save the Turret Information dialog box appears. You can select to overwrite the original turret settings or save the turret settings as the new. Then click OK to continue. |
|  |  | If you select the Manual Select option, click the Select button to continue. |
|  |  | The Save the Turret Information window appears. You can place a check mark before the turret item that you want to save. You can also select to input the turret name at the bottom left. Then click OK to continue. |
|  | Select All | Click this button to select all the sheets in the Sheet List. |
|  | Reset All | Click this to deselect all the sheets. |
|  | OK | Click this button to save the schedule data. |
|  | Cancel | Click this button to cancel all the settings you have made. |
| Output Report | See: Output Report |
| Save NC Data | Save the NC data for the nesting process. See Save NC data |
| Save MJC Data | Select this option to save the data of MJC, IJP, TK, etc. See Save MJC data |
| Do Stack | This option is used to execute the mode that is used to remove parts. You must define the Take Out options in the Machine Set window before you can use the Do Stack option on the shortcut menu. See Do Stack |
| To AP100 CAM | This function is not available for the moment. |
| To Simulation | Select this option to go to FabriSIM or AP100, which is the simulation program you selected in the System Setting window, to perform the NC program simulation. |
| Display Parts Info | Select this option to display the Part Info window, which displays the part information of the selected sheet such as the part size, the quantity of the parts scheduled to be processed, the quantity of the parts actually processed, etc. In the Part Info. window, click the Save Missing Part Plan button to save the part into an Assemble or another ideal folder. When you place check marks in the Consider the quantity of sheets processed and register the part quantity when saving the missing part plan check box, the system will consider the sheet quantity when saving the part plan. For example, the part quantity is 5 and the sheet quantity is 3, so the saved part quantity is 5X3 =15. |
| Display Plan Info | Displays the part information, such as the quantity of the parts that are scheduled to process and the quantity of the parts actually processed. See Display Plan Info. |
| Display Group Tools | Display the list of group tools. All of the tools are on the generated turret for this sheet processing. Select this option to display the ToolList For Schedule window. This window shows the schedule information, such as Machine Name, Material Name, Material Size, Turret Stations, and tools used for each sheet. See: ToolList For Schedule |
| Display Tools Info | Display the tools and tool information used. |
| Sequence Setting | Select to display Sequence Setting window. More details see: Sequence |
| Tool Sequence Setting | To make settings for the Tool Sequence Setting window: |
|  | 1. You can right-click the part layout area to display the shortcut menu. Then select Tool Sequence Setting option to open the Tool Sequence Setting window. |
|  | 2. For tools of same conditions, the system can group this tools as only one. You can click the Grouping button to group the selected tools. And you can click the Ungroup button to cancel the grouping. |
|  | 3. You can change the Tool Sort by click the upward arrow or downward arrow . |
|  | 4. You can define the Start Position or End Position by selecting one from the following five radio options. |
|  | 5. You can select the direction from the Direction drop-down list: Auto, X or Y. You can see the divide number of sheet. And you can also play the check mark in One Direction and AI Sort by Angle check box. |
|  | 6. After finishing settings, you can click OK to continue. |
|  | 7. The following dialog box appears. You can click Yes to re-sequence now. |
| Begin TK Edit | This function is used to edit TK and IJP. Before using this function, you should enable TK and IJP device for the machine. See Begin TK Edit |
| Save SY5 In Sheet | You can save the tool assignment information of the part as a *.SY5 file in the Result View list. To save SY5 in sheet: |
|  | 1. In the Nesting Result list, click the plus button to display the part layout you have specified. In the part layout area, right-click to display the shortcut menu and select Save SY5 in sheet. |
|  | 2. Click one part to open the Save As window (the pattern of the part you select will turn orange) and select the destination folder in Save in dialog. Name the file you want to save in the File name dialog box and click Save button. |
|  | Note: Depending on the database you select (SDD, MiniSDD or File), different windows will display. See: System Setting |
| Edit | Select this option to go to the Manual Edit Mode. See Manual Edit Mode |
| Save the Part | Save the part nesting result as a SY5 file. |
| Manual Tool Assign | Get in the Manual Tool Assignment mode, and the options in the shortcut menu allow you to edit the tool assignment of the part. See Manual Tool Assignment |

| See: | Save MJC Data |
| --- | --- |
|  | Do Stack |
|  | Begin TK Edit |

| See: | Nesting Result List |
| --- | --- |
|  | Information Panel |

### 25.2.1 Save MJC Data

In the result view, you can select Saving MJC Data from the shortcut menu to save the MJC, IJP, and TK data.

Note:

Make sure you have selected File as the Database type in the System Setting window.

Example

| 1. | Open the Machine Set window. And enable the MJC, IJP and TK devices. |
| --- | --- |
| 2. | Specify the relevant settings in the Peripherals window. |
| 3. | Perform the auto execution to process the parts. |
| 4. | Click the number of the sheet. Right-click the part layout area to open the shortcut menu and select Save MJC Data. The Save As dialog box appears. Navigate to the folder where you want to save the NC data. Type an appropriate name in the File name: text box and then click Save. The data will be saved with the filename extension of *.SY2. |

| See: | Do Stack |
| --- | --- |
|  | Begin TK Edit |

### 25.2.2 Do Stack

If TK device is available, you can select Do Stack from the part layout shortcut menu to manually edit the position to stack parts, and then save the changes to the *.SY2 file.

Example

| 1. | In the Machine Set window, navigate to the Take-Out Information panel under Peripherals. Place a check mark in the Taking Out check box, and select PartRemoverll from the Type of Taking Out: drop-down list. |
| --- | --- |
| 2. | Specify the Maximum Height, Table Size X and Y and Maximum Weight in Stacking Height section. |
| 3. | In the Peripherals window, click the Taking Out tab, and place a check mark in the Taking Out On/Off check box. |
| 4. | In the Process After Cutting table of Process After window, select TK as the process after methods. |
| 5. | After performing the auto execution, right-click the part layout and select Do Stack. |
| 6. | The CompStackInterface window displays the places to stack the parts. You can drag and drop the parts to the desired position, and click OK to save your changes. |

| See: | Save MJC Data |
| --- | --- |
|  | Begin TK Edit |

### 25.2.3 Begin TK Edit

This function is used to edit TK and IJP. Before using this function, you should enable TK and IJP device in the Machine Set window, and select TakeOut as the process after method. See: Taking Out Conditions and IJP

To edit TK Settings

| 1. | Right-click in the part layout area, and select Begin TK edit to switch to the TK edit mode. |
| --- | --- |
| 2. | Part name is listed on the left side of the Edit Pickup/IJP window. Select the part you want to edit and the star symbol before the part name becomes blue when you edit the part. Note: Pickup Edit option is selected by default. |
| 3. | Drag the TK arm to the proper position, and click the Vacuum cups with which you want to absorb the part. You can re-click the active vacuum cups to deselect. |
| 4. | Click OK to close the window. Right-click and select End TK Edit to finish the operation. |

To edit IJP

| 1. | Right-click in the part layout area, and select Begin TK edit to switch to open Edit Pickup/IJP window.. |
| --- | --- |
| 2. | Select IJP Edit. |
| 4. | Move the pointer over the IJP, drag it to the ideal place. |
| 5. | Click OK to close the window. Right-click and select End TK Edit to finish the operation. |

| See: | Edit of Pickup/IJP Information window |
| --- | --- |

#### 25.2.3.1 Edit of Pickup/IJP Information window

In the Edit of Pickup/IJP Information window, you can change the IJP position. And you can also specify the TK arm position, and decide which cups or magnets will be used to absorb the parts. See: Begin TK Edit

| Items | Descriptions |
| --- | --- |
|  | Vacuum cups available |
|  | The vacuum cups that have been selected to absorb the part. |
|  | Magnet available |
|  | The Magnets cups that have been selected to absorb the part. |
| Single ARM Move | Select this option, and you can move one TK arm at a time. |
| Both ARM Move | Select this option, and you can move both TK arms at the same time. |
| VX | VX is the horizontal spacing, measured from the part origin (Lower left corner) to the origin of the left arm (Lower left corner). |
| VY | VY is the vertical spacing, measured up or down from the part origin (Lower left corner) to the origin of the left arm (Lower left corner). |
| VDIS1 | VDIST is the distance measured from the one side of one arm to the corresponding side of the other arm. |
| VDIS2 | This is not available now. |
| Increment | Increment value to alter VX, VY or VDIS1 |
| Auto Detect | Automatically decides how to pick up the part. |
| Ignore Hole | Place a check mark in the check box and type a value in the Size: text box, the system will ignore hole whose largest dimension is equal or smaller than the value in the text box. |
| IJP Edit | Edit the IJP position |
| PickUp Edit | Edit the pick up conditions. |
| An edit result is reflect in the same part in all sheets | Apply the modification results to the same parts in all the sheets. |
| An edit result is reflect in the same part on the same sheet | Apply the modification results to the same parts on the current sheet. |
| None | Only apply the modification results to the current parts. |

| See: | Save MJC Data |
| --- | --- |
|  | Do Stack |

## 25.3 Information Panel

The Information Panel is located along the right side of the Parts Layout area. In this panel, you can view the parts’ information, the error information and the NC code.

| See: | The Parts Information Panel |
| --- | --- |
|  | The Error List Panel |
|  | The NC Panel |

| See: | Nesting Result List |
| --- | --- |
|  | Part Layout Shortcut Options |

### 25.3.1 The Parts Information Panel

| 1. | You can click the Parts Info tab to display the part information. You can drag the scroll bar to show all information: No., part quantity, part comment, part name, material type, material thickness, material name, weight, unfold X size, unfold Y size, rectangle area, area with holes, area without holes, group ID and priority. |
| --- | --- |
| 2. | You can right-click the column area to select options in the shortcut menu. |
|  | Note: You can also right-click the part layout area to display the shortcut menu, and select Display Parts Info to display the Parts Info window. |

| See: | The Error List Panel |
| --- | --- |
|  | The NC Panel |

### 25.3.2 The Error List Panel

After displaying the parts layout, you can click the Error List tab to display the error information. See Warning Information Window

| See: | The Parts Information Panel |
| --- | --- |
|  | The NC Panel |

### 25.3.3 The NC Panel

After displaying the parts layout, you can click the NC tab to display the NC information. In this panel you can edit the NC program.

To edit an NC program:

| 1. | Right click the NC program area to display the shortcut menu. Select Edit Mode to get into the Edit mode to modify the code. |
| --- | --- |
| 2. | In the Edit mode, edit the NC program. |
| 3. | After editing the NC program, right-click the NC program area to display the shortcut menu. Select Save and End the Modification to save the changes. Select Ignore and End the Modification to exit the Edit Mode without saving the changes. |

| See: | The Parts Information Panel |
| --- | --- |
|  | The Error List Panel |

# Chapter 26: Manual Edit Mode

Dr.ABE Blank allows you to edit part layout manually by switching to Manual Edit Mode.

After auto execution, you can right-click on the Part Layout area in the sheet mode to open shortcut menu, and select Edit from the shortcut menu to enter the Manual Edit mode.

If you select Auto Execute (Individual Part) to perform nesting process in part mode, you can select Manual Tool Assign from the shortcut menu to switch to the Part Edit mode.

Note:

You can also click  (Part Edit) button in Manual Edit mode to switch to Part Edit mode.

| See | Manual Edit Mode Shortcut Menu |
| --- | --- |
|  | Manual Edit Mode Parameter Panel |
|  | Confirm/Display Setting |
|  | Move |
|  | Add Part |
|  | Remove |
|  | Remnant Edit |
|  | Change Material |
|  | Part Grid |
|  | Sequence Edit |
|  | Reposition Command |
|  | Conform Schedule Tool |
|  | Add New Sheet |
|  | Option |

## 26.1 Manual Edit Mode Shortcut Menu

Right-click part layout area in the Manual Edit mode, a shortcut menu will appear.

| Option | Description |
| --- | --- |
| Zoom In | Select this option to magnify the view of the selected area. |
| Zoom Out | Select this option to reduce the view of the selected area, allowing you to see more of the sheet area. |
| Move | Select this option to move the part. |
| Zoom All | Select this option to get an entire view of the sheet. |
| Auto Scale | Select this option to display all the parts to fit the view. |
| Maximize Window | Select this option to cover the window to full screen. |
| Shorten | Select this option to restore the maximized window. |
| Display Parts Info | Select this option to display the information of the parts nested on the sheet you have specified. The Parts Info window displays the part name, part quantity, part comment, material name, material type, material thickness, weight, size, group ID, priority etc. |
| Undo | Select this option to cancel your last operation. |
| Redo | Select this option to execute your last operation again. |
| Show part outside profile only | Select this option to display part outside profile only. As for complex part, you may use this option to reduce memory usage of the system. |

| See | Manual Edit Mode Shortcut Menu |
| --- | --- |
|  | Manual Edit Mode Parameter Panel |
|  | Confirm/Display Setting |
|  | Move |
|  | Add Part |
|  | Remove |
|  | Remnant Edit |
|  | Change Material |
|  | Part Grid |
|  | Sequence Edit |
|  | Reposition Command |
|  | Conform Schedule Tool |
|  | Add New Sheet |
|  | Option |

## 26.2 Manual Edit Mode Parameter Panel

There are toolbar and parameter section in the Parameter panel. The toolbar consists of Sheet Edit toolbar and Part Edit toolbar (Click Part Edit button to show Part Edit toolbar and enter Part Edit mode.). The Parameter section is where you can specify detailed settings for each option in the toolbar.

Sheet Edit Toolbar

| Icon | Button Name | Description |
| --- | --- | --- |
|  | Confirm/Display Setting | This option allows you to display and confirm part/trace/pattern specified. |
|  | Move | This option allows you to move, rotate and copy part as you set in Parameter section. |
|  | Add Part | This option allows you to add part from SDD or file. |
|  | Remove | This option allows you to delete part or trace. |
|  | Part Edit | Click this button to enter Part Edit mode. See Manual Tool Assignment |
|  | Remnant Edit | This option allows you to cut/edit remnant for better utilization purpose. |
|  | Change Material | This option allows you to change size and sheet code of material. |
|  | Part Grid | This option allows you to specify the conditions to process part grid. |
|  | Sequence Edit | This option allows you to define the sequence to process the parts. |
|  | Reposition Command | This option allows you to add reposition in sheet for clamp. |
|  | Confirm Schedule Tool | This option allows you to check tools in use and station status of a sheet or a schedule. |
|  | Add New Sheet | This option allows you to append a new sheet when you are editing a sheet. |
|  | Option | This option allows you to select whether specified message displays or not when exiting Edit mode, control window size and check collision. |
|  | Scrap Cutting | This option allows you to define scrap-cutting method in order to take out heavy skeleton more conveniently. This function is not available for EM-L machine. |

Part Edit Toolbar

| Icon | Button Name | Description |
| --- | --- | --- |
|  | Confirm/Display Setting | This option allows you to display and confirm part/trace/pattern specified. |
|  | Save Template | This option allows you to save settings as template and use this template to process similar pattern in the future more conveniently. |
|  | Delete Trace | This option allows you to delete specified process trace. |
|  | Joint Edit | This option allows you add or edit joint. |
|  | End Value | This option allows you to modify the process after methods for the laser process. |
|  | Sequence Command in Part | This option allows you to change process sequence by mouse command or list command. |
|  | Lead In Edit | This option allows you to edit Lead In/Lead Out settings, such as length, angle and position. |
|  | Change the Tool Assignment | This option allows you to modify tool assignment for specified pattern. |
|  | Assign Tools-Lines | This option allows you to assign single D or double D tools to specified line. |
|  | Layout Between Single Hit | This option allows you to assign single hit tools to the pattern composed of intersection line. |
|  | Merge | This option allows you to assign tools to match tool element with pattern element. |
|  | Stretch | This option allows you to lengthen process path along moving direction and modify process angle on pattern-by-pattern basis. |
|  | Shift | This option allows you to move tool along the pattern edge in positive or negative direction. |
|  | Direct Assignment | This option allows you to assign tool of specified shape to punch out. |
|  | Move/Copy Tool | This option allows you to move or copy the specified tool assignment. |
|  | Apply Assignment to the Same Inner | This option allows you to apply the assignment in specified inner to all the same inner or the same inner you specify. |
|  | Fix Sequence Order | This option allows you to fix the sequence in processing one loop. |
|  | Change the Nibbling Pitch | This option allows you to modify moving pitch when nibbling tool is processing pattern. |
|  | Laser Hole Division | This option allows you to specify cutting method and Lead In method for laser hole division. |
|  | Show Tool | This option allows you to view the tool assigned in specified pattern. |
|  | Option | This option is the same with that in Sheet Edit Toolbar. |

| See | Manual Edit Mode Shortcut Menu |
| --- | --- |
|  | Manual Edit Mode Parameter Panel |
|  | Confirm/Display Setting |
|  | Move |
|  | Add Part |
|  | Remove |
|  | Remnant Edit |
|  | Change Material |
|  | Part Grid |
|  | Sequence Edit |
|  | Reposition Command |
|  | Conform Schedule Tool |
|  | Add New Sheet |
|  | Option |

## 26.3 Confirm/Display Setting

In the Manual Edit mode, click  button to open the Confirm/ Display Setting panel.

These options allow you to check information about part, trace and pattern.

| Item | Description |
| --- | --- |
| Part | Selected Part to display the basic information of the selected part, including Part Name, Size X, Size Y, Sheet Pattern Quality and Weight. |
| Trace | Select Trace to display the information of the selected trace, including Pattern, Base Point X, Base Point Y, C-axis Value, T No, Management Name, Shape, Angle, Dim X, Dim Y, Axis Speed, M Code and Delay. |
|  | If you select laser trace, the following information will appear: |
| Pattern | Select Pattern to display CAD information of the selected line. |
| Every Hit View | If you select this option, all the tool hits will display in pattern processed. |
|  | Every Hit View disabled. | Every Hit View enabled. |
| Process Direction | Place a check mark in the check box, the system will mark the process direction with arrows. |
| Display Tools by Color | Place a check mark in the check box, the system will use color to display either tools of specified shape or the specified tool. |
| Detail | You can customize color to display tool shape and individual tool. See Example |
|  | Note: |
|  | This function takes effect only when the Display Tools by Color option is selected. |
| Tool Shape | This option allows you to define tools of different shape with different color. All tool shapes are listed in the Tool Shape window. |
| Individual Setting | This option allows you to define specified tools with different color. The tools and tool information used in the current process are listed in the Individual Setting window. |

Example:

| 1. | Click Detail button and the Tool Shape window appears by default. |
| --- | --- |
| 2. | Click the cell before SQ to open Color dialog. |
| 3. | Select one color and click OK |
| 4. | The cell you clicked will show the color you set in Color dialog. |
| 5. | Click Preview button to reflect immediately the changes to pattern processed by specified tool shape. Click OK to finish the setting. |
| 6. | Place a check mark in the Display Tools by Color check box and patterns processed by SQ tool are displayed by color you selected. |

| See | Manual Edit Mode Shortcut Menu |
| --- | --- |
|  | Manual Edit Mode Parameter Panel |
|  | Confirm/Display Setting |
|  | Move |
|  | Add Part |
|  | Remove |
|  | Remnant Edit |
|  | Change Material |
|  | Part Grid |
|  | Sequence Edit |
|  | Reposition Command |
|  | Conform Schedule Tool |
|  | Add New Sheet |
|  | Option |

## 26.4 Move

In the Manual Edit mode, click  button to open Rotate/Move/Copy the Part panel.

| Option | Description |
| --- | --- |
| Move Pitch X | Move part to specified position in X direction. You can click the arrow button next to Move Pitch X: text box to specify the value or type a value in the box directly. See Move part |
| Move Pitch Y | Move part to specified position in Y direction. You can click the arrow button next to Move Pitch Y: text box to specify the value or type a value in the box directly. See Move part |
| Rotate Pitch | Rotate part by specified angle. Click the arrow button next to the Rotate Pitch: text box to change degree or type a value in box. See Rotate part |
| Copy the Part | Place a check mark in this option to copy specified part. See Copy part |
| Adjacent Mode | If you select this option, the system will move the part to the ideal place that is adjacent to a part or the sheet border. In this case, the sheet will be processed economically. You cannot, however, move the part to overlap the other parts or move it off the sheet. |
| Display Part-Spacing | This option is not available now. |
|  | Generally the system will nest parts according to settings specified in Nest Preference. Here you can redefine space between parts by the following options. After setting, you can click Nest Again button to nest parts. |
| Extending Direction | Select this option to determine extending direction after nesting again. You can select Direction X, Direction Y or Both Sides. |
|  | Note: This function is only available for rectangle nesting in Nesting Logic 1. See Nesting Logic 1 |
| Common Width | This option is used to define space between parts when you nest parts. You can click arrow button next to Common Width: text box to change common width or type space value in the box. |
|  | This option is used to calculate common width between parts automatically for optimum utilization of sheet. |
| Nest Again | Click this option to execute nesting according to settings above. See Nest Again |

Move a Part

| 1. | Select one part you want to move in Part Layout area. |
| --- | --- |
| 2. | Click arrow button next to Move Pitch X: drop-down list to set move distance value in X direction. |
| 3. | Click or button and the system will move the specified part right or left. |
|  | Note: You can also use the same method and click orto move part upwards or downwards in Y direction. |

Rotate a Part

| 1. | Select one part you want to rotate in part layout area. |
| --- | --- |
| 2. | Click arrow button next to Rotate Pitch: text box to set rotate angle value. |
| 3. | Click button to rotate the part clockwise to specified degree. Or click button to rotate the part counter-clockwise to the specified degree |
| 4. | If Part rotation affects tool assignment and end value, the following message box will appear. |
| 5. | Place a check mark in Change to the angle that ensures tool assignment check box and select a degree, then click OK button. The part will be rotated to the degree specified here. |
| 6. | Remove a check mark in Change to the angle that ensures tool assignment check box to rotate part according to the setting you specified in Rotate Pitch: text box. |
| 7. | You can also move pointer to the center point of the part you want to rotate. Rotate part to any degree directly when the pointer shape turns into Rotate Point. The number next to Rotate Point indicates the rotation degree. |

Copy a Part

| 1. | Place a check mark in Copy the Part check box and select a part you want to copy. |
| --- | --- |
| 2. | Hold down the left mouse button. When the point shape turns into, you can drag the copied part to a position you want. |

How to nest again

| 1. | Specify the settings as follows. |
| --- | --- |
| 2. | Click Nest Again button. Parts will be nested again. |
|  | Original nesting result | After nesting again |
| 3. | Specify the settings as follows. |
| 4. | Click Nest Again button and the system will nest parts again. |
|  | Original nesting result | After nesting again |
| 5. | Specify the settings as follows. |
| 6. | Click Nest Again button. Parts will be nested again. |
|  | Original nesting result | After nesting again |

| See | Manual Edit Mode Shortcut Menu |
| --- | --- |
|  | Manual Edit Mode Parameter Panel |
|  | Confirm/Display Setting |
|  | Move |
|  | Add Part |
|  | Remove |
|  | Remnant Edit |
|  | Change Material |
|  | Part Grid |
|  | Sequence Edit |
|  | Reposition Command |
|  | Conform Schedule Tool |
|  | Add New Sheet |
|  | Option |

## 26.5 Add Part

In the Manual Edit mode, click  button to open the Add Part panel.

These options allow you to append new part from SDD/MiniSDD database or by opening file.

Note:

| 1. | You can add various type of part, such as .DXF, .DWG, .PRT, .IGA, .SY4, .BMF and the like. |
| --- | --- |
| 2. | You can load more than one part at a time. |

| See | Manual Edit Mode Shortcut Menu |
| --- | --- |
|  | Manual Edit Mode Parameter Panel |
|  | Confirm/Display Setting |
|  | Move |
|  | Add Part |
|  | Remove |
|  | Remnant Edit |
|  | Change Material |
|  | Part Grid |
|  | Sequence Edit |
|  | Reposition Command |
|  | Conform Schedule Tool |
|  | Add New Sheet |
|  | Option |

### 26.5.1 Add parts by opening a file

Click File option in the Add Part panel to open the File Open Dialog window.

Select a file and click the Open button, a part you desire will be added on the existing sheet. Alternatively you can click the Search button from toolbar at the top of the window to look for a part you want to add.

| Item | Description |
| --- | --- |
| File Name | Displays the file name of the part selected currently. |
| Files of Type | Select a file type from drop down list to appear. |
| Material Type | Type a material type in this text box. |
| Thickness | Type a material thickness in this text box. |
| Unit | Select a thickness unit from drop down list. There are two options: Inch and Metric. |
| Show Preview | This option allows you to view the drawing of the part selected currently. |
|  | Click this button to open the Search window. |
|  | In this window, you can look for parts according to conditions you specify. |

### 26.5.2 Add parts from SDD database

Click SDD option in Add Part panel to open the Avon Data Selection Dialog window.

| Item | Description |
| --- | --- |
|  | : Indicates that it is a Sy4 file : Indicates that it is a Sy5 file : Indicates that it contains .IGA file : Indicates that it contains a file from AP100 : Indicates that it contains a NC data file. |
| Add Server | Click this button to open the Add/Remove Server window. |
|  | In this window, you can add server to system. |
| Data Type | Select a data type to display in the part list. |
| All Data | Displays all parts information. |
| Diagram/NC Data | Displays parts information either with diagram or with NC data. |
| Allow Diagram Data | Displays parts information with diagram data only. |
| No NC Data | Displays parts information without NC data. |
|  | Click the Find button to open the Find Data window. |
|  | In this window, you can specify the condition to search part. |
|  | Click this button to hide the 3D and unfold drawing to extend the part list section. |
|  | Click the 3D and unfold diagram button to display three-dimensions and two-dimensions drawing in the right of the window. |
|  | Click this button to open the Option window. |
|  | In this window, you can specify decimal number and language. |
| Part No. | Displays the name of the part selected currently. |
|  | Place a check mark in this check box and system list Sy4 files only. |
|  | Place a check mark in this check box and click the Open button, the Input Quantity window appears. |
|  | In this window, you can type a number in Part NO.: text box to specify part quantity you want to add directly. Alternatively, you can click the 0~9 Number button to enter part quantity. Click OK to confirm. |
|  | Select a part from the part list and click the Add button, the Selected Parts window appears. |
|  | If necessary, change quantity for a selected part or remove a selected part, and then click the Open button to add parts to the current sheet. |
|  | Select a part from the part list and click the Open button in Avon Data Selection Dialog window to add the part to the current sheet. |

Note:

If you select MiniSDD in System Setting, the MiniSDD Read window will be the following when you select SDD to add parts.

Example:

| 1. | After auto execution, the system nests the parts as follows. Right-click on the nesting part layout area and select Edit to switch to the Manual Edit mode. |
| --- | --- |
| 2. | Click button to open Add Part panel and select File or SDD option. |
| 3. | Select a part you want to add and click the Open button. |
|  | Note: |
|  | If the material/thickness of the added part is different from that of the existing part, the following dialog appears. |
| 4. | A new part appears in the working area. |
| 5. | Click to exit the Add Part panel and return to the Move panel. |
| 6. | Drag and drop the newly added part to the desired place. |

## 26.6 Remove

You can remove parts in Edit Mode. Click to open Delete Part panel.

| Item | Description |
| --- | --- |
| Parameter | The parameters in this section are used to edit removing. |
| Delete Object | Define the object you want to delete. |
| Inside Frame | Select this option to delete the parts within the specified frame. See To delete part inside the specified frame |
| Outside Frame | Select this option to delete the parts outside the specified frame. See To delete part outside the specified frame |
| Mouse Command | Define the command of the mouse. |
| All Selection | The selecting frame must include the whole part. See All Selection |
| Partial Selection | The part is selected though it is not completely included in the selecting frame. See Partial Selection |
| Select Same Parts At the Same Time | Place a check mark in the box. If you select one, other same parts can also be selected See Select Same Part at the Same Time |
| Only Same Angle | Place a check mark in the check mark box. If you select one, other same parts with the same angle can also be selected. See Only Same Angle |

To delete part inside the specified frame

| 1. | Select Inside Frame. |
| --- | --- |
| 2. | Click and drag the mouse to form a frame. |
| 3. | The part within the frame is selected and becomes orange. Click to delete. |

To delete part outside the specified frame

| 1. | Select Outside Frame. |
| --- | --- |
| 2. | Click and drag the mouse to form a frame. |
| 3. | The parts outside the frame are selected and become orange. Click to delete. |

All Selection

| 1. | Select Inside Frame and All Selection |
| --- | --- |
| 2. | Click and drag the mouse to form a frame. The frame must cover the parts to be selected completely. |
| 3. | The parts within the frame are selected and become orange. Click to delete. |

Partial Selection

| 1. | Select Inside Frame and Partial Selection. |
| --- | --- |
| 2. | Click and drag the mouse to form a frame. It is not necessary for the frame to cover the parts to be selected completely. |
| 3. | The parts can be selected although the frame does not cover them completely. Click to delete. |

Select Same Part at the Same Time

| 1. | Place a check mark in the Select Same Parts At the Same Time check box. |
| --- | --- |
| 2. | Use the frame to select one part |
| 3. | The other same parts are selected |

Only Same Angle

| 1. | If you place a check mark in the Only Same Angle check box. |
| --- | --- |
| 2. | Use the frame to select one part |
| 3. | Other same parts with the same angle are selected |

Note:

If you select Outside Frame and All Selection at the same time, you will select all the parts. It is the same if you select Outside Frame and Partial Selection at the same time.

| See | Manual Edit Mode Shortcut Menu |
| --- | --- |
|  | Manual Edit Mode Parameter Panel |
|  | Confirm/Display Setting |
|  | Move |
|  | Add Part |
|  | Remove |
|  | Remnant Edit |
|  | Change Material |
|  | Part Grid |
|  | Sequence Edit |
|  | Reposition Command |
|  | Conform Schedule Tool |
|  | Add New Sheet |
|  | Option |

## 26.7 Remnant Edit

In the Manual Edit mode, click button to open the Remnant Cutting/Edit panel.

These options are designed to specify process method, process after value and joint amount to generate remnant. You can also assign size range of tool to process remnant.

| Item | Description |
| --- | --- |
|  | Place a check mark in this check box to activate Add Remnant function. |
| Process Method | This option is used to define Process Method. You can decide to use laser or punch to create remnant. |
| Cutting Condition | This option is available when you select Laser option as Process Method. You can select from E001 to E003 as process method. |
| Cutting Method | This option is used to define which remainder of the sheet will be created as a remnant. |
| Vertical | Select this option to create a remnant sheet with a vertical cutting. |
| Horizontal | Select this option to create a remnant sheet with a horizontal cutting. |
| T Cut-Vertical Left | Select this option to create a remnant with shape cutting. |
| T Cut-Vertical Right | Select this option to create a remnant with shape cutting. |
| T Cut-Horizontal Top | Select this option to create a remnant with shape cutting |
| T Cut-Horizontal Bottom | Select this option to create a remnant with shape cutting. |
| Rectangle | Select this option to create a rectangle shape remnant. |
| L shape | This option is used to create an L shape remnant. There are four optional shapes and click the icon next to this option to change shape. |
|  | When a cutting method is selected, a different graph comprised of various parameters will appear in the upper area of the panel. |
|  | This graph is where you can define distances from process-starting point or process-ending point to the sheet edge, distances between cutting line and sheet edge, and specify the process direction. |
|  | You can type or select a value in these text boxes. Alternatively, you can move the pointer to the green line and drag the line in any direction when the pointer changes into a double-headed arrow. With the movement of the pointer on the sheet, these values in these text boxes update. |
|  | Example: |
|  | Select T Cut-Vertical Left as Cutting Method. Set the graph as this: |
|  | The remnant in the following illustration is generated according to settings above. |
|  | Note: |
|  | A positive value means the machine will over cut the material, while a negative value indicates the length of the material the machine fail to cut. |
| Process After Cutting | Specify a process after method from the drop down list. See Process After |
|  | If you select Punch as process method to create remnant, the Process After Cutting: drop down list will be the following: |
| Joint Amount | This option will be available only when Micro Joint or Wire Joint is selected in Process After Cutting: drop down list. Type or select a value in this text box to specify joint size. |
| Joint Number | This option will be available only when Micro Joint or Wire Joint is selected in Process After Cutting: drop down list. Type or select a value in this text box to specify joint number. |
| Horizontal | Type or select a value to specify quantity of joint you want to create in X direction. |
| Vertical | Type or select a value to specify quantity of joint you want to create in Y direction. |
| Cutting start Form | This option is used to decide cutting start form. There are two options. This option is available when you select Laser option as Process Method. |
|  | Cutting without lead-in. |
|  | Cutting with lead-in. Click this button to active Approach length: text box. |
|  | Type or select a value in the Approach length: text box to decide the length of lead-in. |
|  | without lead-in |
|  | With lead-in |
| No pierce | Place a check mark in the check box and the system will execute cutting without pierce. This option is available when you select Laser option as Process Method. |
|  | Cutting Start without pierce |
|  | Cutting Start with pierce |
| Tool Size X/Y | This option will be available when you select Punch as process method. These options allow you to specify size range of tool that is used to cut the remnant. Type or select a value in the first box to define the minimum value and a value in the second box to define the maximum value. Tool with X/Y size within this range will be used to process remnant. |
|  | This option is used to delete the existed cutting line. Move the pointer to the cutting line until the line becomes orange and click to select it, and then click Delete button. |
|  | Example: |
|  | 1. There exists an cutting line in the following sheet. |
|  | 2. Move the pointer to the cutting line until the line becomes orange |
|  | 3. Click to select it and the cutting line becomes green. |
|  | 4. Click Delete button to delete it. |

Note:

If the cutting line intersects with clamp as follows, when you click button, a warning message box will appear.

| See | Manual Edit Mode Shortcut Menu |
| --- | --- |
|  | Manual Edit Mode Parameter Panel |
|  | Confirm/Display Setting |
|  | Move |
|  | Add Part |
|  | Remove |
|  | Remnant Edit |
|  | Change Material |
|  | Part Grid |
|  | Sequence Edit |
|  | Reposition Command |
|  | Conform Schedule Tool |
|  | Add New Sheet |
|  | Option |

## 26.8 Change Material

In the Manual Edit mode, click  button to open the Change Sheet Size panel.

These options allow you to change the size of the sheet by inputting size or selecting other sheet code.

| See | Manual Edit Mode Shortcut Menu |
| --- | --- |
|  | Manual Edit Mode Parameter Panel |
|  | Confirm/Display Setting |
|  | Move |
|  | Add Part |
|  | Remove |
|  | Remnant Edit |
|  | Change Material |
|  | Part Grid |
|  | Sequence Edit |
|  | Reposition Command |
|  | Conform Schedule Tool |
|  | Add New Sheet |
|  | Option |

### 26.8.1 Change material by auto-calculation

The Auto Calculation button is designed to calculate the part size automatically and generate a new sheet whose size matches the parts the most. The adjusted dimension of the sheet will be displayed in Width: text box and Height: text box.

| 1. | Parts are nested in the sheet as follows. The green rectangle indicates the original sheet whose size is 900x650. |
| --- | --- |
| 2. | Click Auto Calculation button in parameter panel. The newly generated sheet is shown in the green rectangle, while the red rectangle indicates the original sheet. |
| 3. | Meanwhile the new size is displayed in the in Width: text box and Height: text box. |
| 4. | Click the button to apply the changes and the system will use a 236x260 sheet to nest the parts. |

### 26.8.2 Input size to change material

You can directly stretch the sheet in the left part layout area to change the sheet size, alternatively you can type or select a size in Width: text box and Height: text box.

| 1. | When the pointer becomes, drag the pointer to move sheet border to wherever you want. The newly generated sheet is shown in the green rectangle, while the red rectangle indicates the original sheet. |
| --- | --- |
| 2. | As you drag the border, the values directly in the Width: text box and Height: text box in the right panel update automatically to reflect the changes. |
|  | You can also type or select the values in the Width: text box and Height: text box to specify the sheet size, |
| 3. | Click the button to apply the changes and the system will use a 453x342 sheet to nest the parts. |

### 26.8.3 Select sheet code to change material

Select the Sheet Code option to activate the Sheet Code section.

| Items | Description |
| --- | --- |
| Sheet Code | Click this drop down list to display all sheets that have the same thickness and material type as the sheet in use. |
| Rotate Sheet | This option allows you to rotate the sheet selected according to sheet code. Place a check mark in the Rotate Sheet check box to activate this option and select a degree from Rotate Angle: drop down list. There are four options: 0 degree, 90 degree, 270 degree, 360 degree. |
|  | Note: Only when the Sheet Type is Remnant, is this option available. See Sheet Information |

| Note: | A warning message will appear if the sheet size is not big enough. |
| --- | --- |

## 26.9 Part Grid

In the Manual Edit mode, click  button to open the Part Grid panel.

These options allow you to select more than one part to create part grid or perform common punching process.

| Item | Description |
| --- | --- |
| Grid Parts Method | There are five options in drop down list: General Grid Parts, Common Punch, Single Part Common Cut, ABE Common Cut and Common Cut +WC. |
| General Grid Parts | Select this option to perform part grid. See General Grid Parts |
| Common Punch | Select this option to perform common line punch. See Common Punch Note: To use this method, you should select Joint as the Process After method. |
| Single Part Common Cut | Select this option to perform common line punch part by part. After you finish your operation, right click to open a shortcut menu in Result View mode. See Part Layout Shortcut Options Select To Simulation to simulate the process. You can find that the system execute common cut part by part. See Single Part Common Cut Note: You must use laser to process. |
| ABE Common Cut | Select this option to perform common line punch part by part. After you finish your operation, right click to open a shortcut menu in Result View mode. See Part Layout Shortcut Options Select To Simulation to simulate the process. You can find that the system execute common cut part by part. You can use the same way as you make Single Part Common Cut to make ABE Common Cut and simulate the process. See Single Part Common Cut Note: You must use laser to process. |
| Common Cut+WC | Select this option, the system will use chute tool as the last process after performing common cut and other process. After you finish your operation, right click to open a shortcut menu in Result View mode. See Part Layout Shortcut Options Select To Simulation to simulate the process. You can find that the system execute common cut part by part. You can find that the system execute common cut part by part. You can use the same way as you make Single Part Common Cut to make Common Cut + WC and simulate the process. See Single Part Common Cut Note: You must use laser to process. |
| Output G98 | Place a check mark in this option and the system will output G98 to instruct the machine to process the grid. Output G98 in the NC code to indicate the use of part grid macros. System uses this macro when the same part will be processed. |
| Nesting Priority Direction | There are two options: X First and Y First. If you select X first, system will nest parts in X coordinate first. Otherwise system will nest parts in Y coordinate first. |
| Nesting Reference Position | These options in drop down list are used to specify nesting start point. The drop down list has four options: Bottom Left, Bottom Right, Top Left and Top Right. |
|  | Select X first option in Nesting Priority Direction. In following illustrations, the green line with arrow indicates process direction. |
|  | Bottom Left | Bottom Right |
|  | Top Left | Top Right |
| Part-Spacing | This option allows you to type or select the horizontal space and vertical space between parts. Default space value is defined in Part Spacing/Nesting Border of Nesting preference. |
| Quantity | This option allows you to type or select the number of the horizontal or vertical repetitions for the part. |
| Total | This option displays total number of grid part in part layout area. |
|  | Click this button to calculate the optimum part numbers in the sheet automatically. |
|  | Select an existed grid and click this button to separate the grid. |
|  | Click this button to cancel current operation before execution |
|  | Click this button to start current nesting. |
|  | Click this icon to switch between Release Group and Group. Select Release Group you cannot choose different parts to execute part grid. |
|  | This option allows you to choose different part to execute part gird. |

General Part Grid

| 1. | Click part you want in the left part layout area. When part frame becomes green, it indicates that the part is selected. |
| --- | --- |
| 2. | Select General Grid Parts from Grid Parts Method: drop down list. |
| 3. | Specify Nesting Priority Direction and Nesting Reference Position to determine process direction and process start point. |
| 4. | Click arrow button next to Quantity option to change number in X/Y coordinate. Also you can type part number in Quantity X/Y: text box. |
| 5. | Click arrow button next to Part-Spacing option to reduce or increase space between parts, if necessary. |
| 6. | Place a check mark in Output G98 check box to generate G98 in NC code. |
| 7. | Following illustration show part grid result according to settings you specify above. |
| 8. | Click Execute button to complete current operation. |

Common Punch

| 1. | Select Common Punch from Grid Parts Method: drop down list. |
| --- | --- |
| 2. | Select the part want to make part grid in the left Part Layout area. The selected part will be green. |
| 3. | Set the parameters as following: |
| 3. | Select a cutting tool you want to use to cut the common line. The selected tool in Y-axis will be blue and the selected tool in X-axis becomes orange. |
| 4. | Click Execute button, or right click to open shortcut menu and click Complete option. Parts with common line will be processed as follows. |

Single Part Common Cut

| 1. | Select Single Part Common Cut from Grid Parts Method: drop down list. |
| --- | --- |
| 2. | Select the part want to make part grid in the left Part Layout area. The selected part will be green. |
| 3. | Click arrow button next to Quantity option to specify the number of grid in X/Y coordinate. Also you can type part number in Quantity X/Y: text box. |
| 4. | Click Execute button to finish your operation. |
| 5. | In Result View mode, right click to open a shortcut menu. See Part Layout Shortcut Options Select To Simulation to simulate the process. You can find that the system execute common cut part by part. |

| See | Manual Edit Mode Shortcut Menu |
| --- | --- |
|  | Manual Edit Mode Parameter Panel |
|  | Confirm/Display Setting |
|  | Move |
|  | Add Part |
|  | Remove |
|  | Remnant Edit |
|  | Change Material |
|  | Part Grid |
|  | Sequence Edit |
|  | Reposition Command |
|  | Conform Schedule Tool |
|  | Add New Sheet |
|  | Option |

## 26.10 Sequence Edit

In the Manual Edit mode, click  button to open the Sequence Command in Sheet panel. The options in the Sequence Command in Sheet panel allow you to define the sequence to process the part and then take it out.

| Note: |
| --- |
| 1. | To activate this option, the following steps must be taken. |
|  | Step 1. | Assign TakeOut as Process After method in Process After Cutting table of Process After preference. |
|  | Step 2. | Place a check mark in Taking Out On/Off check box in the Take Out panel of Peripherals preference. |
| 2. | If you select Laser machine or Combo machine, a dialog appears when you click button to open the Sequence Command in Sheet panel to remind you that parts should be nested in sheet mode. Click OK to continue. |

| See | Manual Edit Mode Shortcut Menu |
| --- | --- |
|  | Manual Edit Mode Parameter Panel |
|  | Confirm/Display Setting |
|  | Move |
|  | Add Part |
|  | Remove |
|  | Remnant Edit |
|  | Change Material |
|  | Part Grid |
|  | Sequence Edit |
|  | Reposition Command |
|  | Conform Schedule Tool |
|  | Add New Sheet |
|  | Option |

### 26.10.1 Specify the range

Select the Specify the Range option to activate Specify the Range option.

You can divide the process area into equal districts, and then parts will be processed and taken out in the first district and then the adjacent district.

| Item | Description |
| --- | --- |
|  | Click this button to apply the settings. |
|  | Click the Details button to display the Sequence Setting window. You can specify the setting to sequence the parts in detail. See Combo Sequence |
| Starting Position | Specify the starting position to sequence the parts. There are four options, Upper Right, Lower Right, Upper Left and Lower Left. |
|  | If you select Upper Right, the part in the upper right corner of the sheet will be processed first. |
|  | If you select Upper left, the part in the upper left corner of the sheet will be processed first. |
| Sheet Division Direction | Specify the direction to process the parts. There are four options, Direction X, Direction Y, Single Direction X, and Single Direction Y. |
|  | Specify the settings as follows and click Execute button. |
|  | The system will sequence the parts as follows. |
|  | Specify the settings as follows and click Execute button, |
|  | The system will sequence the parts as follows. All the parts in each division area will be processed in the same direction. |
| Sheet Division Quantity | This option allows you to type or select a number in Sheet Division Command: text box to divide the part layout area into equal areas for the processing sequence. The system will process the parts in the first area, and then go on to process the parts in the adjacent area. |
|  | The system will divide the part layout area based on the Direction settings. For example, if you select Direction X, and type 3 in the Sheet Division Command: text box, the system will divide the part layout area as follows. |
|  | The system will divide the part layout area based on the Direction settings. For example, if you select Direction Y, and type 3 in the Sheet Division Command: text box, the system will divide the part layout area as follows. |

### 26.10.2 Mouse Command

Select the Mouse Command option to activate mouse command.

You can use mouse to click the parts to specify their process sequence directly. Alternatively you can place a check mark in Insert check box to change the sequence of two parts selected. The part number in the left part layout area will update automatically.

| Items | Description |
| --- | --- |
|  | Click this button to complete the modification. |
|  | Click this button to cancel your previous operation. |
|  | Click this button to give up all the modifications and restore the process sequence to its original state. |
| Insert | Place a check mark in the check box to enable the Insert functions. |
| Before | Select this option and click the first part, then click the second part. In that case, the sequence of the second part you click will be processed earlier than the first one. |
| After | Select this option and click the first part, then click the second part. In that case, the sequence of the second part you click will be processed later than the first one. |

Example

| 1. | Parts have been processed in the left part layout area as follows. |
| --- | --- |
| 2. | Select Mouse Command option. |
| 3. | Click the 23rd part. The part frame will be red and number on the part will become 1. |
| 4. | Click the rest part orderly and system will assign the sequential number to each part. |
| 5. | Click Complete button. The part frame will restore to be yellow. |
| 6. | Place a check mark in the Insert check box and select Before option. |
| 7. | Click the fourth part first. |
| 8. | Click the fifth part. The fifth part will be processed earlier than the fourth part and the numbers on the part will update automatically. |
| 9. | Click Complete button to confirm. |

### 26.10.3 List Command

Select the List Command option to activate list command.

In this section, the name of all parts in the same process area will be listed by processing sequence and the numbers indicate their sequence. You can select one part name in the list and click upward button or downward button  to change the sequence. Meanwhile your changes will be reflected in the left part layout area.

## 26.11 Reposition Command

In the Manual Edit mode, click button to open the Indicate Reposition panel.

The repositioning is the movement of the clamps to avoid over-travel and dead zones. Machines use clamps to shift the sheet to process the parts that are out of a processing area. A reposition refers to the processing area of specified clamp.

| See | Manual Edit Mode Shortcut Menu |
| --- | --- |
|  | Manual Edit Mode Parameter Panel |
|  | Confirm/Display Setting |
|  | Move |
|  | Add Part |
|  | Remove |
|  | Remnant Edit |
|  | Change Material |
|  | Part Grid |
|  | Sequence Edit |
|  | Reposition Command |
|  | Conform Schedule Tool |
|  | Add New Sheet |
|  | Option |

### 26.11.1 Basic Reposition Operation

These options allow you to add/remove a reposition, edit the reposition movement values, modify the holder positions, and change the reposition positions.

#### 26.11.1.1 Confirm Reposition

Click Confirm Reposition button to open the Confirm Reposition screen.

Example:

| 1. | Right click the cell of the No. column of the original clamp and select Add to add a new reposition. |
| --- | --- |
| 2. | In the Part Layout area, drag the mouse to move the new reposition to the position you desire. Click to confirm the position. |
|  | Click again to confirm the position of the holder. |
|  | Each reposition is assigned a number that appears along the bottom. |
| 3. | In the Parameter panel on the right, correlative data will update automatically. |
| 4. | Select No.2 reposition and type values to change the data directly. |
|  | Changes will be reflected in the left Part Layout area. |
| 5. | Alternatively you can click one number to select one reposition and the selected reposition in Part Layout turns to white. |
| 6. | Click the Amount button. |
|  | In the Part Layout area, the original reposition turns to yellow and a new reposition is shown with white color. Drag and drop the new reposition to any place you desire. |
| 7. | Select one reposition and then click Holder button. |
|  | In the Part Layout area, drag the mouse to move the selected holder to a new position. |
| 8. | You can also right click the cell of the No. column of one reposition to open a shortcut menu and then select Insert option to insert a new reposition before the selected reposition. |
|  | The number of new reposition will take place the number of the selected reposition, meanwhile the selected reposition is assigned a new number in sequence. |
| 9. | You can also remove an existing reposition by selecting Remove option in a shortcut menu except for No.1 reposition. |

#### 26.11.1.2 Manual Reposition

Click Manual Reposition button to clear all the existed repositions except No.1 reposition. A dialog appears when you click this button, reminding you the settings you made will be canceled.

You can click OK button to remove reposition you add and Cancel button to return to Confirm Reposition screen. When you click OK, the Manual Reposition screen will be available.

In this screen, you can add new repositions and edit them as you do in the Confirm Reposition screen.

If you want to switch to the Confirm Reposition screen, the following dialog will appear.

### 26.12.2 Divide Reposition

Click Divide button to open the Divide section.

These options in the section are used to split one process into two processes.

| Item | Description |
| --- | --- |
|  | Select a horizontal trace, click this button when selected trace becomes blue. In the left Part Layout area, and a vertical line appears. Drag mouse to move this line in horizontal direction to any place you desire. |
|  | Right click to open a shortcut menu and select Complete to divide the selected trace as follows. |
|  | Select a vertical trace, click this button when selected trace becomes blue. In the left Part Layout area, a horizontal line appears. Drag mouse to move this line in vertical direction to any place you desire. Right click to open a shortcut menu and select Complete to divide the selected trace. |
|  | This function is not available now. |
|  | Place a check mark to divide part-grid, and then the corresponding Divide Part-Grid section appears as follows. |
|  | This option is used to divide part grid in horizontal direction. Select a part, click this button when the part frame becomes blue. In the left Part Layout area, a vertical line appears. Drag mouse to move this line in vertical direction to any place you desire. |
|  | Right click to open a shortcut menu and select Complete to execute division as follows. |
|  | This option is used to divide part grid in vertical direction. Select a part, click this button when the part frame becomes blue. In the left Part Layout area, a horizontal line appears. Drag mouse to move this line in horizontal direction to any place you desire. |
|  | Right click to open a shortcut menu and select Complete to execute division as follows. |

Note:

Which grid the part belongs to is decided by the center point of each part. The part will be placed in the grid in which its center point is located.

### 26.12.3 Group Reposition

As for the trace located in the position where work zones overlap with each other or one another, system can process the trace in one of repositions automatically. Also you can insert this trace to another reposition. Click Group button to open the Group section.

Suppose there are two repositions in the left Part Layout area as follows. The color of the trace is corresponding to that of process area. The red trace will be processed in the No.1 reposition, while the yellow trace will be processed in the No.2 reposition.

Select a trace that can be processed in either of the two repositions and the selected trace will be blue.

Select No.2 reposition in the right Parameter panel, and then click the Insert to the selected reposition group button.

This trace turns to yellow. It indicates that the trace will be processed in No.2 reposition.

## 26.12 Confirm Schedule Tool

In the Manual Edit mode, click button to open the ToolList For Schedule window.

This window consists of five elementary sections: Toolbar, Schedule list, Turret and tool information table, Turret image and Display Station.

These options allow you to review the schedule information, such as Machine Name, Material Name, Material Size, Turret Stations, and tools used for each sheet.

| See | Manual Edit Mode Shortcut Menu |
| --- | --- |
|  | Manual Edit Mode Parameter Panel |
|  | Confirm/Display Setting |
|  | Move |
|  | Add Part |
|  | Remove |
|  | Remnant Edit |
|  | Change Material |
|  | Part Grid |
|  | Sequence Edit |
|  | Reposition Command |
|  | Add New Sheet |
|  | Option |

### 26.12.1 Toolbar

There are four toolbars in this section: Range toolbar, Shape toolbar, Search toolbar and View button.

#### 26.12.1.1 Range toolbar

Click a range button to display turret stations of that range. The  button is selected by default and stations of all the ranges will be displayed. More information, See Range and Shape button

#### 26.12.1.2 Shape toolbar

Click a shape button to display the tools of that shape. The  button is selected by default and tools of all the shapes will be displayed. More information, See Range and Shape button

#### 26.12.1.3 Search toolbar

| Button | Description |
| --- | --- |
|  | Click Search button to open the Advanced Filter window. |
|  | These options in this window allow you to filter the results by Name, Shape, Range, etc. For example, if you type a C in the Range: text box, and the system will search the current turret and list the stations that are installed tools of C range. |
|  | In the Schedule List pane, right-click to open the Display Setting window. Alternatively you can click in the toolbar to show this window. |
|  | There are three panels: Situation Color, Schedule Color and Sheet Color. These options in this window allow you to set the colors for corresponding Station Situation, Schedule and Sheet. |

#### 26.12.1.4 View menu

You can click the View menu and select the way to display tools and turret.

|  | Option | Description |
| --- | --- | --- |
|  | Used tool only | Display the tools used. |
|  | Tool for sheet | Select this option, and the system will display Sheet Tool columns on the right and show which tools are used for each sheet. |
|  | Tool for schedule | Display the tool for the schedule specified. |
|  | Turret Image | Select this option to display the Turret image. See Turret Image Pane |

### 26.12.2 Schedule list

The Schedule list on the left of the window displays the schedule information.

|  | Shows the Machine Name. Shows the Material Name and Material Size. Shows the schedule. Shows the sheet. |
| --- | --- |

You can click one  item to display all the tools used for the corresponding schedule or click one  item to show all the tools for the corresponding sheet.

### 26.12.3 Turret and tool information table

The turret and tool information table list all the stations and tools in use.

Right-click the column heading and select or remove the check marks to show or hide the corresponding columns.

You can also select Customize to open the Tool Inventory Item window.

Select the item in the list and click the upward/downward button to change the displaying order. You can type a value in Width of Select Column: text box to adjust the width of column selected in the Tool Inventory Item window.

| Column Title | Description |
| --- | --- |
| Station | This option displays the station number. |
| Situation | The Situation column shows the station status for the tool assignment. |
| Origin | The same tool is used in the same station to process the current sheet. |
| Create | A new tool is added to this station. |
| Exchange | A new tool is added to the station to replace the previous one. |
| Rotate | The tool is rotated |
| Move | A new tool is added to the station, and the previous tool is moved to other station |
| Exchange Die | The die is changed. |
| Remove Tool | The tool is removed from the station. |
| Range | This option displays the range of the turret from A to M. Only those tools with dimension ranges matching the station ranges can be placed in the turret. |
| Tool ID | Display the tool identification numbers. Each tool ID is unique and cannot be changed. The tool ID is used as a reference when the system is searching for a specific tool from the stock. |
| Name | The user-defined tool names appear in this column. The user specifies the name when registering the tool in the inventory. |
| Shape | The tool shapes are listed in this column. The basic tool shapes are Round (RO), Square (SQ), Rectangle (RE), Rounded Corner Rectangle (RR), Corner Radius (CR) and Obround (OB). There are also Special (SP), Tapping (TP) and other tool shapes. |
| X | The X dimension of the tool. |
| Y | The Y dimension of the tool. |
| R | The R dimensions of RR and CR tools. Size R is specific for RR and CR tools. The following figures indicate the R dimension for these tools. |
| Clearance | This option displays the clearance of die. |
| Angle | This option displays the angle of the station in the turret. |
| Key | The check mark before a station indicates this station is a keyed station. Shaped tools, such as rectangle and square tools, can only be installed in keyed stations. Non-keyed stations are available for round, center punch and burring tools. |
| Fixed | The Fixed indicates that the tool is installed in a fixed station. The system considers the tool as a permanent fixture within the station and will not remove it or replace it with alternate tools. You can manually remove the tool from the turret. |

### 26.13.4 Turret Image pane

When you click View button to expand menu and place a check mark before the turret image option, a turret illustration appears in the right of the window.

The turret illustration shows the turret layout. The situation of the station is shown with color defined in the Situation Color panel of Display Setting window. The blue color is used to highlight the station being selected.

### 26.12.5 Display Station option

These options at the bottom of the window allow you to define stations of which type will be listed in the table.

| Option | Description |
| --- | --- |
| All Stations | List all the stations on the turret. |
| Empty Stations | List the blank stations. |
| Used Stations | List the stations on which there is no tool. |
| Fixed Stations | List the stations on which there is always the same tool. |
|  | Note: |
|  | If a station with a tool assigned is set to Fixed, no other tools are allowed to assign to it. If an empty station is set to Fixed, no tools are allowed to assign to it. |
| Free Stations | List the stations in which different tools can be installed. |

## 26.13 Add New Sheet

In the Manual Edit mode, click  button to open the Add New Sheet panel.

These options are used to append a new sheet when you are editing a sheet.

Example:

| 1. | Select Input Material option to activate the Input Material section. Select or type value in the text box to define Material Type, Thickness, Size X and Size Y directly. |
| --- | --- |
| 2. | Alternatively you can select Sheet Code option to activate the Sheet Code section. |
| 4. | Click arrow button to select a new sheet from drop down list which containing sheets that have the same thickness as the original sheet has. |
| 5. | Place a check mark in the Rotate Sheet check box and select different angles to rotate the sheet, if necessary. |
|  | Note: |
|  | Only when material type is remnant or skeleton, is Rotate Sheet check box available. See Sheet Information |
| 6. | When you clickbutton, a newly generated sheet with settings you have specified in Parameter panel will display on the left of the window. |

| See | Manual Edit Mode Shortcut Menu |
| --- | --- |
|  | Manual Edit Mode Parameter Panel |
|  | Confirm/Display Setting |
|  | Move |
|  | Add Part |
|  | Remove |
|  | Remnant Edit |
|  | Change Material |
|  | Part Grid |
|  | Sequence Edit |
|  | Reposition Command |
|  | Conform Schedule Tool |
|  | Option |

## 26.14 Option

In the Manual Edit mode, click button to open the Option window.

Those options are designed to decide whether to display specified message when you plan to exit Part Edit mode.

| Item | Description |
| --- | --- |
| Do not display message of applying to part when exiting edit mode | Place a check mark in the check box, the system will not display the message of applying to part when you click button. You can make detailed setting in the following drop-down list. The system will execute it automatically. |
|  | If you clear a check mark in the check box, the system will display the following message after you save the setting and exit Manual Edit mode. Then the following dialog appears when you save the setting and exit Manual Edit mode You may make detailed setting in the Reflect Edit Result window. |
|  | Item | Description |
|  |  | Select this option to apply the editing result to the part you are editing. |
|  |  | Select this option to make detailed settings. There are four groups to select. |
|  |  | Apply the editing result to the same part with the same angle in the current sheet. |
|  |  | Apply the editing result to the same part in the current sheet. |
|  |  | Apply the editing result to the same part with the same angle in all sheets. |
|  |  | Apply the editing result to the same part in all sheets. |
| Do not display message after selecting cancel command | Place a check mark in the check box, the system will not display the message of applying to part when you click button. The system will ignore or save changes automatically when you click button by selecting an option from the following drop-down list. |
|  | If you clear a check mark in the check box, the system will display the following message when you want to cancel the command. |
|  | Click Yes button, the system will end your editing by ignoring the setting you have made. |
|  | Click No button and the system will end your editing by saving the setting you have made. |
|  | Click Cancel button, the system will return to editing mode. |
|  | Place a check mark in Don’t ask me again check box and click Yes/No button. At the same time the system will place a check mark in Do not display message after selecting cancel command check box automatically in the Option window. |
| Do not display message if space is not enough when add parts | Place a check mark in the check box, the system will not display the message when the space is not enough to add part. |
| Use command of editing single part to maximize window | Place a check mark in the check box and click Part Edit button, the system will expand AICAM main window so that it covers the full screen. |
| Window returns to the initial size after editing is complete | Place a check mark in the check box, the maximized window will restore to its previous size after you exit the manual edit mode. |
| Release the Command of not display message after version updated | Place a check mark in this check box, system will not keep the settings of Don’t Display Message you have specified in previous version during version update. |
| Collision check when moving parts | Place a check mark in this check box, the following message will prompt when parts move and collision happens. |

| Take the following part as an example: |
| --- |
| 1. | In Option window, place a check mark in the check box and select Inside Same Sheet and Part of Same Angle in Auto Apply: drop-down list. |
| 2. | Click OK to close the Option window. |
| 3. | In the Manual Edit toolbar, click Part Edit button to enter Part Edit mode. On the left part layout, select one part and add two joints. See Joint Edit |
| 4. | Click button to save the setting. Two joints are automatically added to the part in the same sheet and with the same angle. |

| See | Manual Edit Mode Shortcut Menu |
| --- | --- |
|  | Manual Edit Mode Parameter Panel |
|  | Confirm/Display Setting |
|  | Move |
|  | Add Part |
|  | Remove |
|  | Remnant Edit |
|  | Change Material |
|  | Part Grid |
|  | Sequence Edit |
|  | Reposition Command |
|  | Conform Schedule Tool |
|  | Add New Sheet |

# Chapter 27: Manual Tool Assignment

In Part Edit mode, you can edit manually part by part.

If you select Auto Execute (Nesting) to perform nesting process, you can select Edit from the shortcut menu to enter the Sheet Edit mode. In the Manual Edit Mode, you can click  (Part Edit) button from the toolbar to switch to Part Edit mode.

If you select Auto Execute (Individual Part) to perform nesting process, you can select Manual Tool Assign from the shortcut menu to enter the Part Edit mode directly.

| See | Part Edit Mode Shortcut Menu |
| --- | --- |
|  | Part Edit Mode Parameter Panel |
|  | Confirm/Display Setting |
|  | Save Template |
|  | Delete Trace |
|  | Joint Edit |
|  | End Value |
|  | Sequence Command in Parts |
|  | Lead In Edit |
|  | Change the Tool Assignment |
|  | Assign Tool-Lines |
|  | Layout Between Single Hit |
|  | Merge |
|  | Stretch |
|  | Shift |
|  | Direct Assignment |
|  | Move/Copy Tool |
|  | Apply Assignment the Same Inner |
|  | Fix Process Order |
|  | Change the Nibbling Pitch |
|  | Laser Hole Division |
|  | Show Tool |
|  | Option |

## 27.1 Part Edit Mode Shortcut Menu

Right-click part layout area in the Part Edit mode, a shortcut menu will appear.

| Option | Description |
| --- | --- |
| Zoom In | Select this option to magnify the view of the selected area. |
| Zoom Out | Select this option to reduce the view of the selected area, allowing you to see more of the sheet area. |
| Move | Select this option to move the part. |
| Zoom All | Select this option to get an entire view of the sheet. |
| Auto Scale | Select this option to display all the parts to fit the view. |
| Maximize Window | Select this option to cover the window to full screen. |
| Shorten | Select this option to restore the maximized window. |
| Display Parts Info | Select this option to display the information of the parts nested on the sheet you have specified. The Parts Info window displays the part name, part quantity, part comment, material name, material type, material thickness, weight, size, group ID, priority etc. |
| Undo | Select this option to cancel your last operation. |
| Redo | Select this option to execute your last operation again. |

| See | Part Edit Mode Parameter Panel |
| --- | --- |
|  | Confirm/Display Setting |
|  | Save Template |
|  | Delete Trace |
|  | Joint Edit |
|  | End Value |
|  | Sequence Command in Parts |
|  | Lead In Edit |
|  | Change the Tool Assignment |
|  | Assign Tool-Lines |
|  | Layout Between Single Hit |
|  | Merge |
|  | Stretch |
|  | Shift |
|  | Direct Assignment |
|  | Move/Copy Tool |
|  | Apply Assignment the Same Inner |
|  | Fix Process Order |
|  | Change the Nibbling Pitch |
|  | Laser Hole Division |
|  | Show Tool |
|  | Option |

## 27.2 Part Edit Mode Parameter Panel

There are toolbar and parameter section in the Parameter panel. The toolbar consists of Sheet Edit toolbar and Part Edit toolbar (Click Part Edit button to show Part Edit toolbar and enter Part Edit mode.). The Parameter section is where you can specify detailed settings for each option in the toolbar.

| Icon | Button Name | Description |
| --- | --- | --- |
|  | Confirm/Display Setting | This option allows you to display and confirm part/trace/pattern specified. |
|  | Save Template | This option allows you to save settings as template and use this template to process similar pattern in the future more conveniently. |
|  | Delete Trace | This option allows you to delete specified process trace. |
|  | Joint Edit | This option allows you add or edit joint. |
|  | End Value | This option allows you to modify the process after methods for the laser process. |
|  | Change the Tool Assignment | This option allows you to modify tool assignment for specified pattern. |
|  | Assign Tools-Lines | This option allows you to assign single D or double D tools to specified line. |
|  | Layout Between Single Hit | This option allows you to assign single hit tools to the pattern composed of intersection line. |
|  | Merge | This option allows you to assign tools to match tool element with pattern element. |
|  | Stretch | This option allows you to lengthen process path along moving direction and modify process angle on pattern-by-pattern basis. |
|  | Shift | This option allows you to move tool along the pattern edge in positive or negative direction. |
|  | Direct Assignment | This option allows you to assign tool of specified shape to punch out. |
|  | Move/Copy Tool | This option allows you to move or copy the specified tool assignment. |
|  | Apply Assignment to the Same Inner | This option allows you to apply the assignment in specified inner to all the same inner or the same inner you specify. |
|  | Fix Sequence Order | This option allows you to fix the sequence in processing one loop. |
|  | Change the Nibbling Pitch | This option allows you to modify moving pitch when nibbling tool is processing pattern. |
|  | Show Tool | This option allows you to view the tool assigned in specified pattern. |
|  | Option | This option is the same with that in Sheet Edit Toolbar. |

| See | Part Edit Mode Shortcut Menu |
| --- | --- |
|  | Confirm/Display Setting |
|  | Save Template |
|  | Delete Trace |
|  | Joint Edit |
|  | End Value |
|  | Sequence Command in Parts |
|  | Lead In Edit |
|  | Change the Tool Assignment |
|  | Assign Tool-Lines |
|  | Layout Between Single Hit |
|  | Merge |
|  | Stretch |
|  | Shift |
|  | Direct Assignment |
|  | Move/Copy Tool |
|  | Apply Assignment the Same Inner |
|  | Fix Process Order |
|  | Change the Nibbling Pitch |
|  | Laser Hole Division |
|  | Show Tool |
|  | Option |

## 27.3 Confirm/Display Setting

Click  to open the Confirm/Display Setting panel on the right side of the window.

| 1. | Take the following part as an example. |
| --- | --- |
| 2. | Select Part in the Parameter panel to display the parameters for the selected part, including Part Name, Size, Sheet Pattern Quantity, and Weight. |
| 3. | Select Trace in the Parameter panel to display the parameters for the selected trace. The parameter items are different between the laser trace and the punch trace. |
|  | Laser Trace | Punch Trace |
| 4. | Select Pattern in the Parameter panel to display the various parameters for the selected pattern. |

| See | Part Edit Mode Shortcut Menu |
| --- | --- |
|  | Part Edit Mode Parameter Panel |
|  | Save Template |
|  | Delete Trace |
|  | Joint Edit |
|  | End Value |
|  | Sequence Command in Parts |
|  | Lead In Edit |
|  | Change the Tool Assignment |
|  | Assign Tool-Lines |
|  | Layout Between Single Hit |
|  | Merge |
|  | Stretch |
|  | Shift |
|  | Direct Assignment |
|  | Move/Copy Tool |
|  | Apply Assignment the Same Inner |
|  | Fix Process Order |
|  | Change the Nibbling Pitch |
|  | Laser Hole Division |
|  | Show Tool |
|  | Option |

## 27.4 Save Template

You can use this function to save the assignment for the parts as template.

The template can be used in the future to process similar patterns more conveniently.

In part edit mode, select the part you want to save and then click  on the toolbar to open the Save Template panel on the right side of the window.

You may select one from the two options below,

| Option | Description |
| --- | --- |
| Part Assignment Data | Select this option to save the part assignment data as SY5. See: Save Part Assignment Data |
| Template | Select this option to save template. See: Save Template |

Save Part Assignment Data

| 1. | Select Part Assignment Data option to save as SY5. |
| --- | --- |
| 2. | The corresponding Parameter panel will appear below. Select File in Save Type: drop-down list and then click Save button. |
|  | Note: Select/Remove Assignment button is NOT available. |
| 3. | The Save As window appears. Specify a name in the File name: text box and click Save button to save the assignment data as an SY5 file. |
|  | Note: You can also select SDD or MiniSDD from the Save Type: drop-down list to save the SY5 information into the corresponding database. |

Save Template

| 1. | Select Template option to save as template. |
| --- | --- |
| 2. | The corresponding Parameter panel will appear below. |
| 3. | Select the elements you want to save, such as lines, holes, or notches, etc. The selected elements will be highlighted. |
| 4. | Click Save button in the right Parameter panel to display the List Of Template window. Alternatively, you can right-click the layout area and select Complete. |
| 5. | Specify a name for the template in the File Name: text box and click Save button to save the template. The Template window will then display. You can make further edit for the saved templates in this window. See: Edit of Template |

| See | Part Edit Mode Shortcut Menu |
| --- | --- |
|  | Part Edit Mode Parameter Panel |
|  | Confirm/Display Setting |
|  | Delete Trace |
|  | Joint Edit |
|  | End Value |
|  | Sequence Command in Parts |
|  | Lead In Edit |
|  | Change the Tool Assignment |
|  | Assign Tool-Lines |
|  | Layout Between Single Hit |
|  | Merge |
|  | Stretch |
|  | Shift |
|  | Direct Assignment |
|  | Move/Copy Tool |
|  | Apply Assignment the Same Inner |
|  | Fix Process Order |
|  | Change the Nibbling Pitch |
|  | Laser Hole Division |
|  | Show Tool |
|  | Option |

## 27.5 Delete Trace

Click  to open the Delete Trace panel on the right side of the window.

| Option | Description |
| --- | --- |
| Delete Object |  |
| Inside Frame | Delete the traces inside the mouse frame. |
| Outside Frame | Delete the traces outside the mouse frame. |
| Mouse Command |  |
| All Selection | The trace is selected when being enclosed by the mouse frame. |
| Partial Selection | The trace is selected when any partial segment of it being enclosed by the mouse frame, although it is not completely inside the frame. |

Example

| 1. | Select Inside Frame and drag a mouse frame to enclose a trace. This trace will be selected. |
| --- | --- |
| 2. | Click at the bottom of the panel to delete the selected trace. Alternatively, you can press <Delete> button on the keyboard to delete it. |

| See | Part Edit Mode Shortcut Menu |
| --- | --- |
|  | Part Edit Mode Parameter Panel |
|  | Confirm/Display Setting |
|  | Save Template |
|  | Joint Edit |
|  | End Value |
|  | Sequence Command in Parts |
|  | Lead In Edit |
|  | Change the Tool Assignment |
|  | Assign Tool-Lines |
|  | Layout Between Single Hit |
|  | Merge |
|  | Stretch |
|  | Shift |
|  | Direct Assignment |
|  | Move/Copy Tool |
|  | Apply Assignment the Same Inner |
|  | Fix Process Order |
|  | Change the Nibbling Pitch |
|  | Laser Hole Division |
|  | Show Tool |
|  | Option |

## 27.6 Joint Edit

In Part Edit mode, select  to open Add/Edit Tab panel to edit joints manually.

Add/Edit Tab panel consists of three subordinate panels: Parameter panel, Approach panel and Pierce panel.

| Item | Description |
| --- | --- |
| Parameter |  |
| Distance from End Point | Define the offset value of the joint. You can type the value directly or click the button to change the value. |
| Wire Joint | Type or select a value in the text box to specify the width of the wire joint. |
| Micro Joint | Type or select a value in the text box to specify the width of the micro joint. Note: You cannot add a corner joint to a corner unless the Distance From End Point is set to 0. |
| Both Sides Corner Joint | Add the micro joints on both sides of the corner. If you don’t place a check mark in this check box, the system will assign the joint on one corner side only. |
| Tab Type | Type of tab. You can select joint type from the drop-down list. There are two options: Common Tab and MJC Joint. Note: MJC Joint is a special facility on the machine. |
| Process Joint at Last | If you place a check mark in this check box, the system will process joint at last. |
| Use Joint Tool | If you place a check mark in this check box, the masked options will be enabled, and you can select the Special or Standard option. If you select the Special option, the Dr. ABE dialog box appears, and you can click Yes to continue. |
|  | The Tool Assign Condition window appears. You can set the special tool joint conditions in Joint panel. See Tool Assign Condition |
|  | Note: If there’s no tool exist, the Please select the tool for joint tool assign window appears, and you should select one for joint tool assign from the tool list first. |
| Lap Rate | Type or select a value in the text box to specify the overlap percentage. The system will determine the overlap value using this formula: Overlap= Lap (%) x Tool Total Length |
| Adjust Amount | Type or select a value in the text box to specify the overlap amount. |
| Approach |  |
| Length | Type or select a value in the text box to specify the length of lead-in and lead-out. |
| Angle | Type or select a value in the text box to specify the angle of lead-in and lead-out. |
| Radius | Type or select a value in the text box to specify the radius of lead-in and lead-out. |
| Over Cut | This function is not available now. |
| The Distance from the End Point | This function is not available now. |
| Display Pierce Collision Area | When you select this option, the area where pierce collision exists will be displayed. |
| Pierce |  |
| Pierce Type | Type of pierce. You can select pierce type from the drop-down list. There are four types of joints available for your selection: Laser Pierce, Special Pierce, No Pierce and Punch Pierce. |
| A | Place a check mark in the A check box and type a value between 0 and 999 in the text box to the right to specify an existing pierce type that has been configured for the machine. Note: It’s useful for special pierce. |
| B | Place a check mark in the B check box and type a value from 0 to 99999.9999 in the text box to the right to specify the pierce range. Note: It’s useful for special pierce. |
| Condition | You can set pierce condition here. Note: It’s useful for special pierce. |
| On Line, Outer Corner, Inner Corner | There are three icons on the bottom of the panel. |
|  | Click the icon to open the Custom Lead In/Out Definition window. The Custom Lead In/Out Definition window consists of three panels: On Line, Outer Corner, Inner Corner. You can select, create and modify the lead-in and lead-out types using the options in this window. You can define lead-in/lead-outs for lines and corners. See Edit of lead in and lead out |

To delete joint

| 1. | Take the following part as an example. |
| --- | --- |
| 2. | Click to open Add/Edit Tab panel. Select a joint and the selected joint becomes white. |
| 3. | Click to delete the joint. |
| 4. | Click button to save your operation. |

To add joint

| 1. | Take the following part as an example. We want to add a wire joint. |
| --- | --- |
| 2. | Make setting in Parameter panel as following: |
| 3. | Make setting in Approach panel as following: |
| 4. | In Pierce panel, select Laser Pierce in the Pierce Type: dropdown list. |
| 5. | Click the On Line icon to open Custom Lead In/On Definition window. Here you can select an existed lead in/out method or edit a new one. See: Edit of lead in and lead out The method you select becomes orange and then click OK. |
| 6. | Move the mouse to the loop of the part. A red point appears on the selected line. You can move the point to the desired position of the joint. |
| 7. | Click the line to add the wire joint. |
| 8. | Click button to save your operation. |
| 9. | If you are not satisfied with the new joint, you can select the joint and then change the settings in the right panel or click to delete it. |

| See | Part Edit Mode Shortcut Menu |
| --- | --- |
|  | Part Edit Mode Parameter Panel |
|  | Confirm/Display Setting |
|  | Save Template |
|  | Delete Trace |
|  | End Value |
|  | Sequence Command in Parts |
|  | Lead In Edit |
|  | Change the Tool Assignment |
|  | Assign Tool-Lines |
|  | Layout Between Single Hit |
|  | Merge |
|  | Stretch |
|  | Shift |
|  | Direct Assignment |
|  | Move/Copy Tool |
|  | Apply Assignment the Same Inner |
|  | Fix Process Order |
|  | Change the Nibbling Pitch |
|  | Laser Hole Division |
|  | Show Tool |
|  | Option |

## 27. 7 End Value

Select to open End Value panel on the right side of the window.

| Option | Description |
| --- | --- |
| Type |  |
| Machine Stop | M00 is generated after processing. |
|  | When you select this option, the following panel appears: |
|  | Note: When you select Joint option or None option, the same panel will appear. |
|  | Option | Description |
|  | Axis Speed (F1-F4) | Select a speed option from the drop-down list to specify the feed rate for removing parts. There are four options. The selection of a particular option will determine the code output in the NC program. For example, if you select F1, the system will output a feed rate value of F1 for the device. This is not available now. |
|  | Move Amount | Specify the move amount by scrolling the arrow or typing in the exact value. |
| Chute1/Chute2 | Select Chute 1 or Chute 2 as the end value .The work chute automatically ejects scraps without stopping the machine. See: Work Chute Information The work chute is the most appropriate method to retrieve parts or scraps when the micro joint method cannot be used, especially when processing a part with a corner radius. |
|  | When you select Chute1 or Chute2, the following panel appears: |
|  | Option | Description |
|  | After Open Chute | The machine status after work chute opens. There are three options: None, Machine Stop and Dwell. |
|  | Dwell Time | Select Dwell from the After Open: drop-down list, and type a value in the Dwell Time: text box to define the dwell. |
|  | Axis Speed (F1-F4) | Select a speed option from the drop-down list to specify the feed rate for removing parts. There are four options. The selection of a particular option will determine the code output in the NC program. For example, if you select F1, the system will output a feed rate value of F1 for the device. This is not available now. |
|  | Move Amount | After cutting the sheet, the system will move the sheet first and then open the chute. Type a value in the boxes to define the move distance. |
| Joint | Keep joints after processing. |
| Chute Tool | Some special tools can work as the chute tools to perform the final hit. |
|  | When you select Chute Tool option, the following parameters appears: |
|  | Option | Description |
|  | Cut X/Y | The dimension of the chute tool in the X/Y-axis. |
|  | Offset Y | The distance from the center of the die to the position of the final hit. |
| None | No specific end value. |
| Take Out | TK function is performed after cutting process. |
|  | Option | Description |
|  | Taking Out Position | When the TK function is performed after cutting process, select one station to locate the parts. |
|  | TK/IJP Edit | Edit the TL/IJP settings. |
|  | Note: To enable this function, you should place a check mark in the Yes/No check box in Take-out Information panel. See Take-out Information. |

| 1. | Take the following part as an example. In the Process After Cutting table, specify Joint as the method to deal with the inner loop after cutting. |
| --- | --- |
| 2. | In the Part Edit mode, click to open the End Value panel. None option is selected by default as the end value. Select the inner loop with the mouse and Joint option will be selected automatically in the right panel to show the Process After method of the selected inner loop. |
|  | . |
| 3. | Click to open Add/Edit Tab panel. Delete the joints of the inner loop as follows. See: Joint Edit |
| 4. | Click to open the End Value panel again. Select the inner loop of the part and the select Machine Stop option in the right panel. |
| 5. | Regenerate the NC code and the system will process the part as follows. |

| See | Part Edit Mode Shortcut Menu |
| --- | --- |
|  | Part Edit Mode Parameter Panel |
|  | Confirm/Display Setting |
|  | Save Template |
|  | Delete Trace |
|  | Joint Edit |
|  | Sequence Command in Parts |
|  | Lead In Edit |
|  | Change the Tool Assignment |
|  | Assign Tool-Lines |
|  | Layout Between Single Hit |
|  | Merge |
|  | Stretch |
|  | Shift |
|  | Direct Assignment |
|  | Move/Copy Tool |
|  | Apply Assignment the Same Inner |
|  | Fix Process Order |
|  | Change the Nibbling Pitch |
|  | Laser Hole Division |
|  | Show Tool |
|  | Option |

## 27.8 Sequence Command in Parts

Click  to open the Sequence Command in Parts panel in the right side of the window.

| Option | Description |
| --- | --- |
| Mouse Command | Click to select the traces and change their process sequences. The sequence numbers will automatically update each time when you click. |
| Complete | Click this button to complete the modification. |
| Cancel | Click this button to cancel your previous operation. |
| Clear All | Click this button to give up all the modifications and restore the process sequence to the original status. |
| Insert | Place a check mark in the check box to enable the Insert function. |
| Before | The trace you click will be processed one-step earlier than the one you just clicked. |
| After | The trace you click will be processed one-step later than the one you just clicked. |
| List Command | All the traces will be listed. The numbers indicate the sequence. You can select one trace and click or to change its sequence. The change effect will also be shown in the layout area. |

Example:

| 1. | Open the Sequence Command in Parts panel. You can see the default sequence in the layout area. |
| --- | --- |
| 2. | Select Mouse Command. Click the traces to change their process sequences. The numbers on the traces will automatically update each time when you click. |
| 3. | Select List Command. Select one trace in the list, and then click or to change its sequence. |

| See | Part Edit Mode Shortcut Menu |
| --- | --- |
|  | Part Edit Mode Parameter Panel |
|  | Confirm/Display Setting |
|  | Save Template |
|  | Delete Trace |
|  | Joint Edit |
|  | End Value |
|  | Lead In Edit |
|  | Change the Tool Assignment |
|  | Assign Tool-Lines |
|  | Layout Between Single Hit |
|  | Merge |
|  | Stretch |
|  | Shift |
|  | Direct Assignment |
|  | Move/Copy Tool |
|  | Apply Assignment the Same Inner |
|  | Fix Process Order |
|  | Change the Nibbling Pitch |
|  | Laser Hole Division |
|  | Show Tool |
|  | Option |

## 27.9 Lead In Edit

In Part Edit mode, click  to open Manual Assign Edit panel. Here you can edit the existing lead in/out or add new lead in/out manually.

Manual Assign Edit panel consists of three subordinate panels: Approach panel, Pierce panel and Correction/End Value panel. You can select an existed lead in/out and change it by changing the parameters in the three panels. You can also add a new lead in /out.

The arrow button  indicates the cutting direction and you can click this button to change the direction.

You can select cutting method from the bottom left dropdown list. There are ten options: E001~E010.

You can also select type of lead in/out from the bottom right dropdown list. There are four options: All, Partial, Direct, and Pierce.

Example:

| 1. | Take the following part as an example. |
| --- | --- |
| 2. | Select All to add lead in to a cutting path of the whole loop. |
| 3. | Move the pointer to the position you want add lead in. A red point appears and you can move it to change the lead in position. The blue arrow indicates the lead in direction. You can click the arrow button to change the cutting direction. Click to confirm the position. |
| 4. | If you are satisfied with the position, click to confirm your operation. A lead in will be added. |
| 5. | You can select the lead in and use the mouse to drag it to change its position. |
| 6. | Select Partial to add lead in to a cutting path of some selected patterns. |
| 7. | Move the mouse to the position you want to add lead in. An orange point appears indicating the beginning position to cut patterns. Click to confirm the position. Note: If you select Partial, you can only select the two end points of a pattern as the position to add lead in. |
| 8. | Move the point along the patterns you want to cut. You can click the arrow button to change the cutting direction. |
| 9. | Click to confirm the end point when you are satisfied. And then a lead in will be added to the patterns you selected. |
| 10. | Select Partial to add lead in to a section of cutting path selected. |
| 11. | Move the mouse to the position you want to add lead in. An orange point appears indicating the beginning. Click to confirm the position. Note: If you select Direct option, you can select any place of a pattern as the position to add lead in, which is different from the Partial option. |
| 12. | Move the point along the trace you want to cut. Click to confirm at each turning point. |
| 13. | Click to confirm the end pint when you are satisfied, and then right click to open a shortcut menu. Select complete to finish your operation. |
| 14. | A lead in will be added to the trace you selected. |
| 15. | Select Pierce option to add pierce point to lead in without pierce. |
| 17. | Select an existed lead in and then select Pierce option. Pierce will be added. Note: To use this function, you must select Laser Pierce or Special Pierce as pierce type before you select Pierce option. |
| 18. | If you are not satisfied with the lead in/out, select it and click button to delete it. |

| Option | Description |
| --- | --- |
| Approach |  |
| Length | Specify the length of lead in/out. |
| Angle | Specify the angle of lead in /out. |
| Radius | Specify the radius of lead in /out. |
| Lead Type | Specify the way of executing lead in/out. There are two options here: Cut (G01) and Only Move (G00). Select Cut (G01), the system will execute lead in/out by cutting. Select Only Move (G00), the system will execute lead in/out by only moving the laser head. This is available when you select Partial or Direct option. |
| Over Cut | Specify the over cut value. |
| The Distance from the End Point | Specify the distance between the lead in and the end points of the pattern. This function is available when you select All option. |
|  | If the value is zero, you can select any place on the pattern to add lead in. |
|  | Type 10 in the text box, then distance between the lead in and one of the end points of the pattern is 10. |
|  | The distance from one end point of the pattern to the lead in. |
|  | The distance from the other end point of the pattern to the lead in. |
| Display Pierce Collision Area | Place a check mark in the check box to display the pierce collision area. |
|  | Note: To use the option Display Pierce Collision Area, you should make settings in Laser Tool Assign window first. See Laser Tool Assign |
| Pierce |  |
| Pierce Type | Specify pierce type. There are four options: Laser Pierce, Special Pierce, No pierce and Punch Pierce. See How to add pierce to lead in |
|  | Laser Pierce | Special Pierce |
|  | No Pierce | Punch Pierce |
| A | Place a check mark in the A check box and type a value between 0 and 999 in the text box to the right to specify an existing pierce type that has been configured for the machine. Note: It’s useful for special pierce. |
| B | Place a check mark in the B check box and type a value from 0 to 99999.9999 in the text box to the right to specify the pierce range. Note: It’s useful for special pierce. |
| Condition | You can set pierce condition here. Note: It’s useful for special pierce. |
| On Line, Outer Corner, Inner Corner | There are three icons on the bottom of the panel. |
|  | Click the icon to open the Custom Lead In/Out Definition window. The Custom Lead In/Out Definition window consists of three panels: On Line, Outer Corner, Inner Corner. You can select, create and modify the lead-in and lead-out types using the options in this window. You can define lead-in/lead-outs for lines and corners. See Edit of lead in and lead out |
| Correction/End Value |  |
| End Value | Specify the end value. |
| Z value | Place a check mark in the check box to active this function and specify the Z value by typing or selecting value. |
| Display Work Chute Border | Place a check mark in the check box to display work chute border. Note: To use this function, you should select Chute1 or Chute2 as process after method. |
|  | Move the mouse to the joint and the system will display work chute. |
| Correction Direction | Specify the correction direction (offset value). |
| Convert Inner/Outer | Convert lead in/out form inner to outer, vice versa. |

How to add pierce to lead in

| 1. | Take the following lead in as an example. Suppose we want to add pierce to the lead in. |
| --- | --- |
| 2. | Select this lead in and select Laser Pierce option in the right panel. |
| 3. | Laser pierce will be added. Use the same way to add punch laser or select No Pierce option to delete an existed pierce. |
| 4. | If you want to add punch pierce, a dialog prompts the first time you select Punch Pierce option. |
| 5. | Click OK. And then click button on the toolbar to open Turret Info window. Select a tool by clicking it and click Close. |
| 6. | Select Punch Pierce again to add the pierce. |

| See | Part Edit Mode Shortcut Menu |
| --- | --- |
|  | Part Edit Mode Parameter Panel |
|  | Confirm/Display Setting |
|  | Save Template |
|  | Delete Trace |
|  | Joint Edit |
|  | End Value |
|  | Sequence Command in Parts |
|  | Change the Tool Assignment |
|  | Assign Tool-Lines |
|  | Layout Between Single Hit |
|  | Merge |
|  | Stretch |
|  | Shift |
|  | Direct Assignment |
|  | Move/Copy Tool |
|  | Apply Assignment the Same Inner |
|  | Fix Process Order |
|  | Change the Nibbling Pitch |
|  | Laser Hole Division |
|  | Show Tool |
|  | Option |

## 27.10 Change the Tool Assignment

You can use this function to manually change the tool assignment for the part.

In Part Edit mode, click  on the toolbar to open Change the Tool Assignment panel on the right side of the window.

Note:

When you click  on the toolbar, the Turret Info window will appear as well so that you can select tools from the list in this window.

You may select one of the two options below,

| Option | Description |
| --- | --- |
| Single Hit Center | Change single hit tools. See: To change single hit tools |
| Line | Change line tools. See: To change line tools |

To change single hit tools,

| 1. | Click Single Hit Center button in the Parameter panel. |
| --- | --- |
| 2. | Select the tool you want to use in the Turret Info window that appeared previously. In this instance, select a RO tool of ID number 26. |
| 3. | Then click the single hit tool tracks that you want to change in the layout area. The selected tool tracks will be highlighted. Right-click in the layout area and select Complete. |
| 4. | All the selected single hit tracks will be changed into the RO tool tracks that you specified. |
| 5. | If you want to specify the angle for a certain tool, you need to put this tool on an AI station before select it. In this case, put the SP tool of ID number 15 on an AI station and select it. |
| 6. | Now both the Axis C Value of AI Tool: textbox and Keep the Unchanged C Value: check box are enabled in the Parameter panel. |
|  |  | Note: C Value refers to the angle of the tool. When the Axis C Value of AI Tool: textbox is enabled, the default value in it is 0, which is the default angle of the tool. |
| 7. | Remain 0 in the Axis C Value of AI Tool: textbox. Then select the two RO tools on the left side. Right click and select Complete. The two RO tools are changed into the SP tools with default angle. |
| 8. | Type 225 in the Axis C Value of AI Tool: textbox. Then select the two RO tools on the right side. Right click and select Complete. The two RO tools are changed into the SP tools with angle of 225. |
| 9. | If you place a check mark in the Keep the Unchanged C Value: check box, the Axis C Value of AI Tool: textbox will be disabled. |
| 10. | Then select all the 5 single hit tools and Complete. The center RO tool is now changed into the SP tool with default angle, while the other 4 SP tools on both sides keep their angles unchanged. |

To change line tools,

| 1. | Click Line button in the Parameter panel. |
| --- | --- |
| 2. | Select the tool you want to use in the Turret Info window that appeared previously. In this instance, select a SQ tool of ID number 6. |
| 3. | Then click the line tool tracks that you want to change in the layout area. The selected tool tracks will be highlighted. Right-click in the layout area and select Complete. |
| 4. | The selected line track will be changed into the SQ tool track that you specified. |

| See | Part Edit Mode Shortcut Menu |
| --- | --- |
|  | Part Edit Mode Parameter Panel |
|  | Confirm/Display Setting |
|  | Save Template |
|  | Delete Trace |
|  | Joint Edit |
|  | End Value |
|  | Sequence Command in Parts |
|  | Lead In Edit |
|  | Assign Tool-Lines |
|  | Layout Between Single Hit |
|  | Merge |
|  | Stretch |
|  | Shift |
|  | Direct Assignment |
|  | Move/Copy Tool |
|  | Apply Assignment the Same Inner |
|  | Fix Process Order |
|  | Change the Nibbling Pitch |
|  | Laser Hole Division |
|  | Show Tool |
|  | Option |

## 27.11 Assign Tool-Lines

You can use this function to assign the tools to process lines by shear proof.

In Part Edit mode, click  on the toolbar to open Assign Tools-Lines panel on the right side of the window.

Note:

When you click  on the toolbar, the Turret Info window will appear so that you can select tools from the list in this window.

|  | There are two textboxes above the Parameter panel. The value in the left side textbox is the tool starting position protrusion value. The value in the right side textbox is the tool ending position protrusion value. |
| --- | --- |
|  | For instance, we specify 30 in the left textbox, and 50 in the right textbox. After select a tool from the Turret Info window and assign it on a line, the line will now be processed with the specified protrusion value. |
| Note: If there is a joint at the starting/ending position of a line, the specified protrusion value will be invalid. |

In the Parameter panel, you may select either Shear Proof (G66) or Lap Amount (G28) to assign the tools, and when you finish the edit and regenerate NC data, G66 or G28 NC command line will be output accordingly.

| See: | Shear Proof (G66) |
| --- | --- |
|  | Lap Amount (G28) |

Shear Proof (G66)

| When you select this option, the Parameter panel will display as below, |
| --- |
| Option | Description |
| Pitch | Specify the pitch value in the Pitch: textbox when the tool is used for nibbling process. |
| Slot Last Tool Pitch | Specify the last pitch value in the Slot Last Tool Pitch: textbox for a slotting type tool. |
| Imbalance Flag | This function is only available when a deburring tool is selected. The Imbalance Flag: checkbox is empty by default. In this circumstance, you can only assign the deburring tool on the line with the exact same tool width. For instance, when a RE 5 x 2 deburring tool is selected, we can only assign it on a line with the exact tool width of either 5 or 2. Otherwise, an error message window will display. |
|  | But when you place a check mark in the Imbalance Flag: checkbox, the deburring tool can then be assigned on any line with a tool width that is not less than the shorter side of the deburring tool. For instance, when a RE 5 x 2 deburring tool is selected, now we can assign it on any line as long as its tool width is not less than 2. |
| Collision Check | Place a check mark in the Collision Check: checkbox to enable the function. You may select either Auto or Manual option to check the collision. |
| Auto | Select this to execute automatic collision check. |
| Manual | Select this to execute manual collision check. |
| Collision Ins. | Click this to activate Manual Collision Check. |
|  | Example: |
|  | 1. | Specify the extrusion value as follows: |
|  | 2. | Assign a tool on the specified line. |
|  | 3. | Collision occurs as the following illustration shows. The punch process extends the line edge and interferences with the pattern. |
|  | 4. | Place a check mark in the Collision Check check box and select Auto. |
|  | 5. | The system will check the collisions for the tool assignment, and automatically make changes. |
|  | 6. | If you select Manual, collision also occurs when you finish assigning tool. |
|  | 7. | Click Collision Ins. Button in the right panel.(The Collision Ins. button switches to Collision End button automatically) |
|  | 8. | Move the pointer over the following line segment. |
|  | 9. | Click the line segment, and the system will automatically shorten the punch path. |
|  | 10 | Use the same way to modify the other side and click End Collision button to confirm your modification. |
| Assignment Side | Click the Assignment Side button to shift the tool assignment side along the process direction. There are four options: Auto, Left side, Online and Right side. You can click the button to switch among these four options. |
| Correction during Single Hit | This option enables you to make correction for a single hit tool assignment. |
|  | Suppose both protrusion values are set to 0 (no protrusion), click the Correction during Single Hit button to shift among CE, LF, and LB to make correction for a single hit tool assignment. |
|  |  | Centered by default. No correction. |
|  |  | Correction is made by front-end alignment of the tool. |
|  |  | Correction is made by back-end alignment of the tool. |

Lap Amount (G28)

| When you select this option, the Parameter panel will display as below, |
| --- |
| Option | Description |
| Lap | Specify the overlap value for the tool in the Lap: textbox |
| Layout of Ending Point Correction | Normally, the protrusion occurs more or less in each assignment. This option allows you to make correction for the last hit with no regard of the lap value you have specified so that the protrusion can be avoided. |
|  | In the circumstance that the lap value is set to 27, if the Layout of Ending Point Correction: checkbox remains empty, the tool will be assigned according to the lap value you have specified. The protrusion occurs as the picture indicates below. |
|  | But if you place a check mark in the Layout of Ending Point Correction: checkbox, then the last hit of the assignment will be adjusted with no regard of the lap value you have specified. The protrusion is avoided as the picture indicates below. |
| Select End Punch | Place a check mark in the Select End Punch: textbox. Then when you click in the layout area to assign the tool, the window below will display. |
|  | The window lists all the tools on the current turret. Choose a tool from the list as the last punch tool and click OK to proceed. Now the line is processed with assignment of the last punch tool you have just chosen. |

| See | Part Edit Mode Shortcut Menu |
| --- | --- |
|  | Part Edit Mode Parameter Panel |
|  | Confirm/Display Setting |
|  | Save Template |
|  | Delete Trace |
|  | Joint Edit |
|  | End Value |
|  | Sequence Command in Parts |
|  | Lead In Edit |
|  | Change the Tool Assignment |
|  | Layout Between Single Hit |
|  | Merge |
|  | Stretch |
|  | Shift |
|  | Direct Assignment |
|  | Move/Copy Tool |
|  | Apply Assignment the Same Inner |
|  | Fix Process Order |
|  | Change the Nibbling Pitch |
|  | Laser Hole Division |
|  | Show Tool |
|  | Option |

## 27.12 Layout Between Single Hit

In the Part Edit mode, you can click Layout Between Single Hit to assign a tool to single hit the pattern of two intersecting lines.

The Turret Info window appears.

This window is where you can select a tool from the tool list to process the area two lines intersect. When a tool is assigned to the left working area manually, the turret information of the tool in the Turret Info window turns to red, which indicate that this tool is in use.

Note:

Only the type of “RO”,”RE”,”SQ”,”OB”,”RR” tool can be assigned.

Example

| 1. | We will single-hit the pattern of two intersecting lines. |
| --- | --- |
| 2. | Select a tool in the Turret Info window. |
| 3. | Move the pointer into the left working area, click one line and then click the other line to assign the single-hit tool. |

| See | Part Edit Mode Shortcut Menu |
| --- | --- |
|  | Part Edit Mode Parameter Panel |
|  | Confirm/Display Setting |
|  | Save Template |
|  | Delete Trace |
|  | Joint Edit |
|  | End Value |
|  | Sequence Command in Parts |
|  | Lead In Edit |
|  | Change the Tool Assignment |
|  | Assign Tool-Lines |
|  | Merge |
|  | Stretch |
|  | Shift |
|  | Direct Assignment |
|  | Move/Copy Tool |
|  | Apply Assignment the Same Inner |
|  | Fix Process Order |
|  | Change the Nibbling Pitch |
|  | Laser Hole Division |
|  | Show Tool |
|  | Option |

## 27.13 Merge

Select  to open the Merge panel on the right side of the window.

Example

| 1. | We will assign a tool to process the following slant line. |
| --- | --- |
| 2. | Select a tool in the Turret Information panel. |
| 3. | Move into the working area, right-click and select Merge. The Select assign edge window appears. |
| 4. | Click to select a tool edge. The cross indicates the base point for the tool assignment. |
| 5. | Move the pointer over the slant line. Move the pointer close to the end point of the slant line to specify the base point for the tool assignment. |
| 6. | Click to assign the tool. The specified tool edge is assigned to process the selected slant line. The base point of both the tool and the slant segment match. |

| See | Part Edit Mode Shortcut Menu |
| --- | --- |
|  | Part Edit Mode Parameter Panel |
|  | Confirm/Display Setting |
|  | Save Template |
|  | Delete Trace |
|  | Joint Edit |
|  | End Value |
|  | Sequence Command in Parts |
|  | Lead In Edit |
|  | Change the Tool Assignment |
|  | Assign Tool-Lines |
|  | Layout Between Single Hit |
|  | Shift |
|  | Direct Assignment |
|  | Move/Copy Tool |
|  | Apply Assignment the Same Inner |
|  | Fix Process Order |
|  | Change the Nibbling Pitch |
|  | Laser Hole Division |
|  | Show Tool |
|  | Option |

## 27.14 Stretch

In the Part Edit mode, click Stretch button to open the Stretch panel on the right side of window.

This panel allows you to lengthen or shorten process path of a straight line/a curve on a pattern-by-pattern basis.  There are two methods:

| Method 1. | Just drag and drop the mouse to shift the tool along the moving path. |
| --- | --- |
| Method 2. | Select or type a value in the Tool Stretch Amount: text box to specify an adjustment amount based on the Input Method option. |

| Option | Description |
| --- | --- |
| Tool Select | Specify the base point to move the selected tool along the tool path. |
| End Point | Use the end point of the tool as the base point to adjust the process path. The red point in the following picture indicates the base point and the value in Tool Stretch Amount is 0, which indicate that the selected tool is placed in the original position. |
| Center | Use the center point of the tool as the base point to adjust the process path. The red point in the following picture indicates the base point and the value in Tool Stretch Amount is 0, which indicate that the selected tool is placed in the original position. |
| Input Method | These options become available only when you are adjusting the process path on the arc. |
| Angle | Adjust the process path by modifying the angle value. |
| Circle Length | Adjust the process path by modifying the arc length. |
| Tool Stretch Amount | As you move the pointer, the value in this text box will update automatically to reflect change you have made. Alternatively you can select or type the value to adjust the process path. |
|  | Notes: |
|  | Only when a tool on pattern is selected, is this text box available. If you are adjusting the process path on the lines, select or type a value in the text box to specify the distance to move the tool. If you are adjusting the process path on the arc, select or type a value in the text box to specify the degree or arc length to move the tool. A positive value implies that the tool path will be lengthened, while a negative value reveals that you want to shorten the tool path. |

| See | Part Edit Mode Shortcut Menu |
| --- | --- |
|  | Part Edit Mode Parameter Panel |
|  | Confirm/Display Setting |
|  | Save Template |
|  | Delete Trace |
|  | Joint Edit |
|  | End Value |
|  | Sequence Command in Parts |
|  | Lead In Edit |
|  | Change the Tool Assignment |
|  | Assign Tool-Lines |
|  | Layout Between Single Hit |
|  | Merge |
|  | Shift |
|  | Direct Assignment |
|  | Move/Copy Tool |
|  | Apply Assignment the Same Inner |
|  | Fix Process Order |
|  | Change the Nibbling Pitch |
|  | Laser Hole Division |
|  | Show Tool |
|  | Option |

| See: | Adjust the process path on the lines |
| --- | --- |
|  | Adjust the process path on the arcs |

### 27.14.1 Adjust the process path on the lines

| 1. | On the left part layout area, there is a pattern as follows. |
| --- | --- |
| 2. | Select End Point and move a pointer into the working area. |
| 3. | Click the tool you want to move, and then drag it along the tool path to adjust the tool size when the tool become blue. |
| 4. | When you are satisfied with tab size, click the left mouse button again to complete. |
| 5. | The value in Tool Stretch Amount: text box will reflect change you have made automatically. You can also select or type a value in this text box to specify the distance the tool will elongate from the base point. |

| See: | Adjust the process path on the lines |
| --- | --- |

### 27.14.2 Adjust the process path on the arcs

| 1. | Move the pointer to the tool on the arc. The blue dash line will appear, which indicate that you can drag the pointer to adjust the process path. |
| --- | --- |
| 2. | Drag the pointer along the process path to desired point. |
| 3. | If you are satisfied with the tab angle, click the left mouse button again to complete. |
| 4. | Meanwhile, the Input method option on the right side of window become available, so you can select a method to adjust the process path accurately. |
| 5. | The value in Tool Stretch Amount: text box will reflect change you have made automatically. |
| 6. | You can also select or type a value in the Tool Stretch Amount: text box to specify the angle, the tool path of this angle will be deleted/added. |

| See: | Adjust the process path on the arcs |
| --- | --- |

## 27.15 Shift

In the Part Edit mode, click Shift button to open the Shift panel on the right side of window.

This panel allows you to move the process path of a straight line/a curve on a pattern-by-pattern basis.  There are two methods:

| Method 1. | Just drag and drop the mouse to move the tool along the moving path. |
| --- | --- |
| Method 2. | Select or type a value in the Shift Amount: text box to specify a movement amount based on the Input Method option. |

| Option | Description |
| --- | --- |
| Tool Select | Specify the base point to move the selected tool along the tool path. |
| End Point | Use the end point of the tool as the base point to move the process path. The red point in the following picture indicates the base point and the value in Shift Amount is 0, which indicate that the selected tool is placed in the original position. |
| Center | Use the center point of the tool as the base point to move the process path. The red point in the following picture indicates the base point and the value in Shift Amount is 0, which indicate that the selected tool is placed in the original position. |
| Input Method | These options become available if you are moving the process path on the arc. |
| Angle | Select this option and type a degree in Shift Amount option, The specified process path will be rotated by this angle. |
| Circle Length | Select this option and type an arc length in Shift Amount option, The specified process path will be moved by this arc length. |
| Shift Amount | As you move the pointer, the value in this text box will update automatically to reflect change you have made. Alternatively you can select or type the value to move the process path. |
|  | Notes: |
|  | Only when a tool on pattern is selected, is this text box available. If you are moving the process path on the lines, select or type a value in the text box to specify the distance to move the tool. If you are moving the process path on the arc, select or type a value in the text box to specify the angle or arc length to move the tool. |

| See | Part Edit Mode Shortcut Menu |
| --- | --- |
|  | Part Edit Mode Parameter Panel |
|  | Confirm/Display Setting |
|  | Save Template |
|  | Delete Trace |
|  | Joint Edit |
|  | End Value |
|  | Sequence Command in Parts |
|  | Lead In Edit |
|  | Change the Tool Assignment |
|  | Assign Tool-Lines |
|  | Layout Between Single Hit |
|  | Merge |
|  | Stretch |
|  | Direct Assignment |
|  | Move/Copy Tool |
|  | Apply Assignment the Same Inner |
|  | Fix Process Order |
|  | Change the Nibbling Pitch |
|  | Laser Hole Division |
|  | Show Tool |
|  | Option |

| See: | Move the process path on the lines |
| --- | --- |
|  | Move the process path on the arcs |

### 27.15.1 Move the process path on the lines

| 1. | On the left Part Layout area, there is a pattern as follows. |
| --- | --- |
| 2. | Select End Point and move a pointer into the working area. |
| 3. | Click the tool you want to move, and then drag it along the tool path to move the tool when the tool becomes blue. |
| 4. | When you are satisfied with new position, click the left mouse button again to complete. |
| 5. | The value in Shift Amount: text box will reflect change you have made automatically. You can also select or type a value in this text box to specify the distance the tool will move from the base point. |
|  | Note: |
|  | A positive value in the Shift Amount option implies that movement is along the plus X/Y axis, while a negative value reveals that you want to move the tool path along the minus X/Y axis. |

| See: | Move the process path on the arcs |
| --- | --- |

### 27.15.2 Move the process path on the arcs

| 1. | Move the pointer to the tool on the arc. The blue dash line will appear, which indicates that you can drag the pointer to move the process path. |
| --- | --- |
| 2. | Drag the pointer along the process path to desired point. |
| 3. | If you are satisfied with new position, click the left mouse button again to complete. |
| 4. | Meanwhile, the Input method option on the right side of window become available, so you can select a method to move the process path accurately. |
| 5. | The value in Shift Amount: text box will reflect change you have made automatically. |
| 6. | You can also select or type a value in the Shift Amount: text box to specify the angle, the tool will turn by specified degree clockwise/counter-clockwise. |
|  | Note: |
|  | A positive value in the Shift Amount option implies that specified process path rotates clockwise, while a negative value indicates that you turn the process path counter-clockwise. |

| See: | Move the process path on the lines |
| --- | --- |

## 27.16 Direct Assignment

In the Part Edit mode, Click Direct Assignment button to open the Direct Assignment panel with the Turret Info dialog on the left side of the window.

The Direct Assignment option allows you to place common patterns on the part without adding geometry. Select a tool from the Turret Info dialog, and then select a type to create the patterns. You can define a Direct Assignment region by drawing the pattern on the part or sheet. The selected tool is then assigned to punch out the region.

| See | Part Edit Mode Shortcut Menu |
| --- | --- |
|  | Part Edit Mode Parameter Panel |
|  | Confirm/Display Setting |
|  | Save Template |
|  | Delete Trace |
|  | Joint Edit |
|  | End Value |
|  | Sequence Command in Parts |
|  | Lead In Edit |
|  | Change the Tool Assignment |
|  | Assign Tool-Lines |
|  | Layout Between Single Hit |
|  | Merge |
|  | Stretch |
|  | Shift |
|  | Move/Copy Tool |
|  | Apply Assignment the Same Inner |
|  | Fix Process Order |
|  | Change the Nibbling Pitch |
|  | Laser Hole Division |
|  | Show Tool |
|  | Option |

| See: | Assignment between 2 points |
| --- | --- |
|  | Diagonal Assignment |
|  | Parameter Assignment |
|  | Hole Assignment |

### 27.16.1 Assignment between 2 points

Click to activate the Assignment between 2 Points panel.

The panel allows you to set the conditions for protrusion value, pitch, punch side, and the base point for single-hit assignment.

| Options | Description |
| --- | --- |
| Text boxes | These two text boxes allow you to specify the protrusion value. The value in the left text box indicates the protrusion at the starting point side of process path, while the value in the right reveals the protrusion at the ending point side. |
| Pitch | This option is used to specify the distance between tool hits when nibbling or shearing. |
|  | Note: |
|  | When shearing or nibbling process is executed, this option will be available. |
| Assignment Side | This option is used to specify the position to assign tools to process the open path. Every time you click this button, the image of the button will change. There are four choices: Left Side, Right Side, On Line, Auto. |
| Left Side | Place the tool to the left side of the pattern in the process direction. |
| On Line | Place the tool on the center of the pattern. |
| Right Side | Place the tool to the right side of the pattern in the process direction. |
| Auto | System will place the tool to the optimum position automatically |
| Correction During Single Hit | When a single hit is assigned, it is set at the center of the specified line. Click [LF], [CE], and [LB] to rearrange a tool at a position based on the start and end points. Every time you click this button, the image of the button will change. |
| CE | Assign the tool to single-hit the pattern. The tool center and pattern center will match. |
| LB | Assign the tool to single-hit the pattern from the starting point of the process path. |
| LF | Assign the tool to single-hit the pattern from the end point of the process path. |

| See: | Diagonal Assignment |
| --- | --- |
|  | Parameter Assignment |
|  | Hole Assignment |

### 27.16.2 Diagonal Assignment

Click  to activate the Diagonal Assignment panel.

This option allows you to assign a RE or SQ tool to cutout the inside part of the rectangle or square formed by two points of the diagonal. You can select or type a value in the Input C-axis Value to specify the angle of the pattern.

Example:

| 1. | Select a tool from the Turret Info window. |
| --- | --- |
| 2. | Select or type a value in the Input C-axis Value: text box. |
| 3. | Move the pointer to the left part layout area and click the left button of mouse to define the first point, and then drag it to shape a blue rectangle frame. |
| 4. | Click again to assign the specified tool to the pattern. |

| See: | Assignment between 2 points |
| --- | --- |
|  | Parameter Assignment |
|  | Hole Assignment |

### 27.16.3 Parameter Assignment

Click  to activate the Parameter Assignment panel.

| Option | Description |
| --- | --- |
| Pattern | Click arrow button to open a drop-down list. There are five patterns to choose. These options under the Pattern: drop down list will update as you select different pattern. |
| Direct Single Hit | Assign tools to single-hit pattern. |
| Line Pattern LAA | Assign tools as line at angle pattern. |
|  | Pitch | Select or type the distance between tools. |
|  | Quantity | Select or type the number of hits. |
|  | Pattern Angle | Select or type an angle for tilting pattern. |
|  | Include Standard Position | Place a check mark in this check box to determine whether base hit (first hit) is included or not. |
|  |  | Not Checked | Checked |
| Pattern Grid | Assign tools as grid pattern. |
|  | Prior Direction | Select the X or Y direction for processing priority. |
|  | Pitch | Pitch X and Y for tool hits for X and Y-axis. |
|  | Quantity | Specify the number of tool hits for X and Y-axis. |
|  | Pattern Angle | Select or type an angle for tilting pattern. |
|  | Include Standard Position | Place a check mark in this check box to determine whether base hit (first hit) is included or not. |
|  |  | Not Checked | Checked |
| Arc ARC | Assign tools as Arc pattern. |
|  | Radius | Radius of the pattern. |
|  | Starting Angle | Specify the starting angle for the pattern. |
|  | Pitch Angle | Angle pitch between tool hits. |
|  | Quantity | Specify the number of tool hits. |
|  | Fixed Tool Angle | When AI tool is selected, this option is available. |
|  |  | Not Checked | Checked |
| Round BHC | Assign tools as bold hole circle (BHC) pattern. |
|  | Radius | Radius of the pattern. |
|  | Starting Angle | Specify the starting angle for the pattern. |
|  | Quantity | Specify the number of tool hits. |
|  | Fixed Tool Angle | When AI tool is selected, this option is available. |
|  |  | Not Checked | Checked |
| Tool Standard Position | Specify a reference point as the first hit. |
| AI Tool Angle | Select or type a tilting degree for AI tool. |

| See: | Assignment between 2 points |
| --- | --- |
|  | Diagonal Assignment |
|  | Hole Assignment |

### 27.16.4 Hole Assignment

Click  to activate the Hole Assignment panel.

This panel allows you to specify the way to punch out the hole.

| Option | Description |
| --- | --- |
|  | The round hole is processed as follows. |
|  | The round hole is processed as follows. |
|  | Click this option, and then select a tool from the Please select the tool that are assigned in the middle window. |
|  | Click OK button and the round hole are processed as follows. |

| See: | Assignment between 2 points |
| --- | --- |
|  | Diagonal Assignment |
|  | Parameter Assignment |

## 27.17 Move/Copy Tool

You can use this function to move/rotate/reverse the tracks.

In part edit mode, click  on the toolbar to open Move/Copy Track panel on the right side of the window.

You may select one of the three options below:

| Option | Description |
| --- | --- |
| Move | Move the selected tracks in Move mode. Move the duplicates of the selected tracks in Copy mode. See: To move |
| Rotate | Rotate the selected tracks in Move mode. Rotate the duplicates of the selected tracks in Copy mode. See: To rotate |
| Reverse | Reverse the selected tracks in Move mode. Reverse the duplicates of the selected tracks in Copy mode. See: To reverse |
| Note: To switch between the Move and Copy mode, you can click the Move or Copy button in the parameter panel of each option. |

To move

|  | Select Move option. The panel on the right side of the window will display as below. You can select either Specify the Standard Point or Specify X/Y Move Amount to move the selected tracks. |
| --- | --- |
| A1. | Select Specify the Standard Point option in Move mode from the Parameter panel. |
| A2. | Select the tracks that you want to move. The selected tracks will be highlighted. Right-click in the layout area and select Complete from the shortcut menu. |
| A3. | Click in the layout area to specify a standard point for the original tracks. Then, the current position of your mouse pointer will be the standard point for the imaginary tracks that appear. Move the mouse pointer to move the imaginary tracks. |
| A4. | Once you find the ideal place, click in the layout area to confirm the operation. |
| A5. | Click the Move button to switch to the Copy mode. In this case, we specify 2 in the enabled textbox on the right side of the button. |
| A6. | Now after the standard point is specified, 2 duplicates of the imaginary tracks will appear. |
| A7. | Once you find the ideal place, click in the layout area to finish copying. 2 duplicates of the selected tracks will be made without moving the originals. |
| B1. | You can also select Specify X/Y Move Amount from the Parameter panel to move the selected tracks. |
| B2. | The (X/(Y section will be enabled. Specify the move amount in the (X and (Y: textbox respectively. In this case, we specify 350 for (X, and specify –50 for (Y. |
| B3. | Select the tracks you want to move. Then right-click in the layout area and select Complete from the shortcut menu. The imaginary tracks will appear at the ( position that you have specified. |
| B4. | Click in the layout area to confirm the operation. |
| B5. | Click the Move button to switch to the Copy mode. In this case, we specify 3 in the enabled textbox on the right side of the button. |
| B6. | Now after we select Complete from the shortcut menu, 3 duplicates of the imaginary tracks will appear. Each duplicate is at the specified ( position in accordance with the previous one. Click in the layout area to confirm the operation and make the duplicates without moving the originals. |

To rotate,

|  | Select Rotate option. The panel on the right side of the window will display as below. |
| --- | --- |
| 1. | Select the tracks you want to rotate in the move mode. The selected tracks will be highlighted. Right-click in the layout area and select Complete from the shortcut menu. |
| 2. | Click in the layout area to specify a center point. The imaginary tracks will appear and rotate with the moving angle of the mouse pointer. At the same time, the figure in the Rotation Angle: textbox will automatically update according to the current rotation angle of the imaginary tracks. |
| 3. | Once you find the ideal place, click in the layout area to rotate the tracks. |
|  | Alternatively, you can type a value into the Rotation Angle: textbox directly and press <Enter> to rotate the tracks. |
| 4. | Click the Move button to switch to the Copy mode. In this case, we specify 3 in the enabled textbox on the right side of the button. |
| 5. | Now after the center point is specified, 3 duplicates of the imaginary tracks will appear. Each duplicate is at the position of the ( angle amount in accordance with the previous one. |
| 6. | In this case, we specify 90 in the Rotation Angle: textbox and then press <Enter>. 3 duplicates of the selected tracks are made without moving the original. |

To reverse,

|  | Select Reverse option. The panel on the right side of the window will display as below. You can select either Specify the Standard Point or Axis Position to reverse the selected tracks. |
| --- | --- |
| A1. | Select Specify the Standard Point option in Move mode from the Parameter panel. Then click X Axis button. |
| A2. | Select the tracks that you want to reverse. The selected tracks will be highlighted. Right-click in the layout area and select Complete from the shortcut menu. |
| A3. | Click in the layout area to specify a standard point. The imaginary tracks will appear at the reverse position along the X-axis of the standard point. |
| A4. | If you click Y Axis button in the Parameter panel, the imaginary tracks will appear at the reverse position along the Y-axis of the standard point. |
| A5. | If you click Slant button in the Parameter panel, the current mouse pointer and the specified standard point will form a line. The imaginary tracks will appear at the reverse position along this line. Move the mouse pointer to move this line so that the position of the imaginary tracks will be changed accordingly. |
| A6. | Once you find the ideal place, click in the layout area to reverse the tracks. |
|  | X Axis | Y Axis | Slant |
| A7. | Click the Move button to switch to the Copy mode. You can reverse only one duplicate each time without moving the original tracks. |
|  | Note: In Reverse option, when you click the Move button to switch to Copy mode, the textbox on the right side of the button will NOT be enabled. In the Copy mode of Reverse option, only one duplicate can be made each time. |
| B1. | You can also select Axis Position from the Parameter panel to reverse the selected tracks. Click X Axis button as well. |
| B2. | Select the tracks that you want to reverse. The selected tracks will be highlighted. Right-click in the layout area and select Complete from the shortcut menu. |
| B3. | A horizontal line will appear across the current mouse pointer. The imaginary tracks will appear at the reverse position along this horizontal line. Move the mouse pointer to move this line so that the position of the imaginary tracks will be changed accordingly. |
| B4. | If you click Y Axis button in the Parameter panel, a vertical line will appear across the current mouse pointer. The imaginary tracks will appear at the reverse position along this vertical line. Move the mouse pointer to move this line so that the position of the imaginary tracks will be changed accordingly. |
|  | Note: The Slant button is NOT available when you select Axis Position. |
| B5. | Once you find the ideal place, click in the layout area to reverse the tracks. |
|  | X Axis | Y Axis |
| B6. | Click the Move button to switch to the Copy mode. You can reverse only one duplicate each time without moving the original tracks. |

| See | Part Edit Mode Shortcut Menu |
| --- | --- |
|  | Part Edit Mode Parameter Panel |
|  | Confirm/Display Setting |
|  | Save Template |
|  | Delete Trace |
|  | Joint Edit |
|  | End Value |
|  | Sequence Command in Parts |
|  | Lead In Edit |
|  | Change the Tool Assignment |
|  | Assign Tool-Lines |
|  | Layout Between Single Hit |
|  | Merge |
|  | Stretch |
|  | Shift |
|  | Direct Assignment |
|  | Apply Assignment the Same Inner |
|  | Fix Process Order |
|  | Change the Nibbling Pitch |
|  | Laser Hole Division |
|  | Show Tool |
|  | Option |

## 27.18 Apply Assignment the Same Inner

You may select one of the two options below,

| Option | Description |
| --- | --- |
| All Holes | Apply the assignment of the selected inner to all the other same inners. See: To apply to all the same inners |
| Specified Hole | Apply the assignment of the selected inner to the specified same inners. See: To apply to the specified same inners |

To apply to all the same inners,

| 1. | Select All Holes in the Parameter panel. |
| --- | --- |
| 2. | Move the mouse pointer on one inner. All the same inners will be highlighted together automatically. |
| 3. | In this case, only the inner at the right side has two joints. Now we want to apply the assignment of two joints to all the other same inners. |
| 4. | Click to select the inner with two joints and then click the Apply button in the Parameter panel. Now all the same inners are with the two joints assignment. |

To apply to the specified same inners,

| 1. | Select Specified Hole in the Parameter panel. |
| --- | --- |
| 2. | In this case, only the inner on the right side has no joint. Now we want to apply the no joint assignment to the four inners in the lower row. |
| 3. | Click to select the inner with no joint and then click the four inners in the lower row one by one. Finally, click the Apply button in the Parameter panel. Now all the four inners in the lower row are with no joint assignment. |

| See | Part Edit Mode Shortcut Menu |
| --- | --- |
|  | Part Edit Mode Parameter Panel |
|  | Confirm/Display Setting |
|  | Save Template |
|  | Delete Trace |
|  | Joint Edit |
|  | End Value |
|  | Sequence Command in Parts |
|  | Lead In Edit |
|  | Change the Tool Assignment |
|  | Assign Tool-Lines |
|  | Layout Between Single Hit |
|  | Merge |
|  | Stretch |
|  | Shift |
|  | Direct Assignment |
|  | Move/Copy Tool |
|  | Fix Process Order |
|  | Change the Nibbling Pitch |
|  | Laser Hole Division |
|  | Show Tool |
|  | Option |

## 27.19 Fix Process Order

Note:

The Fix Between Loops: check box is placed with a check mark by default so that the function section below is enabled. Removing the check mark will disable the function section.

Example

| 1. | In this result view, the part is processed in the following order. But now we want to modify the order for it. |
| --- | --- |
| 2. | Move the mouse pointer to the layout area, and click the elements one by one in the new order you want. |
|  | Note: For punch process, there is always a last process element in the part. So you cannot modify the process order for it. The color of the last processing element will be highlighted according to the color you have specified. See: Color of Fix Process Order |
|  | Note: You can click Process Direction Change button to change the process direction for the selected element. |
| 3. | Click Create button to fix the order you have modified. The color of the fixed elements will be highlighted according to the color you have specified. See: Color of Fix Process Order |
| 4. | Select any of the fixed element and use or button to confirm the new process order. If you are still not satisfied, you can select the fixed elements and then click the Release button to cancel the modification for them. |
| 5. | Regenerate the NC code. Now the part will be processed in the order you have just specified. |
|  | Note: If you place a check mark in the Same Tooling Selection: check box, when you select any of the elements with the same tooling, all of them will be highlighted together at the same time. |

Color of Fix Process Order

| 1. | Click a color square to open the palette for the corresponding item. |
| --- | --- |
| 2. | Select a color for the item that you want it to display in the layout area. In this case, we select Yellow for Fix Process Order. |
| 3. | Now, the Fix Process Order color square becomes Yellow. The fixed elements in the layout area are in yellow accordingly. |

| See | Part Edit Mode Shortcut Menu |
| --- | --- |
|  | Part Edit Mode Parameter Panel |
|  | Confirm/Display Setting |
|  | Save Template |
|  | Delete Trace |
|  | Joint Edit |
|  | End Value |
|  | Sequence Command in Parts |
|  | Lead In Edit |
|  | Change the Tool Assignment |
|  | Assign Tool-Lines |
|  | Layout Between Single Hit |
|  | Merge |
|  | Stretch |
|  | Shift |
|  | Direct Assignment |
|  | Move/Copy Tool |
|  | Apply Assignment the Same Inner |
|  | Change the Nibbling Pitch |
|  | Laser Hole Division |
|  | Show Tool |
|  | Option |

## 27.20 Change the Nibbling Pitch

You can use this function to manually change the nibbling pitch.

In Part Edit mode, click  on the toolbar to open Change Nibbling Pitch panel on the right side of the window.

| 1. | Select the nibbling track that you want to change in the layout area. The selected track will be highlighted. The values in the Nibbling Pitch: textbox and Height: textbox will update according to the selected nibbling track. |
| --- | --- |
| 2. | You may either select Nibbling Pitch or Height option in the parameter panel to enable the textbox on the right side. Type a valid value in the enabled textbox and click the Apply button to change. |
|  | Note: The values of Nibbling Pitch and Height are interrelated. When you specify either of them and click Apply, the other will change accordingly. |

| See | Part Edit Mode Shortcut Menu |
| --- | --- |
|  | Part Edit Mode Parameter Panel |
|  | Confirm/Display Setting |
|  | Save Template |
|  | Delete Trace |
|  | Joint Edit |
|  | End Value |
|  | Sequence Command in Parts |
|  | Lead In Edit |
|  | Change the Tool Assignment |
|  | Assign Tool-Lines |
|  | Layout Between Single Hit |
|  | Merge |
|  | Stretch |
|  | Shift |
|  | Direct Assignment |
|  | Move/Copy Tool |
|  | Apply Assignment the Same Inner |
|  | Fix Process Order |
|  | Change the Nibbling Pitch |
|  | Show Tool |
|  | Option |

## 27.21 Laser Hole Division

In Part Edit mode, click  to open Laser Hole Division panel. Here you can make settings to divide hole manually. The settings here are the same with those in Cut Plate

Example

| 1. | The following part has two holes in it. Click to open Laser Hole Division panel. |
| --- | --- |
| 2. | Press the button below Cutting Method to expand the four methods and select cross cutting. Press the button below Lead In Method to expand the four methods and select central pierce. |
| 3. | Specify the max size value: |
| 4. | In the Part Layout area, drag the mouse to either of the perimeter of the hole and you can see the result of division. |

| See | Part Edit Mode Shortcut Menu |
| --- | --- |
|  | Part Edit Mode Parameter Panel |
|  | Confirm/Display Setting |
|  | Save Template |
|  | Delete Trace |
|  | Joint Edit |
|  | End Value |
|  | Sequence Command in Parts |
|  | Lead In Edit |
|  | Change the Tool Assignment |
|  | Assign Tool-Lines |
|  | Layout Between Single Hit |
|  | Merge |
|  | Stretch |
|  | Shift |
|  | Direct Assignment |
|  | Move/Copy Tool |
|  | Apply Assignment the Same Inner |
|  | Fix Process Order |
|  | Change the Nibbling Pitch |
|  | Laser Hole Division |
|  | Show Tool |
|  | Option |

## 27.22 Show Tool

In Part Edit mode, click  on the toolbar to display the Turret Info window.

You can view the current turret and tools usage information in this window.

| See | Part Edit Mode Shortcut Menu |
| --- | --- |
|  | Part Edit Mode Parameter Panel |
|  | Confirm/Display Setting |
|  | Save Template |
|  | Delete Trace |
|  | Joint Edit |
|  | End Value |
|  | Sequence Command in Parts |
|  | Lead In Edit |
|  | Change the Tool Assignment |
|  | Assign Tool-Lines |
|  | Layout Between Single Hit |
|  | Merge |
|  | Stretch |
|  | Shift |
|  | Direct Assignment |
|  | Move/Copy Tool |
|  | Apply Assignment the Same Inner |
|  | Fix Process Order |
|  | Change the Nibbling Pitch |
|  | Laser Hole Division |
|  | Option |

## 27.23 Option

In the Part Edit mode, click button to open the Option window.

Those options are designed to decide whether to display specified message when you plan to exit Part Edit mode.

| Item | Description |
| --- | --- |
| Do not display message of applying to part when exiting edit mode | Place a check mark in the check box, the system will not display the message of applying to part when you click button. You can make detailed setting in the following drop-down list. The system will execute it automatically. |
|  | If you clear a check mark in the check box, the system will display the following message after you save the setting and exit Manual Edit mode. Then the following dialog appears when you save the setting and exit Manual Edit mode You may make detailed setting in the Reflect Edit Result window. |
|  | Item | Description |
|  |  | Select this option to apply the editing result to the part you are editing. |
|  |  | Select this option to make detailed settings. There are four groups to select. |
|  |  | Apply the editing result to the same part with the same angle in the current sheet. |
|  |  | Apply the editing result to the same part in the current sheet. |
|  |  | Apply the editing result to the same part with the same angle in all sheets. |
|  |  | Apply the editing result to the same part in all sheets. |
| Do not display message after selecting cancel command | Place a check mark in the check box, the system will not display the message of applying to part when you click button. The system will ignore or save changes automatically when you click button by selecting an option from the following drop-down list. |
|  | If you clear a check mark in the check box, the system will display the following message when you want to cancel the command. |
|  | Click Yes button, the system will end your editing by ignoring the setting you have made. |
|  | Click No button and the system will end your editing by saving the setting you have made. |
|  | Click Cancel button, the system will return to editing mode. |
|  | Place a check mark in Don’t ask me again check box and click Yes/No button. At the same time the system will place a check mark in Do not display message after selecting cancel command check box automatically in the Option window. |
| Do not display message if space is not enough when add parts | Place a check mark in the check box, the system will not display the message when the space is not enough to add part. |
| Use command of editing single part to maximize window | Place a check mark in the check box and click Part Edit button, the system will expand AICAM main window so that it covers the full screen. |
| Window returns to the initial size after editing is complete | Place a check mark in the check box, the maximized window will restore to its previous size after you exit the manual edit mode. |
| Release the Command of not display message after version updated | Place a check mark in this check box, system will not keep the settings of Don’t Display Message you have specified in previous version during version update. |
| Collision check when moving parts | Place a check mark in this check box, the following message will prompt when parts move and collision happens. |

| Take the following part as an example: |
| --- |
| 1. | In Option window, place a check mark in the check box and select Inside Same Sheet and Part of Same Angle in Auto Apply: drop-down list. |
| 2. | Click OK to close the Option window. |
| 3. | In the Manual Edit toolbar, click Part Edit button to enter Part Edit mode. On the left part layout, select one part and add two joints. See Joint Edit |
| 4. | Click button to save the setting. Two joints are automatically added to the part in the same sheet and with the same angle. |

| See | Part Edit Mode Shortcut Menu |
| --- | --- |
|  | Part Edit Mode Parameter Panel |
|  | Confirm/Display Setting |
|  | Save Template |
|  | Delete Trace |
|  | Joint Edit |
|  | End Value |
|  | Sequence Command in Parts |
|  | Lead In Edit |
|  | Change the Tool Assignment |
|  | Assign Tool-Lines |
|  | Layout Between Single Hit |
|  | Merge |
|  | Stretch |
|  | Shift |
|  | Direct Assignment |
|  | Move/Copy Tool |
|  | Apply Assignment the Same Inner |
|  | Fix Process Order |
|  | Change the Nibbling Pitch |
|  | Laser Hole Division |
|  | Show Tool |

# Chapter 28: Auto Correction Condition Setup

|  | Click the Auto Cleaning Preference button in the main window to display the Autocorrection Condition Setup window. The options in this window allow you to control how the APDOM parses the patterns created in CAD. |
| --- | --- |
| Note: You should make settings in this window for the system to parse the loaded parts before loading them into Dr. ABE. |

| See: | Merge | Fill Gaps |
| --- | --- | --- |
|  | Remove Guidelines | Break |
|  | Get Outer Loop | Extra Entities Removal |
|  | Remove Slot | Small Entities Removal |
|  | Standard Hole Detection | Remove Holes Enclosing Pattern |
|  | Corner Slot | Parts Separation |
|  | Decimal Approximation | Arc Straightening |
|  | Slant Line Removal | Minute Gap Removal |
|  | Polylines To Arc | Special Hole Detection |
|  | Spline to Lines/Arcs | Delete Point |
|  | Ignore Conditions for Large Data |  |

## 28.1 Merge

This option is used to control whether the system parses a line consisting of several line segments into an integrated line or separate lines.

Example

| 1. | The top edge of the following part has a line consists several line segments (as indicated by the red rectangle). |
| --- | --- |
| 2. | If you remove the check mark from the Merge check box, the status of the option becomes Off. |
| 3. | The system will process each of the line segments separately. |
| 4. | If you place a check mark in the Merge check box, the status of the option becomes On. |
| 5. | The system will process the line segments as a single line. |

| See: | Remove Guidelines | Fill Gaps |
| --- | --- | --- |
|  | Get Outer Loop | Break |
|  | Remove Slot | Extra Entities Removal |
|  | Standard Hole Detection | Small Entities Removal |
|  | Corner Slot | Remove Holes Enclosing Pattern |
|  | Decimal Approximation | Parts Separation |
|  | Slant Line Removal | Arc Straightening |
|  | Polylines To Arc | Minute Gap Removal |
|  | Spline to Lines/Arcs | Special Hole Detection |
|  | Ignore Conditions for Large Data | Delete Point |

## 28.2 Fill Gaps

This option is used to control whether to fill the gaps on a pattern drawing. If you set the status of Fill Gaps to On, the system will fill the loop gaps that are within the defined tolerance to make a closed loop. You can specify the tolerance for this option. The minimum value is 0.001.

Example

| 1. | The following part has a gap in the upper right-hand corner. |
| --- | --- |
| 2. | If you remove the check mark from the Fill Gaps check box, the status of this option becomes Off. |
| 3. | Load the part mentioned above to Dr. ABE. Click the Nesting Plan button in the main window to open the Nesting Schedule window. The symbol appears in the CAD column. Click it and then a warning message appears. Dr. ABE will not process this part. The part boundary must be closed. |
| 4. | Place a check mark in the Fill Gap check box, and set a tolerance value in the text box as follows. |
| 5. | The system will close the gap. The part can be processed. |

| See: | Merge | Break |
| --- | --- | --- |
|  | Remove Guidelines | Extra Entities Removal |
|  | Get Outer Loop | Small Entities Removal |
|  | Remove Slot | Remove Holes Enclosing Pattern |
|  | Standard Hole Detection | Parts Separation |
|  | Corner Slot | Arc Straightening |
|  | Decimal Approximation | Minute Gap Removal |
|  | Slant Line Removal | Special Hole Detection |
|  | Polylines To Arc | Delete Point |
|  | Spline to Lines/Arcs | Ignore Conditions for Large Data |

## 28.3 Remove Guidelines

This option is used to control whether to remove guidelines on a pattern drawing. If you set the status of Remove Guidelines to On, the system will remove the guidelines.

Example

| 1. | You might use guidelines in CAD to locate a pattern. The crosshairs on the following part are used to locate the center points of the inner round holes. |
| --- | --- |
| 2. | If you remove the check mark from the Remove Guidelines check box, the status of the option becomes Off. The system considers these guidelines as open paths. |
| 3. | The system will use guidelines. |
| 4. | If you place a check mark in the Remove Guidelines check box, the status becomes On. |
| 5. | The system will remove the guidelines and will not process them. |

| See: | Merge | Fill Gaps |
| --- | --- | --- |
|  | Get Outer Loop | Break |
|  | Remove Slot | Extra Entities Removal |
|  | Standard Hole Detection | Small Entities Removal |
|  | Corner Slot | Remove Holes Enclosing Pattern |
|  | Decimal Approximation | Parts Separation |
|  | Slant Line Removal | Arc Straightening |
|  | Polylines To Arc | Minute Gap Removal |
|  | Spline to Lines/Arcs | Special Hole Detection |
|  | Ignore Conditions for Large Data | Delete Point |

## 28.4 Break

This option is used to control whether to break the intersecting lines to remove the unnecessary line segments. If you set the status of Break to On, the system will break the intersecting entities.

Example

| 1. | A pattern on this part has intersecting lines. |
| --- | --- |
| 2. | When you remove the check mark from the Break check box, the status of this option becomes Off. The system will treat the intersecting lines as open paths. |
| 3. | The result will be as following: |
| 4. | When you place a check mark in the Break check box, the status becomes On. |
| 5. | The system will trim the segments. |

| See: | Merge | Fill Gaps |
| --- | --- | --- |
|  | Remove Guidelines | Extra Entities Removal |
|  | Get Outer Loop | Small Entities Removal |
|  | Remove Slot | Remove Holes Enclosing Pattern |
|  | Standard Hole Detection | Parts Separation |
|  | Corner Slot | Arc Straightening |
|  | Decimal Approximation | Minute Gap Removal |
|  | Slant Line Removal | Special Hole Detection |
|  | Polylines To Arc | Delete Point |
|  | Spline to Lines/Arcs | Ignore Conditions for Large Data |

## 28.5 Get Outer Loop

This option is used to control whether to merge two intersecting patterns. If you set the status of Get Outer Loop to On, the system will recognize the outermost loop of the intersecting loops.

Example

| 1. | There are two patterns on this part that overlap. |
| --- | --- |
| 2. | If you remove the check mark from the Get Outer Loop check box, the status of the option becomes Off The system will process the two patterns as two separate loops. |
| 3. | The result will be as following: |
| 4. | If you place a check mark in the Get Outer Loop check box, the status becomes On. |
| 5. | The system will merge the two loops into one using the outermost boundary of the previous two loops. The remaining lines are removed from the part. |

| See: | Merge | Fill Gaps |
| --- | --- | --- |
|  | Remove Guidelines | Break |
|  | Remove Slot | Extra Entities Removal |
|  | Standard Hole Detection | Small Entities Removal |
|  | Corner Slot | Remove Holes Enclosing Pattern |
|  | Decimal Approximation | Parts Separation |
|  | Slant Line Removal | Arc Straightening |
|  | Polylines To Arc | Minute Gap Removal |
|  | Spline to Lines/Arcs | Special Hole Detection |
|  | Ignore Conditions for Large Data | Delete Point |

## 28.6 Extra Entities Removal

This option is used to control whether to remove the extra entities. If you set the status of Extra Entities Removal to On, the system will remove the specified extra entities inside or outside parts.  You should define the maximum size of the extra entities to be removed.

Example

| 1. | The following part has extra line entities. |
| --- | --- |
| 2. | If you remove the check mark from the Extra Entities Removal check box, the status of the option becomes Off. |
| 3. | The result will be as following: |
| 4. | If you place a check mark in the Extra Entities Removal check box, the status of the option becomes On. Place a check mark in the Remove remnant(s) inside the fig. check box and type a value in the Max Size: text box to define the maximum entities size to be removed. |
| 5. | The system will remove the extra entities inside the part. |
| 6. | Set the conditions as follows. |
| 7. | The result will be as follows. |
| 8. | Set the conditions as follows. |
| 9. | The result will be as follows. |
| 10. | Set the conditions as follows. |
| 11. | The result will be as follows. |

| See: | Merge | Fill Gaps |
| --- | --- | --- |
|  | Remove Guidelines | Break |
|  | Get Outer Loop | Small Entities Removal |
|  | Remove Slot | Remove Holes Enclosing Pattern |
|  | Standard Hole Detection | Parts Separation |
|  | Corner Slot | Arc Straightening |
|  | Decimal Approximation | Minute Gap Removal |
|  | Slant Line Removal | Special Hole Detection |
|  | Polylines To Arc | Delete Point |
|  | Spline to Lines/Arcs | Ignore Conditions for Large Data |

## 28.7 Remove Slot

This option is used to control whether to remove the open path attached to an outer or inner loop. If the status of Remove Slot is set to On, you can place a check mark in the Outside or Inside check box to remove the open path attached to an inner loop or an outer loop.

Example

| 1. | The following part has open paths attached to the inner loop and outer loop. |
| --- | --- |
| 2. | If you remove the check mark from the Remove Slot check box, the status of this option becomes Off. |
| 3. | The system will process the open paths. |
| 4. | Place a check mark in the Remove Slot check box and then place a check mark in the Outside check box. |
| 5. | The system will remove the open path attached to the outer loop. |
| 6. | Remove the check mark from the Outside check box. Place a check mark in the Inside check box. |
| 7. | The system will remove the open path attached to the inner loop. |
| 8. | Place check marks in both the Outside and Inside check boxes. |
| 9. | The system will remove the open paths attached to the inner and outer loops. |

| See: | Merge | Fill Gaps |
| --- | --- | --- |
|  | Remove Guidelines | Break |
|  | Get Outer Loop | Extra Entities Removal |
|  | Standard Hole Detection | Small Entities Removal |
|  | Corner Slot | Remove Holes Enclosing Pattern |
|  | Decimal Approximation | Parts Separation |
|  | Slant Line Removal | Arc Straightening |
|  | Polylines To Arc | Minute Gap Removal |
|  | Spline to Lines/Arcs | Special Hole Detection |
|  | Ignore Conditions for Large Data | Delete Point |

## 28.8 Small Entities Removal

This option is used to control whether to remove small entities (arcs or lines). If the status of Small Entities Removal is set to On, the system will remove the small entities. You can type a value to define the maximum value of Circle Radius and Line Length to be removed.

Example

| 1. | The following part has a very small entity in the bottom right-hand corner. |
| --- | --- |
| 2. | If you remove the check mark from the Small Entities Removal check box, the status of the option becomes Off. |
| 3. | The result will be as follows. |
| 4. | Place a check mark in the Small Entities Removal check box and then define the maximum value of circle radius as follows. |
| 5. | The small arc is removed. |

| See: | Merge | Fill Gaps |
| --- | --- | --- |
|  | Remove Guidelines | Break |
|  | Get Outer Loop | Extra Entities Removal |
|  | Remove Slot | Remove Holes Enclosing Pattern |
|  | Standard Hole Detection | Parts Separation |
|  | Corner Slot | Arc Straightening |
|  | Decimal Approximation | Minute Gap Removal |
|  | Slant Line Removal | Special Hole Detection |
|  | Polylines To Arc | Delete Point |
|  | Spline to Lines/Arcs | Ignore Conditions for Large Data |

## 28.9 Standard Hole Detection

This option is used to control whether to parse the pattern made up of separate lines or arcs as a standard pattern. If the status of Standard Hole Detection is set to On, the system will detect standard holes, such as Rounds, Squares, Rectangles, Obrounds, Rounded Corner Rectangles, Single Ds and Double Ds. You can specify a parameter range for each type of hole. The status can be specified for each type of hole respectively, and will be used for standard hole detection. The default range for each type of hole is 200.

Example

| 1. | The following part has an inner round hole that consists of arcs. |
| --- | --- |
| 2. | If you remove the check mark from the Standard Hole Detection check box, the status of the option becomes Off. |
| 3. | The system process the round hole as a group of arcs and process them one by one. |
| 4. | Place a check mark in the Standard Hole Detection check box and then place a check mark in the Circle check box. You must also enable Use Machine Macro Shape. |
| 5. | The system will treat the inner hole as a standard pattern (hole) and process it. |

| See: | Merge | Fill Gaps |
| --- | --- | --- |
|  | Remove Guidelines | Break |
|  | Get Outer Loop | Extra Entities Removal |
|  | Remove Slot | Small Entities Removal |
|  | Corner Slot | Remove Holes Enclosing Pattern |
|  | Decimal Approximation | Parts Separation |
|  | Slant Line Removal | Arc Straightening |
|  | Polylines To Arc | Minute Gap Removal |
|  | Spline to Lines/Arcs | Special Hole Detection |
|  | Ignore Conditions for Large Data | Delete Point |

## 28.10 Remove Holes Enclosing Pattern

This option is used to control whether to remove the holes enclosing patterns. If the status of Remove Holes Enclosing Pattern is set to On, the system will remove the holes enclosing patterns.

Example

| 1. | The following part has holes enclosed within a triangle pattern. |
| --- | --- |
| 2. | If you remove the check mark from the Remove Holes Enclosing Pattern check box, the status of the option becomes Off. |
| 3. | The system treats the hole enclosing the patterns as an inner loop. |
| 4. | If you remove the check box from the Remove Holes Enclosing Pattern check box, the status becomes On. |
| 5. | The holes enclosing the patterns is removed. |

| See: | Merge | Fill Gaps |
| --- | --- | --- |
|  | Remove Guidelines | Break |
|  | Get Outer Loop | Extra Entities Removal |
|  | Remove Slot | Small Entities Removal |
|  | Standard Hole Detection | Parts Separation |
|  | Corner Slot | Arc Straightening |
|  | Decimal Approximation | Minute Gap Removal |
|  | Slant Line Removal | Special Hole Detection |
|  | Polylines To Arc | Delete Point |
|  | Spline to Lines/Arcs | Ignore Conditions for Large Data |

## 28.11 Corner Slot

This option is used to control whether to process a small circle pattern as a corner slot. If the status of Corner Slot is set to On, the system processes the circle as a corner slot. You can specify the circle radius range for the corner slot.

Example

| 1. | The following part has a circle pattern that encloses the upper right-hand corner. |
| --- | --- |
| 2. | If you remove the check mark from the Corner Slot check box, the status of the option becomes Off. |
| 3. | The system processes the circle as an inner loop. |
| 4. | Place a check mark in the Corner Slot check box and define the maximum circle radius value as follows. |
| 5. | The system will process the pattern as a corner slot. The lines are trimmed to the slot. |

| See: | Merge | Fill Gaps |
| --- | --- | --- |
|  | Remove Guidelines | Break |
|  | Get Outer Loop | Extra Entities Removal |
|  | Remove Slot | Small Entities Removal |
|  | Standard Hole Detection | Remove Holes Enclosing Pattern |
|  | Decimal Approximation | Parts Separation |
|  | Slant Line Removal | Arc Straightening |
|  | Polylines To Arc | Minute Gap Removal |
|  | Spline to Lines/Arcs | Special Hole Detection |
|  | Ignore Conditions for Large Data | Delete Point |

## 28.12 Parts Separation

The option is used to control whether to separate a drawing into two individual parts. If the status of Parts Separation is set to On, the system will separate the combined patterns.

Example

| 1. | You have the following scenario: |
| --- | --- |
| 2. | If you remove the check mark from the Parts Separation check box, the status of the option becomes Off. |
| 3. | Load the part into Dr. ABE. A warning symbol appears in the Nesting Schedule window. |
|  | Click the symbol to display the details. |
| 4. | If you place a check mark in the Parts Separation check box, the status becomes On. |
| 5. | Load the part again. The system now separates the drawing into two individual parts. |

| See: | Merge | Fill Gaps |
| --- | --- | --- |
|  | Remove Guidelines | Break |
|  | Get Outer Loop | Extra Entities Removal |
|  | Remove Slot | Small Entities Removal |
|  | Standard Hole Detection | Remove Holes Enclosing Pattern |
|  | Corner Slot | Arc Straightening |
|  | Decimal Approximation | Minute Gap Removal |
|  | Slant Line Removal | Special Hole Detection |
|  | Polylines To Arc | Delete Point |
|  | Spline to Lines/Arcs | Ignore Conditions for Large Data |

## 28.13 Decimal Approximation

This option is used to define the value digit after decimal, which is read by APDOM. If the status of Decimal Approximation is set to On, type a value to define the effective decimal digits.

Example

| 1. | Place a check mark in the Decimal Approximation check box and type 6 in the Decimal Approximation: text box to define the digit. |
| --- | --- |
| 2. | Check the XML output file after loading the part into Dr. ABE. The decimal digit is 6. The path of XML file is: |
|  | “D:\Program Files\Amada\AI-CAM\AIC_Main\Temp\1900200641185038525” |
| 3. | Type 1 in the text box to define the digit. |
| 4. | Check the XML output file after loading the part into Dr. ABE. The decimal digit is 1. |

| See: | Merge | Fill Gaps |
| --- | --- | --- |
|  | Remove Guidelines | Break |
|  | Get Outer Loop | Extra Entities Removal |
|  | Remove Slot | Small Entities Removal |
|  | Standard Hole Detection | Remove Holes Enclosing Pattern |
|  | Corner Slot | Parts Separation |
|  | Slant Line Removal | Arc Straightening |
|  | Polylines To Arc | Minute Gap Removal |
|  | Spline to Lines/Arcs | Special Hole Detection |
|  | Ignore Conditions for Large Data | Delete Point |

## 28.14 Arc Straightening

This option is used to control whether to parse an arc into several lines. If the status of Arc Straightening is set to On, the system will change the arc to straight lines. You can type values to define the Minimum Radius and Tolerance. If the size of the arc exceeds the defined minimum radius, it will be parsed into several straight lines. The Tolerance determines the number of line divisions. The value in the Tolerance: text box is the maximum distance between the straight line and the portion of the arc the system replaces with the straight line.

Example

| 1. | You have the following scenario: |
| --- | --- |
| 2. | If you remove the check mark from the Arc Straightening check box, the status of the option will be Off. |
| 3. | The result is as follows. The arc remains. |
| 4. | If you place a check mark in the Arc Straightening check box and define the Minimum Radius and Tolerance as follows: |
| 5. | The system will divide the arc into four straight lines. |

| See: | Merge | Fill Gaps |
| --- | --- | --- |
|  | Remove Guidelines | Break |
|  | Get Outer Loop | Extra Entities Removal |
|  | Remove Slot | Small Entities Removal |
|  | Standard Hole Detection | Remove Holes Enclosing Pattern |
|  | Corner Slot | Parts Separation |
|  | Decimal Approximation | Minute Gap Removal |
|  | Slant Line Removal | Special Hole Detection |
|  | Polylines To Arc | Delete Point |
|  | Spline to Lines/Arcs | Ignore Conditions for Large Data |

## 28.15 Slant Line Removal

This option is used to control whether to remove the slant line. If the status for Slant Line Removal is set to On, the system will remove the slant line. You should type a value to define the Step Height. If the slant height is within this range, the system will replace the slant line with a straight line.

Example

| 1. | You have the following scenario. The part consists of a slant or inclined line. |
| --- | --- |
| 2. | If you remove the check mark from the Slant Line Removal check box, the status of the option becomes Off. |
| 3. | The result is as follows. The slant line remains. |
| 4. | If you place a check mark in the Slant Line Removal check box and then define the Step Height as follows: |
| 5. | The result is as follows. The slant line is replaced with a straight line. |
| See: | Merge | Fill Gaps |
|  | Remove Guidelines | Break |
|  | Get Outer Loop | Extra Entities Removal |
|  | Remove Slot | Small Entities Removal |
|  | Standard Hole Detection | Remove Holes Enclosing Pattern |
|  | Corner Slot | Parts Separation |
|  | Decimal Approximation | Arc Straightening |
|  | Polylines To Arc | Minute Gap Removal |
|  | Spline to Lines/Arcs | Special Hole Detection |
|  | Ignore Conditions for Large Data | Delete Point |

## 28.16 Minute Gap Removal

This option is used to control whether to remove the small gaps on a part drawing. If the status of Minute Gap Removal is set to On, the system will remove the small gap. You can type values to define the Range and Line Length.

Note: To use this option, you should place a check mark in the Fill Gaps check box first.

Example

| 1. | There is a small gap on the part. |
| --- | --- |
| 2. | If you remove the check mark from the Minute Gap Removal check box, the status of the option becomes Off. |
| 3. | After you load the part into Dr. ABE, a warning symbol appears in the Nesting Schedule window. |
|  | Click the symbol to display the details. |
| 4. | If you place check marks in both the Fill Gaps check box and the Minute Gap Removal check box, the status of the option becomes On. Type a value in the Line Length and Range: text boxes respectively. |
| 5. | The result is as follows. |

| See: | Merge | Fill Gaps |
| --- | --- | --- |
|  | Remove Guidelines | Break |
|  | Get Outer Loop | Extra Entities Removal |
|  | Remove Slot | Small Entities Removal |
|  | Standard Hole Detection | Remove Holes Enclosing Pattern |
|  | Corner Slot | Parts Separation |
|  | Decimal Approximation | Arc Straightening |
|  | Slant Line Removal | Special Hole Detection |
|  | Polylines To Arc | Delete Point |
|  | Spline to Lines/Arcs | Ignore Conditions for Large Data |

## 28.17 Polylines To Arc

This option is used to control whether to merge several lines into an arc. If the status of Polylines To Arc is set to On, the system will merge the polylines into an arc. You can type a value to define the Maximum Line Length. If the line length is equal to or less than the defined maximum length, the system will merge the line.

Example

| 1. | You have the following scenario: |
| --- | --- |
| 2. | If you remove the check mark from the Polylines To Arc check box, the status of the option becomes Off. |
| 3. | The result is as follows. |
| 4. | If you place a check mark in the Polylines To Arc check box and then define the Max. Line Length as follows: |
| 5. | The system will merge the lines into an arc. |

| See: | Merge | Fill Gaps |
| --- | --- | --- |
|  | Remove Guidelines | Break |
|  | Get Outer Loop | Extra Entities Removal |
|  | Remove Slot | Small Entities Removal |
|  | Standard Hole Detection | Remove Holes Enclosing Pattern |
|  | Corner Slot | Parts Separation |
|  | Decimal Approximation | Arc Straightening |
|  | Slant Line Removal | Minute Gap Removal |
|  | Spline to Lines/Arcs | Special Hole Detection |
|  | Ignore Conditions for Large Data | Delete Point |

## 28.18 Special Hole Detection

If the status of Special Hole Detection is set to On, the system will detect the special holes.

Click the Setup Condition for Special Shape Hole button to open the Setup Conditions for Special Hole Type window. The options in this window allow you to define the special hole detection condition.

| See: | Merge | Fill Gaps |
| --- | --- | --- |
|  | Remove Guidelines | Break |
|  | Get Outer Loop | Extra Entities Removal |
|  | Remove Slot | Small Entities Removal |
|  | Standard Hole Detection | Remove Holes Enclosing Pattern |
|  | Corner Slot | Parts Separation |
|  | Decimal Approximation | Arc Straightening |
|  | Slant Line Removal | Minute Gap Removal |
|  | Polylines To Arc | Delete Point |
|  | Spline to Lines/Arcs | Ignore Conditions for Large Data |

## 28.19 Spline to Lines/Arcs

This option is used to control whether and how to parse a spline into lines/arcs. You can also select a Spline Explode Mode and define whether to write to APDOM.

Example

| 1. | There is a spline inside the following part. |
| --- | --- |
| 2. | Different NC codes will be output when you select different Spline Explode Mode. |
| 3. | If you place a check mark in the Write to APDOM check box, the system will write all of the spline parsing information into APDOM. |
| 4. | If you remove the check mark from the Write to APDOM check box, the system will not write any information about the spline parsing into APDOM. |

| See: | Merge | Fill Gaps |
| --- | --- | --- |
|  | Remove Guidelines | Break |
|  | Get Outer Loop | Extra Entities Removal |
|  | Remove Slot | Small Entities Removal |
|  | Standard Hole Detection | Remove Holes Enclosing Pattern |
|  | Corner Slot | Parts Separation |
|  | Decimal Approximation | Arc Straightening |
|  | Slant Line Removal | Minute Gap Removal |
|  | Polylines To Arc | Special Hole Detection |
|  | Delete Point | Ignore Conditions for Large Data |

## 28.20 Delete Point

This option is used to control whether to delete all of the points or some of the points inside the inner loops and outside the outer loops.

Example

| 1. | You have the following scenario. |
| --- | --- |
| 2. | When you select Delete All Points, the system will delete all of the points. |
| 3. | When you select Only delete outside of figure or inside of the hole, only the points outside the outer loop and inside the inner loop will be deleted. |

| See: | Merge | Fill Gaps |
| --- | --- | --- |
|  | Remove Guidelines | Break |
|  | Get Outer Loop | Extra Entities Removal |
|  | Remove Slot | Small Entities Removal |
|  | Standard Hole Detection | Remove Holes Enclosing Pattern |
|  | Corner Slot | Parts Separation |
|  | Decimal Approximation | Arc Straightening |
|  | Slant Line Removal | Minute Gap Removal |
|  | Polylines To Arc | Special Hole Detection |
|  | Spline to Lines/Arcs | Ignore Conditions for Large Data |

## 28.21 Ignore Conditions for Large Data

If the status of Ignore Conditions for Large Data is set to On, all conditions will be ignored, when the given data containing more than 10000 entities.

The following are exceptions:

- Spline To Lines/Arcs (Coarse mode will be used)

- Decimal Approximation also will be used only if the user has selected it.

| See: | Merge | Fill Gaps |
| --- | --- | --- |
|  | Remove Guidelines | Break |
|  | Get Outer Loop | Extra Entities Removal |
|  | Remove Slot | Small Entities Removal |
|  | Standard Hole Detection | Remove Holes Enclosing Pattern |
|  | Corner Slot | Parts Separation |
|  | Decimal Approximation | Arc Straightening |
|  | Slant Line Removal | Minute Gap Removal |
|  | Polylines To Arc | Special Hole Detection |
|  | Spline to Lines/Arcs | Delete Point |

# Index

A

Absolute	230

Access Information Manager	126

Add New Sheet	869

Add Part	808

Add parts by opening a file	808

Add parts from SDD database	810

Adding a New PDC Station	731

Adding a New Station	724

Additional Width (For Material, Process Range)	497

Additional Width (Traverse)	498

Adjust the process path on the arcs	943

Adjust the process path on the lines	942

Advance	231, 234

Advanced Filter Window	678

AI Tool Angle Sort	517

Angle of Turret	513

Append	44

Apply Assignment the Same Inner	974

Applying a Lead In or Lead Out	289

Arc Straightening	1030

Assign	258

Assign SP Tool to Process Line Segment	417

Assign Tool-Lines	926

Assign tools in the Effective Station Setting mode	631

Assign tools in the Turret Load Setting mode	628

Assignment	372

Assignment between 2 points	951

Assignment Logic	350

Attribute 1	695, 697

Attribute 2	699

Auto Correction Condition Setup	992

Auto Cutout Avoidance	493, 494

Auto Position	554

Auto Sort	687, 689

Automatic Material Selection	236

Avoid Dead Zone	508

B

Backup and Restore Material	78

Basic Dr.ABE Settings	17

Basic Joint Settings	555

Basic Operation	17

Basic Reposition Operation	853

Basic Shape	450

Basic Tool Information	690

Begin TK Edit	779

Bend Line Etching	296

Break	1001

C

CAD Data Drawing	95

CAD Data Load	140

Calculation	351

Change a Part Layout in Adjacent Mode	794

Change Check Boxes	185

Change Lead In for Shorten Traverse	489

Change Material	832

Change material by auto-calculation	833

Change Sheet Size	851

Change the Die Clearance of the Fixed Station	362

Change the Nibbling Pitch	982

Change the Tool Angle to Process	360

Change the Tool Assignment	919

Check the maximum tool	365

Check the minimum tool	368

Chute (L) Setting	576

Chute Setting	578

Clamp Information	60

Clamp Position Change	485

Clamp Removal (Clamp #) 3	484

Clamp Setting	483

Clearance	614

Clearance Setting	614

Code Definition	190

Codes	703

Collision Check	338

Collision Check Tolerance	279

Combi-Sequence	457, 458

Common Line Cutting	320, 523

Common Settings	564

Confirm Reposition	853

Confirm Schedule Tool	862

Confirm/Display Setting	794, 881, 882

Contouring Assignment	387

Corner	318

Corner Joint Settings	567

Corner Slot	1023

Create a Material Type	72, 73

Create a New PDC Turret Type	729

Create a New Turret Type	723

Creating a Lead-in or Lead-out Type	281

Creating a New File	203

Cut Condition Table	308

Cut Plate	579

Cutting Condition	30, 341

Cutting Condition Details	39

Cutting Condition Panel	31

Cutting Edge Information	42

Cutting Pierce Information	41

Cutting Process Information	40

D

Date	649, 656

Date Format	711, 716

Dates	176

Dead Zone	638

Dead Zone of the Station	639

De-burring	396

Decimal Approximation	1028

Decision Method of Lead Length	333

Decision Method of Lead Position	324

Decrease Sheet Quantity When Save NC	124

Defining the Group ID for Parts	182

Defining the Part Priority	181

Delete a Sheet Information	75

Delete Point	1045

Delete Sheet	751

Delete Trace	890

Deleting a Lead In or Lead Out	288

Detail	322

Detail Setting	267

Detail Setting for Processing Pierce First	334

Detailed Joint Settings	563

Diagonal Assignment	953

Difference between Quality and Speed	99

Different Result of the Common Line Cutting	184

Direct Assignment	950

Display Area Pane	205

Display Different Colors for the Elements on the Part	99

Display Material Info	752

Display Plan Info	752

Display Station option	869

Distance Between Tooling	465

Divide Reposition	857

Do Not Avoid Cutout with Joint	502

Do Not Avoid if Distance is Greater than Times of Original	499

Do Not Avoid if the Distance is Smaller than Times of Original	499

Do Not Include the Cutting Bigger Than	499

Do Stack	777

Download Material Type from AP100	76, 77, 81

Dr.ABE Main Window	17

Drawing	96

E

Edit	207

Edit a Material Type	73, 74

Edit Additional Elements Information	441

Edit Group	683

Edit Menu	147

Edit Mode Shortcut Menu	792

Edit of Elements	440

Edit of Path	439

Edit of Pickup/IJP Information window	781

Edit of Template	419

Editing a Lead-in or Lead-out	285

Effect Setting	458

End Value	901

Etch Layout	292

Example of Shift After Nesting	221

Exception to Averaging	51, 348

Expand All is Done after Automatic	103

Extra Entities Removal	1006

F

File	206

File Menu	147

Fill Gaps	995

Filler Parts	609

Fit Tool Style Panel	408

Fix Lead Position for OB and SQ-REC	328

Fix Process Order	978

Fixed Position	552

Flip Macro Pattern for Shorten Traverse	491

For Combination Process, Change Sheet Name Based on the Machine	651

G

General Sequence	458

Generate data	438

Get Information from NC Data	665

Get Outer Loop	1004

Getting Started	16

Grid Nesting	193

Grid Pattern	224

Group	601

Group Reposition	861

Grouping Priority	601

H

Height M104Zx	535

Help	209

Help Menu	156

Hierarchical Structure	199

High-Speed Shutter Less Setting	503

Holder Information	62

Hole Assignment	957

Hole Pattern List	410

How to Backup Material	79

How to Backup the Parameters	119

How to Create a New Laser Material	32

How to Create a Remnant Sheet	85, 87, 244

How to Create a Skeleton Sheet	87, 88

How to Create Skeleton Sheet	243

How to Define the Start Point/Direction	219

How to Download Cutting Condition from VPSS	34

How to Download JKF Files	38

How to Establish a Connection with a Server	142

How to Load CAD Data	140

How to Output the Z Value	551

How to Restore Material	80

How to Restore the Parameters	120

I

Ignore Conditions for Large Data	1047

IJP	64, 586

IJP Position	589

IJP Setting	587

IJP Strings	589

Import Ap100 SP/FM tools into Dr. ABE tool inventory	674, 676

Import AP100 tools into Dr ABE tool inventory	672

Import AP100 Turret Layout	620

Import Buttons	671, 672

Import DXF/DWG SP/FM Shapes	676

Information Area	105

Information Panel	783

Initial Clamp Position	229

Initial Part Number	112

Input size to change material	834

Insert Menu	149

Internal-tab Bend	299

Is G01 Continued	535

J

Joint	254, 382, 552

Joint Edit	893

Joint length and Lead In/Out length	314

Joint Setting Conditions	578

Joint Setting Window	241

Joint Type Table	563

L

Laser Assignment	275

Laser Hole Division	984

Laser Information	29

Laser Joint	585

Laser Pierce	258

Laser Sequence	486

Laser/Punch-1 (Perimeter and Notch Setting for Combination Process)	267

Laser/Punch-2 (Line and Arc Setting for Combination Process)	271

Launch Dr.ABE	16

Layout Between Single Hit	934

Lead In Edit	892, 910

Lead In& Pierce Details	323

Lead In/Out /Pierce Panel	275

Lead In/Out Table	275

License Registration	115

Light Attribute Editor	165

Line/Arc	45, 342

List Command	851

Loading/ Unloading End Position M-Code	542

Loading/ Unloading Thickness M-Code	540

Loading/Unloading Device	66, 539

M

M 108 After M104 Code	538

M Codes	705

Machine Information	23

Machine Information Panel	25

Machine Parameter	22, 45

Machine Parameter Toolbar	22

Machine Parameter Tree View	23

Machine Stop for Prototype	461

Machine Type	679

Macro Shape	47, 344

Main	257, 354

Main Window	91

Manual Edit Mode	789

Manual Edit Mode Parameter Panel	792

Manual Edit Mode Shortcut Menu	791

Manual Reposition	856

Manual Tool Assignment	876, 878

Manual Tool Assignment window	879

Marking Setting	308

Marking Setting for Etching [Count	336

Match To Line	415

Material	178, 188, 528

Material Manager Toolbar	71

Material Parameter	71

Material Selection	235

Material Selection Priority	236

Material Type Information	81, 82

Max Distance between Corner Joint	561

Menus	147

Merge	937, 993

Method of Dividing Long Parts	476

Methods for Specifying the Part Quantity	141, 142

Min Distance between Corner	555

Min Distance between Wire	557

Min Joint Qty	559

Minimum	471

Minimum Lap Amount	478

Minute Gap Removal	1035

Mix Sequence within	515

MJC	63, 583

MJC Setting	584

MJC/IJP Sequence	597

Mouse Command	848

Move	802

Move the process path on the arcs	948

Move the process path on the lines	947

Move/Copy Tool	959

My Nesting Plan	158

N

Nano Joint	43, 318

NC Device Information	53

NC Generate	527

Nest Around Clamps	225

Nesting	179, 190

Nesting Logic 1	213

Nesting Logic 2	223

Nesting Name	645

Nesting Parts by the Production Schedule	217, 218

Nesting Plan	144

Nesting Preference	212

Nesting Result List	737

Nesting Type	214

No Divide of Parts	474

Non AI Station is used with higher Priority	364

Number of Clamp	230

O

Object	548

Open Path	292

Option	77, 127, 871, 988

Option window	130, 132

Oscillator	56

Output G93	532

Output Outside of UV	525

Output Report	749

Output work size comment at the end of G92 command line	533

P

Pair Example	227

Parameter Assignment	954

Parameter Processing	122

Part Edit Mode Parameter Panel	880

Part Edit Mode Shortcut Menu	878

Part Grid	837

Part in Part Example	228

Part Layout Shortcut Options	759

Part Name and Comment	174

Part Rotation	226

Part-Gird Condition	520

Part-Grid	519

Parts List	162

Parts Properties	172

Parts Properties Advanced	187

Parts Properties Summary	144

Parts Removal Sequence	590

Parts Separation	1025

Part-Spacing and Nesting Border	234

Passage Avoidance in the Turret When Moving Axis	510

Path Assignment Method	291

Pattern Information and Assignment Pattern List	411

Pattern Setting	216

PDC Operation	707

Percent After G50	532

Percentage of Laser and Punch	266

Perimeter Tool Assignment	376

Peripherals	55, 583

Points	305

Polylines To Arc	1038

Preference File Pane	203

Preference File Shortcut Menu	204

Preference File Window	197

Preference Frame Current Folder	122

Preference Window Menu	205

Preference Window Overview	197, 198

Preference Window Toolbar	209

Pre-hole of Extrusion or Tapping	302

Priority	663

Process	179

Process After	545

Process After Cutting Table	546

Process and User Define	194

Process Corner Notch	264

Process Direction	480

Process Majority of Parts	478

Process multiple Line Segments as One Segment	356

Process Notch	265

Process Pierce First	280

Process the Perimeters	262

Process the Slit	395

Prototype Condition	604

Punch Clamp Setting	507

Punch Sequence	513

Q

Quantity	175

Quick Start Guide	16

R

Range and Shape buttons	625, 671

Range toolbar	863

Rectangle Tube	312

Reference of Cutting Condition (Size/Shape)	312

Remnant Edit	823

Remnant Name	710, 712

Remnant Name Items	710

Remnant/Skeleton Name	709

Remove	816

Remove Guidelines	999

Remove Holes Enclosing Pattern	1021

Remove Slot	1012

Reposition Command	851

Repositioning	470

Repositioning Type	471

Result View	734

Return to First Position	483

Reusable Sheet	239, 241

Rotation with Different Condition	182

Row Height	754

S

Save MJC Data	775

Save NC Data	740

Save Part	754

Save Schedule/Output Report	742

Save SY4	741

Save SY5 as File	755

Save Template	885

Schedule	597, 643

Schedule list	865

Schedule Name	652, 658

Schedule Name Items	653

Scheduling Priority	662

Search for Stock Tools	358

Search Stations	625, 626, 627, 628, 637

Search toolbar	863

Select Data	174

Select sheet code to change material	836

Select Skeleton/Remnant to Save when Saving NC	125

Selection by Overview	262

Selection Priority	238

Sequence by Dividing the Sheet	464

Sequence Command in Parts	906

Sequence Edit	845

Sequence Number	650, 654, 712

Sequence Processing Object	487

Setting of Outputting Result File window	133

Setup Sheet	530

Shape Data	450

Shape Edit area	438

Shape toolbar	863

Share the tool conditions among machines	692

Share to Size	248

Sheet and Each Part	460

Sheet Information	82, 84

Sheet Name	644, 651

Sheet Name Items	645

Shift	945

Shortcut Menu	164, 200

Show Tool	986

Simple Tool Assignment Setting for the Specified Template	406

Size Definition	189

Skeleton Name	715, 717

Skeleton Name Items	715

Sketch Material Tolerance	249, 252

Sketch Nesting	191

Sketch Type	252, 254

Slant Line Removal	1033

Slit & V Notch	391, 396

Slit Tool Assignment	375

Slot2&3	400

Small Entities Removal	1015

Sort by Process after Cutting	468

Sort Function	518

Sort of Laser & Punch	466

Special Hole Detection	1041

Special Information	189

Special Name	711, 716

Specify the range	846

Specify the Sheet Saver for the nesting tools to avoid reposition	697

Spline to Lines/Arcs	1043

Splitter Bars	198

Stack Distance	592

Standard Hole Detection	1018

Standard Nesting	191

Standard, Remnant, Skeleton and Sketch Materials	84, 85

Start Point/Direction	219

Starting Point/Direction	464

Stretch	940

SubInventory Window	669

SubInventory Window Toolbar	670

System	110

System Backup and Restore	118

System Determining Sheet by Material Name	112

System Information	115

System Requirements	16

System Setting	90, 111

T

T No	625, 626, 628, 637

Tab/Corner Process	313

Take Out	591

Take Out Information	58

Taking Out	594

Taking Out Conditions	591

Taking Out Part Grid as One Part	195

Taking Out Station	194

Tapping Information	69

Target Traverse	495

Template Creation Pane	443

Template Detail Settings	411

Template Icon	435

Template Menu	422

Template Pane	420

Template Parameter	437

Template Toolbar	422

The Column Heading Shortcut Menu	756

The Custom Lead In/Out Definition Window	280

The Customize Window	700

The Error List Panel	785

The NC Panel	786

The No. Column Heading Shortcut Menu	738

The Parts Information Panel	783

The Time Study Information Window	758

The Warning Information Window	758

Time Study	26

TK Process Type	608

To Assign attribute data to a pattern	167

To Shift the Lead in/out away from the Corner	331

Tool Assignment	256

Tool Assignment for Slanted Notch	381

Tool Assignment for the Vertical or Horizontal Notch	379

Tool Assignment Pane	449

Tool Inventory	668

Tool Inventory Table	679

Tool Inventory Table Shortcut Menu	683

Tool Lap Value	369

Tool Menu	149

Tool Window	690

Toolbar	863

Toolbars	156

Tooling Pattern	403

Tools	207

Traverse Setting	497

Treat an Open Path as a Slit	294

Tree View Pane	199

Tube Material Information	88

Turret and tool information table	866

Turret Image pane	868

Turret Layout	618

Turret Picture	628

Turret Section	620, 623, 624

Turret Section Toolbar	625

Turret Station List	635

Turret Type	720

Turret Type (PDC)	727

Turret Type (PDC) Window Items	727

Turret Type Window Items	721

Turret Type Window Short Cut Menu	726

Turret Type(PDC) Window Short Cut Menu	732

TurretLayout Window	623

U

Unfold Reference Line	298

Unloading Skeleton M Code	536

Use G42/G42	534

Use Machine Macro Shape	300

Use Setup Sheet	529

Use Sketch Material for Non-Sketch Parts	239

Use Special Tool to Create Joints	384

Use Wizard for Sheet Size/Name	113

Utilization	226

Utilization Setting	108

V

View	90

View Buttons	626, 678

View menu	865

View Menu	148

View Y Size	98

W

Welcome to Dr. ABE	12

What’s New	13

Window	208

Wire Joint Setting	572

Work Chute Information	67

X

X/Y/R/ CPX Explanation	549

X/Y/R/CPX/Area/Length/Width Explanation	549

Z

Zoom	106